Terminal Program PAC4


PAC4 is a simple terminal program, which uses the BPQ Host Mode to talk
to the switch. The program provides a buffered input line, which allows use 
of the editing keys ins, del, cul, cur, etc. It allows logging to disk
(CTRL/L toggles this function on and off), and maintains a simple 'Response
Time Monitor' function - useful for seeing how badly the network is
performing! A scroll-back buffer is also provided - use PageUp and PageDown


The program has one required paramter (port number), and a second optional
one (M for mono mode). So possible command lines are:

	PAC4 63			; to use stream 63

	PAC4 1 M		; to use stream 1, if you have a mono monitor.

Connection is made to the switch when a message is input. The ESC key 
disconnects you from the switch.

Monitoring is toggled on/off using F1. F2 toggles MCOM mode (monitoring of
control frames as well as info frames). F3 allows you to set MMASK. Press
F3, then key up to 4 hex digits, terminated with a newline. Each bit of MMASK
enables the monitoring of the corresponding radio port. Bit 0 enables port
1, bit 15 port 16. Any combination of bits may be set. The current monitor
settings are dislayed on the status line.


To exit from PAC4, enter CTRL/Y


John Wiseman, G8BPQ
11/4/92