TN210-8.DOC
                          USER COMMAND LIST, PT II
                        ****************************
 
    PARMS  (P) - (Parameters) Issuing this command will yield a status  listing
of the node's  parameters.   There are 23 SYSOP  settable parms in version 2.10
and the node response may look like this:

SKY:W7YB-3}  86 100 255 6 5 1800 6 7 10 1 0 30 3 0 1 100 32 240 2 3 180 4 4

    Each parameter  affects the  node operation  in one way  or another.    The
values chosen for one  node will impact the operation of the other nodes in the
network.   The convention is to number the parameters from left to right in the
example above, starting 1, 2, 3, etc.   Users will not be able to change any of
the parms unless recognized as a SYSOP.    However  users may find various parm
values  of  interest, such as in finding path  quality and timeliness of routes
between nodes.

    ROUTES (R)  -   This command yields a listing of all radio line-of-sight or
wire-connected nodes  "known"  to the node, including those  set  by the  SYSOP
routes   locking  commands.    Due to AX.25 protocol  variations,  Thenet  does
not automatically recognize KA-Nodes,  ROSE, TEXNET,  nor FLEXNET nodes in it's
ROUTES list.  It will recognize G8BPQ, MSYS and TCP/IP nodes.  A typical ROUTES
display may look like:

WTEX:W5CDM-3} Routes:
  0 ODSA01:W5CDM-1 192 30
> 0 DKC:W2RRY-2 192 23
> 0 MAF:KE5PL-1 192 10
  0 FST:N5DCZ-1 192 16
  0 RKN:KE5PL-3 192 11
  0 BGS:KE5PL-4 192 5

    Shown in  column 1,  all of the connections are  via direct radio  port (0)
paths.   The "right arrow"  indicator  tells us  two of the paths are either in
use  or have had  activity within  the past 15 minutes.  All radio paths show a
standard  path quality value of 192.  The last column indicates the most active
node in the list  is ODSA01   with  30 destination  routes showing.   The least
active is BGS with 5 destination routes.

    It is  possible  for  the NodeOp  to lock a non-node alias or callsign into
the ROUTES list.    This is done to indicate  to the observer that a non-TheNet
node is available.  An example might be a KA-node gateway:

MIST:KB7IVK-1} Routes:
> 0 AST:W7FBM-1 192 54
  0 V1KING 192 0!
  0 AST2:W7FBM-8 192 1

    In  this example V1KING is a KA-node  gateway from the local LAN to 28.103.
The  "0" in the number of destination routes column normally indicates a failed
path.   An astute observer would have checked the INFO section and learned that
V1KING  was a gateway.    Also he would  have  noticed  the V1KING entry in the
ROUTES  response was a locked pseudo  call-sign that should  tip him  off there
was something unusual about the entry.    A connect from  MIST  to V1KING would
result in the user being connected to the KA-node.


    USERS (U)  -  A command response might appear as follows:

AZ:N7OO-3} TheNet Plus 2.10st (713)
Uplink(AA5EK)  <-L4->  Downlink(AA5EK K1MEA-7)
Circuit(N5KGP-1 N5MYI)  <-L4->  Circuit(ONT:VE3KYZ-4 N5MYI)
Thrulink(BISBEE:WA7KYT-1)  <-L3->  Thrulink(ONT:VE3KYZ-4)
Circuit(SVALAN:N7OO-4 K1SC)
Uplink(DF2AU)  <..>  CQ(DF2AU-15)

    The first line identifies the node type and version.    This information is
valuable  to  the  experienced user since it provides insight into the commands
supported by the node.     Command support  is similar among the different node
types and their versions, but there are significant differences.  The number in
parentheses indicates the free buffers  (36 byte segments) currently available.
The  amount of free buffers  varies and is dependent upon the total destination
and neighbor nodes listed in the tables,  as well as the number and activity of
it's users.    Free buffers can be used as a "health indicator".   Upon initial
startup, the value will be in the "720" range.     Around the "450 - 500" area,
free  buffer  depletion  may  cause the node to respond with a  "Node busy"  to
command requests.

    Version  2.10 introduces the <-L3->, <-L4-> symbols and the term "Thrulink"
to the  USERS  display.    In the example above, the term "Uplink" refers to an
OSI  level  2  connect  from a local user to the network node.    "Downlink" is
defined  as  an  OSI level 4 network connect to a local user.    A "Circuit" is
either an OSI  level 4 network connect from a source node TO the local node, or
it  may  be  a connect  FROM the local node to a destination node.   "Thrulink"
displays an OSI level 3 circuit from a source node to a destination node.  As a
level 3 circuit, there may be more than one user traversing it bi-directionally
from end-to-end.   User identity can be accomplished by connecting to either of
the  nodes  listed  and performing a USERS command.   Inactive level 3 circuits
will timeout after 5 minutes.