TN210_11.DOC
                               NODE PARAMETERS 
                             *******************

TheNet nodes operate on a DYNAMIC ROUTING CONCEPT.   This means the software is
able  to  make  automatic  allowances  for  node  changes  within the  network.
TheNet recognizes  when new nodes are added to the system and deletes old nodes
that have failed.   It does this through periodic broadcasts containing routing
and obsolescence information.

TheNet  nodes  can be also configured to operate  in a stand-alone environment.
There is a  varying  degree of  adjustment  latitude  that  can allow  the node
to  go through  the extremes of recognizing only itself, just its neighbors, or
all other available nodes within the system.

The NodeOp in concert with network mangement has the options of setting  up the
node to operate  "wide open",  or to selectively  include or  exclude  specific
nodes or users.  It is this flexibility that makes TheNet Plus a popular choice
for networking.      One  of  the tools allowing this is a series of parameters
that  establish various node operating conditions.    Most node parameters will
seldom require attention following  initialization.   A few parameters may need
occasional  attention.    The  next five files  goes into detail on each of the
parameters.     The suggested values given for each parameter will allow proper
node operation in a typical system.

Recent versions of TheNet Plus contain two sets of parameters,  those that  are
programmed (fixed) into the EPROM, and those that are settable by SYSOP action.
The over-riding  factor driving  this dual parameter configuration was the lack
of  internal  EPROM  programming space.   With each  parameter  that was fixed,
bytes were saved.   The saved space was used for additional  node features.  In
each  case,  the  candidate  parameters selected for "fixed" set-up, were those
rarely, if ever, requiring change once the node was in operation.