TN210_12.DOC
                   REMOTE SYSOP PARAMETERS, 1 through 5
                 ****************************************

                  Parameter 1,  MINIMUM QUALITY FOR UPDATE
                  ----------------------------------------

   Sets  the  minimum path  quality value  of other nodes that will be accepted
into  the  routing table.   Nodes included in the broadcasts will be limited to
those  with path  quality values equal or greater than this parameter.   If the
value  is set low,  distant nodes  with  lower path values  (poorer probability
of connect)  will be allowed into the tables.    Higher values will improve the
probabilities   of  a  successful  connection.    A setting of "0" disables the
automatic update function and does not  allow  ANY  nodes to be recognized (not
recommended).    The  value  selected  will depend on several factors.    These
include the purpose of the node, network type and size.   A suggested value for
a multi-user simplex configured node is "86."
(Range:  0-255)


                     Parameter 2, HDLC CHANNEL QUALITY
                     ---------------------------------

    HDLC is an OSI level 2 function  and is  what  the AX.25  protocol is based
upon.    Here, the term is synonymous with RADIO PATH QUALITY.    Since much of
the automatic network  management  techniques of TheNet are centered around the
path  quality concept, the basic conventions will be discussed.  Certain  types
of  packet  networks  (wire links, HF/VHF/UHF radio  with varying  user access)
are more  efficient than others.    The most ideal packet link is a full duplex
wire line between two TNCs.  This, because there isn't any outside interference
to corrupt the circuit.  Least ideal is a multi-user  accessed  HF link subject
to  interference and  changing propagation conditions  between  the  two  TNCs.
Through  observations and studies the following conventions were established:

          TYPE OF PATH BETWEEN TNCs      PATH QUALITY    RELIABILITY

          RS-232 wire line (2 port)          255            99
          Satellite link                     252            98
          RS-232 wire line (3 port) link     248            97
          UHF radio non-user radio link      240            94
          VHF radio non-user radio link      224            88
          VHF/UHF user accessed radio link   192            75
          10 Meter user accessed radio link  180            70
          HF user accessed radio link        128            50

    It should be remembered these path quality values are for ideal situations.
Path  congestion and propagation conditions will lower the values  accordingly.
But  by  convention, the  above  values  will  be used  in  parameters  2 and 3
throughout the system.  The above chart explains why it is undesirable to allow
user access to backbone trunks.    By doing  so, the path  quality is degraded.
Recommended default for a  1200 baud VHF/UHF  user accessed  simplex radio link
is 100 with  the reliable neighbors  permed to 192.  (Range:  0-255)


                     Parameter 3, RS-232 CHANNEL QUALITY
                     -----------------------------------

    Describes the path  (or port)  via the RS-232 connector  (DB-25 or DB-9) at
the rear of the TNC.    If configured for  multi-node operation, this connector
ordinarily attaches to either another TNC/node, or to a diode matrix connecting
three or more TNC/nodes.    As indicated in the above chart, the probability of
a successful connection is highest for two TNCs RS-232 connected.    Therefore,
the highest path quality value is assigned to this configuration.  Diode matrix
connected TNC's have a lower  probability  of connect.  This is because any one
given TNC may be held off  while an active packet is in process to another  TNC
on the matrix.   Thus throughput over diode  matrixed  TNCs  is not as  high as
two direct connected TNCs.    Path quality values for this parameter ordinarily
are  set at  255 for two nodes,  and perhaps  as low as  245  for several diode
matrixed nodes.

NOTE: SYSOPing  the  existing  value  of  Parms 2 and 3 to a different value on
active nodes showing in the ROUTES will not be immediately reflected.  If these
nodes decrement out (fail) and later come back, they will reappear with the new
SYSOPed  Path  Quality  value  assigned  to  them.   A procedure to get the new
value to quickly go into effect  (short of RESETTING the node)  would be to use
the  routes  locking  command.   Lock them in at the new value, then remove the
locks.

The following illustrates how HDLC (radio) CHANNEL QUALITY and RS-232 CHANNEL
QUALITY are displayed in response to a (R)outes command:

CLAMS:WA1ZDA-3} Routes:
  0 ME220:WA2YVL-3 150 16
  1 PENBAY:WA1ZDA-1 255 15
  1 LOBSTR:WA1ZDA-7 255 15

    The  0  and 1's seen in the left column correspond to the port  identifiers
listed  in  parameters 2 and 3.  The 0 means it is a radio port and the 1 is an
RS-232 TNC port.  The 3rd  column is the default settings (in this example) for
parameters  2 and 3.  Here we note the NodeOp has determined the radio path  to
ME220 is not a good "standard" 192 quality path.   Therefore he has assigned it
a value of  150.   If a neighbor node HAD a good 192  quality path, parameter 2
would be set for 192.  Then the  ROUTES  locking technique would be used to set
ME220  to  the  150  value.     In this example, the NodeOp has assigned RS-232
CHANNEL QUALITY values of 255 to both the PENBAY and LOBSTR nodes.   Though not
pertinent  to  this  discussion,  the  final  column  indicates the  number  of
destination routes through that path.
(Range:  0-255)


                      Parameter 4, OBS COUNT INITIAL VALUE
                      ------------------------------------

    The  initial  value  for the  NODES  obsolescence  counter.    This counter
displays  how current  a path is to a  destination node.   The node keeps track
time-wise of all nodes heard during neighbor broadcasts.   By  convention, this
counter is normally defaulted to "6."  If for some reason (QRM or node failure)
a known  node  isn't heard upon receipt of  the  next  neighbor broadcast,  the
obsolescence value for that node  will decrement to "5."    If not heard at the
next broadcast, it goes to "4," etc.  Once the value goes to "0," knowledge  of
that  node is removed from the routing table.  If the node IS heard  before the
value  falls to  "0,"  it automatically is reassigned a "6."   By comparing the
broadcast timer value in parameter 6 against  the  obsolescence count, one  can
calculate how "fresh" a path is.

The  purpose  of  the  obsolescence counter  is to  purge failed nodes from the
routing  tables.     With a  one-half hour  broadcast cycle (1800 seconds),  an
initial value of "6" will allow a  failed node to remain in the  routing tables
of immediate neighbors for up to 3 hours.    Depending  upon the parameters  of
more  distant  nodes,  the  failed node  may  appear  within the  network for a
longer period before finally being decremented out.

Nodes  configured as HF gateways  are subject to variable and sometimes sudden,
propagation shifts.    An initial obsolescence counter  value of "4" on  the HF
node  and on  adjacent  RS-232 connected VHF/UHF nodes  will hasten the purging
of stale nodes from the system.
(Range:  0-255)


                      Parameter 5, OBS COUNT MINIMUM for BCST
                      ---------------------------------------
   Sets  a limit on the  minimum obsolescence value associated with other nodes
to be  included  in the NODES broadcast.    For instance, if a neighbor has not
heard the  CARBON:VE6RCB  node  for 2 or 3 broadcast periods, the likelihood is
high CARBON has failed.  Thus it is good network practice to avoid  sending out
useless node data.   By setting parameter 5 to a value of one less than that of
parameter 4,  freshly  failed  nodes  will not be  included in the  forthcoming
broadcast.    Knowledge of the missed node will remain until decremented out by
parameter 4.  Therefore, if the broadcast was simply missed due to QRM, distant
users would still be able to connect to that node.     If set to a higher value
than parameter 4, the NODES destination table will include only itself.
(Range:  1-255)