TN210_18.DOC
                              ROUTING LOOPS
                            *****************

    When  TheNet  receives  a command instruction to connect to  a  destination
node,  it  will attempt to set up a circuit via the path it has determined  has
the highest  path quality listing.  If this results in a timed out  connection,
it then  will attempt a connect via the next best route.  If this attempt  also
fails, the node will attempt a third path if one is listed.

    Sometimes  a  primary  route  may experience  temporary  failure.   A  node
receiver  down  the line may be subject to interference or desensitization  for
a period.  If this occurs while a connect request is in  progress, its possible
the local node will time the circuit out and attempt a connect on the next best
route listed.  If after a time an unusual delay is noted in having the  connect
request processed, disconnect.  Then, reconnect  to  the local  node and  do an
"N <destination nodecall>"  command.   (Where destination nodecall is the alias
of the destination node one just attempted a connect to).

    Notice  the  position  of  the activity arrow on  the  resultant  response.
Chances  are,  the  activity  arrow  will  show an attempt is being made via  a
"routing  loop" path.  A path that has a "0" path quality, or perhaps to a path
that  leads  elsewhere.   As  long  as the activity arrow  is  pointing  to  an
unconnectable  path,  there  is little one can do but wait until  the  internal
timer  "resets" (usually 15 minutes following the last connect request for that
particular  node).  Then if the circuit is clear, one should be able to make  a
connect via the primary path.