TN210_20.DOC
                             MULTI-PORT OPERATION
                           ************************

    Multiple  TNCs and radios can be interconnected to form a "node stack".   A
diode  matrix is used to route the signals in proper sequence between the TNCs.
Interconnecting  more than two TNCs does decrease the thruput since the circuit
is no  longer operating full duplex.  Diode matrix node stacks of up to 14 TNCs
are in  operation.   Shown  is a four TNC matrix circuit.  For more  than  four
TNCs,  the  circuit  is  appropriately  expanded.


                               RS-232 Four Matrix

    Note:   On the DB-25 connectors, all pin 1's are connected together as  are
all pin 7's.  On EACH DB-25, pins 10 and 23 are jumpered together as are pins 4
and 20.  Comment:  The original TAPR TNC-2 circuit board layout  mistakenly had
CTS connected to pin 20, instead of pin 4.  It took awhile before manufacturers
licensed by TAPR caught and corrected this error.  Meanwhile, it is good policy
to  simply jumper 4 and 20 in case  of a mix of older and newer TNCs being used
in the stack.


                      |-->|-- C2-2                       |-->|-- C2-5
     Connector 1-3----|-->|-- C3-2     Connector 1-20----|-->|-- C3-5
                      |-->|-- C4-2                       |-->|-- C4-5

                      |-->|-- C1-2                       |-->|-- C1-5
     Connector 2-3----|-->|-- C3-2     Connector 2-20----|-->|-- C3-5
                      |-->|-- C4-2                       |-->|-- C4-5

                      |-->|-- C1-2                       |-->|-- C1-5
     Connector 3-3----|-->|-- C2-2     Connector 3-20----|-->|-- C2-5
                      |-->|-- C4-2                       |-->|-- C4-5

                      |-->|-- C1-2                       |-->|-- C1-5
     Connector 4-3----|-->|-- C2-2     Connector 4-20----|-->|-- C2-5
                      |-->|-- C3-2                       |-->|-- C3-5

    This  circuit requires 24 small signal diodes, such as 1N914's, four  DB-25
male  connectors, a supply of small various color coded wire and a small  piece
of perf  board  on  which to mount the diodes and interconnecting  wires.   The
circuits  are wired in sequence.  For Connector 4, for instance, pin 3 is wired
to the anode side of three diodes in parallel.  The cathodes go to Connector 1,
pin 2,  Connector  2,  pin  2 and connector 3, pin 2.  Connector 4  pin  20  is
connected  to  the  anode  of three diodes in parallel.   The  cathodes  go  to
Connector 1, pin 5, Connector 2, pin 5 and connector 3, pin 5.  The wire bundle
going  from each of the DB-25's to the perf board can be any length you prefer,
but possibly 16 inches would be adequate.

    After  the  circuit is wired, use an ohm meter to check continuity on  each
circuit.   As  in the dual port configuration, make sure all TNC's are set  for
9600  baud on their RS-232 ports.  Following power up it will take from 6 to 10
seconds for the adjacent node broadcasts to "wake" them up.


    For information on a commercially available 6-port diode matrix board, send
a SASE to: NorthEast Digital Assn, PO Box 563, Manchester, NH  03105-0563.

    Provided on the distribution diskette is a binary ROM image of TheNet Plus.
Also  provided is the  SET210 utility which easily allows setting up the node's
callsign, SSID, parameters and password to appropriate values.

For those  considering the purchase of an EPROM programmer, JDR Electronics has
a suitable  model at low cost, as does Needham.    But from whatever source, be
sure to specify one that will handle CMOS chips.  Inexpensive EPROM erasers are
available from a number of dealers.

    In  keeping  with  the  high standards set by NORD><LINK, the production of
TheNet Plus is  placed in the public domain with the understanding it is NOT to
be used commercially.


73 and enjoy!
Bill Beech, NJ7P
Jack Taylor, N7OO