Application Notes for use of All Chargecard on a PS/2 Model 30-
286, 50, 50Z, or 60 running 3Com 3+ or 3+Open DOS workstation 
software.

Configuration 1 -   3+ DOS workstation OR
                       (see also config.w3p and autoexec.w3p)
                    3+Open DOS workstation - XNS protocols
                       (see also config.w3o and autoexec.w3o)
                    Full NetBIOS or partial (not shown)
                    Windows/286 (No EMS, no Smartdrive)
                    VGA
                    1MB of motherboard memory
                    3Com EtherLink/MC network adapter

Configuration 2 -   3+ DOS workstation OR
                       (see also config.3p and autoexec.3p)
                    3+Open DOS workstation - XNS protocols
                    Full NetBIOS or partial (not shown)
                    VGA
                    1MB of motherboard memory
                    3Com EtherLink/MC network adapter

*** CAVEATS:  

1) On 3Com's 3+ network operating system, if full NetBIOS must be 
   loaded high, you must use NetBIOS 1.2.1H, available 
   for 3+ customers from 3Com by dialing XXX-XXX-XXXX.  
   (This module is included with 3Com 3+Open systems.) 

2) In a Model 50Z, both the LCC and PLCC adapters must be used.
   Both are available separately from All Computer.  You lose the 
   use of two expansion slots.

3) In a Model 30-286, the PLCC adapter must be used.  This 
   adapter is available separately from All Computer.

INSTALLATION AND CONFIGURATION PROCEDURE - Configuration 1

1) Install the All ChargeCard hardware per instructions.  Follow 
   the instructions VERY CAREFULLY.

2) Use the IBM PS/2 Model 30-286 or 50/60 Reference diskette move 
   the Packet Buffer RAM of the EtherLink/MC card to address 
   C000-C5FF.

3) Add 
   device=<path>\allemm4.sys /RAM /FR=NONE /X=C000-C5FF /EXT=64

   line to config.sys.  Do not load any network drivers high 
   at this time.

   /RAM - tells allemm4 to find any available logical RAM between 
          640K and 1MB.  On a '286 PS/2, VGA memory (A000-AFFF, 
          and B800-BFFF) is not available, neither is extra ROM 
          BIOS memory (in which there are no ROMS, thanks PS/2)
          (E000-EFFF) is not available either.  /RAM figures this 
          out all by itself.

   /X=C000-C5FF - eXcludes the 24K RAM Packet Buffer area of the 
                   EtherLink/MC card.This leaves the largest 
                   contiguous area (104K) available (C600-DFFF).
                   **This parameter MUST match the RAM Packet 
                   Buffer area assigned using the PS/2 Reference 
                   Diskette.

   /EXT=64 - Reserves the first 64K of extended memory (above 
             1MB) for use by himem.sys.

4) Install Windows/286, telling it that extended and expanded 
   memory are available.

5) Add remaining lines to config.sys and autoexec.bat per the 
   appropriate config and autoexec files.  The first line of 
   config.sys MUST be "device=himem.sys".  The second line of 
   config.sys MUST be the "device=<path>\allemm4.sys..." line.  
   The remaining "device =..." lines are in autoexec.bat.  All 
   operating software includes its own "device," "files," 
   "buffers," and "lastdriv" 'commands.'  That is why these are 
   in autoexec.bat rather than config.sys.  

   The "alload" command loads drivers high.

   3+Open only:  In the \3open\doswksta\lanman\lanman.ini file, 
   find the line containing the "redir" command.  Add to the 
   front of it the full path to the alload command:
   i.e.  \<path>\alload redir .....

 6) At this point you may want to experiment with loading drivers 
    in different spots to obtain the best fit; you may also use 
    the PS/2 Reference Diskette to move the location of the 
    Packet Buffer RAM.  Don't forget to change the /X:... 
    parameter of the "device=<path>\allemm4.sys..." line of 
    config.sys to reflect the new location.  Use the alload, 
    device, or xexamem commands interactively with no parameters 
    to look at how memory is used.

    Useful parameters to load drivers in different places are:

    device /LM - loads driver into Low Memory (below 640K)
    device /AF - Assigns (loads) driver into First available 
                 segment
    device /AT - Assigns (loads) driver into starting from the 
                 end (Top) of available memory 

    alload (includes above parameters)
    alload /SG:XX00 - loads driver into specified memory segment 
                      (e.g. /SG:B000)

   ***Experiments have shown that spp.sys wants to be loaded 
   first using the /AF command.  The order of the other device 
   drivers does not matter, but the included autoexec.bat were
   designed to obtain the best fit.

INSTALLATION AND CONFIGURATION PROCEDURE - Configuration 2

1) Install the All ChargeCard hardware per instructions.  Follow 
   the instructions VERY CAREFULLY.

2) Use the IBM PS/2 Model 30-286 or 50/60 Reference diskette move 
   the Packet Buffer RAM of the EtherLink/MC card to address C000-
   C5FF.  This leaves the largest contiguous area (104K) 
   available (C600-DFFF).

3) Add 
   device=<path>\allemm4.sys /RAM /FR=NONE /X=C000-C5FF 

   line to config.sys.  

   /RAM - tells allemm4 to find any available logical RAM between 
          640K and 1MB.  On a '286 PS/2, VGA memory (A000-AFFF, 
          and B800-BFFF) is not available, neither is extra ROM 
          BIOS memory (in which there are no ROMS, thanks PS/2)
          (E000-EFFF) is not available either.  /RAM figures this 
          out all by itself.

   /X=C000-C5FF - eXcludes the 24K RAM Packet Buffer area of the 
                   EtherLink/MC card.  
                   **This parameter MUST match the RAM Packet 
                   Buffer area assigned using the PS/2 Reference 
                   Diskette.

4) Add remaining lines to config.sys and autoexec.bat per 
   attached files.  The first line of config.sys MUST be the 
   "device=<path>\allemm4.sys..." line.  The remaining "device 
   =..." lines are in autoexec.bat.  All operating software 
   includes its own "device," "files," "buffers," and "lastdriv" 
   'commands.'  That is why these are in autoexec.bat rather than 
   config.sys.  

   The "alload" command loads drivers high.

   3+Open only:  In the \3open\doswksta\lanman\lanman.ini file, 
   find the line containing the "redir" command.  Add to the 
   front of it the full path to the alload command:
   i.e.  \<path>\alload redir .....

5) At this point you may want to experiment with loading drivers 
    in different spots to obtain the best fit; you may also use 
    the PS/2 Reference Diskette to move the location of the 
    Packet Buffer RAM.  Don't forget to change the /X:... 
    parameter of the "device=<path>\allemm4.sys..." line of 
    config.sys to reflect the new location.  Use the alload, 
    device, or xexamem commands interactively with no parameters 
    to look at how memory is used.

    Useful parameters to load drivers in different places are:

    device /LM - loads driver into Low Memory (below 640K)
    device /AF - Assigns (loads) driver into First available 
                 segment
    device /AT - Assigns (loads) driver into starting from the 
                 end (Top) of available memory 

    alload (includes above parameters)
    alload /SG:XX00 - loads driver into specified memory segment 
                      (e.g. /SG:B000)

   ***Experiments have shown that spp.sys wants to be loaded 
   first using the /AF command.  The order of the other device 
   drivers does not matter, but the included autoexec.bats were 
   designed to obtain the best fit.