THD ProScan Ver 6.0

          First... Thank you for downloading this file.

          Credits...
     Thanks to all the sysops who, at various stages, helped in the 
betatesting of this product. Many helped me to find "minor" inconsistencies 
and fix them before you got to see it.
     A VERY special thanks to "Witch Doctor" for his great assistance in 
betatesting the first releases and making valuable suggestions about the 
program.. Many of which were implemented, And of course some which were 
not.. But all of his suggestions and comments were considered.
     A special thanks as well to "Eternal Darkness" for his contribution of 
the "user side ansi screen". He willingly gave me a number of "ansi" drawings
with permission to modify them as was necessary to suit my purpose. The ansi 
your users see is only very slightly modified from the ansi I received and I 
think he did an excellent job.
     A thanks as well to David Luckie who reported the problem which Version 
4 fixed. Without his inquiries the integrity of this program might have been 
severely compromised.
     To Neil Dempster for his support and constant questioning (not to 
mention the extra drives).
     And to Tim Strike for his assistance in many aspects, including 
relaying David's concerns and replies so that I might be able to fix the 
problem.
     To TurboPower Software for the use of their EXECSWAP program.

     Support for this tester can usually be found on  TELENET CANADA.  
     Requests for support on  TELENET  CANADA  should  be directed to 
     David Muir.  Inquiries about this tester can be made in  TELENET 
     TELEGARD or BBS support areas.  In the event that Dave is unable 
     to assist  you  directly,  there are numerous people in  TELENET 
     who are familiar enough with  my program to offer some technical 
     assistance. Advice about configuring YOUR BBS program to run THD 
     ProScan would best be handled  by someone familiar with that BBS
     software. I am only familiar with Telegard and T.A.G. in respect
     to having  sufficient knowledge to offer technical assistance in
     setting them up to run this tester. THD ProScan V 6.0 is however,
     generic and can be run by almost ANY BBS with the correct setup.
     
     THD ProScan is an upload tester for ANY BBS which is capable of sending 
a command line of the following format.

"C:\UTILS\THDPRO.EXE D:\NEWFILES\TEST.ZIP"

{Where "C:\UTILS\THDPRO.EXE" is the full path and filename to the THD ProScan
executable file and "D:\NEWFILES\TEST.ZIP" is the full path and filename to 
the file to be tested}.

    ***************************** WARNING *****************************
    Remote dos redirection must NOT be set to a comport or device other 
    than "CON"  during the running  of this upload  tester.  Failure to
    pay attention "could" ( in some cases ) cause paths to be displayed
    to a remote user.  If necessary, redirect the output on the command
    line by appending " >CON" to the end of the line.  This will not be
    necessary in MOST cases. If you do not see the utilities performing
    their functions, the output is being  redirected to somewhere else.
    ************************* END OF WARNING **************************

    
 *******************************  WARNING  *********************************
 **     This  Version of  THD  ProScan  is designed  to  recognize files  **
 **  created by PKZIP 204c, 204e and  204g.  Therefore it  requires that  **
 **  your version of PKZIP be PKZIP 204g.                                 **
 **     The use of any version prior to 204g  WILL result in valid files  **
 **  failing the  CRC  test.  While it  does still  recognize and handle  **
 **  version  1.10  files,  it also  recognizes the  newer file formats.  **
 **  Version 1.10 will  NOT be able to  handle the new  formats and will  **
 **  cause the files to fail testing.                                     **
 **      This, of course, only applies  to those of you who wish to test  **
 **  "ZIP" type files.                                                    **
 **      If you are going to test "ZIP" files with this tester, then you  **
 **  MUST use PKZIP 204g or risk failing files.                           **
 ***************************** END OF WARNING ******************************


Features..
     - Identifies all archives by their internal signatures.
     - Including self extracting archives.
     - Allows files to be rejected based on the dates of the files
        inside the archives.
     - Can reject files by name using a "hack list" (HACK****.COL file 
        compatible)
     - Supports "heuristic" testing for suspicious code using
       F-PROT.EXE or TBSCAN.EXE.
     - Support for remote ansi or ASCII as determined by auto ansi detect.
     - Suppression of remote output through the use of "comport 0".
     - Suppression of remote output through the use of a user defined
        comport.
     - Option to NOT modify "ZIP" archives which have a valid "AV".
     - Strips comments from all archives before any processing is done
        (to avoid "ansi bombs" in comments). This features will not protect
        the end users if the "internal" archives contain such bombs.
     - Recreates full directory structure "from" the temporary directory, 
         thus allowing all internal archives to be tested regardless
         of how deeply imbedded they may be.
     - Does not allow the "overwrite" option on any of the archive types.
        (stops some forms of "hacking")
     - Add your loaders and/or archive comment to the main archive.
     - Will use one of as many as three drives to test files by
        searching in order to find enough available space on one of them.
     - "Intelligent" installation which will attempt to do as much of
        the installation for you as is possible.
     - The configuration of either of the two previous versions of
        THDPRO.EXE can be used automatically.
     - Full control over the options available and paths to archive utilities.
     - Support for ZIP-GIF-TD0-ARC-ARJ-PAK-HYP-LZH-SQZ file types.
     - Will Virus scan all file types regardless of types configured.
     - Remove unwanted files from the archives tested.
     - Option to hang up on users who upload viruses.
     - Option to reboot after a viral detection.
     - No Known ways to "alter" the operation of your BBS through it's use.
     - Can be run on two or more nodes simultaneously.
     - All operations controlled by a single executable file.

     WHAT WILL IT DO.. 
          THD ProScan will ..
         1) Check (and/or reject) files from a user supplied list of files
         2) Strip the file comment
         3) CRC test the file
         4) FIND a drive with enough space to test the file
         5) Create a directory called "THDTEMP.$$?" on that drive
         6) Remove files (if configured) from the archive.
         7) Check dates to reject old files (if selected).
         8) Expand the archive into that directory while recreating
               its internal path structure.
         9) It will then scan each of the files in that directory and
               all subdirectories below it.
        10) It then selectively searches each of the subdirectories created
               for testable archives. If found, it repeats the above process
               until no more archives are found. In this way EVERY imbedded
               archive is tested, regardless of where it is in the directory
               structure or how far imbedded it is. Every directory created 
               by the original archive or any of the embedded archives is 
               tested and scanned by THD ProScan.
        11) Add your loaders to the archive
        12) It maintains a log in your BBS directory of all actions performed.
        13) Add your file comment.
        14) It then proceeds to remove the temporary directory structure.
        15) Reports the appropriate errorlevel to dos.

     The actual process is of course much more complex.. But the above 
overview is a decent summary.

     Requirements...
          This tester requires 
          PC/XT (or compatible)
          MS-DOS 3.3 (or higher)(other "DOS" systems MAY be acceptable)
          A FOSSIL DRIVER (user output will not be sent if no fossil is found
                           but the testing will still be done)
          McAFEE's VIRUSCAN (the newer the better)
          APPROX 325k FREE memory (**)

          **    Memory requirements will vary depending on your version
                of SCAN.EXE. The actual overhead of this program is 100k.
                The "add" feature of SQZ.EXE will require significantly
                more memory than is noted above. Use of SQZ.EXE can require
                as much as 520k free for the "add loaders" option to operate
                correctly. This is due to the archiver itself and nothing
                can be done about it from my end. Lack of memory will not
                cause those files to fail but will simply not add the files
                if memory is insufficient. Use of F-Prot for heuristic 
                testing may also require more memory. A quirk with SQZ.EXE
                also may affect it's ability to add loaders or comments and
                these options have been disabled in the circumstances where
                SQZ could erase the original archive.
                        Compensation for these conditions is attempted though
                the use of TurboPower Software's EXECSWAP program which will
                swap approximately 48k out of memory to give these intense 
                programs more room to run.


     The following utilities are required depending on which file types you 
wish to test.
          LHA.EXE        for "LZH" files
          ARJ.EXE        for "ARJ" files
          SQZ.EXE        for "SQZ" files
          PKZIP/PKUNZIP  for "ZIP" files (supports vers 1.10 - 2.04g)
          PKARC/PKXARC   for "ARC" files
          PAK.EXE        for "PAK" files
          HYPER.EXE      for "HYP" files
          TDCHECK.EXE    for "TD0" files
          GIFTEST(ver 4) for "GIF" files
          F-PROT.EXE     for Heuristic file testing
          or
          TBSCAN.EXE     for Heuristic file testing


INSTALLATION...

     Included are 11 files.. NEWINV6.TXT,THDPRO-6.ADD,THDDEMO.COM,
THDPRO.DOC,THDPRO.EXE, HISTORY.DOC and THDINSTL.EXE. WARNING.TXT, 
THDSETUP.TXT ANSWERS.TXT and THDTERM3.ZIP.
     THDPRO.EXE is the actual upload tester and controls or performs 
all actions of the "testing" from "File Allocation Table move" to removal 
of the temporary directory.
     THDTERM3.ZIP is an archive containing a simple interface for use of THD 
ProScan without a BBS. Read the documentation included in that archive 
pertaining to its use.
     HISTORY.DOC is a simplified history of THD ProScan.
     NEWINV6.TXT is a listing of the changes and added features between
version 5 and this release. Please see HISTORY.DOC for a list changes to 
the program.
     WARNING.TXT is a text file listing the warning above in regards to
the use of PKZIP204G.
     THDSETUP.TXT is a text file explaining how to set up THD ProScan to run 
on a T.A.G., RA2 gamma1, or TELEGARD BBS. As well it contains a simple batch 
file for processing entire directories of files.
     THDPRO-6.ADD is a sample file comment for use with the tester. It
serves only as an example and is NOT required for proper operation of 
the tester.
     ANSWERS.TXT is a file containing questions and answers that may 
assist you in understanding the program better.
     THDINSTL.EXE is the INSTALL/CONFIGURATION utility. It MUST be run 
in order for the scanner to operate correctly.
     Basically all that is required is that the THDPRO.EXE be in your 
current directory when you run THDINSTL.EXE.
     THDINSTL.EXE will search the executable file for any previously 
configured settings. If none are found it will go through the 
installation step by step. If however it finds that the installation 
has previously been run, it will simply load the previous information 
and take you to the final two option screens. From these two screens 
you may select (by letter) to modify any of the previous configuration 
parameters. 
     The "original" installation process can be defaulted to by running
"THDINSTL.EXE /F". This will cause the install to NOT look for old 
settings and simply start an install as if it were the first time.
     When you run the installation, it will ask you a number of yes/no 
questions and depending on your answers will prompt you for certain things. 
Some things are mandatory.
     Running THDINSTL.EXE followed by the full path and filename to your
version 4 or 5 THDPRO.EXE will cause it to take all the settings from 
that version and place them into version 6.
     THDINSTL.EXE also accepts "/NOMOVE" as a parameter. This option causes 
THDPRO.EXE to suspend all of it's moving and renaming of files. This option 
is recommended ONLY if the BBS program that you use suffers problems when 
unable to locate the file moved or renamed by THD ProScan. This setting is 
reset each time THDINSTL is run and must be used every time in order to
maintain the "No Move" option.

        The use of "ù" (alt 249) is forbidden in ALL entries in
        the installation. If used, the string in which it was used will
        be "CUT" down to the character immediately preceding it. This 
        will result in unpredictable results. DO NOT use that character.
 ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
 º A-- BBS name              -- Your BBS Name                              º
 º B-- Comport               -- 2     | Local Comport     -- 3             º
 º C-- Test Drives           -- C: D: E:                                   º
 º D-- Reboot?               -- N                                          º
 º E-- Drop Virus uploader   -- Y                                          º
 º F-- Protect "AV" zip files-- Y                                          º
 º G-- THDPro Log size       -- 50000                                      º
 º H-- BBS directory         -- D:\BBS                                     º
 º I-- Reject Directory      -- D:\BBS\DLS\SYSOP                           º
 º J-- Files to be added     -- D:\MYLOADER.TXT                            º
 º K-- Files to remove       -- README.ROS BBSAD.*                         º
 º L-- Comment File          -- D:\BBS\UTILS\COMMENT.TXT                   º
 º M-- File dates            -- Limited to 15 days.                        º
 ºIf any of the above is incorrect, Enter the corresponding letter         º
 ºPressing [enter] will move to the next checking screen                   º
 ºPress [enter] or letter to correct --->                                  º
 ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
"BBS NAME"
                This of course could be your name or alias if you prefer, 
                BUT something must be entered.
                This entry MUST be between 4 and 35 characters in length.

"COMPORT - Local Comport"

                This MUST be a valid comport as the tester will output to
                the comport on every run. (the comport need not be active to
                run the scanner, but must exist). A comport of "0" may be
                selected if you wish to suppress all remote output. (useful
                if you wish to test a file while online to a BBS).
                      Local comport is a comport which you would like THD
                ProScan to always treat as a local only comport. Useful for
                sysops who use a node of their BBS strictly for local
                logons. This option simply tells THDPRO.EXE that if the
                comport sent is {the local comport} to use comport 0
                instead.
"TEST DRIVES
                This is a list of valid drives that THD ProScan can use
                to test the archives.
"REBOOT"
                Do you wish THD ProScan to Reboot the computer after
                finishing it's testing if it finds a virus?
"DROP VIRUS UPLOADER"
                Do you wish to drop carrier (hang up) on users who
                upload virus infected files?
"AV PROTECTION"
                Do you wish to NOT modify "Zip" files with a valid "AV"?
"THD PRO LOGSIZE" 
                Multiple choice of the maximum size to write to the 
                log file. After exceeding this size, the next test will 
                rename that file and create a new THDPRO.LOG file.
"BBS Directory" 
                This directory need not be your BBS directory. It can be 
                any existing directory where you would like to keep the 
                "log" file created by the tester. This is also the 
                directory you will be in at the completion of a successful 
                test.
"REJECTED DIRECTORY"
               This is the directory into which you wish files which fail 
               the scan portion or cannot be tested should be "moved".
"FILES TO BE ADDED"
                Files that you wish to be added to every archive tested.
                You can enter individual filenames (wildcards supported).
                OR a single directory with "*.*".(max 40 characters)
"FILES TO REMOVE"
                A list of files to remove from each archive tested.
                Wildcards are supported (40 characters max)
"COMMENT FILE"
                The full path to a file to be used as an archive comment
                (Will only be inserted in those file types which allow
                more than a single line comment).
"FILE DATES"
                Can be limited by "AGE" or by "DATE" or not at all. This 
                date limitation is based on the files INSIDE the archive.
                The archive date itself is not considered in this 
                calculation. Be very care how you use this function.
                GIF and TD0 files are not subject to date checking.
 ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
 º N-- Scan.exe path         -- D:\SCAN.EXE                                º
 º O-- PkZip.exe Path        -- D:\PKZIP.EXE                               º
 º P-- PkunZip.exe Path      -- D:\PKUNZIP.EXE                             º
 º Q-- Arj.exe Path          -- D:\ARJ.EXE                                 º
 º R-- Lha.exe Path          -- D:\LHA.EXE                                 º
 º S-- Pak.exe Path          -- D:\PAK.EXE                                 º
 º T-- PkArc.com Path        -- D:\PKARC.COM                               º
 º U-- Pkxarc.com Path       -- D:\PKXARC.COM                              º
 º V-- Hyper.exe Path        -- D:\HYPER.EXE                               º
 º W-- Giftest.exe Path      -- D:\GIFTEST.EXE                             º
 º X-- TDcheck.exe Path      -- D:\TDCHECK.EXE                             º
 º Y-- Hacklist Path         -- D:\HACKLIST.TXT                            º
 ºIf any of the above is incorrect, Enter the corresponding letter         º
 ºPressing [enter] will complete the installation.                         º
 ºPressing "Z" will take you back to the previous option screen.           º
 ºPress [enter] or letter to correct --->                                  º
 ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

"????????.??? PATH"
                All of the above which are configured MUST include full 
                drive\path\filename in order for the tester to operate 
                correctly.
                Of the above... only "SCAN.EXE" is absolutely mandatory.
                The others should be configured as needed to test the
                corresponding file types.
                                         
"HACKLIST PATH" 
                Hacklist Path is the complete path and filename to a file 
                which contains a list of file "names". This file can not 
                contain extensions or the "." between the name and extension.
                The "COL" files contained in the "Hack Report" can be used 
                "as is" for this purpose.
                If you wish to create your own list of undesirable files, 
                you need simply create a file which consists of filenames. 
                One name per line and all in capital letters. The following 
                would be acceptable as a hack list.

                PKZ201
                HACKFILE
                GARBAGE

                If this were your list then all files with those names 
                (regardless of their extensions) would be failed.
                This option can be skipped by pressing "enter" when prompted.

        The final screen asks about "Heuristic testing". This screen offers 
the option of heuristic tesing of files through the use of either F-PROT.EXE 
or TBSCAN.EXE. The name of these files must be precisely "TBSCAN.EXE" and 
"F-PROT.EXE" as the tester will only run them if they are identified by 
their proper name. These testers will almost definately give false positive 
readings and I STRONGLY suggest that you read their accompanying documentation 
before deciding to use them.
        THD ProScan will NOT fail files based on the result of these tests
and includes the option for your information only. All test details are kept 
in a logfile called "HEURIST.LOG". Only files which report possible problems 
will result in entries to this log. This log will be in the same directory 
as your THDPRO.LOG file and will NOT be subject to a size limitation. As a 
result, you will need to delete this logfile manually on occassion to avoid 
it becoming too large.
        Pay special attention to the habit of these testers to report false 
positives. Many normal files can do things in a way that might cause these 
testers to warn you of "possible" danger. DO NOT assume that the files are 
bad simply because these testers detect suspicious code. However if you 
have the ability, you will want to treat these files with a little added 
care before assuming they are safe.
        My personal preference of the two testers is ThunderByte's TBSCAN.
It is faster than F-PROT and requires less memory. On the other hand F-Prot 
gives fewer false detections. Keep in mind that F-PROT.EXE may require more 
memory than you have available to you and that it will not test files if 
there is insufficient memory.
        Neither of these two testers is used to detect "known" viruses 
(although they both have the ability) and support in that capacity is 
unlikely to be introduced in the near future. (But you never know)

All entries which require a "directory" require that there be no ending "\" 
at the end of the path. All Filename entries require full path and filenames.
     The entries made in the installation MUST NOT exceed 40 characters
per entry. If you enter more than 40 characters the entry will be accepted,
but cut down to the first 40 characters. However, if file paths are cut by 
this process, the results are totally unpredictable. If any of your entries 
wraps on the final two screens of the install.. THEY WILL NOT FUNCTION as 
intended and you will need to use files in a different location than those 
entered.
     Although the program could possibly accept filenames without paths in 
some instances, I STRONGLY suggest you not accept such entries and modify 
them to include a full path.

The install will attempt to locate the "SCAN and ARCHIVE" files that you 
     wish to use for testing. As well as the correct number of drives that 
     are available (of which THD ProScan can use a maximum of 3).
If you read the instructions given for each step during the install process 
     and follow them exactly, you should encounter no problems at all with 
     the setup procedure. The install can be exited at any time by pressing 
     "CTRL-BREAK". No information from that session will be saved. (Unless 
     perhaps you manage to press it while the program is in the middle of 
     saving the information you have entered)

                              THDPRO.DOC
                          -You're reading it

                              THDDEMO.COM
     A simple demonstration of the user side view of what happens while the 
scanner is running. This is included just in case you have never seen this
tester in action before. Your side will display the various utilities 
performing their duties and a short explanation of what the tester is doing.
                              
                              "THE TESTER"

     This is my first ever "real" program. It was made to satisfy a number 
of people who saw my "batch program", THDscan, but were unwilling to use it 
based on it's dependency on 4DOS or NDOS.
     The reason that this program uses 100k of memory is due to a very large
"stack" segment which is reserved for the use of "imbedded" archives. By 
reserving such a large stack, the program is able to run recursively for
much longer and thus test imbedded archives far beyond the first level.
I may reconsider the "size" of the reserved portion in later versions. But I
trust that most "shells" from BBS programs can leave enough memory for this
program to run as is.
     This program is just as secure as THDscan and more secure than Ziplab or
PKINSERT. There is no way to change the "way" this scanner operates (without
hacking it) for a good reason. Even some of the most noted upload testers 
make a very serious flaw in the way they handle uploaded archives. By not 
allowing the user to change these settings, I avoid someone opening one of 
those "all too evasive" back doors and hacking into your system. So please 
don't ask me to change the parameters that this program uses. They are that 
way for a reason. (I will of course be happy to change any that prove to be 
incorrect or cause "real" problems).
     This scanner will exit with one of 7 DOS errorlevels.
ERRORLEVEL 0 - All tests were passed satisfactorily.
               - The scanner will also exit with this errorlevel under
               a number of "odd" circumstances which will avoid having
               a file fail due to some unforeseen difficulty.(This includes
               failing to supply a proper path to the file to be tested and
               a number of other small things)
ERRORLEVEL 1 - An imbedded archive failed the CRC test.
ERRORLEVEL 3 - The file has failed due to the date restriction.
ERRORLEVEL 4 - The file was failed for being on the Hack list.
ERRORLEVEL 5 - An imbedded archive failed the CRC test due to a disk read 
               error. (used by some BBS programs to determine if the file
               is to be resumed later.)
ERRORLEVEL 10- A virus was detected during the "scan".
ERRORLEVEL 15- The main archive failed the CRC test.

     The reason for having an errorlevel 1 exit, is that this tester 
originally did recognize imbedded archives by name, And as such "could" 
have attempted to unarchive a file with the same extension as a valid archive 
format without that file actually being an archive. This of course would 
cause the file to fail the CRC test. By setting the "errorlevel for success" 
in your BBS program to "1" you could avoid failing these files. However, I 
suggest that the errorlevel be set to "0" as no reputable programmer would 
use the extensions of known archivers to name files of another format. But 
it is, of course, your option.
        This is left over from version 1. And although the reasoning is
no longer accurate. I thought that there may still be some persons out
there that use it. If not.. then there is no loss.

        The operation of the scanner could not be simpler. You need simply
run THDPRO.EXE while supplying it with the FULL path and filename of the
file to be tested. I STRONGLY suggest that you also supply the full path
and filename to THDPRO.EXE as well (not necessary but it too can help to
reduce hacking). So the proper syntax would be as follows...

        C:\UTILS\THDPRO.EXE D:\NEWUPS\TESTFILE.ZIP
        {Where THDPRO is located in "C:\UTILS" and the file to be tested
        is "TESTFILE.ZIP" which is located in "D:\NEWUPS"}

        The tester optionally accepts one other parameter. That second 
parameter can be a single digit between 0 and 8. This parameter is the 
number of the comport to be used for remote output and is only necessary if 
you wish output to a comport other than the one specified during the 
install. Using "0" will not send any remote output. Numbers between 1 and 8 
will send to the comport of the corresponding number. If run without 
parameters, It will simply display the correct syntax. ERRORLEVEL 0 will be 
returned in any event where a file is not tested (to avoid the BBS software 
deleting files due to improper syntax).
        While geared toward the testing of archived files, The tester will
viruscan any file type for which it is not configured. So having your BBS 
use this tester to scan "EXE" and "COM" files is an excellent idea. (The 
addition of "self extracting" testing makes this a good idea as well.) The
passing or failing of such files will be based solely on the result of 
the scan and no other operations will be attempted on the file aside from
the heuristic scan. Any valid filename can be passed if you wish it to be 
"scanned". I suggest that you configure your BBS to "test" all files with 
"executable" extensions as well as any "OVL/OVR" files.


NOTES-
     If a file fails the scan portion or is for some reason unable to 
be tested, the file will be moved to a directory you specify. Priority 
is given to a "File Allocation Table" move. Thus if the destination drive 
is the same as the source drive, only the "FAT" will be modified (this 
allows a 4 megabyte file to be moved in less than 1 second.) If the source 
and destination differ then the file will be moved by "copying" it to the 
destination and deleting the original (if the copy was successful). If the 
file cannot be moved for whatever reason, it will be renamed with an 
extension of "THD" (if it could not be tested) or "VIR" if it failed the 
viruscan, it will be renamed during the move if it was virus infected 
regardless of success of the move operation).
     This programs creates and removes a directory called "THDTEMP.$$#". 
Where "#" represents a number between 0 and 8. If you have a directory which 
could have the same name as one created by this program... Either rename the 
directory or do not allow that drive to be used for testing. There is no 
recovering from the removal of this directory.
     This program depends on the fossil driver to send messages to the user. 
If no fossil is active, the testing process will still occur, but the user 
side will be blank. The fossil is also used to drop carrier and/or reboot 
the system if you have chosen those options in the installation.
     This program no longer requires the remote user to have "ANSI.SYS". 
If the user does not have this, he/she will see the a "bare bones" 
description of what the tester is doing. There will be no "glitz" on
the ASCII output. 
     I strongly suggest that after the installation is complete and the
executable file is in it's permanent place, that you make it a read-only 
file. This will be yet another deterrent for "wanna-be" hackers who would 
attempt to overwrite this file.
     The only known problem with this tester is that if an unscrupulous 
person attempts to overwrite certain files on your system, the program will 
hang pending "user input". IF YOU EVER see such a prompt on your system 
while this program is running, DO NOT ALLOW the overwrite. This program 
accounts for all "normal" circumstances of overwrite attempts and will hang 
only if the user finds a way to overwrite files outside of this testers 
control. Allowing such overwrites could result in total disaster.

           This  program  and  all  of  its  associated names, files,
     logos and makeup are  Copyright 1992, 1993 PainSoft.  Absolutely
     no duplication  in  whole  or  in  part  is  allowed.  With  the
     exception of  duplication of  the entire  archived  set of files
     for  distribution to  those  in need of it's  services.  None of
     the copyrighted  material may be  changed in any way,  except by
     the author.  Changes made by  the author's "original/unmodified"
     installation program will be considered to have been made by the
     author for  the  purpose  of this  copyright.  The files  may be
     rearchived in  ANY fashion which requires them to be restored to
     their original condition before use. (Portions Copyright Borland
     International). The  Author  accepts no  responsibility  for the
     actions of this program.  It is FREEWARE  and  NO  charge may be
     made for it's distribution. It's NOT a commercial product and as 
     such the ONLY acceptable charge for it will be "actual, physical
     cost of duplication". I do not profit from it monetarily and any
     attempt  of other  persons to  do  so  shall  be  considered  an 
     infringement of my copyright.
       Other products mentioned are copyrighted by their respective
     owners and  include their own restrictions for use.  Please be
     sure to  register those products if requested by the copyright
     owners.

Thank You for taking the time to read this document. I hope this upload 
tester serves you well and helps to keep your system free of viral infection 
and a little safer from potential hackers.
                 David Muir
                     of
                ..PainSoft..