================================================================================
         DOSMAX.EXE :  Ver. 1.5, Copyright (1992) by Philip B. Gardner
================================================================================

  DOSMAX.EXE is a device driver which will maximize the use of low memory
  by moving MS-DOS 3.1 and above system data to upper memory blocks provided
  by your upper memory manager.  It is not necessary to use any other
  programs to create upper memory data types like FILES, BUFFERS, FCBS,
  or LASTDRIV from Quarterdeck's QEMM386.  These data types are referred
  to as "sub-segments" in the rest of this document.

  In addition, if you are a DOS 5.0 user and are loading DOS high, then
  DOSMAX can prevent DOS from loading into the HMA and move the code block
  to an upper memory block.  This improves performance and allows programs
  which use the HMA more efficiently to utilize the HMA instead.  Such 
  programs include Microsoft WINDOWS and Quarterdeck's DESQVIEW.  DOSMAX
  can also move a portion of COMMAND.COM into an upper memory block instead
  of the HMA.  This feature recovers space in low memory which is available
  when DOS is in the HMA.

  Support is automatically provided for Microsoft WINDOWS 3.0 so that all
  FILES in your CONFIG.SYS can be loaded high.  Normally this would prevent
  WINDOWS from running, but the problem is circumvented.

  Support is provided for:

    * allowing DOS the HMA, but still moving the sub-segment data types
    * forcing DOS low, sub-segments still moveable
    * moving only the DOS SYSTEM code block into upper memory
    * providing only WINDOWS high file support (DOS 4.x and above)
    * moving a portion of COMMAND.COM into high memory instead of the HMA
    * moving the primary COMMAND.COM's environment (master environment)
    * DOS Versions 3.1 - 3.31, DOS 4.x, and DOS 5.x (or better?)

  DOSMAX automatically moves all the data that can be moved dependent only
  upon the availability of upper memory.  It will automatically stop moving
  data when it determines that memory would be fragmented if the move was
  completed.

  Finally, a command line mode is provided to move the Master Environment,
  control Windows support, and check and report on the status of the high
  memory area reserved for COMMAND.COM.

================================================================================

(Requirements)::

        * 286 processor or better
        * Requires MS-DOS Version 3.10 or better
        * For maximum memory, set STACKS=0,0 in CONFIG.SYS

================================================================================

(Installation)::

        (CONFIG.SYS)::

        Installation of DOSMAX.EXE requires modifying the contents of
        your CONFIG.SYS file.  You must configure DOS not to use hardware
        STACKS if the sub-segment data types are to be moved.

        STACKS=0,0              (No Stacks to maximize memory)

        DOS 5.0 should configure DOS to load high into the HMA.  The UMB
        parameter is optional, since both DOS 5.0 upper memory management
        and XMS upper memory blocks are supported.

        DOS=HIGH[,[UMB][NOUMB]] (Both DOS 5.0 UMB's and XMS UMB's supported)

        Add a DEVICE= line for DOSMAX.EXE in your config.sys.  DOSMAX
        should be loaded before the XMS and UMB memory manager.  It is 
        also recommended that DOSMAX is the very first device driver, but
        not absolutely necessary.  The /A0 option disables high memory
        support for COMMAND.COM.  This switch should be used if your
        primary shell is not COMMAND.COM.

        DEVICE=DOSMAX.EXE [/A0][other options]
        DEVICE=(Memory Manager)

        One advantage of using DOSMAX.EXE, is that the BUFFERS=, FCBS=,
        FILES=, and LASTDRIVE= parameters may be configured normally.

        BUFFERS=XX[,YY]         (XX = # of buffers, YY = lookahead cache)
        FCBS=XX,YY              (XX = # of FCBS, YY = # of protected FCBS)
        FILES=NN                (NN = # of system files)
        LASTDRIVE=Z             ( Z = Last reserved drive)

        Remove all INSTALL= lines from your CONFIG.SYS, or the sub-segment
        data types will not be moveable.  This action is not necessary if
        the program leaves no resident portion of itself in lower memory.

        REM INSTALL=(TSR)       (Remove to maximize memory)

        By default, DOSMAX.EXE will generate a message for each successful
        operation or event.  The display then pauses to allow you to
        read the report.  After you are satisfied with the configuration
        and you want to disable the REPORT and PAUSE feature, use:

        DEVICE=DOSMAX.EXE /R- /P- 

        (AUTOEXEC.BAT)::

        It is not necessary to modify the contents of AUTOEXEC.BAT, but
        since DOS data creators like FILES and BUFFERS are no longer
        required, it is recommended that these lines are removed

        REM BUFFERS=XX          (Remove FILE and BUFFER creator TSR's)
        REM FILES=NN

        In addition, the AUTOEXEC may be modified to automatically move
        the master enviroment to high memory.  This feature will only
        work with COMMAND.COM and is unlikely to work with other primary
        shells like 4DOS from J.P. Software.  4DOS already has a feature
        to move most of the primary shell and the master environment high.
        Use the /E- switch to disable the master environment move.

        DOSMAX.EXE [/E-]        (Add a command line invocation of DOSMAX)

        By default, DOSMAX.EXE, invoked from the command line, will generate
        a message for each successful operation or event.  The display will
        not pause in the command line mode unless the /P+ switch is used.
        After you are satisfied with the configuration and you want to disable
        the REPORT feature, use:

        DOSMAX.EXE /R- [/E-]
 
        All switch options and possible messages for DOSMAX are detailed
        below:

================================================================================

(Syntax)::

        The only thing to remember about syntax for the command line is
        that just about anything works.  What this means is that you
        should be able to type in the options on the command line the
        way they make sense to you.

        To illustrate this point, the following command line example
        is mutated several different ways.

        DEVICE=DOSMAX.EXE /H+ /R- /P- /A0
        DEVICE=DOSMAX.EXE -H+ -R- -P- -A0
        DEVICE=DOSMAX.EXE H R- P- A0
        DEVICE=DOSMAX.EXE HR-P-A
        DEVICE=DOSMAX.EXE -H+-R-P-A

        ... and so on.

(Switch Options)::

        (REPORT)::      R[+ or -]        (toggle:  default +)

        Use /R- to disable the report after you are satisfied
        with the configuration of DOSMAX.EXE

        (PAUSE)::       P[+ or -]        (toggle:  default +)

        Use /P- to disable the pause after the report as long
        as there are no errors or warnings.

        (WINDOWS)::     W[+ or -]        (toggle:  default +)

        Use /W- to disable Windows high file support.  This
        switch is mainly provided for diagnostic purposes.

        (SKIPSUBS)::    S[+ or -]        (toggle:  default -)

        Use /S+ to tell DOSMAX to not move sub-segments data types.
        The switch is provided mainly for diagnostic purposes, but
        may be useful when not enough high memory is available to
        move both the DOS code block and the sub-segments, or if
        you find this feature does not work in your configuration.

        (LOW)::         L[+ or -]        (toggle:  default -)

        Use /L+ to allocate DOS code block in low memory.  As
        long as DOS=HIGH is still in your CONFIG.SYS, the
        sub-segments should be moveable.  This switch may be useful
        if there is not enough high memory to load both the DOS code
        block and the sub-segment data types into High Memory and a
        free HMA is desired.

        (HIGH)::        H[+ or -]        (toggle:  default -)

        Use /H+ to allow DOS to load into the HMA anyway.  This
        switch may also be used with DOS=LOW, since DOSMAX simply
        ignores whether DOS is HIGH or LOW when it initializes
        and checks later to see if it is safe to move sub-segments.

        (NOPAUSE)::     N[+ or -]        (toggle:  default -)

        Use /N+ to never pause after the report, even if there
        are errors.  This switch can be used if your configuration
        generates a warning or error message which you choose to ignore.

        (VDISKHDR)::    V[+ or -]        (toggle:  default -)

        Use /V+ to use an alternate method of stopping DOS from
        allocating the HMA.  This switch is only necessary if
        DOSMAX reports that the DOS version is incompatible, and
        it will only work with memory managers which can detect a
        VDISK Header in the HMA when the memory manager initializes
        and mark's it as allocated.

        (FILE SIZE)::   Fnn                (value:  nn = 59 )

        Use /Fnn to set the System File Size:  The upper limit of nn
        is 61 in device mode, and 82 in command line mode.  The lower
        limit is 35.  Values other than the MS-DOS 4.0 - 5.0 System 
        File Size of 59 are only allowed if the true MS-DOS version is
        greater than 5.0.  The /Fnn switch is only necessary if DOSMAX.EXE
        can't determine the System File Size automatically.

        (ALLOCATION SIZE)::     Annnnn    (value:  nnnnn = 2080)

        Use /Annnnn to set the number of bytes reserved in upper memory
        for COMMAND.COM and other DOS 5.0 and above programs which have
        the capability of moving a portion of themselves into the HMA.
        These programs use INT 2Fh Function 4Ah to allocate a fixed number
        of bytes from the HMA.  DOSMAX has the capability of emulating
        this function in high memory.  By default, DOSMAX reserves 2080
        bytes, which is the space needed to shrink COMMAND.COM.  To
        reserve more memory, increase this value.

        The command line mode of DOSMAX reports the size and allocation
        status of this area.  If the amount allocated or requested is not
        equal to the amount reserved, DOSMAX will report what the proper
        value should be.  Users of replacement shells like 4DOS.COM from
        J.P. Software, should disable this option with /A0. Disabling the
        option or using the report feature of the command line mode to
        set the exact amount of memory required, is recommended since
        INT 21h 3306h (Get True Ver.), which is also hooked by DOSMAX,
        must return with a bit set which indicates that DOS is in the HMA
        until the amount of memory reserved is completely exhausted.

        (ENVIRONMENT)::         E[+ or -]       (toggle:  default +)     

        Use /E- to disable finding and moving the master environment to
        upper memory.  This feature is for COMMAND.COM users, so, the
        option should be disabled for other shells such as 4DOS from
        J.P. Software which have their own option to move the environment
        to upper memory.  DOSMAX does not support the master environment
        for these alternative shells independently and the feature is
        unlikely to function with these alternative shells.

        (TEST ENVIRONMENT)::    T[+ or -]       (toggle:  default -)

        Use /T+ to enable a master environment move with a special test
        mode enabled.  This feature implements an extra level of security.
        The algorithum verifies that the master environment is both found
        and that it is moveable, by testing with a shell command which
        affects the master environment through the INT 2Eh interface.  It
        is recommended that this switch not be used in a batch file.  When
        the shell processes an INT 2Eh command, it first completes the
        current batch file, then performs the INT 2Eh command.  This
        means that if DOSMAX.EXE is run from the AUTOEXEC.BAT file to move
        the master environment and the /T+ option is set, then its command
        line always appears to be the last line of the batch file.  Do not
        execute DOSMAX.EXE from a nested batch file with the /T+ option.

        *  everything in square brackets "[]" is optional

(CONFIG.SYS Line)::

        DEVICE=DOSMAX.EXE [/ or -][R[-]P[-]W[-]S[+]L[+]H[+]N[+]V[+]FnnAnnnnn]

        device mode default: /R+P+W+N-A2080

        *  Report status messages
        *  Pause after report
        *  Enable Windows Support
        *  Pause on errors or warnings
        *  Reserve 2080 bytes for INT 2Fh Function 4Ah (COMMAND.COM)

(Command Line Mode)::

        C:\> DOSMAX.EXE [/ or -][R[+]P[+]W[-]N[+]E[+]T[-]Fnn]

        command line mode default:  /R+P-W+N+E+T-   (S,L,H,V, and A ignored)

        *  Report status messages
        *  Don't pause after report
        *  Enable Windows Support
        *  Never Pause even on errors or warnings
        *  Find and move the master environment
        *  No special environment test

================================================================================

(Report Format)::

        DOSMAX.EXE :  Ver. 1.5, Copyright (1992) by Philip B. Gardner
             ERROR :  (Error Messages)
           WARNING :  (Warning Messages)
            ADVICE :  (Advisory Messages)
                   :  (Report Messages)
                   :  (Allocation Status)
             PAUSE :  Press any key to continue... 

================================================================================

(Error Messages)::

        MS-DOS version 3.10 or above is required
        DOS is HIGH or in ROM already
        Include DOS=HIGH in CONFIG.SYS
        XMS manager already installed
        Extended Memory not available
        DOS version is not compatible
        Can't load in High Memory
        Couldn't write VDISK Header
        Device not found, or version mismatch

================================================================================

(Warning Messages)::

        Unknown option in command line
        Extra characters on command line
        Unable to free HMA
        A20 Not Disabled
        STACK Sub-Segment present
        Possible STACK Sub-Segment present
        DOS Sub-Segment list is unmoveable
        System File Size not determined or out of range
        Unable to validate System Data area
        Couldn't size System File Table
        Couldn't size System FCB Table
        Couldn't trace Buffer Chain
        Couldn't find Lastdrive Array

================================================================================

(Advisory Messages)::

        Should be the first DEVICE= in CONFIG.SYS
        Set STACKS=0,0 in CONFIG.SYS
        Possible INSTALL= in CONFIG.SYS
        Try using /Fnn switch
        Try using /V+ switch
        For maximum efficiency use /A00000

================================================================================

(Report Messages)::

        HMA was reserved, but is now free
        A20 Disabled
        DOS System forced low
        DOS System in HMA
        DOS System not in HMA
        DOS Sub-Segments skipped
        Windows support enabled
        Windows support disabled
        System File Size set to 00
        Found 00000 bytes allocated of 00000 bytes

================================================================================

(Allocation Status)::

        SYSTEM   moved to 0000
        Not enough Hi Memory for SYSTEM  
        LASTDRIV moved to 0000
        Not enough Hi Memory for LASTDRIV
        BUFFERS  moved to 0000
        Not enough Hi Memory for BUFFERS 
        WKBUFFER moved to 0000
        Not enough Hi Memory for WKBUFFER
        FCBS     moved to 0000
        Not enough Hi Memory for FCBS    
        FILES    moved to 0000
        Not enough Hi Memory for FILES   
        COMMAND  space at 0000
        Not enough Hi Memory for COMMAND

================================================================================

(Sub-Segment List)::

        The Sub-Segment List is searched from bottom to top for a block
        of moveable sub-segments, then moved in reverse order.  The
        termination of the list must be the MCB of the PSP of DOSMAX.EXE.
        This prevents fragmentation of memory.  This means INSTALL=
        should not be used in CONFIG.SYS, and STACKS=0,0 must be used,
        or else the sub-segments will not be moveable.

        The following chart attempts to show what can and cannot be moved
        with DOSMAX.EXE

                        Sub-Segment Type                Not Moved  Moved
        ----------------------------------------------- ---------  -----
        "D"        DEVICE DRIVER                            x 
        "E"        DEVICE DRIVER APPENDAGE                  x
        "I"        IFS (Installable File System) DRIVER     x
        "F"        FILES=                                            x
        "X"        FCBS=                                             x
        "C"        BUFFERS /X Option (EMS workspace area)            x
        "B"        BUFFERS=                                          x
        "L"        LASTDRIVE=                                        x
        "S"        STACKS=                                           x
        "T"        INSTALL=                                 x (ignored)

================================================================================

(Changes)::

    (Version 1.1)::

    (1) Fixed problem not cleaning up properly, when DOS goes to HMA
        anyway, (only /V+ switch, and some XMS Managers).

    (2) Fixed problem that occurred if no XMS UMB's available, and DOS 5
        UMB's tried, and if no DOS UMB's available either (not just not
        enough), memory was allocated from low memory, even though
        allocation strategy was set to try UMB's only.  Made sure UMB
        Link state was set properly.

    (3) Added support for DOS Versions 3.10 - 3.31 and DOS Version 4.x

    (4) Improved File Size determination algorithum

    (Version 1.2)::

    (1) Improved detection of DOS=LOW, and reduced the possibility of
        an errant "Should be the first DEVICE= in CONFIG.SYS" message.

    (Version 1.3)::

    (1) Added support for INT 2Fh, Function 4Ah, so that COMMAND.COM
        (and others??) can move a portion of their code to high memory
        too.  For COMMAND.COM users with DOS 5.0, this saves 2.1k of
        low memory.  Added the /Annnn switch to support this feature,
        plus an allocation status check for the command line mode.
        4DOS users should disable this feature with option /A0.

    (Version 1.4)::

    (1) Added capability to find and move the master environment for
        COMMAND.COM users.  Also implemented a special test mode with
        the /T+ option, which verifies that the master environment
        has been found and that it is moveable.  This test mode should
        only be necessary for diagnostic purposes.

    (Version 1.5)::

    (1) Added base 10 number display for /A parameter and changed
        System File Size message to base 10.

================================================================================