CHIPSET.EXE is a small program that simply checks to see if your PC
has one of the memory controllers required to use The Last Byte
Memory Manager.

To see if your PC has one of the supported memory controllers, simply
enter the following command at the DOS prompt and follow the prompts:

	A>CHIPSET

If your PC has one of the supported devices, then The Last Byte
Memory Manager will work on your PC, and you will be able to load
device drivers, TSRs, DOS buffers and more into upper memory above
640k.

If your PC uses another kind of chipset, it may not be supported for
one of the following reasons:

(1) No shadow ram hardware:
---------------------------

  	Some chipsets do not provide shadow ram support.

        Examples: VLSI Technologies 82C100 series
		  Western Digital chipsets
		  Texas Instruments TACT82300 series
		  Early Suntac chipsets (ST62BC001-6)
		  United Microelectronics Corp. UM82C231


(2) No shadow ram read/write mode:
----------------------------------

	Some chipsets have shadow ram, but it can only be put into
	either write-only mode (for copying rom contents to ram), or
	read-only mode (to prevent accidental writes into what's
	supposed to be a copy of rom).

      	Examples: ACC Microelectronics chipsets
		  Headland Technologies chipsets
		  G2 chipsets


(3) DMA (Direct Memory Access) can't get to the shadow ram:
-----------------------------------------------------------

  	Many device drivers and TSRs use either use DMA directly, or
	else they employ disk buffers that DOS accesses via DMA.
	The hardware design of some memory controller chips prevent
	DMA from accessing the shadow ram, and thus loading this kind
	of software into shadow ram memory is pointless.

	Note: In some cases, a portion of their shadow ram memory may
	be made usable by using the chip's hardware support for
	expanded memory which typically supports DMA.  However, this
	precludes use of The Last Byte Memory Manager together with
	an expanded memory manager specifically designed for these
	chips.

        Examples: VLSI Technologies VL82C286 & VL82C386 TOPCAT


(4) Controller incompatible with design of The Last Byte Memory Manager:
------------------------------------------------------------------------

	The Last Byte Memory Manager is table-driven, making it
	relatively easy to adapt to different memory controller
	architectures, but there are limits!  

	Examples: Zymos chipsets
		  United Microelectronics Corp. (UM82C384,'388,'389)
		  Forex Computer Corp. FRX36C100
		  Silicon Integrated System Corp. (SIS) chipsets


(5) Shadow ram control can be made inaccessible once configured:
----------------------------------------------------------------

  	Some controllers are designed so that they can be "locked"
	at the end of software initialization, requiring a hardware
	reset to unlock, and thus preventing The Last Byte Memory
	Manager from accessing the controller.

        Example: Intel 82335, 82335SX


Some of these chips, however, have hardware support for LIM 4.0 EMS,
and thus many of their motherboards come with a EMS device driver
designed specifically to take advantage of this capability.  So in
many cases, you can install this driver first, and then The Last Byte
Memory Manager can use it to manage upper memory.

A free demo version of The Last Byte Memory Manager may be downloaded
from our BBS at the number below Monday through Friday between 5pm
and 8am PST, or 24hrs a day on weekends.  The filename is
TLB-Vnnn.ZIP, where the "nnn" is replaced by the latest version
number.  The demo version is fully functional except that it limits
you to 32k of memory and no more than two device drivers and/or TSRs
loaded into upper memory.

	Key Software Products
	440 Ninth Avenue
	Menlo Park, CA 94025
	(415) 364-9847