THE LAST BYTE MEMORY MANAGER (tm)


                       An Upper Memory Manager for MS-DOS




                                  Version 2.00






                              Copyright (C) 1990-92

                               All Rights Reserved


                                       by


                              KEY SOFTWARE PRODUCTS

                                440 Ninth Avenue
                          Menlo Park, California 94025

                                 (415) 364-9847














        The Last Byte Memory Manager is a trademark of Key Software Products.
         MS-DOS and Windows 3.0 are trademarks of Microsoft Corporation.
             DR-DOS is a trademark of Digital Research Incorporated.
                      4DOS is a trademark of J.P. Software.
                     Hyperdisk is a trademark of HyperWare.
            Other company trademarks are used with the company name.



        



                        THE LAST BYTE MEMORY MANAGER (tm)


                                Table of Contents


        CHAPTER 1 - INTRODUCTION        ...........................    4
           1.1  Important Advantages       ........................    4

        CHAPTER 2 - SYSTEM REQUIREMENTS       .....................    6
           2.1  Supported Hardware       ..........................    6
           2.2  Checking Compatibility Using CHIPSET     ..........    8

        CHAPTER 3 - DISTRIBUTION FILES       ......................   11

        CHAPTER 4 - GETTING STARTED       .........................   13
           4.1  Testing LASTBYTE.SYS HIGHDRVR.SYS and HIGHTSR.EXE     13
           4.2  Mapping Upper Memory with HIGHMEM    ..............   15
           4.3  Running the LICENSE Program     ...................   16

        CHAPTER 5 - DETAILED DESCRIPTIONS       ...................   17
           5.1  LASTBYTE.SYS        ...............................   17
           5.2  HIGHAPND.EXE and HIGHAPND.SYS      ................   23
           5.3  HIGHBFRS.EXE (MS-DOS 3 only)     ..................   25
           5.4  HIGHDISK.SYS        ...............................   27
           5.5  HIGHDRVR.SYS        ...............................   28
           5.6  HIGHEMS3.SYS and HIGHEMS4.SYS      ................   28
           5.7  HIGHENV.EXE        ................................   29
           5.8  HIGHFILE.EXE        ...............................   31
           5.9  HIGHHOLE.EXE        ...............................   31
           5.10  HIGHINST.EXE        ..............................   32
           5.11  HIGHKEY.EXE        ...............................   33
              5.11.1  Options        ..............................   33
              5.11.2  Editing Commands       ......................   33
           5.12  HIGHMARK.EXE        ..............................   35
           5.13  HIGHMEM.EXE        ...............................   36
           5.14  HIGHSPLR.EXE        ..............................   36
           5.15  HIGHTSR.EXE        ...............................   37
              5.15.1  The /NOENV Option      ......................   38
           5.16  HIGHUMM.SYS        ...............................   39
           5.17  HIGHUNDO.EXE        ..............................   40

        CHAPTER 6 - HINTS / SUGGESTIONS / EXPLANATIONS    .........   41
           6.1  The /SIZE Option      .............................   41
              6.1.1  Measuring Load Requirements Using "/SIZE"    .   41
              6.1.2  Achieving Best Fit Using "/SIZE:n1"    .......   42
              6.1.3  Borrowing Initialization Memory Using "/SIZE:n   42
           6.2  The /LOW Option      ..............................   42
           6.3  The /RESTRICT Option      .........................   43
           6.4  The /!NOPAUSE Option      .........................   43
           6.5  Specifying Command Line Options with Indirect Files   43
           6.6  Using the DOS=F000:32 Option     ..................   44
           6.7  Video Display RAM above 640k    ...................   45
           6.8  Video Adapter Bios ROMs     .......................   46



        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



                        THE LAST BYTE MEMORY MANAGER (tm)


           6.9  LASTBYTE.SYS and Expanded Memory     ..............   46
           6.10  Fine-Tuning your Adapter Hardware Configuration      47

        CHAPTER 7 - USE WITH OTHER SOFTWARE     ...................   49
           7.1  Microsoft's FASTOPEN and MODE programs    .........   49
           7.2  Microsoft's SHARE program      ....................   49
           7.3  Microsoft's MS-DOS 5.0      .......................   50
              7.3.1  Using DEVICEHIGH and LOADHIGH     ............   51
              7.3.2  Using HIGHDRVR and HIGHTSR     ...............   51
           7.4  Microsoft's Windows 3.0      ......................   52
              7.4.1  Modifying the Windows SYSTEM.INI File    .....   52
              7.4.2  Positioning an EMS Page Frame    .............   53
              7.4.3  "Unsupported Data Configuration"      ........   53
              7.4.4  HIGHMEM and Windows 386 Enhanced Mode   ......   54
              7.4.5  HIGHDISK and Windows 386 Enhanced Mode   .....   54
           7.5  HyperWare's HyperDisk       .......................   54
           7.6  J.P. Software's 4DOS      .........................   55
           7.7  David Hamilton's BUFFIT      ......................   55
           7.8  Charles Lazo's WAS      ...........................   56

        APPENDIX 1 - HOW TO REACH US     ..........................   57

        APPENDIX 2 - ACKNOWLEDGEMENTS        ......................   58

        APPENDIX 3 - CHIPSET LIMITATIONS       ....................   59

        APPENDIX 4 - LICENSED DISTRIBUTORS       ..................   61

        APPENDIX 5 - LIMITED WARRANTY       .......................   63

























        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Apr 12, 1992    THE LAST BYTE MEMORY MANAGER (tm)               4


                        CHAPTER 1 - INTRODUCTION        


        The  Last  Byte  Memory  Manager is a collection of software that
        can  provide  up to 384k of additional memory to your computer in
        the  upper  memory  area between 640k and 1 meg.  It does this by
        using  left-over  shadow  ram  memory,  existing fixed read/write
        (RAM)  memory, or by mapping expanded memory (EMS) pages into the
        upper area.  

        With  The Last Byte Memory Manager, device drivers, terminate and
        stay  resident  (TSR)  programs,  MS-DOS  disk  buffers,  and the
        master  environment  can  be  moved up into upper memory, leaving
        more   conventional   memory   available   for  your  application
        programs.   Depending  on  your hardware, you may also be able to
        extend  the  total  conventional  memory  from 640k to as much as
        736k.  

        The  Last  Byte  Memory  Manager comes with utility programs that
        use  upper  memory  to  create ram disks, print spoolers, command
        line  recall (history) buffers, emulated expanded memory, and TSR
        "markers"  (to  facilitate  TSR removal).  But best of all, these
        utilities  can  even  use  disabled  shadow  ram  memory normally
        hidden  behind the display buffer, read-only memories (ROMs), and
        other adapter cards.  


        1.1 Important Advantages        

        The  Last  Byte  Memory Manager offers six significant advantages
        over other MS-DOS Upper Memory Managers: 

             o  The  Last  Byte  Memory Manager uses no conventional
                memory.  

             o  The  Last  Byte  Memory  Manager  will work with any
                processor  chip,  even the 8088 used in the original
                IBM  PC.   Many memory managers require a 386 cpu or
                better.  

             o  The  Last Byte Memory Manager does not use protected
                mode  software.   This  means that unlike those that
                do,   The   Last  Byte  Memory  Manager  is  totally
                compatible  with  any  protected  mode software, not
                just Microsoft Windows.  

             o  The  Last  Byte  Memory  Manager doesn't require any
                extended  memory.   Other  memory managers depend on
                the  processor's  ability  to  remap physical memory
                from above 1MB into the upper memory area.  




        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Apr 12, 1992    THE LAST BYTE MEMORY MANAGER (tm)               5


             o  On  motherboards  that  use  one  of  the  supported
                memory   controller  chips,  The  Last  Byte  Memory
                Manager,  unlike  all  other MS-DOS memory managers,
                can  use  the unused shadow ram normally disabled by
                the  display  buffer,  ROMs  or adapter cards.  This
                gives  it  the  unique  ability  to  use all 384k of
                upper memory! 

             o  The  Last Byte Memory Manager does not slow down the
                performance  of  your computer, both because it does
                not  incur  the 5-10% execution overhead inherent in
                protected   mode,   and   because  it  uses  regular
                (full-speed)  memory.  (Some memory managers use the
                actual  EGA/VGA  graphics  buffer  as MS-DOS memory,
                but  the  display  buffer  memory  of  some  EGA/VGA
                adapter  cards  can  be  as much as six times slower
                than regular memory.)  





































        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Apr 12, 1992    THE LAST BYTE MEMORY MANAGER (tm)               6


                     CHAPTER 2 - SYSTEM REQUIREMENTS       


        Fundamentally,  The Last Byte Memory Manager requires version 3.1
        or  later of MS-DOS and some method of implementing memory in the
        upper  memory  area  between  640k  and  1  meg.   Any  Intel (or
        Intel-compatible)  processor  will  do,  including  the  original
        Intel 8088 cpu.  No extended memory is required.  


        2.1 Supported Hardware        

        To  install The Last Byte Memory Manager, your computer must have
        any one of the following: 

             o Fixed  the 32-bit "Built In Memory" installed in some
                Compaq 386 machines), or 

             o  An  expanded memory board (EEMS, LIM 3.2 EMS, or LIM
                4.0 EMS), or 

                ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
                ³ NOTE: Using a LIM 3.2 EMS board is not advised  ³ 
                ³ as a method of providing upper memory.  It pro- ³ 
                ³ vides only 64k of upper memory and prevents ap- ³ 
                ³ plication software from using expanded memory.  ³ 
                ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ 

             o  A  386sx,  386,  486,  or  486sx  processor  and the
                Microsoft  Windows  3.0 or DOS 5 versions of EMM386,
                or 

             o  One of the following shadow ram controller chips: 

        Chips and Technologies:

             82C212 - From the CS8221 NEAT (tm) chipset
             82C222 - From the CHIPS/250 PS/2 50/60 chipset
             82C230 - The PS/2 30 Single Chip Controller
             82C235 - The SCAT (tm) Single Chip AT VLSI chip
             82C241 - From the CS8223 LeAPset (tm) chipset
             82C302 - From the CS8230 386/AT CHIPSet (tm)
             82C307 - From the CS8231 386/AT CHIPSet (tm)
             82C311 - From the CS8233 PEAK 386/AT CHIPSet (tm)
             82C322 - From the CHIPS/280 PS/2 70/80 chipset
             82C351 - From the CS82310 PEAK DM/386 AT CHIPSet (tm)
             82C812 - From the CS8281 NEATsx (tm) chipset
             82C836 - The SCATsx (tm) Single Chip AT VLSI chip
             82C841 - From the CS8283 LeAPset-sx (tm) chipset





        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Apr 12, 1992    THE LAST BYTE MEMORY MANAGER (tm)               7


        ETEQ Microelectronics:

             82C491 - From the Cougar 386DX/486DX chipset

        Forex Computer Corporation:

             FRX36C300 - From the FRX36C300/200 Cache chipset

        Intel Corporation:

             82343 - From the 82340SX Chip Set
             82346 - From the 82340DX Chip Set
             82359 - From the 82350DT EISA Chip Set

        OPTi Electronics:

             82C281 - From the Cache SX/AT chipset (w/posted write)
             82C282 - From the Cache SX/AT chipset (w/o posted write)
             82C283 - From the Block Interleave SX/AT chipset
             82C382 - From the HiD/386 AT chipset
             82C391 - From the 386WB PC/AT chipset
             82C461 - From the Notebook PC/AT chipset
             82C482 - From the HiB/486 AT chipset
             82C493 - From the 486SXWB PC/AT chipset
             82C496 - From the DXBB PC/AT chipset
             82C682 - From the 386/486WB EISA chipset

        Sun Electronics (SUNTAC):

             ST62C202 - From the chipset 20 for 286
             ST62C241 - From the chipset 24 for 386
             ST62C251 - From the chipset 25 for 286 and 386sx

        Symphony Laboratories:

             SL82C361 - From the SL82C360 80386DX/SX chipset
             SL82C461 - From the SL82C460 80486 chipset

        Texas Instruments:

             TACT82411  - The Snake Single-Chip AT Controller
             TACT82S411 - The Snake+ Single-Chip AT Controller

        United Microelectronics Corporation (UMC):

             UM82C212 - From the UM82C210 386SX/286 AT Chip Set
             UM82C481 - From the UM82C480 50Mhz 80486 Chip Set







        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Apr 12, 1992    THE LAST BYTE MEMORY MANAGER (tm)               8


             ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
             ³ NOTE: The UM82C212 is indistinguishable from    ³ 
             ³ the Chip & Technologies 82C212.  CHIPSET and    ³ 
             ³ LASTBYTE.SYS will identify it as the latter.    ³ 
             ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ 

        VLSI Technology:

             VL82C202 - PC/AT-Compatible High Speed Memory Controller
             VL82C320 - From the TOPCAT 286/386sx Chip Set
             VL82C330 - From the TOPCAT 386 DX Chip Set
             VL82C486 - Single Chip, High Performance 486 PC/AT Controller

             ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
             ³ NOTE: There is a pin on the VLSI VL82C202 that  ³
             ³ controls whether or not the shadow ram memory   ³
             ³ has been relocated above 1 meg as extended      ³
             ³ memory.  This pin is usually connected to a     ³
             ³ jumper or DIP switch on the motherboard.  It    ³
             ³ may be necessary to change the jumper or DIP    ³
             ³ switch setting to work properly with this chip. ³
             ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ 

        Not  all  memory controller chips allow use of the entire 384k of
        upper  memory.  Consult the appendix on "CHIPSET LIMITATIONS" for
        further information.  


        2.2 Checking Compatibility Using CHIPSET      

        CHIPSET  is  a program that simply checks to see if your computer
        has  one  of the memory controllers required to use The Last Byte
        Memory Manager.  

                A>CHIPSET 

        CHIPSET  will identify the particular memory controller you have,
        if  any.   If it can't find a memory controller, it will look for
        fixed  memory  in the upper area or expanded memory as a means of
        installing  The  Last  Byte Memory Manager.  If it is successful,
        it  will  give  you  the  option  of automatically linking to the
        INSTALL  program  to  setup  for  use  of  The  Last  Byte Memory
        Manager.  

        CHIPSET  and INSTALL automatically sense whether you have a color
        or  monochrome  display  to  determine how to present data on the
        screen.   However,  you  may  force  the mode by using one of the
        /MONO, /COLOR, or /LCD command line options.  

        If  your  computer  has  one of the listed devices, then The Last
        Byte  Memory  Manager  should  work  on  your  computer.  If your



        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Apr 12, 1992    THE LAST BYTE MEMORY MANAGER (tm)               9


        computer  uses  another  kind of chipset, it may not be supported
        for one of the following reasons: 


             o  Some chipsets do not provide shadow ram support.  

                Examples: VLSI Technologies 82C100 series 
                          Western Digital chipsets 
                          Texas Instruments TACT82300 series 
                          Early Suntac chipsets (ST62BC001-6) 
                          United Microelectronics Corp. UM82C231 


             o  Some  chipsets  have  shadow ram, but it can only be
                put  into  either  write-only  mode (for copying rom
                contents  to  ram),  or  read-only  mode (to prevent
                accidental  writes into what's supposed to be a copy
                of rom).  

                Examples: ACC Microelectronics chipsets 
                          Headland Technologies chipsets 
                          G2 chipsets 


             o  Many  device  drivers  and  TSRs  either  use Direct
                Memory  Access  (DMA)  directly, or else they employ
                disk  buffers  that  MS-DOS  accesses  via DMA.  The
                hardware  design  of  some  memory  controller chips
                prevent  DMA from accessing the shadow ram, and thus
                loading  this  kind  of  software  into  shadow  ram
                memory is pointless.  

                Examples: VLSI Tech. VL82C286 & VL82C386 TOPCAT 


             o  The   Last   Byte   Memory   Manager   software   is
                table-driven,  making it relatively easy to adapt to
                different   memory   controller  architectures,  but
                there are limits!   

                Examples: Zymos chipsets 
                          United Micro. Corp. UM82C384, '388, '389 
                          Forex Computer Corp. FRX36C100 
                          Silicon Integrated   System   Corp.  (SIS)
                chipsets 


             o  Some  memory  controllers  are designed so that they
                can   be   "locked"   at   the   end   of   software
                initialization,   requiring   a  hardware  reset  to
                unlock,  and  thus  preventing  The Last Byte Memory



        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Apr 12, 1992    THE LAST BYTE MEMORY MANAGER (tm)              10


                Manager from accessing the controller.  

                Examples: Intel 82335, 82335SX 


        Some  of these chips, however, have hardware EMS support and thus
        many  of  their  motherboards  come  with  an  EMS  device driver
        designed  specifically  to take advantage of this capability.  So
        in  many  cases,  you can install this driver first, and then The
        Last  Byte  Memory  Manager can use it to manage the upper memory
        area.  











































        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Apr 12, 1992    THE LAST BYTE MEMORY MANAGER (tm)              11


                      CHAPTER 3 - DISTRIBUTION FILES       


        Version  2.00  of  The  Last  Byte Memory Manager consists of the
        following  distribution  files.  Feel free to upload this package
        to   any   bulletin  board,  but  please  be  sure  all  original
        (unmodified) distribution files are included in the upload.  

        CHIPSET.EXE     A program to test your computer for compati-
                        bility with The Last Byte Memory Manager.

        CLOCK.EXE       A TSR program to display the current time in the
                        upper left-hand corner of the screen.  (Requires
                        ANSI.SYS.)

        HIGHAPND.EXE    A program to enable/disable an extension of conven-
        HIGHAPND.SYS    tional memory beyond 640k up to 704k or even 736k,
                        depending on your hardware configuration.

        HIGHBFRS.EXE    A program to put the MS-DOS 3.xx disk buffers
                        (i.e., as specified in the "BUFFERS=" command
                        of CONFIG.SYS) in upper memory.

        HIGHDISK.SYS    A device driver that creates a ram disk in
                        upper memory.

        HIGHDRVR.SYS    A device driver used to load other device 
                        drivers into upper memory.

        HIGHEMS3.SYS    A pair of device drivers that emulate expanded
        HIGHEMS4.SYS    memory in upper memory.

        HIGHENV.EXE     A program to move the master environment from
                        conventional memory to upper memory.

        HIGHFILE.EXE    A program to implement the DOS "FILES=" option
                        using upper memory rather than conventional
                        memory.

        HIGHHOLE.EXE    A program to locate empty space in shadowed ROMs
                        that can be converted to free High-DOS memory.

        HIGHINST.EXE    Exactly like HIGHTSR, except used with the
                        "INSTALL=" command in a CONFIG.SYS file.

        HIGHKEY.EXE     A command line recall editor similar to the DOS 5
                        DOSKEY program, but which can store the command
                        line history in bank-switch memory.

        HIGHMARK.EXE    A program to mark TSR's so that they may be
                        removed from upper memory at a later time.



        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Apr 12, 1992    THE LAST BYTE MEMORY MANAGER (tm)              12



        HIGHMEM.EXE     A program to display a map of upper memory usage.

        HIGHSPLR.EXE    A program to create a printer spooler in upper
                        memory.

        HIGHTSR.EXE     A program to load TSR's into upper memory.

        HIGHUMM.DOC     A device driver that application programmers may
        HIGHUMM.SYS     use to access upper memory from their own pro-
                        grams.  (For a detailed specification of the soft-
                        ware interface, see the information in the file
                        HIGHUMM.DOC.)

        HIGHUNDO.EXE    A program to remove TSR's (and their associated
                        mark) that have been previously marked with
                        HIGHMARK.

        INSTALL.EXE     A program to automatically create or modify your
                        CONFIG.SYS and AUTOEXEC.BAT files for use with
                        The Last Byte Memory Manager.

        LASTBYTE.DOC    This text file.

        LASTBYTE.SYS    A device driver that must be loaded before any
                        other software of The Last Byte Memory Manager.

        LICENSE.EXE     A program to install your name and personal
                        access key for full operation of LASTBYTE.SYS.

        ORDERFRM.DOC    A text file containing individual and site
                        license order forms.

        TLBMM.EXE       A program that returns a non-zero errorlevel
                        if The Last Byte Memory Manager is not
                        installed.  (Useful in .BAT files.)

        WHATSNEW.120    A text file describing changes since the
                        previous version.















        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Apr 12, 1992    THE LAST BYTE MEMORY MANAGER (tm)              13


                       CHAPTER 4 - GETTING STARTED       


        The  first  thing  to  do is to be sure that The Last Byte Memory
        Manager  will  work  on your computer.  You can do this by simply
        running  the program called CHIPSET.  If successful, it will then
        ask  you  if  you would like to run the INSTALL program to create
        or  modify  your  CONFIG.SYS  and AUTOEXEC.BAT files for use with
        The  Last  Byte  Memory  Manager.   If  you  prefer,  you can run
        INSTALL and it will automatically run CHIPSET for you.  


        4.1 Testing LASTBYTE.SYS HIGHDRVR.SYS and HIGHTSR.EXE     

        To  install The Last Byte Memory Manager on a floppy diskette for
        testing, perform the following three steps: 

             Step 1:  Use  the  MS-DOS  FORMAT  command  with the /S
                      option  to  prepare  a  bootable  floppy disk.
                      You will need this in step 2.  

             Step 2:  Run  the  CHIPSET program.  If it succeeds, it
                      will  ask  you "Do you want to run the INSTALL
                      program  now?".  Answer yes.  When it displays
                      the  first  screen  of  the  INSTALL  program,
                      select   the   first   option,   "Creating   a
                      demonstration   diskette"   and   follow   the
                      prompts.  

             Step 3:   Once  you  have  created  your  demonstration
                      diskette,  press  Ctrl-Alt-Del  to reboot your
                      computer from the diskette.  

        If  everything  goes  ok,  during  the  boot you'll briefly see a
        sign-on box that looks something like the following: 



















        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Apr 12, 1992    THE LAST BYTE MEMORY MANAGER (tm)              14


        ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
        º         THE LAST BYTE MEMORY MANAGER (tm) Version 2.00a           º
        º Copyright (C) 1990-92, Key Software Products, All Rights Reserved º
        º                   Licensed for EVALUATION ONLY                    º
        ÇÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¶
        º         25.0 Mhz 80386 with Chips & Technologies 82C302C          º
        ÇÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¶
        º  Address Range  Size    Width    Bandwidth    Description         º
        º   00000-9FFFF  640 KB  32 bits  38.0 MB/Sec   Conventional Memory º
        º   A0000-FFFFF  384 KB  32 bits  38.0 MB/Sec   Shadow Ram Memory   º
        º   A0000-AFFFF   64 KB  16 bits   3.1 MB/Sec   VGA Graphics Buffer º
        º   B8000-BFFFF   32 KB  16 bits   3.1 MB/Sec   VGA Color Text Bfr  º
        º   C0000-C7FFF   32 KB  16 bits   3.1 MB/Sec   VGA Adapter Bios    º
        º   C8000-CB7FF   14 KB   8 bits   1.3 MB/Sec   Fixed Disk Bios     º
        º   CB800-CBFFF    2 KB   8 bits   1.3 MB/Sec   Fixed Disk Ram      º
        º   F0000-FFFFF   64 KB  16 bits   3.1 MB/Sec   AMI Bios (03/01/90) º
        ÇÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¶
        º Conventional  High-DOS     Bank-Switch   Shadowed Roms  Excluded  º
        º     640k        32k            32k            96k         224k    º
        ÇÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¶
        º The Last Byte Memory Manager is a trademark of Key Software Prod. º
        ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

        If  your  computer  stops  before displaying the entire box shown
        above,  or  if  it  fails to operate properly after booting, this
        may  be  because  The Last Byte Memory Manager failed to identify
        one  of  your  installed  adapters  that uses some portion of the
        upper  memory  address  space.   If this happens, you'll probably
        need  to  use  an  "EXCLUDE="  option on the LASTBYTE.SYS command
        line  to  manually  disable  the  corresponding  region(s)  where
        conflict  occurs.   To  temporarily  get around this problem, you
        can  reboot  and manually bypass all The Last Byte Memory Manager
        device  drivers  and  TSR's  by  simultaneously  holding down the
        <alt>  key,  the  <ctrl>  key,  and  either  the  <leftshift>  or
        <rightshift> key during the boot sequence.  

        After  AUTOEXEC.BAT  is  finished, the screen will be filled with
        the  output  of  the HIGHMEM program and the current time will be
        displayed  in  inverse  video in the upper left-hand corner.  The
        latter  verifies  that HIGHTSR has successfully loaded CLOCK into
        upper memory and that ANSI.SYS is installed and operating.  

        To  exit  from  HIGHMEM,  simply press the Esc key.  If you like,
        you  can  run  HIGHUNDO  to remove the CLOCK program from memory,
        and then HIGHMEM again to see that it has been removed.  

        Once  you  are  convinced  that  The  Last Byte Memory Manager is
        working  satisfactorily,  you may install it on your hard disk by
        making drive C: the current drive by entering 

                C: 



        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Apr 12, 1992    THE LAST BYTE MEMORY MANAGER (tm)              15



        and rerunning CHIPSET or INSTALL.  


        4.2 Mapping Upper Memory with HIGHMEM     

        Depending  on  what  adapter  cards you have installed, HIGHMEM's
        output should look something like that shown below.  


      HIGHMEM v2.00a (C) Key Software Products 1990-92. All Rights Reserved.

      MCB  Hex Address Description [Type] <Mark> High-DOS Bnk-Swtch  Total
      ÄÄÄÄ ÄÄÄÄÄÄÄÄÄÄÄ ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ ÄÄÄÄÄÄÄÄ ÄÄÄÄÄÄÄÄÄ ÄÄÄÄÄÄÄ
      B000 A0000-AFFFF Reserved Memory Group:                       
      B79D A0000-A042F ÌÍTSR Marker          <1>             1,072  
      B002 A0000-A042F º ÀÄ8-bit EGA Graphics Buffer                  1,072
      B79B A0430-A7FFF ÌÍ8-bit EGA Graphics Buffer        [ 31,696] [31,696]
      B004 A8000-AFFFF ÈÍ8-bit EGA Graphics Buffer                   32,768
      B006 B0070-B10CF ANSI           [DEV]        4,192              4,192
      B10D B10E0-B112F CLOCK          [ENV]  <1>      80                 80
      B113 B1140-B12EF CLOCK          [TSR]  <1>     432                432
      B12F B1300-B79AF [ùùùFreeùùù]             [ 26,288]           [26,288]
      B79F B7A00-B7EFF LASTBYTE       [DEV]        1,280              1,280
      B7FE B8000-FFFFF Reserved Memory Group:                       
      B7F0 B8000-BFFFF ÌÍ8-bit EGA Color Text Buffer                 32,768
      B7F2 C0000-C3FFF ÌÍShadowed 8-bit EGA Bios Rom                 16,384
      B7F4 C4000-C7FFF ÌÍExcluded Block                              16,384
      B7F6 C8000-CB7FF ÌÍ8-bit Fixed Disk Adapter Bios               14,336
      B7F8 CB800-CBFFF ÌÍ8-bit Fixed Disk Adapter Ram                 2,048
      B7FA CC000-EFFFF ÌÍExcluded Block                             147,456
      B7FC F0000-FFFFF ÈÍShadowed 16-bit AMI Main Bios               65,536
                                                 ÄÄÄÄÄÄÄ   ÄÄÄÄÄÄÄ  ÄÄÄÄÄÄÄ
                            Upper Memory In Use:   5,984     1,072  334,736
                            [Free Upper Memory]:  26,288    31,696   57,984
                                   MCB Overhead:     496       n/a      496
                                                 ÄÄÄÄÄÄÄ   ÄÄÄÄÄÄÄ  ÄÄÄÄÄÄÄ
                             Total Upper Memory:  32,768    32,768  393,216


        The  column  labelled  "Bank-Switch"  shows  which entries can be
        used  as  bank-switch  memory  for  a  ram disk, a print spooler,
        emulated EMS memory, or TSR markers.  

        Numbers  enclosed in brackets (e.g., "[ 26,128]") refer to memory
        that  is  available for use.  Once you have licensed your copy of
        The  Last  Byte  Memory Manager, the "Excluded Block" shown above
        would  be  added  to the free High-DOS memory pool, and the other
        entries  labelled  "EGA  ...  Buffer"  would be added to the free
        bank-switch memory pool.  




        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Apr 12, 1992    THE LAST BYTE MEMORY MANAGER (tm)              16


        The  column  labelled "Mark" is used in conjunction with HIGHMARK
        and HIGHUNDO.  


        4.3 Running the LICENSE Program      

        The   Last   Byte  Memory  Manager  is  distributed  as  a  fully
        functional  set  of  software.  In its original form, you will be
        able to use all the features, but with three restrictions: 


             o  The  amount of upper memory available to you will be
                limited  to  32k  of High-DOS memory and another 32k
                of Bank-Switch memory, and 

             o  The  maximum  number  of  device drivers and/or TSRs
                will be limited to 2.  

             o  The HOLE option of LASTBYTE.SYS is not available.  


        Access  to  the rest of upper memory requires that you purchase a
        personal  eight-character  access  key  and  install it using the
        LICENSE  program.   The  access key may be obtained directly from
        Key  Software  Products  or  one  of  the authorized distributors
        listed  at the end of this document.  The LICENSE program must be
        run  on the same computer on which you intend to install The Last
        Byte Memory Manager.  

        LICENSE   automatically  senses  whether  you  have  a  color  or
        monochrome  display  to  determine  how  to  present  data on the
        screen.   However, you may force the mode using one of the /MONO,
        /COLOR, or /LCD command line options.  

        Once  you  have  licensed  your  copy  of  LASTBYTE.SYS  you will
        immediately  have  access  to the rest of upper memory.  No other
        files,  diskettes, or manuals need to be ordered.  We do not send
        out  a  new  diskette  or printed manual when you order an access
        key;  otherwise  the  price  would  have  to be greater.  You may
        obtain  your  access  key  by  mail by filling out the order form
        (included  in  the  file  ORDERFRM.DOC)  and  mailing it with the
        calculated  amount to Key Software Products, or by contacting one
        of  our  distributors.   If  you  order by mail, be sure to print
        your  name  clearly  - it will be displayed in the sign-on screen
        of LASTBYTE.SYS and is used to determine your access key.  









        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Apr 12, 1992    THE LAST BYTE MEMORY MANAGER (tm)              17


                    CHAPTER 5 - DETAILED DESCRIPTIONS       


        A  complete  detailed  description of the command line syntax and
        options  of  each  device  driver and utility program in The Last
        Byte  Memory  Manager  is  provided below.  With the exception of
        LASTBYTE.SYS   which   comes   first,   they   are  organized  in
        alphabetical order for ease of reference.  


        5.1 LASTBYTE.SYS         

        During  initialization,  LASTBYTE.SYS  scans upper memory looking
        for  Bios  ROMs,  display  ram, and adapter cards that occupy the
        upper  memory  area.   The  unoccupied  portion  of  upper memory
        defaults  to  High-DOS memory (for device drivers and TSR's).  If
        your  computer uses one of the supported memory controller chips,
        the  occupied  portion  of  the upper memory area will default to
        Bank-Switch  memory  that can be made accessible for Ram disks, a
        Print Buffer, emulated EMS memory, etc.  

        These  defaults  can  be  modified  by  the  use  of command line
        options.    There   are   several   command   line   options  for
        LASTBYTE.SYS.  Many of these use a format like: 

                <keyword>=<base>:<size> 

        where  "<keyword>"  is  one  of  the  option  keywords and may be
        abbreviated  by  its  first  letter,  "<base>"  is  a  four-digit
        hexadecimal  segment  address  in  the  range  A000  to FC00, and
        "<size>" is a decimal number in kilobytes.  

        There are two restrictions on these options: 

             o  The  base must be exactly 4 hexadecimal digits, must
                lie  at  or  above  A000,  and must be a multiple of
                0020  (512  bytes).   (For  APPEND,  the  base  must
                always be A000, or may be omitted.) 

             o  The size must be in the range 1-384 kb.  

        The  "multiple  of 0020" requirement for the base is necessary to
        be  consistent  with  the  way  that The Last Byte Memory Manager
        organizes  high  memory  during  initialization.   However,  this
        requirement  is  often  affected by the coarser resolution of the
        memory controllers: 

        The  upper area is partitioned into blocks.  Some controllers use
        16k  blocks,  some use 32k blocks, and some use 64k blocks.  Each
        block  must  be either totally enabled or disabled.  I.e., if any
        part  of  a  block's address space is disabled by the presence of



        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Apr 12, 1992    THE LAST BYTE MEMORY MANAGER (tm)              18


        an  adapter  card,  the  entire  block  of memory is disabled and
        cannot be made available as High-DOS Memory.  

             APPEND=<base>:<size>  -or-  APPEND=<size> 

                  Allocates  a  region of upper memory for appending
                  to   the   end   of   conventional   memory,  thus
                  increasing  it  beyond  640k.   The  memory is NOT
                  added  until  it  is  enabled  with  HIGHAPND.  If
                  "<base>"   is  used,  it  must  be  A000.   (Note:
                  "<size>"  is  limited  to  16k  in  the unlicensed
                  version  so  that  some High-DOS memory will still
                  be available.) 

                  For  example,  to  force  the  64k  address  range
                  starting  at  segment  A000  to be appended to the
                  end  of  the  640k  of  Conventional  memory,  the
                  proper option syntax would be: 

                                      APPEND=64

             BANKSWITCH=<base>:<size> 

                  Forces   a  region  of  upper  memory  that  would
                  normally  be  used  as  High-DOS memory to be made
                  available as Bank-Switch memory.  

                  ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
                  ³ This option requires a memory controller chip.  ³
                  ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ 

             CACHE  -or-  CACHE=<kbytes> 

                  Forces  LASTBYTE.SYS  to  think  that  there  is a
                  cache  between  the CPU and main memory and to set
                  its  size.   (This  has  nothing  to  do with disk
                  caching!)   This option is not normally necessary;
                  LASTBYTE.SYS  automatically  detects  the presence
                  of  a  cache  and  its size.  If you use the CACHE
                  option   without  specifying  the  size,  it  will
                  default to 512k.  

                  Activating  bank-switch memory causes the contents
                  of  a  cache  (if  present) to be invalid; this is
                  known  as a "cache coherency" problem.  If a cache
                  is   detected  during  installation,  LASTBYTE.SYS
                  checks  to see if any portion of the upper address
                  space  is cached.  If not, then no cache coherency
                  problem exists.  

                  If  the  upper  address  space is cached, however,



        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Apr 12, 1992    THE LAST BYTE MEMORY MANAGER (tm)              19


                  LASTBYTE.SYS  will flush the cache on every access
                  to  Bank-Switch  memory  in  order  to prevent the
                  cache  from providing invalid data to the CPU.  On
                  a   486  it  does  this  by  executing  a  special
                  instruction  that  resets  the  cache.   On  other
                  processors,  the  cache  is  flushed by filling it
                  from  low  memory.   In  the latter case, the size
                  value  discussed  above  is  used to determine how
                  much to fill.  

             DOS=<base>:<size> 

                  Forces   a  region  of  upper  memory  that  would
                  normally  be used as Bank-Switch memory to be made
                  available as High-DOS memory.  

             EXCLUDE=<base>:<size> 

                  Forces  a  region  of  upper memory unavailable as
                  either High-DOS or Bank-Switch memory.  

             HOLE=<base>:<size> 

                  Creates  a  "hole"  of free High-DOS memory within
                  the  address space of a ROM that is shadowed.  Use
                  the  HIGHHOLE  program  to  determine  where these
                  holes  are  located,  and the corresponding values
                  of <base> and <size>.  

                  ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
                  ³ NOTES: (1) The HOLE option is not available in  ³
                  ³ the unlicensed version of LASTBYTE.SYS. (2) The ³
                  ³ <base> and <size> parameters of the HOLE option ³
                  ³ are different from other options: <size> is in  ³
                  ³ bytes and must be a multiple of 16; <base> may  ³
                  ³ be any hexadecimal value from A000 to FFFF.     ³
                  ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

             MOVE=VIDEOBIOS 

                  Tries  to  move  an  EGA  or  VGA bios to a better
                  location  within  the  available  upper  memory in
                  order to reduce fragmentation of free memory.  

             MOVE=MAINBIOS[,ADDHOLES] 

                  Tries  to  move the main bios to a better location
                  within  the  available  upper  memory  in order to
                  reduce     fragmentation     of    free    memory.
                  "MOVE=MAINBIOS,ADDHOLES"  will  create seven holes
                  in  the  residual  8k  left at FE00 for a total of



        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Apr 12, 1992    THE LAST BYTE MEMORY MANAGER (tm)              20


                  more than 3k.  

             MOVE=OVERLAY 

                  This  option  is  for  chipsets  in which the main
                  bios  shadow  ram  cannot be made read/write (OPTi
                  and   ETEQ).    This   option  puts  that  ram  in
                  write-only  mode,  copies the video bios on top of
                  the   main   bios   initialization   code  at  the
                  beginning  of  the  bios,  then returns the ram to
                  read-only  mode.   Then  the old video bios region
                  is converted to usable Hi-DOS memory.  

             MOVE=XBDA 

                  This  option relocates the Extended Bios Data Area
                  (XBDA),  if  it  exists,  into  Upper Memory.  The
                  XBDA   is  usually  1k  reserved  at  the  top  of
                  conventional  memory  by  the  main Bios.  Not all
                  machines   use   an   XBDA,   but  if  it  exists,
                  LASTBYTE.SYS  will  report  639k  of  Conventional
                  Memory  instead  of 640k, and HIGHAPND will refuse
                  to  append  any  memory.   Some  machines  may not
                  operate  properly  with  a  relocated XBDA, so use
                  this   option   with  caution.   (Note  that  some
                  computer  viruses  also  "steal"  the  top  1k  of
                  memory.) 

             PHYSICAL=<memorycontroller>[,OVERRIDE][,NOEMS] 

                  where  "<memorycontroller>  is  determined  by the
                  CHIPSET program.  

                  The "OVERRIDE" suboption: 

                  Many  memory  controller chips can relocate all or
                  part  of  shadow  ram  to  the  top  of (extended)
                  memory.   If  LASTBYTE.SYS  fails  to install with
                  the   error   message:   "Shadow   Ram  memory  is
                  relocated/remapped",   try   adding  the  OVERRIDE
                  suboption  to  the PHYSICAL option.  This disables
                  any  shadow  ram relocation that may be in effect,
                  regardless   of   your   CMOS  configuration  menu
                  setup.   The CMOS setup menu of your BIOS may also
                  provide  an option to disable relocation directly,
                  but  there  are  some  that  determine  whether to
                  relocate  or  not  based  on  other  configuration
                  options.   






        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Apr 12, 1992    THE LAST BYTE MEMORY MANAGER (tm)              21


                  The "NOEMS" suboption: 

                  May  be  used in conjunction with PHYSICAL=LIM4EMS
                  or  EEMS  to  use  the  64k page frame as High-DOS
                  Memory;   must   be   used   in  conjunction  with
                  PHYSICAL=LIM3EMS.    Doing   so   disables   other
                  (normal) use of all expanded memory.  

             RESTRICT=<ab>,<cd>,<ef> 

                  Address  lines  A15  and  A16  are  not latched in
                  hardware  design of the AT bus.  As a consequence,
                  some  16-bit  adapter cards do not properly decode
                  these   address   lines  within  the  narrow  time
                  constraints  imposed  by  the Address Latch Enable
                  (ALE)  signal, and will occassionally respond to a
                  memory  access  that  is  directed  at  some other
                  portion  of  the  address space.  Thinking that it
                  is  for  them, they force the transfer into 16-bit
                  mode  even  though the intended recipient requires
                  8-bit  mode,  and  thus cause erroneous data to be
                  transferred  to  the  bytes  in  the  odd-numbered
                  addresses.  

                  The  most  common  (and damaging) occurence occurs
                  during  the  8-bit  DMA transfers between a floppy
                  disk  drive  and  upper  memory  near  the address
                  space  occupied  by  an  offending  16-bit adapter
                  card.  

                  Due  to organization of the address signals on the
                  AT  bus,  this  phenomena only occurs when the two
                  address  areas  are  within  the same 128k region.
                  There  are  three  such regions in the upper area:
                  A0000-BFFFF,    C0000-DFFFF,    and   E0000-FFFFF.
                  LASTBYTE.SYS  automatically senses the presence of
                  16-bit  adapter  cards  in  each  of  these  three
                  regions  and  records  this information within its
                  resident   image   for   use   by  its  utilities.
                  LASTBYTE.SYS  skips  this  test if it detects a PC
                  with  a  Micro  Channel  bus (like the PS/2) since
                  problem was corrected in its design.  

                  The  RESTRICT  option is provided to override this
                  automatic  detection  of 16-bit adapters.  Each of
                  the  three  arguments (one per 128k region) should
                  be  replaced  by  either "0" (indicating no 16-bit
                  adapters),  or  "1"  (indicating the presense of a
                  16-bit adapter).  

                  For   example,  the  option  RESTRICT=1,1,0  would



        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Apr 12, 1992    THE LAST BYTE MEMORY MANAGER (tm)              22


                  imply   that  one  or  more  16-bit  adapters  are
                  located  in  the  first  two 128k regions of upper
                  memory  (A000-DFFF),  so  that  when the /RESTRICT
                  option  of  HIGHDRVR,  HIGHTSR, HIGHINST, HIGHUMM,
                  HIGHEMS3,  and  HIGHEMS4  is  used,  only High-DOS
                  memory   in   the   region   E000-FFFF   will   be
                  allocated.   This is the default for HIGHBFRS, but
                  may   be   disabled  by  use  of  its  /NORESTRICT
                  option.  

             SHADOW=<base>:<size> 

                  The  Last  Byte  Memory Manager will automatically
                  copy  the  video  bios and main bios to shadow ram
                  if  they  aren't  already  shadowed.   However, it
                  will  not  do  so for other adapter ROMs.  This is
                  because  some  controllers  "hide"  a small RAM by
                  overlaying  it  in  a  portion of the same address
                  space  they  declare  as  being  filled  with ROM.
                  Such  a  RAM  is no longer accessible when the ROM
                  is  shadowed,  usually causing the adapter to stop
                  functioning.  

                  This  option  is  for  those  who want to forces a
                  region  of  memory  (presumably  ROM) to be copied
                  into  shadow  ram.   If other hardware is detected
                  outside  the specified region, but within the same
                  memory  controller block which conflicts with this
                  request,  a  corresponding  error  message will be
                  displayed    and    LASTBYTE.SYS   will   not   be
                  installed.  

                  ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
                  ³ This option requires a memory controller chip.  ³
                  ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ 

             TEXT=n 

                  The  information  screen invoked by the "?" option
                  defaults  to  bright  white  on  blue  if  a color
                  display  is  active,  and  to  inverse  video if a
                  monochrome   monitor   is   active.   This  option
                  changes  the  default  to  'n',  where  n  is  the
                  hexadecimal  value  of  the attribute byte used to
                  paint the screen.  

             ? (A question mark) 

                  Causes  LASTBYTE.SYS  to erase the screen, display
                  a  summary  of  what  it finds in the upper memory
                  area,  and  pause for two seconds to give the user



        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Apr 12, 1992    THE LAST BYTE MEMORY MANAGER (tm)              23


                  an   opportunity  to  read  the  information.   To
                  freeze  this  display  for  a longer period, press
                  <Ctrl>-S;   then   to   continue  with  CONFIG.SYS
                  processing, press any key.  


        5.2 HIGHAPND.EXE and HIGHAPND.SYS       

        HIGHAPND.EXE  is  a  program that can only be used in conjunction
        with  the  "APPEND="  option  of LASTBYTE.SYS.  HIGHAPND.SYS is a
        device  driver  version  of  HIGHAPND.EXE.  Either can be used to
        append  some of the upper memory that begins at 640k onto the end
        of conventional memory (and also to return later to 640k).  

        Monochrome  (MDA),  Hercules,  and CGA display adapters don't use
        the  64k  region starting at A000, and so this memory can be used
        to  extend  conventional memory from 640k to 704k, provided there
        is  available  read/write  memory  in  this  area.   CGA  display
        adapters  also  don't  use  the next 32k either, and so CGA users
        may be able to extend conventional memory all the way to 736k.  

        EGA  and  VGA  display adapters have a 64k hi-resolution graphics
        display  buffer  that  is  located  at A000.  This buffer is only
        needed  when you are using only hi-resolution graphics.  When the
        display  is  in either text or low-resolution CGA graphics modes,
        this  memory  is  not  used,  and may be replaced (switched) with
        shadow  ram memory if available, or the display buffer itseld may
        be  used  to  extend conventional memory.  Since most EGA and VGA
        adapters  usually  don't use the 32k region at B000, you may even
        be able to extend conventional memory up to 736k.  

        You  may either use HIGHAPND.SYS during CONFIG.SYS processing, as
        in: 

                DEVICE=HIGHAPND.SYS ON  {Extends conv. memory beyond 640k}
                        . . .
                DEVICE=HIGHAPND.SYS OFF {Resets conv. memory to 640k}

                ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
                º WARNING: HIGHAPND.SYS may not work properly     º 
                º with some versions of MS-DOS; in such cases,    º 
                º use HIGHAPND.EXE instead.  There is no benefit  º 
                º to using HIGHDRVR.SYS to load HIGHAPND.SYS      º 
                º because it never stays resident.                º 
                ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

        or  use  HIGHAPND.EXE  during  AUTOEXEC.BAT processing (or at any
        time after the computer is booted), as in: 






        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Apr 12, 1992    THE LAST BYTE MEMORY MANAGER (tm)              24


                A>HIGHAPND ON   {Extends conv. memory beyond 640k}
                        . . .
                A>HIGHAPND OFF  {Resets conv. memory to 640k}

                ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
                º WARNING: HIGHAPND.EXE may not work properly     º 
                º with DR DOS. In such cases, use HIGHAPND.SYS.   º 
                ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼


        Don't  forget  -  both  HIGHAPND.SYS and HIGHAPND.EXE require the
        use of an APPEND option on the LASTBYTE command line.  

        HIGHAPND  can  be  used  without  any  command  line  options  to
        determine  the  current size of conventional memory and the state
        of EGA/VGA hi-resolution graphics: 

                A>HIGHAPND 

        You  can  put  these  commands  into  a  batch  file  to simplify
        switching  back  and  forth.   For example, if you want the extra
        memory  all  the  time  except  when you need hi-res graphics for
        Microsoft Windows, create a batch file like the following: 

                @ECHO OFF 
                HIGHAPND OFF 
                WIN %1 %2 
                HIGHAPND ON 

        HIGHAPND  will automatically disable any EGA or VGA hi-resolution
        graphics   capability   whenever  conventional  memory  has  been
        extended  beyond  640k.   This  makes  software  that attempts to
        sense  what  type  of display adapter is installed think that you
        have  only  a  CGA  adapter.   Later,  when you need the graphics
        capability,   you   can   disable   the   memory   extension  and
        hi-resolution graphics will be automatically re-enabled.  

        If  you  have  hi-res  graphics  disabled  and run a program that
        tries  to use hi-res graphics without first sensing for an EGA or
        VGA  adapter,  LASTBYTE.SYS  will  notice  the conflict, issue an
        error   message,   and  terminate  the  program.   Some  programs
        redirect  a  few  interrupts during their initialization and then
        restore  them  before termination.  LASTBYTE.SYS's termination of
        graphics  programs  doesn't know how to restore these interrupts,
        so  in  some cases you may have to reboot the computer.  In other
        words,  if  you  experience this kind of program termination with
        an  application  program, it's best to reboot and prepare a batch
        file (as shown above) to run the program.  

        HIGHAPND  provides  more  detailed  control  over this protection
        through  the  /HIRESGFX  option  as described below.  This may be



        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Apr 12, 1992    THE LAST BYTE MEMORY MANAGER (tm)              25


        helpful,  for  example,  with software that uses the 43 (50) line
        text  mode of the EGA (VGA) adapter.  (The setting of this option
        is only meaningful when HIGHAPND ON is in effect.) 

             /HIRESGFX=TRAPPED 

                  Disables   all  EGA/VGA  high-resolution  graphics
                  functions  provided  by  video  BIOS interrupt 10h
                  and   makes   programs  think  a  CGA  adapter  is
                  installed.  (This is the default.) 

             /HIRESGFX=SENSED 

                  Disables   all  EGA/VGA  high-resolution  graphics
                  functions  provided  by  video BIOS interrupt 10h,
                  but  does  let  programs  sense the presence of an
                  EGA or VGA adapter.  

             /HIRESGFX=ALLOWED 

                  Allows  all  video  BIOS  interrupt  10h  function
                  calls,  even  if  they  might  use the 64k EGA/VGA
                  graphics display buffer at A000-AFFF.  

                              Technical Note      

             HIGHAPND  requires  either  a memory controller chip or
             an   EGA   or  VGA  display  adapter.   If  the  memory
             controller  chip  can enable shadow ram memory at A000,
             then   shadow   ram  memory  will  be  used  to  extend
             conventional  memory;  otherwise, HIGHAPND will convert
             the  graphics  display buffer of the EGA or VGA display
             adapter into an extension of conventional memory.  



        5.3 HIGHBFRS.EXE (MS-DOS 3 only)      

                ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
                º WARNING:  Placing MS-DOS buffers in high memory º
                º can result in the loss of data.  I.e., it can   º
                º damage the directory and file allocation tables º
                º of your disk.  Read everything in this section  º
                º before considering the use of this utility.     º
                ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

        HIGHBFRS  can  be  used  to  place  MS-DOS  3.x  buffers in upper
        memory,  but  you  must  be  careful that this does not cause DMA
        transfers  into  a  128k  region  of  memory  containing a 16-bit
        adapter,  or else you may damage the data on your disk.  (See the
        discussion  of  the  "RESTRICT" option of LASTBYTE.SYS.) HIGHBFRS



        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Apr 12, 1992    THE LAST BYTE MEMORY MANAGER (tm)              26


        offers  two  solutions  to  this problem: The first (and default)
        solution  is  to  restrict  buffer  placement  to particular 128k
        regions where there is no conflict.  

        If  all three 128k regions contain 16-bit adapters, then a second
        (different)  solution  may  be both necessary and sufficient.  It
        intercepts   transfers  between  floppy  disk  drives  and  upper
        memory,  and  redirects  the  transfer  through  an  intermediate
        sector  buffer  in  conventional (low) memory.  The corresponding
        command line option would be: 

                                HIGHBFRS /FLOPPY

        Almost  all  hard  disk  controllers  use 16-bit CPU instructions
        (rather  than  DMA)  to  transfer data and thus do not incur this
        problem.   

        HIGHBFRS   defaults   to   the  maximum  number  of  buffers  and
        automatically  determines  the  safest  location for loading them
        into  upper memory by checking with LASTBYTE.SYS for the location
        of  16-bit  adapter  cards,  if  any.   If none of the three 128k
        segments  is  considered  "safe",  it will enable interception of
        floppy  transfers.   Any  of  these defaults can be overridden by
        one or more of the following command line options: 

             BUFFERS=<number> 

                  Changes  the number of MS-DOS buffers to the value
                  specified;  "<number>"  is  a number from 1-99, or
                  may be replaced by the word "MAXIMUM".  

             /NORESTRICT (Abbreviated "/N") 

                  Disables   the   default   restriction  on  buffer
                  placement   caused   by  the  presence  of  16-bit
                  adapter  cards  or by use of the "RESTRICT" option
                  on the LASTBYTE.SYS command line.  

             /FLOPPY (Abbreviated "/F") 

                  Enables  redirection  of  Bios  INT 13h calls that
                  attempt  to  transfer  data  between a floppy disk
                  drive  and  upper  memory.   If  redirected,  such
                  transfers   go   through  an  intermediate  buffer
                  located   in   conventional   memory.    (Disables
                  restrictions on buffer placement.) 

        When  HIGHBFRS  is  invoked  with  no  command line arguments, it
        simply  reports the number of MS-DOS buffers presently located in
        upper  memory  and  whether  or not transfers between floppy disk
        drives  and upper memory are redirected.  You may use the HIGHMEM



        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Apr 12, 1992    THE LAST BYTE MEMORY MANAGER (tm)              27


        program  to determine where the buffers have been placed in upper
        memory.  

        Microsoft  recommends setting the "BUFFERS=" option in CONFIG.SYS
        according  to  the  type  of  application  most  frequently used.
        Implicit  within  this  recommendation is the assumption that you
        won't  change  the  value  very  often  since it requires editing
        CONFIG.SYS and rebooting.  

        In  general, more buffers help when running programs that perform
        random  access on a relatively small number of disk records (such
        as  the  index  for a database program), or if your disk has many
        subdirectories organized on several levels.  

        Since  HIGHBFRS  allows you to increase or decrease the number of
        buffers  dynamically,  you  could create some batch files to tune
        the  number  of  buffers to fit the application you're running at
        the moment.  


        5.4 HIGHDISK.SYS         

        HIGHDISK.SYS  is  a  device  driver that implements a ram disk in
        upper  memory.   Bank-Switch  Memory  is  allocated first, and if
        that  isn't  enough, then High-DOS Memory is allocated to satisfy
        the  total request.  The device driver automatically loads itself
        into  upper  memory, putting most of itself in bank-switch memory
        if  available,  without  using  HIGHDRVR  or the DOS 5 DEVICEHIGH
        command, as in: 

                               DEVICE=HIGHDISK.SYS

        This  creates  a  ram  disk that uses all available upper memory,
        with 32 directory entries and sectors of 128 bytes each.  

        A  command line option may be used to specify the size of the RAM
        disk as in: 

                             DEVICE=HIGHDISK.SYS 100

        This creates a 100k byte ram disk.  

        Other  command  line  options may be used to change the number of
        bytes per sector and directory entries, as in: 

                         DEVICE=HIGHDISK.SYS 100 256 64

        This  creates  a  100k  RAM disk with 256 bytes per sector and 64
        root directory entries.  





        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Apr 12, 1992    THE LAST BYTE MEMORY MANAGER (tm)              28


                ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
                º NOTE: If you have used the command DOS=UMB or   º
                º DOS=HIGH,UMB with HIGHUMM.SYS to let DOS 5.0    º
                º manage the Upper Memory Blocks, you must limit  º
                º how much upper memory HIGHUMM can use so that   º
                º some will be available for HIGHDISK.            º
                ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼


        5.5 HIGHDRVR.SYS         

        HIGHDRVR  is  a  device  driver that is used to load other device
        drivers  into upper memory.  For a brief introduction to its use,
        see  the  section  titled  "Testing LASTBYTE.SYS HIGHDRVR.SYS and
        HIGHTSR.EXE"  in  the  "GETTING STARTED" chapter at the beginning
        of   this  manual.   Also  see  the  sections  in  the  "HINTS  /
        SUGGESTIONS   /  EXPLANATIONS"  chapter  near  the  end  of  this
        document on the /SIZE, /LOW, and /RESTRICT options.  

        The command line syntax of the CONFIG.SYS line for HIGHDRVR is: 

                DEVICE=[path]HIGHDRVR.SYS <filespec> 

        where  '<filespec>'  is  the  filename of the device driver to be
        loaded  high,  optionally  prefixed  by  a  drive  and  directory
        specifcation.   The  filespec  may  be preceded by one or more of
        the  /SIZE,  /LOW, and /RESTRICT options, and followed by options
        at  the  end  of  the  command line as required by the particular
        driver to be loaded.  

        When  HIGHDRVR  searches  the disk for the device driver to load,
        it follows the following search strategy: 

             (1)  If  '<filespec>'  includes  a  drive  or directory
                  specification,  this  will  be the only place that
                  HIGHDRVR will look.  

        Otherwise, HIGHDRVR will search for the driver in: 

             (2)  The current (root) directory, and then 

             (3)  The same directory where HIGHDRVR was found.  


        5.6 HIGHEMS3.SYS and HIGHEMS4.SYS       

        Two  expanded  memory  emulators  are provided with The Last Byte
        Memory  Manager.   Both  use  upper  memory  as  expanded memory.
        HIGHEMS3.SYS  is  compliant  with  the  older  LIM  3.2 spec, and
        HIGHEMS4.SYS  with  the  newer  LIM  4.0 spec.  Both are included
        since  the  HIGHEMS3.SYS requires much less memory for the device



        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Apr 12, 1992    THE LAST BYTE MEMORY MANAGER (tm)              29


        driver  itself  than HIGHEMS4.SYS.  In many applications, you may
        find that 3.2 is all you need.  

        These  device  drivers  emulate expanded memory!  That means that
        they  use  software  to  copy  data  back  and  forth between the
        logical  EMS  memory (pages) and the page frame.  Obviously, this
        is  much  slower  than  the  performance  you  would realize with
        hardware  support,  or even with EMM386.  Therefore, these device
        drivers  are  provided  as  a  last  resort for those who have no
        other  way of providing EMS memory to their applications, such as
        users with only 1 meg of memory.  

        Both  HIGHEMS3.SYS and HIGHEMS4.SYS have an optional command line
        parameter  which  is the number of 16k EMS pages to allocate.  If
        omitted,  the  maximum  allocation  will  be  used.   Bank-Switch
        memory  is  allocated  first,  and  if  that  isn't  enough, then
        High-DOS Memory is allocated to satisfy the total page request.  

        Use  only  one  of  these  device  drivers,  and  load  it  after
        LASTBYTE.SYS.   The  driver automatically loads itself into upper
        memory,  putting  much  of  itself  into  bank-switch  memory  if
        available,  without  the  need  for  either HIGHDRVR or the DOS 5
        DEVICEHIGH  command.   Also  see  the  section  on  the /RESTRICT
        option  in  the "HINTS / SUGGESTIONS / EXPLANATIONS" chapter near
        the end of this document.  

                ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
                º NOTE: If you have used the command DOS=UMB or   º
                º DOS=HIGH,UMB with HIGHUMM.SYS to let DOS 5.0    º
                º manage the Upper Memory Blocks, you must limit  º
                º how much upper memory HIGHUMM can use so that   º
                º some will be available for HIGHEMS3/HIGHEMS4.   º
                ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼


        5.7 HIGHENV.EXE         

        HIGHENV  is  a  utility  that moves the master environment of the
        command  processor  (typically  COMMAND.COM)  out of conventional
        memory  and  into High-DOS memory.  It can also be used to change
        the size of the environment at any time.  

                ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
                º WARNING: HIGHENV is incompatible with Novell.   º 
                ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

        If  used  without  a  command line option, HIGHENV simply reports
        the  location,  capacity,  and  length of the master environment.
        If  the  environment  has not been moved from low memory, it also
        examines  and  reports  potential  references  to the environment
        that  exist  within  the  command  processor.  If one or more are



        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Apr 12, 1992    THE LAST BYTE MEMORY MANAGER (tm)              30


        located, the first line(s) of output from HIGHENV will be: 

              "Potential command processor patch at location XXXX."

        where  "XXXX"  will  vary  from one command processor to another.
        HIGHENV  should  be used this way at least once to determine what
        "/PATCH" options (described below) may be required.  

        To  move  the  master environment into upper memory, you must use
        one  or  more  /PATCH  options  and  may use a /SIZE option.  The
        patch  options  specify  locations  in the command processor that
        must  be  modified.   (If  there  are no locations in the command
        processor  that  need  to  be  modified,  use  /PATCH=NONE.)  The
        /PATCH  option  may  only be specified once, when the environment
        is  moved  from  low  to  upper  memory.  The patch locations are
        recorded  in  upper  memory and are automatically adjusted if the
        environment  is repositioned within upper memory as the result of
        a subsequent use of HIGHENV to resize the environment.  

        The  size  option  is  simply  a  number that specifies the extra
        space   in   bytes  to  be  allocated  to  accomodate  additional
        environment  strings  besides  those already established.  If the
        size  option  is  omitted, the size of the environment block (and
        thus its capacity for growth) will not be changed.  

                ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
                º WARNING: The SET command of COMMAND.COM norm-   º 
                º ally warns you if you run out of space in the   º 
                º master environment.  However, if you have used  º 
                º HIGHENV to move it into upper memory, this      º 
                º safeguard no longer exists - you'll just write  º 
                º over the next thing in upper memory!  Be sure   º 
                º to check the HIGHENV report to be sure that you º 
                º have enough extra space in the environment so   º 
                º that this won't occur.                          º 
                ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

        A  maximum  of four command processor locations to be patched may
        be specified in either of two ways: 

                A>HIGHENV 256 /PATCH=1057 /PATCH=1536 

                -or- 

                A>HIGHENV 256 /PATCH=1057,1536 

        Each  of the patch numbers specify a location in the memory image
        of  the  command  processor;  these locations contain the segment
        address  of the master environment, and must be modified to point
        to  the  new master environment in upper memory.  Possible values
        to  be  used  are  restricted  to  those  locations reported when



        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Apr 12, 1992    THE LAST BYTE MEMORY MANAGER (tm)              31


        HIGHENV  is  run  with  no  command  line  options and before the
        environment has been moved into upper memory.  

        COMMAND.COM  usually  contains  only one such location that needs
        to  be  patched;  4DOS  contains  none (use /PATCH=NONE).  (Note:
        HIGHENV  always  patches  the  environment  address stored in the
        program  segment  prefix  of  the  command processor - this patch
        does not need to be specified.) 

                ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
                º NOTE: The /U option of 4DOS is an alternative   º 
                º method for placing the master environment in    º 
                º upper memory.  You don't need to use HIGHENV if º 
                º you are already using the /U option of 4DOS.    º 
                ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

        Once  moved into upper memory, the size of the environment may be
        changed  by  using  HIGHENV  with  simply  a  size  option.   For
        example,  to  shrink  the environment to only enough room for the
        current environment strings, use: 

                A>HIGHENV 0 

        Or  to  change  the  growth  capacity  to  allow  for the current
        environment strings plus 100 bytes more, use: 

                A>HIGHENV 100 


        5.8 HIGHFILE.EXE         

        This  program  is  used  to  implement  most  of  the  CONFIG.SYS
        "FILES=n"   directive   in   High-DOS   memory   rather  than  in
        Conventional  memory.   The  amount  of  memory  required  by the
        "FILE=n"  directive is approximately 'n' times 59 bytes.  Set the
        minimum  of  FILES=8  in  the CONFIG.SYS file, and then place the
        rest in High-DOS memory.  For example, the command: 

                                   HIGHFILE 42

        will  add an additional FILES=42 (2500 bytes) in High-DOS memory,
        for a total of FILES=50.  

                ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
                ³ NOTE: Windows 3.0 may not run in 386 Enhanced   ³
                ³ mode with FILES in upper memory.                ³
                ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ 







        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Apr 12, 1992    THE LAST BYTE MEMORY MANAGER (tm)              32


        5.9 HIGHHOLE.EXE         

        HIGHHOLE  is  a utility program that finds unused space ("holes")
        in  ROMs.   A  "hole"  is  defined  as a sequence of at least 256
        bytes,  all  having  the  same  value, and usually corresponds to
        unused,  left-over  space  in  the  ROM.  If the ROM is shadowed,
        this  space  can  usually  be converted into free High-DOS memory
        using the "HOLE=" option of LASTBYTE.SYS.  

                ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
                ³ NOTE: The HOLE option is not available in the   ³
                ³ unlicensed version of LASTBYTE.SYS.             ³
                ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ 

        These  holes  are  often  less  than 1k in size, but sometimes as
        large  as  6k.   Since  The Last Byte Memory Manager uses a "best
        fit"  strategy  when  allocating  Hi-DOS memory, even the smaller
        holes  can  become  useful to hold the master environment created
        by  HIGHENV,  the  markers  of  HIGHMARK,  or with utilities like
        HIGHDISK  and  HIGHSPLR  that  can  distribute their memory among
        several  small pieces.  In addition, The Last Byte Memory Manager
        will  use  the  smallest  holes for memory control blocks (MCB's)
        that must be allocated for Bank-Switch memory needs.  

        HIGHHOLE   merely   locates  probable  holes,  and  suggests  the
        corresponding  option  to be used with LASTBYTE.SYS.  To activate
        these  holes,  you must then modify your configuration to include
        these  options.   No  option  will be suggested for a hole if (1)
        the  corresponding  ROM  area is not shadowed, (2) the hole is in
        the  Bios  Data Area (FE05-FFFF), or (3) the corresponding shadow
        ram is not controlled by The Last Byte Memory Manager.   

        NOTE:  Use of LASTBYTE.SYS's HOLE option will cause warm boots to
        be converted into cold boots.  


        5.10 HIGHINST.EXE         

        HIGHINST  is simply a TSR version of HIGHTSR that is designed for
        use  with  the  MS-DOS "INSTALL=" directive of a CONFIG.SYS file.
        MS-DOS  requires  that  the program named in an INSTALL directive
        to  be the name of a TSR, and anything else (e.g., HIGHTSR, which
        is  not  a  TSR)  will produce an error message.  A small part of
        HIGHINST   (96   bytes)  will  remain  resident  in  conventional
        memory.  

        For  a  full  description of command line options and syntax, see
        the  description  for  HIGHTSR.   Also  see  the  sections on the
        /SIZE,  /LOW, and /RESTRICT options in the "HINTS / SUGGESTIONS /
        EXPLANATIONS" chapter near the end of this document.  




        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Apr 12, 1992    THE LAST BYTE MEMORY MANAGER (tm)              33



        5.11 HIGHKEY.EXE         

        HIGHKEY  is  a  advanced  command line editor that can recall and
        edit  previous  commands.   HIGHKEY  is  similar  to  the  DOSKEY
        program  in  DOS  5,  but with filename completion and the unique
        ability  to  store the command line history and much of itself in
        bank-switch  memory.   It  does not support DOSKEY macros, or the
        editing keys F7, F9, Alt+F7, or Alt+F10.  

        To install HIGHKEY, simply enter it as a command at the prompt: 

                A>HIGHKEY 

        This  will  allocate  a  recall buffer with a default size of 512
        bytes,  but  which  can  be changed at any time with the use of a
        command line option.  


        5.11.1 Options         

        All of the keywords that follow may be abbreviated.  

        /BUFSIZE=n      Empties the recall buffer, and resizes it to 'n'
                        bytes.  If 'n' is replaced by the word "MAXIMUM",
                        the recall buffer size will use all available memory
                        up to 65535 bytes.

        /INSERT         Sets the default typing mode to insert.

        /OVERSTRIKE     Sets the default typing mode to overstike.

        /HISTORY        Displays the contents of the command line
                        recall buffer on the screen.

        filespec        A filename, optionally preceeded by a drive and
                        directory specification.  If used with the /HISTORY
                        option, causes the recall buffer to be written to
                        the specified file.  If used without the /HISTORY
                        option, it loads the recall buffer from the file.


        5.11.2 Editing Commands        

        Some  of  the  HIGHKEY  editing commands use what is known as the
        "template".   The  template  is  initialized  to  a  copy  of the
        previous  command line, but may be modified by one or more of the
        editing commands.  

        Left Arrow              Moves the cursor back one character.




        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Apr 12, 1992    THE LAST BYTE MEMORY MANAGER (tm)              34


        Right Arrow             Moves the cursor forward one character.

        Up Arrow                Recalls the previous command and stores
                                it in the template.

        Down Arrow              Recalls the next command and stores it
                                in the template.

        PgUp                    Recalls the oldest command and stores it
                                in the template.

        PgDn                    Recalls the most recent command and stores
                                it in the template.

        Ctrl+Left Arrow         Moves the cursor back one word.

        Ctrl+Right Arrow        Moves the cursor forward one word.

        Home                    Moves the cursor to the beginning of
                                the command line.

        End                     Moves the cursor to the end of the
                                command line.

        Esc                     Erases the command line; does not affect
                                the template.

        Ins                     Toggles insert versus overwrite mode.

        Backspace               Deletes the character to the left of the
                                cursor; does not affect the template.

        Del                     Deletes the character at the cursor; does
                                not affect the template.

        Ctrl+End                Deletes from the cursor to the end of
                                the line; does not affect the template.

        Ctrl+Home               Deletes from the beginning of the line
                                up to but not including the cursor; does
                                not affect the template.

        F1                      Copies one character from the template.

        F2                      Waits for a keypress, then inserts charac-
                                ters from the template up to but not in-
                                cluding the first occurrence of that key.

        F3                      Copies the remainder of the template to
                                the command line.




        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Apr 12, 1992    THE LAST BYTE MEMORY MANAGER (tm)              35


        F4                      Waits for a keypress, then deletes charac-
                                ters from the template up to but not in-
                                cluding that key.  The template is then
                                displayed on the command line.

        F5                      Copies the command line to the template
                                and then erases the command line.

        F6                      Inserts an end-of-file character (Ctrl+Z).

        F8                      Searches for the next command that matches
                                the characters in the command line up to
                                the position of the cursor, then copies
                                that command to the template.

        Tab                     Searches for a file on the disk whose name
                                matches the partial filespec given by the
                                text indicated by the cursor.  If found,
                                the filespec is completed on the command
                                line.


        5.12 HIGHMARK.EXE         

        Sometimes  it  can  be  useful  to  remove one or more TSR's from
        memory,  either  because  you  no longer want to use the features
        that  they  provide  or perhaps in order to make room for another
        set of TSR's.  

        In  order  to  be  able  to  remove  a  group of TSR's from upper
        memory,  they must be be marked.  To mark them, run HIGHMARK once
        before  you  use  HIGHTSR  to load the TSR's.  Then later, simply
        run  HIGHUNDO  - the mark and all of its associated TSR's will be
        removed.  

        HIGHMARK  may  be  executed  more than once to establish multiple
        levels  of  TSR's  to  be  removed.   Each  execution of HIGHMARK
        places  another  mark in memory with a unique mark number.  Every
        TSR  loaded  by HIGHTSR is automatically associated with the most
        recent  execution  of  HIGHMARK.   You can use HIGHMEM to see the
        marks,  their  mark  number, and the set of TSR's associated with
        the  mark.   Every execution of HIGHUNDO will then remove the set
        of TSR's associated with the most recent HIGHMARK.  

        You  may  specify  a  mark level on the command line of HIGHUNDO.
        This  will  cause it to remove all the TSR's and marks whose mark
        number  is  greater  than  or  equal to the number on the command
        line.  

        IMPORTANT:  When  a  mark  is  removed  using HIGHUNDO, two basic
        things  happen: (1) the interrupt vector table is restored to its



        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Apr 12, 1992    THE LAST BYTE MEMORY MANAGER (tm)              36


        state  prior  to  the  corresponding HIGHMARK, and (2) any memory
        control  blocks  marked  with  the same mark number are released.
        If  you  have  installed  one  or  more  TSR's since the mark was
        established,  but  did so without the use of HIGHTSR, these TSR's
        will  be  disabled but they will not be removed from memory.  The
        following three examples indicate this consequence: 

                Disabled and            Diabled but     Disabled but
                removed                 remains         remains
                --------                ------------    ------------
                A>HIGHMARK              A>HIGHMARK      A>HIGHMARK
                A>HIGHTSR CLOCK         A>CLOCK         A>LOADHIGH CLOCK
                A>HIGHUNDO              A>HIGHUNDO      A>HIGHUNDO


        5.13 HIGHMEM.EXE         

        HIGHMEM  is  a  program that provides a display of what is loaded
        into  the upper memory area.  For a detailed description on using
        the  HIGHMEM  program,  see  the  section  titled  "Mapping Upper
        Memory  with  HIGHMEM"  in  the  "GETTING STARTED" chapter at the
        beginning of this manual.  

        HIGHMEM   automatically  senses  whether  you  have  a  color  or
        monochrome  display  to  determine  how  to  present  data on the
        screen.   However, you may force the mode using one of the /MONO,
        /COLOR, or /LCD command line options.  


        5.14 HIGHSPLR.EXE         

        HIGHSPLR  is  a  interrupt-driven  print  spooler  that creates a
        print  buffer  in  upper  memory.   Once installed, programs that
        send  output to the printer are no longer held up waiting for the
        printer,  but  rather  simply  send  their  output to the buffer.
        Characters  in  the  buffer  are  then sent to the printer by the
        resident  portion  of  HIGHSPLR while your computer is free to do
        other work.  

        Unlike  the MS-DOS printer spooler (PRINT), HIGHSPLR is driven by
        the   printer   hardware  interrupt  line  that  signals  printer
        "ready",  rather  than  the  timer  tick (that only interrupts 18
        times   per   second).   Unlike  PRINT,  this  allows  full-speed
        transfers  (e.g.,  up  to  about  8,000  cps) to the printer even
        while executing other programs.  

        HIGHSPLR  tries  to  place  its buffer in Bank-Switch memory, but
        will  use  High-DOS  memory if a sufficient amount of Bank-Switch
        memory  is not available.  The size of the buffer will default to
        all  available  Bank-Switch  and  High-DOS  memory,  but  may  be
        restricted (or resized later) by a command line option.  



        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Apr 12, 1992    THE LAST BYTE MEMORY MANAGER (tm)              37



        HIGHSPLR   supports   both  parallel  and  serial  printers,  but
        defaults  to  LPT1.  Multiple copies of HIGHSPLR can be installed
        to  support  more  than  one  printer.   HIGHSPLR  determines the
        physical  i/o  port  address  and  interrupt vector automatically
        from  the  device  name  (e.g.,  LPT2), but these defaults can be
        altered with command line options.  

        HIGHSPLR  also  has  a  unique "monitor" option.  While output is
        being  sent  to  the printer, you can monitor the actual transfer
        rate by entering the command, 

                A>HIGHSPLR MONITOR 

        The  monitor  operation may be terminated at any time by pressing
        a  key, or will automatically terminate when the print buffer has
        been   emptied.   Once  terminated,  HIGHSPLR  will  display  the
        maximum  and  average  transfer rates measured during the monitor
        operation.  

        The  command  line  syntax  for  HIGHSPLR  is  given  below.  All
        parameters  are  optional and may be specified in any order.  All
        of  the  options  except  LPT, COM, and IRQ may be abbreviated by
        their first letter; 

                HIGHSPLR [opt] [opt] ... [opt]

                where opt may be selected from:

                LPT1    LPT2    LPT3    POLL    COM1    COM2    COM3    COM4
                IRQ0    IRQ1    IRQ2    IRQ3    IRQ4    IRQ5    IRQ6    IRQ7
                RESET   NOTEST  MONITOR         KBYTES=#        PORT=#
                or FLOW=<type>, where <type> is selected from:

                XON     DTR     RTS     NONE (default)

        Normally,  neither  the  "PORT"  or  "IRQ"  options are necessary
        since  they  are  automatically  derived  from the "COM" or "LPT"
        option.   Use  "POLL"  if  you don't want to use interrupt-driven
        output;  this may be necessary if another parallel port is in use
        for  some  other  purpose  (e.g., with Lantastic/Z).  The "RESET"
        option  provides a way to cancel printing from the buffer (and do
        a  form-feed) at any time.  One of the FLOW control options (XON,
        DTR,  RTS)  may  be  required  with some serial (COM) printers to
        provide  flow  control.  The "NOTEST" option disables the default
        test  for functionality of the physical port that occurs when the
        software is first installed.  







        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Apr 12, 1992    THE LAST BYTE MEMORY MANAGER (tm)              38


        5.15 HIGHTSR.EXE         

        HIGHTSR  is  a  program  that  is  used to load TSR programs into
        upper  memory.   For  a  brief  introduction  to its use, see the
        section    titled    "Testing   LASTBYTE.SYS   HIGHDRVR.SYS   and
        HIGHTSR.EXE"  in  the  "GETTING STARTED" chapter at the beginning
        of  this  manual.   In  addition  to  the /NOENV option described
        below,  also  see  the sections on the /SIZE, /LOW, and /RESTRICT
        options  in the "HINTS / SUGGESTIONS / EXPLANATIONS" chapter near
        the end of this document.  

        The command line syntax for HIGHTSR is: 

                [path]HIGHTSR <filespec> 

        where  '<filespec>'  is  the  filename  of  the TSR program to be
        loaded  high,  optionally  prefixed  by  a  drive  and  directory
        specifcation.   The  filespec  may  be preceded by one or more of
        the  /SIZE,  /LOW, /NOENV, and /RESTRICT options, and followed by
        options  at  the  end  of  the  command  line  as required by the
        particular TSR to be loaded.  

        When  HIGHTSR searches the disk for the device driver to load, it
        follows   the   same  strategy  that  MS-DOS  uses  when  loading
        programs: 

             (1)  If  '<filespec>'  includes  a  drive  or directory
                  specification,  this  will  be the only place that
                  HIGHTSR will look.  

        Otherwise, HIGHTSR will search for the TSR program in: 

             (2)  The current directory, and then 

             (3)  Those  directories  given  by the PATH environment
                  variable.  


        5.15.1 The /NOENV Option       

        All  programs,  including  TSR's,  are  allocated  two regions of
        memory  when  they  are  loaded:  One is the area for the program
        itself,  and  the  other  is for a copy of the environment.  Most
        TSR's  don't  make  use  of  their environment, and some actually
        release it to the operating system rather than hanging onto it.  

        If  HIGHMEM  finds  an environment block, the corresponding entry
        in  the  "Description"  column will have the name of the TSR that
        it  belongs  to  (such as "CLOCK.EXE") followed by the indication
        "[Env]".    Occassionally,  you  may  see  a  similar  indication
        "[Dat]";  this  is  a  data block explicitly allocated by the TSR



        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Apr 12, 1992    THE LAST BYTE MEMORY MANAGER (tm)              39


        for some unknown purpose.  

                        TSRs that eliminate their PSP   

             The  authors  of  some  TSR's  attempt to save a little
             extra  memory  by  having  the  TSR  eliminate  its own
             Program  Segment  Prefix  (PSP)  during initialization.
             Doing  so  makes  it  impossible  to identify the TSR's
             environment    block.     However,   this   byte-saving
             mentality    will   usually   mean   that   the   TSR's
             initialization  code  also  eliminates  its environment
             block, so this is rarely a problem.  


        If  you  see  a  block labelled "[Env]" in the output of HIGHMEM,
        then  you  can  use  the /NOENV command line option of HIGHTSR to
        release this block, even if the TSR didn't: 

                HIGHTSR /NOENV CLOCK 

        As  noted  earlier,  some  TSRs  will  release  their environment
        anyway  and  so you may be tempted to load them without using the
        /NOENV  option.   This  usually  will  create  a  "hole" in upper
        memory  since  the  TSR's  environment is almost always allocated
        just  below  the TSR itself.  Use of the /NOENV option forces the
        environment  to  be  allocated down in conventional memory (where
        it will be reclaimed later) so that the "hole" is eliminated.  


        5.16 HIGHUMM.SYS         

        HIGHUMM  is  a  device  driver that creates, and lets application
        software  use,  Upper  Memory  Blocks (UMB's) in the upper memory
        area  via  a  standard  protocol that is part of what is known as
        the  Extended  Memory Specification (XMS).  The number, size, and
        location  of  UMB  blocks vary widely depending upon the types of
        hardware adapter cards resident within the upper address space.  

        HIGHUMM may be installed in one of two ways: 

             o  If  an  XMS  driver  (such as HIMEM.SYS) has already
                been  loaded,  HIGHUMM  will link into it, providing
                an  implementation  of  the  two  XMS  functions for
                accessing  what  the  XMS specification refers to as
                "Upper Memory Blocks" (UMB's).  For example, 

                        DEVICE=LASTBYTE.SYS {and any options}
                        DEVICE=HIGHDRVR.SYS C:\DOS\HIMEM.SYS {and any options}
                        DEVICE=HIGHUMM.SYS

                Although  described in the XMS specification, so far



        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Apr 12, 1992    THE LAST BYTE MEMORY MANAGER (tm)              40


                the  UMB  functions have not been implemented in any
                version  of  HIMEM.SYS.   If your XMS driver happens
                to  also  be a UMB provider, HIGHUMM will abort with
                a  corresponding  error  message.   You may then use
                the  /REPLACE option on the HIGHUMM.SYS command line
                to   force   it  to  take  over  responsibility  for
                providing UMBs.  

             o  If  an  XMS driver has not been loaded, then HIGHUMM
                will  become a UMB-Only XMS device driver, providing
                support  for XMS functions 00h (Get Version Number),
                10h   (Allocate  UMB  Block),  11h  (Deallocate  UMB
                Block).    All   other  XMS  functions  will  return
                failure,   indicating   that  the  function  is  not
                implemented.  For example, 

                        DEVICE=LASTBYTE.SYS {and any LASTBYTE options}
                        DEVICE=HIGHUMM.SYS

                                Important!       

                If  another  XMS  device driver is used (e.g., to
                provide  management  of  extended  memory  or the
                upper  memory  area),  it  must  be loaded before
                HIGHUMM.SYS.  


        If  you  want  to limit how much upper memory can be allocated by
        HIGHUMM  as UMB's, you can specify this in kbytes as an option on
        the HIGHUMM.SYS command line, as in: 

                DEVICE=HIGHUMM.SYS 60 

        This  provides  a guarantee that some amount of upper memory will
        never  be  allocated  by  HIGHUMM.SYS,  and  will  thus  still be
        available for other uses.  

        HIGHUMM  requires  that  LASTBYTE.SYS  be  installed  first.   It
        automatically  loads  itself  into  upper memory, putting much of
        itself  into  bank-switch  memory  if  available,  without  using
        either  HIGHDRVR  or  the DOS 5 DEVICEHIGH command.  Also see the
        section  on  the  /RESTRICT  option in the "HINTS / SUGGESTIONS /
        EXPLANATIONS" chapter near the end of this document.  


        5.17 HIGHUNDO.EXE         

        For  a complete discussion of HIGHUNDO see the description of its
        companion program, HIGHMARK in an earlier section.  





        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Apr 12, 1992    THE LAST BYTE MEMORY MANAGER (tm)              41


               CHAPTER 6 - HINTS / SUGGESTIONS / EXPLANATIONS    


        The  following  article  provides  an excellent definition of the
        various   kinds   of  memory,  such  as  conventional,  extended,
        expanded,  high,  and  upper.   More  important,  however, is its
        discussion  of  how  various  adapter cards make use of the upper
        address  space,  and  may  provide  some insight if you're having
        problems   getting  The  Last  Byte  Memory  Manager  to  install
        properly: 

             Barry  Simon,  "How  to Get the Most from Your System's
             High  DOS Memory", PC Magazine, Vol. 9, No. 10 (May 29,
             1990), pp. 347-358.  


        6.1 The /SIZE Option       

        This option may be used with HIGHDRVR, HIGHINST, and HIGHTSR.  

        The  amount  of  High-DOS memory required to load a device driver
        or  TSR  is  the  larger  of two amounts: (1) the amount required
        during  initialization  and  (2)  the  final resident requirement
        once  installed.   Either or both of these may be greater than or
        equal to the size of the file.  

        Most   device   drivers   and   TSR's  require  more  memory  for
        initialization  than  when  resident,  although  there  are a few
        (such   as   SMARTDRV.SYS  and  NANSI.SYS)  which  require  extra
        resident  memory  for  buffers,  etc.   The  normal  operation of
        HIGHDRVR,  HIGHTSR,  and  HIGHINST  is  to  use  the largest free
        High-DOS  memory  block  to  load the software since the resident
        memory  requirement cannot be determined until after the software
        has been loaded and initialized.  

        Unfortunately,  this  can  lead  to  a  less  than optimum use of
        memory.   If  the  memory  requirements were known, then a memory
        block  could  be  selected using a "best fit" strategy; i.e., the
        smallest  free  High-DOS  memory  block  which  is larger than or
        equal  to  the  load  requirement.   This usually results in much
        better utilization of memory.  

        6.1.1 Measuring Load Requirements Using "/SIZE"     

        If  inserted  on  the  command  line  of  HIGHTSR,  HIGHINST,  or
        HIGHDRVR as shown below: 

                           HIGHTSR /SIZE PRINT /D:PRN

        then  both  the  initialization and resident requirements will be
        displayed  on  the console after the software has been loaded and



        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Apr 12, 1992    THE LAST BYTE MEMORY MANAGER (tm)              42


        initialized.  

        6.1.2 Achieving Best Fit Using "/SIZE:n1"     

        The  larger  of  the initialization and resident requirements may
        be  specified  with  the  /SIZE  option  to  force  a  "best fit"
        allocation.  For example: 

                      HIGHTSR /SIZE:17120 PRINT.EXE /D:PRN

        6.1.3 Borrowing Initialization Memory Using "/SIZE:n1 n2"    

        Usually  the resident requirement is less than the initialization
        requirement.   If  there  isn't  enough  free  High-DOS memory to
        satisfy  the  initialization requirement, but there is enough for
        the  resident  requirement,  then  you  may still be able to load
        your  software  by adding a second parameter to the /SIZE option,
        as in: 

                      HIGHTSR /SIZE:16208,5776 PRINT /D:PRN

        In  this  example, the initialization requirement is specified by
        the  first parameter and is 16208 bytes; the resident requirement
        is  specified  by  the  second parameter and is 5776 bytes.  Note
        that  specifying  the  second parameter is not helpful unless the
        resident    requirement   is   less   than   the   initialization
        requirement.  

        When  the  second  parameter  is  used, HIGHTSR first looks for a
        free  area larger than or equal to the initialization requirement
        (the  first parameter); if found, it simply loads the software in
        this  area  and  the  second  paramter  is  ignored.   Otherwise,
        HIGHTSR  searches  for  a  free  area larger than or equal to the
        resident  requirement  (the  second  parameter),  and  which  has
        "data"  allocated  immediately  above  it that can be temporarily
        moved  to create enough free memory to satisfy the initialization
        requirement.   Such  "data"  includes  High-DOS  memory  used  by
        HIGHDISK,  HIGHEMS3,  HIGHEMS4,  HIGHSPLR,  HIGHKEY,  and for TSR
        markers.  


        6.2 The /LOW Option       

        This option can be used with HIGHDRVR, HIGHINST, and HIGHTSR.  

        As  noted  earlier,  TSR's  and device drivers often require much
        more  memory  during  installation  as  compared to that required
        once  they  are  resident.   This  can  prevent loading them into
        High-DOS  memory  even  if  there's enough for the resident image
        (but not enough for initialization).  




        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Apr 12, 1992    THE LAST BYTE MEMORY MANAGER (tm)              43


        HIGHTSR,  HIGHINST,  and  HIGHDRVR  provide an option "/LOW" that
        can  be  used  with  some  TSR's and device drivers to get around
        this problem: 

                HIGHTSR /LOW APPEND 

                -or- 

                DEVICE=HIGHDRVR.SYS /LOW MYDRIVER.SYS 

        For  example,  the  first  example above loads a TSR (APPEND.EXE)
        and  initializes  it  in  low (conventional) memory where there's
        lots  of  room,  then copies the (smaller) resident image up into
        upper memory.  

                ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
                º WARNING: The design of some software may pre-   º 
                º vent the /LOW option from working properly.     º 
                º Don't use it unless necessary, and then only    º 
                º after you have tested it to be sure everything  º 
                º works as expected.  (For example, it will NOT   º 
                º work with PRINT, SHARE, FASTOPEN, MODE, or      º 
                º HyperDisk.)                                     º 
                ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼


        6.3 The /RESTRICT Option       

        This  option  can  be  used  with  HIGHDRVR,  HIGHINST,  HIGHTSR,
        HIGHUMM,  HIGHEMS3,  and HIGHEMS4.  When used, it restricts which
        128k  regions of upper memory may be allocated for use with these
        utilities.   For  a  detailed discussion of why these regions may
        need  to  be  restricted and how to control the restrictions, see
        the   discussion   of   the   RESTRICT  option  in  the  detailed
        description of LASTBYTE.SYS.  


        6.4 The /!NOPAUSE Option       

        All  of  the  utility  programs  (*.EXE files) that come with The
        Last   Byte  Memory  Manager  support  the  command  line  option
        "/!NOPAUSE".   This option eliminates the wait-for-keyboard pause
        after  an error message is displayed.  When one of these programs
        terminates  with  an  error  message,  it also returns a non-zero
        errorlevel  which  can be tested in batch files to make automatic
        decisions  about  how  to  proceed.  The  /!NOPAUSE option simply
        makes use of the errorlevel more practical.  







        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Apr 12, 1992    THE LAST BYTE MEMORY MANAGER (tm)              44


        6.5 Specifying Command Line Options with Indirect Files   

        Some  of the device drivers and utility programs in The Last Byte
        Memory  Manager  package  may  require  lots  of  options  to  be
        specified.   To  avoid  lengthly command lines, these options can
        be  placed  in  a text file if the name of that file is specified
        on  the command line preceded by the '@' character.  For example,
        you'd  probably  run  out of room if all of the following options
        were required on the LASTBYTE.SYS command line: 

                   APPEND=64 DOS=B000:32 DOS=F000:32 ? 82C302

        As  an  alternative,  create  a  corresponding  text  file called
        LASTBYTE.CFG (for example), and put the options into it: 

                A000:64 
                DOS=B000:32 DOS=F000:32 
                ? 82C302 

        (Carriage returns in the indirect file are treated as blanks) 

        Then the CONFIG.SYS command line becomes simply: 

                DEVICE=LASTBYTE.SYS @LASTBYTE.CFG 

        In  effect,  options  taken  from  the indirect file are inserted
        into  the  command  line,  so  that  one  or  more  indirect file
        references  may  be  placed  among  other  options on the command
        line: 

                DEVICE=LASTBYTE.SYS ? @TLB.1 A=A000:32 @C:\TLB\TLB.2 

        Indirect  files  may  be  used  on the command line of any device
        driver  (.SYS  files) or utility program (.EXE files) in The Last
        Byte Memory Manager package.  


        6.6 Using the DOS=F000:32 Option      

        The  64k  region  starting  at paragraph address F000 is the Bios
        ROM.   Many  computers  use  a  Bios  ROM  developed  by  AMI  or
        Phoenix.   The  more  recent  versions  of  these ROMs devote the
        first  32k  to  initialization  code that is only used during the
        boot  sequence, and use the second 32k for that portion that must
        remain  available  at  all  times.  (This seems to be true of the
        Award Bios as well, but has not been verified.) 

        By  the time your computer gets to the point in its boot sequence
        where  it  is  installing  the  device  drivers (e.g., when it is
        installing  LASTBYTE.SYS),  the  Bios  initialization  code is no
        longer  needed.   If  you  have  one of these AMI or Phoenix Bios



        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Apr 12, 1992    THE LAST BYTE MEMORY MANAGER (tm)              45


        chips,  you  can  capture  another 32k of upper memory by using a
        DOS=F000:32 option on the LASTBYTE.SYS command line.  

        Of  course,  whenever  you  press Ctrl-Alt-Del to do a warm boot,
        the  ROM  Bios  initialization  code  needs to be executed again!
        And  that could be a problem since you've effectively disabled it
        with   the   DOS=F000:32   option!    Fortunately,   LASTBYTE.SYS
        intercepts   all   keyboard  input  and  keeps  an  eye  out  for
        Ctrl-Alt-Del.   When it sees the warm boot request, it will force
        a  cold  boot  if  you've  used  the  DOS=F000:32  option.   This
        re-enables  the  entire  64k  Bios ROM so that the initialization
        code  is  reactivated  before  the processor tries to execute it.
        Otherwise a normal warm boot is used.  

                ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
                º WARNING: Some TSRs intercept keyboard interrupt º 
                º 9, and jump directly into a fixed location in   º 
                º the Bios ROM where the Warm Boot code begins.   º 
                º Unfortunately, this will bypass LASTBYTE.SYS's  º 
                º attempt to turn the ROM back on.                º 
                ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼


        6.7 Video Display RAM above 640k     

        In  general,  the  region A0000-BFFFF is the video display buffer
        area.   Various  display  adapters  (MDA, Hercules, CGA, EGA, and
        VGA)  typically  use only a small subset of this space.  The Last
        Byte  Memory  Manager  automatically  senses  what  kind of video
        display adapter is installed and reserves the space it uses.  

        The  MDA  (monochrome)  adapter  implements  a  4k text buffer at
        B0000-B0FFF,  and  the  CGA (color) adapter implements a 16k text
        and  graphics  buffer  at B8000-BBFFF.  The Hercules adapter uses
        the  entire 64k region at B0000-BFFFF in graphics modes, although
        only  the  first  4k of this space (B0000-B0FFF) is used for text
        modes.  

        The  EGA  and  VGA adapters have a 64k graphics display buffer at
        A0000-AFFFF,  and a 32k text display buffer at either B0000-B7FFF
        (when  used  with  a monochrome display), or at B8000-BFFFF (when
        used with a color display).  

        The  following  chart summarizes these regions as well as some of
        the  DOS  and  APPEND  optons  you  may  be  able  to  use on the
        LASTBYTE.SYS  command  line  with these adapters.  Unfortunately,
        the  ROM  bios  on  a  (very)  few  PC's may write into locations
        outside  the  area reserved for a particular type of display.  If
        you  decide  this  is  happening, you may need to add one or more
        EXCLUDE  options to the LASTBYTE.SYS command line to disable that
        region.  



        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Apr 12, 1992    THE LAST BYTE MEMORY MANAGER (tm)              46



             LASTBYTE.SYS Command Line Options for Display Adapters

             Adapter         Reserved        DOS         APPEND
             -------         --------        -------     -------
             CGA             B800:16                     96
             MDA             B000:4                      64
             Hercules        B000:64         B400:48     64

             EGA/VGA         A000:64         BC00:16     96
             w/Color         B800:32 
             Display

             EGA/VGA         A000:64         B400:16     64
             w/Mono          B000:32
             Display

             VGA Bios        C000:32         C600:8 (see next section)

                  Note: Windows 3.0 may write in the region B000-BFFF.

        The  ability  to  use  the  DOS and APPEND options depends on the
        availability  of other memory in the indicated area.  For further
        information, consult the appendix on "CHIPSET LIMITATIONS".  


        6.8 Video Adapter Bios ROMs      

        MDA  and CGA use the standard ROM Bios; they have no ROM of their
        own.   EGA  and  VGA adapters, however, incorporate their own ROM
        Bios  chip  right on the adapter card.  LASTBYTE.SYS successfully
        recognizes these ROMs, but has to treat VGA in a special manner: 

        The  VGA  adapter  made  by  IBM  has  a  24k  ROM  installed  at
        C0000-C5FFF,  which  means  that  the 8k at C6000-C7FFF should be
        usable.   Although  almost  all  VGA  clones have a ROM signature
        that  indicates  24k,  many of them use the C6000-C7FFF space for
        ROM  Bios  or  RAM  extensions  that  provide  their  "Super VGA"
        features.    In   particular,   the  Video7  and  Paradise  VGA's
        incorporate  their  own  RAM from C6000-C7FFF.  (This may also be
        true  of  other  VGA boards that uses a VLSI chip manufactured by
        Chips   and  Technologies,  Tseng  Labs,  Paradise,  or  Headland
        Technologies.)    For   this   reason,  when  LASTBYTE.SYS  finds
        anybody's  VGA  adapter, it automatically assumes that there is a
        32k ROM at C0000-C7FFF.  









        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Apr 12, 1992    THE LAST BYTE MEMORY MANAGER (tm)              47


        6.9 LASTBYTE.SYS and Expanded Memory      

        Expanded  memory always has an associated device driver.  If that
        driver  is loaded before LASTBYTE.SYS in the CONFIG.SYS file (and
        if  the  hardware is enabled) LASTBYTE.SYS will recognize the 64k
        EMM  page frame of the expanded memory and do the right thing: It
        will  treat the page frame like any other adapter ram and disable
        the  motherboard RAM that falls in the same address space so that
        it  doesn't  interfere  with the page frame.  For example, if the
        EMM  driver is loaded first, LASTBYTE.SYS will report the 64k EMM
        page frame as "EMS Page Frame".  

        This  works  fine,  of  course,  but loading the EMM driver first
        precludes  the  possibility  of loading it into upper memory.  To
        get  the  EMM  driver  into  upper  memory  means that it must be
        loaded after LASTBYTE.SYS, but you must be careful! 

        If   LASTBYTE.SYS  is  loaded  first,  the  page  frame  will  be
        recognized only in two cases: 

             o  The   page   frame   used  by  the  expanded  memory
                controller  built  into some memory controller chips
                will   be  recognized  and  reported  as  "EMS  Page
                Frame".  

             o  The  page  frame  of a REAL expanded memory board is
                (if  enabled)  recognized  and  reported as "Adapter
                RAM".  

        In either case, LASTBYTE.SYS will not use that memory space.  

                ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
                º WARNING: Some EMS boards must be enabled by     º 
                º their device driver before they respond as      º 
                º read/write memory.  This prevents LASTBYTE.SYS  º 
                º from recognizing them, and you may need a       º 
                º BANKSWITCH option to keep LASTBYTE.SYS from     º 
                º using the page frame memory space.              º 
                ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

        If  you  don't  have  an  expanded  memory board, but have used a
        device  driver  (like EMM386) that EMULATES expanded memory using
        extended  memory,  then LASTBYTE.SYS will not know about the page
        frame  unless  the  emulator is loaded first.  If LASTBYTE.SYS is
        loaded   first,   then   you   must   use   a   "EXCLUDE="   (not
        "BANKSWITCH="!)  command line option of LASTBYTE.SYS to reserve a
        64k  region  where  the  emulated  page frame can be placed.  For
        EMM386,  the  page  frame must be positioned at C000, C400, C800,
        CC00, D000, D400, D800, DC00, or E000.  





        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Apr 12, 1992    THE LAST BYTE MEMORY MANAGER (tm)              48


        6.10 Fine-Tuning your Adapter Hardware Configuration     

        Many  adapter  cards  occupy  some  portion  of the upper address
        space.   Some  of  these  cards,  such  as SCSI Disk Controllers,
        often  have  DIP  switches or jumpers that can be used to set the
        address space they occupy to one of a few alternatives.  

        If  the memory map displayed by HIGHMEM is fragmented because one
        of  these adapters sits between two "....DOS Free" areas, you may
        want  to  try  to  reposition  the address space occupied by that
        adapter  by  modifying  the  DIP switch or jumper settings on the
        card.  

        Having  one  large  free  memory block is better than two smaller
        ones  because TSR's and device drivers almost always require more
        memory  during  initialization  than  once  installed.   In other
        words,  neither of the two smaller blocks may be large enough for
        the installation, but might if they were combined.  




































        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Apr 12, 1992    THE LAST BYTE MEMORY MANAGER (tm)              49


                    CHAPTER 7 - USE WITH OTHER SOFTWARE     


        7.1 Microsoft's FASTOPEN and MODE programs     

        The  FASTOPEN  and  MODE programs that come with MS-DOS are TSR's
        and  as  such may be loaded into upper memory with either HIGHTSR
        or  HIGHINST.   Once installed, each requires very little memory,
        something  on  the  order  of 10k or less.  However, neither will
        install  unless  a  lot  of  memory  is available - approximately
        50-90k.   (The  actual requirement depends partly on command line
        options;  you  can  determine  the  requirement  using  the /SIZE
        option of HIGHTSR or HIGHINST.) 

                ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
                º WARNING: Do NOT use the /LOW option of HIGHTSR  º 
                º or HIGHINST with FASTOPEN or MODE - it won't    º 
                º work and could damage data on your disk!        º 
                ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

        The  worst  part  is  that  if  FASTOPEN  fails to install itself
        successfully,  it  doesn't  issue  any  error message - it simply
        doesn't   display   the   normal   "FASTOPEN  installed"  sign-on
        message.   Moral:  Let  FASTOPEN and MODE be the first TSR's that
        are  installed into High Memory in your AUTOEXEC.BAT file so that
        they get access to the maximum amount of memory.  

        The  second  hassle  with  these two TSR's is that they cannot be
        removed  by  using  HIGHMARK and HIGHUNDO.  Evidently they modify
        memory  other than that tracked by HIGHMARK (the interrupt vector
        table and that memory allocated to them).  


        7.2 Microsoft's SHARE program       

        MS-DOS  4  installs the SHARE program automatically if you have a
        hard  disk which is greater than 32 MB in a single partition.  It
        does  this  without  asking  because  it is otherwise possible to
        corrupt  the  data on the disk when running programs that use the
        old File Control Block (FCB) approach to access files.  

        Unfortunately,  some  internal parts of MS-DOS 4.0 also still use
        FCB's!   So  don't  try  to  prevent  SHARE  from being loaded by
        removing  it  from  your system!  If MS-DOS can't find it, you'll
        get  a  warning message during the boot saying that "SHARE should
        be   loaded   for   large  media".   You  could  load  it  during
        AUTOEXEC.BAT   processing,  but  you'll  still  get  the  warning
        because the check occurs during CONFIG.SYS processing.  






        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Apr 12, 1992    THE LAST BYTE MEMORY MANAGER (tm)              50


                ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
                º NOTE: Version 5 of MS-DOS has corrected this    º 
                º problem and no longer loads SHARE automatically º 
                º regardless of the size of your hard disk.       º 
                ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

        So  how  can  you load this TSR into upper memory without getting
        the   warning?    MS-DOS   recently   introduced  the  "INSTALL="
        directive  that  allows  TSR's  to be installed during CONFIG.SYS
        processing.   Programs  that Microsoft suggests be loaded in this
        manner include FASTOPEN, KEYB, NLSFUNC, and SHARE.  For example: 

                            INSTALL=C:\DOS\SHARE.EXE

        The  above  command,  however,  causes SHARE to be loaded down in
        conventional memory.  to get it into upper memory, use: 

                      INSTALL=HIGHINST.EXE C:\DOS\SHARE.EXE

                ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
                º WARNING: Do NOT use the /LOW option of HIGHINST º 
                º with SHARE - it won't work and could damage     º 
                º data on your disk!                              º 
                ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼


        7.3 Microsoft's MS-DOS 5.0       

        With   the  introduction  of  MS-DOS  5.0,  Microsoft  has  added
        extensive  support  for  loading software into high memory.  This
        includes  not  only  device drivers and TSRs, but also the MS-DOS
        disk  buffers,  the master environment, and most of the operating
        system itself.  

        This  capability  requires the use of an Upper Memory Block (UMB)
        server  such as Key Software Products' HIGHUMM.SYS.  Although the
        MS-DOS  5.0  version  of EMM386 has been modified to provide such
        support,  there  are several disadvantages to using it instead of
        The Last Byte Memory Manager to load software high: 

             o  EMM386   requires   a   386   or  better  processor.
                (HIGHUMM does not.) 

             o  EMM386  requires  that  HIMEM.SYS  be  loaded first.
                (HIGHUMM  does  not.   However, HIMEM is also needed
                to  load  the  operating system itself into extended
                memory;  The  Last Byte Memory Manager allows you to
                load HIMEM into upper memory using HIGHDRVR.) 






        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Apr 12, 1992    THE LAST BYTE MEMORY MANAGER (tm)              51


             o  Using  HIMEM  and EMM386 as the basis of UMB support
                requires  that  both  be  loaded  into  conventional
                memory, where they use approximately 10k bytes.  

             o  EMM386  puts  the  processor  into  protected  mode,
                adding  an  instruction  execution  time  penalty of
                about 5%.  

        There  are  two  basic  approaches  that  you  can  take  to load
        software  into  upper  memory  using MS-DOS 5.0 and The Last Byte
        Memory  Manager.   The  first  of these is to install HIGHUMM and
        use  the  'DEVICEHIGH'  and  'LOADHIGH'  commands  introduced  in
        MS-DOS   5.0;   the   other   is  to  use  HIGHDRVR  and  HIGHTSR
        (HIGHINST).  

        We  recommend  the  latter  approach because HIGHDRVR and HIGHTSR
        provide  a  richer  set  of options for controlling the load high
        process.  


        7.3.1 Using DEVICEHIGH and LOADHIGH      

        To  use  this  approach,  your CONFIG.SYS file should contain the
        following lines: 

                DOS=HIGH,UMB 
                DEVICE=LASTBYTE.SYS {and any options} 
                DEVICE=HIGHDRVR.SYS C:\DOS\HIMEM.SYS 
                DEVICE=HIGHUMM.SYS {and any options} 

        Then  you can use the MS-DOS 5.0 DEVICEHIGH command in additional
        lines  of  your CONFIG.SYS file to load your other device drivers
        into upper memory, as in: 

                DEVICEHIGH={device driver to be loaded high} 
                DEVICEHIGH={device driver to be loaded high} 
                        . . .  
                DEVICEHIGH={device driver to be loaded high} 

        With  this  CONFIG.SYS file, your AUTOEXEC.BAT file may load TSRs
        high using the MS-DOS 5.0 LOADHIGH command as in: 

                LOADHIGH C:\DOS\PRINT 


        7.3.2 Using HIGHDRVR and HIGHTSR      

        The  second approach is to use the HIGHDRVR and HIGHTSR utilities
        of  The  Last  Byte  Memory Manager in the normal manner.  To use
        this  approach, your CONFIG.SYS file should contain the following
        lines: 



        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Apr 12, 1992    THE LAST BYTE MEMORY MANAGER (tm)              52



                DOS=HIGH 
                DEVICE=LASTBYTE.SYS {and any options} 
                DEVICE=HIGHDRVR.SYS C:\DOS\HIMEM.SYS 

        Then  you can use HIGHDRVR in additional lines of your CONFIG.SYS
        file to load your other device drivers into upper memory, as in: 

                DEVICE=HIGHDRVR.SYS {device driver to be loaded high} 
                DEVICE=HIGHDRVR.SYS {device driver to be loaded high} 
                        . . .  
                DEVICE=HIGHDRVR.SYS {device driver to be loaded high} 

        With  this  CONFIG.SYS  file,  your AUTOEXEC.BAT file should load
        TSRs high using HIGHTSR as in: 

                HIGHTSR C:\DOS\PRINT 


        7.4 Microsoft's Windows 3.0       

        In  general,  The  Last  Byte Memory Manager has a high degree of
        compatibility  with  Windows  3.0.   If  you  are  having trouble
        running  Windows,  first  be  sure  that  your system is properly
        configured  so  that it runs without The Last Byte Memory Manager
        installed.    If   you   have   isolated  the  problem  to  their
        combination,  then perhaps the following information will help to
        correct the problem: 


        7.4.1 Modifying the Windows SYSTEM.INI File     

        With  Windows  3.0 running in 386 enhanced mode, LASTBYTE.SYS and
        Windows  will  both  try  to  use  the  upper  memory  area, thus
        creating  a  conflict.   To  avoid  the  conflict,  you  must ask
        Windows  to  not  use  this  region.  This can be done with a few
        configuration  options  in  the  [386Enh]  section of the Windows
        SYSTEM.INI file: 

                  EMMExclude=A000-FFFF
                  HighFloppyReads=no
                  DualDisplay=yes
                  SystemROMBreakPoint=no

        If  you have used the "EXCLUDE" option of LASTBYTE.SYS to disable
        any  region  of  the upper memory, then Windows may be told it is
        ok  to  use  that  area.   For example, if LASTBYTE.SYS is loaded
        using the line: 

                       DEVICE=LASTBYTE.SYS EXCLUDE=D000:64




        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Apr 12, 1992    THE LAST BYTE MEMORY MANAGER (tm)              53


        then  you may use the following configuration option (in addition
        to the EMMExclude option above) in your SYSTEM.INI file: 

                              EMMInclude=D000-DFFF

        The  EMMInclude  option  will take precedence over the EMMExclude
        option when the two overlap, as above.  


        7.4.2 Positioning an EMS Page Frame     

        If  you  are using the Real or Standard modes of Windows, you may
        have  installed  an EMS device driver for those applications that
        need  expanded  memory.  In an attempt to reduce fragmentation of
        upper  memory, it is useful to position the EMS Page Frame either
        at  the  bottom  or  top  of  an  otherwise empty region of upper
        memory.   However,  if  you  have  used the DOS=F000:32 option to
        gain  another  32k  of  DOS  memory, don't position your EMS Page
        Frame  at  E800  -  Windows  will not run with it any higher than
        E000.  

        The  Enhanced  386  mode  of  Windows  will automatically emulate
        expanded   memory   for   those  applications  that  require  it.
        Unfortunately,   Windows   ignores   the  EMMExclude  option  and
        positions  the  EMS  page frame in upper memory.  If the same 64k
        area  is used by The Last Byte Memory Manager for something else,
        your   system   may   hang.   To  correct  the  problem,  add  an
        "EMSPageFrame=nnnn"  option  in  your  SYSTEM.INI  file  to  tell
        Windows   where   to   put  the  page  frame,  combined  with  an
        "EXCLUDE=nnnn:64"  option  on  the  LASTBYTE.SYS  command line to
        keep it from using this area.  


        7.4.3 "Unsupported Data Configuration"       

        The  386  Enhanced  mode of Windows 3.0 has a restriction that it
        cannot  run  when  certain  types  of  software  have been loaded
        high.   When this happens, Windows will terminate and display the
        error  message,  "Unsupported  Data  Configuration".   This  only
        happens  in  386  Enhanced mode, and is not related in particular
        to use of The Last Byte Memory Manager.  

        Device  drivers  that are known to load high without this problem
        include  HIMEM.SYS,  MOUSE.SYS, SETVER.SYS, ANSI.SYS, and all the
        Key  Software Products device drivers.  A device driver and a TSR
        known  to  cause this problem are EGA.SYS and DOSKEY.COM.  If you
        are  experiencing  this error message, you can either run Windows
        in   another   mode,   or   try  modifying  your  CONFIG.SYS  and
        AUTOEXEC.BAT files to locate and remove the offending software.  

        Microsoft   is  removing  this  restriction  in  version  3.1  of



        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Apr 12, 1992    THE LAST BYTE MEMORY MANAGER (tm)              54


        Windows.  


        7.4.4 HIGHMEM and Windows 386 Enhanced Mode    

        MS-DOS  applications  run from inside Windows 3.0 are given their
        own   "virtual"   address  space  of  640k.   Windows  tells  the
        processor   to  map  memory  references  in  this  space  to  the
        particular  640k  of  physical memory which has been allocated to
        the  application.   References  outside this range are considered
        invalid  and  thus  return  garbage.   Since HIGHMEM is a program
        that  inspects  upper  memory  between 640k and 1 meg, there's no
        way  it  can  execute  properly  in  this  context.  HIGHMEM will
        behave normally outside of Windows.  


        7.4.5 HIGHDISK and Windows 386 Enhanced Mode    

        HIGHDISK.SYS  also  uses memory in the 640k to 1 meg range and so
        is  susceptible  to the same problems that HIGHMEM experiences as
        discussed  above.  Outside of Windows, and in any mode other than
        386 Enhanced Mode, HIGHDISK will behave normally.  


        7.5 HyperWare's HyperDisk        

        HyperDisk  is  a  shareware disk caching utility.  It's too large
        to  load  high  with  HIGHDRVR  or  HIGHTSR  under  the 32K limit
        imposed  by  the  unlicensed  evaluation version of The Last Byte
        Memory  Manager.   However,  if  your  computer  uses a Chips and
        Technologies  NEAT  or  386/AT  chipset, you can work around this
        limitation  by  using HyperDisk's "XS" option to load itself into
        the  48k block starting at E400.  Be sure to exclude this area by
        using the following option on the LASTBYTE.SYS command line: 

                DEVICE=LASTBYTE.SYS EXC=E400:48 

        If  you  have a licensed version of The Last Byte Memory Manager,
        or  if  you don't have one of the Chips and Technologies chipsets
        mentioned  above,  then  a  better  approach  is  to  use  either
        HIGHDRVR  or  HIGHTSR  (as  appropriate)  to  load HyperDisk high
        (without  HyperDisk's  "XS" option).  This method guarantees that
        the minimum amount of upper memory will be used.  











        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Apr 12, 1992    THE LAST BYTE MEMORY MANAGER (tm)              55


        HyperDisk  can  be  downloaded  from  HyperWare's  BBS  at  (615)
        864-6871, or obtained directly from: 

                HyperWare 
                RR#1, Box 91 
                Pall Mall, TN 38577 
                Voice: (615) 864-6868 
                FAX: (615) 864-6870 


        7.6 J.P. Software's 4DOS       

        4DOS  is  a  shareware  replacement for COMMAND.COM.  HIGHUMM.SYS
        may  be  used  to  move the 4DOS command processor and its master
        environment  into  "Upper  Memory  Blocks"  (UMB's)  in the upper
        memory  area,  thus  reducing  the  amount of conventional memory
        below 640k used by 4DOS from 3.4k bytes to 256 bytes.  

        First  you  must install HIGHUMM.SYS as described earlier in this
        manual.   Then  add  a  "SHELL="  line  to  CONFIG.SYS  for 4DOS,
        including  the options "/U" (to place the command processor in an
        UMB)  and  "/E:512U" (to place the master environment in an UMB).
        The  value "512" is of course only an example - other environment
        sizes  may  be  specified.   You  may  also want to specify these
        options   for   secondary   shells  in  the  4DSHELL  environment
        variable.  Consult the 4DOS documentation for further details.  

        4DOS  may  be downloaded from Channel 1 BBS at (617) 354-8873, or
        obtained directly from: 

                J.P. Software             CompuServe: 75300,210 
                P.O. Box 1470             BIX: "trawson" 
                E. Arlington, MA 02174    Internet, Bitnet, etc: 
                Voice: (617) 646-3975       75300.210@compuserve.com 
                Fax: (617) 646-0904 


        7.7 David Hamilton's BUFFIT       

        There's  a very nice shareware scroll-back TSR called BUFFIT that
        saves  lines  of  text that have been scrolled off the top of the
        screen  and allows you to pull them back down for review.  One of
        the  advantages  of  version  3.0  and later of BUFFIT is that it
        will  load  itself  entirely  into a UMB provided by HIGHUMM.SYS,
        thus using no conventional memory at all.  

        To  install  BUFFIT into upper memory, first you must install the
        HIGHUMM.SYS  device  driver  by  inserting the following lines in
        your CONFIG.SYS file: 

                DEVICE=LASTBYTE.SYS {and any LASTBYTE options} 



        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Apr 12, 1992    THE LAST BYTE MEMORY MANAGER (tm)              56


                DEVICE=HIGHUMM.SYS 

        Then  all  you  have to do is reboot your computer and run BUFFIT
        from  the  command  line,  or  else  add  it to your AUTOEXEC.BAT
        file.  

        BUFFIT  is  available  from  a number of BBS's, usually under the
        filename BUFFIT30.ZIP.  


        7.8 Charles Lazo's WAS       

        On  a  computer  with  no  expanded memory, you might want to use
        HIGHEMS3  to  provide  some  Expanded  Memory  for Charles Lazo's
        scroll-back  TSR, WAS.COM.  This utility saves lines of text that
        have  been  scrolled  off the top of the screen and allows you to
        pull  them  back down for review.  WAS is available from a number
        of BBS's, usually under the filename WAS062.ZIP.  




































        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Apr 12, 1992    THE LAST BYTE MEMORY MANAGER (tm)              57


                        APPENDIX 1 - HOW TO REACH US     


        The  KSP  telephone  (415-364-9847)  is shared by our BBS and our
        voice  mail  answering  system.   Approximate  hours of operation
        are: 

                   Voice mail system: 8am - 5pm PST (weekdays)

                 BBS system: 5pm - 8am PST (24 hrs on weekends)

               BBS Parameters: 1200/2400/9600 baud (v.32, v.42bis)
                             8 data bits, No Parity

        If  your call is answered by the voice mail system, it can take a
        message   that will be automatically forwarded to someone who can
        return  your  call as soon as possible.  In addition, it offers a
        touch-tone driven menu of useful information about our product.  

        If  you have access to electronic mail, you can send us a message
        via any of the following: 

        On BITNET, send mail to: DLEWIS@SCU.BITNET

        On COMPUSERVE, send mail to: >Internet:DLEWIS@SCUACC.SCU.EDU

        On CONNECT, send mail to: CONNECT id "DASNET"

                1st line of message: \"DLEWIS@SCUACC.SCU.EDU\"@DASNET

        On FIDONET, send mail to: UUCP

                1st line of message: To: DLEWIS@SCUACC.SCU.EDU

        On INTERNET, send mail to: DLEWIS@SCUACC.SCU.EDU

        On MCI,

                 At the "To:" prompt enter: DLEWIS (EMS)
                At the "EMS:" prompt enter: Internet
                At the "Mbx:" prompt enter: DLEWIS@SCUACC.SCU.EDU

        On PRODIGY, send mail to: VGDC59A

        On TELENET's Telemail Service:

                Send to: [INTERMAIL/USCISI]TELEMAIL/USA
                1st line of message: Forward: ARPA
                2nd line of message: To: DLEWIS@SCUACC.SCU.EDU





        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Apr 12, 1992    THE LAST BYTE MEMORY MANAGER (tm)              58


                      APPENDIX 2 - ACKNOWLEDGEMENTS        


        The  Last  Byte  Memory  Manager  wouldn't  exist without all the
        companies  that  manufacture  the  shadow  ram  memory controller
        chips,  and  who  have  provided techinical information on how to
        program  their  configuration registers.  If you know of a memory
        controller  chip  we  haven't included, please let us know and we
        will try to add it.  

        The  Last  Byte  Memory  Manager consists of almost a megabyte of
        source  code,  written  mostly in C with a sprinkling of assembly
        language,  and  compiled using version 3.1 of the DeSmet/C-Ware C
        compiler.   We  are grateful for the simplicity, flexibility, and
        speed  of this compiler, as well as the generous support provided
        by Joel and Susan Farley of C-Ware Corporation.  

        The  Last Byte Memory Manager could not have been created without
        the  gracious  support  of  many  people.   We  wish to thank the
        following  individuals  who  helped  to  test  beta  versions  or
        offered  useful  suggestions  for  new  features: Ron Cohen, J.B.
        Compton,   David   Durgee,  Mike  Hagerty,  Scott  Jordahl,  Alan
        Lambert,  Rob  Nee,  Kevin Parris, Dan Proctor, Graham Robertson,
        Ken   Sanquist,  Tony  Sheehan,  Peter  Summers,  Steve  Hodsdon,
        Anthony  Cox, My Phung, Martin Beckmann, and Prof. Timo Salmi (of
        the University of Vaasa, Finland).  

        Thank's  also  go to Tom Rawson of J. P. Software for providing a
        copy  of  4DOS, to Sue Nageotte of Digital Research for providing
        a  copy  of DR DOS, and to Pat Gelsinger of Intel Corporation for
        lending  his  intimate  knowledge  of the 80x86 instruction sets.
        And  finally, a special thanks to Serge Caron and Roger Cross for
        their suggestions, technical advice, patience, and friendship.  





















        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Apr 12, 1992    THE LAST BYTE MEMORY MANAGER (tm)              59


                     APPENDIX 3 - CHIPSET LIMITATIONS       


        Some  of the features offered by The Last Byte Memory Manager are
        dependent  on  the  presence  of  a  shadow ram memory controller
        chip,  what  memory  it  controls,  and  the organization of that
        memory  into  regions.   Shown  below is a summary of RAM and ROM
        regions  controlled  by  each of the memory controller chips that
        we  support.   Each  entry indicates the starting segment address
        of  memory, followed by an indication of the organization of that
        memory into regions.  

        Part No.        Ram Range       RAM Regions             ROM Regions
        --------        ---------       ----------              -----------
        82C212          A000-FFFF       A000:24x16k             C000:4x64k
        82C222          A000-FFFF       A000:24x16k             C000:4x64k
        82C230          A000-FFFF       A000:24x16k             C000:4x64k
        82C235          A000-FFFF       A000:24x16k             C000:8x32k
        82C241          A000-FFFF       A000:24x16k             C000:4x64k
        82C281          C000-EFFF       C000:12x16k             C000:3x64k
        82C282          C000-EFFF       C000:12x16k             C000:3x64k
        82C283          C000-EFFF       C000:12x16k             C000:3x64k
        82C302          A000-FFFF       A000:24x16k             C000:4x64k
        82C302C         A000-FFFF       A000:24x16k             C000:4x64k
        82C307          A000-FFFF       A000:24x16k             C000:4x64k
        82C311          A000-FFFF       A000:24x16k             C000:4x64k
        82C322          A000-FFFF       A000:16x16k,1x128k      C000:2x64k,1x128k
        82C351          A000-FFFF       A000:24x16k             C000:4x64k
        82343           C000-EFFF       C000:12x16k             n/a
        82346           C000-EFFF       C000:12x16k             n/a
        82359           A000-FFFF       A000:24x16k             n/a
        82C382          C000-EFFF       C000:12x16k             C000:3x64k
        82C391          C000-EFFF       C000:12x16k             C000:3x64k
        82C461          C000-EFFF       C000:12x16k             C000:3x64k
        82C482          C000-EFFF       C000:12x16k             C000:3x64k
        82C491          C000-EFFF       C000:12x16k             C000:3x64k
        82C493          C000-EFFF       C000:12x16k             C000:3x64k
        82C496          C000-EFFF       C000:12x16k             C000:3x64k
        82C682          C000-FFFF       C000:8x16k,2x64k        n/a
        82C812          A000-FFFF       A000:24x16k             C000:4x64k
        82C836          A000-FFFF       A000:24x16k             C000:8x32k
        82C841          A000-FFFF       A000:24x16k             C000:4x64k
        FRX36C300       C000-FFFF       C000:6x32k,1x64k        n/a
        SL82C361        C000-FFFF       C000:8x16k,2x64k        C000:8x16k,2x64k
        SL82C461        C000-FFFF       C000:8x16k,2x64k        C000:8x16k,2x64k
        ST62C202        E000-FFFF       E000:4x32k              n/a
        ST62C241        E000-FFFF       E000:4x32k              n/a
        ST62C251        E000-FFFF       E000:4x32k              n/a
        TACT82411       A000-FFFF       A000:24x16k             C000:4x64k
        TACT82S411      A000-FFFF       A000:24x16k             C000:4x64k
        UM82C212        A000-FFFF       A000:24x16k             C000:4x64k



        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Apr 12, 1992    THE LAST BYTE MEMORY MANAGER (tm)              60


        UM82C481        C000-FFFF       C000:8x16k,2x64k        C000:8x16k,2x64k
        VL82C202        A000-FFFF       A000:6x64k              n/a
        VL82C320        C000-EFFF       C000:12x16k             n/a
        VL82C330        C000-EFFF       C000:12x16k             n/a
        VL82C486        A000-FFFF       A000:24x16k             n/a

















































        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Apr 12, 1992    THE LAST BYTE MEMORY MANAGER (tm)              61


                    APPENDIX 4 - LICENSED DISTRIBUTORS       


        You  can  order directly from Key Software Products or any of the
        licensed  distributors  listed  below.   Those  which  can accept
        credit  card  orders are noted.  If you order by credit card, you
        must  indicate  the  type  of  card,  the  card number, your name
        exactly as printed on the card, and the card expiration date.  

        Information  in  this  list  is subject to change without notice.
        Foreign  exchange rates vary and thus affect overseas pricing, so
        it   is  a  good  idea  to  check  with  the  distributor  before
        ordering.  

        Distributors  are  for ordering only.  For additional information
        about  dealer pricing, volume discounts, site licensing, shipping
        of  product,  returns,  latest  version number or other technical
        information, call or write Key Software Products directly.  

        Most  distributors  can  provide  the  access  key directly.  The
        Public   (software)  Library,  however,  accepts  your  telephone
        order,  and  then  forwards  an  E-Mail  message  to Key Software
        Products.   Delivery of this message may take one or two days. We
        will  contact you and provide the access key upon receipt of this
        purchase confirmation.  

        Companies  interested  in obtaining 10 or more copies of The Last
        Byte  Memory  Manager  with  discounted  pricing  should  have an
        officer  of the company (such as the president, a vice president,
        director,  etc.) complete the Site License Order Form and send it
        directly  to Key Software Products, British Software Licensing in
        the  United  Kingdom,  or  to  Eurocom  Shareware in Holland.  No
        other distributor will process a Site License request.  


        KEY SOFTWARE PRODUCTS           Phone: (415) 364-9847
        440 Ninth Avenue                Price: US $29.95 + Tax (CA)
        Menlo Park, CA 94025            Method: Check


        The Public (software) Library   Phone: (800) 242-4775, or
        P.O. Box 35705                         (713) 524-6394
        Houston, Texas 77235-5705         FAX: (713) 524-6398
                                        CompuServe: 71355,470
                                        Price: US $29.95 + Tax (TX)
                                        Method: MC, Visa, AmEx,
                                                Discover Card







        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Apr 12, 1992    THE LAST BYTE MEMORY MANAGER (tm)              62


        HYPERWARE (makes HyperDisk)     Phone: (615) 864-6868
        RR#1, Box 91                      FAX: (615) 864-6870
        Pall Mall, TN 38577             CompuServe: 72230,2321
                                        Price: US $29.95 + Tax (TN)
                                        Method: Master Card, Visa


        EUROCOM SHAREWARE               Contact: Mr. Gary van Beeck
        Zwedenburg 119                  Phone: (+31.70) 347-3777
        NL-2591 BD The Hague              FAX: (+31.70) 347-7356
        HOLLAND                         Price: Hfl 74.-- (guilders only)
                                        Method: By Eurocheque, or
                                        Postbank (Giro): 188423
                                        payable to: G. van Beeck


        BRITISH SOFTWARE LICENSING      Contact: Mr. Graham Robertson
        280 (T/L) West Princes Street   Phone: (44.41) 339-8855 x5021
        Glasgow G4 9EU                         (44.41) 339-7264 (msg)
        UNITED KINGDOM                  Price: 21 pounds
                                        Method: Access, Visa, MC, Eurocard

        Internet E-Mail: Graham_Robertson@vme.glasgow.ac.uk































        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Apr 12, 1992    THE LAST BYTE MEMORY MANAGER (tm)              63


                      APPENDIX 5 - LIMITED WARRANTY       


        This  software  is provided 'as is' without warranty of any kind,
        either  expressed  or  implied, including, but not limited to the
        implied   warranties   of   merchantability  and  fitness  for  a
        particular  purpose.   The  entire  risk  as  to  the quality and
        performance of the program is with you.  

        Some  states do not allow the exclusion of implied warranties, so
        the  above  exclusions may not apply to you.  This warranty gives
        you  specific  legal  rights  and  you may also have other rights
        which vary from state to state.  

        Key  Software  Products  has  taken  due  care  in  preparing the
        documentation  and  software  included  in  The  Last Byte Memory
        Manager   to   ascertain  their  correctness  and  effectiveness.
        However,  Key  Software  Products does not warrant that operation
        of  this  software  will  be  uninterrupted or error free.  In no
        event  shall  Key  Software  Products be liable for incidental or
        consequential  damages  in  connection with or arising out of the
        furnishing, performance, or use of this software.  


                                     LICENSE

        You  MAY  use  this software on any computer or computers in your
        possesion, but on no more than one computer at any given time.  

        You  MAY  copy this software into any machine readable or printed
        form  for  backup or modification purposes in support of your use
        of the software.  

        You  MAY  distribute  the original unmodified, unlicensed version
        of  this  software,  but you may not charge a fee exceeding $5.00
        to  cover  the  cost of duplicating, shipping, and handling.  You
        may NOT distribute a licensed version of this software.  

        You  may  NOT  use,  copy, modify, sublicense, assign or transfer
        this  software  and  its license, or any copy or modification, in
        whole  or  in  part,  except  as  expressly  provided for in this
        license.  












        Copyright (C) 1990-92, Key Software Products. All Rights Reserved