WHAT'S NEW IN VERSION 2.00

- LASTBYTE.SYS: Now automatically measures and displays the processor
	cache size, if there is one.

- LASTBYTE.SYS, LICENSE.EXE: The hardware signature test has been
	eliminated.  The need for the protection that it provided has
	been eliminated by a change in the overall protection
	strategy.

- LASTBYTE.SYS: A new "PHYSICAL" option is now REQUIRED (!) on the
	LASTBYTE.SYS command line to specify the particular memory
	controller, as in PHYSICAL=82C302.  The automatic detection
	of memory controller chipset type has been removed because it
	caused some motherboards to "lock up".

- LASTBYTE.SYS: Added options "MOVE=VIDEOBIOS" and "MOVE=MAINBIOS" which
	try to move the corresponding bios to a better location
	within the available upper memory that reduces fragmentation
	of free memory.  "MOVE=MAINBIOS,ADDHOLES" will create seven
	holes in the residual 8k left at FE00 for a total of more
	than 3k.

- LASTBYTE.SYS: Added option "MOVE=OVERLAY" for chipsets in which the
	main bios shadow ram (F000-FFFF) cannot be made read/write
	(OPTi and ETEQ).  This option puts that ram in write-only
	mode, copies the video bios on top of the main bios
	initialization code at the beginning of the bios, then
	returns the ram to read-only mode.  Then the old video bios
	region is converted to usable Hi-DOS memory.

- HIGHTSR,HIGHDRVR: Added a second numeric parameter to the "/SIZE:n"
	option, as in "/SIZE:n1,n2", where "n2" is the final
	(resident) size.  If specified and the largest free block is
	only large enough to satisfy "n2" but not "n1", then data
	blocks residing in High-DOS memory immediately above the free
	area are temporarily removed to provide "n1" free bytes
	during initialization and then replaced after initialization
	when the final resident requirement is "n2".  Examples of
	such data blocks include data for HIGHDISK, HIGHEMS3/4,
	HIGHSPLR, HIGHKEY, HIGHENV, etc.

- HIGHUMM, HIGHDISK, HIGHEMS3, HIGHEMS4, and HIGHKEY: Now load most
	of their code into Bank-Switch memory if available, leaving
	only a small stub (~175-300 bytes) in High-DOS memory.
	HIGHDISK has also been optimized to reduce total memory
	requirements by 13%.

- LASTBYTE.SYS, HIGHUMM, HIGHEMS3, and HIGHEMS4: No longer leave a
	32-byte stub in conventional memory.  HIGHDRVR only leaves a
	stub when the driver loaded into upper memory is a "block"
	device such as a ram disk.

- HIGHDRVR.SYS: Now loads character device drivers that contain more
	than one logical device.

- HIGHSPLR.EXE: The option "POLL" now disables interrupt-driven output;
	this may be necessary, for example, if you're using another
	parallel port with Lantastic/Z.  The option "RESET" now
	issues a form feed after emptying the buffer.

- HIGHFILE.EXE: A new utility to place FILES=n in upper memory.

- The user abort key set (Ctrl+Alt+Left_Shift) has been modified so
	that either left or right shift may be used.

- All *.EXE files: Added a new option "/!NOPAUSE" that eliminates the
	wait-for-keyboard pause after an error message is displayed.
	When one of these programs terminates with an error message,
	it also returns a non-zero errorlevel which can be tested in
	batch files to make automatic decisions about how to proceed.
	The /!NOPAUSE option simply makes use of the errorlevel more
	practical.

- LASTBYTE.SYS: The "NOFRAME" (now called "NOEMS") and "OVERRIDE"
	options are now specified as part of the "PHYSICAL" option
	since they are specific to the memory controller, as in
	PHYSICAL=82C212,OVERRIDE.

- LASTBYTE.SYS: Implemented "NOEMS" option for SUNTAC chipsets to
	provide another 128k of upper memory for users who don't
	need EMS, as in PHYSICAL=62C241,NOEMS.  Also implemented
	"OVERRIDE" option to force enable shadow ram (instead of
	relocation) & Expanded Memory (if used w/"NOEMS"), as in
	PHYSICAL=62C241,OVERRIDE or PHYSICAL=62C241,NOEMS,OVERRIDE.

- INSTALL.EXE: A new utility to automate the installation process
	and to prepare a demonstration/evaluation diskette.

- CHIPSET.EXE: The approach to detection of chipset type has been
	completely reworked, motivated by needing to find a better
	way to handle PC "lock up".

- LICENSE, HIGHMEM, CHIPSET (and INSTALL): The user interface has
	been completely reworked to include color, menus, and
	pop-windows.  These programs automatically sense the presence
	of a color or monochrome display and adjust accordingly;
	however, you may force the mode by using one of the /MONO,
	/COLOR, or /LCD command line options.

- LASTBYTE.SYS: The information screen invoked by the "?" option now
	defaults to bright white on blue if a color display is
	active, and to the same inverse video if a monochrome monitor
	is active; added a "TEXT=n" command line option that allows
	this default to be changed to 'n', where n is the hexadecimal
	value of the attribute byte used to paint the screen.

- HIGHMEM.EXE: Now distinguishes "Mappable EMS Memory" from "EMS Page
	Frame" so that page frames no longer appear larger than 64k.

- HIGHMEM.EXE: Now displays contents of memory below 640k as well as
	contents of upper memory.

- TLBMM.EXE: A new utility that simply returns a non-zero error level
	if LASTBYTE.SYS is not installed.  (Useful in batch files to
	make decisions based on whether or not LASTBYTE is installed.)

- LASTBYTE.SYS: Identifies manufacturer and date of main Bios ROM.
	Automatically converts initialization portion to additional
	High-DOS memory (e.g., DOS=F000:32) if first half of rom is
	empty or a phantom duplicate of the second half.

- LASTBYTE.SYS and HIGHMEM.EXE: Now identifies Bios Rom of Disk
	controller as such.

- LASTBYTE.SYS: Use of the video text display buffer area for
	High-DOS memory is now protected against innapropriate video
	mode changes (INT 10h, AH=0).  For example, if the monochrome
	text region (B000-B7FF) is in use as High-DOS memory, then an
	attempt to switch to video mode 7 will be aborted; similarly,
	if the color text region (B800-BFFF) is in use, then an
	attempt to switch to video modes 0-6 will be aborted.

- HIGHTSR, HIGHINST, HIGHMARK, HIGHUNDO: Improved allocation of TSR
	markers so as to reduce memory fragmentation.

- All .EXE and .SYS files have been compressed to conserve user disk
	space and to speed loading of software into memory.

- LASTBYTE.SYS: Version 2.00 uses a very different internal structure
	that separates the low-level details of all the different
	memory controllers from the rest of LASTBYTE.SYS.  The new
	structure simplifies adding support for new chipsets without
	requiring changes to the rest of the software.

- HIGHSPLR: Added a new "NOTEST" option to disable the default test
	of the physical port that occurs when it first installs.

- LASTBYTE.SYS, CHIPSET.EXE: Added support for the Intel 82343,
	82346, and 82359, for the OPTi 82C283, 82C461, 82C493,
	82C496, and 82C682 chipsets, for the VLSI Technology
	VL82C320, VL82C330, and VL82C486, and for Compaq 32-bit BIM
	memory.

- HIGHDISK.SYS, HIGHEMS3.SYS, HIGHEMS4.SYS: These three device
	drivers copy large amounts of data from one part of memory to
	another.  If running on a 386 or 486 (or SX), these drivers
	will now automatically use the 32-bit version of REP MOVS for
	faster operation.

- All EXE files have been modified so that if the "?" option is used on
	the command line, then only the title line and "Usage:" will
	be printed; i.e., the "Line:" and "Error:" lines are supressed.