PRINTING NOTES:

          This file is an ASCII  text file of the Strip Chart  Library user
          manual.  It is about 45 pages long.

          Use a non-proportional font (example: Courier) and a font size of
          12 points for best printing results.

          If  you are  importing  this file  to a  word  processor such  as
          WordPerfect, set the word processor's top, bottom, left and right
          margins to zero.



















                                 STRIP CHART LIBRARY
                                    USER'S MANUAL


                                Shareware Version 1.00
                                      July, 1993






























                                 Copyright (c) 1993 
                                 Christopher Lim
                                 517 Cobb Court
                                 La Puente, California 91746









                                COPYRIGHT INFORMATION

          Copyright (c) 1993 by Christopher S. Lim.  All rights reserved.
          This is a shareware program.  Please refer to the READ.ME file
          for registration, licensing and distribution information.

          The author makes no warranty of any kind with regard to the
          program or documentation, including, but not limited to, the
          implied warranties of merchantability and fitness for a
          particular purpose.  The author shall not be liable in any event
          for incidental or consequential damages in connection with, or
          arising out of, the furnishing, performance, or use of the
          program.



          TRADEMARKS

          Borland is a registered trademark of Borland International.
          Epson LQ and Epson FX are registered trademarks of Seiko Epson
             Corporation.
          IBM is a registered trademark of International Business Machines.
          Microsoft is a registered trademark of Microsoft Corporation.











                                  TABLE OF CONTENTS
                                  =================


          Chapter 1  Getting Started . . . . . . . . . . . . . . . . . .  1

          Chapter 2  Using the Strip Chart Library . . . . . . . . . . .  3

          Chapter 3  Library Reference . . . . . . . . . . . . . . . . .  8

          Chapter 4  Error Messages. . . . . . . . . . . . . . . . . . . 42






            
            
            
                                  C H A P T E R   1
            
                                   Getting Started
            
            
            INTRODUCTION
            ============================================================
            
            *** NOTE: Please read the READ.ME file before doing anything
                 else.
            
            The Strip Chart Library is a C printer graphics library for
            plotting strip charts on inexpensive dot matrix printers.  A
            strip chart is a continuous two-dimensional graph which
            plots one or more traces (waveforms) versus time.  The Strip
            Chart Library contains functions that mimic and even exceed
            the most useful features of very costly strip chart
            recorders:
            
               - Traces can be sized and placed anywhere on the chart.
               - Traces may overlay or overlap other traces.
               - Text and comments can be positioned anywhere on the
                 chart.
               - Reference time axes can be positioned anywhere on the
                 chart.
               - Events (high-low signals), with different marker types,
                 are supported.
               - Waveform grid display, clipping and axis labeling are
                 supported.
               - The number of channels is limited only by amount of
                 memory.
               - Virtually any  "plotting speed" may be simulated when
                 playing back previously acquired data.


            SYSTEM REQUIREMENTS
            ============================================================
            
            Computer Hardware and Software
            ------------------------------
            The Strip Chart Library was designed and tested for IBM PC
            compatible computers running the DOS operating system.  A 25
            Mhz 80386 or faster PC is highly recommended.
            






                                          1






            Supported Compilers
            -------------------
            The libraries were compiled with the following compilers:
            
               SCBCS.LIB   Borland C/C++ Version 3.1 (Small Memory
                           Model)
            
               SCMSS.LIB   Microsoft C/C++ Version 7.0 (Small Memory
                           Model)

            If you use a different compiler or need a different memory
            model, you will have to recompile the library source code.
            Library source code is available to registered users.  Please
            refer to the READ.ME file for registration information.

            Supported Printers
            ------------------
            The Strip Chart Library supports the following tractor feed
            dot-matrix printers:
            
                 Epson FX (9-pin) or compatible dot matrix printers
                 Epson LQ (24-pin) or compatible dot matrix printers
            
            Both the narrow and wide carriage versions of the above
            printers are supported.  Color printers are currently not
            supported.  To improve performance, a large printer buffer
            is recommended.
            
            
            PRINTER SETUP
            ============================================================
            
            The printer must be set up as follows:
            
               Printer Mode:  EPSON COMPATIBLE
               Auto Line Feed:  OFF
               Paper Feed Type:  TRACTOR FEED 
               Paper-Out Sensor: ON
               Print Direction For Graphics (24 pin only):  UNIDIRECT
               Skip Over Perforation:  OFF
            
            NOTE:  Most of the above functions are normally set through
            the printer dip switch settings; consult your printer manual
            on how to do this.  You may need to experiment with the
            other dip switches and user-settable functions of the
            printer to get the best output.  Run the sample test
            programs to the check the quality of printer output.






                                          2







            
            
                                  C H A P T E R   2
            
                            Using the Strip Chart Library
            
            
            OVERVIEW
            ============================================================
            
            This section presents a brief summary of the functions
            available in the Strip Chart Library.  For more detailed
            information about these functions, consult Chapter 3,
            Library Reference.
            
            The Strip Chart Library uses an objected-oriented approach
            for creating and plotting strip charts:  you control the
            appearance of the strip chart by adding windows to the
            paper and display data by adding the desired data values to
            each window.  The library takes care of the details of
            plotting the data.
            
            Writing a program with the Strip Chart Library consists of
            five steps:  Planning the Strip Chart, Initializing the
            Strip Chart, Adding Windows to the Strip Chart, Adding Data
            to the Windows, Terminating the Strip Chart.  The following
            sections cover these steps in more detail.
            
            Include File
            ------------
            Only one include file, SC.H, is required for every C source
            file that calls a function from the Strip Chart Library.
            
            Error Handling
            --------------
            Error conditions in the Strip Chart Library are handled in
            two ways:  (1) through calling an error trap function
            defined by SC_SetErrorTrap, and (2) through returning a non-
            zero error code (a zero value indicates no error) by most
            functions in the Strip Chart Library.  Using SC_SetErrorTrap
            is the easier and preferred method; however, the error
            return code is useful for pinpointing which portion of your
            code committed the error.  The nature of the error can be
            examined by calling function SC_ErrorMsg.  If an error
            condition occurs, it is strongly suggested that you
            immediately terminate or reinitialize the Strip Chart
            Library as unpredictable results could occur if you continue
            with the program.
            
            
            

                                          3







            PLANNING THE STRIP CHART
            ============================================================
            
            Windows and Page Layout
            -----------------------
            Carefully plan the layout of the strip chart.  Divide the
            strip chart into windows.  A window is a rectangular area on
            the strip chart of fixed height and potentially infinite
            length.  There are five types of windows:
            
                 "Event Windows" accept and display event (two-state or
                 high-low) signal levels.
            
                 "Text Windows" accept and display messages.
            
                 "Time Windows" display reference time axes.
            
                 "Title Windows" accept and display a fixed string at
                 specified intervals.
            
                 "Trace Windows" accept and plot waveforms.
            
            Units of Measure
            ----------------
            Decide whether you want to use either English units (in
            inches) or Metric units (in centimeters) to describe plot
            length dimensions such as character height, window height
            and window offset.  You specify the type of unit to use in
            function SC_Init.
            
            Decide on the basic time unit you will use.  For most cases,
            you will probably be using seconds as the basic time unit. 
            However you may choose any other measurement of time such as
            minutes, hours, or even weeks or months.   To keep
            terminology simple in this manual, we will assume that you
            will be using seconds as the basic time unit.
             
            Trace data are specified in real world coordinates (for
            example, in volts).  When you create a Trace Window, you
            specify the maximum and minimum amplitudes in real world
            coordinates that correspond to the top and bottom of the Trace
            Window.  See the descriptions for function SC_AddTraceWindow
            and SC_Trace in Chapter 3 for more information.

            Plot Speed
            ----------
            Plot speed does not refer to the actual speed of paper or
            chart movement but to the relationship of the chart's
            horizontal dimension to the basic time unit.  For example,
            if you select a plot speed of 2 inches per second, two
            inches measured along the horizontal (long side) of the

                                          4






            chart is equivalent to 1 second of time.  You specify the
            plot speed in function SC_Init.
            
            
            INITIALIZING THE STRIP CHART LIBRARY
            ============================================================
            
            Here is a summary of the functions used to initialize the
            Strip Chart Library:
            
               SC_Init             Initializes the Strip Chart Library
                                   and the printer.  Except for
                                   functions SC_SetErrorTrap and
                                   SC_PrinterReady, SC_Init must be
                                   called prior to any other function in
                                   the Strip Chart Library.
            
               SC_SetErrorTrap     Specifies a function to trap errors.
            
               SC_PrinterReady     Checks if the printer is on-line and
                                   ready to receive data.
            
            
            ADDING WINDOWS TO THE STRIP CHART
            ============================================================
            
            After initialization, the next step is to add windows to the
            strip chart.  Adding windows consists of calling a
            SC_Add???Window function with the window position (yoffset),
            window height (yheight), and other window-specific control
            flags as arguments.  Windows may be positioned anywhere
            within the physical dimension of the paper; it is
            permissible to have overlapping windows.  The number of
            windows that may be added is limited only by available
            memory on your computer.  The SC_Add???Window function, on
            success, returns a pointer (SC_WINDOW *) that is used to
            identify the window in subsequent operations.  Below is the
            summary of the functions to add windows:
            
               SC_AddEventWindow   Adds an Event Window to the strip
                                   chart.
               
               SC_AddTextWindow    Adds a Text Window to the strip
                                   chart.  The height of the window
                                   determines the character height.
               
               SC_AddTimeWindow    Adds a Time Window to the strip
                                   chart.  Time Windows consist of two
                                   subwindows of equal height:  one
                                   subwindow contains the horizontal
                                   axis and time tick marks, and a
                                   second subwindow to display text

                                          5






                                   labels.
            
               SC_AddTitleWindow   Adds a Title Window to the strip
                                   chart.  Character height is equal to
                                   the window height.
            
               SC_AddTraceWindow   Adds a Trace Window to the strip
                                   chart.
            
            
            Controlling the Appearance of Trace Windows
            -------------------------------------------
            The following functions control the appearance of Trace
            Windows:
            
               SC_SetHorizontalGrids Controls the number of horizontal
                                     grids in Trace Windows.
                 
               SC_SetTimeGrids       Controls the frequency of timing
                                     grids in Trace Windows.
            
               SC_SetYlabels         Controls the appearance of vertical
                                     axis labels in Trace Windows.
            
            The above functions only affect Trace Windows added later. 
            Trace Windows that were created before calling any of the
            above functions are not affected.
            
            
            ADDING DATA TO STRIP CHART WINDOWS
            ============================================================
            
            After the Strip Chart Library has been initialized and
            windows added to the strip chart, data can now be displayed
            in the windows.  The following functions are used to add and
            display data in the windows:
            
               SC_Event       Sets the event level (0 or 1) in an Event
                              Window.
            
               SC_Text        Adds a character string to a Text Window.
            
               SC_Title       Sets the title message in a Title Window.
            
               SC_Trace       Sets the trace amplitude in a Trace
                              Window.
            
               SC_Draw        Plots the contents of all windows up to
                              the current time position to an internal
                              printer buffer.  SC_Draw should only be
                              called after all windows are updated to
                              the current time position.

                                          6






            
               SC_Advance     Advances the paper to the next time
                              position.
            
            Functions SC_Event, SC_Text, SC_Title and SC_Trace add data
            to their respective windows at the current time position. 
            Calling SC_Draw is a signal to the Strip Chart Library that
            you have finished adding data to all windows for the current
            time position and the Library will proceed to plot the data. 
            The SC_Advance function moves the chart to the next time
            position after which the Library is ready to accept more
            data.   It must be stressed that SC_Draw must be called
            after data are added all windows and before calling
            SC_Advance to advance the paper.
            
            There are special cases where multiple calls to SC_Draw are
            required before calling SC_Advance.  One example involves
            Trace Windows displaying step functions or square waves; see
            the example in file EX_STEP.C.
             
            
            TERMINATING THE STRIP CHART
            ============================================================
            
            To terminate the strip chart, call function SC_Close:
            
               SC_Close    Closes the Strip Chart Library.  All windows
                           are closed, the contents of internal buffers
                           are flushed, and memory allocated by the
                           Strip Chart Library are released.
            
              





















                                          7







            
            
                                  C H A P T E R   3
            
                                  Library Reference
            
            
            
            SC_AddEventWindow
            ============================================================
            
               Adds an Event Window to the strip chart.
            
            SYNTAX
            
               #include "sc.h"
               SC_WINDOW *SC_AddEventWindow(double yoffset, 
                 double yheight, int markerType, int fillType, 
                 int *error);
            
            RETURN VALUE
            
               On success, SC_AddEventWindow returns a pointer to the
               window.  In the event of an error, it returns NULL.
            
            REMARKS
            
                 yoffset [in] is the distance (in inches or centimeters)
                 from the top of the strip chart to the top of the Event
                 Window.  yoffset must be greater than zero.
            
                 yheight [in] is the window height in inches or
                 centimeters.
            
                 markerType [in] is the type of event marker.  An event
                 marker is used to display the state or level of a
                 binary (two-state or high-low) signal.  Four types of
                 event markers are available:               
            
                 SCM_PULSE--Event levels are displayed by high-low
                    pulses.
            
                 SCM_TICK--Event level changes are displayed by
                    vertical tick marks.
            
                 SCM_BAR--The high level is represented by bars.
            
                 SCM_BARLINE--Same as SCM_BAR except with a baseline
                    added.
            
                 fillType [in] specifies the fill type for SCM_BAR or

                                          8






                 SCM_BARLINE event markers.  Three fill types are
                 available:
                 
                    NO_FILL--Bars are not shaded.
                    HALF_FILL--Bars are lightly shaded with dots.
                    SOLID_FILL--Bars are fully shaded.
            
                 error [out] is a pointer to an error code.  A non-zero
                 error code indicates an error condition.
            
            SEE ALSO
            
               SC_Event, SC_yoffset
            
            EXAMPLE
            
            #include <stdio.h>
            #include <stdlib.h>
            #include "sc.h"
            
            int main(void)
            {
               int i;
               int error;
               SC_WINDOW *eventWindow;
            
               /* Initialize: 8.5 inch wide paper, plot speed = 1
                inch/second */
               SC_Init(LPT1, SC_24PIN, SC_LOW_RES, INCHES, 8.5, 1.0,
                &error);
            
               /* Add Event Window 0.5" from top of paper, 0.25 inch
                window height, use pulse event markers
               */
               eventWindow = SC_AddEventWindow(0.5, 0.25, SCM_PULSE,
                NO_FILL, &error);
            
               /* Draw events */
               for (i=0; i < 10; i++) /* 10 second plot */
               {
                  if ((i%2) == 0)
                     SC_Event(eventWindow, 0, &error); /* set event low
                                                        */
                  else
                     SC_Event(eventWindow, 1, &error); /* set event high
                                                        */
            
                  SC_Draw();
                  SC_Advance(1.0); /* one second steps */
               }
            
               SC_Close();

                                          9






               return 0;
            }
            
            
            
            SC_AddTextWindow
            ============================================================
            
               Adds a Text Window to the strip chart.
            
            SYNTAX
            
               #include "sc.h"
               SC_WINDOW *SC_AddTextWindow(double yoffset, 
                 double yheight, int *error);
            
            RETURN VALUE
            
               On success, SC_AddTextWindow returns a pointer to the
               window.  In the event of an error, it returns NULL.
            
            REMARKS
            
                 yoffset [in] is the distance (in inches or centimeters)
                 from the top of the strip chart to the top of the Text
                 Window.  yoffset must be greater than zero.
            
                 yheight [in] is the window height in inches or
                 centimeters.  The character height is equal to the
                 window height.
            
                 error [out] is a pointer to an error code.  A non-zero
                 error code indicates an error condition.
            
            SEE ALSO
            
               SC_Text, SC_yoffset
            
            EXAMPLE
            
            #include <stdio.h>
            #include <stdlib.h>
            #include "sc.h"
            
            int main(void)
            {
               int i;
               int error;
               SC_WINDOW *textWindow;
            



                                          10






               /* Initialize: 8.5 inch wide paper, plot speed = 1
                inch/second */
               SC_Init(LPT1, SC_24PIN, SC_LOW_RES, INCHES, 8.5, 1.0,
                &error);
            
               if (error)
               {
                  printf("%s\n",SC_ErrorMsg(error));
                  return 1; /* exit */
               }
            
               /* Add Text Window 1.5" from top of paper, 
                0.25" window height
               */
               textWindow = SC_AddTextWindow(1.5, 0.25, &error);
            
               /* Draw */
               for (i=0; i < 10; i++) /* 10 second plot */
               {
                  /* Display "hello world" every 2 seconds */
                  if ((i%2) == 0)
                     SC_Text(textWindow,"Hello World!",&error);
                  SC_Draw();
                  SC_Advance(1.0); /* one second steps */
               }
            
               SC_Close();
               return 0;
            }
            
            
            
            SC_AddTimeWindow
            ============================================================
            
               Adds a Time Window to the strip chart.
            
            SYNTAX
            
               #include "sc.h"
               SC_WINDOW *SC_AddTimeWindow(double yoffset, 
                 double yheight, int type,
                 double tickInterval, int minorDiv,
                 char * (*userFunc)(SC_WINDOW *timeWindow, 
                     double elapsedTime, unsigned long labelCount),
                 int *error);
            
            RETURN VALUE
            
               On success, SC_AddTimeWindow returns a pointer to the
               window.  In the event of an error, it returns null.
            

                                          11






            REMARKS
            
                 yoffset [in] is the distance (in inches or centimeters)
                 from the top of the strip chart to the top of the Time
                 Window.  yoffset must be greater than zero.
            
                 yheight [in] is the window height in inches or
                 centimeters.  The character height of the labels is
                 approximately one-half  the window height.  The height
                 of the major tick marks is approximately one-half the
                 window height.
            
                 type [in] specifies the type of the time window.  There
                 are two types of time windows:
            
                    LABELS_BELOW_AXIS--Time labels are placed below the
                    time axis.  Time tick marks are pointing upward. 
            
                    LABELS_ABOVE_AXIS--Time labels are placed above the
                    time axis.  Time tick marks are pointing downward.
            
                 tickInterval [in] specifies the time interval (in
                 seconds) between major tick marks.
            
                 minorDiv [in] specifies the number of minor divisions
                 between major tick marks.
            
                 userFunc [in] is a user-defined function to create the
                 string label to be placed at the major tick marks. 
                 userFunc returns a pointer to the label string.  At
                 every major tick interval, userFunc is called by the
                 library and passed the following arguments:
               
                    timeWindow--This is a pointer to the Time Window
                    where the label will be placed.  If you have more
                    than one Time Window in your strip chart, you can
                    specify the same userFunc for each Time Window and
                    check the timeWindow argument to tell which Time
                    Window is about to be labeled.
            
                    elapsedTime--This is the elapsed time (in seconds)
                    from the start of the plot.  The first major tick
                    mark always occurs at the very beginning of the plot
                    where userFunc is called with elapsedTime set to
                    0.0.
            
                    labelCount--This is the number of labels that has
                    been printed for this Time Window.  The first major
                    tick mark always occurs at the very beginning of the
                    plot where userFunc is called with labelCount set to
                    0.  The relationship between labelCount and
                    elapsedTime is:

                                          12






            
                      elapsedTime = labelCount * tickInterval.
            
                 error [out] is a pointer to an error code.  A non-zero
                 error code indicates an error condition.
            
            EXAMPLE
            
            #include <stdio.h>
            #include <stdlib.h>
            #include "sc.h"
            
            char *LabelFunc(SC_WINDOW *w, double elapsedTime, unsigned
                long labelCount)
            { /* user function to handle time axis labels */
               static char buf[80]; /* string buffer must be declared as
                                       static */
               sprintf(buf,"%05.2f",elapsedTime); /* elapsedTime is in
                                                     seconds */
               return buf;
            }
            
            int main(void)
            {
               int i;
               int error;
               SC_WINDOW *timeWindow;
            
               /* Initialize: 8.5 inch wide paper, 
                plot speed = 1 inch/second */
               SC_Init(LPT1, SC_24PIN, SC_LOW_RES, INCHES, 8.5, 1.0,
                &error);
            
               /* Add Time Window 1.0" from top of paper, 
                0.25" window height,
                  labels above time axis, label every 2 seconds, 
                5 divisions between labels.
               */
               timeWindow = SC_AddTimeWindow(1.0, 0.25,
                LABELS_ABOVE_AXIS, 2.0, 5, LabelFunc, &error);
            
               /* Draw */
               for (i=0; i < 10; i++) /* 10 second plot */
               {
                  SC_Draw();
                  SC_Advance(1.0); /* one second steps */
               }
            
               SC_Close();
               return 0;
            }
            

                                          13






            
            
            SC_AddTitleWindow
            ============================================================
            
               Adds a Title Window to the strip chart.
            
            SYNTAX
            
               #include "sc.h"
               SC_WINDOW *SC_AddTitleWindow(double yoffset, 
                 double yheight, double interval, int *error);
            
            RETURN VALUE
            
               On success, SC_AddTitleWindow returns a pointer to the
               window.  In the event of an error, it returns null.
            
            REMARKS
            
                 yoffset [in] is the distance (in inches or centimeters)
                 from the top of the strip chart to the top of the Title
                 Window.  yoffset must be greater than zero.
            
                 yheight [in] is the window height in inches or
                 centimeters.  The character height is equal to the
                 window height.
            
                 interval [in] is the time interval (in seconds) for
                 displaying the title string.
            
                 error [out] is a pointer to an error code.  A non-zero
                 error code indicates an error condition.
            
            SEE ALSO
            
               SC_Title, SC_yoffset
            
            EXAMPLE
            
            #include <stdio.h>
            #include <stdlib.h>
            #include "sc.h"
            
            int main(void)
            {
               int i;
               int error;
               SC_WINDOW *titleWindow;
            



                                          14






               /* Initialize: 8.5 inch wide paper, 
                plot speed = 1 inch/second */
               SC_Init(LPT1, SC_24PIN, SC_LOW_RES, INCHES, 8.5, 1.0,
                 &error);
            
               /* Add Title Window 5.5" from top of paper, 
                  0.25" window height,
                  display every 2.0 seconds
               */
               titleWindow = SC_AddTitleWindow(5.5, 0.25, 2.0, &error);
            
               /* Set title string. */
               SC_Title(titleWindow, "Hello World!", &error);
            
               /* Draw */
               for (i=0; i < 10; i++) /* 10 second plot */
               {
                  SC_Draw();
                  SC_Advance(1.0); /* one second steps */
               }
            
               SC_Close();
               return 0;
            }
            
            
            
            SC_AddTraceWindow
            ============================================================
            
               Adds a Trace Window to the strip chart.
            
            SYNTAX
            
               #include "sc.h"
               SC_WINDOW *SC_AddTraceWindow(double yoffset,
                 double yheight, double ymin, double ymax, 
                 unsigned int flags, int *error);
            
            RETURN VALUE
            
               On success, SC_AddTraceWindow returns a pointer to the
               window.  In the event of an error, it returns null.
            
            REMARKS
            
                 yoffset [in] is the distance (in inches or centimeters)
                 from the top of the strip chart to the top of the Trace
                 Window.  yoffset must be greater than zero.
            
                 yheight [in] is the window height in inches or
                 centimeters.

                                          15






            
                 ymin [in] is the real world Y coordinate corresponding
                 to the bottom border of the Trace Window.
            
                 ymax [in] is the real world Y coordinate corresponding
                 to the top border of the Trace Window.  The values of
                 ymin and ymax may be changed dynamically at any time by
                 calling the SC_SetTraceRange function.
            
                 flags [in]  are flags that control the appearance of
                 the trace window.  Flags may be combined with the use
                 of the C bitwise OR ("|") operator.
            
                    SCF_NOFLAGS--Disables all flags.
            
                    SCF_BORDER--Adds a border around the window.
               
                    SCF_GRID--Adds horizontal and vertical grids. 
                    Vertical (time) grid spacing are set through the
                    SC_SetTimeGrids function.  Horizontal grid spacing
                    are set through the SC_SetHorizontalGrids function. 
                    The SC_SetTimeGrids and SC_SetHorizontalGrids
                    functions must be called before calling
                    SC_AddTraceWindow.
            
                    SCF_YLABEL--Adds labels to the Y axis.  The format
                    of the labels can be specified through the
                    SC_SetYlabels function.  SC_SetYlabels must be
                    called prior to calling SC_AddTraceWindow.
            
                    SCF_CLIP--Segments outside the window are clipped.
                    If a segment is clipped, a thick solid line is drawn
                    at the top or bottom border where clipping occurs.
            
                 error [out] is a pointer to an error code.  A non-zero
                 error code indicates an error condition.
            
            SEE ALSO
            
               SC_SetHorizontalGrids, SC_SetTimeGrids, SC_SetTraceRange,
               SC_SetYlabels, SC_Trace, SC_yoffset
            











                                          16






            EXAMPLE
            
            #include <stdio.h>
            #include <stdlib.h>
            #include "sc.h"
            
            int main(void)
            {
               int i;
               int error;
               double y;
               SC_WINDOW *traceWindow;
            
               /* Initialize: 8.5 inch wide paper, 
                plot speed = 1 inch/second */
               SC_Init(LPT1, SC_24PIN, SC_LOW_RES, INCHES, 8.5, 1.0,
                &error);
            
               /* Set timing (vertical) grids to be 1 second apart. */
               SC_SetTimeGrids(1.0, &error);
            
               /* Set Y label format; display at 2.0 second intervals.
                */
               SC_SetYlabels(10.0/72.0, "%+0.1f", 2.0, &error);
            
               /* Divide trace into 4 equal sections. */
               SC_SetHorizontalGrids(4, &error);
            
               /* Add Trace Window 2.5" from top of paper, 
                1.0" window height,
                amplitude range from -1.0 to 1.0, display borders,
                display grids, label Y axis.
               */
               traceWindow = SC_AddTraceWindow(2.5, 1.0,
                -2.0, 2.0, SCF_BORDER | SCF_GRID | SCF_YLABEL,
                &error);
            
               /* Draw a triangle wave of amplitude 2.0 */
               y = 2.0;
               for (i=0; i < 10; i++) /* 10 second plot */
               {
                  SC_Trace(traceWindow, y, &error);
                  y = y * -1.0;
                  SC_Draw();
                  SC_Advance(1.0); /* one second steps */
               }
            
               SC_Close();
               return 0;
            }
            
            

                                          17






            
            SC_Advance
            ============================================================
            
               Advances the paper.
            
            SYNTAX
            
               #include "sc.h"
               void SC_Advance(double interval);
            
            REMARKS
            
               interval [in] is the time interval (in seconds) to
               advance the paper.  Function SC_Draw should normally be
               called before calling SC_Advance.
            
            SEE ALSO
            
               SC_Draw
            
            EXAMPLE
            
            #include <stdio.h>
            #include <stdlib.h>
            #include "sc.h"
            
            int main(void)
            {
               int i;
               int error;
               double y;
               SC_WINDOW *traceWindow;
            
               /* Initialize: 8.5 inch wide paper, 
                  plot speed = 1 inch/second */
               SC_Init(LPT1, SC_24PIN, SC_LOW_RES, INCHES, 8.5, 1.0,
                &error);
            
               /* Add Trace Window 2.5" from top of paper, 
                  1.0" window height,
                  amplitude range from -1.0 to 1.0, display borders.
               */
               traceWindow = SC_AddTraceWindow(2.5, 1.0,
                  -2.0, 2.0, SCF_BORDER, &error);
            







                                          18






               /* Draw a triangle wave of amplitude 2.0 */
               y = 2.0;
               for (i=0; i < 10; i++) /* 10 second plot */
               {
                  SC_Trace(traceWindow, y, &error);
                  y = y * -1.0;
                  SC_Draw(); /* display y */
                  SC_Advance(1.0); /* advance to next position, 
                one second steps */
               }
            
               SC_Close();
               return 0;
            }
            
            
            
            SC_Close
            ============================================================
            
               Closes the Strip Chart Library.
            
            SYNTAX
            
               #include "sc.h"
               void SC_Close(void);
            
            REMARKS
            
               SC_Close signals the end of the strip chart.  The
               contents of internal buffers are flushed, and memory
               allocated by the Strip Chart Library are released.
            
            SEE ALSO
            
               SC_Init
            
            EXAMPLE
            
            #include <stdio.h>
            #include <stdlib.h>
            #include "sc.h"
            
            int main(void)
            {
               int error;
            
               /* Initialize: 8.5 inch wide paper, 
                  plot speed = 1 inch/second */
               SC_Init(LPT1, SC_24PIN, SC_LOW_RES, INCHES, 8.5, 1.0,
                &error);
            

                                          19






               /*
                     Program body
                        :
                        :
            
               */
            
               SC_Close(); /* close the Strip Chart Library */
               return 0;
            }
            
            
            
            SC_Draw
            ============================================================
            
               Plots the contents of all windows up to the current time 
               position.
            
            SYNTAX
            
               #include "sc.h"
               void SC_Draw(void);
            
            REMARKS
            
               SC_Draw plots the contents of all windows up to the
               current time position to an internal printer buffer. 
               Actual printing is done only after this printer buffer is
               filled.  SC_Draw is normally called immediately before
               the SC_Advance function to flush the window contents
               before advancing the paper. 
            
            SEE ALSO
            
               SC_Advance
            
            EXAMPLE
            
            #include <stdio.h>
            #include <stdlib.h>
            #include "sc.h"
            
            int main(void)
            {
               int i;
               int error;
               double y;
               SC_WINDOW *traceWindow;
            



                                          20






               /* Initialize: 8.5 inch wide paper, 
                  plot speed = 1 inch/second */
               SC_Init(LPT1, SC_24PIN, SC_LOW_RES, INCHES, 8.5, 1.0,
                &error);
            
               /* Add Trace Window 2.5" from top of paper, 
                  1.0" window height,
                  amplitude range from -1.0 to 1.0, display borders.
               */
               traceWindow = SC_AddTraceWindow(2.5, 1.0,
                  -2.0, 2.0, SCF_BORDER, &error);
            
               /* Draw a triangle wave of amplitude 2.0 */
               y = 2.0;
               for (i=0; i < 10; i++) /* 10 second plot */
               {
                  SC_Trace(traceWindow, y, &error);
                  y = y * -1.0;
                  SC_Draw();
                  SC_Advance(1.0); /* one second steps */
               }
            
               SC_Close();
               return 0;
            }
            
            
            
            SC_ErrorMsg
            ============================================================
            
               Returns an error message string.
            
            SYNTAX
            
               #include "sc.h"
               char *SC_ErrorMsg(int error);
            
            RETURN VALUE
            
               Pointer to an error message string.
            
            REMARKS
            
                 error [in] is an error code number.  A non-zero value
                 indicates an error occurred within the Strip Chart
                 Library.  It is recommended that your program terminate
                 or reinitializes itself if an error is detected;
                 unpredictable results could occur if you continue with
                 the program.
            


                                          21






            SEE ALSO
            
               SC_SetErrorTrap
            
            EXAMPLE
            
            #include <stdio.h>
            #include <stdlib.h>
            #include "sc.h"
            
            int main(void)
            {
               int error;
            
               /* Initialize: 8.5 inch wide paper, 
                  plot speed = 1 inch/second */
               SC_Init(LPT1, SC_24PIN, SC_LOW_RES, INCHES, 8.5, 1.0,
                &error);
            
               if (error)
               {
                   printf("%s\n", SC_ErrorMsg(error))
                   return 1; /* abort program */
                }
              
               /*
                     Program body
                        :
                        :
               */
            
               SC_Close();
               return 0;
            }
            
            
            
















                                          22






            SC_Event
            ============================================================
            
               Sets the event level in an Event Window.
            
            SYNTAX
            
               #include "sc.h"
               void SC_Event(SC_WINDOW *eventWindow, int eventlevel, 
                 int *error);
            
            REMARKS
            
                 eventWindow [in] is a pointer to the Event Window.
            
                 eventLevel [in] is the new level (0 = low, 1 = high) to
                 display.
            
                 error [out] is a pointer to an error code.  A non-zero
                 error code indicates an error condition.
            
               Gaps may appear in the plot if SC_Event is called twice
               for the same Event Window without an intervening call to
               SC_Draw.
            
            SEE ALSO
            
               SC_AddEventWindow
            
            EXAMPLE
            
            #include <stdio.h>
            #include <stdlib.h>
            #include "sc.h"
            
            int main(void)
            {
               int i;
               int error;
               SC_WINDOW *eventWindow;
            
               /* Initialize: 8.5 inch wide paper,
                   plot speed = 1 inch/second */
               SC_Init(LPT1, SC_24PIN, SC_LOW_RES, INCHES, 8.5, 1.0,
                &error);
            
               /* Add Event Window 0.5 from top of paper,
                  0.25 inch window height, 
               use pulse event markers
               */
               eventWindow = SC_AddEventWindow(0.5, 0.25, SCM_PULSE,
                NO_FILL, &error);

                                          23






            
               /* Draw events */
               for (i=0; i < 10; i++) /* 10 second plot */
               {
                  if ((i%2) == 0)
                     SC_Event(eventWindow, 0, &error); /* set event low
                */
                */
                  else
                     SC_Event(eventWindow, 1, &error); /* set event high
                */
                */
            
                  SC_Draw();
                  SC_Advance(1.0); /* one second steps */
               }
            
               SC_Close();
               return 0;
            }
            
            
            
            SC_Init
            ============================================================
            
               Initializes the Strip Chart Library.
            
            SYNTAX
            
               #include "sc.h"
               void SC_Init(int port, unsigned char printerType,
                 unsigned char plotResolution, double units, 
                 double paperWidth, double plotSpeed, int *error);
            
            REMARKS
            
                 port [in] specifies the parallel port to which the
                 printer is attached, and is one of the following:
            
                 LPT1--parallel port 1.
                 LPT2--parallel port 2.
                 LPT3--parallel port 3.
            
                 printerType [in] specifies the type of printer.  The
                 following printer types are currently recognized:
            
                    EPS_9PIN -- Specifies Epson compatible 9-pin dot
                    matrix printers.
            
                    EPS_24PIN -- Specifies Epson compatible 24-pin dot
                    matrix printers.

                                          24






            
                 plotResolution [in] specifes the printer graphics mode
                 to be used and is one of the following:
            
                    LOW_RES -- Low resolution plots:
                    For 9 pin printers: 72 dpi  (horizontally) by 60 dpi
                    (vertically). For 24 pin printers: 180 dpi
                    (horizontally) by 180 dpi (vertically). 
            
                    HIGH_RES -- High resolution plots:
                    For 9 pin printers: 72 dpi (horizontally) by 240 dpi
                    (vertically).  For 24 pin printers: 180 dpi
                    (horizontally) by 360 dpi (vertically).
            
                 units [in] specifies the units of length measurement to
                 be used and is one of the following:
            
                    INCHES--Use inches as the unit of measurement.
                    CENTIMETERS--Use centimeters as the unit of
                    measurement.
               
                 paperWidth [in] specifies the paper width in inches or
                 centimeters.
            
                 plotSpeed [in] specifies the "plotting speed" in inches
                 (or centimeters) per second.  This parameter specifies
                 the relationship between the plotter horizontal
                 dimension (in inches or centimeters) and time (in
                 seconds).
            
               error [out] is a pointer to an error code.  A non-zero
               error code indicates an error condition.
            
            SEE ALSO
            
               SC_Close
            
            EXAMPLE
            
            #include <stdio.h>
            #include <stdlib.h>
            #include "sc.h"
            
            int main(void)
            {
               int error;
            
               /* Initialize: 8.5 inch wide paper, 
               plot speed = 1 inch/second */
               SC_Init(LPT1, SC_24PIN, SC_LOW_RES, INCHES, 8.5, 1.0,
                &error);
            

                                          25






               /*
                     Program body
                        :
                        :
            
               */
            
               SC_Close();
               return 0;
            }
            
            
            
            SC_PrintChar
            ============================================================
            
               Low level function to send a character to the printer.
            
            SYNTAX
            
               #include "sc.h"
               void SC_PrintChar(char c);
            
            REMARKS
            
                 c [in] is the character or command code to send to the
                 printer attached to the parallel port specified with
                 the SC_Init function.  SC_Init must be called  before
                 using SC_PrintChar.
            
               SC_PrintChar is a low level function; do not use this
               function unless you are absolutely sure you know what you
               are doing!
            
            
            
            SC_PrinterReady
            ============================================================
            
               Checks if the printer is ready to accept data.
            
            SYNTAX
            
               #include "sc.h"
               int SC_PrinterReady(int port);
            
            RETURN VALUE
            
               SC_PrinterReady returns 1 if the printer is ready to
               receive data.  It returns zero if the printer is not
               ready.
            

                                          26






            REMARKS
            
                 port [in] specifies the parallel port to which the
                 printer is attached, and is one of the following:
            
                 LPT1--parallel port 1.
                 LPT2--parallel port 2.
                 LPT3--parallel port 3.
            
            EXAMPLE
            
            #include <stdio.h>
            #include <stdlib.h>
            #include "sc.h"
            int main(void)
            {
               int error;
            
               /* Check if printer ready */
               if (!SC_PrinterReady(LPT1))
               {
                  printf("Printer not ready!\n");
                  return 1; /* exit program */
               }
            
               /* Initialize: 8.5 inch wide paper, 
                plot speed = 1 inch/second */
               SC_Init(LPT1, SC_24PIN, SC_LOW_RES, INCHES, 8.5, 1.0,
                &error);
            
               /*
                     Program body
            
                        :
                        :
            
               */
            
               SC_Close();
               return 0;
            }
            
            
            









                                          27






            SC_SetErrorTrap
            ============================================================
            
               Sets up a function to process errors..
            
            SYNTAX
            
               #include "sc.h"
               void SC_SetErrorTrap(void (*func)(char *msg));
            
            REMARKS
            
                 func [in] is a pointer to a function that is called
                 when an error occurs in the Strip Chart Library.  func
                 is passed a pointer to an error message string.  It is
                 recommended that your program terminate or
                 reinitializes itself if an error is detected;
                 unpredictable results could occur if you continue with
                 the program.
            
            SEE ALSO
            
               SC_ErrorMsg
            
            EXAMPLE
            
            #include <stdio.h>
            #include <stdlib.h>
            #include "sc.h"
            
            void ErrorTrapFunc(char *msg)
            { /* user function to trap errors */
               printf("%s\n",msg); /* display error message */
               exit(1); /* abort program and exit */
            }
            
            int main(void)
            {
               int error;
            
               SC_SetErrorTrap(ErrorTrapFunc);
            
               /* Initialize: 8.5 inch wide paper, 
                  plot speed = 1 inch/second */
               SC_Init(LPT1, SC_24PIN, SC_LOW_RES, INCHES, 8.5, 1.0,
                &error);
            






                                          28






               /*
                     Program body
                        :
                        :
            
               */
            
               SC_Close();
               return 0;
            }
            
            
            
            SC_SetHorizontalGrids
            ============================================================
            
               Specifies the number of horizontal grid lines in Trace
               Windows.  This function only affects Trace Windows added
               after calling this function.
            
            SYNTAX
            
               #include "sc.h"
               void SC_SetHorizontalGrids(int divisions, int *error);
            
            REMARKS
            
                 divisions [in] is the number of horizontal divisions. 
                 The number of horizontal grid lines drawn is equal to
                 divisions minus 1.
            
                 error [out] is a pointer to an error code.  A non-zero
                 error code indicates an error condition.
            
            SEE ALSO
            
               SC_AddTraceWindow
            
            EXAMPLE
            
            #include <stdio.h>
            #include <stdlib.h>
            #include "sc.h"
            
            int main(void)
            {
               int i;
               int error;
               double y;
               SC_WINDOW *traceWindow;
            


                                          29






               /* Initialize: 8.5 inch wide paper, 
                  plot speed = 1 inch/second */
               SC_Init(LPT1, SC_24PIN, SC_LOW_RES, INCHES, 8.5, 1.0,
                &error);
            
               /* Set timing (vertical) grids to be 1 second apart. */
               SC_SetTimeGrids(1.0, &error);
            
               /* Set Y label format; display at 2.0 second intervals.
               */
               SC_SetYlabels(10.0/72.0, "%+0.1f", 2.0, &error);
            
               /* Divide trace into 4 equal sections. */
               SC_SetHorizontalGrids(4, &error);
            
               /* Add Trace Window 2.5" from top of paper, 1.0" window
                  height, amplitude range from -1.0 to 1.0, display
                  borders, display grids, label Y axis.
               */
               traceWindow = SC_AddTraceWindow(2.5, 1.0,
                  -2.0, 2.0, SCF_BORDER | SCF_GRID | SCF_YLABEL,
                  &error);
            
               /* Draw a triangle wave of amplitude 2.0 */
               y = 2.0;
               for (i=0; i < 10; i++) /* 10 second plot */
               {
                  SC_Trace(traceWindow, y, &error);
                  y = y * -1.0;
                  SC_Draw();
                  SC_Advance(1.0); /* one second steps */
               }
            
               SC_Close();
               return 0;
            }
            
            
            














                                          30






            SC_SetTimeGrids
            ============================================================
            
               Specifies the time interval between vertical grid lines
               in Trace Windows.  This function only affects Trace
               Windows added after calling this function.
            
            SYNTAX
            
               #include "sc.h"
               void SC_SetTimeGrids(double interval, int *error);
            
            REMARKS
            
                 interval [in] is the time interval (in seconds) between
                 vertical grid lines.
            
                 error [out] is a pointer to an error code.  A non-zero
                 error code indicates an error condition.
            
            SEE ALSO
            
               SC_AddTraceWindow
            
            EXAMPLE
            
            #include <stdio.h>
            #include <stdlib.h>
            #include "sc.h"
            
            int main(void)
            {
               int i;
               int error;
               double y;
               SC_WINDOW *traceWindow;
            
               /* Initialize: 8.5 inch wide paper, 
                  plot speed = 1 inch/second */
               SC_Init(LPT1, SC_24PIN, SC_LOW_RES, INCHES, 8.5, 1.0,
                &error);
            
               /* Set timing (vertical) grids to be 1 second apart. */
               SC_SetTimeGrids(1.0, &error);
            
               /* Set Y label format; display at 2.0 second intervals.
                */
               SC_SetYlabels(10.0/72.0, "%+0.1f", 2.0, &error);
            
               /* Divide trace into 4 equal sections. */
               SC_SetHorizontalGrids(4, &error);
            

                                          31






               /* Add Trace Window 2.5" from top of paper, 1.0" window
                  height, amplitude range from -1.0 to 1.0, display
                  borders, display grids, label Y axis.
               */
               traceWindow = SC_AddTraceWindow(2.5, 1.0,
                  -2.0, 2.0, SCF_BORDER | SCF_GRID | SCF_YLABEL,
                  &error);
            
               /* Draw a triangle wave of amplitude 2.0 */
               y = 2.0;
               for (i=0; i < 10; i++) /* 10 second plot */
               {
                  SC_Trace(traceWindow, y, &error);
                  y = y * -1.0;
                  SC_Draw();
                  SC_Advance(1.0); /* one second steps */
               }
            
               SC_Close();
               return 0;
            }
            
            
            
            SC_SetTraceRange
            ============================================================
            
               Changes the minimum and maximum real world coordinates of
               a Trace Window.   A thick vertical line is automatically
               drawn at the current time position to indicate the
               change.
            
            SYNTAX
            
               #include "sc.h"
               void SC_SetTraceRange(SC_WINDOW *traceWindow, 
                 double ymin, double ymax, int *error);
            
            REMARKS
            
                 traceWindow [in] is a pointer to the Trace Window.
            
                 ymin [in] is the new real world Y coordinate which
                 corresponds to the bottom border of the trace window.
            
                 ymax [in] is the new real world Y coordinate which
                 corresponds to the top border of the trace window.
            
                 error [out] is a pointer to an error code.  A non-zero
                 error code indicates an error condition.
            


                                          32






            SEE ALSO
            
               SC_AddTraceWindow
            
            EXAMPLE
            
            #include <stdio.h>
            #include <stdlib.h>
            #include "sc.h"
            
            int main(void)
            {
               int i;
               int error;
               double y;
               SC_WINDOW *traceWindow;
            
               /* Initialize: 8.5 inch wide paper,
                  plot speed = 1 inch/second */
               SC_Init(LPT1, SC_24PIN, SC_LOW_RES, INCHES, 8.5, 1.0,
                &error);
            
               /* Set timing (vertical) grids to be 1 second apart. */
               SC_SetTimeGrids(1.0, &error);
            
               /* Set Y label format; display at 2.0 second intervals.
               */
               SC_SetYlabels(10.0/72.0, "%+0.1f", 2.0, &error);
            
               /* Divide trace into 4 equal sections. */
               SC_SetHorizontalGrids(4, &error);
            
               /* Add Trace Window 4" from top of paper, 
                  1" window height, amplitude range is initially from -2.0
                  to 2.0, display borders, display grids, label Y axis.
               */
               traceWindow = SC_AddTraceWindow(4.0, 1.0, -2.0, 2.0,
                  SCF_BORDER | SCF_GRID | SCF_YLABEL, &error);
            
               /* Draw a triangle wave of amplitude 2.0 */
               y = 2.0;
               for (i=0; i < 10; i++) /* 10 second plot */
               {
                  SC_Trace(traceWindow, y, &error);
            
                  y = y * -1.0; /* triangle wave */
            
                  SC_Draw();
                  SC_Advance(1.0); /* one second steps */
            
                  /* Change the window amplitude range to -4.0 to 4.0 at
                     time = 5.0 seconds.

                                          33






                   */
                  if (i == 5)
                     SC_SetTraceRange(traceWindow, -4.0, 4.0, &error);
               }
            
               SC_Close();
               return 0;
            }
            
            
            
            SC_SetYlabels
            ============================================================
            
               Specifies the label format of  the vertical axis in Trace
               Windows.  This function only affects Trace Windows added
               after calling this function.
            
            SYNTAX
            
               #include "sc.h"
               void SC_SetYlabels(double charHeight, char *format,
                 double interval, int *error);
            
            REMARKS
            
                 charHeight [in] is the character height (in inches or
                 centimeters).
            
                 format [in] is a C printf format string to be used for
                 the vertical axis labels.  Use floating point
                 specifiers in the format string, for example: "%9.3f"
                 or "%+10.4e".  To display labels as integers, use 
                 "%-1.0f".
            
                 interval [in] is the time interval (in seconds) between
                 displaying the labels.
            
                 error [out] is a pointer to an error code.  A non-zero
                 error code indicates an error condition.
            
            SEE ALSO
            
               SC_AddTraceWindow
            








                                          34






            EXAMPLE
            
            #include <stdio.h>
            #include <stdlib.h>
            #include "sc.h"
            
            int main(void)
            {
               int i;
               int error;
               double y;
               SC_WINDOW *traceWindow;
            
               /* Initialize: 8.5 inch wide paper,
                  plot speed = 1 inch/second */
               SC_Init(LPT1, SC_24PIN, SC_LOW_RES, INCHES, 8.5, 1.0,
                &error);
            
               /* Set timing (vertical) grids to be 1 second apart. */
               SC_SetTimeGrids(1.0, &error);
            
               /* Set Y label format; 10 point character height; 
                  display at 2.0 second intervals. */
               SC_SetYlabels(10.0/72.0, "%+0.1f", 2.0, &error);
            
               /* Divide trace into 4 equal sections. */
               SC_SetHorizontalGrids(4, &error);
            
               /* Add Trace Window 2.5" from top of paper, 
                  1.0" window height, amplitude range from -1.0 to 1.0,
                  display borders, display grids, label Y axis.
               */
               traceWindow = SC_AddTraceWindow(2.5, 1.0,
                  -2.0, 2.0, SCF_BORDER | SCF_GRID | SCF_YLABEL,
                  &error);
            
               /* Draw a triangle wave of amplitude 2.0 */
               y = 2.0;
               for (i=0; i < 10; i++) /* 10 second plot */
               {
                  SC_Trace(traceWindow, y, &error);
                  y = y * -1.0;
                  SC_Draw();
                  SC_Advance(1.0); /* one second steps */
               }
            
               SC_Close();
               return 0;
            }
            
            
            

                                          35






            SC_Text
            ============================================================
            
               Displays a text string in a Text Window.
            
            SYNTAX
            
               #include "sc.h"
               void SC_Text(SC_WINDOW *textWindow, char *string, 
                 int *error);
            
            REMARKS
            
                 textWindow [in] is a pointer to the Text Window in
                 which to display the string.
            
                 string [in] is the ASCII text string to display.
            
                 error [out] is a pointer to an error code.  A non-zero
                 error code indicates an error condition.
            
               Calling SC_Text for a Text Window that has not yet
               finished printing the string from a previous call to
               SC_Text will cause the two strings to be printed over
               each other.
            
            SEE ALSO
            
               SC_AddTextWindow
            
            EXAMPLE
            
            #include <stdio.h>
            #include <stdlib.h>
            #include "sc.h"
            
            int main(void)
            {
               int i;
               int error;
               SC_WINDOW *textWindow;
            
               /* Initialize: 8.5 inch wide paper, 
                  plot speed = 1 inch/second */
               SC_Init(LPT1, SC_24PIN, SC_LOW_RES, INCHES, 8.5, 1.0,
                &error);
            
               if (error)
               {
                  printf("%s\n",SC_ErrorMsg(error));
                  return 1; /* exit */
               }

                                          36






            
               /* Add Text Window 1.5" from top of paper, 
                  0.25" window height
               */
               textWindow = SC_AddTextWindow(1.5, 0.25, &error);
            
               /* Draw */
               for (i=0; i < 10; i++) /* 10 second plot */
               {
                  /* Display "hello world" every 2 seconds */
                  if ((i%2) == 0)
                     SC_Text(textWindow,"Hello World!",&error);
                  SC_Draw();
                  SC_Advance(1.0); /* one second steps */
               }
            
               SC_Close();
               return 0;
            }
            
            
            
            SC_Title
            ============================================================
            
               Specifies the title string for a Title Window.
            
            SYNTAX
            
               #include "sc.h"
               void SC_Title(SC_WINDOW *titleWindow, char *titleString,
                 int *error);
            
            REMARKS
            
                 titleWindow [in] is a pointer to the Title Window in
                 which to display the string.
            
                 titleString [in] is a pointer to a text string.
            
                 error [out] is a pointer to an error code.  A non-zero
                 error code indicates an error condition.
            
            SEE ALSO
            
               SC_AddTitleWindow
            






                                          37






            EXAMPLE
            
            #include <stdio.h>
            #include <stdlib.h>
            #include "sc.h"
            
            int main(void)
            {
               int i;
               int error;
               SC_WINDOW *titleWindow;
            
               /* Initialize: 8.5 inch wide paper, 
                  plot speed = 1 inch/second */
               SC_Init(LPT1, SC_24PIN, SC_LOW_RES, INCHES, 8.5, 1.0,
                &error);
            
               /* Add Title Window 5.5" from top of paper, 
                0.25" window height, display every 2.0 seconds
               */
               titleWindow = SC_AddTitleWindow(5.5, 0.25, 2.0, &error);
            
               /* Set title string. */
               SC_Title(titleWindow, "Hello World!", &error);
            
               /* Draw */
               for (i=0; i < 10; i++) /* 10 second plot */
               {
                  SC_Draw();
                  SC_Advance(1.0); /* one second steps */
               }
            
               SC_Close();
               return 0;
            }
            
            
















                                          38






            
            SC_Trace
            ============================================================
            
               Sets the current trace amplitude in a Trace Window.
            
            SYNTAX
            
               #include "sc.h"
               void SC_Trace(SC_WINDOW *traceWindow, double y, 
                 int *error);
            
            REMARKS
            
                 traceWindow [in] is a pointer to the Trace Window.
            
                 y [in] is the current trace amplitude in the same real
                 world units as the window limits, ymin and ymax,
                 specified in the SC_AddTraceWindow function.  When you
                 call SC_Draw, a line will be drawn between the last two
                 points in the Trace Window set by the last two calls to
                 SC_Trace.
            
                 error [out] is a pointer to an error code.  A non-zero
                 error code indicates an error condition.
            
               Gaps may appear in the trace plot if SC_Trace is called
               twice for the same Trace Window without an intervening
               call to SC_Draw.
            
            SEE ALSO
            
               SC_AddTraceWindow, SC_SetTraceRange
            
            EXAMPLE
            
            #include <stdio.h>
            #include <stdlib.h>
            #include "sc.h"
            
            int main(void)
            {
               int i;
               int error;
               double y;
               SC_WINDOW *traceWindow;
            
               /* Initialize: 8.5 inch wide paper, 
                  plot speed = 1 inch/second */
               SC_Init(LPT1, SC_24PIN, SC_LOW_RES, INCHES, 8.5, 1.0,
                &error);
            

                                          39






               /* Set timing (vertical) grids to be 1 second apart. */
               SC_SetTimeGrids(1.0, &error);
            
               /* Set Y label format; display at 2.0 second intervals.
               */
               SC_SetYlabels(10.0/72.0, "%+0.1f", 2.0, &error);
            
               /* Divide trace into 4 equal sections. */
               SC_SetHorizontalGrids(4, &error);
            
               /* Add Trace Window 2.5" from top of paper, 
                  1.0" window height, amplitude range from -1.0 to 1.0,
                  display borders, display grids, label Y axis.
               */
               traceWindow = SC_AddTraceWindow(2.5, 1.0,
                  -2.0, 2.0, SCF_BORDER | SCF_GRID | SCF_YLABEL,
                &error);
            
               /* Draw a triangle wave of amplitude 2.0 */
               y = 2.0;
               for (i=0; i < 10; i++) /* 10 second plot */
               {
                  SC_Trace(traceWindow, y, &error);
                  y = y * -1.0;
                  SC_Draw();
                  SC_Advance(1.0); /* one second steps */
               }
            
               SC_Close();
               return 0;
            }
            
            
            
            SC_yoffset
            ============================================================
            
               Global variable which keeps track of the page offset of
               the bottom border of the last window added.
            
            SYNTAX
            
               #include "sc.h"
               extern double SC_yoffset;
            
            REMARKS
            
               SC_yoffset provides an easy way to add windows
               sequentially to the strip chart.  Initially, SC_yoffset
               is set to zero (the top of the page).  When you add a
               window, SC_yoffset is set to the bottom of the window,
               that is, SC_yoffset is set to yoffset + yheight, where

                                          40






               yoffset is the window offset from the top of the page and
               yheight is the window height.
            
            EXAMPLE
            
            #include <stdio.h>
            #include <stdlib.h>
            #include "sc.h"
            
            int main(void)
            {
               int i;
               int error;
               SC_WINDOW *titleWindow;
               SC_WINDOW *traceWindow1, *traceWindow2, *traceWindow3;
            
               /* Initialize: 8.5 inch wide paper,
                  plot speed = 1 inch/second */
               SC_Init(LPT1, SC_24PIN, SC_LOW_RES, INCHES, 8.5, 1.0,
                &error);
            
               /* Add Title Window 0.5" from top of paper, 
                  0.25" window height, display every 2.0 seconds
               */
               titleWindow = SC_AddTitleWindow(SC_yoffset+0.5, 0.25,
                2.0, &error);
            
               /* Add three trace windows, each 1.0" high with 0.25"
                  spacing between windows */
               traceWindow1 = SC_AddTraceWindow(SC_yoffset+0.25, 1.0,
                  -2.0, 2.0, SCF_NO_FLAGS, &error);
               traceWindow2 = SC_AddTraceWindow(SC_yoffset+0.25, 1.0,
                  -2.0, 2.0, SCF_NO_FLAGS, &error);
               traceWindow3 = SC_AddTraceWindow(SC_yoffset+0.25, 1.0,
                  -2.0, 2.0, SCF_NO_FLAGS, &error);
            
               /* 
               Program Body
               :
               :
               */
            
               SC_Close();
               return 0;
            }
            
            
            
              




                                          41







            
                                  C H A P T E R   4
            
                                    Error Messages
            
            
            
            This chapter lists the error messages returned by function
            SC_ErrorMsg.
            
            Out of memory
               The system has run out of memory.  Try using the large
               memory model for your compiler.
            
            Incorrect window type for this function
               You  passed a pointer (SC_WINDOW *) to a window that is
               inappropriate for this function.  For example,  function
               SC_Text accepts only pointers to Text Windows; passing a
               Trace Window pointer to SC_Text will generate this error.
            
            YMIN equals YMAX
               You passed the same numerical value for arguments ymin
               and ymax to functions SC_AddTraceWindow and
               SC_SetTraceRange.
            
            Window offset must be greater than zero
               The value of argument yoffset must be greater than zero
               when calling functions SC_Add???Window.
            
            Window height must be greater than zero
               The value of argument yheight must be greater than zero
               when calling functions SC_Add???Window.
            
            Invalid printer type/resolution
               You passed invalid values for arguments printerType
               and/or plotResolution to function SC_Init.
            
            Time interval must be greater than zero
               You passed a time interval argument that is less than or
               equal to zero.  All time interval arguments must be
               greater than zero.
            
            Number of divisions must be greater than zero
               You passed a number of horizontal or vertical grid
               divisions argument that is less than or equal to zero. 
               The number of horizontal or vertical grid divisions must
               be greater than zero.
            
            String is a null pointer
               You passed a NULL pointer for a string argument.  Use an
               empty string ("") to pass a null string.

                                          42






            
            Character height must be greater than zero
               The value of argument charHeight must be greater than
               zero in function SC_SetYlabels.
            
            
            














































                                          43