(10U


                        Clipper Memory Management

                            by Roger Donnay


                 A. Linking Techiques for Memory Management

                   1. Dynamic Overlaying of Clipper Code
                   2. Dynamic Overlaying of C/ASM Code
                   3. Using EMS or UMB Ram for Overlays
                   4. Static Overlays
                   5. Reloadable Overlays
                   6. Overlaying Library Modules
                   7. Speed Optimization

                 B. Programming Techniques for Memory Management

                   1. Symbol Management
                   2. Memory effects of Database usage


     ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
     º  LINKING TECHNIQUES FOR MEMORY MANAGEMENT  º
     ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

        The Clipper compiler has the responsiblity of converting source
        code to "machine-readable" code.  This .OBJect code can not
        be "executed" by the machine however until it is "linked" to
        other .OBJect code segments in the Clipper libraries.  This
        is the responsibility of the linker.  Linking or "fixing up"
        references made by your code to external variables and functions
        is necessary to insure that your compiled program will address or
        call other programs, including functions in the Clipper libraries
        and DOS functions.

        A linker's basic job is to combine objects which have been
        compiled separately.  Objects contain symbols of three types:

        a.  PUBLIC symbols - those symbols which are callable from
                             other objects

        b.  STATIC symbols - those symbols which are callable only
                             from within the same object

        c.  UNDEFINED symbols - symbols which exist in other objects
                             and are referenced or used by this object
                             (also referred to as EXTERNAL symbols).

        The Role of Linkers in developing large applications has taken
        a new turn in the past few years.  In addition to providing
        segment-linking, they are now also expected to provide the
        best "memory image" possible.  This means that the linker must
        be sophisticated in it's management of code segments during
        the running of an application.  The physical size of a
        Clipper application is no longer representative of it's memory
        image, because the linker "overlays" the code segments to
        use the smallest possible amount of memory.  Some type of
        code (such as Clipper P-CODE) is easy to overlay while other
        types (ASM) may be more difficult.  Applications that are
        almost all Clipper-compiled code will usually produce the best
        memory image regardless of the physical size of the .EXE.

        The subjects of this seminar are the two most commonly-used
        linkers available on the market today for linking Clipper 5.0
        applications.  They are:

         RTLINK -   A Clipper-5.0 specific linker developed by
                    Pocketsoft, Inc.  This is the linker that is
                    bundled with Clipper 5.0.

         BLINKER -  A Third-Party Clipper-specific linker published
                    by Blink, Inc. for Summer 87 and 5.0 applications.



      ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
      º  DYNAMIC Overlaying of Clipper Code  º
      ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

        Very large Clipper applications can consist of more code than
        can be loaded into the available amount of DOS memory and may
        not be able to execute due to insufficient memory.  Clipper
        5.0 has a "Dynamic Overlay Manager" actually built into the
        Clipper libraries that helps prevent this problem by loading
        the code into memory only as it is needed by the application
        that is running.  The linker helps prepare the application
        to use this capability of 5.0 by splitting the Clipper-compiled
        application code into fixed-size "pages" that share a pre-
        allocated area of memory.  These pages of code are then
        written to a seperate .OVL file or to the end of the .EXE
        file as determined by your linker options.  When a procedure or
        function is called, the "dynamic-overlay manager" first checks
        to see if it is in memory.  If it is, then it jumps to the
        called function.  If it is not in memory, it loads the function
        from disk into any "free" location available in the overlay
        pool.  If no free space can be found in the overlay pool, the
        overlay manager discards pages that have not been called
        recently to free space to load the called procedure.

        The larger the overlay pool, the less often the overlay manager
        needs to load from disk and the faster your program will run.
        The size of the dynamic overlay pool needed for your application
        is automatically determined by Clipper.

        The great thing about Clipper 5.0's dynamic overlaying system is
        that you, the programmer, don't need to do anything to create
        overlays.  It is all done automatically by the linker.  Only
        Clipper-compiled modules, not C/ASM modules, are overlayed
        "dynamically", although since much of the Clipper libraries has
        been compiled in Clipper, even large portions of the Clipper
        libraries will be dynamically overlayed.

        Application libraries and third-party libraries written in
        Clipper will also be automatically overlayed by RTLINK and
        BLINKER. In many cases it is more beneficial to write functions
        in Clipper (using LOCAL memvars) than in C or ASM because it
        will not increase the executable memory model.  Even Clipper
        code that has been linked into to Pre-link libraries will be
        dynamically overlayed.


        INTERNAL/EXTERNAL Overlays
        ---------------------------

        INTERNAL overlays are dynamic pages which are written to the end
        of the .EXEcutable program file.  During the running of the
        application, the dynamic overlay manager reads the disk and loads
        dynamic pages from this file.   This is the default overlay
        method of RTLINK and BLINKER and it is often advantageous to use
        internal overlays to reduce the number of file handles being
        opened by your application.  In some cases however, you may
        find that using multiple overlay files will increase the
        speed performance of your application because extracting code
        from several small files which are all opened at the same time
        is often faster that extracting code from one large file.

        EXTERNAL overlays are sets of dynamic pages which are written to
        a seperately designated file more commonly referred to as an
        overlay file.  The positional command /DYNAMIC[:<ovlfile>] or the
        freeformat command DYNAMIC INTO <ovlfile> will tell RTLINK to
        write the dynamic pages to a file named <ovlfile>.  You may
        wish to create a seperate overlay file when your application
        .EXE is too large to fit on a distribution disk.

        Examples:

         Rtlink>   DYNAMIC INTO myprog.ovl
         Blinker>  SECTION INTO myprog.ovl

         Rtlink>   DYNAMIC INTO myprogs.ovl MYPROG1, MYPROG2
                   DYNAMIC INTO myfuncs.ovl MYFUNC1, MYFUNC2
         Blinker>  SECTION INTO myprogs.ovl MYPROG1, MYPROG2
                   SECTION INTO myfuncs.ovl MYFUNC1, MYFUNC2




      ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
      º  DYNAMIC Overlaying of C / ASM Code  º
      ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

        BLINKER also provides the ability to dynamically overlay code
        written in C or Assembly.  This is the most common code found
        in many third-party libraries.  RTLINK also provides for
        overlaying of C/ASM but it is more complex and requires
        understanding more about the code being overlayed.  See
        STATIC OVERLAYS and RELOADABLE OVERLAYS for more information
        on overlaying C/ASM code with RTLINK.

        In the previous chapter, we discussed that application code
        compiled with the Clipper-compiler is dynamically overlayed
        using the overlay manager built inside the Clipper libraries.
        This Clipper-specific internal overlay manager is incapable
        of overlaying C/ASM code, so it is the responsibility of the
        linker to provide this capability.  Each linker has it's own
        methods for overlaying this kind of code.  BLINKER uses an
        overlay pool that is allocated at the start of the application.
        The size of this pool is determined at link-time.  The larger
        the overlay pool, the faster the application will run because
        overlays will not be reloaded into memory from disk so often.

        The dynamic-overlay capabilities of BLINKER require that the
        objects being overlayed are "well-behaved".  After much
        experimentation with our own libraries and many third-party
        libraries, it is now more clear what constitutes well-behaved
        modules:

         a. Well-behaved code uses the Clipper EXTEND interface,
            registers or the stack for parameter passing and does
            not use undocumented features of Clipper.

         b. All Clipper-compiled .OBJects are dynamically-
            overlayable.

        Modules which CANNOT be dynamically-overlaid are:

         a. Routines which handle interrupts.

         b. Modules in which the DATA area is changed during
            runtime rather than allocating memory in the root area.

        Dynamic overlaying of third-party libraries can be an
        aggravating learning experience if you don't get support from
        the third party vendor in trying to accomplish this task.
        Most of the third-party vendors now break their libraries
        into separate overlayable and non-overlayable .LIB files to
        make the task much easier.

        Once you have determined which .OBJ files and/or .LIB files
        are acceptable for overlaying, the task of telling the
        linker to do this is quite simple.  A BLINKER link-script
        will look similar to an RTLINK script except there is always
        only one (1) overlay area because all code uses the same
        overlay "pool".

        Example of a BLINKER script for overlaying C/ASM:

        # Allocate 50k to the overlay pool
        BLINKER OVERLAY OPSIZE 50
        BEGINAREA
          # Clipper-compiled application code
           FILE myprog1.obj, myprog2.obj
          # C/ASM files
           FILE ccode.obj, asmcode.obj
          # C/ASM libraries
           LIB ccode.lib, asmcode.lib
        ENDAREA



      ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
      º  Using EXPANDED or UMB RAM for OVERLAYS  º
      ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

        BLINKER provides a several very useful feature for increasing
        the amount of available memory for Clipper applications, i.e.,
        the use of Expanded (EMS) or Upper Memory Blocks (UMB).

        -- EMS --

        Many computers have EMS memory.  EMS memory managers such as
        QEMM, 386MAX and DOS 5.0 create a memory area above
        conventional memory referred to as the "page frame".  This 64k
        block of memory is mapped to an area of ram that can execute
        8086 code.  Blinker takes advantage of this feature by
        allocating the 64k EMS page frame rather than conventional DOS
        memory for their runtime overlay pool.  This frees an additional
        64k of memory for use by Clipper because the overlays are loaded
        into the page frame rather than conventional ram.  If no EMS is
        present when the application starts, then the overlay pool will
        be established in normal (conventional) ram.  To enable this
        feature, use the Blinker command:

          BLINKER OVERLAY PAGEFRAME ON

        -- UMB --

        Expanded memory managers will also create an area between the
        640k and 1 meg memory address called UMB (upper memory blocks).
        This is the area where you would normally load your memory-
        resident programs such as DOS, network-drivers, etc.  If your
        enviroment gives you about 40k - 60k of contiguous memory
        available in the UMB area, Blinker will load the overlay pool
        into the UMB area rather than conventional area, thus freeing
        more memory for your Clipper application.  To enable this
        feature, use the Blinker command:

          BLINKER OVERLAY UMB ON



      ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
      º  STATIC Overlays  º
      ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

        STATIC overlays are supported by RTLINK only.  They provide a
        method of overlaying C and ASM code which cannot be overlayed by
        the dynamic-overlay manager.  C and ASM code is not as easily
        relocatable as Clipper compiled PCODE (pseudo-code) therefore it
        cannot be overlayed "dynamically".  A function which is
        dynamically loaded and unloaded from a pool is usually found in
        different places in memory at different times during the running
        of the program.  When a C or assembly routine is called by an
        application linked with RTLINK it must be loaded in memory at
        the same address every time.  This is accomplished by
        designating overlay AREAS where many different modules will
        occupy the same memory space, but only one-at-a-time.
        Designing Static overlays requires a more thorough understanding
        of the structure of your program.

        Static overlay segments usually look like this in your link
        file:

          # area 1
          BEGINAREA
            SECTION FILE A
            SECTION FILE B
            SECTION FILE C
          ENDAREA

          # area 2
          BEGINAREA
            SECTION FILE D
            SECTION FILE E
            SECTION FILE F
          ENDAREA

        You must be sure that you properly place your objects in the
        overlay segments to prevent computer "lock-up" or "crashing"
        at runtime.  In the above example, any procedure or function in
        FILE A may call any procedure or function in FILE D, E or F
        because they are in different areas, however if a function in
        FILE A calls a procedure or function in FILE B, then your program
        will crash as soon as the program returns to FILE A because FILE A
        was removed from memory to load FILE B.

        Overlay management with "static overlays" is the most time-
        consuming because it requires extensive analysis of the
        structure of the program to insure that the modules are placed
        properly in the overlay areas.

 


      ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
      º  RELOADABLE Overlays  º
      ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

        The following overlaying technique may be considered
        controversial because it is an "unsupported" and "undocumented"
        feature of the RTLINK linker supplied with Clipper-5.0.  I feel
        however, that it is important to cover this subject because
        without an understanding of how to use this feature it may be
        impossible to develop certain types of Clipper applications.
        dCLIP is an example of a Clipper application that would not have
        been possible if I could not use "reloadable" overlays.  Please
        be aware that this subject material is not supported by
        Nantucket and is provided as information to be used at your own
        risk.

        I have been RELOADING objects from the Summer 87 Clipper libraries
        for years, so when I received my copy of Clipper-5.0, the first
        thing I attempted to do was to overlay some of the larger C/ASM
        modules in the Clipper libraries using the RELOAD command in
        my linker script file.  The Nantucket development team had the
        foresight to insure that their C and ASM compiler assigned a
        UNIQUE name to each Clipper C/ASM object in the Clipper libraries,
        thus allowing, you, the Clipper programmer to use both the
        RELOAD command and MODULE command in your .LNK script files.

        So what are "Reloadable Overlays"?  These are a form of STATIC
        overlay in which segments of code are placed into overlay sections
        that occupy the same memory space at runtime, however the "calling
        module" is automatically "reloaded" into memory when returning
        from the "called module".

        Reloadable overlay segments usually look like this in your link
        file:

          RELOAD FAR 200
          # area 1
          BEGINAREA
            SECTION FILE A
            SECTION FILE B
            SECTION FILE C
          ENDAREA

          # area 2
          BEGINAREA
            SECTION FILE D
            SECTION FILE E
            SECTION FILE F
          ENDAREA


        Not all Clipper applications are going to need to use these
        reloadable static overlays, but if your application relies
        heavily on third-party libraries written in C/ASM, then it is
        recommended that you learn this technique.

        The main advantage of "reloadable overlays" over conventional
        "static overlays" is that you are never in danger of "lockup"
        in the event that a procedure or function in FILE A calls a
        function or procedure in FILE B because FILE A will be reloaded
        into memory on return from FILE B.  Make sure when you use the
        RELOAD command that you always use it as follows:

          RELOAD FAR <stack size>

        where the <stack size> is the amount of memory in hex bytes to
        use for saving addresses.  My experience is that most
        applications will run just fine with a stack size of 200.  If
        your application does recursive nesting, however, you may need
        to increase the stack size.  Recursive nesting is described as
        follows:  Procedure A calls Procedure B which calls Procedure A
        which calls Procedure B, etc, etc, etc.  Each time a procedure
        is called, its return address is "pushed" onto the stack, and
        each time you return to the calling procedure the address is
        "popped" from the stack.  In the above example, if this
        recursive condition were allowed to continue for a large number
        of iterations, the stack would be overrun and the program may
        crash.

        Although your application will not crash using RELOAD, it may
        slow down a bit if overlay segments are not structured properly,
        because each time an overlay is reloaded the application must
        go to disk.  In the above example if a function in FILE A
        repetitively calls a function in FILE B then your application
        will be very "disk intensive" and will run slowly.  If a
        function in FILE A repetitively calls a function in FILE D there
        will be no slowing at all because both modules will remain in
        memory.

        Overlay management of C/ASM code with "reloadable overlays" is
        less time-consuming and more reliable than simple conventional
        "static overlays" and provides an additional advantage of
        allowing more modules to be overlayed, thereby saving additional
        memory usage.




      ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
      º OVERLAYING LIBRARY MODULES º
      ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

        The MODULE command provides the important capability of
        overlaying the larger modules of CLIPPER.LIB or any other
        third-party library.  With previous versions of these linkers,
        the overlaying of libraries was restricted to ALL modules in a
        library or NO modules in a library.  This is ok for libraries
        which were designed for overlaying, but in most cases it is
        simply not practical to overlay an entire library due to speed
        performance problems.  There are many modules in CLIPPER.LIB
        which can be overlayed without crashing the program, yet runtime
        performance can be disastrous.  Determining the proper "set" of
        modules and the optimum "overlay pool size" is simply a matter
        of trial and error.  For example, overlaying the MACRO module in
        one application may have very little affect on speed performance
        because of the design of the program and it's probable negligible
        On the contrary, it was completely unacceptable to overlay MACRO
        in the dCLIP engine because dCLIP relies heavily on the MACRO
        compiler for many of it's interpretive operations.

        The MODULE command is very useful in that it allows your linker
        to place "modules" from libraries into overlays.   You can
        organize your projects by placing all your C/ASM objects in
        libraries with a library manager such as Microsoft's LIB.EXE
        then by using the SECTION MODULE <module> command in your link
        file you can place any module into any overlay area.

        Rtlink:

          LIB mylib
          BEGINAREA
            SECTION MODULE myfileA,myfileB
            SECTION MODULE myfileC
            SECTION MODULE myfileD
          ENDAREA

        The MODULE <module> command in RTLINK requires that the <module>
        exists in one of the declared libraries and that the name is
        "unique" to that module otherwise the command will be ignored and
        the module will be linked into the root memory area.  This is not
        a problem with the Clipper libraries because the modules are given
        unique names.

        BLINKER supports the MODULE command differently and, in my
        opinion, better than RTLINK.  Blinker allows you to define a
        specific module from a specific library to be linked into the
        application, thus you don't need to worry about the module being
        unique to one library.  For example, if you have two libraries,
        both containing an ERRORSYS module, you can decide which ERRORSYS
        you want linked into the program.

        Blinker:

          LIB mylib
          BEGINAREA
            LIB grump
            MODULE errorsys FROM grump
            MODULE myfileA,myfileB
            MODULE myfileC
            MODULE myfileD
          ENDAREA


        DETERMINING THE MODULE NAMES IN A LIBRARY
        ------------------------------------------

        Every ".OBJect" file placed into a library is also assigned a
        "module" name.  This module name is stored in the "COMENT"
        record of the object in the library.  The "module" name of an
        object is assigned by the compiler of the object and is usually
        given the name of the original source code.   The Clipper
        compiler assigns the same name as the .OBJ file, however many
        compilers will assign the name of the SOURCE file as the module
        name including drive letters and directories.  For example, let's
        say we want to place the Funcky FINDATTR() function into an
        overlay.  First, we must figure out what "module" name was
        assigned to the FINDATTR() function.  There are library manager
        utility programs which can help you figure this out, but I'm
        going to show you how to do it simply with your linker.
        During VERBOSE linking the "module" name of each object being
        linked into the program is displayed on the screen as follows:

          FUNCKY50.LIB(C_MAXCHO)         <- Clipper code
          FUNCKY50.LIB(C_PUTKEY)         <- Clipper code
          FUNCKY15.LIB(findattr.C)       <- "C" code
          FUNCKY15.LIB(finddate.C)       <- "C" code
          FUNCKY15.LIB(findfirs.C)       <- "C" code
          FUNCKY15.LIB(chrfound.ASM)     <- "Assembly" code
          FUNCKY15.LIB(strcente.ASM)     <- "Assembly" code


        You must make sure that you insert the command VERBOSE into your
        link script file to insure that this information is displayed.
        Next, when you perform the link, make sure route the dislay
        output to a file so you can have the information in text file
        format:

          RTLINK @MYPROG > MYPROG.TXT

        MYPROG.TXT will contain the complete list of modules linked into
        your program.  Now, we must take this information and use it to
        develop an overlay strategy.  The name of each module linked into
        the program is shown (in parenthesis) and must be referred to
        "exactly" as it is spelled.  For example, to place the function
        FINDATTR() into an overlay, we must first determine the "module"
        name which would contain the FINDATTR() function.  Fortunately,
        the FUNCKY15 library uses the same prefix name as the actual
        function, so in perusing the list of linked objects in MYPROG.TXT
        we find a module named "findattr.c".  To place this module in an
        overlay section, simply use the command:

            SECTION MODULE findattr.c

        BLINKER's  MODULE command is more useful than RTLINK's because
        it searches both the THEADR record and the COMENT record for the
        name of each module.  This means that you don't need to
        reference the MODULE name as precisely with these linkers as with
        RTLINK.  For example, if the module name in a library is
        FINDATTR.C, BLINKER will overlay it by with the following
        command:  MODULE FINDATTR,  because it will determine that what
        you are trying to overlay is FINDATTR.OBJ.


        OVERLAYING THE CLIPPER LIBRARIES
        ---------------------------------

        Overlaying the Clipper libraries is accomplished quite
        differently with each linker, therefore I have included
        examples for each linker.

        ----------
          RTLINK
        ----------

        RTLINK uses Static reloadable overlays with and the MODULE
        command to overlay much of the Clipper libraries and thereby
        reduce memory usage in your Clipper-5.0 applications.  The
        below link script example creates an overlay area for overlaying
        the larger modules in the Clipper libraries which are not likely
        to call each other recursively, therefore you will probably
        notice very little difference in speed performance yet you will
        get up to 50K more memory overhead depending on how much of the
        Clipper libraries your application uses.

        You may get a "warning" message during link time if your
        application does not call one of the modules referenced in an
        overlay area.  In the event this happens, simply remove that
        module from the link file.  For example, if you are not using
        MEMOEDIT() in your application remove the line:

             SECTION MODULE 50\MEMOEDIT



          FI <my files>
          LIB <my libs>
          OUTPUT <my .EXE>
          RELOAD FAR 200
          BEGINAREA
            SECTION MODULE 50\MEMOEDIT, 50\MEMOTRAN, 50\MEMOREAD
                    MODULE 50\MEMOWRIT, 50\MEMOLINE, 50\MLCOUNT
                    MODULE 50\MLPOS
            SECTION MODULE 50\IS, 50\EXAMPLEC, 50\HARDCR, 50\PAD
                    MODULE 50\PADL, 50\PADC, 50\PADR, 50\ASCAN
                    MODULE 50\ASORT, 50\DIRECTRY, 50\AEVAL, 50\ACOPY
                    MODULE 50\ADEL, 50\AINS, 50\COPYFILE, 50\TYPEFILE
                    MODULE 50\SCROLL, 50\GETE, 50\DISKSPAC
            SECTION MODULE 50\SDF1, 50\SDF0, 50\SDFDYN, 50\DLM1
                    MODULE 50\DLM0, 50\DELIMDYN, 50\DBCREATE
                    MODULE 50\DBJUNCT, 50\DBSTRUCT, 50\ACHOICE
            SECTION MODULE 50\NET, 50\ACCEPT, 50\DATE, 50\OSDATE
            SECTION MODULE 50\FGET, 50\OLDBOX, 50\OLDCLEAR, 50\RUN
                    MODULE 50\SEND, 50\JOINLIST, 50\SORTOF, 50\SORTBLOC
          ENDAREA
          BEGINAREA
            SECTION MODULE 50\TBROWSE0
            SECTION MODULE 50\TBROWSE1
            SECTION MODULE 50\EXAMPLEA, 50\PHILES, 50\DBF0, 50\DTX0
                    MODULE 50\INITEXIT, 50\TXOPEN, 50\BOX, 50\STRTRAN
          ENDAREA

        When placing modules into overlays, you must use extreme care to
        not overlay functions which are called by "interrupts" or may be
        called "recursively".  Code which is called by interrupts is
        called by a direct vector rather than an overlay vector this can
        cause computer lockup if the code segment is not currently in
        memory.  Code which is called recursively would be something like
        special string handling routines that might be called in a
        do..while loop.  If this function were placed in an overlay, you
        may experience considerable slowing and/or disk access.

        Many third-party library developers now distribute their product
        in two libraries: a "resident" library and an "overlayable"
        library.  Most of the work has already been done for you in
        determining which modules can be overlayed.  If the module is part
        of the "resident" library, don't make any attempt to try to
        overlay it or you will experience runtime problems.  Also, don't
        make an attempt to overlay "Clipper code" because this code is
        automatically overlayed into "dynamic-pages".


        -----------
          BLINKER
        -----------

        Overlaying the Clipper libraries with Blinker is simpler than
        Rtlink because only one overlay area needs to be defined for
        all overlayable modules, files and libraries.  Like Rtlink,
        Blinker will automatically overlay any code in any library
        that is compiled with the Clipper compiler.

          BLINKER OVERLAY OPSIZE 50
          BLINKER PROCEDURE DEPTH 50
          FI <my root files>
          LIB <my root libs>
          OUTPUT <my .EXE>
          BEGINAREA
             FILE <my overlayable files>
             ALLOCATE <my overlayable libraries>
             # Modules from CLIPPER.LIB
             MOD accept,acopy,adel,aeval,ains,appinit,atail,box,cmem,date
             MOD dbcmd2,dbcmd3,dbcmd4,dbcmd5,dbcreate,dbf0,dbfdyn,dbjunct
             MOD dbstruct,dtx0,dtx1,dtxdyn,dynina,errsys0,errsys1,fget
             MOD getenv,gets0,gets1,gets2,gx,joinlist,lupdate,memory
             MOD mrelease,msave,net,oldbox,oldclear,philes,run,saverest
             MOD sdf0,sdf1,seq,setcurs,sortbloc,startsym,tb,txopen,vall
             MOD vblock,vdb,vdbg,version,vmacro,vnone,vops,vpict,vterm
             MOD workarea,xmacro
             ALLOCATE extend
           ENDAREA
           LIB clipper, terminal ,dbfntx
 


      ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
      º  SPEED OPTIMIZATION  º
      ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

        Most features of the new generation of linkers are designed
        for memory optimization.  Unfortunately, improving memory
        performance "almost always" works against speed performance
        when the job is being handled by the linker.  Overlaying of
        code requires that code segments be swapped in and out of
        memory and that "overlay vectors" rather than "direct vectors"
        are used to access the code.  This increased overhead will
        slow down the application and often-times create unacceptable
        runtime performance.

        Simply overlaying an entire library is not always the best
        choice when speed performance is critical.  For example, a
        function that skips a record pointer through a database must
        be called once for each record.  If this function is in an
        overlay then the speed of browsing a database, locating a
        record, or reindexing a file can be greatly affected because
        the function must be called via the overlay manager.  Speed
        is not usually a problem when overlaying code that has been
        compiled by Clipper, because the Clipper-code overlay manager
        is actually part of the Clipper libaries and is very efficient
        in the manner in which it dynamically overlays pages of P-CODE
        (Clipper .OBJs).  C and ASM native code on the other hand must
        be overlayed by the linker's overlay manager and can greatly
        affect performance if an often-used function is not in the
        "root" memory area.

        In my opinion, there is no good rule-of-thumb for determining
        which modules should be overlayed other than the time-tested
        method of "trial and error".  I have spent hours and hours
        testing different overlay strategies to end up with the
        just-right balance of speed vs memory optimization.  This
        investment of time has always payed me great dividends because
        from then on I was confident that I done my homework and that
        my application was "perfectly tuned".

        The linkers included in this discussion offer some other fine
        features that can provide improved speed performance without
        sacrificing memory performance, however, they require that you
        utilize some of the advanced features of your computer
        hardware to get the benefit.

        1. OVERLAY CACHING

        Both RTLINK and BLINKER (release 2.0) support the feature of
        "caching" overlays to improve runtime speed on computers with
        EMS or XMS memory.  A "cache" is an area of memory that has
        been pre-allocated for storing code segments that have been
        overlayed and need to be swapped out to make room in memory
        for new code.  Rather than discarding the code segment and
        then reloading from disk each time it is needed, it can be
        reloaded from the "cache" memory.  Obviously, memory to memory
        loading is much faster than disk to memory loading.

         Blinker
         --------

         Blinker 2.0 uses the following commands for caching with XMS
         (2.0 and higher):

          BLINKER CACHE XMS niMax[%], niMinLeave[%]

         For example the command BLINKER CACHE XMS 50%, 1024 will use
         a maximum of 50% of all available XMS, but leave at least
         1024KB available for other programs.

         Even faster caching is available by using EMS (extended memory)
         drivers because memory is handled in large contiguous blocks
         rather than the smaller 64k "pages" such as the XMS (expanded
         memory) drivers.  Use the following command for caching using
         EMS (4.0 and higher)

           BLINKER CACHE EMS niMax[%], niMinLeave[%]


        Rtlink
        -------

         Rtlink's caching system is only useful when using STATIC
         overlays.  In a previous chapter, I showed you how to overlay
         the Clipper libraries and third-party libraries using the
         RELOAD command, BEGINAREA..ENDAREA, and the MODULE command.

         To improve overlaying performance of C/ASM code in STATIC
         overlays, use the following Rtlink caching commands:

           CACHE EXPANDED <memory in K> | <% of available>
           CACHE EXTENDED <memory in K> | <% of available>


        2. OVERLAY POOL SIZE

          Blinker provides for control of the overlay pool size to
          allow more code segments to remain in memory and prevent
          excessive "swapping" in and out of the pool.  Increasing
          the size of the overlay pool will usually have the affect
          of improving speed performance, but not always.  This is
          another of those "trial and error" options.  The disadvantage
          of increasing the pool size is that the application memory
          will be reduced, so don't use more overlay pool than is
          needed for the application.

           Blinker:  BLINKER OVERLAY OPSIZE <nMemoryK>


        3. FORCING SEGMENTS TO ROOT

           Many times when overlaying a library, it is desirable to
           "exclude" code segments from being overlayed to improve
           speed.  Most often, the reason for the exclusion is
           because the segment is used globally by many routines or
           in loops that perform thousands of operations.  Sometimes,
           a segment is just so large that overlaying causes it to
           be swapped in and out of memory much too often.  There are
           several methods to help you with moving code from an
           overlayed library to the "root" memory.

           Rtlink
           -------
           All modules in libraries that are Clipper-compiled .OBJs
           will be automatically overlayed when the library is declared
           with the LIB command in your link script.  To force a
           Clipper module from a library to link to the root memory area,
           use the RESIDENT command and the MODULE command as follows:

           # MYLIB.lib contains my clipper code
           LIB MYLIB
           RESIDENT
           # force MYFUNCS.obj and MYPROCS.obj to the root
           MODULE MYFUNCS, MYPROCS
           # everything from now on is overlayed
           DYNAMIC

           Blinker
           -------
           Specified modules in Clipper-compiled libraries and C/ASM
           libraries which have been overlayed can be forced to root
           memory by using the MODULE command "outside" the BEGIN...
           ENDAREA.  Example:

           BEGINAREA
             # overlay my Clipper application library
             LIB MYLIB
             # overlay my C library
             LIB CFUNCS
           ENDAREA
           # force MYFUNCS.obj and MYPROCS.obj to the root
           MODULE MYFUNCS, MYPROCS
           # force CFUNCS.obj to the root
           MODULE CFUNCS

           Blinker 2.0 also supports a handy feature for automatically
           forcing segments that are smaller than a specified size to
           the root area.  Very small rountines (less than 32 bytes)
           take up more root space when they are overlaid, due to the
           overlay manager table entries, than they would if they
           were simply left in the root.  Additionally, very small
           overlaid routines execute disproportionately slower, since
           the time overhead in loading / calling them may be large
           in comparison with the actual execution time of the routine.

           BLINKER OVERLAY THRESHOLD <nBytes> will allow you to force
           all segments that are smaller than <nBytes> into the root.

  



    ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
    º  PROGRAMMING TECHIQUES FOR MEMORY MANAGEMENT  º
    ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼


      ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
      º  SYMBOL Management  º
      ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

        For a dynamic-overlay manager to work effectively, it is
        important that it load overlays at the smallest possible code-
        segment level, i.e., the procedure/function rather than the
        entire object.  This requires managing the symbol table
        seperately from the code and data, therefore, these linkers
        place the symbol table into the root memory area and each
        function into a separate overlay segment.

        Symbols cannot be overlayed, therefore it is important that
        you program in a manner consistent with producing the smallest
        number of symbols in your Clipper-compiled objects.  Here are
        some tips for reducing the symbol table size in your
        applications.
        

        1.  COMPILE SMALLER SEGMENTS ( C/ASM )

        If you are writing code in C or Assembly, then the overlay
        manager must bring an entire code segment into memory at one
        time.  If you have many large code segments, then the size
        of the overlay pool may need to be increased.  Normally, the
        requirements of the application dictate the size of the code
        segments, but it should be noted that a little extra time
        in optimizing the size of your code will usually pay off if
        you have a large library of routines.

        Clipper-compiled code is loaded "dynamically" so this is not
        a requirement when programming in Clipper.


        2. USE CONSTANTS INSTEAD OF MEMVARS

        Clipper memory variables are always treated as "symbols".
        Refrain from using a memory variable if a constant is
        sufficient.  For example, an unnecessary symbol can be
        eliminated by changing the code:

        escapekey=27
        DO WHILE INKEY()#escapekey
          *clipper code
        ENDDO

        to:

        DO WHILE INKEY()#27
         *clipper code
        ENDDO

         or:

        #define K_ESC 27
        DO WHILE INKEY()#K_ESC
          *clipper code
        ENDDO


        3. USE ARRAYS INSTEAD OF MEMVARS

        Every different Clipper memvar name creates a "symbol", whereas
        an array name creates only ONE symbol.  The following example
        shows how to save considerable memory in a clipper application
        by reducing the symbol count with an array.

        This code produces 10 symbols:

          mname = name
          maddress = address
          mcity = city
          mstate = state
          mzip = zip
          @ 1,1 SAY 'Name   ' GET mname
          @ 2,1 SAY 'Address' GET maddress
          @ 3,1 SAY 'City   ' GET mcity
          @ 4,1 SAY 'State  ' GET mstate
          @ 5,1 SAY 'Zip    ' GET mzip
          READ
          REPL name WITH mname, address WITH maddress,;
          city WITH mcity, state WITH mstate, zip WITH mzip


        This code produces 6 symbols:

          PRIVATE gets[5]
          gets[1] = name
          gets[2] = address
          gets[3] = city
          gets[4] = state
          gets[5] = zip
          @ 1,1 SAY 'Name   ' GET gets[1]
          @ 2,1 SAY 'Address' GET gets[2]
          @ 3,1 SAY 'City   ' GET gets[3]
          @ 4,1 SAY 'State  ' GET gets[4]
          @ 5,1 SAY 'Zip    ' GET gets[5]
          READ
          REPL name WITH gets[1], address WITH gets[2],;
          city WITH gets[3], state WITH gets[4], zip WITH gets[5]


        The following code also produces 6 symbols, however the 5.0
        pre-processor is used here to create both DEBUG and NON-DEBUG
        versions of compiled object code.  In the following example
        the pre-processor is used to convert the 5 memvars to an array
        when compiling the final version.

        To compile the below code WITHOUT symbol substitution for
        debugging purposes, compile as follows:

          CLIPPER <my app> /dDEBUG

        To compile the below code WITH symbol substitution for your
        final application, compile as follows:

          CLIPPER <my app>

        The /dDEBUG switch has the same effect as the comand:

          #define DEBUG

        in your source code, however, it is much more convenient
        because it allows you to make debug or non-debug versions of
        your code simply from the DOS command line or .BAT files.

          #ifndef DEBUG  && compiling non-DEBUG version
            LOCAL gets[5]
            #define mname     gets[1]
            #define maddress  gets[2]
            #define mcity     gets[3]
            #define mstate    gets[4]
            #define mzip      gets[5]
          #endif
          mname = name
          maddress = address
          mcity = city
          mstate = state
          mzip = zip
          @ 1,1 SAY 'Name   ' GET mname
          @ 2,1 SAY 'Address' GET maddress
          @ 3,1 SAY 'City   ' GET mcity
          @ 4,1 SAY 'State  ' GET mstate
          @ 5,1 SAY 'Zip    ' GET mzip
          READ
          REPL name WITH mname, address WITH maddress,;
          city WITH mcity, state WITH mstate, zip WITH mzip



        4. USE THE SAME NAME MEMVARS WHENEVER POSSIBLE

        Again, every "different" Clipper memvar in a module creates a
        symbol.  If an object contains several procedures, use the
        same name for memvars even though they may not perform the same
        or similar functions.   For example, procedure A and procedure
        B both need 5 memvars.  If procedure A declares its memvars with
        5 unique names and procedure B declares its memvars with 5
        unique names, then 10 symbols are used in the linked
        application.  To eliminate 5 symbols, make sure that procedure
        B assigns the same name to the memvars as procedure A.   This
        is not possible of course, if the memvars need to be public to
        both procedures and perform different functions, only if they
        are private.


        5.  USE COMPLEX EXPRESSIONS INSTEAD OF MEMVARS

        The following three lines of codes represents the method that
        most Clipper programmers choose to accomplish most programming
        tasks.  It makes sense to code this way for readability, but
        if you are writing a very large application, this technique
        can be very symbol-intensive.  The following three lines of
        code will read the disk file READ.ME into a memvar named
        READ_FILE, save the changed code into a file named EDIT_FILE,
        then write the changed code back to the disk file READ.ME.

          read_file=MEMOREAD('READ.ME')
          edit_file=MEMOEDIT(read_file)
          MEMOWRIT('READ.ME',edit_file)

        These three lines of code can be replaced by one complex
        expression which uses no symbols at all.

          MEMOWRIT("READ.ME",MEMOEDIT(MEMOREAD("READ.ME")))

        An additional advantage to coding this way is that less
        free-pool or VMM memory is used because the process of
        temporarily storing the text in READ_FILE and EDIT_FILE is
        completely eliminated.  If you find that creating complex
        expressions such as this are unreadable and hard to maintain
        then use the 5.0 pre-processor to accomplish the same task as
        follows:

          # DEFINE read_file MEMOREAD('READ.ME')
          # DEFINE edit_file MEMOEDIT(read_file)
          MEMOWRIT('READ.ME',edit_file)

        The above code is just as readable as the original three lines
        of code but will not create any symbols at compile time.  Try
        compiling this code with your Clipper 5.0 compiler and use the
        /P switch to write the pre-processed code to a .PPO file, then
        look at the .PPO file to see what is actually compiled.


        6. USE LOCALS AND STATICS INSTEAD OF PRIVATES AND PUBLICS

        Sometimes it is just not possible or practical to write code
        without using symbols, so if you find yourself in this
        situation, Clipper 5.0 provides the new feature of
        "LOCALIZING" symbols to the code segment which is currently
        being executed rather than placing the symbol in the main
        symbol table.  Local symbols are effectively "overlayed"
        because they are treated as part of the code segment rather
        than given a place in the main symbol table.

        Not only does this save valuable memory but it also improves
        speed performance because the public symbol table does not need
        to be searched each time a STATIC or LOCAL symbol is referenced
        in your code.  Of course, if the symbol you are referencing is
        needed for the entire application or is used in a macro, then it
        must be declared as PRIVATE or PUBLIC.  Symbols which are not
        declared at all are automatically assumed to be PRIVATE, so make
        sure you use the LOCAL declaration for all symbols in your code
        which you do not want to end up in the main symbol table.

        The following example shows how to save considerable memory in
        a clipper application by reducing the symbol count with LOCAL
        declarations.

        This code produces 6 main memory symbols:

         PRIVATE mcity,mstate,mzip
         mcity = city
         mstate = state
         mzip = zip
         @ 3,1 SAY 'City   ' GET mcity
         @ 4,1 SAY 'State  ' GET mstate
         @ 5,1 SAY 'Zip    ' GET mzip
         READ
         REPL city WITH mcity, state WITH mstate, zip WITH mzip


        This code produces 3 main memory symbols and 3 local symbols:

         LOCAL mcity := city, mstate := state, mzip := zip
         @ 3,1 SAY 'City   ' GET mcity
         @ 4,1 SAY 'State  ' GET mstate
         @ 5,1 SAY 'Zip    ' GET mzip
         READ
         REPL city WITH mcity, state WITH mstate, zip WITH mzip
 


     ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
     º MEMORY EFFECTS OF DATABASE USAGE º
     ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

       Many programmers have taken an affection to "data-driven"
       programming to speed up the development of custom applications.
       As a developer of programming tools, rather than custom
       applications, I find that data-driven programming techniques
       don't serve me well due to the impact on both speed and memory
       performance.  This seminar is dedicated to memory issues so
       we won't discuss the speed issues.  Since Clipper evolved as
       an X-Base type language, the common approach to data-driven
       programming is to create an "engine" or "kernel" .EXE program
       that retrieves "custom" information about the application
       from a set of database files.  The more sophisticated the
       system, the more data files are required for configuring the
       application.  It is important to understand the impact of
       databases on memory usage when designing applications that use
       many databases.

       When a database is opened with the USE command, all the field
       names are placed into the public symbol table.  This allows
       database field names to be used in expressions in the same
       manner as memvars.  Because this symbol table is PUBLIC, the
       field names will remain in the symbol table, even after the
       database is closed.  Clipper employs no mechanism to remove
       symbols from the symbol table, only to add them.  As each
       database is opened the symbols are added, thereby reducing
       the remaining available root memory ( MEMORY(0) ).  It is
       conceivable that an application could run out of memory if
       many databases are opened and closed.  Fortunately, symbols
       of the same name are "reused" in the symbol table, so if you
       open and close the same database many times, the symbol memory
       space will not be reduced.  Keeping this in mind, it is a
       good practice to use databases with fields of the same name.

       To improve speed operation, some programmers will open data-
       dictionary databases at the start-up of the program, load
       the custom program configuration into arrays, then close the
       databases.  This action will reduce the amount of VMM memory
       needed for file buffers and lower the number of DOS handles
       required, but the symbols will still be added to the symbol
       table even though they may never be accessed by the program.
       A data-driven application in which the databases are used
       only during the start-up of the application could be re-designed
       to convert the database information to a text file to generate
       a "runtime" version of the application that will load the
       array(s) from a text file rather than databases, thereby
       eliminating the symbol-table problem.