þþþþþþþþ                 þþ   þþþþþþþþ        þþ
            þþ                       þþ   þþ              þþ       V1.30â
           þþ                       þþ   þþ              þþ
          þþþþþþ  þþþþþþ  þþþþþþ  þþþþ  þþþþþþ  þþþþþþ  þþþþþþþ  þþþþþþ
         þþ          þþ  þþ       þþ   þþ      þþ      þþ   þþ  þþ  þþ
        þþ      þþþþþþ  þþþþþþ   þþ   þþ      þþ      þþ   þþ  þþ  þþ
       þþ      þþ  þþ      þþ   þþ   þþ      þþ      þþ   þþ  þþ  þþ
      þþ      þþþþþþ  þþþþþþ  þþþþ  þþþþþþ  þþþþþþ  þþ   þþ  þþþþþþ

 ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ
  Written by Tobias Burchhardt, (c) 1991-'93 by Software Technik Burchhardt
 ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ






Features at a glance
====================

   * Very fast and fully featured TOSSER/SCANNER for QBBS- (aka Hudson) and
     JAM-Messagebase

   * powerful internal  AreaFix  with  'Forwarding'-feature  and  automatic
     unlinking of passive Passthrough-areas (*registered version only*)

   * Dupe checking with a database of maximum 131000 duperecords

   * Complete netmail routing and packing, easy handling of  multiple  QBBS
     netmail-boards.

   * Networking and multitasking support. Can be simultaneously be used  in
     RemoteAccess- or FrontDoor-multiline-environments. Messagebase will be
     locked while execution. Read messages while tossing in another task.

   * Nice Full-screen tossing mode

   * Complete  zone  and point support. This applies  to inbound as well as
     outbound mail.

   * Full  ARCmail-security  using  passwords with 3 security levels and  2
     different inbounds.

   * Complete QBBS-messagebase-maintenance-utility included. No need to use
     additional utilities. (* JAM support will be made available later! *)

   * Full-screen integrated SETUP utility,  no  need  to  use  an  external
     editor.

   * Easy to use area grouping with assigned  defaults,  use  defaults  for
     each group in every new area (manually or automatically created).

   * Automatic area-adding function with  optional  updating  of  your  BBS
     Configuration files (RA/QBBS/SBBS/ProBoard or TAG)

   * Carbon-Copy-function - filter out special messages and  copy  them  to
     special boards while tossing.

   * Usage of available EMS memory for data and file-buffers

   * Compatible with the FTSC standards FTS-0001  as  well  as  FSC-0039  &
     FSC-0048.

   * Direct screen-writes, DESQview,  PCMOS/386  and  OS/2  aware,  use  of
     ANSI.SYS possible


Noncommercial Shareware Notice, Legal Stuff and Disclaimer
==========================================================

    This is copyrighted software owned by Software Technik Burchhardt. This
  is NOT public domain or freeware.  Software Technik Burchhardt grants you
  a  TEMPORARY  license to try this software for EVALUATION purposes ONLY !
  You may use this package for an evaluation time of 30 days.   After  this
  time  you  have  to  register  FastEcho  or  stop using it ! Any other or
  further use of this software is strictly  forbidden  and  may  result  in
  legal action !

    To  register  FastEcho, please refer to LICENSE.DOC and the order forms
  included in REGISTER.ARJ in this package. This is for NONCOMMERCIAL users
  only ! Commercial users please contact Software Technik Burchhardt  or an
  official FastEcho/commercial dealer.

    FastEcho  is  provided  'as  is', without warranty of any kind, neither
  expressed nor implied. The author only guarantees that FastEcho  and  the
  included tools occupy diskspace.

    In no event will the author be liable to you for any damages, including
  lost profits, lost savings or other incidental or  consequential  damages
  arising out of the use of this program.

    All  mentioned  products and packages are copyrighted by and trademarks
  of their respective holders.

    Registered users receive a key file with a unique serial number.  These
  files are copyrighted stuff owned by Software Technik Burchhardt and MUST
  NOT  be distributed, hacked, reengineered etc. If you don't follow  these
  rules,  your license expires immediately and legal actions may be started
  against you.

    One unique key allows you to run FastEcho on ONE computer at  the  same
  time  only (One computer runtime license).  If you are using the same key
  on different systems (Sysop-Points for example) you need an extra license
  (key) for the other system(s) !  This does not apply to multiline systems
  running FastEcho on the same machine but on several lines.


Description
===========

    FastEcho  is one of the fastest tosser/scanner for the QBBS-Messagebase
  (aka the Hudson-Messagebase) currently available and supports the new JAM
  messagebase introduced with  RemoteAccess  2.00.   Further,  the  package
  contains  all  features  needed  to run a point or a node; smart netmail-
  packing/routing included. Typically every step TOSS, SCAN and PACK is run
  in one pass, including un-/packing of  mail-bundles,  importing/exporting
  of mails and processing of AreaFix-requests.

    It  can  be  run  with  FrontDoor, InterMail, D'Bridge, BinkleyTerm and
  Portal of Power  (Binkley  mode)  and  has  currently  been  tested  with
  FrontDoor  2.02,  2.20a,  D'Bridge 1.5x, InterMail 2.2x, BinkleyTerm 2.5x
  and Portal of Power 0.61.

    This  documentation  is  only a simple guide for you to get to know the
  most important facts  about  FastEcho.  It  doesn't  contain  a  complete
  description of FastEcho and the included tools. If you have any questions
  about  the  possibilities of FastEcho, first of all run all programs with
  '?' - you'll get a  usage-screen  that  will  help  you  in  most  cases.
  Further,  rely on the context-sensitive-online-HELP provided with FESETUP
  - simply press F1.


System Requirements
===================

    Soft- & Hardware
    ----------------

        * An IBM PC, XT, AT or compatible, i386/i486 CPU supported

        * DOS 3.31+ or OS/2 2.x DOS compatibility box

        * FrontDoor 2.02/nc+, FrontDoor 2.20/c, InterMail 2.22+,
          D'Bridge 1.53+, BinkleyTerm 2.50+ or Portal of Power 0.61+
          and optionally RemoteAccess 1.11/2.00, QuickBBS 2.76+,
          SuperBBS 1.17+, ProBoard 1.22/1.31 or T.A.G. 2.6d+ or any
          other QBBS/JAM compatible BBS software

        * A fido '*.msg' style netmail-directory

        * A QBBS-style messagebase

        * Memory requirements:

                FastEcho       350kB - 500kB (1kB when swapping)
                FEUtil            upto 500kB
                FESetup                330kB and more

        * a FILES=??? in your CONFIG.SYS at least at the number of systems
          specified in the Node-Manager plus 20

          Example:  30 systems specified  -->  FILES=50

          or: the value you define for 'Maximum open .QQQs' plus 20


    At least one of these de-/compression utilities:

        * PKZIP/PKUNZIP 1.10/2.04g
        * ARJ 2.30/2.41a
        * LHARC 1.13c/LHa 2.13
        * PKPAK/PKUNPAK 3.61
        * ARC 6.02
        * ZOO 2.10
        * PAK 2.51
        * SQZ 1.08


    Optionally   an  extractor  program  that  copes  with  different  de-/
  compression programs like:

        * General Unpack Shell GUS 1.61 or later
        * PolyXarc 2.1a or later


    For  a  much  better  performance  on  node systems forwarding mails to
  downlinks it is strongly advised to set the 'Temporary Outbound' path  to
  a  RAM  disk  with  at  least 1MB storage.  FastEcho will create outbound
  mail-packets on this disk which speeds up the tossing pretty  much.   The
  more  mail  you  have  to forward, the bigger the RAM disk should be. You
  shall in no event set this 'Temporary' path to your harddisk as this will
  typically slow down  the  tossing  speed  !   You  can  further  increase
  performance by setting 'Temporary Inbound' to a disk drive different from
  the normal 'Outbound'. This way FastEcho will extract the ARCmail bundles
  to  this  drive  and  process  them.  This can reduce disk accessing time
  (spent on head seeks) and especially in LAN environments speed up tossing
  if the normal 'Inbound' was on a network drive and the 'Temporary' is  on
  a local drive.

    If   SHARE   is   loaded,  FastEcho  supports  Messagebase-Sharing  and
  RemoteAccess-Messagebase-Locking.  You can read messages within one  task
  while  tossing  or  scanning  in the other task.  This may also be called
  'Network Mode'.

    FEUtil and FastEcho automatically  detect  a i386  or  higher  CPU  and
  use  some  optimized routines. If you recognize any problems, you may use
  "SET FEOPT=NO386" to disable the 386-support.


Considerations for registered users of FastEcho 1.0?
====================================================

    This  new  version of FastEcho behaves different on Node-systems and on
  Point-systems.  Therefore there are two different kinds of keys available
  at  different  prices.  All keys created for FastEcho 1.0?  are so called
  'Point-Keys', they disable the new version's possibility of downlinks and
  the processing of AreaFix-mails.  If you became a node (or  already  were
  when  registering 1.0? but didn't need the new features at this time) and
  now  NEED  the downlink capabilities I suggest the following to work with
  the new FastEcho until you get a new key:

    Rename  the  FASTECHO.KEY  to  somewhat  else,  so FastEcho doesn't any
  longer recognize it and runs as 'Unregistered Evaluation Copy'. Play some
  time with it and find out  on  yourself,  if  it's  worth  updating  your
  existing  'Point-Key'  to a 'Node-Key'.  [See REGISTER.ARJ for details on
  updating an existing key]

    Note: the fact that you have registered the 1.0? does NOT allow you  to
  use  FastEcho as an 'unregistered' copy longer than the evaluation period
  mentioned in the Shareware Notice !!!


Short Installation Guide
========================

    If you have worked with tossers like  Tosscan,  IMail,  GEcho  etc.   I
  don't  think  that  the  installation of FastEcho will be hard to do. You
  only need a AREAS.BBS [well, it's not really needed, but it will save you
  a lot of time and work] and  the  knowledge  about  your  system  [paths,
  addresses  etc.].  Simply run FESetup and I guess you'll find it familiar
  to other software-packages. FESetup can  import  the  some  configuration
  files of IMail 1.21a and 1.35, TosScan 1.00,  GEcho  1.01  or  FMail
  0.94 as well as an AREAS.BBS file for an easy setup.

    Pressing F1 will give you  a  context-sensitive  help  on  almost  each
  topic.  I suggest to use this feature any time you have problems with the
  setup. Therefore I didn't include the information given in this  help  in
  this document.


        FESetup
        -------
                Information     Gives a short notice about the program

                Switches        Help page about commandline switches

                Shell to DOS    self-explanatory

                Quit            dito


        System
        ------
                Network addresses

                                Here   you   place  YOUR  address(es),  the
                                domain(s) and - if you are a point  -  your
                                Pointnet [aka Fakenet].


                User names

                                These  are  typically  the  name(s)  of the
                                sysop(s) currently using your mailer and/or
                                editor locally.


                Miscellaneous

                                Some global data FastEcho needs to run.


                Pathnames

                                Your paths etc.


                Filenames
                                Define names of some files (logfile etc.)


                Parameters
                                Some global parameters (duperecords etc.)
                                for FastEcho


                Advanced Options

                                Several global options for FastEcho


                ARCmail Options

                                Global options who FastEcho should handle
                                ARCmail bundles


                FEUtil parameters

                                Several options/parameters for FEUtil


                Compression Programs

                                Upto 8 different programs  for  compressing
                                OUTGOING mail-bundles


                Decompression Programs

                                FastEcho automatically detects the archiver
                                used   for  compression  of  inbound  mail-
                                bundles. Therefore you  have  to  tell  him
                                which  decompression  program (and command-
                                line) he should run to unpack them.


                External Programs

                                You can define 2 external programs or batch
                                files which can be run after  unpacking  of
                                compressed  mail or before packing outbound
                                mails.  Can  be  used  for  some  statistic
                                programs analysing .PKT files for example.


                Group names

                                Here you can assign names  for  the  groups
                                later  used in the Area-Manager to make the
                                handling of the areas more easier.


                Origins

                                These  lines  will  be used, if your editor
                                doesn't  include "* Origin:"'s in your out-
                                going echomails.


        Data
        ----
                Node-Configuration

                                Here  you  set  up  all  the  nodes you are
                                exporting  (net-)mails  to. For help on the
                                different  flags  rely  on   F1   and   the
                                documentation of your mailer


                Group Area Defaults

                                The default settings (see below) which will
                                be  used  for  new  areas,  either  created
                                manually in the  Area-Configuration  or  by
                                Auto-Area-Create.


                Area-Configuration

                                Here you specify all your areas. Note, that
                                to  run  FastEcho  properly,  you  have  to
                                define  ONE  area  as  the  'Badmailboard',
                                otherwise it will  fail.  To  enable  dupe-
                                checking,  you  have  to  define ONE are as
                                'Dupeboard'.


                Carbon-Copies

                                This  is  one  of  the  unusual features of
                                FastEcho.  While  tossing   it   may   copy
                                certain  mails  not  only  in  the   normal
                                echo-area, but also in another board.  Here
                                you may setup the necessary information


                AreaFix-Options

                                Several AreaFix options


        Export
        ------
                AREAS.BBS

                                Export an QBBS style AREAS.BBS file


                FASTECHO.SYS

                                Export a human readable copy of the current
                                FastEcho  Configuration.  Include  in  Bug-
                                Reports if necessary.


                ROUTE.FE

                                Export  a  generic  route file for FastEcho
                                Pack -R<file> out of  the  routing  config-
                                uration set up in the Node-Configuration.


        Import
        ------
                Echolist
                                Import  area comments from an echolist file
                                like FIDONET.NA


                AREAS.BBS, IMAIL.ND, ...

                                Possibility to import several configuration
                                files  when  you are switching from another
                                Echomail-Processor to FastEcho.  Note  that
                                your current configuration will be lost !


Running FASTECHO.EXE
====================

    FastEcho  does have several commands and commandline-switches. These are
  listed here:

   TOSS - Toss Incoming Mail
   -------------------------

      This executes  FastEcho's  TOSS  function.   This  will  search  your
    inbound files directory for mail and toss it into your messagebase(s) -
    netmail-messages  will  end up in the netmail-directory, while echomail
    will  be  put  into the correct messagearea. Mails will be forwarded to
    the systems linked to the echomail-areas (on node-systems).

      Should TOSS encounter an ARCmail file from which  it  cannot  extract
    the mail-packets successfully, it will  rename  the  file  to  have  an
    extension of .BAD so that you can look at it - the  file  will  not  be
    processed again until you rename it back to .PKT.

      TOSS will leave with different errorlevels depending on  what  action
    was actually performed:

         0      -      no mails imported
        10      -      netmail imported
        11      -      echomail imported
        12      -      net- & echomail imported

      This  enables  you  to  set  up  your  batch-files  according  to the
    errorlevel.

    Switches
    --------

                -B     Retoss Badmail

                        This  will  force  TOSS to search the badmail-board
                        just  before tossing incoming mails for messages in
                        the badmail-board which can  be  retossed  (put  in
                        simulated inbound .PKTs and be tossed again).

                -C     Make Carbon-Copies

                        This  enables  the  'Carbon-Copy'-feature.  Special
                        mails are not only stored in the  normal  echomail-
                        area  but  also in a area you specified in the your
                        setup.  Please refer to the online-help of  FESetup
                        for further details.

                -F     Don't create File-attach

                        This  disables FastEcho to create a new file-attach
                        when  it  creates  new compressed mail bundles.  Be
                        aware  that  without a proper file-attach, FastEcho
                        will create a new ARCmail bundle the next  time  it
                        runs and will create the last one.  So  make  sure,
                        that  your  bundle will be processed prior to a new
                        run of FastEcho !

                -S     temporarily turn off Security checks

                        Run  with  this  switch,  FastEcho  Toss  will  not
                        perform  any  security  checks  on  incoming  mail-
                        packets.


   SCAN - Scan for Outgoing Mail
   -----------------------------

      This  enables  the  echomail  SCAN function.  The messagebase will be
    searched for outgoing echomail exporting it  to  packets.  Further,  it
    will scan the messagebase for  netmails  stored  in  netmailboards  and
    moves them to your *.MSG netmail-directory for further processing.

      If not found in the exported message, tearline and  origin-line  will
    be  added  to  it  in the packet. The unregistered FastEcho will always
    replace  the tearline  with  "--- FastEcho <Version>".  The  registered
    FastEcho will add its own ^ATID-kludge in the exported mail to show the
    reader that this mail was scanned by FastEcho.


    Switches
    --------
                -N     Don't use NETMAIL/ECHOMAIL.BBS and .JAM

                        To speed up  the SCAN  FastEcho uses by default the
                        ECHOMAIL.BBS file normally created by  your  editor
                        when   you   write   a new message (NETMAIL.BBS for
                        netmails, extension .JAM for  messages  written  in
                        JAM  areas).  This file contains the numbers of all
                        new written messages. If you - for some purposes  -
                        don't  want FastEcho to use it, this feature may be
                        disabled.

                -A     Always use NETMAIL/ECHOMAIL.BBS and .JAM

                        This will force FastEcho to SCAN  your  messagebase
                        only  if  you've  written  new  messages  and  your
                        editor   created   one  or  more  of  these  files.
                        Otherwise it will just exit without any action.

                -F     Don't create File-attach

                        [see above]


  PACK - Pack outgoing netmails
  -----------------------------

     This calls the  netmail-packer.   This  means  that  the  not-yet-sent
   netmails are packed accordingly to your routing setup with FESetup or to
   the runtime-parameters you  may  specify.   Only  netmails  without  any
   'priority-flags' such  as  'Crash',  'Direct'  or  'Immediate'  will  be
   packed.  Further FastEcho will not touch netmails that include a ^aFLAGS
   kludge  in  it,  except  those only containing PVT, K/S or CFM (Private/
   Priviledged, Kill/Sent and Confirmation Receipt Request).

     If you only call FastEcho PACK without any special  routing-statements
   it  will  use  the  default  routing  you  set  up  in the Node-Manager.
   Otherwise it will perform the routing you specify in the command-line or
   use the routing information specified in a special route file.


   Routing Commandline Statements
   ------------------------------

        PACK [-F] [-I] Address [Address] [Address]... [via Address]

          If you don't specify  a  'via'  address,  the  netmails  will  be
        packed  for  each  address and one packet will be  created for each
        address.   Otherwise   all   netmails  destined  to  the  specified
        addresses  will  be  packed  and  routed  to the 'via' address. The
        destination-addresses may be shortened if packing for (your) points
        - for example 'PACK .3 .4 .5 .6' will pack the  netmails  for  your
        points.

          You   may   specify  wildcards  '*'  &  '?'  in  the  destination
        address-fields.  If you do so, the 'via' address is mandatory !!!

          This wildcarding is more flexible than the wildcarding  that  may
        be used in the Node-Manager as it may be used within an address.

          Valid wildcarded addresses are for example:

                2:24*           -    will pack all mails for region 24

                9:492/6??.*     -    will pack  all mails for all 6?? nodes
                                     and  their  points  (for  example 610,
                                     623.2 etc.).  This enables you to per-
                                     form a kind of HUB-routing.

                *:345/*         -    will  pack mails for all nets 345,  no
                                     matter to which zone they belong


   Route file commands
   -------------------

        PACK [-F] [-I] -R<filename>

          The <filename> must point to  a  ASCII  file  containing  routing
        statements  being  compatible  with  the ROUTE.FD file supported by
        FrontDoor.  The route file is processed top-down - the last command
        matching a netmails destination address will be used. You  may  use
        the same wildcards defined above for pattern matching.

          Supported are the following verbs/commands:

                Route-to <destination> <address> [<address> ...]

                No-Route <address> [<address> ...]

                Direct <address> [<address> ...]

          and
                Except <address> [<address> ...]

          Each command has to fit in one line, the 'Except' command applies
        to the previous command.

          'Route-to' should be self-explanatory, it will instruct  FastEcho
        to route netmails matching one  of  the <address> field(s) via  the
        <destination> address.

          'No-Route' and 'Direct'  cause  FastEcho  not  to  route  netmail
        addressed  to  one of the <address> fields, but pack it directly to
        this system. The difference between  'No-Route'  and  'Direct'  is,
        that 'No-Route' doesn't check the '.point' of the address and there
        fore  packs  mails  addressed to point systems via their boss node,
        while 'Direct' will force them to be packed directly for the point-
        system.


          Available macros for <address> are:

          MYZONE     - Expands to <zone>:* with <zone> being  the  zone  of
                       your primary network address

          MYNET      - Expands to <zone>:<net>/* (again from  primary  net-
                       work address address)

          MYPOINTS   - Expands to <zone>:<net>/<node>.* for ALL  your  net-
                       work addresses

          LISTED     - 'Direct LISTED' will cause netmails to  all  systems
                       defined in FESetup's Node-Configuration to be packed
                       direct without routing them


        NOTE: Netmails can only be routed via or to systems listed  in  the
              Node-Configuration !


   Switches
   --------

                -I      -      Only pack netmails which have the In-Transit
                               flag set, don't pack 'Local' netmails

                -F      -      Don't create File-attach

                                [see above]


  AFIX - process AreaFix requests
  -------------------------------

     This function scans the netmail-directory for  messages  addressed  to
   AreaFix, AreaMgr,  AreaLink  or  EchoMgr  on  your  system.   With  such
   messages your downlinks can link/unlink themselves to echomail areas and
   perform several other changes.

     For an complete listing of all  metacommands  accepted  by  FastEcho's
   AreaFix have a look at the enclosed file 'AREAFIX.HLP' - it  also  gives
   hints for your downlinks/points on how to write a mail  to  AreaFix,  it
   should be defined as 'AreaFix-Helpfile' in your Setup.

     All commands are processed top-down, so  note  that  the  metacommands
   '%DAYS'  and  '%MSGS' have  to  be  defined  BEFORE  the  area(s),  that
   actually should be rescanned.

     Note: the processing of AreaFix request is run automatically after the
   TOSS function has been completed !


  NOTIFY - send link information to your downlinks
  ------------------------------------------------

     This  command  lets  you  send link information normally requested via
   'AreaFix %INFO' to all or to selected downlinks.

     Run without any parameter, it will send this info to all systems which
   have 'Send Notify' turned on.

     Also, you may specify the single systems  which  should  receive  this
  info by giving their address on the commandline like:

                FastEcho Notify 2:245/31 1:2607/302

     Further,  you  may  abbreviate  the   system's   addresses   -   valid
   abbreviations are ('*' and '?' are allowed wildcards):

                        .1              send to your Point .1

                        31              send to node 31 in the network
                                        of your primary matrix-address

                    245/31              same as above

                       2:*              send to all systems in zone 2


  HELP - send help information to your downlinks
  ----------------------------------------------

     This  command is closely related to the NOTIFY command, except that it
   performs a 'AreaFix %HELP'. It accepts the same parameters as NOTIFY.



  STAT - generate echomail statistics
  -----------------------------------

     This starts the statistical function of FastEcho. Every TOSS or SCAN a
   database will be updated containing the  number  of  tossed  or  scanned
   messages  on  each  board and the number of mails sent to  and  received
   from  each  system  in  the Node-Configuration.  This function creates a
   human  readable  statistics  from this database.  The statistics will be
   added  to  the  file specified in FESetup unless you call it with the -O
   option to overwrite the file.

     By  default  FastEcho  STAT  will  leave  the database untouched after
   generation, so any new TOSS or SCAN after STAT will add the new data.

     If run with the -R - switch, FastEcho  will reset the  database  after
   execution, so the next STAT will only show the statistics after the last
   STAT  -R.   This  enables  you for example to generate weekly or monthly
   statistics  rather  than  a  overall  statistics  that will be generated
   without resetting the database. With -RS you can kill the records of the
   amount of mails sent to and received from each system  [second  part  of
   statistics].  Be  aware that the -R switch resets the data of ALL areas,
   even if you've used the -G switch as well.

     You can further only list areas belonging to groups in the statistics.
   With  STAT  -G<groups> you can tell FastEcho which areas it should list.
   This  also  applies to the list of systems - only systems will be listed
   that have access to one of the listed groups.

     Example: FASTECHO STAT -GABJMZ will list all areas belonging to groups
   A, B, J, M and Z and the systems that have access one or more  of  these
   areas.

     The database is stored in FASTECHO.DAT.


Running FESETUP.EXE
===================

  FESetup accepts several commandline-switches - run with '?' it displays:

        ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍµUsageÆÍ¸
        ³                                                          ³
        ³ You may call FESETUP.EXE using following switches:       ³
        ³                                                          ³
        ³ -C        : Color display [with Snow-Checking on CGA]    ³
        ³ -A        : Use alternative colors                       ³
        ³ -M        : Monochrome display                           ³
        ³ -B        : access screen via Bios [very slow]           ³
        ³                                                          ³
        ³ -IE<file> : Import Echolist <file>                       ³
        ³ -O        : Overwrite existing descriptions [-IE only]   ³
        ³                                                          ³
        ³ -XA       : eXport AREAS.BBS                             ³
        ³ -XS       : eXport FASTECHO.SYS [FastEcho configuration] ³
        ³                                                          ³
        ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾


Running FEUTIL.EXE
==================

   FEUtil is QBBS-Messagebase-utility  that  helps  you  to  maintain  your
 messagebase. It has built-in help-screens for all commands available  with
 '?'.

 Following commands are available. The switches may be shortened !

  Index
  -----

   FEUtil Index

     The Index command can be used to create the following  indexfiles  out
   of MSGHDR.BBS:

          MSGIDX.BBS     This file contains the messagenumber and -board of
                         each record in the messagebase

          MSGTOIDX.BBS   This file contains the names of the addressees  of
                         each record in the messagebase

          MSGINFO.BBS    This file contains global information  about  your
                         messagebase regarding the number of  messages  (on
                         each board, totally, highest/lowest message etc.)

     Note that these indexfiles are also created  by  the  Pack,  Sort  and
   Purge commands, so normally this command is not needed.


  Purge
  -----

   FEUtil Purge [-Delete]

     The  Purge  command  is  used  to  delete messages based on criterions
   specified in the Area-Manager of FESetup. These criterions may be set on
   per-area-basis or per default.

   Switches:

        -D or -Delete     Delete all messages in unknown boards


  Pack
  ----

   FEUtil Pack [-Force] [-Overwrite] [-Renumber] [-Delete]

     The  Pack command allows to compress the messagebase-files by removing
   deleted messages and/or removing crosslinked messages.

     FEUtil Pack without -Overwrite or -Force will create new  messagebase-
   files  and  delete  the old upon error-free execution. The -Force switch
   causes the files to be overwritten, which has some  advantages  and dis-
   advantages:
               - no free disk-space needed
               - less fragmentation
               ! possible total loss of data if interrupted while execution

     The -Overwrite switch will cause FEUtil to only overwrite the message-
   basefiles  if  short  of  disk-space. Without these switches FEUtil will
   quit without packing if not enough disk-space is available.

     FEUtil  will  automatically  renumber  if the highest messagenumber is
   higher than what you defined for 'AutoRenumber' in FESetup  rather  than
   always renumber with -Renumber.


   Switches:

        -F or -Force      Force overwriting of the existing messagebase-
                          files
        -O or -Overwrite  Overwrite existing files only if short of disk-
                          space
        -R or -Renumber   Renumber messages and update LASTREAD pointers
                          (may be done by AutoRenumber)
        -D or -Delete     Delete messages crosslinked in MSGTXT.BBS


  Link
  ----

   FEUtil Link

     The  Link  command  can  link  messages  with  the  same  subject to a
   reply-chain that can be followed with your message-editor.

     FEUtil will always create new chains rather than linking new  messages
   to existing chains like other programs do. It will remove  'Re:',  '(R)'
   and familiar junks from the subjects.


  Sort
  ----

   FEUTIL Sort [-Backup]

     The Sort command allows to sort all unread messages by boardnumber and
   date and time of posting.

     FEUtil will remove all reply chains while sorting, so you  should  run
   'FEUtil Link' each time you used Sort.

   Switch:

        -B or -Backup    Keep the original MSGHDR.BBS as backup (.BAK)


  Undelete
  --------

   FEUtil Undelete [Board]

     The  Undelete  command  allows  you  to  undelete  messages  that  are
   currently  deleted by FEUtil Purge or your message-editor.  The undelete
   may either be performed on the whole messagebase or on a special area.

     If specified, Board may be the area-name ('FDECHO.GER' for example) or
   the QBBS-board-number preceded by a '#' (e.g. '#121'). If not specified,
   the whole messagebase will be searched for deleted messages.

     Beware that FEUtil can't undelete messages after the  messagebase  has
   been PACKed right  before,  because  FEUtil  PACK  removes  all  deleted
   messages !


  Import
  ------

   FEUtil Import [-Incl file] [-Excl file]

     This function imports netmails addressed to your system from the *.MSG
   netmail-directory into your QBBS netmailboards you defined in the  Area-
   Manager.  You may define different netmailboards for your different akas
   (be setting 'Use Aka' for each area) - the mail will get imported to the
   correct board.

     Besides from the possibility to exclude the names of the  'Users'  and
   'Sysops'  defined  in  FESetup,  you  can  'include' and 'exclude' mails
   addressed to special users by using the '-Incl' and '-Excl' files. These
   files may either be plain text files with one user name each line (case-
   insensitive) or QBBS-compatible 'USERS.BBS' files used/created  by  your
   BBS software.

     If  '-Incl'  is used, only mails to one of the users specified in this
   file will be imported. Mails *not* to one of the users will  be  ignored
   and left in your *.MSG netmail.

     If  '-Excl'  is  used,  mails to users listed in this file will not be
   imported, even if they are listed in the '-Incl' list  as  the  exclude-
   check is run AFTER the include-check.


  Post
  ----

   FEUtil Post <File> <Board> [-From Name] [-To Name] [-Subj Line]
                              [-Flags <flags>] [-Addr <address>] [-Delete]

     This function lets you send the  contents  of  an  ASCII  file  as  an
   echomail or netmail message.  It creates a  new  message  in  the  given
   board,  optionally  containing  the  values  of From, To and Subj in the
   header  and  the  contents of the file as message text.  You can use DOS
   wildcards for <file> to post more than one file in a single run. If  you
   post a netmail, you have to use -Addr to specify the addressee's netmail
   matrix address and can use -Flags to specify different netmail flags.

     Defaults (if not given at commandline) for the header are:

                From:   first user defined under 'User names' in FESetup
                        OR "SysOp" if not defined

                To:     "All"

                Subj:   filename

     To  enter  values  containing more than one word you have to set these
   words in double-quotes. Otherwise FEUtil won't accept them and return an
   error. Example:

                FEUtil Post c:\dummy #10 -To "All OS/2 freaks"

     Board may either be the area-name ('SHAREWRE' for example) or the QBBS
   board-number preceded by a '#' (e.g. '#122').

     Valid <flags> are: Pvt, Crash, File, Kill, Hold, Dir, Imm, Del, Trunc,
   CFM and RRQ. Multiple flags can be added with a '+' ('Pvt+Crash').

     If  you  call  POST  with the -Delete, it will erase the posted <file>
   after successfully processing it.


  Move
  ----

   FEUtil Move <Board1> <Board2>

     The  move  functions  moves  all  messages from Board1 to Board2. Like
   before, the board may either be the area-name or  the  QBBS-board-number
   preceded by a '#'.


  Check
  -----

   FEUtil Check [-Delete]

     This  functions  checks  your complete QBBS messagebase for any errors
   and  optionally  deletes  all  mails  that  are  found  to be bad and/or
   rebuilds your index files (MSGIDX.BBS, MSGTOIDX.BBS and MSGINFO.BBS).

     If  '-Delete'  is NOT specified, it will simply tell you what is wrong
  (or 'No error' if everything is allright) and then return  an  Errorlevel
  of 111.


Environment Variables
=====================

  Following environment variables are used by FastEcho if specified:

        FD         If you specify FrontDoor as Mailer and  Auto-Area-Create
                   adds a new area, if not set, FastEcho  will  search  the
                   current directory for FrontDoor's configuration files.

        IM         same as above, but for InterMail

        DB         see above, but for D'Bridge

        FE         Points to  the directory of your FastEcho configuration,
                   where FastEcho-related files are expected/created

        FEOPT      This variable may be used for special runtime-parameters

                   Usage:

                        SET FEOPT=flag,flag,...

                   Following flags are available:

                        USEBIOS         use  BIOS-calls  when  printing  to
                                        screen rather  than  direct screen-
                                        writes

                        USEANSI         use  ANSI  driver when  printing to
                                        screen rather  than  direct screen-
                                        writes (uses BIOS as well)

                        NO386           This  disables  the  386-support in
                                        FastEcho/FEUtil

                        NOEMS           don't use EMS for memory expansion

                        NOAFIX          don't  process  AreaFix-mails after
                                        tossing

                        NOPACK          don't pack outbound mail - leave it
                                        as   .QQQ  in  outbound  directory.
                                        (will be processed  the  next  time
                                        you run FastEcho)

                        NODUPES         temporarily  don't   perform  dupe-
                                        checking

                        NOEXPORT        don't forward  mails  to  downlinks
                                        while tossing

                        NOSEENBY        disable the  checking  of  SEEN-BYs
                                        and  therefore  the  dupe-detection
                                        on   this  basis,  mails  will  get
                                        exported  even  if  the  system  is
                                        already listed in the SEEN-BYs

                        NOMSGID         Don't use MSGID  for  dupechecking,
                                        calculate a header checksum instead

                        NOAUTOFAIL      Prevents  FastEcho  from  automatic
                                        failure  when  a sharing  violation
                                        occurs

                        RDEBUG          Log routing debug information  when
                                        using  a  route file (FastEcho Pack
                                        -R<file>)

                        STRIPTEAR       strip the  complete  tearline.  The
                                        message will only have a "* Origin"
                                        without leading '---'

                        PACKONE         Tells  FastEcho  to  only call  the
                                        compression programs with ONE  .PKT
                                        each  time  instead of calling them
                                        with as many as possible. This does
                                        not apply to  compression  programs
                                        with a 'List' prefix set up.


        QBBSLOCK   Specify the period of time in which FastEcho TOSS should
                   check the MBUNLOCK.NOW semaphore (when sharing the QBBS-
                   messagebase).

                   Usage:

                   SET QBBSLOCK=XX              <XX seconds>

                   Instructs  FastEcho  to  check  this  semaphore every XX
                   seconds and temporarily unlock the  QBBS-messagebase  if
                   desired.  If not set, FastEcho will check for this  file
                   before processing a new inbound packet. For better  per-
                   formance don't set it to less than 10 seconds!


Errorlevels
===========

                Errorlevel              Meaning
                ------------------------------------------------------
                        0               nothing to do/no errors
                        1               packed/scanned net-/echomail
                        3               key-failure
                       10               imported netmail
                       11               imported echomail
                       12               imported echo- & netmail
                      246               interrupted by user
                      247               Can't write netmail file
                      248               Can't write messagebase files
                      249               Can't create .PKT file
                      250               wrong switch
                      251               size mismatch
                      252               Can't lock messagebase
                      253               exceeding messagebase limits
                      254               not enough memory
                      255               general error


Semaphore Files
===============

                File                    Purpose
                ----------------------------------------------------------
                NEWAREAS.FE             FastEcho TOSS has added  new areas
                                        to the FastEcho setup
                PACKQBBS.FE             FastEcho TOSS has encountered that
                                        your  messagebase   is  going  off
                                        limits.  Check this  in your batch
                                        files  to  allow  automatic  main-
                                        tenance of your messagebase

                Note: Both files will be created  in  the  FastEcho  system
                      directory (the directory FASTECHO.CFG is read from) !

                MBUNLOCK.NOW            FastEcho  TOSS  will check for this
                                        file  in  the messagebase directory
                                        and  will  temporarily  unlock  the
                                        messagebase it was found/updated

                Note: The following files will only be  created/updated  if
                      you  have  specified  the  'Semaphore'  directory  in
                      FESetup/System Data !

                FDRESCAN.NOW,           Will be updated/created if new net-
                FMRESCAN.NOW            mails   (file-attaches  e.g.)  have
                                        been  created  and  'Force   Mailer
                                        Rescan'  turned  on  in   FrontDoor
                                        environments

                IMRESCAN.NOW,           same as above,  but  for  InterMail
                IERESCAN.NOW            environments

                DBRIDGE.RSN             same as  above,  but  for  D'Bridge
                                        environments

                DBRIDGE.NMW             will be created  when  new  netmail
                                        has been received by FastEcho TOSS

                DBRIDGE.EMW             will be created when  new  echomail
                                        has  been  tossed  by  FastEcho. It
                                        contains  the group letters of  the
                                        areas with new echomail


Batchfiles
==========

    Here is an example how to run FastEcho and FEUtil in batch-mode:

        :START
        [...]

        rem --- Packmail ---

        :SCANNER
        fastecho scan
        goto start

        rem --- Unpackmail ---

        :UNPACKBAD
        fastecho toss -b -c
        goto AFTERTOSS

        :UNPACKMAIL
        fastecho toss -C

        :AFTERTOSS
        if errorlevel 12 goto ECHOMAIL
        if errorlevel 11 goto ECHOMAIL
        if errorlevel 10 goto ONLYNET
        if errorlevel  0 goto ONLYNET

        :ECHOMAIL
        feutil sort -b
        feutil link -i

        :ONLYNET
        newscan N -PL -F -R -X -SN
        itrack
        goto start

        rem --- PackNetmail ----

        :PACKNETMAIL
        itrack

        rem     Pack mails for points
        fastecho pack .1 .2 .3 .4 .5 .6 .7 .11

        rem     Default routing
        fastecho pack -rROUTE.FE

        goto START

        rem --- Messagebase-maintenance ---

        :MAINTAIN
        feutil Purge
        feutil Pack -Force -Delete

        goto START


Help Systems, Registration Sites, Support
=========================================

    If  you  want to register FastEcho or want to obtain nearer information
  about FastEcho please refer to following Help Systems:

        Headquarters:
                        Software Technik Burchhardt
                        Mittelkamp 18
                        D-45731 Waltrop
                        Germany

                        Tel. ++49-2309-77597 (voice)
                             ++49-2309-77019 (fax/data)
                             ++49-2309-77499 (data)

                        Email:  2:243/5039@fidonet.org (Tobias Burchhardt)
                                2:245/39@fidoclassic
                                9:492/6050@virnet
                                27:1331/701.20@signet.ftn

                        or via InterNet: tobi@hds.rmi.de


        Help & Registration BeNeLux:

                        RCE Macar‚
                        Postbus 5711
                        3008 AS  Rotterdam
                        Holland

                        Email:  2:285/501@fidonet (Rob Macare)
                                9:310/301@virnet
                                27:1331/1@signet.ftn


        Help & Registration Spain/Portugal:

                        Atlantis BBS
                        Apartado Postal 3.097
                        18080 Granada
                        Spain

                        Email:  2:385/801@fidonet (Alfredo Sanchez)
                                9:341/101@virnet


        Help & Registration Canada:

                        Alex Stuart
                        2759 Belmont Ave.
                        Victoria, B.C.
                        Canada
                        V8R 4A9

                        Email:  1:340/30@fidonet


        Registration United States of America:

                        Ed Meloan
                        1110 Terrace Circle Drive
                        North Augusta, SC 29841-4349
                        USA

                        Email:  1:360/1@fidonet


        Help & Register United Kingdom:

                        David Ekins
                        286 Elm Road
                        Upper Marham
                        KINGS LYNN
                        Norfolk
                        PE33 9NQ


        Help & Register Italy:

                        Marco Piazza
                        Viale Angeloni n.241
                        47023 Cesena (FO)
                        Italy

                        Email:  2:332/319@fidonet


        Help & Register Isreal:

                        Rudy's Place BBS
                        PO BOX 8394
                        Rishon Le-Zion, 7525
                        Isreal

                        Email:  2:403/138@fidonet (Nemrod Kedem)


    For further information regarding registration,  please  refer  to  the
  enclosed LICENSE.DOC and the registration forms in REGISTER.ARJ !


    Support Sites
    -------------

      These sites always have the latest version of FastEcho available  for
    download  or  file-request, can provide help for  setting  up  FastEcho
    and will try to help when you have problems with FastEcho.

      Bob R.             The Anonymous BBS      1:154/40    +1-414-251-2580
      Joseph Gaspard     ROBOCOP BBS            1:202/911   +1-619-299-0351
      Ken Maskall        The Breeze Inn         1:2607/302  +1-215-559-0553
      Scott J Miller     Programmer's Haven 1   1:2607/103  +1-215-797-9378
      Alex Stuart        Quantum Leap BBS       1:340/30    +1-604-595-4407
      Allan Christiansen The Ranger BBS         2:230/178   +45-62-206914
      Tobias Burchhardt  WayForward BBS         2:243/5039  +49-2309-77019
      Rob Macare         Maasstad BBS           2:285/501   +31-10-4862184
      Marco Piazza       Spectrum               2:332/319   +39-547-611271
      Alfredo Sanchez    Atlantis BBS           2:345/801   +34-58-123848
      Nemrod Kedem       Rudy's Place           2:403/138   +972-3-9667562
      Mauricio Andrade   FastEcho Support       4:80/4      +55-71-244-8764


    Further watch out for the international FidoNet help conference FE_HELP
  which is currently available on the U.S. backbone and in Zone 2.  If  you
  have  problems  to get this area contact either Tobias Burchhardt or Dave
  Rasche or one of your nearest support sites.

    For german-speaking FidoNet members the help conference FASTECHO.GER is
  available  in  Regions 24, 30 and 31. For users in Region 28 please refer
  to FASTECHO.028.

    All FastEcho public releases and FastEcho related utilities are hatched
  into a fileecho named FASTECHO, for details on that topic please  contact
  your nearest support site or betatester.


Thanks
======

    I would like to thank all people that contributed to the development of
  FastEcho with excellent ideas and bug reports.

    Thanks  to  Genesis, Queen, Faith No More, Red Hot Chili Peppers, De La
  Soul, YES, Foreigner, Toto, The Blues Brothers Band, Beastie Boys, Sam  &
  Dave, Ice-T, Rage against the machine, Van Halen, The  Police, Metallica,
  Spin Doctors, White Zombies, Suicidal Tendencies, Ugly Kid Joe,  Pantera,
  Green Jelly and finally Guns'n'Roses for their great music.

    Thanks to all the people who registered FastEcho 1.0X or 1.2X and  made
  it possible for me to keep on developing.


    The beta crew:

        Europe:

        Alberto Vidal, Allan Christiansen, Alon Gingold,  Andre  Boogaards,
        Andreas  Neuhaus,  Andreas  Walter, Arjen Schouten, Arjen Schouten,
        Arne  Handtmann,  Axel  Cordt,  Bernd  Hinkmann, Carsten Schroeder,
        Christian  Beckmann,  Christian  Mueller,  Daniel  Zeilmann,  David
        Ekins, dirk astrath, Eduardo Jacob,  Efraim  Bayarri,  Egons  Bush,
        Erik Wachtmeester, Eyal  Zach,  Frank  Albuschat,  Frank  Lachmann,
        Frederico Diaz Lopez, Gareth Lewin, Gerard van Essen, Hans Siemons,
        Hostas  Red,  Hugo  Landsman,  Jan  Boelsma,  Jens  Freitag,  Joerg
        Gutzke,  Joerg  Michael,  John Crossno, Jon Greaves, Joop Mellaart,
        Jose  Miguel  Rodriguez,  Juan  Cienfuegos, Juan Ignacio Rodriguez,
        Jupp Demary, Klaus Ditze, Klaus Harms, Maik Voege,  Manfred  Pegam,
        Manolo Vidal, Marco Piazza, Markus Ebel,  Markus  Schmidt,  Michael
        Kramm,   Mike   Hartmann,  Nemrod  Kedem,  Noel  Bradford,  Orlando
        Castillo,  Oskar  Azanza, Pedro Navarro, Peter Farwig, Peter Hampf,
        peter janssens, Peter van der Linde,  ROn  van  der  Nagel,  Rainer
        Cremer, Raymond Dijkxhoorn, Rob  Macare,  Robert  Maiwald,  Roeland
        Jansen, Sikko Stienstra, Stefan Schuessler,  Sven  Mueller,  Thomas
        Schaetzer,  Thorsten  Frische,  Thorsten  Rossner, Torsten Vollmer,
        Uriel  Segal,  Volker  Astrath,  Volker Imre, Walter Schick, Werner
        Niedermeier, Wim Bonis


        North-America:

        Alex Stuart, andrew farmer, Ben Hamilton,  Bob  R.,  Bruce  Bodger,
        Charles Buchanan, Denis Newkirk, Ed Dobie, Ed Meloan, George  Bird,
        Hugh Bell, Joe McElmeel, Jonathan  Hulley-Miller,  Joseph  Gaspard,
        Ken  Hacker, Ken Maskall, Mark Moran, mark howard, Matt Montgomery,
        Max  Vonderhorst, Todd Punderson, Paul Harney, Paul Williams, Paula
        Pautler, Scott J Miller


        South-America:

        Araken Salamene, Carlos Strauch, Ivan Martinez, Mauricio Andrade


        Asia:

        Kuan-yu Chen, Marty Wang


        Sorry if I forgot one ! :-) [Write a netmail in this case]


Technical Notes
===============

  * The FTSC product-code for FastEcho is 0xAF (hex), 175 (dec).

  * FastEcho can handle up to 200 systems and 960 areas.

  * FastEcho can process echomail messages up to  64kB,  depending  on  the
    settings in FESetup/Advanced Options/Messagebuffer.

  * The mail-packets  created  by  FastEcho  are  compatible  to  FTS-0001,
    FTS-0004 and FSC-0039, using the Type 2+ packet-header  and  supporting
    the Capability Word.  FastEcho will also  recognize  incoming  FSC-0048
    mail-packets.

  * Linefeeds are always stripped when  processing  mails,  soft  CR's  are
    treated as normal, valid characters.

  * SEEN-BY lines and ^APATH kludges are created and updated.

  * SEEN-BY  is  used  for  duplicate  prevention - if a system is  already
    listed in the SEEN-BY of an incoming message, FastEcho will not forward
    that  message to this system.  [This does NOT apply to point-systems as
    the SEEN-BY are 2D only !]

  * FastEcho can parse both Fido/Opus-  and  SEAdog-style  date-fields,  it
    generates SEAdog-style date-fields when exporting echomail.

  * FastEcho  supports the RemoteAccess/FrontDoor QBBS-messagebase  sharing
    specifications.

  * The dupechecking algorithm checks the ^MSGID kludge if available and  a
    header checksum if not. In order to store the maximum 131000 records in
    while tossing/scanning it needs 512kB of EMS memory (# of records * 4).

  * Outbound mail-packets generated by FastEcho have a .QQQ  extension.  To
    compress them, FastEcho renames them to .PKT and adds 2 <NUL> bytes  at
    the end of the packets. If any error occurs while running the archiver,
    FastEcho will rename them back to .QQQ, so the may be compressed  in  a
    further run of FastEcho.

  * For  a  better performance, unlike other  echomail processors, FastEcho
    keeps the outbound mail-packets open while processing. Therefore to run
    without  error you must give FastEcho at least that many FILES=??? that
    are  needed  to  have  the  packets  for  every  system  defined in the
    Node-Manager simultaneously open.

  * FastEcho supports the 4D addressing which BinkleyTerm 2.50+ offers  for
    points.

  * FastEcho supports the '.BSY' files  created  by  BinkleyTerm  2.50+  in
    multiline-environments   and  will  not  compress  mail  for  a  system
    currently online.

  * FastEcho supports the crc.`nn semaphore files FrontDoor 2.20/c  creates
    in  multiline-environments  and  will  not  compress  mail for a system
    currently online.

  * FastEcho  supports  the  RemoteAccess-Messagebase-Locking  technique as
    proposed  in  RALCK003.DOC  by  Andrew Milner including the support for
    MBUNLOCK.NOW (supported by GoldEd 2.40+, RemoteAccess 2.00, FM 2.20).

  * Before calling an external de-/compression utility,  FastEcho checks if
    the  archive  file  is currently locked/opened by another task and will
    skip  it  to  prevent Share Violations when the utility tries to access
    the file and doesn't have a proper exception handler.

  * FastEcho  was  written  in  C++ (compiled with Borland C++ Version 3.1)
    and assembly language (Turbo Assembler Version 3.1).

  * File-IO is performed using standard DOS filehandle functions.  The  PSP
    filehandle table is expanded to 230 entries.

  * All programs automatically detect  DESQview and  write  to  its  screen
    buffer.  They further detect OS/2 2.x as well as PCMOS/386 and give  up
    time-slices  in  these  environments  if  possible  (when  waiting  for
    messagebase (un-)locking for example).

  * The configuration file of FastEcho may be  used  with  GoldED  2.41  or
    later using the "AREAFILE FastEcho <path>" keyword and with timEd alpha
    10 or later using the "FastEchoCFG <file+path>" keyword.

  * The structures for 'C' and 'Pascal' of FASTECHO.CFG  are  available  as
    FECFG130.ARJ (or magic filename FECFG).

  * The swapping routines used are provided by Thomas Wagner (EXEC 3.3) and
    allow EMS-, XMS- and disk-swapping.

  * FESetup makes intensive use of the TesSeRact CLX  User  Interface  TCXL
    Version 5.52.06 copyrighted by Innovative Data Concepts.

  * FastEcho uses the JAM(mbp) API - Copyright 1993  Joaquim  Homrighausen,
    Andrew Milner, Mats Birch, Mats Wallin. ALL RIGHTS RESERVED.

[EOF]