Disk Performance Test
                                  Version 1.0
                                August 20, 1991



























                          IDK Computer Systems, Inc.
                             129 Cambridge Street
                           Syracuse, New York 13210
                                (315) 475-5598







       1.0  Objectives

                The objective of this project is to invent a method,
       consisting of a computer program and operating instructions, for
       testing the performance of disk subsystems operating in an OS/2
       protect mode environment.  The computer program, distributed with
       this document, is in a file named "DPERF.EXE".  The latter
       sections of this document constitute the operating instructions.


       2.0  Requirements

                The computer program for this test executes on all
       80286, 80386 and 80486 based microcomputer systems that are
       capable of supporting the Microsoft OS/2 operating system.  The
       performance figures yielded by running the program are normalized
       so that they are not affected by the type of central processing
       unit (CPU) or the fundamental clock rate (MHz) of the CPU.  The
       performance figures are be affected by the revision level of the
       OS/2 operating system being used, the file system in use, the
       disk cache system, sector interleave, and the hardware and device
       driver software provided by the disk subsystem vendor.
       Concurrent programming is used to test performance of interrupt
       handling in the disk subsystem device driver.  Separate
       performance figures are shown for read and write tests to measure
       the performance of the disk cache system.  The computer program
       is able to execute on monochrome or color systems, and with MFM,
       RLL, ESDI, IDE or SCSI format drives.  The disk subsystem test is
       able to test local area network simulated disk drives.


       3.0  Test Method

                The computer program for this test consists of two
       principal components:  A CPU Performance Test and a Disk
       Performance Test.  The CPU Performance Test was developed so that
       the results of the Disk Performance Test could be normalized to
       eliminate the effects of differing speed CPU hardware.


       3.1  CPU Performance Test

                During the development phase of this test, compensation
       factors were measured that allow the program to display
       performace figures which are independent of the CPU type and
       fundamental clock frequency.  A CPU Performance Test was written
       to consist primarily of sixteen bit data moves from memory to
       sixteen bit data moves from register to memory, data compare
       instructions, conditional branches, and stack operations.
       Thirty-two bit arithmetic, multiplies, divides, thirty-two bit
       address calculations and string manipulations were deliberately
       omitted from the instruction mix because they are not executed
       frequently enough in the operating system code to affect test
       results within the 0.005% error margin.  The CPU Performance Test
       was designed to mimic the code that is executed in the operating
       system.

                The CPU Performance Test consists of two nested loops.
       The inner loop contains the move, compare, branch and stack
       instructions, and executes for a little under 20 microseconds on
       an IBM Personnal Computer AT running at 8 MHz.  The inner loop is
       executed fifty times to give a nominal execution time of one
       millisecond.  The outer loop executes ten thousand times to give
       the entire test a duration of ten seconds.  The OS/2 Global
       Information Segment, whose address can be obtained by a call to
       the operating system, records the elapsed time since the system
       was turned on or restarted, in milliseconds, continuously
       updated.  The test program records this time at the beginning of
       the two nested loops, then again after the loops finish.  By
       successive approximation, the number of iterations for the outer
       loop was adjusted to the center of the spread which would yield
       observed elapsed time of 10,000 milliseconds on the IBM Personal
       Computer AT running at 8 MHz.  The value of ten seconds was
       chosen for the test so that four significant figures of accuracy
       could be maintained with the one millisecond clock resolution of
       the operating system.


       3.2  Disk Performance Test.

                In order to measure the effects of various forms of
       caching, directory structures and concurrent I/O processing,
       a test was developed which included file writes and file reads of
       various sizes in a multi-thread environment.  Five threads were
       created in the program, each of which writes a file, then reads
       it back.  Elapsed time in milliseconds is reported by each thread
       at the completion of writing the file, and at completion of
       reading the file back.  The record sizes for the files and the
       number of records in each file are shown in Table I.


                        Table I - Record and FIle Sizes

               File Name       Record Size     Number of Records
               -------------------------------------------------
               DPERF001.TMP    1 byte          3,000
               DPERF002.TMP    10 bytes        2,000
               DPERF003.TMP    100 bytes       1,000
               DPERF004.TMP    1,000 bytes     300
               DPERF005.TMP    10,000 bytes    100

       The file sizes were chosen to correspond to record sizes
       most typically written by application programs.  The number of
       records for each file were chosen so that the complete writing of
       each file would take approximately the same amount of time.

                To compute the normalization that eliminates the effects
       of varying CPU performance, the CPU Performace Test (detailed in
       the previous section), and the concurrent file write/read test
       were executed on several different CPU configurations.  In each
       case, the disk drive, the disk controller, and the operating
       system were held constant.  The disk drive used for development
       was a Seagate model ST412, which is a type 1 drive on the IBM
       Personal Computer AT.  The disk controller used for development
       was a Western Digital model WD1003-WA2, which is equivalent to
       the controller supplied by IBM with the Personal Computer AT.
       The operating system used for development was OS/2 version 1.21.
       A floppy disk containing the operating system was prepared and
       set up to have swapping disabled, caching disabled and
       protect-only.  The drive was formatted for the FAT (File
       Allocation Table) directory structure, having a sector interleave
       of 3.  Table II shows the recorded total execution times for the
       various CPU configurations used during test development.






             Table II - Execution Time vs. CPU Type (sheet 1 of 2)

       System                   CPU Test (ms)   Disk Test (ms)
       --------------------------------------------------------
       IBM PC/AT - 8 MHz        10000           139593
                                10000           146656
                                10000           137531
                                10000           140969
                                10000           138657

       Generic 386SX -           4313           128781
         16 MHz                  4312           135125
                                 4313           138250
                                 4312           128281
                                 4313           125344

       Generic 386SX -           8813           142844
         8 MHz                   8812           145125
                                 8813           141437
                                 8812           140906
                                 8813           134687

       Novacor NEAT 286 -        5875           134218
         12 MHz                  5875           136125
                                 5875           128688
                                 5875           134781
                                 5875           135844

       Novacor NEAT 286 -        3437           129718
         20 MHz                  3438           123969
                                 3437           128656
                                 3438           132469
                                 3437           128813

       King of Neat 286 -        4343           132968
         16 MHz                  4344           128375
                                 4343           128719
                                 4344           130656
                                 4343           135875

       King of Neat 286 -        3469           124875
         20 MHz                  3469           132250
                                 3469           123750
                                 3469           127500
                                 3469           124156






             Table II - Execution Time vs. CPU Type (sheet 2 of 2)

       System                   CPU Test (ms)   Disk Test (ms)
       --------------------------------------------------------
       King of Neat 286 -        8843           141406
         8 MHz                   8844           135531
                                 8843           138687
                                 8844           144219
                                 8843           142781

       Generic NEAT 286 -        2875           124062
         25 MHz                  2875           122782
                                 2875           117968
                                 2875           126343
                                 2875           126831

       Generic NEAT 286 -        9094           143437
         8 MHz                   9094           141656
                                 9094           143219
                                 9094           144312
                                 9094           136844

       AMD 386, OPTI Chipset -   1188           117343
         40 MHz                  1188           116157
                                 1188           121031
                                 1188           114750
                                 1188           118281

       AMD 386, OPTI Chipset -   3594           138781
         10 MHz                  3594           128250
                                 3594           135843
                                 3594           137125
                                 3594           125656

       The total execution times shown in Table II are measured from the
       point just prior to creating the first sub-thread in the test
       program to the point at which the last of the five threads had
       completed reading and deleting its test file.  Total execution of
       each thread includes opening its file for writing, writing the
       file, closing the file, re-opening the file for reading, reading
       the file, closing the file again and deleting the file.

                Observation of the test results during development
       showed that, though the CPU Performance Test reported a very
       constant figure, the execution time of the Disk Performance Test
       results were somewhat stochastic.  A BASIC program was written to
       use the least squares method to average the relationship between
       CPU performance and disk subsystem performance.  Because of the
       fact that the total execution times consist of two independent
       parts, the CPU contribution and the disk contribution, a linear
       relationship exists between the CPU performance and the total
       disk test time.  If the execution time of the CPU Performance
       Test is plotted along the abscissa of a graph and the total disk
       test time is plotted along the ordinate, then the X-intercept
       would be the total disk time if there were zero CPU contribution.
       The slope of this graph would be the ratio of time required to
       execute the operating system execution over the CPU Performance
       Test execution time.  The slope of the graph was calculated as
       2.464064;  meaning that the operating system overhead for OS/2
       version 1.21 for this test is about 25 seconds on an 8 MHz IBM
       Personal Computer AT.  The intercept of the graph was calculated
       as 118,977.7; meaning that the disk operations would have taken
       about 119 seconds had the CPU been infinitely fast.  These, of
       course, are average figures.  Some of the observed total disk
       test times are actually lower than 119 seconds because of the
       random nature of asynchronous events in the operating system.
       The BASIC program that was used to compute these figures is
       included with this report in a file named "DPERF.BAS".


       3.3 Normalization Algorithm

                Given that we have a standard for disk subsystem
       performance in the configuration of a Seagate ST412 drive with
       a Western Digital WD1003-WA2 controller, being driven by OS/2
       version 1.21 running from a floppy disk with swapping, caching
       and DOS mode disabled, we can begin to compare other disk
       subsystems to this.  The standard was selected to be the slowest
       configuration that it is reasonably likely that someone might
       implement as of the date of this report.  Thus we can compute a
       performance figure stating that the performance of a new and
       improved system is X number of times greater than the standard.
       The performance figure is a ratio of new subsystem speed to the
       standard.

                During the development of this test, we measured the
       ratio of execution time for the operating system overhead vs. a
       known loop of common instructions.  This ratio was computed to be
       2.464064 as an average over sixty samples.  Multiplying the
       execution time, in milliseconds, for the CPU Performance Test for
       any test configuration by this ratio will give the number of
       milliseconds of operating system overhead for that test
       configuration.  Subtracting this number of milliseconds of
       operating system overhead from the total disk test time yields
       the raw disk time in milliseconds - which is the time that the
       test would have taken to execute if the CPU contribution to the
       test time were not present.  This raw disk test time can then be
       divided by the raw disk test time for the standard ST412
       configuration to yield the reciprocal of the disk performance
       improvment.  What is actually displayed by the test program is
       the standard time, 118,977.7 milliseconds, divided by the raw
       disk test time for the new disk subsystem.


       4.0  Results

                Each time that the computer program for this test runs,
       it records test results to a log file named "DPERF.LOG" on the
       current drive.  If this file does not exist, then the program
       creates it, otherwise it appends new results to the old.  Figure
       1 shows an example of a typical log file from ten test runs using
       two computers and three disk subsystems:







       IDK Disk Subsystem Performance Test
       (c) 1991 IDK Computer Systems, Inc.
       Syracuse, New York 13210 - (315) 475-5598

       Date: 8/22/91   Time: 11:52:17   Operating System: OS/2 1.21
       Test System: Generic NEAT 286 - 25 MHz                Drive: C
       Drive Type: Maxtor 7120AT
       Controller Type: IDE
       Test Conducted by: P. Gleason
       Remarks: Run from floppy disk, no swap, no cache,
       no DOS.

       CPU Performance (relative to 8 MHz 80286): 3.30

             Write Test
       Rec Size  Records  msec
       1         3,000     16562
       10        2,000     10187
       100       1,000     32250
       1,000     300       51312
       10,000    100       27843

              Read Test
       Rec Size  Records  msec
       1         3,000      7125
       10        2,000      4813
       100       1,000      8937
       1,000     300        2688
       10,000    100       10188

       Disk Subsystem Performance (relative to type 1): 2.530
       --------------------------------------------------------------------------------
       IDK Disk Subsystem Performance Test
       (c) 1991 IDK Computer Systems, Inc.
       Syracuse, New York 13210 - (315) 475-5598

       Date: 8/22/91   Time: 11:55:12   Operating System: OS/2 1.21
       Test System: Generic NEAT 286 - 25 MHz                Drive: C
       Drive Type: Maxtor 7120AT
       Controller Type: IDE
       Test Conducted by: P. Gleason
       Remarks: Run from floppy disk, no swap, no cache,
       no DOS, FAT file system.

       CPU Performance (relative to 8 MHz 80286): 3.33

           Figure 1 - Disk Performance Test Log File (sheet 1 of 1)






             Write Test
       Rec Size  Records  msec
       1         3,000     15531
       10        2,000     14562
       100       1,000     34031
       1,000     300       51375
       10,000    100       28750

              Read Test
       Rec Size  Records  msec
       1         3,000     10937
       10        2,000     10438
       100       1,000      7594
       1,000     300        2718
       10,000    100       12062

       Disk Subsystem Performance (relative to type 1): 2.522
       -----------------------------------------------------------------
       IDK Disk Subsystem Performance Test
       (c) 1991 IDK Computer Systems, Inc.
       Syracuse, New York 13210 - (315) 475-5598

       Date: 8/22/91   Time: 11:57:24   Operating System: OS/2 1.21
       Test System: Generic NEAT 286 - 25 MHz                Drive: C
       Drive Type: Maxtor 7120AT
       Controller Type: IDE
       Test Conducted by: P. Gleason
       Remarks: Run from floppy disk, no swap, no cache,
       no DOS, FAT file system.

       CPU Performance (relative to 8 MHz 80286): 3.30

             Write Test
       Rec Size  Records  msec
       1         3,000     18593
       10        2,000     11562
       100       1,000     32281
       1,000     300       51218
       10,000    100       25656

           Figure 1 - Disk Performance Test Log File (sheet 2 of 7)






              Read Test
       Rec Size  Records  msec
       1         3,000      7438
       10        2,000      3906
       100       1,000      8125
       1,000     300        2719
       10,000    100       11656

       Disk Subsystem Performance (relative to type 1): 2.533
       -----------------------------------------------------------------
       IDK Disk Subsystem Performance Test
       (c) 1991 IDK Computer Systems, Inc.
       Syracuse, New York 13210 - (315) 475-5598

       Date: 8/22/91   Time: 12:06:03   Operating System: OS/2 1.21
       Test System: Generic NEAT 286 - 25 Mhz                Drive: C
       Drive Type: Maxtor 7120AT
       Controller Type: IDE
       Test Conducted by: P. Gleason
       Remarks: Run from floppy disk, no swap, no cache,
       no DOS, FAT file system.

       CPU Performance (relative to 8 MHz 80286): 3.33

             Write Test
       Rec Size  Records  msec
       1         3,000     13750
       10        2,000     11625
       100       1,000     29562
       1,000     300       51312
       10,000    100       34906

              Read Test
       Rec Size  Records  msec
       1         3,000     10406
       10        2,000      6562
       100       1,000      5000
       1,000     300        2625
       10,000    100       10906

       Disk Subsystem Performance (relative to type 1): 2.531
       -----------------------------------------------------------------
       IDK Disk Subsystem Performance Test
       (c) 1991 IDK Computer Systems, Inc.
       Syracuse, New York 13210 - (315) 475-5598

           Figure 1 - Disk Performance Test Log File (sheet 3 of 7)






       Date: 8/22/91   Time: 12:10:57   Operating System: OS/2 1.21
       Test System: Generic NEAT 286 - 25 MHz                Drive: C
       Drive Type: Maxtor 7120AT
       Controller Type: IDE
       Test Conducted by: P. Gleason
       Remarks: Run from floppy disk, no swap, no cache,
       no DOS, FAT file system.

       CPU Performance (relative to 8 MHz 80286): 3.30

             Write Test
       Rec Size  Records  msec
       1         3,000     16719
       10        2,000     16063
       100       1,000     31938
       1,000     300       52750
       10,000    100       29500

              Read Test
       Rec Size  Records  msec
       1         3,000      8656
       10        2,000      3718
       100       1,000     11281
       1,000     300        2750
       10,000    100       11281

       Disk Subsystem Performance (relative to type 1): 2.456
       -----------------------------------------------------------------
       IDK Disk Subsystem Performance Test
       (c) 1991 IDK Computer Systems, Inc.
       Syracuse, New York 13210 - (315) 475-5598

       Date: 8/21/91   Time: 11:30:48   Operating System: OS/2 1.21
       Test System: AMD 386, OPTI Chipset - 40 MHz           Drive: C
       Drive Type: Maxtor LT213A
       Controller Type: IDE
       Test Conducted by: P.Gleason
       Remarks: HPFS 386 present, 2 Mbytes FAT system
       cache, Lanman file server, swap on, no DOS, FAT
       file system on this drive, lazy on.
       CPU Performance (relative to 8 MHz 80286): 8.42

           Figure 1 - Disk Performance Test Log File (sheet 4 of 7)






             Write Test
       Rec Size  Records  msec
       1         3,000      5156
       10        2,000      5250
       100       1,000     24250
       1,000     300       35812
       10,000    100       17312

              Read Test
       Rec Size  Records  msec
       1         3,000      2750
       10        2,000      3531
       100       1,000      9406
       1,000     300        1250
       10,000    100       12031

       Disk Subsystem Performance (relative to type 1): 3.454
       -----------------------------------------------------------------
       IDK Disk Subsystem Performance Test
       (c) 1991 IDK Computer Systems, Inc.
       Syracuse, New York 13210 - (315) 475-5598

       Date: 8/21/91   Time: 11:35:48   Operating System: OS/2 1.21
       Test System: AMD 386, OPTI Chipset - 40 MHz           Drive: C
       Drive Type: Maxtor LT213A
       Controller Type: IDE
       Test Conducted by: P. Gleason
       Remarks: HPFS 386 present, FAT file system on this
       drive, 2048K FAT cache, swap on, no DOS, Lanman
       file server, lazy on.
       CPU Performance (relative to 8 MHz 80286): 8.42

             Write Test
       Rec Size  Records  msec
       1         3,000      3125
       10        2,000      7250
       100       1,000     26688
       1,000     300       35719
       10,000    100       16500

           Figure 1 - Disk Performance Test Log File (sheet 5 of 7)






              Read Test
       Rec Size  Records  msec
       1         3,000      2625
       10        2,000      3000
       100       1,000      7250
       1,000     300        1063
       10,000    100       12063

       Disk Subsystem Performance (relative to type 1): 3.479
       -----------------------------------------------------------------
       IDK Disk Subsystem Performance Test
       (c) 1991 IDK Computer Systems, Inc.
       Syracuse, New York 13210 - (315) 475-5598

       Date: 8/21/91   Time: 11:39:21   Operating System: OS/2 1.21
       Test System: AMD 386, OPTI Chipset - 40 MHz           Drive: D
       Drive Type: Fujitsu M2249SA
       Controller Type: Always Technology IN-2000
       Test Conducted by: P. Gleason
       Remarks: HPFS 386, HPFS on this drive, swap, no
       DOS, lazy cache.

       CPU Performance (relative to 8 MHz 80286): 8.42

             Write Test
       Rec Size  Records  msec
       1         3,000      1907
       10        2,000      3407
       100       1,000      2844
       1,000     300        2625
       10,000    100        4250

              Read Test
       Rec Size  Records  msec
       1         3,000      2625
       10        2,000      2406
       100       1,000      2406
       1,000     300          94
       10,000    100        1469

       Disk Subsystem Performance (relative to type 1): 36.835
       -----------------------------------------------------------------
       IDK Disk Subsystem Performance Test
       (c) 1991 IDK Computer Systems, Inc.
       Syracuse, New York 13210 - (315) 475-5598

           Figure 1 - Disk Performance Test Log File (sheet 6 of 7)






       Date: 8/21/91   Time: 11:42:34   Operating System: OS/2 1.21
       Test System: AMD 386, OPTI Chipset - 40 MHz           Drive: D
       Drive Type: Fujitsu M2249SA
       Controller Type: Always Technology IN-2000
       Test Conducted by: P. Gleason
       Remarks: HPFS 386, HPFS on this drive, swap, no
       DOS, Lanman file server, lazy cache.

       CPU Performance (relative to 8 MHz 80286): 8.42

             Write Test
       Rec Size  Records  msec
       1         3,000      2438
       10        2,000      1282
       100       1,000      2657
       1,000     300        1938
       10,000    100         219

              Read Test
       Rec Size  Records  msec
       1         3,000      1937
       10        2,000      1500
       100       1,000       250
       1,000     300         125
       10,000    100        1406

       Disk Subsystem Performance (relative to type 1): 66.468
       -----------------------------------------------------------------
       IDK Disk Subsystem Performance Test
       (c) 1991 IDK Computer Systems, Inc.
       Syracuse, New York 13210 - (315) 475-5598

       Date: 8/21/91   Time: 11:44:33   Operating System: OS/2 1.21
       Test System: AMD 386, OPTI Chipset - 40 MHz           Drive: D
       Drive Type: Fujitsu M2249SA
       Controller Type: Always Technology IN-2000
       Test Conducted by: P. Gleason
       Remarks: HPFS 386, HPFS on this drive, swap, no
       DOS, Lanman file server, lazy cache.

       CPU Performance (relative to 8 MHz 80286): 8.42

           Figure 1 - Disk Performance Test Log File (sheet 7 of 7)






             Write Test
       Rec Size  Records  msec
       1         3,000      3032
       10        2,000      1750
       100       1,000       157
       1,000     300          94
       10,000    100          94

              Read Test
       Rec Size  Records  msec
       1         3,000      2468
       10        2,000      3032
       100       1,000       218
       1,000     300         125
       10,000    100        1000

       Disk Subsystem Performance (relative to type 1): 40.331