ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
                  ³        INTERRUPT DISPATCHER 2.1        ³
                  ³ (C) Copyright 1991 by Kevin Dahlhausen ³
                  ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ


        Interrupt Dispatcher is a utility that allows you to 
   call DOS and BIOS interrupts and view the results in binary, hex, 
   and decimal. There is also a pop-up window that may be used as a
   data buffer.


   	All you need to do is set up the the required registers and press 
   F1. The program will generate the interrupt and display the resulting 
   values of the registers in hexadecimal, decimal and binary notation. 
   Pressing F2 exits the program.  Certain interrupts require pairs of 
   registers to point to data structures in memory. This is accomplished 
   by pressing F3 to bring up the data buffer window. Enter the desired 
   data, following the on-screen help, and press ESC to return to the 
   register screen. Move to the desired register and press F4. The segment 
   or offset of the data buffer will be entered into the register depending 
   on the appropriate usage of that register.




                   WHAT ARE DOS AND BIOS INTERRUPTS?

        The word 'interrupts' refers to the DOS and BIOS software
   interrupts in the following discussion. The interrupts are a set of
   built in routines that talk to the the computer hardware on a basic
   level.  Their purpose is to shield the programmer from the minor 
   hardware variations among different machines.  The interrupt 
   structure is one reason we can run software for the IBM PC on so 
   many compatibles.  The interrupts perform services such as getting or 
   setting the system date/time, creation of files, retrieving 
   information about the equipment installed on the computer, etc.


        For example, function 30h of interrupt 21h returns the version of
   DOS running running on the machine. To find out what version your
   computer is using, run Interrupt Dispatcher and set the following
   parameters:

                           INT  = 21
                           AX   = 3000

        Now press F1.  The display will change.  The major version number
   will be returned in the L part of AX (look at the decimal version).  The
   minor version will be returned in Ah. So if the value 0A03 (this is hex
   number) is returned in the AX field, you would be running DOS version 3.10


   WARNING:    Be carefull when using this program.  There are
               interrupts that write to the disk drives. You 
	       should be safe if you work from a reference 
	       manual, but don't just pick values at random.



                               HISTORY

        A friend  bought "The Programmer's PC Sourcebook" (Thom
      Hogan, Microsoft Press).  Among other things, this book contains
      a listing of the software interrupts and their functions. Initially
      we wrote short DEBUG programs to learn about them. This method was
      crude and took time to set up each interrupt. A program designed for
      the sole purpose of experimenting (playing?) with the interrupts
      would be much more convenient. Thus was the birth of Interrupt 
      Dispatcher.


        This program is distributed as Freeware. No fee, other than a 
      nominal disk and handling fee may be charged for it.  Persons
      intrerested in distributing this program with a commercial
      package may contact me as listed below. 


      I welcome any comments regarding Interrupt Dispatcher, and can
      be reached at:

      AP096@CWNS16.INS.CWRU.EDU			Kevin Dahlhausen
						8627 Scarlet Oak Lane
						Parma, Ohio 44130