Cyrix 486SLC/486DLC
                         Cache Controller

The SETCACHE.EXE program initializes the Cyrix 486 chips internal Cache
to the desired mode. When the Cyrix chips are reset, cache is disabled.
This program allows the user to setup cache for maximum operation speed.

The SETCACHE program may be executed in the AUTOEXEC.BAT file to enable
cache operation at startup, or may be executed at any time from the
command line. The default values have proven to be the fastest operation,
however each user can establish their own setup. It may be that the
't' option can have a beneficial affect.

Command Line options are as follows:

Cache Control program for Cyrix 486SLC/486DLC Microprocessors.
COPYRIGHT 1993 BY JOHN HICKEY of J. JENKS ENTERPRISES.
}SETCACHE [options]
Defaults to 2-way assoc., all mem. cached except A0000-FFFFF.
Options as follows:
t - DOS memory area A0000-FFFFF is cached.
l - Cache inhibit 64K at 1 meg boundaries.
m - Cache mode is direct-mapped.
h - Flush Cache on CPU Hold.
r#aaaaas - Inhibit cache at region #, starting
    at address aaaaa X 1000h, for s size, where:
#     - 1 to 4
aaaaa - 00000-FFFFF hex = address bits 31-12 of inhibited memory.
s     - 0-F size code as follows:
 size-code     Range  size-code     Range  size-code     Range
 0 - none       N/A   1 - 4KBytes   aaaaa  2 - 8KBytes   aaaaj
 3 - 16KBytes  aaaak  4 - 32KBytes  aaaal  5 - 64KBytes  aaaa0
 6 - 128KBytes aaaj0  7 - 256KBytes aaak0  8 - 512KBytes aaal0
 9 - 1MBytes   aaa00  A - 2MBytes   aaj00  B - 4MBytes   aak00
 C - 8MBytes   aal00  D - 16MBytes  aa000  E - 32MBytes  aj000
 F - 4GBytes  00000(Cache is totally inhibited)
a = 0-F Hex  j = 0, 2, 4, 6, 8, A, C or E Hex  k = 0, 4, 8 or C Hex
l = 0 or 8 Hex     Spaces unnecessary between options.
02 00 000000 000000 000000 000000

SETCACHE with no options will initialize the Cache to the default values
of 2-way associative cache and all memory cached except A0000 to FFFFF,
and displays the above help screen.

To setup the Cache to the default values without printing the Help screen,
follow the SETCACHE command with a space.

Option
  t      - Cache DOS memory area A0000-FFFFF.
  l      - Inhibit Caching of 64k bytes at each 1meg boundary.
  m      - Cache Mode is direct mapped.
  h      - Flush cache on CPU HOLD.
r#aaaaas - Inhibit Cache in specific memory regions.
         #     - Non-Cacheable Region number 1 to 4.
         aaaaa - Region beginning boundary address in 4k segments (1000 hex).
                 The boundary address must start on specific power of 2
                 address, depending upon the size code. Valid addresses
                 will be rounded down to the nearest appropriate value.
         s     - Size code 0-F hex specifying region granularity.

        Size           Boundary   Boundary
        code           addr range ending digit(s)
         0 - not        N/A
         1 - 4KBytes   aaaaa(000) 0-F
         2 - 8KBytes   aaaaj  "   0,2,4,6,8,A,C,E
         3 - 16KBytes  aaaak  "   0,4,8,C
         4 - 32KBytes  aaaal  "   0,8
         5 - 64KBytes  aaaa0  "   00-F0
         6 - 128KBytes aaaj0  "   00,20,40,60,80,A0,C0,E0
         7 - 256KBytes aaak0  "   00,40,80,C0
         8 - 512KBytes aaal0  "   00,80
         9 - 1MBytes   aaa00  "   000-F00
         A - 2MBytes   aaj00  "   000,200,400,600,800,A00,C00,E00
         B - 4MBytes   aak00  "   000,400,800,C00
         C - 8MBytes   aal00  "   000,800
         D - 16MBytes  aa000  "   0000-F000
         E - 32MBytes  aj000  "   0000,2000,4000,6000,8000,A000,C000,E000
        *F - 4GBytes   00000  "   Cache is totally inhibited.

After the SETCACHE program executes, the values currently in the
Cache Controller registers are read back and are displayed as follows:

RX RY area-1 area-2 area-3 area-4

where
 RX     = Cache Control Register CCR0
 RY     = Cache Control Register CCR1
 area-n = aaaaas for Non-Cacheable Region n.

The Cache Controller settings will remain unchanged until a System Reset
is done or SETCACHE is rerun with new parameters.


                          !!CAUTION!!!

Do not attempt to run this program on any CPU other than a 80486.
It uses 486 unique instructions and will cause illegal instruction
faults on lesser CPU's!!



SETCACHE.EXE is the Copyrighted work of John Hickey and J. JENKS Enterprises.

    Copyright June, 1993
    All Rights Reserved

    Author         : John C. Hickey
    Date of release: 06/04/93

Please let me know if you have any problems or find the program to be
useful. Registered users may call if they have any problems, and will
be notified of any upgrades.

John Hickey
J. Jenks Enterprises
2155 Philippe Pkwy
Safety Harbor, Fl, 34695

(813) 726-0648