PM System Documentation
                                   Copyright 1992-3 by Frank Murray 



          1. Overview 
          
          PM System is distributed as a stand alone executable program with 
          supporting files.  No other software is needed to operate the 
          program other than a compatible version of DOS.  PM System will 
          run in windows as a DOS application by following windows 
          procedures.  PM System runs in background or foreground depending 
          on the windows setup. 

          Preventive maintenance is something most facility managers talk 
          about doing someday, but somehow never get to doing it.  PM 
          System is meant to make that process easy.  This is a system 
          where basic equipment data is gathered and assigned maintenance 
          tasks to do throughout the year.  Work orders are generated. Work 
          completed and data is then input.  A maintenance history for 
          equipment is kept and available for reference as needed. 

          The system was designed and programmed by an engineer in the 
          maintenance field for over 20 years.  Simplicity, accuracy and 
          minimum amount of keyboard entry were desired.  Reports need to 
          be meaningful but not cluttered with too much data.  The system 
          needed to be easily managed and learned.  Hopefully, you will 
          find this to be true. 



          2. System Requirements 

                 A. Available Memory of 512 or more 

                 B. Hard drive is strongly recommended but, will work on 
                     a floppy with over 600 Kbytes available.  Floppies 
                     are much slower and may run out of storage space as 
                     data files are added. 

                 C. Printer which is IBM/Epson compatible. Standard and 
                     laser printers work well with default values.  No 
                     special printer setup is normally required.  The 
                     printing menu provides more detail.
                     


          3. Installation 

                 A. The distribution disks should be copied and the original 
                    stored in a safe place.  Refer to your DOS manual for 
                    copying procedure.  Some versions are in a ZIP format.  
                    These should be unzipped to a floppy or to a hard drive 
                    directory.   

                 B. The backup copy should be labeled and inserted in the 
                    default drive.  If loaded to a hard drive, set default 
                    to the drive and directory files have been put in. 

                 C. A file .BAT will be copied to your root directory.
                    This file is used to make start up of the program 
                    easier, particularly if more than one installation is 
                    made (multi-location version). Two directories will 
                    also be created, one for system and location files, the 
                    second for common task and documentation files. Default 
                    directories are suggested but can be chosen during 
                    installation  See operation for more detail.
       
                 D. Typing INSTALL will give on screen information about 
                    the installation procedure.  The install program 
                    will verify available space and drives.  You can 
                    substitute for default drives and directories if 
                    desired.  The program will check for existing files and 
                    caution you before overwriting them. Be particularly 
                    cautious if overwriting files with a .DBF extension if 
                    you have previously added data to PM System.

                 E. Updates - a easy to follow update program may be included 
                    on any update disk (3.5 or 5 1/4).  It is suggested to 
                    backup your hard disk data before beginning any update.  
                    Place the update disk  the default drive and type 
                    UPDATE <enter> key.   Additional help will be provided 
                    during update process. Do not use an update command 
                    unless special circumstances indicate an update to the 
                    program is needed. 

                 F. Caution should be used before reinstalling PM System 
                    program over a previously installed location.  This 
                    will write over equipment, task and history data files. 
                    PM System asks you to verify before writing over 
                    existing files. 



          4. Backup 

          It is suggested that a method of backup of data files be 
          established to prevent a total loss of information in the event 
          of disk failure, power failure, virus or other form of bad luck 
          comes your way.  Refer to your DOS manual or other software 
          program to establish a backup method.



          5. Tasks  

          Standard tasks are provided for some typical pieces of equipment, 
          however, manufacturers recommendations should be followed as the 
          main source of preventive maintenance tasks.  It is also 
          important to include safety notes and/or warnings as part of the 
          tasks. 
          
          The task listing is a separate subdirectory and is common to all 
          the PM System separate building programs and subdirectories.  
          Changing a task in one program will change it for all programs. 
          
          A task locator is included in the utility and setup sub menu.  
          At times it may be desirable to modify a task for a particular 
          equipment.  This function will search the equipment file for any 
          other use of that task number.



          6. Operation 

                 A. Use PM System, once the system is booted up, by 
          changing to directory C:\  Then Type  PM1  press ENTER key. 
          PM System will load the default installation of   PM1.
          If any other than default settings were used you can start the 
          program by changing to the root directory of the drive PM System 
          was installated to. Then type the name of the directory selected 
          for installation.  A batch file was created with the same name 
          and placed in the root directory of the drive selected.  For 
          example if you installed to D drive  and  directory TOWERS 
          
                select drive D   by typing    D:  <enter> key
                then                 type     TOWERS   <enter> key

                 B. Alternate to paragraph A. above.  If the batch file in 
          the root directory is not used for startup change to the 
          directory of installation and  type PM   <enter> key.    PM 
          System will load and the main menu will be on the screen.  (To 
          change  directory  Type   CD\PM1  at the C:\>  prompt  See your 
          DOS manual for more detail) 
               
                 C. Task file location is remembered by the system memory 
          variables set during installation.  They should not be moved or 
          the system files will not function correctly.  The same task 
          and documentation files can and should be used if more than one 
          system setup is used (multi-location site license).  

                 D. ESC key is used throughout to escape from the procedure 
          in effect at the time.  Pressing ESC key will usually return you 
          to the previous menu after a screen message.  

                 E. Select desired item by moving Lighted Menu Bar using 
                        Up arrow key      previous lighted bar 
                        Down arrow key    next lighted bar 
                        Home key          start of lighted bar 
                        End key           end of lighted bar 
                      Press Return key when lighted bar is on your choice 

                 F. Input screens use the following keys for Cursor 
          Movement 
                        Up arrow key      previous highlighted item 
                        Down arrow key    next highlighted item 
                        Left arrow        cursor moves left 
                        Right arrow       cursor moves right 
                        Home key          start of highlighted items 
                        End key           end of highlighted items 
                        Return (or Enter) will move to next item 
                        Backspace         erases one space to left 
                        PgDn & PgUp key   save page and continue 

          Some items will only accept input which is valid or meaningful to 
          the category.  Dates must be valid dates.  Only numbers can be 
          input in certain areas, likewise with letters in other areas. 
          Incorrect entries will beep and stay on that item till correctly 
          entered.  Entries are not required in all items and the return 
          key on a blank entry will move to the next item.  Pressing return 
          key on last item of screen will go to next screen. 
       
          Upper or lower case letters can be used.  Printed data will be 
          printed as it was input, so it is best to be consistent for 
          proper grammar and appearance when entering information. Capitals 
          for proper names, etc. and the rest lower case is suggested.  The 
          second best option is all capitals.  PM System starts up with 
          capital lock key to upper case.  Press Caps Lock key once to 
          shift to lower case. 



          7.  Input Work Order Completion    

          This menu selection is used to input data on completed, skipped, 
          partially completed, or unscheduled work on a piece of listed 
          equipment.   The equipment number and job number must be 
          entered.  The date of the work completion, mechanic's initials or 
          number, time in hours and status should be input. Skipped or 
          partially completed tasks should have a date entered on the 
          input.  If no date is entered it will not appear on the completed 
          report and will show up on the backlog report. Hours and tasks 
          done will be totaled on completed reports. If a scheduled work 
          order is not input it will appear on the backlog report when 
          printed.  The comment section allows for notes on the work done 
          and becomes part of the equipment history. The comments are also 
          used for an explanation of why the work may not have been done or 
          only partially completed. 

          Unscheduled work may be included in the equipment history by 
          entering the equipment number and the job # of "UN".  Unscheduled 
          work order input will ask for a trace #, this is printed on the 
          previously printed unscheduled work order.  It is important to 
          enter the trace # if possible.  Entering the trace # will clear 
          the work order from the backlog report of unscheduled  work 
          orders and bring line 1 of the work order into the comment 
          section of the input screen.  This information can be edited and 
          will then be stored in the equipment history file.  Comments 
          appropriate to the work done should be made.  Unscheduled work 
          which did not have a unscheduled work order printed does not need 
          a trace #.  The default of 0 should be inserted. 

          To minimize keystroke entry, default entries show on the input 
          screen.  It is only necessary to input information that is to be 
          changed by moving the cursor to the item to be changed.  The 
          latest screen will appear for the next input screen.  This should 
          help reduce input time for repetitive data entry. 

          When no more entries are to be made enter "N" in the screen 
          highlighted area.   Input data is processed after all data is 
          entered.  Equipment numbers, jobs and other data are checked for 
          accuracy then processed and stored to the history files. This 
          process will take several minutes depending on the size of the 
          history files and the amount of data to process.  The speed of 
          the computer will also have a big impact.  The screen will show 
          the equipment number being processed. 
          
          Instructions indicate that the printer must be ready before 
          proceeding.  Any input data that does not match correctly will be 
          rejected and sent to the printer.  Processing of all good data 
          will continue.  Rejected data should be checked for most likely 
          typographical input errors.  i.e. wrong equipment #'s, wrong or 
          no job # for that equipment #, etc.  Verify data and input again 
          later. 



          8. Report Printing Menu 

          The lighted bar is used to select the choices or to return to the 
          previous menu.  
                
          This submenu is used to select the report which is to be printed.  
          The reports may ask for additional information and will ask you 
          to make sure the printer is ready.  
          
          Printing is intended to work on most all printers.  Fancy or 
          special fonts have been purposely avoided.  Printer output is 
          designed for 80 characters wide with 10 characters per inch to be 
          printed on 8 1/2 inch wide paper. Page length is intended for 11 
          inch paper with 6 rows per inch.  These are the default values 
          for most printers.  This has worked well on dot matrix and laser 
          printers.  Ideally, you should not have to make any special 
          printer setup.  This may not always be the case.  For best 
          printing results set your printer to these values and make any 
          adjustments from there, as needed. 

          All reports (except monthly work order printing) will print 
          approximately  60 lines of print per page and print the page 
          number on the bottom of the page.  Many reports keep several 
          lines of information linked together and will skip to the next 
          page "early" to keep continuity of material.  An adjustment for 
          lines per page can be made in the Utility and Set Up Building Menu 
          in the Setup Building Data selection.  The Lines per page default 
          is 66 lines.  This can be changes to suit your needs.  Should you 
          eject blank pages or print a page with just a page number on top 
          reduce the lines per page appropriately.  This setting will be 
          saved and should not need to be changed once it is correct.  
          Normally, this setting will not be larger than the printer default 
          settings.  This setting will not affect Monthly Work Order 
          Printing but will affect all other printing including the 
          Individual Work Order Printing. 
          
          Monthly work order printing differs slightly from all other 
          reports printed in PM System.  These work orders are printed two 
          to a 8 1/2 by 11 inch page (historically suitable to tradesman 
          use).  8 1/2 by 5 1/2 inch traction feed carbonless paper is also 
          readily available and is well suited to printing work orders.  
          Full size (letter) pages can be cut in the middle if desired.  
          Dot matrix and other standard printers will set the paper 
          perforation just at the top of the printhead.  Laser and inkjet 
          single page printers usually set default top and bottom margins 
          of 1/2 inch leaving 60 lines of print per page.  The laser or 
          inkjet printer may need to be adjusted on the printer to get a 
          well balanced work order printing.  Adjustments should be made, as 
          needed, to the printer default settings or controls for the page 
          length.


               A. Monthly PM Schedule 
          
          This report prints the selected month's preventive maintenance 
          tasks for all equipment due for service during the month.  
          Equipment is listed numerically with the task details printed 
          below.  This list can readily be used to track work order 
          assignments to mechanics, and for scheduling and follow up during 
          the month.  This is often used by supervisors to track assignment 
          of work orders to mechanics.
          
               B. Annual PM schedule    
          
          This report prints the entire calendar years preventive 
          maintenance tasks for all equipment due for service during the 
          year.  Equipment is listed numerically with the task details 
          below.  This is often used as a presentation of planned activity 
          and also used to evaluate maintenance activity throughout the 
          year.  It is a handy reference during the year and used to 
          evaluate adequacy of task assignment. 
                           
               C. Task Description List Printed  
          
          This list is essential as reference when entering new equipment 
          data.  This is used to select the proper task numbers when 
          planning the preventive maintenance tasks.  Basic tasks are 
          provided but custom or special tasks can be added easily (see Task 
          Descriptions Add or Change). 
              
               D. Backlog Work Order Report
          
          A submenu provides for a choice of scheduled or unscheduled 
          backlog reports.
          
          The scheduled backlog report compares the current years planned 
          preventive maintenance schedule to the history file.  It will 
          print out tasks which have not been completed, skipped or 
          partially done.  Input calls for a year, a starting month and a 
          ending month for the report.  The current year, the first month 
          and current month are the default elements to look at a backlog 
          for the current year to date.  The program will compare other 
          years and months but will compare to the current maintenance 
          schedule.  Past years backlog may, therefore, be misleading if 
          changes were made to the task schedule. 

          The backlog report creates a temporary file (histemp.dbf) and 
          index to speed up the backlog search process.  These files will 
          be erased at completion of the report.  The screen reports some 
          data about equipment number being processed, the approximate 
          percentage done, and the number of items in the temporary file.
          When the report is complete some poorly arranged musical notes 
          will alert the user to completion.  

          Note: If a new piece of equipment is added at a later date a 
          backlog report will show as not done.  This may also occur if the 
          system is started at a time other than January.  To over come this 
          either enter the tasks as skipped or do not add task assignments 
          for earlier than the current month and revise the next year. 

          The unscheduled backlog report tracks unscheduled work orders 
          which were printed in the individual work order printing section 
          of the print menu.  These work orders are assigned a trace # 
          which is used to link it back to a unscheduled work order file.
          Upon input of data with the trace # it will clear the work order 
          file and include the data in the appropriate equipment history 
          file. The unscheduled backlog report will print a list of 
          unscheduled work order information (between the dates indicated) 
          which has not yet been input to the system.

               E. Work Order Printing - Month  
          
          This selection will print work orders for equipment which have tasks 
          scheduled for the selected month.  Work orders are printed on 1/2 
          of the standard (8 1/2 X 11) sheet of paper, two work orders to a 
          page.  Default settings on your printer need to be checked if 
          problems are encountered printing work orders. 
          
          In addition to providing tasks descriptions, locations etc. work 
          orders have space provided for recording the date completed, job 
          status, mechanic initials, time spent (hours), performing the 
          work and space to record any notes to enter into the equipment 
          history.  This information is then entered into the Input Work 
          Order Completion menu item.  

               F. Completed Work Order Report
          
          This choice will print a report for all pieces of equipment and 
          will list all jobs done and the task numbers only.   This report 
          will include work done between the two dates entered after 
          selecting this menu choice.  A summary of the tasks done, total 
          hours of work and average time per job are provided.

               G. Single Unit History Report    
          
          This choice will print a report for one piece of equipment and 
          will list all jobs done and the task numbers only.   The equipment 
          number is entered as input along with starting and ending dates.
          The report will include completed, skipped, partially done and 
          unscheduled work orders.  A summary of the tasks done, total 
          hours of work and average time per job are provided.

               H. Individual Unit Work Order

          This selection will go to a lighted bar submenu giving the 
          choices of duplicate of scheduled work order or a unscheduled 
          work order for printing.  These work orders are printed one to a 
          page.  
          
          Duplicate will request equipment number and the month for 
          the work order.  This is mainly for replacing a lost work order 
          without having to reprint an entire months work orders. 
          
          Unscheduled will request equipment number and provide three lines 
          for the work to be done to that equipment.  All three lines are 
          printed on the work order but only line 1 is saved in the 
          unscheduled work order file.  Put the most critical information 
          on this line. A trace # is assigned to each unscheduled work 
          order.  It is suggested to assign an equipment number (9999 
          is used most often) or numbers for general items not assigned 
          regular scheduled maintenance.  This will provide tracking for 
          work done to other items and areas.  Unscheduled work order 
          completion should be input in the regular method using the trace 
          # if given one.   Unscheduled work orders are monitored for 
          completion with the backlog report for unscheduled work orders. 

               I. Equipment Listing Report

          This report provides a brief list of all equipment in the PM 
          System inventory.  It is printed chronologically with the equipment 
          number first, followed by name, manufacturer, model, serial number, 
          location, type of unit and lastly voltage.  This list is useful 
          for locating a unit by number or name.



          9. Equipment  Add Change Delete 
          
          Equipment information is entered, changed and deleted from this 
          selection.  The basic layout and input information can be printed  
          by bringing up the Add screen and while holding the Shift Key 
          down press the PrtSc key.  On most printers this will print 
          whatever is on the screen, there may be variations in the 
          output. The format shown below can also be photocopied.
          Data entered into the equipment input form is as below       

   Equipment number ____ Equip Name _________________________ Type __________

   Manufacturer ____________________ Model __________ Serial _______________

   Volts___ Location__________________________________________________

   Other Information____________________________________________________________
                    ____________________________________________________________
                    ____________________

                    Preventive Maintenance Task Assignments

           January   February   March     April      May      June
     Task 1  ___       ___       ___       ___       ___       ___
     Task 2  ___       ___       ___       ___       ___       ___

            July     August   September  October  November   December
     Task 1  ___       ___       ___       ___       ___       ___
     Task 2  ___       ___       ___       ___       ___       ___

          The title is equipment.  However, the system can be used as a 
          reminder or ticker system for almost anything.  The equipment 
          could be a contract to be negotiated 90 days before renewal.  A 
          task could be created to supplement the information.  It could 
          also be a birthday or anniversary reminder.

          The lighted bar menu is used to select the choices or to return 
          to the previous menu.  

                 A. Add is used to put a new piece of equipment into the 
                 system.   Equipment numbers are selected by the user  
                 usually according to a number assignment plan, however 
                 this is not necessary.  Equipment numbers are 4 digit 
                 numbers.  It is suggested to use all 4 digits for equipment 
                 numbers to avoid confusion with leading and trailing blank 
                 spaces. It is best to have the data for input ready 
                 before starting.  However, missing or incorrect data can 
                 be changed by  using the change menu item.   The equipment 
                 data is self explanatory for the most part.  The "Other 
                 Information" line is used for general notes which 
                 will be useful to the mechanic doing the work.  The task 
                 assignment is made last.  Each month has two entry 
                 possibilities for tasks.  Both can be used, only one or 
                 neither.  It is only necessary to enter 3 digit task 
                 number in the appropriate lighted box.  The system will 
                 accept task numbers which do not yet have tasks assigned 
                 to them.  See tasks for information on standard tasks and 
                 on user make tasks.

                 B. Change is used to change or check the equipment data of 
                 an existing piece of equipment.  You need only enter the 4 
                 digit number and the program will locate the data for you 
                 if it exists.  Change any data, except equipment #, by 
                 cursoring to it and typing over it.  Press PgDn to save 
                 the changes as shown. 
                  
                 C. Delete will ask for the equipment number of the 
                 equipment to delete.  When found the data will be shown 
                 for verification.  You will then confirm the decision to 
                 delete. 



          10. Task Descriptions Add or Change 

          The lighted bar menu is used to select the choices or to return 
          to the previous menu.  Special or custom tasks can be made as the 
          need arises.

                 A. Add is used to put a new task into the system.   Task 
                 numbers are selected by the user according to a number
                 assignment plan shown below.  Task numbers are 3 digit
                 numbers.  It is best to use all 3 for task numbers to
                 avoid confusion with leading and trailing blank spaces.
                 It is best to have the information ready before starting.
                 However, data can be changed by using the change menu item.   
                 Standard tasks, suitable for many pieces of equipment are 
                 provided as part of the basic program.  Special needs 
                 and/or equipment necessitate use of special or custom 
                 tasks.    

                 In adding new tasks the following conventions should be 
                 observed to make any updates easier.  Users should use the 
                 last (right) digit of 5 or higher combine with the 
                 appropriate first two digits. 

          Task Coding Categories               Task Coding Subcategories 

          1XX  - Air Conditioning/Ref          X0X  Frequent (monthly) 
          2XX  - Air Handling units            X1X  Frequent (monthly) 
          3XX  - Heat Pumps                    X2X  Frequent (monthly) 
          4XX  - Pumps & plumbing              X3X  Quarterly 
          5XX  - Electrical                    X5X  Semi Annual 
          6XX  - Mechanical                    X7X  Annual 
          7XX  - Engines & Vehicles 
          8XX  - Specialties 
          9XX  - Misc 
          0XX  - Reserved 

                 B. Change is used to change or check the task details. a 
                 existing piece of equipment. You need only enter the 3 
                 digit number and the program will locate the data for you 
                 if it exists.  Change any detail, except task #, by 
                 cursoring to it and typing over it.  Press PgDn to save the 
                 changes as shown. 
                  
                 C. Delete is not a menu option.  Either do not use the task 
                 or write over it to change it to be a more meaningful task.  
                 It is suggested to keep all tasks and create more or 
                 special ones as needed, following the above numbering 
                 system.



          11. View Equipment History

          This selection will show on the screen the work completed for a 
          selected equipment number between the dates selected.  The 
          completed task numbers, dates done, mechanic and any comments put 
          in the history will be displayed on the screen.  Each completed 
          work order will scroll on the screen about every 10 to 15 seconds.  
          If you wish faster display press the <ENTER> key after each item.
          You may print an identical copy from the print menu.  If you wish 
          just a copy of the screen display, most computers (if printer is 
          on) will print a copy by pressing the <SHIFT> key and the <PrtSc> 
          at the same time.



          12. Scroll Equipment List
      
          This entry will scroll on the screen the list of equipment which 
          is in the equipment database.  It will list in numerical or 
          alphabetical order (sub menu choice) with the name first, then 
          equipment number, type and location. This will continue through 
          the entire list and return to the previous menu.  It is not 
          possible to go backwards.  

          A new item will appear every second and will scroll up the screen. 
          Pressing the <RETURN> key will make the screen scroll faster. 
          Pressing the <Esc> key will exit from the process.  Pressing 
          <Ctrl> and <S> keys at the same time will stop the screen from 
          scrolling until any key is pressed.  Most computers (if printer is 
          on) will print a copy of the screen by pressing the <SHIFT> key 
          and the <PrtSc> at the same time. 



          13. Utility and Setup Building Menu  

          This submenu is used to reindex files that may have been 
          corrupted, change building data which shows on report headings, 
          print PM System documentation and to select colors for screen 
          displays on color monitors.

               A. Fix Database Index Files

          Index files are used to keep database information organized and to 
          find items promptly.  Index files can occasionally get scrambled.  
          This may happen if the computer is shut off improperly, a power 
          failure, improper program shutdown or possibly an undiscovered 
          "bug"  in the program.  It should not be necessary to use this 
          feature unless the program appears to be having problem finding 
          data.  It will not harm anything if done unnecessarily.  It will 
          take a few minutes depending on file size.

               B. Setup Building Data     
          
          This menu item is used to enter the name and other data on 
          the building which will be assigned to this PM System.  Some of 
          the information will be printed as part of the heading on various 
          reports.  This should performed before printing, but may be changed 
          at any later date. 

          Task and document file installation is also displayed in the setup 
          data screen.

          Printing page length setting is made in this menu.  Normally the 
          default value of 66 lines per page (letter size 11" paper - six 
          lines per inch) works best.  See printing menu section for more 
          detail on adjustment of this.   The lines should not normally be 
          larger than the printer default setting.

               C. Print PM System Documentation

          These documents are printed when this menu item is selected.  A 
          description of the items is provided along with other useful 
          information about use of the system.

               D. Color Selections for Screen     

          Selections are made for the colors to display on a color monitor 
          by using numbered selections.  A different number is used for 
          foreground (lettering) and background.  A second color combination 
          is used for highlight areas such as menu light bars and data input 
          areas.  Note: if the same code number is entered for foreground 
          and background the screen will not show properly.  
          
          Normally a monochrome screen will not be affected by the color 
          settings. Occasionally, a monochrome screen with a color video 
          driver card may cause the screen to appear incomplete.  Should 
          this occur and you cannot reset the color settings you will need 
          to copy (refer to your DOS manual) COLORS.MEM from your 
          distribution disk to C:\PM1 or other directory you use PM System 
          on.
          
               E. Locate History Record to Delete

          This utility function is intended to be used to delete equipment 
          history entries made in error or a duplicate entry.  You must know 
          the equipment number and the date of completion to locate the 
          record to delete.  When found, the screen will show the entire 
          record entry.  You will be asked to verify that this is the entry 
          you wish to delete.  In the case of duplicate or more entries the 
          first entry should respond (N) then (Y) to the second and later 
          entries you wish to delete.  The record number of the database 
          history file also shows on the screen.  This is to assist in 
          identifying duplicates.  Duplicate records will not have the same 
          record number.  Observe these closely since the screen updates 
          quickly with duplicates.   The process will continue if more 
          deletions are desired for other equipment numbers.  When you 
          return to the previous menu on completion the screen will show the 
          prior number of records, pack the history file then show the 
          remaining number of records.  The difference is the number 
          deleted.  The equipment history should be checked for accuracy 
          after record deletion.  Packing and reindexing will take time 
          depending on the file size. 

               F.  Task # used in what Equipment

          This feature is to find what other equipment uses a particular 
          task.  Periodically it will be necessary to change or modify a 
          particular task for a piece of equipment.  Since a task may be 
          used for many pieces of equipment the change may not be 
          appropriate for all.  This feature will scroll on the monitor any 
          equipment using that task number.  After verification the task can 
          be modified or a new task added if the changes are not proper for 
          all equipment using that task. 
          
          Pressing the <Enter> key during the search process will speed up 
          the process.  Pressing  <Ctrl> + S keys at he same time will stop 
          the screen.  Press any key to resume.  Pressing <Shift) + <Prt 
          Scr> at the same time sends the current display on the screen to 
          the printer if it is on line. 

               G. Return to Main Menu  
          
          This will return you to the main selection menu. 


          14. QUIT Program and Return to DOS  

          Quit menu selection will close all open files and orderly shut 
          down the program and return you to the DOS prompt in the current 
          directory.  It is best to end the session by this quit procedure.  
          Other methods can corrupt an open file and cause a loss of data.


                              The End



          For additional information contact:

          Murray Enterprise
          Suite 305
          1101 Seafarer Circle 
          Jupiter, Fl. 33477-9066