Zmodem Rev 16.01

                      Copyright (c) 1989, 90, 91, 92, 93
                                     By
                      International TeleCommunications
                              ALL RIGHTS RESERVED



                    Table Of Contents
                            i

Limited Warranty .......................................... Page   1
Distribution Policy And Copyright ......................... Page   1
   Copyright .............................................. Page   1
   -- Test-Drive Distribution Policy -- ................... Page   2
Introduction .............................................. Page   2
Zmodem Command Line Switches .............................. Page   3
   /S ..................................................... Page   3
   -T<d,w,o> .............................................. Page   4
   /R ..................................................... Page   6
   /U ..................................................... Page   6
   /F ..................................................... Page   6
   @ ...................................................... Page   7
   /K ..................................................... Page   7
   /N ..................................................... Page   8
   /P ..................................................... Page   8
   /V ..................................................... Page   8
   /B ..................................................... Page   8
   /L ..................................................... Page   9
      Environment Lock Variable ........................... Page   9
Required Switches ......................................... Page   9
   Your Receive Batch File ................................ Page  10
   Send Batch File ........................................ Page  10
Error Levels .............................................. Page  10
Bbs/Terminal Programs ..................................... Page  10
Serial Drivers And Multi-Port Cards ....................... Page  11
   Intelligent Multi-Port Stargate ........................ Page  11
   Intelligent Multi-Port Arnet ........................... Page  12
   Intelligent Multi-Port Digiboard ....................... Page  12
   Fossil ................................................. Page  13
   Non-Intelligent Serial Cards ........................... Page  13
   Non-Intelligent Digiboards ............................. Page  13
      Setting Up  The Digi Pc/4 Board ..................... Page  14
         Setting The Jumpers .............................. Page  14
         Multi-Board Connectors ........................... Page  15
         Dip Switches ..................................... Page  15
      Setting Up A Digiboard Pc/8 ......................... Page  16
         Setting The Jumpers .............................. Page  16
         Multi-Board Connectors ........................... Page  17
         Dip Switches ..................................... Page  17
      Setting Up The Digiboard Pc/16 ...................... Page  18
   Non-Intelligent Stargate ............................... Page  20
   Non-Intelligent Ast .................................... Page  20
   Non-Intelligent Boca ................................... Page  21
8259 Interrupt Management ................................. Page  21
Zmodem License ............................................ Page  22


         Zmodem          Technical Reference Manual          Page   1

                             Limited Warranty

         This   products provided "as is" without  warranty   of   any
         kind.   The entire risk as to the results and performance  of
         the  program  is assumed by you.  Should  the  program  prove
         defective,  you  (and not International TeleCommunications  )
         assume the entire cost of all necessary  servicing, repair or
         correction.   Further, International TeleCommunications  does
         not warrant, guarantee, or make representations regarding the
         use of, or the results of the use of this program in terms of
         correctness,    accuracy,   reliability,   currentness,    or
         otherwise;  and  you  rely on the program  and  its   results
         solely   at  your own risk.  International TeleCommunications
         cannot  accept   responsibility for system  damage,  loss  of
         profit,   or   any    other    special,    incidental,     or
         consequential damage  resulting  from  the use or   inability
         to  use  this product.

         International  TeleCommunications  DOES   warrant   to    the
         original  licensee of a REGISTERED product that  the  program
         disk(s)  on which  the  program  is  recorded be  free   from
         defects   in materials and workmanship under normal  use  and
         service  for  a period  of  ninety  (90) days from  the  date
         of   delivery   as  evidenced  by  a copy  of  your  receipt.
         International  TeleCommunications' entire liability and  your
         exclusive  remedy  shall  be replacement  of  the   disk  not
         meeting  International TeleCommunications Limited Warranty.

                       Distribution Policy And Copyright

                                   Copyright

              Despite  the method of marketing, Zmodem is not in   the
              public  domain.    It  is the  proprietary  property  of
              International  TeleCommunications.    All   rights   are
              reserved.      Copying,  duplicating,     selling     or
              otherwise    distributing    this product    except   as
              expressly   permitted  in the   TEST-DRIVE  Distribution
              Policy  below   is a  violation  of  the  Law.  However,
              we grant you  the right,  in fact encourage you  to make
              and  distribute as  many copies   of   this   TEST-DRIVE
              version   as   you    wish,   using    any    acceptable
              medium  of exchange, with the following provisions:











         Zmodem          Technical Reference Manual          Page   2

                     -- Test-Drive Distribution Policy --

          1.   Please feel free to distribute this TEST-DRIVE version as
               often as you like, to any interested parties.
          2.   Please do not distribute the program without all of its
               original related files, addendum files, and documentation.
          3.   Please obtain our written permission prior to distribution
               with any "Bundled" software packages.
          4.   Please do not accept payment for the program; a copying fee of
               $10.00 per diskette may be charged when distributed by a
               non-profit user-group.
          5.   Please do not alter the program or documentation in any
               manner.
          6.   NOTE - Individuals, groups, vendors, or other software
               distribution companies which market diskettes containing
               the TEST-DRIVE programs for profit must obtain written
               permission from International TeleCommunications prior to
               distribution.

                                    Introduction

              Zmodem.exe  is  a  full  function  stand  alone   Zmodem
              protocol driver.

              Zmodem.exe offers exceptional fast Zmodem file transfers
              and   it  fully  supports  ZSKIP,   Resume   interrupted
              Transfers,  32  and  16 bit CRC  error  detection,  8259
              interrupt  management, and a wide range  of  intelligent
              and  non-intelligent serial cards (also  support  Fossil
              and has an internal driver).

              Zmodem.exe  is  one  of the fastest  (we've  been  told)
              Zmodem drivers you are likely to find.

              It  is  the only stand alone zmodem driver  that  offers
              support for such a WIDE range of serial card as well  as
              8259 interrupt managment (faster transfers).

















         Zmodem          Technical Reference Manual          Page   3

                          Zmodem Command Line Switches

         Each  switch must be preceded by either a forward slash   '/'
         or a dash '-'.

         O   Should Always Be Used With Osiris BBS.
         V   Engage ANTI-PMS Screen, For Use With Osiris BBS Only.
         S   Use RTS flow control.
         K   Keep Aborted Transfers.
         @   Use Send Control File.
         U   Place Uploads In This Directory.
         R   Receive Files
         N   Osiris Node Number, Osiris BBS Only.
         L   Lock Serial Rate.
         B   Connect Baud Rate.
         P   Serial Port.
         F   Send These Files.
         T   Time Slicing.


                                         /S
                                9600 bps and higher
                                   Slow Computer

              If   you have a high speed modem you MUST have a   16550
              Uart. Attempting  to run at high speeds without one will
              result  in errors.

              You  might sneak by without a 16550 if you have a   fast
              386, or 486.

              A  good way to check is by watching your  transfers.  If
              you  are under  an  error correcting connect,  then  you
              should   almost  NEVER  get an  error  reported  by  ANY
              transfer protocol.

              Getting   errors  reported (by ANY  transfer   protocol)
              while under  MNP  or  ARQ  can only mean.

              1.  The protocol goofed (Zmodem doesn't goof).
              2.  You   may  have another   application   interfering
                  with serial interrupts.
              3.  You have hardware problems.
              4.  You do not have a 16550 Uart.


              If   you have a 16550 installed, then you can  rule  out
              number four  and that leaves you with two or three.

              If you have a multi-tasker or a network and a 16550 then
              the network and/or multi-tasker is stealing to much time
              and  the 16550 fifo's are being over run.


         Zmodem          Technical Reference Manual          Page   4

              If you have a 16550 and NOTHING else that may  interfere
              with  the   serial  interrupts,  then  you   more   than
              likely  have hardware problems.

              If  it is option 4, buy one and install it. 16550  uarts
              cost about $20.00 and are WELL worth it.

              Unless   you   have  hardware problems, I can  HELP  you
              by  kicking   in RTS flow control. This does  slow  down
              transfers,  but  it  is better to slow  them  DOWN  than
              experience errors.

              If   you have to, add /S to the command line.  But  only
              use   it if  you  HAVE  to and only until you  fix   the
              CAUSE  of  the problem.

                                   -T<d,w,o>

              This  governs  the  TYPE of time  slicing  the  protocol
              driver will use. Leaving off the -T switch means no time
              slicing.

              D= Desqview or Topview
              W= Windows
              O= OS-2

              E.g. -TD, -TW, -TO

              While time slicing does reduce the drain on your CPU  it
              may,  depending  on  the  multitasker  (OS-2,   Windows,
              Topview, or Desqview) and your hardware, greatly  reduce
              transfer rates.

              Despite   the  term  "Multitasking",   multitasking   is
              impossible using a single CPU. The CPU can only  process
              a single instruction (2 integer instructions if the  new
              Intel  P5  chip is used) at once.  Multitasking  with  a
              single CPU is nothing more than quickly swapping in  and
              out  programs giving each a short period of time to  run
              before swapping in another one.

              For  instances,  when  Windows  swaps  away  it  freezes
              everything in that windows and this includes ANY  device
              drivers  or interrupt service routines. If you  use  the
              internal serial driver, it to is frozen and cannot  send
              data that may be in the transmit buffer.








         Zmodem          Technical Reference Manual          Page   5

              While all multitaskers do this, some are more  efficient
              than  others. Some will give interrupt  services  higher
              priority  than  other tasks and allow them to  use  much
              more CPU time. Even if the application only gets  access
              to  the CPU once ever oh . . . 9 clock  tics,  interrupt
              routines used by that application may get access to  the
              CPU every 2 clock tics. This is sometimes referred to as
              multi-threading.

              There  are  conditions when it doesn't  matter  how  the
              multitasker  works.  For instances,  intelligent  serial
              cards.

              If  you  have  an intelligent serial  card,  it  handles
              sending  the data and the multitasker does not  stop  it
              from doing so by swapping out the window. In this  case,
              always use Time slicing.

              Fossil drivers can sometimes get around this if they are
              loaded    BEFORE   the   multitasker.   However,    some
              multitaskers will not allow dual access, from  different
              windows, to the fossil.

              To determine if your system works better with or without
              time slicing, testing is the only way.

              Do uploads and downloads using time slicing and  without
              using  time slicing. If you run a single  node,  compare
              the transfer rates.

              If you run multiple nodes, it gets more involved.  After
              getting  the  first set of figures,  repeat  the  entire
              process but make sure you have someone doing the uploads
              and downloads on ALL nodes at once. THEN compare ALL the
              transfer  rates. Doing multiple transfers at  once  DOES
              effect  the  outcome. You may find that  while  transfer
              rates drop drastically with a single transfer, they  may
              actually go up when you have multiple transfers going at
              once.

              When you are doing the tests, keep in mind that transfer
              rates WILL vary, but only a little bit. Look for the big
              differences and don't worry about 1 to 3 percent.











         Zmodem          Technical Reference Manual          Page   6

                                         /R
                                   Receive Files

              When   I  encounter  this switch, I  will  go   directly
              to receive files mode.

              You   MUST  make sure that /R is the  very  last  switch
              used.  If it  is not, then you will be missing important
              command  line switches.

                                         /U
                       Place inbound files in this directory

              You   can  direct Zmodem to place inbound  files  in   a
              specific directory by using the /U command.

              I will verify the directory you specified, so make  sure
              it is a VALID directory.

              You   cannot use Drive  designators or ROOT  directories
              with the /U switch.

              For   instance,    /UC:  or  /UC:\. C:  and  C:\  aren't
              listed in the FAT and I cannot validate them.

              Make   sure  you do NOT use a trailing   backslash  with
              the   /U path, I'll ADD a backslash when I concate   the
              file name with the path you specified.

              E.g., d:\uploads\ is NOT valid, it should be  d:\uploads
              Here    is   a   sample   of   a   GOOD   /U    setting:
              /UC:\TELIX\UPLOADS

                                         /F
                                  Send These Files

              When   I   find  the  /F,  I  will  immediately    begin
              sending.

              YOU   should  make  sure that you have listed  ALL   the
              OTHER commands  before using /F. Make sure you place ONE
              blank  space  between  the  /F  switch  and  the   first
              filename.

              Place one blank space between ADDITIONAL files names, if
              you  have  specified more than one. You  may  include  a
              drive and path with the file names.







         Zmodem          Technical Reference Manual          Page   7

              E.g.,  c:\uploads\file1.exe is a valid file name.

              You can use the DOS wild card characters '?' and '*'.  I
              will  expand  those  characters to match  any  file   in
              that directory.

              I   do   not place limits on the number of files    that
              can  FOLLOW  /F,  but  DOS DOES! DOS    restricts    the
              number  of characters you can place  on  a command  line
              to 128.

              DOS   also limits you to nine batch parameter   symbols,
              %1 through %9.

                                         @

              I'll assume USE this file as  a  "SEND"  control file.

                   e.g. -@D:\OSIRIS\SEND2.CTL

              Since   DOS forces me to work with 128 and   nine  batch
              variables,  using  @  to  send   file   names   is   the
              preferred method of passing the names.

              The  information following  @ is the full  drive,  path,
              and file name of a TEXT file.

              I   do  not place restrictions on the  number  of  files
              that you  can  have listed and you can include the  full
              drive,   path,  along  with name of the  file.  You  can
              include DOS wild card characters, '?' and '*'.

                   E.g., C:\PCboard\Tlx310a.exe is valid.
                   E.g., C:\Telix\*.arj is valid.

              Each line in the file must contain only ONE filename and
              has to end with the DOS CR/LF sequence.

              Sample Send Control File:

              C:\DRIVERS\MPT110.ZIP
              C:\DRIVERS\TMOD610.ARJ
              C:\DRIVERS\ZMOD*.*

                                         /K
                               Keep Aborted Transfers

              If   you  drop  carrier or time out, I will  delete  the
              aborted file.





         Zmodem          Technical Reference Manual          Page   8

              If  you're  using Zmodem with a TERMINAL program,   then
              you  will  WANT to keep the file. Adding   /K   to  your
              Zmodem command line tells  ME  you  want to keep aborted
              transfers.

                                         /N
                                    Node Number

              If    you're  running OSIRIS, you can include   /Nx   on
              the command line.

              E.g., /N1  /N2  /N3  . . .  /N255

              Add /N*N to your protocol command lines.

              I'll    display the callers name, city, and  state    at
              the bottom of the screen, useful when you walk into  the
              room  and WONDER who  is currently downloading what.

                                         /P
                                      Com Port

              You   have to tell me which serial port your  caller  is
              ON  by including /Px on the command line.

              E.g., /P1  /P2  /P3  . . .  /P8

                                         /V
                                Engage PMS Screening

              This   can ONLY be used on an OSIRIS system. This  tells
              me   to allow  Osiris  to monitor the serial  port  with
              its   ANTI-PMS  screening  system.

                                         /B
                                 Connect Baud Rate

              You have to provide the TRUE CONNECT RATE, most  of  the
              time this is the same as your SERIAL baud rate.

              e.g. /B1200  /B2400  /B9600

              If you have a high speed modem with a FIXED serial rate,
              the CONNECT  rate may not always be the same, but   that
              doesn't  change  anything. You still  should  pass   the
              TRUE connect  rate and not the SERIAL rate.








         Zmodem          Technical Reference Manual          Page   9
                                      /L
                                   Lock Rate

              This tells me you have a LOCKED Serial Port.

              E.g.

              /L38400
              /L57600
              /L19200
                                Environment Lock Variable

                   You can define an  environment    variable   called
                   COMx=BaudRate.  Replace  x  with the   serial  port
                   number   and BaudRate with the  LOCKED  baud rate.

                   e.g. COM1=19200

                   Do  NOT add blank spaces or comma's. Make sure  you
                   use  Upper Case.

                   You can do that in the AUTOEXEC.BAT file or in  the
                   BATCH file you use to CALL Zmodem.

                   e.g.

                   cls
                   SET COM2=38400
                   Zmodem -B%1 -P%2 -R
                   Exit
                               Required Switches

         Each  Zmodem installation will require TWO switches. It  does
         not matter  what type of BBS/Terminal program you're going to
         use.

         It does not matter if it is SEND or RECEIVE.

         /Bxxxxx and /Px

         You  should  replace   xxxxx  in  the /B  with   the  correct
         CONNECT rate or 0. Replace the x in /P with  the correct  COM
         port.

         /B9600 /P2  (Connect Rate 9600, COM 2)
         /B2400 /P1  (Connect Rate 2400, COM 1)

         It is not important WHERE you place the switches, as long  as
         they are NOT the LAST switch used.






         Zmodem          Technical Reference Manual          Page  10

                              Your Receive Batch File

              Your   Receive   Batch  file  will  require   only   one
              additional switch, /R.

              It MUST be the very last switch on the command line.

              The  MINIMUM command line for receiving would be:

              Zmodem /B2400 /P1 /R

              2400  and  1 can  be supplied by DOS  batch   variables,
              e.g. Zmodem /B%1 /P%2 /R

              Other   optional   switches,  /U  . . .  /K  etc.,  must
              be included BEFORE the /R switch.

                                  Send Batch File

              Your  "SEND" batch file only "requires"  ONE  additional
              switch, /F or -@.

              The MINIMUM command line for sending a file:

              /B2400 /P2 /F FILENAME#1 FILENAME#2 FILENAME#3

              or

              /B2400 /P2 -@CTRL_NAME

              2400,   2,  FILENAME#1, FILENAME#2,   FILENAME#3,   etc.
              may  be supplied by  DOS  batch variables.

              E.g., Zmodem /B%1 /P%2 /F %3 %4 %5 %6 %7 %8 %9

                                Error Levels

         I  will  exit,  following the transfer, with  an error  level
         of 0  or  1.

         Zero,  0,  indicates  a  successful  transfer  and  one,   1,
         indicates an error.

                             Bbs/Terminal Programs

         I  use  a very basic command line setup  which  should  allow
         Zmodem to be used by almost any program. I do NOT expect that
         it will work with EVERYTHING.

         If  you are using something that it will just flat  not  work
         with then send it to me. You  can upload it or mail it and  I
         will attempt to find  out why.


         Zmodem          Technical Reference Manual          Page  11


                      Serial Drivers And Multi-Port Cards

         Zmodem  supports  Intelligent multi-port serial  cards,  non-
         intelligent  multi-port  serial cards, fossils,  and  has  an
         internal  serial driver (fastest method of dealing  with  the
         serial port).

         Zmodem  defaults to the  internal high speed driver, but  you
         can  change the driver type by using the use the  environment
         variable COMDRV, ONLY AVAILABLE IN REGISTERED VERSION.

         COMDRV=FOSSIL

         {Intelligent Serial Cards}

         COMDRV=STARGATE
         COMDRV=DIGI
         COMDRV=ARNET

         {Non-Intelligent Serial Cards}

         COMDRV=NDIGI
         COMDRV=NSTARGATE
         COMDRV=AST
         COMDRV=BOCA

                          Intelligent Multi-Port Stargate

              Load  the  Star  Gate device driver,  ACL.SYS,  in  your
              config.sys.  When  your  system  boots,  run  ACLDL   to
              download your code.

              Zmodem  defaults to the 16 port with the I/O address  of
              0x200  at D000:000 starting at COM 5. If  your  hardware
              doesn't  match this, you'll need to create a  SERIAL.CFG
              control file in SAME directory that houses Zmodem.Exe or
              re-configure your stargate board.

              SERIAL.CFG for STARGATE Intelligent Multi-port Cards:

              The  first line of this file should contain 5  settings,
              separated by a single space.

              BOARD BOARD_SEGMENT PORT FIRST_PORT_NUMBER NUMBER_OF_PORTS

              Board:  Stargate  board to use (0 - 3).  This  tells  us
              which board you want to use.

              Board_segment:  Segment of the Star Gate board's  memory
              window.



         Zmodem          Technical Reference Manual          Page  12

              Port: The Address of the board's I/O latch.

              First_port_number:  Name given to the first port on  the
              board  (1,2,3,etc). The designation of the  port  number
              for the first port on the board is arbitrary.

              Number_of_ports: Number of ports on the board.

              Example:

              {SERIAL.CFG}

              0 0xd000 0x300 4 8

                            Intelligent Multi-Port Arnet

              When  you  load  the Arnet device  driver,  port  number
              assignments  are printed on the display. These  are  the
              number you'd use for the zmodem serial port parameter.

              Use  the /N5 switch on ASP.SYS. If you do not  use  this
              switch,  attempts to set handshaking will result  in  an
              error.

              The  files, box.bin and fastbios.bin, supplied with  the
              Arnet boards, must be in your root directory for this to
              work  properly. These files are used by ASP.SYS at  boot
              time.

                          Intelligent Multi-Port Digiboard

              Run  the Digiboard config. program (XIDOSCFG.EXE)  which
              asks you for the desired port numbers. Also, install the
              device  driver  supplied with the board. You  must  also
              complete the following steps:

              1. Set up the board NOT to use interrupts.

              2. Setup to support INT 0x14 for most drivers and  EBIOS
              for the XIDOS5 driver.

              3.  Change  the configuration to enable ports,  if  your
              driver  requires  it. Make sure "NONE" is  the  selected
              handshaking for ports.

              4.  Reboot  your  system. During the  boot,  the  driver
              should   respond   with   the   message    "successfully
              initialized board".






         Zmodem          Technical Reference Manual          Page  13

                                       Fossil

              Any  fossil  driver will work.  See  documentation  that
              comes with the fossil driver for details.

                            Non-Intelligent Serial Cards

              Non-Intelligent  boards  frequently  come  with   device
              driver  software. This software provides INT 14H  access
              to  the  UART on the board.

              Do N O T use this software with Zmodem. Zmodem  accesses
              the  hardware directly without the use of  any  external
              drivers.

                             Non-Intelligent Digiboards
                                   (COMDRV=NDIGI)

              The  Digiboard  DigiCHANNEL PC/16, PC/8,  and  PC/4  are
              multi-channel  communications  boards  that  provide   a
              serial  communications  subset for  IBM  and  compatible
              computers.  Each  of  the  boards  supports  full  modem
              control  on  each port. Up to two DigiCHANNEL  PC/16,  4
              PC/4  or  PC/8  boards  can be  installed  on  a  single
              computer providing up to 32 additional ports.

              To   insure  connection  flexibility,  3   options   are
              available:

              1. An I/O mate connection box with external connections.

              2. An octopus cable with four or eight DB25 connectors.

              3.  An  RJ45  connection box with  eight  RJ45  or  RJ11
              connectors.

              The   DIGI  PC/4  and  PC/8  addressing  and   interrupt
              selection  are flexibly and not limited to preset  IRQs,
              address,  or  address  ranges.  The  user  may  set  DIP
              switches to select different status registers (DS1)  and
              I/O  port  addresses  (DS2 - DS9), as  well  as  setting
              jumpers to select either one or two interrupts.

              The DIGI PC/16 offers hardware jumpers for selecting  an
              interrupt  and  a PAL with preset I/O  port  and  status
              register addresses.

              There  are  six possible system interrupts that  may  be
              selected for the DIGI PC/X board: IRQ2 - IRQ7.  However,
              IRQ3  and IRQ4 are commonly reserved for  standard  COM1
              and COM2 serial hardware.



         Zmodem          Technical Reference Manual          Page  14

              If  multiple  boards are installed in one  system,  each
              board is given a unique I.D. such as board 0 and board 1
              by setting the board ID jumpers. The status register and
              IRQ  of  ALL boards can be set to the same  values,  and
              the  boards are daisy changed with special  cables  that
              pass  signals  from the interrupt sequence.  When  daisy
              chained,  the  boards are treated like  one  board.  The
              boards  can  also be setup  independently  on  different
              interrupts.

                            Setting Up  The Digi Pc/4 Board

                   The  COM/4  board  has 4  serial  interface  ports,
                   individual address and interrupt settings, and  two
                   8 bit status ports. It is preset and tested at  the
                   factory  at IRQ3; address 100, 108, 110,  and  118;
                   status port ON, and set to address 140. Check  your
                   system for any peripherals that may use either  the
                   preset  interrupt  or  addresses. If  there  is  no
                   conflict,  you can install the COM/4 board  without
                   modifications.  However,  if  you  need  to  change
                   settings, details are provided below.


                                     Setting The Jumpers

                        Jumpers  1-4 are used to choose the  interrupt
                        for each individual port.

                        For odd interrupts IRQ3, IRQ5, or IRQ7 set the
                        shunt   between   pins  1  and   2   for   the
                        corresponding jumper.

                        For  even interrupts IRQ2, IRQ4, or  IRQ6  set
                        the  shunt  between  pins  2  and  3  for  the
                        corresponding  jumper. Ports 1 through  4  map
                        with jumpers 1-4 respectively.

                        J9  and  J10  are used to  set  the  board  ID
                        number.  The  setting will depend  upon  which
                        board  it represents. If more than  one  board
                        is used in the system, each board must be  set
                        to  a unique identification number. The  first
                        board  should always be set to 0. If you  have
                        daisy  changed more than one  board, you  will
                        use  the  board #s 1-3. The  settings  are  as
                        follows:







         Zmodem          Technical Reference Manual          Page  15


  Board #            J9                       J10
  ------------------------------------------------------------
    0        between pins 2 and 3     between pins 1 and 2
    1        between pins 2 and 3     between pins 1 and 2
    2        between pins 1 and 2     between pins 2 and 3
    3        between pins 1 and 2     between pins 1 and 2

                        J85  through  J90  are used  to  select  which
                        interrupt  the  board  will  use.  Set   these
                        jumpers as follows:

                         IRQ#               Jumper#
                         ---------------------------
                         2                  J90
                         3                  J85
                         4                  J89
                         5                  J86
                         6                  J88
                         7                  J87

                                    Multi-Board Connectors

                        P2 and P3 are jumpers used to daisy chain  two
                        boards  together  using  a  special  DigiBoard
                        cable. If you are only using one board,  place
                        a  shunt  on  pins 2 and 3 of  both  of  these
                        jumpers. This is VERY important. Without  this
                        shunt, no interrupts will be received.

                                         Dip Switches

                        Address line A3 through A9 determine the  port
                        address  and  are logic-selected  on  the  DIP
                        switches  for  each  port  for  switches   DS3
                        through  DS5. The DIP switches for  each  port
                        can  be set to any NON-CONFLICTING address  in
                        the I/O map from 0000H to 03FFH.

                        Switch positions 1-7 switch set the address of
                        each port. Position 1 corresponds to A9, 2=A8,
                        3=A7,  4=A6, 5=A5, 6=A4, 7=A3. Position  8  of
                        each  switch enables or disables the port.  We
                        recommend  assigning consecutive port  numbers
                        for easy of use.

                        The  following table lists  suggested  address
                        and   switch   settings  for   the   DigiBoard
                        DigiCHANNEL PC/4 board:





         Zmodem          Technical Reference Manual          Page  16


   Port#   Base    Dip                  Switch Settings
           Address Switch   1    2    3    4    5    6    7    8
   ----------------------------------------------------------------
    Status 140H    DS1      ON   OFF  ON   OFF  ON   ON   ON   ON
    port
   ----------------------------------------------------------------
     1     100H    DS2      ON   OFF  ON   ON   ON   ON   ON   ON
     2     108H    DS3      ON   OFF  ON   ON   ON   ON   OFF  ON
     3     110H    DS4      ON   OFF  ON   ON   ON   OFF  ON   ON
     4     118H    DS5      ON   OFF  ON   ON   ON   OFF  OFF  ON

                        Position   (Switch  setting  8)   enables   or
                        disables the port where ON = enabled.


                              Setting Up A Digiboard Pc/8

                   The   PC/8  board  has  eight   individual   ports,
                   individual address and interrupt settings and two 8
                   bit status ports.

                   The PC/8 board is preset and tested at the  factory
                   using  IRQ3; address 100, 108,110, 118,  120,  128,
                   130,  and  138; status port ON and set  to  address
                   140.

                                     Setting The Jumpers

                        Jumpers J1-J8 are used to choose the interrupt
                        for  each  port.  For  odd  interrupt  numbers
                        including  IRQ3, IRQ5, or IRQ7, set the  shunt
                        between  pin  1 and 2  for  the  corresponding
                        jumper.

                        For  even  interrupts, set the  shunt  between
                        pins  2 and 3. All ports HAVE to use the  same
                        interrupt to work properly. Ports 1 through  8
                        map to jumpers 1-8 respectively.

                        J9  and  J10  are used to  set  the  board  ID
                        number.  The  setting will depend  upon  which
                        board  it represents. If more than  one  board
                        is used in the system, each board must be  set
                        to  a unique identification number. The  first
                        board  should always be set to 0. If you  have
                        daisy  changed more than one  board, you  will
                        use  the  board #s 1-3. The  settings  are  as
                        follows:





         Zmodem          Technical Reference Manual          Page  17

  Board #            J9                       J10
  ------------------------------------------------------------
    0        between pins 2 and 3     between pins 1 and 2
    1        between pins 2 and 3     between pins 1 and 2
    2        between pins 1 and 2     between pins 2 and 3
    3        between pins 1 and 2     between pins 1 and 2

                        J85  through  J90  are used  to  select  which
                        interrupt  the  board  will  use.  Set   these
                        jumpers as follows:

    IRQ#               Jumper#
    ---------------------------
    2                  J90
    3                  J85
    4                  J89
    5                  J86
    6                  J88
    7                  J87

                                    Multi-Board Connectors

                        P2 and P3 are jumpers used to daisy chain  two
                        boards  together  using  a  special  DigiBoard
                        cable. If you are only using one board,  place
                        a  shunt  on  pins 2 and 3 of  both  of  these
                        jumpers. This is VERY important. Without  this
                        shunt, no interrupts will be received.

                                         Dip Switches

                        Address line A3 through A9 determine the  port
                        address  and  are logic-selected  on  the  DIP
                        switches  for  each  port  for  switches   DS3
                        through  DS5. The DIP switches for  each  port
                        can  be set to any NON-CONFLICTING address  in
                        the I/O map from 0000H to 03FFH.

                        Switch positions 1-7 switch set the address of
                        each port. Position 1 corresponds to A9, 2=A8,
                        3=A7,  4=A6, 5=A5, 6=A4, 7=A3. Position  8  of
                        each  switch enables or disables the port.  We
                        recommend  assigning consecutive port  numbers
                        for easy of use.

                        The  following table lists  suggested  address
                        and   switch   settings  for   the   DigiBoard
                        DigiCHANNEL PC/8 board:






         Zmodem          Technical Reference Manual          Page  18

   Port#   Base    Dip                  Switch Settings
           Address Switch   1    2    3    4    5    6    7    8
   ----------------------------------------------------------------
    Status 140H    DS1      ON   OFF  ON   OFF  ON   ON   ON   ON
    port
   ----------------------------------------------------------------
     1     100H    DS2      ON   OFF  ON   ON   ON   ON   ON   ON
     2     108H    DS3      ON   OFF  ON   ON   ON   ON   OFF  ON
     3     110H    DS4      ON   OFF  ON   ON   ON   OFF  ON   ON
     4     118H    DS5      ON   OFF  ON   ON   ON   OFF  OFF  ON
     5     120H    DS6      ON   OFF  ON   ON   OFF  ON   ON   ON
     6     128H    DS7      ON   OFF  ON   ON   OFF  ON   OFF  ON
     7     130H    DS8      ON   OFF  ON   ON   OFF  OFF  ON   ON
     8     138H    DS9      ON   OFF  ON   ON   OFF  OFF  OFF  ON

                        Position   (Switch  setting  8)   enables   or
                        disables the port where ON = enabled.


                             Setting Up The Digiboard Pc/16

                   This  board  is, in most respects,  the  functional
                   equivalent of two DigiChannel PC/8 boards operating
                   together.  The  PC/16 features the same  method  of
                   interrupt  sequencing in hardware, sparing the  CPU
                   from having to POLL the individual ports. While the
                   PC/8  has several DIP switches and jumpers to  set,
                   the PC/16 has all addresses set in the hardware.

                   Default values are set at IRQ3, UART base address =
                   100h, and status register = 140H.

                   To install the board, set the jumpers including the
                   board  selection  jumper  and  the  IRQ   selection
                   jumper.

                   Check other peripherals for conflicts with the pre-
                   set addresses. If a conflict occurs, you will  HAVE
                   to change the I/O port on the OTHER device.

                   Connector  Jumper  P3 is used to  daisy  chain  two
                   boards together using a special Digiboard cable. If
                   you are only using one board, place a shunt on this
                   jumper.  It  is located  in  the  upper  right-hand
                   corner of the board.

                   Interrupt  Jumper J1 through J6 are used to  select
                   which interrupt the board will use. Set the jumpers
                   as follows





         Zmodem          Technical Reference Manual          Page  19

                    IRQ#           Set the shunt at Jumper #
                    ----------------------------------------
                    2                       J1
                    3                       J2
                    4                       J3
                    5                       J4
                    6                       J5
                    7                       J6


                   Set the BOARD I.D. Jumper J7 is used to number  the
                   board if you have more than one cascaded.

                   For  Board #0 set the shunt between pins 2  and  3.
                   For Board #1 set the shunt between pints 1 and 2.


              Telling Zmodem about the non-intelligent digiboard board
              requires  you  to create a SERIAL.CFG file in  the  same
              directory that houses Zmodem.exe.

              The  first  line  of this  file  contains  four  fields,
              separated by a single space.

<IRQ> <Shared_port_status> <First_Port_Number> <Port_Count>

              <IRQ> The IRQ line used by this board 3-7.

              <Shared_port_status>  Address  of the  status  port  (in
              HEX).

              <First_Port_Number> Number of the first port. This is an
              arbitrary port number.

              <Port_Count> Total number of ports on the board. Be sure
              to  put the correct total number of ports and  NOT  just
              the  number of ports you'll be USING. E.g. 4, 8, 16,  or
              32.

              The  Second  line  should contain  the  PORT  ADDRESSES,
              separated  by a single space, for each port on the  card
              (In HEX). If you defined Port_Count as 4, then you would
              have FOUR fields on this line. If you defined port count
              as 16 then Sixteen fields.

              Example, four port digiboard with default settings using
              COM5 as the first port number.

              {SERIAL.CFG}

              3 0x140 5 4
              0x100 0x108 0x110 0x118


         Zmodem          Technical Reference Manual          Page  20

                              Non-Intelligent Stargate
                                 (COMDRV=NSTARGATE)

              Telling Zmodem about the non-intelligent Star Gate board
              requires  you  to create a SERIAL.CFG file in  the  same
              directory that houses Zmodem.exe.

              Serial.cfg  contains  a  single  line  with  3   fields,
              separated by a single space.

              IRQ FIRST_PORT_NUMBER FIRST_PORT_ADDRESS

              IRQ  The IRQ line used by this board (2-7).

              FIRST_PORT_NUMBER  Number of the first port. This is  an
              arbitrary port number.

              FIRST_PORT_ADDRESS   Address (In HEX) of the first  UART
              on the board.

              Example:

              {SERIAL.CFG}

              3 5 0x180

                                Non-Intelligent Ast
                                    (COMDRV=AST)

              Telling  Zmodem  about  the  non-intelligent  AST  board
              requires  you  to create a SERIAL.CFG file in  the  same
              directory that houses Zmodem.exe.

              Serial.cfg  contains  a  single  line  with  3   fields,
              separated by a single space.

              IRQ FIRST_PORT_NUMBER FIRST_PORT_ADDRESS

              IRQ  The IRQ line used by this board (2-7).

              FIRST_PORT_NUMBER  Number of the first port. This is  an
              arbitrary port number.

              FIRST_PORT_ADDRESS   Address (In HEX) of the first  UART
              on the board.

              Example:

              {SERIAL.CFG}

              3 5 0x1a0



         Zmodem          Technical Reference Manual          Page  21

                                Non-Intelligent Boca
                                   (COMDRV=BOCA)

              Telling  Zmodem  about the  non-intelligent  BOCA  board
              requires  you  to create a SERIAL.CFG file in  the  same
              directory that houses Zmodem.exe.

              Serial.cfg  contains  a  single  line  with  4   fields,
              separated by a single space.

              IRQ FIRST_PORT_NUMBER PORT_COUNT FIRST_PORT_ADDRESS

              IRQ  The IRQ line used by this board (2-7).

              FIRST_PORT_NUMBER  Number of the first port. This is  an
              arbitrary port number.

              PORT_COUNT Total number of ports on the board (4 or 8).

              FIRST_PORT_ADDRESS   Address (In HEX) of the first  UART
              on the board.

              Example:

              {SERIAL.CFG}

              3 5 4 0x180

                           8259 Interrupt Management

         The interrupt manager automatically assigns priority to  each
         of  the systems interrupts. The timer counter, keyboard,  and
         cascaded interrupt all have higher priority than the UART.

         To  gain  the  MAXIMUM  throughput  (especially  when  multi-
         tasking),  we suggest that you allow Zmodem to alter the  IRQ
         manager so the UART has the highest priority.

         You can do this using the environment variable 8259=IRQ{1-7}

         Examples:

         8259=IRQ4
         8259=IRQ3

         Keep  in  mind that only ONE of the uarts  (in  a  multi-uart
         environment) can be switched to the HIGHEST priority,  select
         the one that contains the fastest modem.

         Intelligent Multi-port cards use a single shared IRQ. This is
         the one you want to give highest priority to.



         Zmodem          Technical Reference Manual          Page  22

                               Zmodem License

                             Please Read Carefully

         WHEN you register Zmodem, you indicate your   acceptance   of
         these terms.

         1. License Grant. International TeleCommunications will grant
         you  a non-exclusive license to use one copy of Zmodem  on  a
         single  computer or on a single terminal connect to a  single
         computer. Neither concurrent use on two or more computers nor
         use  in a local area network is authorized  without  advanced
         written  consent of International TeleCommunications and  the
         payment of additional license fees.

         2. International TeleCommunications' Rights. You  acknowledge
         and   agree   that  Zmodem  is  a  proprietary   product   of
         International   TeleCommunications,   protected   under   U.S
         copyright  law,  international treaty provisions,  and  trade
         secret laws of general applicability. You further acknowledge
         and  agree  that all rights, title, and interest  in  and  to
         Zmodem    are   and   shall   remain    with    International
         TeleCommunications.

         3. Other Restrictions. You may not lease or rent Zmodem.  You
         may not disassemble, decompile, or reverse engineer Zmodem.

         4.   Zmodem   is  licensed  "AS   IS,"   and    International
         TeleCommunications disclaims any and all warranties,  whether
         express  or  implied,  including  (without  limitation)   any
         implied  warranties  of  merchantablity  or  fitness  for   a
         particular purpose.

         5. Limitation of Liability. International TeleCommunications'
         cumulative  liability to you or any other party for any  loss
         or  damage  resulting from any claims,  demands,  or  actions
         arising out of or relating to this agreement shall not exceed
         the license fee paid to International TeleCommunications  for
         the   use  of  Zmodem.  In  no  event   shall   International
         TeleCommunications  be liable for any  indirect,  incidental,
         consequential, special, or exemplary damages or lost profits,
         even if International TeleCommunications has been advised  of
         the possibility of such damages. Some states do not allow the
         limitation  or  exclusion  of  liability  for  incidental  or
         consequential  damages, so the above limitation or  exclusion
         may not apply to you.

         6.  Governing Law. This license agreement shall be  construed
         and  governed  in accordance with the laws of  the  State  of
         Missouri.




         Zmodem          Technical Reference Manual          Page  23

         7. Severability. Shall any term of this license agreement  be
         declared  void  or unenforceable by any  court  of  competent
         jurisdiction,  such declaration shall have no effect  on  the
         remaining terms hereof.