--------------------------------------------------------------------------                                  
                                  DX OnLine
                               KD5ON Software
                                 Steve Brown
                               2940 Koop Road
                              Lima, Ohio 45807
                               (419) 999-2187
-------------------------------------------------------------------------

DX OnLine is an antenna bearing/range, signal propagation system that runs 
on an IBM or compatible personal computer.

It is a result of an effort that started in 1989 and has more than 1,500 
hours of effort in it. (Probably more if you ask my XYL.)

Because of the complexity of the programs, I have targeted people with
computers beyond the basic 8088 with a Hercules monitor scenario.

DX OnLine requires a minimum of an 80286 with 640K and a color EGA or VGA 
monitor and a hard disk. I will warn you that even on an 80286 some 
functions such as the 24 hour MUF prediction will seem slow. Even some 
older 80386's will take a drag on the 24 hr. I use a 386-20 with a 
co-processor and it hums right along. 80486's work great.

It is my opinion that more and more hams are progressing to more advanced 
systems so I decided not to sacrifice features to accommodate older systems.

Although it is not required, a mouse (Microsoft compatible) is highly
recommended. What I feel is one of DX OnLine's nicest feature, the "ROAM" 
mode requires a mouse.

Some of DX OnLine's features include:

World Map:   The primary display of DX OnLine is a full color map
             of the world.

Browse mode: As you move the mouse around on the world map, the 
            antenna   bearing and range is constantly updated.
             While in browse mode, if you click a mouse button, a window
             pops up with the current signal propagation prediction.
             For fine movement of the cursor, you may use the arrow keys.
            
Prompt mode: This mode prompts you for a specific prefix or QTH 
             (city,   state, country,etc.). The search is such is that it 
             looks for occurrences of the select parameters keyed.

             I like this as I don't have to remember how to spell places
             like "KYRGYZSTAN". You could key "KY","YRG","STAN",
             etc. and it would find it. Note that keying "STAN" would 
             also find "TURKMENISTAN", STANLEYVILLE, etc.

             One thing to keep in mind is that the system has a limit in
             that it only likes 250 matches for the prompted data. So
             don't key in "W" for a prefix with no limiting QTH prompt.
~~~~
                               DX OnLine

Print capability: You may print a listing a DX bearings from your 
             home QTH to all locations in the target data base.

Temporary home QTH override: you may temporarily override your home QTH 
             data to allow you to demonstrate DX OnLine for someone else 
             from their own home QTH or to print a DX Bearing listing 
             for them.

Gray Line:   A continually (every 5 minutes) updated representation 
             of the "Gray Line" or day/night terminator is shown on the
             primary map display.

Time   The time is shown, both local and UTC.

Grid square: The grid square is shown for both home QTH andTargets. 
             The target grid square is shown both in prompt and 
             browse modes as well as on the Antenna bearing listing.

CQ Zone:     The CQ zone is shown for target QTH's while in prompt mode 
             and on the antenna bearing listing.

QTH data base: A data base of target QTH's is provided. You may edit or  
             add to this file as you desire.

Prefix cross reference: This is another of what I feel is a nice feature.
             A data base of prefix to prefix cross references is provided.
             Many are included. You may add to this data base as desired.

             This allows you to, for example, key prefix "PP". The X-Ref
             routine would determine this to be Brazil with a primary
             prefix of "PY"

             It also has a USA cross reference. It makes a best guess. For
             example, you could key my prefix "KD5" and it would put me
             in the "W5" call area.  I know I'm in the W8 area, but I have
             future plans to incorporate a callbook database into the
             current call assignment strategy, the KC4's in the W4 call 
             area will have to live with this for now.

Current period propagation prediction: You can pop up a window that will 
             give a propagation prediction for the current time to the 
             currently selected target QTH. This can be done by selecting 
             menu option  m(U)f then (C)urrent. While in browse mode, 
             clicking either mouse button will go directly to this option. 
             While in this screen, you may advance the time by 1 hour by 
             pressing "H" or by 1 day by pressing "D"

24-hour propagation prediction: Displays a full color graph predicting 
             the propagation for the next 24 hours from yourhome QTH 
             to the  currently selected target based on the current 
             Sunspot # or solar flux # you have entered. 
~~~
-------------------------------------------------------------------------
                           INSTALLING  DX OnLine
-------------------------------------------------------------------------

             The diskette(s) supplied are NOT in packed format so
             installation is a relatively simple matter.

             1. Log on to the Root directory
                            CD \ <enter>
             2. Create DXOL directory
                            MD \DXOL <enter>
             3. Change to DXOL directory
                           CD \DXOL <enter>
             4. Put DX OnLine diskette in diskette drive
             5. Load diskette to hard drive
                          Copy a:*.* <enter> (if copying from A drive)
                                           or
                          Copy b:*.* <enter> (if copying from B drive)
             6. If more than one diskette, repeat steps 4 & 5
                           for each diskette.
                (Would only apply if you requested 5-1/4" single density 
                 diskettes [360kb])

~~~
---------------------------------------------------------------------------                                     
                                     DX Online                           
                             OPERATING INSTRUCTIONS
---------------------------------------------------------------------------

1. Change to the directory that contains the DX OnLine programs and data 
   files. If this directory is "DXOL", key  CD \DXOL and press the enter key.

2. Run the program by keying DXOL and pressing the enter key.
 
   The program will go thru a short initialization process after which a 
   map of the World will be displayed. If you have a Microsoft compatible 
   mouse installed, you will be placed in the "Browse" mode and the mouse 
   cursor will be at approximately 0 degrees longitude and 0 degrees latitude 
   and the  antenna bearing and distance from the home QTH will be displayed 
   under the map. Note that the initial home QTH information is from my home 
   QTH of Lima Ohio.

   Try moving the mouse and watch the display update. Press a mouse button 
   and watch what happens.

Notice that just above the map is a menu bar similar to the following:

              (M)ode  m(U)f  (P)rint  (F)ile  e(X)it

To select a menu option, key the letter enclosed in parentheses. For example, 
the File menu is selected by keying "F". You do not have to press enter.

The first thing you will want to do is configure the system to your home 
QTH.To do this:
           
            1. Select the File menu by keying "F"
            2. Select edit home QTH by pressing "H"

You may now enter your Call, QTH, Latitude, Longitude and hours to adjust 
for UTC. As I said, the initial information shown is for my home QTH so you 
may see how the entries should be made.

The UTC hours adjustment is enter as East or West rather than + or -. This 
is to coincide with the longitude.
For the continental U.S.:
                            Time Zone              Enter  
                              EST             5 hr 0 min W 
                              CST             6 hr 0 min W
                              MST             7 hr 0 min W
                              PST             8 hr 0 min W
 
For daylight savings time add 1 hour. You will have to manually adjust this 
field when the time changes.

Once you have made your changes, save the Home QTH information and exit. 
You will now be returned to the main program and everything will be relative 
to your own home QTH.
~~~
                                DX OnLine

You will now want to configure DX OnLine for your printer.

To do this, select Menu Option (P)rinter. Then select option (C)onfigure.

You will be shown a list of available printers. You may scroll back and 
forth through the list to find your printer. Once you have found it,enter 
the # that corresponds to your printer.

If your printer is not listed, try "Epson FX" for a dot matrix or H-P
Laserjet for a laser. It is virtually impossible to put every make and
model of printer in the master printer definition file.

If nothing works, all may not be lost. The printer configuration file is
in pretty plain language. The name of this file is "DXOLPRTR.CFG". You may 
use any editor to edit this file. The format is as follows:

The file must have EXACTLY 9 fields and in EXACTLY the following order.  
(If your printer doesn't use one of the control strings, insert a blank 
line).
            
            1.  Printer text description
            2.  Printer reset code
            3.  Compressed print OFF
            4.  Compressed print ON
            5.  Proportional print OFF
            6.  Enhanced print OFF
            7.  Enhanced print ON
            8.  ASCII character for Degree symbol
            9.  ASCII character for Minute symbol

You may enter any data into the control string fields. To enter a character 
that is not available (such as an ESC code), enter a backslant (\) followed 
by the 3 position decimal ASCII code for the desired character. Any keyboard 
character may be keyed directly. For example, you could key "\027@". The 
system would recognize this as esc@ which is the reset control code on 
Epson FX printers. If you enter a character with a backslant, be sure to 
enter exactly 3 numeric characters following. Don't leave off any leading  
zeros. 

Because of the multitude of different character sets available on many 
printers, the degree and minute symbols may not always be correct. They  
are initially set to correspond with the standard PC character set. This 
should work in most cases. If it doesn't, look in your printer manual to 
find the proper ASCII character needed and edit file DXOLPRTR.CFG as 
described above.

If you make manual changes to the printer configuration file, you might 
want to incorporate these changes into the master printer definition file. 
This file is called "DXOLPRTR.DEF". It is in exactly the same format as 
DXOLPRTR.CFG except that it contains information for all available printers.

Again, be very careful that any printer definition records added to this 
file contain exactly 9 fields (or lines).
~~~
                                 DX OnLine

The following is a list of the Primary Menu options and the secondary  
prompts that will appear as a result of selecting the primary option.

(M)ode
      (R)oam mode    Changes to ROAM mode (if you have a mouse)

      (P)rompt mode  Changes to the prompt for target QTH mode

      (T)emp QTH     Toggles the use of a temporary Home QTH.
                     If going into a temporary QTH, displays a screen
                     to enter the temporary QTH information.

m(U)f
      (C)urrent      Displays propagation predictions as of the current 
                     time. This is the same as hitting a mouse button in the
                     ROAM mode.

      24 hour (P)rediction  Computes and displays a graph of the
                    predicted signal propagation from the current time
                    thru the next 24 hours from your home QTH to the
                    currently selected target QTH.
      
      Change (S)sn  Change the Sunspot # (Solar Flux) to the current
                    values. This is available from a number of sources
                    including WWV and ARRL bulletins. A SS# of 175 is
                    set as an itial value.

(P)rint 
      dx (A)ntenna bearing list  Prints and antenna bearing  chart from 
                    your home QTH (or a temporary QTH) to alllocations 
                    in the target QTH data base. The information shown 
                    is Prefix,QTH,Longitude,latitude,long path bearing,
                    short path bearing,short path range in statute miles, 
                    nautical miles and kilometers,the target Grid Square 
                    and the CQ zone.

       (R)egister   Prints a form to register DX OnLine. Since this is  
                    a registered copy, this is here as a courtesy in case
                    you or a friend wish to order another copy.

       (D)ocumentation  Prints this documentation.

       (C)onfigure printer  Configures DX OnLine to function with your
                   printer.

e(X)it
      (Y)es        Exit DX OnLine and return to system
      (N)o         No, do not exit yet
~~~
                                 DX OnLine

Note:  while in prompt mode, an additional menu option is shown.

(T)arget           This brings up a prompt to select a prefix and/or
                   target QTH.

When prompting for a target, keep the following in mind:

The system looks for occurrences of the keyed data. The following 
are examples of prefix and/or QTH prompt selections:
  
    PREFIX               QTH                            RESULT
    ------            ---------               ------------------------------
     F                                        All prefixes starting with "F"                               
                                                      (F,FG,FH,etc.)
                         
                         LON                  London,England, etc.                                                        
     
     G                   LON                  London England
                         
                         PORT                 Lisbon,Portugal  Portland,OR  
                                              Portland,ME  etc.
                         
                         UGAL                 Lisbon, Portugal  etc.
     
     GX                                       All "G" prefixes - used prefix 
                                              X-ref to convert

If you have any major problems. let me know.

73 es Gud DX
Steve, KD5ON