ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
                    ³  THS - TNC Hostmode Server   ³
                    ³ PHS - PK-xxx Hostmode Server ³
                    ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾

				HB9CVV
			     January 1994

                          Version 6.1x - OS/2

	THS is an OS/2 Packet Radio terminal program to control a TNC-1 or
	TNC-2 with the WA8DED or equivalent Firmware.

	PHS is an OS/2 Packet Radio terminal program to control a PK-232 or
	PK-900 multi-mode terminal node controller. The firmware of the
	PK firmware must be dated 30.DEC.88 or later.

	Both programs are 32-bit textmode applications and run either in an
	OS/2 full screen or in an OS/2 window under OS/2 2.x only.


		     Major features of THS/PHS
		     ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ

	* PHS: support of packet, amtor, rtty, ascii, morse, signal and
	  pactor modes (depending on firmware).
	* PHS: supports both radio modems of a PK-900 simultanuesly.
	* user configurable comm-port, colors and texts.
	* split screen operation.
	* command and parameter entry in mode sensitive dialog windows.
	* extended help functions.
	* review of received text (backscrolling).
	* snapshooting of the review-buffer to file.
	* logging (capturing) to file.
	* send text from file.
	* binary file transfer using YAPP protocol (packet mode).
	* multi-channel operation (packet mode).
	* heard list showing the path (packet mode).
	* Net/Rom frames are decoded (packet mode).
	* wordwrapping is available.
	* built-in message editor.
	* support for screens up to 80*60.

	THS contains a subset of the features of PHS because the TNC is
	packet mode only.

	For PHS, the document describes the operation for the PK-232. A
	PK-900 can be operated like a PK-232, but only the first modem
	("Radio 1") is serviced in this case. For the 'true' PK-900
	operation, please see the appendix.


        ******************************************************************
        * A note to PK-900 users: It is highly recommended NOT to use    *
        * the PK-900 at a communication line speed of 19200 baud, but    *
        * use 9600 baud only. The PK-900 seems to have problems at 19200 *
        * baud (which can be seen by the use of a line monitor).         *
        ******************************************************************




			NOTE
		    ÍÍÍÍÍÍÍÍÍÍÍÍ

	XHS is a hobby project and covers my needs, so I implemented the
	features which I wished to have, and did not bother to fit all tastes
	and to match all possibilities.  XHS may well be not adequate for
	your requirements, please remember however that you are not forced to
	use it, nor did you have to pay for it.



	      Changes and modifications since version 4.03
	      ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ

	6.11  Silly bug removed which prevents older firmware which is not
	      able to understand the newer "HOST 5" command (but only 
	      "HOST Y/N" to be recognized.

        6.1   Added support for the 01-DEC-93 firmware from AEA. Users of
              older firmware which is not supporting all commands will see
              some error messages for the unsupported commands during
              startup when PHS loads the PK-xxx parameters. These 
              unsupported commands are simply marked "unsupported" by PHS 
              and consequently are not available.

              The Help message file has not been edited for the new commands
              yet, I am tired of typing manual pages. Anybody willing to do
	      this (if you look into the help-files, the format is obvious)
	      is invited to send it to me for incorporation...

              Due to the common source code, THS also got the version 
              number 6.1, but has not experienced any changes.

        6.02  Corrected program aborts caused by weird responses of the
              PK-900 firmware to CO commands. Using IBM C/C++ Tools now.

	6.00  Added support for the PK-900 (two modems). Ported XHS for
	      compilation with the IBM CSet 32-bit compiler. Version 6 will
	      now require OS/2 2.x and will not run under OS/2 1.x.

	5.00  Added Pactor mode support for the PK-232 01-MAR-93 firmware.

	      Added word-wrapping for word-oriented (i.e. non-Packet)
	      modes.





                        PRINCIPLES OF OPERATION
                        ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ

	THS/PHS have been developed from the equivalent, older DOS programs.
	The term "XHS" is also used for "THS or/and PHS".

	XHS uses the OS/2 Communications driver for the RS-232 line to the
	terminal device and make full use if a buffered hardware port is
	available.

	XHS runs the firmware software exclusively in HOST mode, which
	permits a maxiumum of control and cooperation. XHS is written in C
	for the IBM C-Set compiler.

	The internal implementation of XHS in form of several concurrent
	threads. This permits full parallel service of communications
	control, screen, and keyboard - you will never notice delays when you
	type (opposed to other similar programs).

	The windowing system is implemented using the VITAMIN C library (with
	modifications), a commercially available software library.  Vitamin C
	permits writing to non-active windows, so scrolling in an underlying
	window is possible.

	This feature, together with the real-time operation, permits to
	continue the receiving and displaying of received packets even when
	support windows (e.g.  help windows or parameter dialog windows) are
	opened.

	The PK-232 device or the TNC device are also called "device" or "TNC"
	in this document.


                              INSTALLATION
                              ÍÍÍÍÍÍÍÍÍÍÍÍ

	It is expected that you are familiar with the operation of the TNC or
	the PK-232 and with the documents describing that software.

	PHS consists of the following files:

        	PHS.EXE         PK-232 Hostmode Server.
		PHS.CFG		Configuration file.
		PHSHELP.MSG	Help file.
		PHSHELP.IDX	Index file.
        	XHS6.DOC        Document file

	THS consists of the following files:

        	THS.EXE         TNC Hostmode Server.
		THS.CFG		Configuration file.
		THSHELP.MSG	Help file.
		THSHELP.IDX	Index file.
        	XHS6.DOC        Document file

	The first four files must reside in the same directory. Before you
	can run THS or PHS, you MUST edit the configuration file THS.CFG or
	PHS.CFG respectively, to reflect YOUR environment, and possibly you
	might have to configure your TNC or PK-232 also.  Please refer to the
	description of the configuration file at the end of this manual.

	The syntax to call THS/PHS is: "THS [filename]", or "PHS [filename]"
	where filename is the name of a configuration file. If filename is
	omitted, PHS will use the default filename PHS.CFG, and THS will use
	THS.CFG.

	The TNC and the PK-232 both have a support battery to buffer the
	parameter values.  If you use this battery, some TNC/PK-232 parameter
	must be preset to values which allow THS/PHS to communicate with the
	TNC/PK-232. The communication line parameters of the TNC/PK-232 must
	be set to 8 bits, no parity, and the line speed must match the
	selected line speed for THS/PHS.

	Alternatively, when no battery is connected, PHS will switch the
	PK-232 to the selected line speed of PHS.

	Though not neccessarily required for hostmode operation THS/PHS
	requires the standard 8-wire connection (lines 2-8 and 20) for the
	RS-232 communication line.  You can however override this requirement
	by a parameter in the configuration file (and loose the detection if
	the device is online).

	The following chapters describe the operation of PHS. THS is a
	functional subset of PHS because a TNC-1 or TNC-2 operates in packet
	mode only, so part of the features of PHS are not available for THS.




                        PHS OPERATION
                        ÍÍÍÍÍÍÍÍÍÍÍÍÍ

	After you invoked PHS, you get the PHS opening screen:
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ



     ÕÍÍÍÍÍÍÍÍÍÍ PK-232 Host mode Server V6.00 [OS/2] - HB9CVV ÍÍÍÍÍÍÍÍÍÍÍÍ¸
     ³                                                                     ³
     ³  Initializing COM3, 9600bd - DSR: on, CTS: on, CD: on, FIFO: yes    ³
     ³  Initializing PK-232 - please wait........done.                     ³
     ³  PK-232 eprom date is: 01-MAR-93.                                   ³
     ³  Loading TNC parameters: done.                                      ³
     ³  Loading CFG parameters: done.                                      ³
     ³  READY. Use ALT/Z for help.                                         ³
     ³                                                                     ³
     ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾



                                                         ³    º 23-MAR 12:34:56



ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

	PHS will read the number-of-lines of your current video mode from the
	system and adjust its windows accordingly. For all of the screendumps
	shown here, the standard of 25 lines has been used.

	The single line with the date and time is the statusline, which is
	normally invers - you cannot see this in this printout. You also see
	that PHS divides the screen into the upper receive window and the
	lower transmit window which are seperated by the statusline. The
	statusline is different for each mode.  During initialisation and for
	a short time during the PK-232 mode switching the statusline is
	blanked in the left part.

	You can change the colors of all windows (this includes the
	statusline) by editing the associated values in the configuration
	file.

	When this opening screen disappears, PHS switches the PK-232 into the
	initial PK-232 mode, which is also specified in the configuration
	file.

	If the RESETDEVICEONEXIT Parameter of the Config-File is NO
	(recommended) the you will realize that PHS temporarily switches the
	PK-232 into the morse mode during the initialisation phase. Also,
	when you exit PHS, the PK-232 is left in the morse mode.

	If "FIFO: yes" is displayed, then the OS/2 communications driver
	reported the presence of a buffered asynchronous communictions chip,
	and has enabled the fifo-buffer operation of this chip. Note that
	non-IBM drivers may not report this, but still use a buffered chip.


                        THE GENERAL KEYS
                        ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

	The ESC key is the general help key to call the help window. If you
	press ESC in packet mode, then the packet-mode help screen pops up:

ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
  ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ PACKET MODE ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
  ³                                     º                                     ³
  ³ ALT/P   TNC mode param setup menu   º ALT/I   TNC text-param setup menu   ³
  ³ ALT/T   PHS parameter setup menu    º ALT/V   View OS/2 directory         ³
  ³ ALT/W   Command string directory    º ALT/F   View function-key setup     ³
  ³ ALT/L   Logging (capture) on/off    º ALT/R   or  Review (scrollback)    ³
  ³ ALT/S   Send an ASCII file          º ALT/K   Call Editor                 ³
  ³ ALT/B   Enter urcall (remote call)  º CTRL/U  Erase TX-window             ³
  ³ ALT/X   Exit PHS                    º CTRL/X  Erase RX-window             ³
  ³ ALT/M   Switch TNC modes            º ESC     Direct command entry        ³
  ³ ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ º ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ ³
  ³ ALT/C   Connect menu                º ALT/H   Show formatted heard list   ³
  ³ ALT/D   Disconnect                  º ALT/G   Show raw heard list         ³
  ³ PgUp    Binary file upload (YAPP)   º INS     Toggle status line display  ³
  ³ PgDn    Binary file download (YAPP) º <->     Select Channel              ³
  ³                                     º                                     ³
  ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾


 M1234 º VHF º UA:00 RTY:00 ³ DISCONNECTED               ³    º 23-MAR 12:34:56


ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

	The help window called by ALT/Z is mode sensitive. The upper half of
	the help window (down to the seperator) is identical for all modes
	because the keys are valid in all modes and are called general keys.
	The lower half presents the keys which are mode specific, and are
	called mode keys.

	We will now discuss the actions and the support windows caused by the
	general keys presented in the upper part of the help window, followed
	by a discussion of the individual modes and the mode-related keys and
	windows.

	Note that when any support window is open and you want to cancel it,
	press any key and the window will disappear. If there is no action
	from the keyboard, any of these windows will also disappear after
	some time.

	You will also notice that the activity in the receive window will
	continue when any of the support windows is popped up.




	ALT/P is a general key and available for all modes. It pops up a
	window and shows the PK-232 parameters which are related to the
	currently selected mode.  Consequently, the ALT/P window is discussed
	individually for each mode later.

	ALT/I pops up the PK-232 text parameter setup window:

ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ



                              ÕÍÍÍ SELECT ÍÍÍ¸
                              ³              ³
                              ³ (A) CFROM    ³
                              ³ (B) DFROM    ³
                              ³ (C) MFROM    ³
                              ³ (D) MTO      ³
                              ³ (E) UNPROTO  ³
                              ³ (F) BTEXT    ³
                              ³ (G) CTEXT    ³
                              ³ (H) AAB      ³
                              ³              ³
                              ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾



 M1234 º VHF º UA:00 RTY:00 ³ DISCONNECTED               ³    º 23-MAR 12:34:56


ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

	To select the command parameter for inspection or change, you can
	either press the marked character (A, B, C etc), or move the scroll
	bar up and down and then press ENTER (the bar is just not visible in
	this printout).  This window will then disappear and the associated
	parameter entry window will pop up.

	This window will pop up regardless of the current PK-232 mode.



	When you select CFROM, DFROM, MFROM or MTO then the associated
	parameter entry window pops up - for example:

ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ


                 ÕÍÍÍ CFROM ÍÍÍÍ¸
                 ³              ³
                 ³     ALL      ³
                 ³              ³
                 ³              ³
                 ³              ³
                 ³              ³
                 ³              ³
                 ³              ³
                 ³              ³
                 ³              ³
                 ³              ³
                 ³              ³
                 ³ <F1>  HELP   ³
                 ³ <ESC> ABORT  ³
                 ³ <F10> ACCEPT ³
                 ³              ³
                 ³              ³
 M1234 º VHF º UAÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾CONNECTED               ³    º 23-MAR 12:34:56

  Valid entries are: ALL / NONE / YES / NO
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

	You can enter a qualifier (ALL, NONE, YES or NO) and a list of
	callsigns.

                       Operation of Support Windows
                       ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

	For all support windows which show the parameter values of commands,
	PHS always READS the current parameter values first so you can
	inspect the actual values and then apply changes. The cursor is the
	positioned on the first input field, and the size of each input field
	is visible on the screen (which is not visible in the printouts
	here). You move to another commands input field with the down-arrow
	and up-arrow keys. For each command you will always get a short help
	line on the bottom of the screen. If you need more help about the
	command and the parameters, press F1.

	With kind permission from AEA, the help texts for the PK-232 commands
	have been derived from manual files supplied by AEA and is
	copyrighted material.

	Finally you may press either F10 to accept the data and apply the
	parameter values, or ESC to discard it, in case you changed your
	mind.




	You must follow the rules for the parameters of a command as
	described in the PK-232 manual.  In case of the CFROM window - if you
	enter ALL, followed by a callsign list this makes no sense, and you
	will get an error message from the PK-232:

ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ


                 ÕÍÍÍ CFROM ÍÍÍÍ¸
                 ³              ³
                 ³     ALL      ³
                 ³              ³
                ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ TNC: ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
                ³ CFROM - msg from device: "Too many params"  ³
                ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾
                 ³   HB9DDD     ³
                 ³   HB9EEE     ³
                 ³   HB9FFF     ³
                 ³              ³
                 ³              ³
                 ³              ³
                 ³ <F1>  HELP   ³
                 ³ <ESC> ABORT  ³
                 ³ <F10> ACCEPT ³
                 ³              ³
                 ³              ³
 M1234 º VHF º UAÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾CONNECTED               ³    º 23-MAR 12:34:56


ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

	MFROM and MTO is preset to "NO", followed by your callsign. The
	reason for this is that PHS monitors when connected, and this
	excludes your own packets from the monitor screen. You should not
	change this if not absolutely neccessary.




	Here is an example of the UNPROTO parameter entry window:

ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

                 ÕÍÍ UNPROTO ÍÍÍ¸
                 ³              ³
                 ³ To:          ³
                 ³   DB0CZ      ³
                 ³ via          ³
                 ³   HB9PD-7    ³
                 ³   DB0HP      ³
                 ³              ³
                 ³              ³
                 ³              ³
                 ³              ³
                 ³              ³
                 ³              ³
                 ³              ³
                 ³ <F1>  HELP   ³
                 ³ <ESC> ABORT  ³
                 ³ <F10> ACCEPT ³
                 ³              ³
 M1234 º VHF º UAÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾CONNECTED               ³    º 23-MAR 12:34:56

  Callsign and SSID of a digipeater
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

	In this example the cursor is positioned somewhere in the "via" list
	of callsigns.




	If you selected the BTEXT window, you will get this screen:

ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ





  ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ BEACON TEXT ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
  ³                                                                          ³
  ³ *** Peter, Qth: Port/Biel - JN37OC                                       ³
  ³                                                                          ³
  ³     <F1> HELP    <ESC> ABORT    <CR> or <F10> ACCEPT                     ³
  ³                                                                          ³
  ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾



 M1234 º VHF º UA:00 RTY:00 ³ DISCONNECTED               ³    º 23-MAR 12:34:56

  Enter beacon text. Use % to clear it
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

	The initial beacon text has been sent from the beacon string in the
	configuration file during the initialisation phase of PHS. It is read from the
	TNC for presentation, so you will always see the actual beacon text. Note
	however that PHS limits the length of the beacon string to 72 characters.

	You will get a similar window for the CONNECT message (CTEXT), and for AAB. The
	input field for CTEXT is also 72 characters, for AAB it is 16 characters.




	The ALT/V key pops up this window which allows you to specify a OS/2 directory
	for viewing, e.g.:

ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

     ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Directory ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
     ³                                                      ³
     ³ C:\OS2\*.*                                           ³
     ³                                                      ³
     ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾

ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ .... ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

	Next you will get something like this:

ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ


	 ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ DIRECTORY ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
         ³                                             ³
         ³  DOS     .SYS      1536   19-DEC-91  08:13  ³
         ³  DOSCALLS.LIB     51200   28-NOV-90  21:19  ³
	 ³  E       .EXE     69120   19-DEC-91  06:59  ³
	 ³  EAUTIL  .EXE     38400   19-DEC-91  08:19  ³
	 ³  EPM     .INI       512   08-JAN-92  20:08  ³
	 ³  EXTDSKDD.SYS      2048   19-DEC-91  08:18  ³
	 ³  FDISK   .COM    109568   19-DEC-91  05:41  ³
	 ³  FDISKPM .EXE     72704   19-DEC-91  05:46  ³
	 ³  FIND    .EXE     31744   19-DEC-91  08:22  ³
	 ³  FORMAT  .COM     65024   19-DEC-91  08:44  ³
	 ³  HELP    .CMD      1024   06-AUG-91  10:05  ³
	 ³  HELPMSG .EXE     37888   19-DEC-91  08:27  ³
	 ³  HPFS    .IFS    128512   21-DEC-91  02:14  ³
	 ³  INI     .RC      18944   08-JAN-92  19:41  ³
	 ³  INISYS  .RC       1536   08-JAN-92  19:41  ³
	 ³  KBD01   .SYS     28160   19-DEC-91  08:50  ³
	 ³          ...more...                         ³
 M1234 ºN³                                             ³º     º 24-FEB 16:28:59
	 ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾

ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ



	ALT/W pops up the command string directory:

ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
                     ÕÍÍÍÍÍÍÍÍÍÍ COMMAND STRINGS ÍÍÍÍÍÍÍÍÍÍ¸
                     ³                                     ³
                     ³ (A) C DK1SL VIA HB9F                ³
                     ³ (B) C HB9SDD                        ³
                     ³ (C) C HB9PD                         ³
                     ³ (D) C HB9BRC                        ³
                     ³ (E) C 4U1ITU-8 VIA HB9PD-7, HB9X... ³
                     ³                                     ³
                     ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾








 M1234 º VHF º UA:00 RTY:00 ³ DISCONNECTED               ³    º 23-MAR 12:34:56


ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

	You will see the command string lines from the configuration file
	(these are the lines with the COMMANDSTRING keyword).  The number of
	command strings is limited to 20, and the length of each line is
	limited to 72. Because the width of this window is far less than 72,
	all lines which are too long to fit are truncated for presentation,
	which is indicated by the "...".

	Again, to select a command for execution, you can either press the
	marked character (A, B, C etc), or move the scroll bar up and down
	and then press ENTER (the bar is just not visible in this printout).

	Quite obviously, a line must contain a valid PK-232 command or you
	will get an error message when you try to execute it. PHS not allow
	the execution of all PK-232 commands - it will refuse to send
	commands which would interfere with its operation. Please refer to
	the discussion of ESC key.




	ALT/F lets you inspect your function key setup:

ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
                     ÕÍÍÍÍÍÍÍÍ FUNCTION KEY SETUP ÍÍÍÍÍÍÍÍÍ¸
                     ³                                     ³
                     ³ F01  Name & Qth                     ³
                     ³ F02  Rig SHORT                      ³
                     ³ F04  Rig LONG                       ³
                     ³ F05  FEC CQ                         ³
                     ³ F06  RYRYRY                         ³
                     ³                                     ³
                     ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾








 M1234 º VHF º UA:00 RTY:00 ³ DISCONNECTED               ³    º 23-MAR 12:34:56


ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

	You will get the function key title string, not the function key text
	which can be much longer than the title, and even contain several
	lines.

	The function key title strings as well as the function key text
	strings are defined in the configuration file.

	This window also pops up should you press a function key which has
	not been loaded with a string. Whenever you press a 'loaded' function
	key, then the associated function key text is inserted in your output
	to the PK-232.




	ALT/T in any mode pops up the PHS parameter setup window:
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
                                                  ÕÍ PHS Parameters ÍÍ¸
                                                  ³                   ³
                                                  ³ POLLDELAY      50 ³
                                                  ³ BELL            1 ³
                                                  ³ CBELL           1 ³
                                                  ³ WORDWRAP       78 ³
                                                  ³ MWINDOW         0 ³
                                                  ³ FILTER          1 ³
                                                  ³ YPKLEN        254 ³
                                                  ³ MAXPFRAM       20 ³
                                                  ³ MSTAMP          1 ³
                                                  ³                   ³
                                                  ³  <F1>  HELP       ³
                                                  ³  <ESC> EXIT       ³
                                                  ³  <F10> SET PARAM  ³
                                                  ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾



 M1234 º HF  º UA:00 RTY:00 ³ DISCONNECTED               ³    º 23-MAR 12:34:56

  Enable the BELL (1/0)
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

	The cursor is positioned at the input field of the first parameter
	(BELL).  With any such setup window, you use  the up- and down-arrows
	to select  the parameter which you want to change.

	As with the ALT/P parameter entry windows, PHS reads the actual
	values, lets you apply changes, writes the parameters and then
	re-reads them again. If you violated a given range for a parameter,
	then no change is done, and this is immediately visible after PHS
	reread the parameters.

	The PHS parameters are parameters for PHS rather than for the PK-232,
	and allow you to:

	- change the polldelay of THS/PHS. To avoid an excessive system
	  load, THS/PHS does not poll the device continuosly but inserts
	  small delays between successive polls. You may somewhat finetune
	  Systemload vs THS/PHS performance here.

 	- enable or disable if you want to hear 'bells' sent to you from a
	  connected station (you will never hear bells from monitored
	  stations) (BELL).  This parameter is effective in the packet modes
	  only.

	- enable or disable if you want to hear a bell (warble) when you get
	  a connect (CBELL). This parameter is effective in the packet modes
	  only.

	- set the packet frame length for binary transfers (YPKLEN). This
	  parameter is effective in the packet modes only.

	- set the column position of input word wrapping (WORDWRAP) - a zero
	  disables wrapping.

 	- define the window which gets the monitored frames (MWINDOW).  By
	  default, this is window zero (because channel zero is the monitor
	  channel).  You can however route all monitored frames to another
	  channel window of your own choice. This parameter is effective in
	  the packet modes only.

 	- filter out non-printable charcters (MFILTER). If this is enabled,
	  only BELL, HT, LF, VT, FF, CR and the characters with ASCII values
	  from 0x20 to 0x7E are displayed as is, the filtered charcter are
	  shown as a small solid rectangle.  If you use a national character
	  set, MFILTER should be disabled.

   	The initial setting of MFILTER is defined in the configuration file's
	PHS parameter definition line.

	YPKLEN needs an explanation. For binary sends, PHS switches the
	PK-232 into  the transparent mode and the packet length  is defined
	by YPKLEN. That is,  PHS will read YPKLEN slices from the file, add
	the YAPP protocol layer and send it to the PK-232 (the PK-232
	parameter PACLEN remain always preset to the maximum value of 256
	bytes).




	ALT/K invokes the online editor of PHS. You are first asked for a
	filename of a file which you want to edit. If the filename does not
	exist, PHS asks you if you want to create the file. If you confirm,
	you can start editing. In the example the filename "ROLF.MSG" was
	given and because such a file did not exist, PHS was told to create
	the file. Pressing F1 pops up a series of help windows for the
	editor:

ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
   ÉÍÍÍÍÍÍÍÍÍ File: "ROLF.MSG"  Line:005  Col:14  Free=7838  Insert   ÍÍÍÍÍÍÍÍÍ»
   ºHallo Rolf,                                                                º
   º                                                                           º
   ºiÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ HELP - Use F2 to exit ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸   º
   ºs³                                                                     ³   º
   ºa³                                                                     ³   º
   º ³ ESC            Exit the editor. You get the option to save the      ³   º
   º ³                file to disk. If you don't, calling the editor       ³   º
   º ³                again will place you exactly where you left.         ³   º
   º ³ INSERT KEY     Toggles insert and overwrite modes                   ³   º
   ÈÍ³ F8             Toggles whether carriage returns are symbolically    ³ÍÍÍ¼
     ³                displayed in the edit window                         ³
     ³ F9             Toggles editor display from 128 ASCII characters     ³
     ³                to 256 IBM characters                                ³
     ³ UP-ARROW       Moves cursor up a line                               ³
     ³ DOWN-ARROW     Moves cursor down a line                             ³
     ³ LEFT-ARROW     Moves cursor left a space                            ³
     ³ RIGHT-ARROW    Moves cursor right a space                           ³
     ³                                                            more...  ³
     ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾

 M1234 º VHF º UA:00 RTY:00 ³ DISCONNECTED               ³    º 23-MAR 12:34:56


ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

	After you finished editing you will save the file to disk. This file
	can then be sent by pressing the ALT/S key in any PK-232 mode. You
	cannot send an unsaved file. At any time you can edit the saved file
	again.

	You will not save the file to disk (but keep the text it the editors
	buffer) if you temporarliy want to exit the editor and want to
	continue editing later. If the editor is called with a previously
	unsaved buffer, it pops up with the cursor positioned excatly where
	you left before.

	When you edit, just realize that the Amtor and RTTY modes do not
	support the full ascii character set.

	The editor buffer is limited to 8000 bytes which is sufficient for
	message editing.




                       Printing and Logging
                       ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

	There is no 'direct' print support for the OS/2 versions of THS/PHS
	because the printers under OS/2 are normally spooled and not directly
	accessible. It is recommended to log to a file and print that file
	later.

	ALT/L toggles the logging to a file. Logging can be enabled
	individually for each channel which will go to different files. When
	you press ALT/L then a window pops up and asks you for the filename
	of the file which will receive the logged data. You cannot specify
	anything else but the filename, the extension is always "CAn" where
	'n' is the channel number. The logfiles will be created in the
	current OS/2 directory.

	You are offered a filename which is constructed from the current date
	and time but you are free to select another filename. The filename
	which is offered has the format "MDD_hhmm.CAn" where 'M' is the
	hexadecimal number of the month (i.e.  1 to 9 for january to
	september, and A, B and C for october, november and december). 'DD'
	is the day of the month, 'hh' is the hour and 'mm' is the minute. A
	logfile started October 23, at 12:34 for channel 3 would be given the
	filename "A23_1234.CA3". Furthermore, if a subdirectory "LOG" exists
	in the current directory, then the file is opened in the LOG
	subdirectory, otherwise in the current directory.

ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
 M1234 º VHF º UA:00 RTY:00 ³ DISCONNECTED               ³  L º 23-MAR 12:34:56
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

	If logging is on for a channel, this is indicated by the logging-flag
	"L" in column 61 of the statusline.

	When logging is already switched on for the channel and you press
	ALT/L then you are asked if you want to stop logging.

	Everything which appears on the receive window of a channel will go
	to the logfile if logging is enabled for that channel.




	ALT/S permits to send any file containing Ascii text. You are asked
	for the filename of the file to be sent. This filename is preset to
	the filename you specified for editing (if you did edit before) but
	can be overwritten.

ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
KANALZUTEILUNG
*** Bulletin-ID: 158902HB9PD ***
     ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ ASCII FILE SEND ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
de HB³                                                                ³
     ³ Filename: PRIGCHAN.TXT                                         ³
Als B³ Sending line 22 of 37 - ALT/A to abort                         ³
"USER³                                                                ³
ausreÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾
abgerufen.
Interessant dabei duerfte neben dem Call der USER auch sein auf
welcher Frequenz der jeweilige Benutzer die Box erreicht hat.

Die Kanalzuteilung ist wie folgt organisiert:

Total 18 Kanaele
****************

Kanal 1-4      Direktzugang auf 70cm Freqq. 430.675

Kanal 5-9
               Store und Forward mit HB9AJ, HB9XC und DB0CZ
 M1234 º VHF º UA:05 RTY:00 ³ INFORMATION TRANSFER       ³    º 23-MAR 12:34:56


ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

	Note that the line number which is sent refers to the line which is
	currently sent to the PK-232, not the line which is actually
	transmitted by the PK-232.

	In the packet modes, the text scrolls behind the ASCII FILE SEND
	window when it is sent. In the other modes, the text scrolls in the
	transmit window, and in the receive window the echo will appear from
	the PK-232 when the text is transmitted.




	ESC pops up the direct command input window:

ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ




ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ TNC COMMAND ENTRY ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³ CMD> MYSELCAL               ÕÍÍÍ RESPONSE ÍÍÍÍ¸                              ³
ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ³ MYSELCAL: HCVV  ³ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾
                              ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾







 AMTOR LISTEN  º RECEIVE  ³  Phasing      º              ³    º 23-MAR 12:34:56

ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

	You use the 'normal' command mnemonics of the dialog mode of the
	PK-232. PHS translates this into hostmode commands, and also
	translates the host-mode response back to the dialoge mode mnemonics.

	For THS, you must use the mnemonics of the normal TAPR firmware -
	this is translated into the (more cryptic) WA8DED mnemonics by THS
	and vs.

	In the CMD entry window you can inspect ALL parameters and modify
	most of them.  Writing of some parameters is disabled however because
	a direct execution would interfere with the operation of PHS. In
	either case you will get a message like one of the following:

ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ TNC COMMAND ENTRY ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³ CMD> PA   ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ INFORMATION ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸            ³
ÔÍÍÍÍÍÍÍÍÍÍÍ³ PACKET: disabled - use ALT/M to switch device modes ³ÍÍÍÍÍÍÍÍÍÍÍÍ¾
            ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾

ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ TNC COMMAND ENTRY ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³ CMD> MFÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ INFORMATION ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸         ³
ÔÍÍÍÍÍÍÍÍ³ MFILTER: disabled - this parameter must remain unchanged  ³ÍÍÍÍÍÍÍÍÍ¾
         ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾

ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ


	ALT/M in any mode pops up the device mode select screen:

ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ



                              ÕÍÍ DEVICE MODE ÍÍÍ¸
                              ³                  ³
                              ³   Packet (V)HF   ³
                              ³   Packet (H)F    ³
                              ³  Amtor (L)isten  ³
                              ³  Amtor (S)tandby ³
                              ³   (R)TTY Baudot  ³
                              ³     (A)SCII      ³
                              ³     (M)orse      ³
                              ³     S(I)gnal     ³
                              ³  Pa(C)tor Listen ³
                              ³ (P)actor Standby ³
                              ³                  ³
                              ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾



 M1234 º HF  º UA:00 RTY:00 ³ DISCONNECTED               ³    º 23-MAR 12:34:56


ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

	To select the PK-232 mode, you can either press the marked character,
	or move the scroll bar up and down and then press ENTER. The bar is
	not visible in this printout.

	The two different modes for packet just use different values for some
	PK-232 parameters.

	Packet VHF and HF use the parameter values recommended by AEA.

	The different packet modes are indicated in the statusline. You will
	see "VHF" in place of "HF" if the PK-232 is in packet-VHF.

	The FAX and NAVTEX modes are not supported.

	The remainder of the general keys will be discussed after the
	discussion of the individual modes.




                                PACKET MODES
                                ÄÄÄÄÄÄÄÄÄÄÄÄ

	There is one difference between the packet-modes and the other modes:
	in packet you are offered one monitor channel window and four
	connectable channel windows (for all other modes there is just one
	receive window). The channels numbers are from zero to four, but
	channel zero is marked with an "M" to remind you that this is the
	monitor channel. You use the left-arrow and right-arrow keys to
	switch the channels. When you switch to a new channel, the full
	(upper) receive window is completely replaced by the new channel
	window. The status line changes also, reflecting the status of
	currently selected window.

	The channel indicator is on the leftmost side of the status line. The
	current channel is indicated by a reverse letter, that is, one of the
	letters of the M1234 string - which is normally (like the rest of the
	statusline) dark on cyan - is cyan on black. Also, if you selected
	one channel - this is called the active channel and the active
	(receive) window - and ANOTHER channel gets input, then the indicator
	of that channel changes to white on cyan. Once you selected that
	window for inspection, the indicator returns to its normal color.

	The monitored channel gets all monitored packets and you cannot
	connect on this channel. The statusline for the monitored channel is:

ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
 M1234 º VHF º          ÄÄÄ MONITOR CHANNEL ÄÄÄ          ³    º 23-MAR 12:34:56
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

	However you can redirect the monitored input to one of the
	connectable channels if you want to see the monitoring there. Please
	refer to the MWINDOW command in the ALT/T window.

	For the channels 1 to 4 the status line is like this:

ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
 M1234 º VHF º UA:03 RTY:00 ³ INFORMATION TRANSFER       ³    º 23-MAR 12:34:56
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

	The number after the "UA:" is the number of unacknowledged frames,
	RTY displays the number of retries so far. The next field is the link
	state.

	Pressing the INS key toggles the status line to the other display
	format:

ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
 M1234 º VHF º HB9PD via HB9PD-7                         ³    º 23-MAR 12:34:56
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

	The UA/RTY and linkstate field is replaced by the connectee. If you
	use several digipeaters and the string is gets too long, the
	connectee string is truncated on the right hand side.

--------------------------- NOTE ON THS ---------------------------------------

	The statusline for THS is like:

ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
 M1234 º NS:07 UA:03 RTY:00 ³ INFORMATION TRANSFER       ³    º 23-MAR 12:34:56
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

	Where NS indicates the number of frames which have been already moved
	to the TNC but have not yet been sent.



	ALT/P in packet mode pops up the packet mode PK-232 parameter setup
	window:

ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ PK-232 Parameters ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
          ³                                                           ³
          ³ ACKPRIOR        Y   HID             N   RESPTIME        0 ³
          ³ AUDELAY         0   LITE            N   RETRY          10 ³
          ³ AX25L2V2        Y   MAXFRAME        4   SLOTTIME       30 ³
          ³ AXDELAY         0   MCON            6   SQUELCH         N ³
          ³ AXHANG          0   MID             0   TRIES           0 ³
          ³ BEACON        E 0   MONITOR         6   TXDELAY        40 ³
          ³ CHECK          25   MRPT            Y   USERS           4 ³
          ³ CMSG            N   MSTAMP          N   WHYNOT          N ³
          ³ CODE            2   MYALIAS    BIENNE   XMITOK          Y ³
          ³ CONPERM         N   MYCALL     HB9CVV                     ³
          ³ DWAIT          16   PASSALL         N   <F1>  HELP        ³
          ³ FRACK           8   PERSIST        84   <ESC> EXIT        ³
          ³ FRICK           0   PPERSIST        Y   <F10> SET PARAM   ³
          ³ FULLDUP         N   RELINK          N                     ³
          ³                                                           ³
          ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾



 M1234 º VHF º UA:00 RTY:00 ³ DISCONNECTED               ³    º 23-MAR 12:34:56

  Audio delay in 10mS (range 0-120)
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

	PHS/THS always reads the parameters from the PK-232/TNC, so you
	always get the actual PK-232 or TNC-1/2 parameters. You can now move
	the cursor to a command and change the parameter.  To apply the
	changes, press F10. PHS then writes the parameters to the PK-232 and
	re-reads them again. If a parameter which you have changed again gets
	the old value, then you have violated a range check and the PK-232
	refused to accept your value. The process of reading, writing, and
	re-reading is indicated in the window. It also takes a few seconds,
	even when the communiation line to the PK-232 is operated at 9600
	bauds.

	You will see all parameter which are valid for the packet mode, and
	which you may change. You may miss some packet mode commands here -
	but the parameters of such commands must remain unchanged at preset
	values for a proper operation of PHS.

	There are some commands like MRPT and PASSALL which should be changed
	only if neccessary, because there is still a possible interaction.
	For example, quite obviously, if you surpress the indication of
	digipeaters in monitored frames then the HEARD-List of PHS will not
	contain only incomplete information. Also, if PASSALL is YES, you can
	get 'clobbered' callsigns in the heard-list.

	For some commands (BEACON, MCON and MONITOR) you will get a secondary
	selection window which offers you discrete choices.




	A typical screen from the monitored channel is like this:

ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
HB9X-7*>HB9X-9 [I;3,3]:
NON - Bid 21A90BHB9X deja recu
8>
HB9X-6*>4U1ITU-8 (RR;3)
HB9X-6*>4U1ITU-8 [I;3,2]:
SB ALL    < OH1HS  @ EU $787_ON4HU
HB9X-7*>HB9X-9 (RR;4)
HB9X-6*>4U1ITU-8 (RR,F;3)
HB9X-7*>HB9CED [I;3,2]:
MOL:HB9X-7} Invalid command (CONNECT CQ IDENT NODES PARMS ROUTES USERS)
HB9X-7*>HB9DIG>HB9DIG-7 [RR,P;6]
HB9X-6*>4U1ITU-8 (RR,F;3)
HB9DIG-7>HB9DIG*>HB9X-7 [I;1,6]CF:
þNET/ROM frame: orgin node DB0FRG-2 to dst node HB9X-7, ttl: 24
INFO ACK: ckt 0/238, rxseq 2
HB9X-7*>HB9X-9 [I;4,4]:
NON - Bid 21A90BHB9X deja recu
8>
HB9X-7*>HB9CED [RR,P;3]
HB9X-7*>HB9CED (RR,F;3)
HB9X-6*>4U1ITU-8 (RR;4)
 M1234 º VHF º          ÄÄÄ MONITOR CHANNEL ÄÄÄ          ³    º 23-MAR 12:34:56


ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

	If something is scrolled off-screen, press ALT/R or Up-arrow to
	review it again.  Reviewing is possible individually for all channels
	on packet (and for the single channel of the other modes). The lower
	(transmit) window will be superseded by:

ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ .... ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
			 Cursor on line   0 of 200
		     REWIEW - Use:   PgUp PgDn, ESC to exit
			   ALT/L - Snapshot to file
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

	Use the indicated keys for moving, and ESC to leave the reviewing.
	The number of lines which you have for reviewing depends on
	parameters in the configuration file. The minimum is 50, the maximum
	is about 500. These values can be set individually for each channel.

	Whenever you start reviewing, PHS makes a copy the current active
	receive window to the review buffer, and then covers the upper 85% of
	the receive window to present the review buffer. The "Cursor on line"
	gives you an indication where you are inside the review buffer.
	During review, receiving to the (mostly covered) receive window
	continues.

	ALT/L lets you snapshot the review buffer to a file in the current
	OS/2 directory. The filename is generated from the date and time and
	the extension is always "SNP". For the 23 October at 12:34:56 the
	generated filename will be "A23_1234.SNP" (see "Logging and Printing"
	for a discussion of the generated filenames). Furthermore, if a
	subdirectory "LOG" exists in the current directory, then the file is
	opened in the LOG subdirectory, otherwise it is opened in the current
	directory.




	You press ALT/H to get the heard list formatted and sorted last heard
	first:

ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
BBS HÕÍÍÍÍÍÍÍ HEARD LIST (entries: 10) - XXXX - <Enter> to connect ÍÍÍÍÍÍÍÍ¸
     ³  1. 23-MAR 12:34:56  HB9X-7                                         ³
Enreg³  2. 23-MAR 12:34:56  HB9CED-15                                      ³
Enreg³  3. 23-MAR 12:34:56  HB9DIG-7 via HB9DIG                            ³
     ³  4. 23-MAR 12:34:56  HB9AC-8 via HB9DIG HB9AC                       ³
Pas d³  5. 23-MAR 12:34:56  DG7KAR-8 via HB9DIG DB0DQ DB0GE-2              ³
HB9CE³  6. 23-MAR 12:34:56  HB9X-6                                         ³
DG7KA³  7. 23-MAR 12:34:56  HB9X-9                                         ³
HB9AC³  8. 23-MAR 12:34:56  DG7KAR-7                                       ³
HB9CE³  9. 23-MAR 12:34:56  HB9X-14                                        ³
HB9X-³ 10. 23-MAR 12:34:56  DB1EC-15                                       ³
HB9X-ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾
HB9DIG-7>HB9DIG*>HB9X-7 (RR,F;1)
HB9X-7*>HB9CED [I;1,2]:
tion pour l'instant.

(H)elp (C)heck (L)ist (R)ead (S)end (E)rase (D)ir (U)sage (SP)eak (Q)uit
HB9CED de HB9X>
HB9CED-15*>HB9X [I;2,0]:
C HB9N-7
HB9X-7*>HB9CED (RR;2)
 M1234 º VHF º          ÄÄÄ MONITOR CHANNEL ÄÄÄ          ³    º 23-MAR 12:34:56


ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

	If you select the raw heard list, you get the original frames
	unformatted but still sorted by time:

ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
EnregÕÍÍÍÍÍÍÍ HEARD LIST (entries: 10) - XXXX - <Enter> to connect ÍÍÍÍÍÍÍÍ¸
Enreg³  1. 23-MAR 12:34:56  HB9CED-15*>HB9X (RR;3)                         ³
     ³  2. 23-MAR 12:34:56  HB9X-7*>HB9CED (RR,F;2)                        ³
Pas d³  3. 23-MAR 12:34:56  HB9DIG-7>HB9DIG*>HB9X-7 (RR,F;1)               ³
HB9CE³  4. 23-MAR 12:34:56  HB9AC-8>HB9AC>HB9DIG*>HB9X-9 [C,P]             ³
DG7KA³  5. 23-MAR 12:34:56  DG7KAR-8>DB0GE-2>DB0DQ>HB9DIG*>HB9X-7 (RR,F;4) ³
HB9AC³  6. 23-MAR 12:34:56  HB9X-6*>4U1ITU-8 (DM,F)                        ³
HB9CE³  7. 23-MAR 12:34:56  HB9X-9*>HB9X-7 (DM,F)                          ³
HB9X-³  8. 23-MAR 12:34:56  DG7KAR-7*>4U1ITU-8 (RR;4)                      ³
HB9X-³  9. 23-MAR 12:34:56  HB9X-14*>HB9DIG>HB9AC>HB9AC-8 [I;2,1]:         ³
HB9DI³ 10. 23-MAR 12:34:56  DB1EC-15*>4U1ITU-8 [D,P]                       ³
HB9X-ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾
tion pour l'instant.
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ .... ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

	The heard list will contain a maximum of 50 different stations. If
	more than 50 stations have been heard, the oldest call is superseded.
	You use the arrow keys to scroll within the heard list. A scroll bar,
	which again is not visible here is moving - you can position the bar
	on an entry on the heard list and simply press the ENTER key to try a
	connect. You must first select an unconnected channel, pop up the
	heard-list by ALT/H, select the entry and press ENTER.

	The arrows are visible in place of the "XXXX" which you see here in
	the heard list title.  These little arrows cannot be used in this
	printout and had to be substituted.



	ALT/C pops up the Connect window, this has the same look-and-feel
	like the UNPROTO window which we discussed before. To summarize, if
	you want to initialize a connection, you have three choices:

     		- the Connect-window by ALT/C
     		- by a selection of the heard-list
     		- by an entry in the command directory (ALT/W), provided you
		  have preset connect commands there.

	ALT/D is used to initialize a disconnect.

	If someone is connecting you, PHS will give a sound (warble). For
	incoming connects the PK-232 selects the lowest unconnected channel,
	which might not necessarily be the channel which you have currently
	selected for display.  You will still realize such a connect because
	of the warble, and because the channels indicator is highlighted.

	Any text which you type will appear in the lower transmit window. If
	word-wrapping is on (which is the default, see ALT/T), your text will
	wrap. The input text is sent to the PK-232 when you press the ENTER
	key. It is then removed from the transmit window and inserted into
	the receive window.  Additionally the text is highlighted in the
	receive window, so you can easily distinguish between your text and
	the received text.

	Note that the transmit buffer of PHS is 250 characters. You will get
	the warning "At end of TX-buffer" if you reached the end of the
	buffer. You will get the warning "At beginning of TX-buffer" when you
	erase characters and no more characters are available for deletion.

                        BINARY FILE TRANSFERS
                        ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

	The next and last chapters for the Packet-modes show how binary
	transfers are done. PHS implements the YAPP protocol as defined by
	Jeff Jacobson, WA7MBL.  Care should be exercised when employing
	binary transfers because upon entry of the yapp transfer mode, PHS
	will change the PK-232 parameters to obtain maximum throughput. These
	parameters are reset to the previous values when you leave the yapp
	transfer mode. To keep friends, yapp-transfers should not be done on
	qso channels - use a free channel. You also CANNOT change channels
	during a binary transfer, you will have to finish or abort the
	transfer first.  Consequently you can invoke a binary transfer on ONE
	channel only. Again, this is optimized for throughput and is intended
	to provide fast transfers.

	Yapp uploading (sending of a binary file) is invoked with the PgUp
	key, downloading (receiving) with the PgDn key. PHS will ask you for
	a filename first, and then enter the yapp transfer mode. Note that
	when you are receiving, you will also have to specify the filename of
	a file which will get the data.

	Note: YAPP transfers have not been extensively tested in the OS/2
	      versions.



	When sending a binary transfer, you get a window like this:

ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
                    ÕÍÍÍÍÍ Uploading (YAPP) - ALT/A: Cancel - ALT/K: Kill ÍÍÍÍÍ¸
23-MAR-89  12:29:32 ³                                                          ³
                    ³    FILE: PHS.EXE                                         ³
                    ³    Size:  198583                                         ³
                    ³    Date: 23-MAR-89 20:41                                 ³
                    ³                                                          ³
                    ³  Header:  PHS.EXE  198583 bytes, 23-MAR-89 20:41         ³
                    ³   Bytes:    11938 read,   10414 sent                     ³
                    ³    Rate:       95 bytes/sec, time to go:  33:00          ³
                    ³                                                          ³
                    ³   STATE:  Sending DATA                                   ³
                    ³                                                          ³
                    ³   TNC buffer full, waiting.                              ³
                    ³                                                          ³
                    ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾




 M1234 º VHF º UA:06 RTY:00 ³ INFORMATION TRANSFER       ³    º 23-MAR 12:34:56


ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

	The bytes read indicate the number of bytes read from the file, the
	bytes sent is the number of acknowledged bytes. The message "TNC
	buffer full, waiting." indicates that the PK-232s buffer are full and
	that PHS is waiting for the PK-232 to become ready for another slice
	of data.

	Unfortunately the PK-232 does not buffer more than MAXF frames, which
	reduces the maximum obtainable troughput to below 100 bytes per
	second. With other devices like TNC-2 or the PC*Packet Adapter it is
	possible to reach up to 125 bytes per second. Yes, the link is 1200
	bauds, but AX-25 is a syncronous protocol, so a single data byte is
	not framed with start and stop bits as on asynchronous RS-232 links.
	The theoretical maximum is 1200/8 bytes per second, and the AX-25
	protocol overhead reduces this number then by at least 15%.

	If you want to abort a transfer, you can use ALT/A to cancel it,
	which uses the cancel mechanism of the yapp protocol. If you got a
	bad link however you will have a TNC full with untransmitted frames
	and the frame with the cancel request queued behind. Unfortunately
	the only way to flush the untransmitted data in the PK-232 is a
	disconnect.

	This is why ALT/K has been introduced: ALT/K will kill the transfer
	by disconnecting the link and then will re-connect. All of this is
	accompanied by messages on the screen.

	The YAPP-download window is similar to the upload window. Note
	however that the number for the troughput (bytes/sec) will always
	differ slightly between receiver and sender - there are always some
	data packets on the air.




                                AMTOR MODES
                                ÄÄÄÄÄÄÄÄÄÄÄ

	ALT/Z in the amtor modes pops up the amtor-modes help screen:

ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

  ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ AMTOR MODES ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
  ³                                     º                                     ³
  ³ ALT/P   TNC mode param setup menu   º ALT/I   TNC text-param setup menu   ³
  ³ ALT/T   PHS parameter setup menu    º ALT/V   View OS/2 directory         ³
  ³ ALT/W   Command string directory    º ALT/F   View function-key setup     ³
  ³ ALT/L   Logging (capture) on/off    º ALT/R   or  Review (scrollback)    ³
  ³ ALT/S   Send an ASCII file          º ALT/K   Call Editor                 ³
  ³ ALT/B   Enter urcall (remote call)  º CTRL/U  Erase TX-window             ³
  ³ ALT/X   Exit PHS                    º CTRL/X  Erase RX-window             ³
  ³ ALT/M   Switch TNC modes            º ESC     Direct command entry        ³
  ³ ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ º ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ ³
  ³ ALT-C   Start ARQ call              º GRAY +  Start FEC transmit          ³
  ³ ALT-Y   Start SELFEC call           º GRAY -  FEC: Receive - immediate    ³
  ³ INS     LISTEN: Resynchronize       º         ARQ: Break link - immediate ³
  ³         ARQ: Force changeover       º GRAY *  Clear PK-232 tx buffer      ³
  ³ DEL     Force LETTERS case          º        Toggle LISTEN <> STANDBY    ³
  ³ ÄÄÄÄÄÄÄÄÄÄÄÄÄ in text ÄÄÄÄÄÄÄÄÄÄÄÄÄ º ÄÄÄÄÄÄÄÄÄÄÄÄÄ in text ÄÄÄÄÄÄÄÄÄÄÄÄÄ ³
  ³ CTRL-D  FEC: Switch to receive      º CTRL-O  Send LETTERS character      ³
  ³         ARQ: Break link             º CTRL-N  Send FIGURES character      ³
  ³ CTRL-F  Like CTRL-D, add CW-id      º CTRL-B  Send "urcall de mycall"     ³
  ³ CTRL-T  Send date+time              º END     Send "BTU <CTRL-B> +?"      ³
 A³                                     º                                     ³
  ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾


ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

	The single 'A' visible on the left side is from the covered status
	line. If you had setup another screen size before calling PHS (e.g.
	80*43), then the statusline would not be covered by the window and
	would be visble.

	The status line in the Amtor modes is like:

ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
 AMTOR LISTEN  º RECEIVE  ³  Phasing      º              ³    º 23-MAR 12:34:56
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

	where the second field will indicate either "RECEIVE" or "TRANSMIT",
	and the first field will show "AMTOR LISTEN", "AMTOR STANDBY" "AMTOR
	QSO", "FEC" or "SELFEC". The third field indicates the current PK-232
	status and closely follows the LED indicators of the PK-232. The
	forth field is always empty. The fifth field will contains the "L"
	indicator, when logging is on.

	Opposed to the packet mode, where your text is sent to the PK-232
	when you press the ENTER key, in non-packet modes your text is sent
	to the PK-232 on a word-by-word basis, and is buffered in the PK-232.
	The text is not cleared in the lower transmit window but instead it
	will scroll there. It is echoed in the upper receive window by the
	PK-232 whenever it is sent out (echo-as-sent). The wordwise operation
	allows you to correct only the current word. It is not possible to
	correct text which has already been sent to the PK-232. For an
	indication about what has already been sent to the PK-232, the
	already-sent text is highlighted. So if you typed in:

        	Did you have to apply any modificati

	and the cursor is positioned after the 'i', then all previous lines,
	and this line up to and including the word 'any' is highlighted, but
	'modificati' is not, because it has not yet been sent.

	You start a FEC transmission with the GRAY PLUS key (on the keypad).
	Normally you will not stop the transmission with the GRAY MINUS key
	because the PK-232 will then immediately switch to receive,
	regardless of still untransmitted text.  If you switch to receive
	with untransmitted text, you will get a warning message from PHS
	("transmit data remaining"). This data will be sent the next time
	when you switch to transmit. However you have the option to flush the
	data by clearing the PK-232's transmit buffer with the GRAY-* key.

	Anytime you can insert a CTRL/D or CTRL/F into the text which you
	input. The PK-232 will switch to receive whenever it detects such a
	character (refer to the PK-232 manual) in the transmit data stream.
	Just a note: when you insert a CTRL/D followed by a carriage return
	(Enter-key), then you will get the transmit-data-remaining warning,
	because after switching to receive by the CTRL/D, the carriage return
	is still untransmitted.

	To start a Amtor QSO, press ALT/C and you will get a small window
	which lets you enter the other stations selcal. For a SELFEC
	transmission, press ALT/Y.

	You may use ALT/B to pop up a window which lets you enter the remote
	stations callsign, and once you did, whenever you insert a CTRL/B
	into the transmit text, it is replaced by PHS with the string "
	<remote-callsign> DE <my-callsign> ".  My-callsign is from line one
	in the configuration file (a possible packet-SSID is removed).

	For convenience, in ARQ, the END key inserts the Amtor-changeover
	signal "+?" into the transmit text.

	If you are in Amtor-Listen mode and you have difficulties to monitor
	an Amtor-qso use the INS key to force a resynchronisation. If you are
	in an ARQ qso, the INS key forces a changeover.



	ALT/P in the amtor modes pops up the amtor-modes PK-232 parameter
	setup window:

ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

                                   ÕÍÍÍÍÍÍÍÍÍÍ PK-232 Parameters ÍÍÍÍÍÍÍÍÍÍ¸
                                   ³                                       ³
                                   ³ ADELAY          4   SRXALL          Y ³
                                   ³ ARQTMO         60   TXREV           Y ³
                                   ³ ARQTOL          3   WIDESHFT        N ³
                                   ³ CODE            2   WRU             N ³
                                   ³ MYALTCAL     HCVV                     ³
                                   ³ MYIDENT   KBPCVVV   <F1>  HELP        ³
                                   ³ MYSELCAL     HCVV   <ESC> EXIT        ³
                                   ³ RFEC            Y   <F10> SET PARAM   ³
                                   ³ RXREV           N                     ³
                                   ³                                       ³
                                   ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾

 AMTOR LISTEN  º RECEIVE  ³  Phasing      º              ³    º 23-MAR 12:34:56

  ARQ transmit delay in 10mS (range 1-9)
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ



                                PACTOR MODES
                                ÄÄÄÄÄÄÄÄÄÄÄÄ

	ALT/Z in the pactor modes pops up the pactor-modes help screen:

ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

 ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ PACTOR MODES ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
 ³                                     º                                     ³
 ³ ALT-P   PK-232 param setup menu     º ALT-I   PK-232 textparam setup menu ³
 ³ ALT-T   PHS parameter setup menu    º ALT-V   View OS/2 directory         ³
 ³ ALT-W   Command string directory    º ALT-F   View function-key setup     ³
 ³ ALT-L   Logging (capture) on/off    º ALT-R   or  Review (scrollback)    ³
 ³ ALT-S   Send an ASCII file          º ALT-K   Call Editor                 ³
 ³ ALT-B   Enter urcall (remote call)  º CTRL-U  Erase TX-window             ³
 ³ ALT-X   Exit PHS                    º CTRL-X  Erase RX-window             ³
 ³ ALT-M   Switch PK-232 modes         º ESC     Direct command entry        ³
 ³ ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ º ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ ³
 ³ ALT-C   PACTOR connect menu         º ALT-D   CONNECT: Break link immedia ³
 ³ GRAY *  Clear PK-232 tx buffer      º GRAY +  Start UNPROTO transmit      ³
 ³ GRAY -  UNPROTO: Receive, immediate º INS     LISTEN: Resynchronize       ³
 ³         CONNECT: Break link immedia º         CONNECT: Force changeover   ³
 ³ DEL     CONNECT: Break link         º        Toggle LISTEN <-> STANDBY   ³
 ³ ÄÄÄÄÄÄÄÄÄÄÄÄÄ in text ÄÄÄÄÄÄÄÄÄÄÄÄÄ º ÄÄÄÄÄÄÄÄÄÄÄÄÄ in text ÄÄÄÄÄÄÄÄÄÄÄÄÄ ³
 ³ CTRL-D  UNPROTO: Switch to receive  º CTRL-Y  CONNECT: Changeover         ³
 ³         CONNECT: Break link         º CTRL-F  Like CTRL-D, add CW-id      ³
 ³ CTRL-B  Send "urcall de mycall"     º CTRL-T  Send date+time              ³
 ³ END     Send "BTU <CTRL-B><CTRL-Y>" º                                     ³
P³                                     º                                     ³
 ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾

	The single 'P' visible on the left side is from the covered status
	line. If you had setup another screen size before calling PHS (e.g.
	80*43), then the statusline would not be covered by the window and
	would be visble.

	The status line in the Pactor modes is like:

ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
 PACTOR LISTEN º RECEIVE  ³  Phasing      º              ³    º 23-MAR 12:34:56
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

	where the second field will indicate either "RECEIVE" or "TRANSMIT",
	and the first field will show "PACTOR LISTEN", "PACTOR STANDBY",
	PACTOR CONNECT" or "PACTOR UNPROTO". The third field indicates the
	current PK-232 status and closely follows the LED indicators of the
	PK-232. The forth field is always empty. The fifth field will
	contains the "L" indicator, when logging is on.

	Opposed to the packet mode, where your text is sent to the PK-232
	when you press the ENTER key, in non-packet modes your text is sent
	to the PK-232 on a word-by-word basis, and is buffered in the PK-232.
	The text is not cleared in the lower transmit window but instead it
	will scroll there. It is echoed in the upper receive window by the
	PK-232 whenever it is sent out (echo-as-sent). The wordwise operation
	allows you to correct only the current word. It is not possible to
	correct text which has already been sent to the PK-232. For an
	indication about what has already been sent to the PK-232, the
	already-sent text is highlighted. So if you typed in:

        	Did you have to apply any modificati

	and the cursor is positioned after the 'i', then all previous lines,
	and this line up to and including the word 'any' is highlighted, but
	'modificati' is not, because it has not yet been sent.

	You start an UNPROTO transmission with the GRAY PLUS key (on the
	keypad).  Normally you will not stop the transmission with the GRAY
	MINUS key because the PK-232 will then immediately switch to receive,
	regardless of still untransmitted text.  If you switch to receive
	with untransmitted text, you will get a warning message from PHS
	("transmit data remaining"). This data will be sent the next time
	when you switch to transmit. However you have the option to flush the
	data by clearing the PK-232's transmit buffer with the GRAY-* key.

	Anytime you can insert a CTRL/D or CTRL/F into the text which you
	input. The PK-232 will switch to receive whenever it detects such a
	character (refer to the PK-232 manual) in the transmit data stream.
	Just a note: when you insert a CTRL/D followed by a carriage return
	(Enter-key), then you will get the transmit-data-remaining warning,
	because after switching to receive by the CTRL/D, the carriage return
	is still untransmitted.

	To start a Pactor QSO, press ALT/C and you will get a small window
	which lets you enter the other stations callsign.

	As soon as you are connected in Pactor, the other (remote) stations
	callsign will appear in the statusline. When you are transmitting
	during the qso and want to change-over, type CTRL-Y or press the END
	key to get the BTU-string which is:

	    BTU <remote callsign> de <my callsign><CTRL-Y>

	If you are in Pactor-Listen mode and you have difficulties to monitor
	an Pactor-qso use the INS key to force a resynchronisation. If you are
	connected, the INS key forces an immediate (!) changeover.



	ALT/P in the pactor modes pops up the pactor-modes PK-232 parameter
	setup window:

ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

                                                  Õ PK-232 Parameters ¸
                                                  ³                   ³
                                                  ³ CODE            2 ³
                                                  ³ MYPTCALL   HB9CVV ³
                                                  ³ PT200           Y ³
                                                  ³ PTHUFF          1 ³
                                                  ³                   ³
                                                  ³ <F1>  HELP        ³
                                                  ³ <ESC> EXIT        ³
                                                  ³ <F10> SET PARAM   ³
                                                  ³                   ³
                                                  ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾




 PACTOR LISTEN º RECEIVE  ³  Phasing      º              ³    º 23-MAR 12:34:56


ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ



                                RTTY MODE
                                ÄÄÄÄÄÄÄÄÄ

	ALT/Z in rtty mode pops up the rtty-mode help screen:
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
  ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ RTTY MODE ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
  .                                     .                                     .
  .                                     .                                     .
  ³ ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ º ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ ³
  ³ GRAY +  Transmit                    º GRAY *  Clear TNC transmit buffer   ³
  ³ GRAY -  Receive - immediate         º DEL     Force LETTERS case          ³
  ³ ÄÄÄÄÄÄÄÄÄÄÄÄÄ in text ÄÄÄÄÄÄÄÄÄÄÄÄÄ º ÄÄÄÄÄÄÄÄÄÄÄÄÄ in text ÄÄÄÄÄÄÄÄÄÄÄÄÄ ³
  ³ CTRL/D  Switch to receive           º CTRL/O  Send LETTERS character      ³
  ³ CTRL/F  Like CTRL/D, add CW-id      º CTRL/N  Send FIGURES character      ³
  ³ CTRL/B  Send " urcall de mycall "   º CTRL/T  Send date+time              ³
  ³                                     º                                     ³
  ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾

 RECEIVE  º RTTY          º                              ³    º 23-MAR 12:34:56


ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

	ALT/P in rtty mode pops up the rtty mode PK-232 parameter setup
	window:
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

                                                  ÕÍ TNC Parameters ÍÍ¸
                                                  ³                   ³
                                                  ³ ACRRTTY        72 ³
                                                  ³ CCITT           N ³
                                                  ³ CODE            0 ³
                                                  ³ CRADD           N ³
                                                  ³ DIDDLE          Y ³
                                                  ³ RBAUD          45 ³
                                                  ³ RXREV           N ³
                                                  ³ TXREV           N ³
                                                  ³ USOS            Y ³
                                                  ³ WIDESHFT        N ³
                                                  ³ WRU             N ³
                                                  ³                   ³
                                                  ³ <F1>  HELP        ³
                                                  ³ <ESC> EXIT        ³
                                                  ³ <F10> SET PARAM   ³
                                                  ³                   ³
                                                  ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ .... ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ



                                ASCII MODE
                                ÄÄÄÄÄÄÄÄÄÄ

	ALT/Z in the ascii mode pops up the ascii-mode help screen:
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
  ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ ASCII MODE ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
  .                                     .                                     .
  .                                     .                                     .
  ³ ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ º ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ ³
  ³ GRAY +  Transmit                    º GRAY *  Clear TNC transmit buffer   ³
  ³ GRAY -  Receive - immediate         º                                     ³
  ³ ÄÄÄÄÄÄÄÄÄÄÄÄÄ in text ÄÄÄÄÄÄÄÄÄÄÄÄÄ º ÄÄÄÄÄÄÄÄÄÄÄÄÄ in text ÄÄÄÄÄÄÄÄÄÄÄÄÄ ³
  ³ CTRL/D  Switch to receive           º CTRL/F  Like CTRL/D, add CW-id      ³
  ³ CTRL/B  Send "urcall de mycall"     º CTRL/T  Send date+time              ³
  ³                                     º                                     ³
  ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾

 RECEIVE  º ASCII         º                              ³    º 23-MAR 12:34:56


ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

	ALT/P in ascii mode pops up the ascii mode PK-232 parameter setup
	window:
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

                                                  ÕÍ TNC Parameters ÍÍ¸
                                                  ³                   ³
                                                  ³ ABAUD         300 ³
                                                  ³ ACRRTTY        72 ³
                                                  ³ DIDDLE          Y ³
                                                  ³ RXREV           N ³
                                                  ³ TXREV           N ³
                                                  ³ WIDESHFT        N ³
                                                  ³ WRU             N ³
                                                  ³                   ³
                                                  ³ <F1>  HELP        ³
                                                  ³ <ESC> EXIT        ³
                                                  ³ <F10> SET PARAM   ³
                                                  ³                   ³
                                                  ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ .... ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ



                                MORSE MODE
                                ÄÄÄÄÄÄÄÄÄÄ

	ALT/Z in the morse mode pops up the morse-mode help screen:
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
  ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ MORSE MODE ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
  .                                     .                                     .
  .                                     .                                     .
  ³ ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ º ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ ³
  ³ GRAY +  Transmit                    º INS     Unlock receive speed (WPM)  ³
  ³ GRAY -  Receive - immediate         º DEL     Lock receive speed (WPM)    ³
  ³ GRAY *  Clear TNC transmit buffer   º                                     ³
  ³ ÄÄÄÄÄÄÄÄÄÄÄÄÄ in text ÄÄÄÄÄÄÄÄÄÄÄÄÄ º ÄÄÄÄÄÄÄÄÄÄÄÄÄ in text ÄÄÄÄÄÄÄÄÄÄÄÄÄ ³
  ³ CTRL/D  Switch to receive           º CTRL/B  Send "urcall de mycall"     ³
  ³ CTRL/T  Send date+time              º                                     ³
  ³                                     º                                     ³
  ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾

 RECEIVE  º MORSE         ³ 20 WPM º                     ³    º 23-MAR 12:34:56


ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

	ALT/P in morse mode pops up the morse mode PK-232 parameter setup
	window:
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

                                                  ÕÍ TNC Parameters ÍÍ¸
                                                  ³                   ³
                                                  ³ MSPEED         20 ³
                                                  ³ MWEIGHT        10 ³
                                                  ³                   ³
                                                  ³ <F1>  HELP        ³
                                                  ³ <ESC> EXIT        ³
                                                  ³ <F10> SET PARAM   ³
                                                  ³                   ³
                                                  ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ .... ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ



                                SIGNAL MODE
                                ÄÄÄÄÄÄÄÄÄÄÄ

	ALT/Z in the signal mode pops up the signal-mode help screen:
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

  ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ SIGNAL MODE ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
  .                                     .                                     .
  .                                     .                                     .
  ³ ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ º ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ ³
  ³ INS     Ok - accept & switch        º                                     ³
  ³ ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ NOTE ÄÄÄÄÄÄÄÄÄÄÄÄÄÄ º                                     ³
  ³    DO NOT SWITCH TO FAX or NAVTEX   º                                     ³
  ³                                     º                                     ³
  ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾



 RECEIVE  º SIGNAL                                       ³    º 23-MAR 12:34:56


ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

	Please do not switch to an unsupported mode (FAX or NAVTEX), it will
	not work.

	There is no signal mode PK-232 parameter setup window.




	Finally, the secret ALT-key:

	Whenever you give ALT/A, any incoming message to the currently
	selected window is accompanied by a deep summing tone. Another ALT/A
	disables the sound. There is no visible indication of ALT/A, because
	obviously there is an audible one.  I often use ALT/A when my partner
	says "wait a minute", because I have no klicking relais in my TRX
	which would attract my attention after that minute. Obviously, ALT/A
	should be avoided in non-packet modes...




                        THE CONFIGURATION FILE
                        ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ

	PHS reads the configuration file whenever you start PHS.  The
	configuration file contains information about hardware and software
	parameters. If this information is not accurate, PHS will be unable
	to proceed.

	You must edit the file PHS.CFG to reflect your hardware
	configuration, callsigns and texts. If you are not able to edit a
	text-file you cannot operate PHS.

	Here is an example of a configuration file:

ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
	Devicetype = 4              ; PK-900.
	Callsign   = HB9CVV         ; My callsign
	;PTCallsign = HB9CVV/A      ; My Pactor callsign (optional)
	Selcall    = HCVV           ; My selcall
	Comport    = COM4           ; COMport name
	Baudrate   = 9600           ; The baudrate
	UseRS232Controls        = YES
	ChannelMwindowsize      = 200
	Channel1Windowsize      = 200
	Channel2Windowsize      = 100
	Channel3Windowsize      = 100
	Channel4Windowsize      =  50
	ChannelM2windowsize     = 200	; Channel M2 and A-D for PK-900 only.
	ChannelAWindowsize      = 200
	ChannelBWindowsize      = 100
	ChannelCWindowsize      = 100
	ChannelDWindowsize      =  50
	StartupPK232mode	= 2
	EditorColumnSize        = 70
	EditorRowSize		= 0
	MFILTERenabled          = NO
	UTCoffsethours		= -1
	Polldelay		= 50
	ResetDeviceOnExit       = YES
	Skip_ParamInit          = NO

	CommandString           = C DK1SL VIA HB9F
	CommandString           = C HB9SDD
	CommandString           = C HB9PD
	CommandString           = C HB9PD VIA HB9PD-7

	StartupDeviceCmd	= MYALIAS BIENNE
	StartupDeviceCmd	= TXREV YES
	StartupDeviceCmd	= RXREV NO
	StartupDeviceCmd	= TXDELAY 30/50

	ConnectMsg = Operator is OFFLINE, this message is recorded...
	BeaconText = *** Peter, Qth: Port/Biel - JN37OC ***

	F01KeyTitle = Name & Qth
	F01KeyText = My name is Peter, the QTH is Port, 20 miles west...

	F02KeyTitle = Rig SHORT
	F02KeyText = -
	The rig here is: a 486/33-PC, PK-900, Yaesu FT-990, 100W to a GP. -
	I am using my own PK-232/900 Hostmode Server (PHS) program under OS/2.

	F03KeyTitle = Rig LONG
	F03KeyText = -
	The rig here is:-
	-----------------------------------------------------------
	Programs  : THS (TNC Hostmode Server - OS/2) V6.0-
	            PHS (PK-232/900 Hostmode Server - OS/2) 6.0.-
	Computers : (1) 486/33, 16MB RAM, 660MB disk, OS/2 2.1.-
	            (2) 486/33, 16MB RAM, 660MB disk, OS/2 2.0.-
	TRX       : FT-990, 100W.-
	            TW-4100E, 45W.-
	Antenna   : DX-2000 GP for HF.-
	            X-300 2m/70cm vertical.-
	TNC       : TNC-1 with TNC-2 board and WA8DED firmware.-
	            PK-232 with Pactor firmware.-
	            PK-900 with Pactor firmware.-
	-----------------------------------------------------------
	In use: PHS, 486/33, PK-900, FT-990, GP.

	F05KeyTitle = FEC CQ
	F05KeyText = -
	4 CQ CQ CQ CQ CQ DE HB9CVV HB9CVV HB9CVV (HCVV)-
	3 CQ CQ CQ CQ CQ DE HB9CVV HB9CVV HB9CVV (HCVV)-
	2 CQ CQ CQ CQ CQ DE HB9CVV HB9CVV HB9CVV (HCVV)-
	1 CQ CQ CQ CQ CQ DE HB9CVV HB9CVV HB9CVV (HCVV)-
	SELCAL HCVV HCVV HCVV - PSE KKKKK-
	(

	F06KeyTitle = RYRYRY
	F06KeyText = RYRYRYRYRYRYRYRYRYRYRYRYRYRYRYRYRYRYRYRYRYRYRY

	F07KeyTitle = Pactor CQ
	F07KeyText = -
	4 CQ CQ CQ CQ CQ DE HB9CVV HB9CVV HB9CVV-
	3 CQ CQ CQ CQ CQ DE HB9CVV HB9CVV HB9CVV-
	2 CQ CQ CQ CQ CQ DE HB9CVV HB9CVV HB9CVV-
	1 CQ CQ CQ CQ CQ DE HB9CVV HB9CVV HB9CVV-
	PSE KKKKK-
	(

	ReceiveWindow_Text		= Green on Black
	TransmitWindow_Text             = Cyan on Black
	StatuslineText                  = White on Blue
	Review_Text                     = White on Blue

	ServiceWindow_Border            = White on Blue
	ServiceWindow_Text              = Blue on lightgrey

	CommandEntry_Border             = White on Black
	CommandEntry_Text               = Yellow on Red
	CommandEntry_InactiveField      = Yellow on Green
	CommandEntry_ActiveField        = Yellow on Green

	ParameterDialog_Border          = LightGreen on Black
	ParameterDialog_Text            = Black on lightgrey
	ParameterDialog_InactiveField   = Blue on Lightgrey
	ParameterDialog_ActiveField     = White on Blue

	ParameterHelp_Border            = White on Blue
	ParameterHelp_Text              = Lightcyan on Blue

	FileXfer_Border                 = Black on lightgrey
	FileXfer_Text                   = White on Brown

	EditorWindow_Border             = White on Blue
	EditorWindow_Text               = Yellow on Blue
	EditorWindow_ActiveField        = Yellow on Red

	HeardList_Border                = LightRed on Brown
	HeardList_Text                  = White on Brown

	;OnScreenChannelId               = LightBlue on Lightgrey
	OnScreenChannelId               = White on Blue
	OffScreenChannelId              = Cyan on Blue
	OffScreenChannelIdData          = Yellow on Blue
	SentTextInReceiveWindow         = default
	EchoAsSentText			= default

ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

	All lines have the format: KEYWORD = PARAMETER and are not case
	sensitive. A semicolon must preceed comments. If a line ends with a
	dash ('-'), then the dash is replaced by a newline character and the
	following line is appended.  This feature is used for multi-line text
	string parameters.

	There are mandatory and optional keywords. The CALLSIGN keyword
	(obviously) is mandatory, CHANNEL1_WINDOWSIZE is not - if you omit an
	optional keyword, you get the defaults.

	"DeviceType"

		Use '1' if you use a TNC-1 with the WA8DED (or equivalent)
		firmware, a '2' for a TNC-2 with the WA8DED firmware, a '3'
		for the PK-232 and a '4' for a PK-900. Mandatory.

	"Callsign" and "Selcall"

		You guessed it. Both are mandatory for PHS, for THS, only
		"Callsign" is mandatory.

	"PTCallsign"

		Callsign for Pactor. Defaults to "Callsign".

	"Comport" and "Baudrate"

		The Comport name and the baudrate to be used. Mandatory.

	"UseRS232Controls"

		Use 'NO' if you only have a 3-wire connection. Optional, the
		default is YES.

	"ChannelMwindowsize", "Channel1windowsize", "Channel2windowsize",
	"Channel3windowsize" and "Channel4windowsize"

		Number of lines for the monitor channel and the four
		operating channels. Optional, the default for each is 200.

	"StartupPK232mode"

		You can select the initial PK-232 mode here. The mode numbers
		are 0 to 9 for Packet-VHF, Packet-HF, Amtor-Listen,
		Amtor-Standby, RTTY, Ascii, Morse, Signal, Pactor-listen and
		Pactor-Standby mode.  This is the mode which the PK-232 should
		enter immediately after startup.  Optional, PHS only. The
		default is 2 for Amtor-Listen.

		If RESETONDEVICEEXIT is NO, you will instead get the actual
		device's mode.

	"EditorColumnSize" and "EditorRowSize"

		Defines the editor window size, columns and rows. The range
		for the column is 64 to 79, and includes the window border.
		If a given value exceeds one of the limits, then the
		according limit value is taken.  If you omit this parameter,
		or specify a zero, then the default value of 76 is taken. The
		range for the row depends on the size of the (upper) receive
		window, which itself depends on the number of lines of your
		current video mode. The range if from half that window to
		full size minus one. For the standard 25 line mode, the range
		is 10 to 20, also including the border.  The default here is
		the lowest value, i.e. half the size of the receive window.

	"MFILTERenabled"

		This determines the initial value of the MFILTER variable,
		see the description of the ALT/T command.  "NO" disables the
		filtering, "YES" enables it.  Optional, the default (e.g. if
		omitted) is NO.

	"BELLenabled"

		This determines the initial value of the BELL variable,
		see the description of the ALT/T command. "NO" disables the
		filtering, "YES" enables it. Optional, the default (e.g. if
		omitted) is "NO".

	"UTCoffsethours"

		During startup, PHS gets the current system time of your PC,
		adds the "UTCoffsethours", and loads this date and time into
		the PK-232. The intention is to have the PK-232 loaded with
		the UTC rather than with the local time - in case you want to
		use the CTRL/T feature of the PK-232 to send date and time.
		Note however that if there is a non-zero UTC offset
		specified, then the link status messages (e.g.  "CONNECTED
		to") are always time-stamped by the PK-232 and will
		consequently show the PK-232s time. This time differs by the
		offset hours from the time on the status line of PHS.

		The date/time of the PK-232 is refreshed every full hour by
		PHS because the PC's clock is more accurate that the PK-232
		clock.

		Optional, PHS only. The default is zero.

	"Polldelay"

		To avoid an excessive system load, THS/PHS does not poll
		the device continuosly but inserts small delays between
		successive polls. You may somewhat finetune Systemload vs
		THS/PHS performance here.  The range is 1 to 999 mS.

		Optional, the default is 50 (mS). You can change this
		parameter also online in the ALT-T window.

		Note however that when THS/PHS is run in an AVIO window, 
		considerable CPU time may be needed for the text display 
		(depending how fast your video system is).

	"ResetDeviceOnExit"

		Normally, THS and PHS will reset the device during startup,
		to get clean conditions for the price of loosing all stored
		information. If ResetDeviceOnExit is NO, then THS/PHS does
		not reset the device but tries to derive the devices current
		state. This is however not fail safe under all conditions.
		The preferred value for this optional parameter is the
		default of YES.

	"Skip_Paraminit"

		If NO, then PHS/THS does not load the parameters during
		startup. Not doing this, the device can be in a state
		where the operation of PHS will fail. You should set
		this parameter only to NO when you have used PHS/THS
		for a while and do not use other terminal programs
		which might modify these parameters to their own use.

	"CommandString"

		The parameter is a text string and must contain a valid TNC
		or PK-232 command.  Up to 20 "CommandString" lines with a
		text not exceeding 72 characters are possible.  They are
		stored by THS/PHS and presented together with a selection
		character when you press ALT/W.  When you press the selection
		character or move the bar to the desired entry, then the
		associated string is sent as a command to the on-screen
		channel. Intended to build a call-sign directory for
		connects, you may however use other commands there as well,
		so it is called "Command String Directory". CommandStrings
		are optional.

		THS users note: The TNC commands use the TAPR syntax, NOT the
		more cryptic WA8DED syntax.

	"StartupDeviceCmd"

		You can specify up to 10 StartupDeviceCmd lines. The
		parameter text must not exceed 40 characters and is sent as
		command to the TNC/PK-232 when THS/PHS loads the TNC/PK-232
		parameters during startup.

		This is done *after* THS/PHS has sent the default set of
		parameter commands and so allows the user to override the
		default parameter set of THS/PHS.  You should however take
		some care - the text is sent must be a valid command and can
		only contain a command which does not interfere with THS/PHS
		operation. The non-interfering commands which appear in the
		ALT/P windows. Optional.

	"ConnectMsg"

		The parameter text is your connect message, and may not
		exceed 72 characters, if it does, then the text is truncated.
		This text is loaded connect message any time online.
		Mandatory.

	"BeaconText"

		The parameter text is your beacon text, and may not exceed 72
		characters, if it does, then the text is truncated. This text
		is loaded into the TNC/PK-232 when THS/PHS is started. You
		can however alter your cbeacon text any time online.
		Mandatory.

	"F01KeyTitle" & "F01KeyText" to "F10KeyTitle" & "F10KeyText"

		The function key title string and the function key text is
		assigned to the appropriate function key. The keytitle string
		is a descriptor text (up to 30 characters), the keytext
		string cannot exceed 1000 characters. The keytext strings are
		intended for reasonable sized texts like station descriptions
		or cq calls.

		When you press ALT/F then THS/PHS shows the titles of the
		text strings in a window box. The titles also come up when
		you press a function key which has nothing assigned.

		When you press a function key to which a text has been
		assinged, THS/PHS will send this text string to the
		TNC/PK-232.

		The function-key text must contain only printable characters,
		and two characters have a special meaning: The '(' character
		at the end of a line (and only at the end of a line !) is
		translated into CTRL/D when PHS reads the line.  The '<'
		character is translated into CTRL/F (if at the end of a
		line).  CTRL/D and CTRL/F are used by the PK-232 to switch to
		receive when embedded in text.

		In the sample CFG-file you find a FEC-cq call. The single
		line with the opening-bracket character (which is at the end
		of that line) is translated into CTRL/D and the PK-232 will
		switch to receive at the end of this cq-call.

		All FxxKeyTitle and FxxKeyText keywords are optional.

	The COLOR keywords.

		The (mandatory) color keywords are used to define the
		appearance of THS/PHS. You may alter the parameters to fit
		your taste. The parameters have the form

			<foreground color> on <background color>

		Possible colors are:

			Foreground      Background

			BLACK		BLACK
			BLUE		BLUE
			GREEN		GREEN
			CYAN		CYAN
			RED		RED
			MAGENTA		MAGENTA
			BROWN		BROWN
			LIGHTGRAY	LIGHGRAY
			DARKGRAY	|
			LIGHTBLUE	|
			LIGHTGREEN	|
			LIGHTCYAN	|- not for background
			LIGHTRED	|
			LIGHTMAGENTA	|
			YELLOW		|
			WHITE		|

	"OnScreenChannelId"
	"OffScreenChannelId"
	"OffScreenChannelIdData"

		On the left side of the statusline in the Packet-mode are the
		channel indicators: the string "M1234" - for the monitor
		channel and the channels one to four. One of these channels
		is visible on-screen, all others are off-screen. You use the
		left and right arrow keys to get the desired channel
		on-screen. Because all channels are always active, an
		off-screen channel may receive date any time.

		"OnScreenChannelId" defines the color attributes of the
		on-screen channel, "OffscreenChannelId" defines the color
		attributes for an off-screen channel which has not got new
		received data, and "OffscreenChannelIdData" defines the color
		attributes for an off-screen channel which has got new data.

		Whenever an off-screen channel receives new, unseen (because
		it is off-screen) data, then, to give you an indication, the
		color attribute changes from "OffScreenChannelId" to
		"OffscreenChannelIdData".

	"SentTextInReceiveWindow"

		In all modes, the text you type is echoed in the lower
		(transmit) window.  In the packet mode, when you send the
		text by typing a carriage return, the text is moved to the
		upper (receive) window, and the transmit window is cleared.
		THS/PHS uses different attributes so you can easily
		distinguish the text which you sent from the text you
		receive.  By default, the text sent has the same text and
		background color as the received text, but is intensified.
		This is what you get if you specify "SentTextInReceiveWindow
		= Default". If specify a color instead, THS/PHS will use
		these color attributes.

		Example:  if you have defined "ReceiveWindow_Text = Green on
		Black" and you want your text reversed, not intensified, then
		define "SendTextInReceiveWindow = Black on Green" here.

	"SentTextInTransmitWindow"

		In the non-packet modes, the entered text for transmission is
		sent to the PK-232 word-by-word and you get the echo in the
		receive window from the PK-232 (echo-as-sent) when it is
		actually transmitted.

		For to get an indication up to which part of your text has
		already been sent to the PK-232 (and not yet transmitted),
		that part is highlighted in the TRANSMIT window if you
		specify "Default". If you prefer another presentation, you
		can experiment with color values.

		Mandatory, PHS only.




                        ERROR REPORTS
                        ÍÍÍÍÍÍÍÍÍÍÍÍÍ

	Whenwever PHS detects an error, it will open a window and display an
	error message and optionally parameters. Note that it is not always
	possible to recover from these errors. The message types are

    		RS-232 Port Overrun error
    		RS-232 Port Parity error
    		RS-232 Port Framing error
    		RS-232 Port BREAK interrupt
    		Hostmode waiting for SOH: timeout
    		Hostmode waiting for databyte: timeout
    		Hostmode excessive input, no ETB
    		Unknown error during input, code: nnnn

	The RS-232 errors are signalled by the OS/2 communications device
	driver.

	Parity and framing errors, or break interrupt may indicate a chip
	problem, this could however be on either end of the serial line. Try
	to use another port on the PC, and/or reduce the transmission baud
	rate.

	Whenever you get an overrun error this indicates that the your PC is
	not fast enough to process the incoming characters. This can be
	solved by either reducing the frequency in which the incoming
	characters appear, i.e. by reducing the communications baudrate, or
	by using a more sophisticated serial communications controller chip,
	or by increasing the CPU speed.

	The "hostmode" errors signal a problem with the PHS-PK-232 hostmode
	communication. Up to now I have ever only seen the first one (timeout
	waiting for SOH), and only during startup of PHS. A hardware reset of
	the PK-232 and or a hardware (!) reset of the PC cured it (on the PC
	side, a CTRL-ALT-DEL will not help).

                       DECODING OF NET/ROM FRAMES
                       ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ

	PHS decodes Net/Rom routing broadcast messages and the inter-node
	frames into a plain English text format. For an interpretation of the
	various variables shown, please refer to "Net/Rom Version 1.3
	Documentation" from Software 2000 Inc.

                              FINAL REMARKS
                              ÍÍÍÍÍÍÍÍÍÍÍÍÍ

	I will be interested in your proposals and comments. Please note
	however that I will feel no obligation of any kind. I am a
	professinal software designer, but THIS is a hobby project.

	My address is:          Peter H. Heinrich
        	                     HB9CVV
                	        Allmendstr. 25
                        	CH-2562 Port
                        	Switzerland

	You can also contact me on CompuServe [71470,32].


                             REVISION HISTORY
                             ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ

	2.xx    1988            Releases of THS (DOS)
	3.00    October 1989    Initial release (PHS for DOS)
	4.00    October 1991    Beta release (PHS/THS for OS/2)
	        February 1992   Inital release (PHS/THS for OS/2)
	5.00    March 1993      Internal release
	6.00    May 1993        Beta release (PHS/THS for OS/2 2.x).




				PK-900
                                ÍÍÍÍÍÍ


        ******************************************************************
        * A note to PK-900 users: It is highly recommended NOT to use    *
        * the PK-900 at a communication line speed of 19200 baud, but    *
        * use 9600 baud only. The PK-900 seems to have problems at 19200 *
        * baud (which can be seen by the use of a line monitor).         *
        ******************************************************************

                                                                         
	To enable the proper operation for a PK-900, you must set a             
	devicetype of 4 in the configuration file.

	The statusline for the PK-900 will be slightly different to reflect
	the operation of the second modem ("Radio 2"). This is what you see
	when Radio 1 is in Amtor-Listen mode and this channel is selected:

 AMTOR LISTEN   º RECEIVE  ³ Phasing     º              º    º MABCD º 19:09:03

	The MABCD string contains the channel indicators of the four
	channels of Radio 2 (A, B, C, and D) and the monitor channel for
	Radio 2 (M). To select one of these channels, use the left or right
	arrow keys. The statusline will change to:

  1    º VHF º UA:00 RTY:00 ³ DISCONNECTED              º    º MABCD º 19:15:21

	and one of the indicators (MABCD) is highlit to show which channel
	is currently selected. The single "1" is the indicator of the Radio
	one channel - in non-packet modes, there is only one channel.

	If you have a Radio-2 channel selected, the mode-swich command (by
	ALT/M) will allow you to change between Packet-VHF and Packet-HF
	only - other modes are available only on Radio-1.

	If you are on a Radio-1 channel, and switch the mode to Packet, the
	status line will be like this:

 M1234 º HF  º UA:00 RTY:00 ³ DISCONNECTED              º    º MABCD º 19:23:24

	Again, one of the indicators either on one of the Radio-1 channels
	(M1234) or of the Radio-2 channels (MABCD) is highlit to indicate
	the currently active channel. Use the left or right arrow keys to
	change to another channel.

	PHS maintains two different heard-lists, one for each radio of the
	PK-900. Whenever you type ALT/H or ALT/G, the heardlist for the
	currently selected radio is shown.

	When ALT/I is pressed, then PHS shows twelve entries in the selection
	list for the PK-900 - CFROM-2, DFROM-2, MFROM-2 and MTO-2 is added for
	Radio-2.

	Please also remember that most of the packet-related PK-900 commands
	have now two parameters, seperated by a slash ("/") where the first
	parameter applies to RADIO 1, and the second parameter after the slash
	is for RADIO 2. Consequently, if you press ALT-P on a packet-channel,
	you get something like this:

ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ .... ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

	  ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ PK-900 Parameters ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
          ³                                                           ³
	  ³ ACKPRIOR      Y/Y   FULLDUP       N/N   RESPTIME      0/0 ³
	  ³ AUDELAY       2/2   HID           N/N   RETRY       10/10 ³
	  ³ AX25L2V2      Y/Y   LITE          N/N   SLOTTIME    30/30 ³
	  ³ AXDELAY       0/0   MAXFRAME      4/4   SQUELCH       N/N ³
	  ³ AXHANG        0/0   MCON          6/6   TRIES           0 ³
	  ³ BARGRAPH        0   MID           0/0   TXDELAY     30/50 ³
	  ³ BEACON    E 0/E 0   MODEM         4/4   USERS         2/2 ³
	  ³ BRIGHT         50   MONITOR       6/6   WHYNOT          N ³
	  ³ CHECK       25/25   MRPT          Y/Y   XMITOK          Y ³
	  ³ CMSG          N/N   MSTAMP          N                     ³
	  ³ CONPERM         N   PASSALL       N/N   <F1>  HELP        ³
	  ³ DWAIT       16/16   PERSIST     84/84   <ESC> EXIT        ³
	  ³ FRACK         5/8   PPERSIST      Y/Y   <F10> SET PARAM   ³
	  ³ FRICK         0/0   RELINK        N/N                     ³
	  ³                                                           ³
	  ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾

 1    º VHF º UA:00 RTY:00 ³ DISCONNECTED              º    º MABCD º 19:30:29

 Eable acknowledgement priority (Y/N)
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ .... ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

	In the Config-file, there are now five more keywords - ChannelM2size
	and ChannelAsize to ChannelDsize for the new channels of Radio-2.

	Please note that the help-text for the commands is no longer
	complete.  A long time ago I got the PK-232 command summary from AEA,
	this was then used for the helptext. Unfortunately, it is no longer
	possible to get this from AEA, and I do not like to type always the
	latest command summary from the manuals. I did it for some commands,
	but got tired to do this for all. Thanks for your understanding...

	When the RESETdeviceonexit parameter of the Config-file is ON (which
	is the (recommended) default) then PHS switches both radios OFF on
	exit, and (always) ON when started. This means that the RADIO 1 and
	RADIO 2 indicators of the PK900 LCD panel go off when PHS exits. In
	case you want to operate the PK900 with another program, you must
	first issue a "RADIO 1/2" command to enable both radios (modems).

	Version 6.01 and higher has the ALT-1 and ALT-2 keys to toggle
	Radio-1 or Radio-2 on/off. However, it is possibly not wise to
	switch a modem off during a qso...

ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ end of file ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
 				 so far.