+----------------------------------------------------------------------------+
|        Part of the cALMER Utilities for IBM PC/AT and compatibles          |
|       Copyright (C) 1991 by cALMER Utilities [All Rights Reserved]         |
|  361 Somerville Road, Hornsby Heights NSW 2077 Australia [+612]  482 1715  |
+----------------------------------------------------------------------------+

        SIPlus (Systems Information Plus) provides a vast range of information 
        about your hardware.  Not everything will make sense to you, but since 
        you probably never have any need to know the details just take it
        for granted that what is displayed is the information your
        system is prepared to reveal.

        Not all computers will have the same information displayed,
        on some models, almost nothing of interest is shown as it is
        not possible to retrieve that information.

        I started writing SIPlus many moons ago because I was curious
        just what type of computer was sold to me and how accurate
        the sales persons statements where.

        This has annoyed quite a few hardware people who objected to
        the program showing just what a load of rubbish their
        machines are.  Unfortunately, their bribes consisted of the
        types of machines the program was showing up as bad, so
        instead of accepting free computers so I could adjust SIPlus
        to accommodate their incompatibilities, I've decided to put
        a compatibility rating (CCR) into the program.

        A CCR of 100% indicates that it is, from a programming point
        of view, 100% compatible with the equivalent IBM machine,
        i.e. an AT or XT.  IBM PS/2 models do not show up 100% since
        IBM has changed a lot of things internally.  As I am not rich
        enough to afford one of those, I'll have to wait till some
        clones appear on the market.

        A CCR of less than 60% means that you've been had.  To date,
        I have been made aware of only one such computer.  The CCR is
        calculated by evaluating tests based on IBM Technical
        Documentation.

POTENTIAL PROBLEMS using SIPLUS:

        On some computers, SIPLUS will simply lock-up the system,
        i.e., a complete systems crash will eventuate.  This will
        be due to some timing errors or possibly to a flaky CPU.
        If SiPlus locks up on you, do the following:

        Set an environment variable called CA-STAT to contain either
        NOCPU or NOROM.

        i.e., from DOS key in (no '"')    "SET CA-STAT=NOCPU<Enter>" 
              or                          "SET CA-STAT=NOROM<Enter>" 
              or both                     "SET CA-STAT=NOCPU NOROM<Enter>" 

        NOCPU tells SIPlus not to perform a CPU test, while
        NOROM tells SIPlus not to perform a ROM test / search.

        Unfortunately, it is not possible to trap the errors created
        by these tests programatically as the program never gets to
        know about the problem....


PRINTING SIPLUS information.

        Press the <Print Screen> key when viewing SIPlus information 
        or redirect output to printer thus: "SIPLUS >PRN<Enter>"

        You will need SIPlus if you have problems with NBY, the anti-
        virus / Trojan program.  (See NBY.DOC)


.end of document siplus.doc