GT POWER - 16.00
           Copyright (c) 1987, 1988, 1989, 1990: by P & M Software Co.
                            All rights are reserved.



                               GT Netmail System

                                QUICK REFERENCE
                                     GUIDE

                                  NETMAIL 400

                             by Warren Leadbeatter







                             P & M Software Company
                             3104 E. Camelback Rd. 
                             #503
                             Phoenix, AZ  85016    
                             U.S.A

                             Voice Phone: (602) 285-9914
                             Modem Phone: (602) 285-1146














                                    - 1 -






                               Table of Contents
                     ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~


     The Mail Bagger
     ~~~~~~~~~~~~~~~
        Mail Bagger Command Line Options . . . . . . . . . . . . . . . .  4


     The Mail Distributor
     ~~~~~~~~~~~~~~~~~~~~
        Mail Distribution Command Line Options . . . . . . . . . . . . .  6


     The Mail Driver
     ~~~~~~~~~~~~~~~
        The Subdirectories . . . . . . . . . . . . . . . . . . . . . . .  8

        Command Line usage . . . . . . . . . . . . . . . . . . . . . . .  8

        DOS Shell  . . . . . . . . . . . . . . . . . . . . . . . . . . .  9

        Passwords  . . . . . . . . . . . . . . . . . . . . . . . . . . .  9

        Command Line Options . . . . . . . . . . . . . . . . . . . . . . 10

        A NOTE about G_UNPAK . . . . . . . . . . . . . . . . . . . . . . 10

        Command Line Options for CRASH! Mail . . . . . . . . . . . . . . 15

        The /F WOOF FRONT END Option . . . . . . . . . . . . . . . . . . 15

        Example HOST.BAT for FRONT END . . . . . . . . . . . . . . . . . 16

        WOOF FRONT END Error Levels  . . . . . . . . . . . . . . . . . . 17

     The ROUTING.BBS
     ~~~~~~~~~~~~~~~
        Structure  . . . . . . . . . . . . . . . . . . . . . . . . . . . 18

        Phone Number Transforms  . . . . . . . . . . . . . . . . . . . . 18

        Modem Dial Modifiers . . . . . . . . . . . . . . . . . . . . . . 19

        CALL WINDOWS . . . . . . . . . . . . . . . . . . . . . . . . . . 19

        Call windows modifiers . . . . . . . . . . . . . . . . . . . . . 19

        Example ROUTING.BBS  . . . . . . . . . . . . . . . . . . . . . . 21



                                    - 2 -





     Q BAGS and the Q Converter
     ~~~~~~~~~~~~~~~~~~~~~~~~~~
        Quick BAGS Description . . . . . . . . . . . . . . . . . . . . . 22
        
        Q Convert (QCVT105)  . . . . . . . . . . . . . . . . . . . . . . 22

        Selective generation and/or inclusion of Q Bags  . . . . . . . . 23

        BAG CONSOLIDATION Flags  . . . . . . . . . . . . . . . . . . . . 23


     DOT Commands
     ~~~~~~~~~~~~
        NetMail DOT Commands . . . . . . . . . . . . . . . . . . . . . . 24


     Your Notes
     ~~~~~~~~~~

        Start  . . . . . . . . . . . . . . . . . . . . . . . . . . . . . 28


































                                    - 3 -



     MBAGGER Command Line Options
     ~~~~~~~~~~~~~~~~~~~~~~~~~~~~


          /CF ..... Suppress  all  .FR  requests   encountered  during  the
                    bagging  run.

          /CD ..... Suppress  all  .DX  requests   encountered  during  the
                    bagging run.

          /CA ..... Suppress both .FR and .DX requests.  As if you had both
                    /CF and /CD on the command line at the same time.

          /Dn ..... This option specifies the number of days  you  wish  to
                    retain  old  bags  of  Echomail.  These  bags  must  be 
                    retained for awhile so  that  they  are  available  for 
                    newcomers  and  for people who miss a day or two of the 
                    conference.  The system defaults to 14  days,  I  would 
                    not advise a shorter period,  but this mechanism can be 
                    used to lengthen the period.  I use /D31 on  my  system 
                    at  001/003,  but I have no crunch on disk space at the 
                    moment.  

          /G ...... Do not Bag Mail. Instead only analyze existing mailbags
                    to see if any consolidations can be performed.
                    Used in G_UNPAK.BAT. See MDRIVER /G

          /Knn .... The  'nn'  should  be be a  unique number between 1 and
                    65535.   It  is  used  with  the .CY command to encrypt
                    messages on your system.
                    Please note, you should  _NOT_ use te same /k number on
                    the MBAGGER and MDIST command lines.   Keep this number
                    SECRET.

          /L ...... Causes  MBAGGER  to  use  the   NAME=  entry  from  the
                    SCHEDULE.BBS  file  in the  ORIGIN  line of the message
                    without converting it to UPPERCASE.

          /N ...... This  option  enables  MBAGGER to be run more than once
                    per day.  On the first run of MBAGGER,  this option  is 
                    not used,  but all subsequent runs on that day MUST use 
                    the /N command line switch. /N stands for NEXT RUN.

          /NL ..... Suppress  the new  G bag  logging from MBAGGER.  If not
                    present,  MBAGGER will  cause entries  to be written to
                    GBAG.LOG to document the creation/update of G bags.

          /NP ..... This  option causes the  MBAGGER  program  to  skip the
                    pruning of echomail from  \MAILOUT  and is quite useful
                    in speeding the operation of the program.  The echomail
                    need not be pruned more than once a day.





                                    - 4 -



     MBAGGER Command Line Options Cont'd
     ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~

          /OC ..... This option allows the  MBAGGER program to be used with
                    GT POWER 14.03 and before.  The native mode of  MBAGGER
                    will be the GT POWER 15.50 mode.

          /Q ...... When you specify the  /Q option  on the command line of
                    MBAG411, Q  bags  will be generated for all conferences
                    that are sponsored by your system, in  addition  to the
                    regular E bags.  You may examine the results to see the
                    efficiency (or lack thereof) of the new procedure.

          /QO ..... The  /QO  option will cause  MBAG411 to generate Q bags
                    ONLY. If you require E bags later, the QCVT program can
                    be used to create E bags from your Q bags.

            Note:  If  you  are  handling  Q  bags  then the  MBAG  program
                   *should* be run with the /Q option AT ALL TIMES. Several
                   people have reported  problems due to the fact that they
                   have used the Q option occasionally, or not at all (and
                   have used QCVT to generate Q bags).  If  you  process  Q
                   bags, then use the /Q option on ALL executions of  MBAG.
                   If you run QCVT, you might consider using  /QO for speed
                   sake.

          *  See the Q BAGS and QCVT SECTION for more info Q bags

          /R ...... This option is used to specify an  alternative  routing
                    file.  If  not specified,  the program will process the 
                    standard ROUTING.BBS, but with this option, any routing 
                    file may be named for input.  For example: 

                         /R:foo.bar

                    In this case,  the routing instructions would  be  read 
                    from the file 'foo.bar'.  

          /VG .... Produce a verbose listing of the GCONSOL file on screen.
                   WITHOUT  the  /VG  option, the  GCONSOL file will not be
                   listed.

          /X ...... Bag  mail in  a normal  fashion, but  skip any echomail
                    conference which is sponsored by the local sysop.  This
                    prevents  problems with  multiple baggings  on the same
                    day by echomail  sponsors. The  echomail sponsor  would
                    need at least 1 run per day without this option.

  /ZX /ZI /ZS ..... are now permissible command line arguments for MBAG and
                    MDIST.  This gives MBAG and MDIST support for the newer
                    version of PKZIP, which no long use the 1..4 numbers in
                    conjunction with choosing compression methods.




                                    - 5 -




     MDIST Command Line Options
     ~~~~~~~~~~~~~~~~~~~~~~~~~~

          /G ...... Do   not   Distribute   mail.   Instead   examine   all
                    consolidated bags that have been received  addressed to
                    the local node and break them down into their component
                    parts. Used in G_UNPACK.BAT.  SEE MDRIVER /G

          /Knn .... The 'nn' should be a unique number between 1 and 65535.
                    It is used with the .CY  command to decrypt messages to
                    your system. Please note, you should _NOT_ use the same
                    /K number on the MDIST and MBAGGER command lines.  Keep
                    the  number on  your  MBAGGER  line  secret, _but_ tell
                    those, who wish to send encrypted messages  to you, the
                    number you have  selected  for use on your  MDIST  line
                    (otherwise incoming messages may not be decrypted).

          /NA ..... No  Remote  File  Attach.  This command  causes any .RA
                    received  from  a  remote  system  to  be  discarded. A
                    message will be returned to the  sender explaining that
                    the .RA was not authorized.

          /NR ..... Causes  the  response to the  .GL  command to exclude a
                    full list of available  echomail  conferences.  Instead
                    producing  a  report  of  the  current  status  of  the
                    requestor's conferences only.

          /NL ..... Causes  MDIST  to  suppress  keeping the new G bag log.
                    This  new  log is now  produced  by  default,  and this
                    switch can be used to suppress it.  If the log is kept,
                    a record of each G bag processed through  MDIST and its
                    contents will be kept in a file called  GBAG.LOG.  This
                    file  will  grow indefinitely, it is up to the sysop to
                    periodically archive it.  MDIST will build a new one if
                    an existing GBAG.LOG file is not found.

          /OC ..... This option allows the MDIST program to be used with GT
                    POWER 14.03 and before.  The native mode of  MDIST will
                    be the GT POWER 15.00 mode.

          /R ...... This allows the user to specify the use of an alternate
                    routing  file instead of the standard ROUTING.BBS file.
                    For example:

                                MDIST  /r:hay.stk

                    In this example,  MDIST would read the required routing
                    instructions  from the  file 'hay.stk', instead  of the
                    ROUTING.BBS file.






                                    - 6 -





     MDIST Command Line Options Cont'd
     ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~


          /SA ..... Save  both  B  and  G  bags  prior  to  unpacking   and
                    distributing.  Same  as  above  for  the  /SB  and  /SG
                    options.

          /SB ..... Save B bags prior to unpacking and distributing  to the
                    message base.  The bags are saved in MAILARC.ARC, which
                    will be created in the \MAILIN directory.  The sysop is
                    responsible  for  pruning bags  from  this  archive  as
                    required.

          /SG ..... Save  G bags prior to unpacking and distributing.  Same
                    as above for the /SB option.

          /V ...... This  option can  be used when G bag logging is enabled
                    (which is the default).   The  /V option causes verbose
                    logging of G bags before they are unpacked.  MDIST will
                    invoke  PKARC  or PKZIP, as required, with the V option
                    and  append the  output  to  the  GBAG.LOG  file.  Thus
                    providing  a complete record of the files  contained in
                    the G bag.

          /VG .... Produce a verbose listing of the GCONSOL file on screen.
                   WITHOUT  the  /VG  option, the  GCONSOL file will not be
                   listed.

  /ZX /ZI /ZS ..... This gives MBAG and MDIST support for the newer version
                    of PKZIP, which  no  longer  use  the  1..4  numbers in
                    conjunction with choosing compression methods.  This is
                    used to select the storage  method to  be used with the
                    /SB, /SG and /SA options listed above. Unpacking of ZIP
                    format is handled automatically, the MDIST program will
                    auto-sense ZIP vs ARC format bags.


















                                   - 7 -



     MDRIVER
     ~~~~~~~

     NOTE!
     ~~~~~                                                                .
        This  program  must  now  be  installed  to use.   The installation
        procedure is quite simple,  the  first  time  the program  is  run,
        it will prompt you for the required information:  name,  S/N and GT
        key.    The  program  should  not  be  renamed   until   successful
        installation has been done.   Also,  you should have the program in
        the  GTPATH  directory  and it should be made the default directory
        when the installation is done.

     Sub Directories
     ~~~~~~~~~~~~~~~
          \MAILWORK ........... Usually empty.  Temporary work area.
          \MAILOUT ............ Outgoing mail bags.
          \MAILOUT\FILEOUT .... Outgoing  files for use  with "File Attach"
                                and "File Request".
          \MAILOUT\DEADLTR .... Stale mail.  Put  here when  can't deliver.
          \MAILIN ............. Incoming mail bags.
          \MAILIN\FILEIN ...... Incoming  files  sent via  "File Attach" or
                                as a result of a "File Request".
          \MAILIN\PROBLEMS .... Incoming  mail  bags  that  for some reason
                                couldn't be unpacked (eg.Damaged Bags). Can
                                be either B, E or G bags.  Moved  here  for
                                manual inspection and disposal.
     
     Command Line Usage
     ~~~~~~~~~~~~~~~~~~

        There are several command line parameters for the MDRIVER  program.
        They are as follows:

           The netmail CRC Identification number.
           The session start time.
           The session end time.
           The latest start time for the session.

        These  are  the  basic  parameters  and  must be specified and must
        be specified in the order listed.  For example:

                    MDRIVER  XXXX-YYYY  4   5  0455

        The above example would run the Netmail from 4 am to 5 am.  And the
        latest start time would be 4:55 am.

                    MDRIVER  AAAA-BBBB  4:30   5:25  5:20

        The  above  example would run the  Netmail from 4:30 am to 5:25 am.
        And the latest start time would be 5:20 am.

        In the above  examples,  the XXXX-YYYY  and  AAAA-BBBB are the CRC
        Identification  Number   pairs   obtained   from   the  GT Netmail
        Coordinator.

                                    - 8 -



     DOS SHELL
     ~~~~~~~~~

        DOS Shell and  Quick Shell.   These are new options available only
        while MDRIVER is waiting for an incoming call.

        a) Press 'S' to obtain the  DOS  Shell.   The  routing  file   and
           nodelist are reloaded upon return to MDRIVER.

        b) Press 'Q' to obtain the  Quick  Shell.   No files are  reloaded
           upon return to MDRIVER.

        c) A menu will be put on screen to remind you of these options.

     PASSWORDS
     ~~~~~~~~
        A new file,  GTNETPWD.BBS,  must be created with a text  editor to
        hold the passwords.   Each password will be used to identify 1 and
        only 1 connection.      For example, if 079/000 calls 004/000, and
        Bryan and Jim agree to the password "lumpy".       Here is how the
        GTNETPWD.BBS file would look on each system.

        GTNETPWD.BBS on 079/000               GTNETPWD.BBS on 004/000
        -----------------------               -----------------------
        004/000,lumpy                         001/003,noise
        001/003,random                        079/000,lumpy

        Please notice:

        The password for the 079/000 to 004/000 connection is 'lumpy'  and
        that  it  is  privately  agreed  upon  between  the  two   systems
        themselves.  No other person need be aware of the chosen password.
        Both systems  must have the same password listed for each other.

        The password for 079/000 to  001/003  is  *not*  the same  as  the
        password  for  004/000 to 001/003.   That is,  these passwords are
        always selected independently for each unique connection.

        If you  list a password for a system, then that system must supply
        that password.   If the calling system is unprepared to supply the
        required password, then it will not connect.

        This method should provide a very high degree of security.

        The passwords can be composed of any legal ASCII character, except
        for CR/LF/EOF (EOF = Ctrl-Z).   But I  would  recommend  that  you
        stick to more normal characters.      Passwords are limited to ten
        (10) chars.








                                    - 9 -



     MDRIVER Command Line Options
     ~~~~~~~~~~~~~~~~~~~~~~~~~~~~


          /A ...... This new switch allows the operator to specify the ring
                    upon which the phone should be answered.   By  default,
                    MDRIVER will answer on the 2nd ring. This seems to work
                    somewhat more reliably than the 1st ring answering.

          /Bnn .... The  'nn'  is the  number  of times  you wish to try to
                    connect to a remote  city  through  PC  Pursuit at 2400
                    baud (if available), before dropping down to 1200. This
                    parameter only  affects the dialing  through PC Pursuit
                    to a remote city (i.e. the Telenet "C D" command).

          /CA%3 ... See CRASH! MAIL Section

          /CC ..... See CRASH! MAIL Section

          /E ...... Allows the user to specify the maximum number of errors
                    to allow during a netmail transfer before aborting  the 
                    session.  Very  useful  to  keep from wasting time on a 
                    bad connection.  Values below 3  are  not  recommended.  
                    For example: 

                         /E3

                    This  would  allow 3 errors to occur before the session 
                    would terminate.  

          /F ...... See FRONT END Section

          /G ...... MDRIVER xxxx-yyyy ... /G ...

                    This command would cause the  MDRIVER  program to SHELL
                    to a special batch file at  the end  of any call during
                    which the local system has received a consolidated bag.
                    The name of the special  batch file is  G_UNPAK.BAT.  A
                    sample follows:

                           MDIST    /R:r0100.bbs    /G
                           MBAGGER  /R:routing.cr1  /G

                    This  would  cause any consolidated bag received during
                    a   session   to  be   immediately   broken   down  and
                    re-consolidated in the indicated manner (by the routing
                    and bag consolidation instructions).


         NOTE about G_UNPAK
         ~~~~~~~~~~~~~~~~~~
         The /G command line option for MDRIVER has been redone.  No longer
         will MDRIVER invoke the G_UNPAK.BAT file.       There simply isn't
         enough room in memory for it to run reliably. See next page also.


                                    - 10 -



     MDRIVER Command Line Options Cont'd
     ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~

         Instead, MDRIVER will exit with errorlevel  255  whenever a  G bag
         unpack is triggered via the /G command line option. The sysop must
         arrange his batch file to account for  this  and  restart  MDRIVER
         after the unpack operation is complete.

          /H ...... Allows  for  the  specification  of  a  custom   "Human
                    Notice".   Instead  of  the  default  notice,  you  can 
                    customize the notice you system uses  to  notify  human 
                    callers  of  the  netmail  processing in progress.  For 
                    example: 

                         /H:foo.bar

                    The file 'foo.bar' will be displayed to human callers.  

          /In...... Use  BIMODEM  to do transfers.  DO NOT  use PC Pursuit.
                    Use like this:

              /I         Use BiModem.  Not on PC Pursuit. No max baud rate.
              /I2400     Use BiModem.  Not on PC Pursuit.  At or below 2400
                         baud.

          /IPn..... Use  BIMODEM  to do transfers. Yes, use on  PC Pursuit!
                    Use like this:

              /IP        Use BiModem.  Enable PC Pursuit. No max baud rate.
              /IP4800    Use BiModem.  Enable PC Pursuit.  At or below 4800
                         baud.
          
          /Lnn .... This option would cause  MDRIVER  to try each node only
                    'nn' times before  removing  it from  the calling queue
                    for the session.  For example:

                         /L3

                    This would cause the  MDRIVER  to try each node 3 times
                    then giving up.  The nodes will be dialed in the normal
                    rotation, of course --this does not affect the order in
                    which they are called.

          /Mn ..... Limits outgoing calls so  that they will not "fallback"
                    below this lower limit. The 'n' is the lowest baud rate
                    that may be used in a "fallback" situation.

                    For example:

                               /M2400

                    would limit "fallbacks" so that they would not go below
                    2400 baud.



                                    - 11 -



     MDRIVER Command Line Options Cont'd
     ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~

          /NC ..... This option would cause  MDRIVER to take the crash call
                    for long enough to get the caller's id, then disconnect
                    Effectively this is an option to say: NO CRASH CALLS AT
                    THIS TIME.  But it will update the  GTNET.LOG  file and
                    show you the ID of the calling system.

          /NOW .... This  can be placed on the command line where the start
                    time is usually given.  This insures that  MDRIVER will
                    begin immediately, no matter what the  current time is.
                    Of course, care must still be  taken  with  the  ending
                    time,   but  the  latest  start  time  is  now  ignored
                    (although it must still be stated).  For example:

               New style:

                mdriv043 xxxx-yyyy /now 2459 2459 /cc /q /r:routing.cr2 /zc

               Old style:

                mdriv043 xxxx-yyyy 0100 2459 2459 /cc /q /r:routing.cr2 /zc

          /NL ..... Do not answer incoming calls.  Assumes sysop is present
                    and  will not continue normal operation after a RING is
                    detected, until sysop hits the <CR> key.

          /NR ..... Do  not  answer incoming calls.  Assumes sysop is _not_
                    present  and  _will_  continue normal operation after a
                    30  second  pause.  No keystroke is required to restart
                    operation.

                    These options are useful if you wish to make a outgoing
                    crash mail  call from a  phone  normally used for voice
                    operations. Please note that these options should _not_
                    be used on  your  regular  data line, since  they  will
                    interfere with the normal handling of incoming calls.

          /OW ..... This  option  turns  the CALL WINDOWS, described below,
                    into a full scheduling mechanism.
                    All inbounds/outbounds  will be  auto-generated to make
                    the MDRIVER call the designated systems at the required
                    time (all other calls will be automatically suppressed)
                    The OW stands for   "Outbound Windows".   Since the /OW
                    option  generates  inbound  and   outbound   statements
                    automatically,  the  node  range  option  of  the  CALL
                    WINDOWS  should  not  be  used.  The program can become
                    easily confused.
         **********
         * WARNING: DO NOT use the option unless you are using CALL WINDOWS
         ********** Extra outbound calls will be placed if this  command is
                    used in the absence of CALL WINDOWS.



                                    - 12 -



     MDRIVER Command Line Options Cont'd
     ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~


          /P ...... Allow calls to be made to  900  series nodes. Normally,
                    no call would be made to 900 series systems.

          /Q:x .... This  is  an  old  option  with  a  new  twist.  The /Q
                    continues to  mean  that the  MDRIVER  will  quit after
                    placing all calls. But now you may specify a particular
                    node  that  is  to  be  called.  The 'x' has the format
                     'net-node'.  For example:
             /Q:009-000
                    This  would force a call to 009/000, then exit from the
                    program.
             /Q009000
                    This  is  the  same  as  above.  The punctuation is for
                    readability only, and may be omitted by the user.
             /Q
                    This  would  allow   MDRIVER   to  follow  the  routing
                    instructions, and quit after all calls have completed.

          /QI ..... The  purpose  of  this command line option is the cause
                    MDRIVER  to  quit  after  a  specific  incoming call is
                    received.

                    For example:   /QI:009-000

                    This would cause MDRIVER to quit to DOS after receiving
                    a call from 009/000.   During  this run,  no  out-going
                    calls will be made.

          /R        Allows for the use of alternate routing files,  instead
                    of the standard ROUTING.BBS file.  

                         /R:some.rte

                    The MDRIVER will get routing instructions from the file 
                    'some.rte', instead of ROUTING.BBS.  

          /RL ..... MDRIVER has a new command line option, /RL. This option
                    must be used to enable the new result  code  logging of
                    BUSY and NO CARRIER. The default will now be to not log
                    these items,  and  /RL  will turn the  logging of these
                    items on.

          /Tm:n ... Allows the user to specify the allowed maximum times in
                    seconds to be connected to  PC Pursuit  and to still be
                    allowed to redial on a BUSY.  In other words, when  the
                    program is about to redial after a BUSY,  it checks the
                    current connect time against this limit,  if the  limit
                    has been exceeded, then it  will  cease  redialing  and
                    disconnect from PC Pursuit.



                                    - 13 -



     MDRIVER Command Line Options Cont'd
     ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~


          /ZC ..... Enables the use of the Zmodem protocol through DSZ.COM.

          /ZE ..... Enables the use of the Zmodem protocol through DSZ.EXE.

                    If  you  are  enabling  either  DSZ,  then  the version
                    selected, either EXE or COM,  must be  available in the
                    GT POWER home directory.  For example, if you have:

                    set GTPATH=C:\GT

                    Then DSZ must be located in the C:\GT directory.  It is
                    not invoked via a "shell" or a batch file, but  for the
                    sake  of  security and speed, it is  executed  directly
                    from MDRIVER as a "child" process.  This  allows a very
                    close cooperation  between  the two programs.  But the
                    result is that the  normal  ZM??.BAT batch files cannot
                    be used, nor is the regular  DOS PATH  searched to find
                    DSZ.


































                                      - 14 -




     Command Line Options for MDRIVER to handle CRASH! Mail:
     ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~

          /CC ..... Make outgoing CRASH! Mail calls.

          /CA%3 ... Answer incoming CRASH ! Mail call.  This should only be
                    used in the  GTCRASH.BAT  file,  which is automatically
                    invoked by the  GT POWER  host when an  incoming CRASH!
                    Mail call is received.  This option will only be usable
                    when GT POWER 14.03 is released.

                    The "Crash Answer" command line switch must be followed
                    by "%3", so that the  GT POWER  Host  can pass the baud
                    rate to the MDRIVER program. This option should only be
                    used within the GTCRASH.BAT batch file.

                    After an incoming CRASH! Mail call is finished, MDRIVER
                    will   automatically  release  control  and  allow  the
                    reloading of the GT POWER Host.

                    An example of a GTCRASH.BAT file is shown below:

                           c:
                           cd \gt
                           mdriv033 9999-9999 /CA%3 /ZE
                           mdist


        NOTE:  To enable CRASH! Mail, the NODELIST must be updated to
               reflect which systems are "crashable". This is done by
               placing an '*' before the system name.
 
               The DOOR.EXE program must be available for GTCRASH.BAT 
               to work properly.





     THE 'WOOF' FRONT END
     ~~~~~~~~~~~~~~~~~~~~

          /F ..... The /F command line option for MDRIVER  has  been added.
                   This option allows MDRIVER to act as a frontend  for  GT
                   POWER. The advantage of this feature is that time can be
                   saved when receiving netmail or crashmail calls, i.e. no
                   wait for loading MDRIVER!  The  procedure  for utilizing
                   this feature is somewhat complex.   Please  refer to the
                   batch file included on the following page as an example:






                                    - 15 -




       HOST.BAT
       --------
          rem
          rem  Sample batch file for using the WOOF Frontend
          rem
          c:
          cd \gt
          set GTPATH=c:\gt
          :FRONT
          rem
          rem  Note: a netmail session kicks in at 24:00 via errorlevel 4
          rem        as setup in the SCHEDULE.BBS file.
          rem
          mdriv048 1234-5678 /now 2459 2459 /D10 /Ow /Zc /A1 /F
          if errorlevel 254 goto BBSLOC        . Local logon
          if errorlevel 192 goto BBS192        . DCE baud = 19200
          if errorlevel 96  goto BBS96         .    ''    = 9600
          if errorlevel 24  goto BBS24         .    ''    = 2400
          if errorlevel 12  goto BBS12         .    ''    = 1200
          if errorlevel 4   netmail            . Netmail scheduled event
          if errorlevel 3   goto BBS3          . DCE baud = 300
          if errorlevel 1   reboot             . ERROR: reboot computer
          goto end                             . Exit from HOST.BAT
          :BBS192
          gt1550 *1234-5678 /T10 /MN /S /Q /V:E /L7 /F:19200:1
          if errorlevel 254 goto FRONT         . Normal return to WOOF Frontend
          if errorlevel 4   netmail            . Netmail scheduled event
          if errorlevel 1   reboot             . ERROR: reboot computer
          goto end                             . Exit from HOST.BAT
          :BBS96
          gt1550 *1234-5678 /T10 /MN /S /Q /V:E /L7 /F:9600:1
          if errorlevel 254 goto FRONT
          if errorlevel 4   netmail
          if errorlevel 1   reboot
          goto end
          :BBS24
          gt1550 *1234-5678 /T10 /MN /S /Q /V:E /L7 /F:2400:1
          if errorlevel 254 goto FRONT
          if errorlevel 4   netmail
          if errorlevel 1   reboot
          goto end
          :BBS12
          gt1550 *1234-5678 /T10 /MN /S /Q /V:E /L7 /F:1200:1
          if errorlevel 254 goto FRONT
          if errorlevel 4   netmail
          if errorlevel 1   reboot
          goto end
          :BBS3
          gt1550 *1234-5678 /T10 /MN /S /Q /V:E /L7 /F:1200:1
          if errorlevel 254 goto FRONT
          if errorlevel 4   netmail
          if errorlevel 1   reboot
          goto end
          :BBSLOC
          gt1550 *1234-5678 /T10 /MN /S /Q /V:E /L7 /F:LOCAL:1
          if errorlevel 254 goto FRONT
          if errorlevel 4   netmail
          if errorlevel 1   reboot
          :end
          c:
          cd \gt
                                    - 16 -



     THE 'Woof' FRONT END (cont'd)
     ~~~~~~~~~~~~~~~~~~~~

          Notice the extensive usage of errorlevels.       The usage of the
          "WOOF Frontend" requires that the SCHEDULE.BBS use nothing except
          errorlevel triggered events.  Of the type "QUIT n", where 'n'  is
          the indicated errorlevel.    There are a few reserved errorlevels
          though, that must not be used for anything else:

          Errorlevel        Meaning
          ----------        -------
               0            Exit from the batch file.
               1            Error.  The system should either reboot or
                            exit from the batch file.
               3            Frontend has taken a call at a DCE baud rate
                            of 300.  Invoke the BBS to handle at the proper
                            rate.
              12            Same as 3, but DCE baud rate = 1200.
              24            Same as 3, but DCE baud rate = 2400.
              48            Same as 3, but DCE baud rate = 4800.
              96            Same as 3, but DCE baud rate = 9600.
             192            Same as 3, but DCE baud rate = 19200.
             254            Local logon to the BBS.
             255            /G bag unpack.

          The frontend will handle all  incoming  calls: netmail, crashmail
          and BBS callers.


     FIDO CRASH MAIL RUNS
     ~~~~~~~~~~~~~~~~~~~~
          MDRIVER will now recognize a string of "q.q." to be a  Fido  type
          crashmail run.    This  is  intended  to be  used  with the  Woof
          Frontend,  if the "q.q.q." string is received,  then the frontend
          will quit with an errorlevel as follows to indicate the  DCE baud
          rate:

                        DCE         ERROR
                        BAUD        LEVEL
                        ====        =====
                         300 ....... 200
                        1200 ....... 201
                        2400 ....... 202
                        4800 ....... 203
                        9600 ....... 204
                       19200 ....... 205
                       38400 ....... 206

          The  batch  file  for  your  Woof  frontend  should  trap   these
          errorlevels and take an appropriate action.  If you are running a
          Fido mailer, then invoke that  mailer.   If not,  then you should
          probably run a  DROPDTR  type program, or  perhaps invoke the host
          mode at the proper baud rate,  assuming  that  a  human  caller is
          online.


                                    - 17 -



     ROUTING.BBS
     ~~~~~~~~~~~

          The netmail programs now support file inclusion.  That is you can
          break your routing file down and build them back.

          For example:

             ;
             ;   MAIN NETMAIL ROUTING FILE FOR 001/033
             ;
             $ PURSUIT.RTE
             ;
             $ OUTBOUND.RTE
             ;
             $ WINDOWS.RTE
             ;
             $ ROUTE.RTE
             $ ECHO.033
             END
             ;
             $ DISTRIB.RTE
             ;
             ECHOMAIL HOURS 0100-2459

          Each  line  that  begins  with  a '$'  names another  file to  be
          included into the current ROUTING.BBS. This makes it very easy to
          track each functional section of the routing file. File inclusion
          is completely optional.

     PHONE NO TRANSFORMS.
     ~~~~~~~~~~~~~~~~~~~~
          An additional section for the ROUTING.BBS file.  This  section is
          intended to make it easier for  sysops  outside of  the  USA  and
          Canada to setup their dialing strings.

          Here is the basic format:

            PHONE NO TRANSFORMS
                61-2 -> 02
                61-5 -> 065
            END

           Up to 50 transforms can be specified.  In the example above, the
           first  entry  shows  that phone  numbers  from the nodelist that
           begin with "61-2" will have that string replaced by "02".    For
           example, 61-2-671-5538 would become 02-671-5538.









                                    - 18 -



     MODEM PRE-DIAL String
     ~~~~~~~~~~~~~~~~~~~~
           The Modem Dial Pre-String is configurable.  Normally this string
           defaults  to  something like 'ATDT'.    It  may  be  selectively
           overridden by placing the new pre-string on a CALL WINDOW entry.
           The  override  becomes  global,  however,  and  is  not directly
           associated with the CALL WINDOW - it is just a convenient way to
           associate a net/node with a particular pre-string.

             For example:

                   009/000,2435-2450  'ATX3DT'

     CALL WINDOW MODIFIERS
     ~~~~~~~~~~~~~~~~~~~~~
           /IN, /CC and /? are now CALL WINDOW modifiers.  These parameters
           are used within the CALL WINDOWS section of the routing file. As
           follows:

          /IN ..... Specifies an INbound window.       If an INbound window
                    exists for a node, then it must call within that   time
                    frame, otherwise the call will be rejected.

          /CC ..... Specifies a window that is to use   CRASH Call methods.
                    In other words, the destination system is  probably not
                    in netmail during the specified time frame.

          /? ...... Specifies a conditional window.   A conditional  window
                    is a window that will be executed if the      specified
                    system  has not be previously connected   with  on  the
                    current date.  To enable the /? option to work, MDRIVER
                    will now keep a new log file, GTNETDAY.LOG.    This log
                    will be  automatically  restarted  at the  beginning of
                    each day. It will record each system connected with and
                    the duration of each connect.         This log does not
                    accumulate, so  there is no maintenance associated with
                    it.  It exists for the sole purpose of allowing the /?
                    option to function.

          Here are some examples:

                 CALL WINDOWS
                     009/000,2435-2450
                     079/000,2401-2416
                     001/032,2430-2455
                     004/005,0145-0200
                     009/000,0315-0345 /?
                     031/000,0230-0300 /IN
                     001/003,0401-0415
                     001/032,0315-0330 /?
                     004/005,0330-0345 /?
                     009/000,0501-0530 /CC /?
                 END



                                    - 19 -




     CALL WINDOWS (cont'd)
     ~~~~~~~~~~~~~~~~~~~~

          Please note that the /CC and /? can be used in combination.    It
          does  not make any sense to use /IN in conjunction with the other
          two, since it is not used in relationship to outgoing calls.

          /=n ..... Where the  'n'  is a number  in the range 1.....7. This
                    option would restrict the associated window  to the day
                    of the week specified.  Where  1=Sunday, 2=Monday, etc.
                    More than one '/=' can be given per window.

                    For example:

                     009/000,0200-0230 /=1 /=4

                    This window would be executed on Sunday and Wednesday.

          /MB ..... This  option  would restrict  the associated window to
                    being performed only when a (M)ail (B)ag was   waiting
                    to be delivered.  The mailbag can be either   of the G
                    or B variety.


          /NPP .... This option disables PC Pursuit for the call going  out
                    under the current window.  Normally,     MDRIVER  would
                    force   PC Pursuit   usage   whenever  possible,   this
                    modifier allows a temporary suspension of   PC  Pursuit
                    usage.

          /EX ..... This option is related to the  /IN  or inbound  option.
                    With it you can dedicate a CALL WINDOW to the indicated
                    system.  It can be used for either incoming or  outgoing
                    calls.  But any CALL WINDOW with this option    becomes
                    exclusive to the listed system.  For example:

                    009/000,0200-0215 /EX

                    This  means that no incoming call from any system other
                    than 009/000  will be taken during  the 15 minute  span
                    02:00-02:15.














                                    - 20 -



        EXAMPLE ROUTING.BBS
        ~~~~~~~~~~~~~~~~~~~

        PREFIXES  LOCAL (*)  DISTANT (*)

        PHONE NUMBER TRANSFORMS
             61-2- -> ,
             61-65- -> 065
        END

        CALL WINDOWS
             302/000,0340-0415 'ATB1DT'
             302/023,0440-0515 /IN
        END

        INBOUND NODES
             302/023
        END

        OUTBOUND NODES
             302/000
        END

        ROUTING INSTRUCTIONS
        ;
        ; instructions for echos
        ;
             ACCEPT E00/001 -> 302/000
             ACCEPT E01/999 $nxnx-nxnx      <--- CRC for echo goes here
             ACCEPT E99/073 -> 302/000
             ACCEPT 001-300/000-899 -> 302/000
             ACCEPT 001-300/900-999 -> 302/000
        ;
        ;instructions for netmail
        ;
             ACCEPT 302/000
             ACCEPT 302/001-015 -> 302/000
             ACCEPT 302/017-022 -> 302/000
             ACCEPT 302/023
             ACCEPT 302/024-899 -> 302/000
             ACCEPT 302/900-999 -> 302/000
             ACCEPT 303/000-099 -> 302/000
             ACCEPT 307/000-099 -> 302/000
             ACCEPT 308/000-099 -> 302/000
             ACCEPT 310/000-899 -> 302/000
             ACCEPT 310/900-999 -> 302/000
             ACCEPT 800-999/000-899 -> 302/000
             ACCEPT 800-999/900-999 -> 302/000
        END

        BAG CONSOLIDATION
                302/000,ZQ
                302/023,ZQ
        END

        MESSAGE DISTRIBUTION
               E00/001      -> F:\GTECHO\GTSUPPRT    ,  GT_Support
               E01/999      -> F:\GTECHO\someecho    ,  Some_desc
               E99/073,1    -> SKIP                  ,  ACS_HAM_RADIO
        END


                                    - 21 -



     Q BAGS and CONVERT (QCVT105)
     ~~~~~~~~~~~~~~~~~~~~~~~~~~~~

     (Q)uick Bags!

           (Q)uick Bags are replacements for the old E bags.  You know  the
           bags that are named like this: E0954001.E00.  Now we will have a
           replacement  for the E bags, named like the E bags, but with the
           first character  of  the filename  equal to Q, like this:

           Q0954001.E00.

           (Q)uick bags are 20-50% smaller than regular E bags created with
           PKARC,    and maybe even smaller than ZIPped E bags, since these
           archivers do not   handle   small files  like messages well.  To
           create a (Q)uick bag we use our own squeeze program, called NMSQ
           (which must be placed into your GTPATH directory).     Also, the
           WORDLIST file must be present.  This  is  a  dictionary of words
           used in a pre-compression process.

           The QCVT program is being  made  freely  available to  everyone.
           It performs three different tasks:

           1.  Take E bags and generate Q bags from them.  Option /Q.
           2.  Take Q bags and generate E bags from them.  Option /E.
           3.  Take Q bags and generate M files (in \MAILWORK).  No option.

           Here are some command line examples:

                QCVT [filespec] [option]

           If not specified, the filspec will default to \MAILOUT\*.*
           If not specified, the option will default to #3 above, which
           breaks down Q bags into their component M files.

                QCVT /E

           Means to search  \MAILOUT for all Q bags and generate E bags, if
           they do not already exist.

                QCVT /Q

           Means to search \MAILOUT  for all E bags and generate Q bags, if
           they do not already exist.

                QCVT q0955001.e01

           Take this Q bag  and break it down into  M message files in  the
           \MAILWORK directory.







                                    - 22 -



     Selective generation of Q Bags
     ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~

           Selective generation of  Q bags is possible by adding a Q to the
           line  in the   MESSAGE  DISTRIBUTION  section  for the indicated
           conferences.

           Like this:

                  MESSAGE DISTRIBUTION
                     E01/009,10   -> D:\BETA_ECO , ;GT_Beta_Echo
                     E01/011,10,Q -> D:\TEST_ECO , ;Q_Test_Echo
                  END

           In this example,    E01/009 will have only E  bags generated and
           E01/011  will  have both Q and E bags generated. Of course, this
           assumes that no  /Q  is given on the   MBAG  command line.  This
           syntax is only useful for  conferences that you sponsor.


     Selective inclusion of Q Bags
     ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~

           Selective inclusion of  Q  bags in  G  bags  may be accomplished
           by a similar mechanism in the BAG CONSOLIDATION section.

           Like this:

                      BAG CONSOLIDATION
                         001/032,Z
                            E00/001,955
                            E01/009,955
                            E01/010,955
                         003/000
                            E01/009,955
                            E01/010,955
                         009/000,ZQ
                            E00/001,955
                            E00/005,955
                      END

           In the above example, nodes 001/032 and 003/000 will  get normal
           E bags put into their  G  bags,  but node 009/000 will receive Q
           bags if they are available. If  Q bags are  not  available, then
           009/000 will receive regular E bags.

           Flags for node entries.

           Z ....... Use PKZIP to build G Bags for the indicated node.

           F ....... Override ';' in Message Distribution. Allows the
                     indicated node to receive a full .GL report when
                     requested.



                                    - 23 -



     NETMAIL DOT COMMANDS
     ~~~~~~~~~~~~~~~~~~~~


          .FA ..... The .FA command will  accept  a  path  other  than  the
                    \MAILOUT\FILEOUT directory.

                    For example:

                    .FA foo.bar

                    Would pick-up FOO.BAR from the \MAILOUT\FILEOUT
                    directory.

                    .FA \lotus\spread.wks

                    Would pick-up SPREAD.WKS from the \LOTUS directory.

          .FR ..... Here is an example of a "File Request" command:

                    .FR nodelist.arc

                    This   would   cause  the  file  "nodelist.arc"  to  be
                    requested from the destination system when  the message
                    containing the ".FR" command is delivered.

          .DX ..... Here is an example of a "Direct Xpress" command.

                    .DX

                    This would cause  the  message which  contains  the .DX
                    to  be  routed  directly  to  the  addressee's  system,
                    without any store and forward operation.

          .CC ..... An  internal  system  command,  used  by  the system to
                    garble netmail messages. Should not be directly used by
                    individuals.

          .CY ..... Encrypt  the  information  on the line following.  This
                    information will be returned to normal on the receiving
                    system.















                                    - 24 -



        DOT Commands Cont'd
        ~~~~~~~~~~~~~~~~~~~


          .CS ..... Acts like a continuous run of .CY commands. For example
                    if you wanted to encrypt an entire paragraph or message
                    Like this:

                    .CStart
                    These lines will be encrypted.
                    This is the second line to be encrypted.
                    .CStop

                    The two lines shown between the .CStart and .CStop will
                    be   encrypted.  The .CS command  works  with  the  .KE
                    command in the same way that the .CY command does, with
                    the extra attraction that the .KE command may itself be
                    encrypted.  Like this:

                    .CSstart
                    .KE 8123
                    All lines between the .CStart and .CStop are encrypted.
                    This is another line encrypted.
                    .CStop

                    This   just  adds  one  more  level  of  protection  to
                    sensitive data.

          .EC ..... An  internal  system  command,  used  by  the system to
                    garble echomail conferences.  Should  not  be  directly
                    used by individuals.

          .KE ..... This command affects the encryption process done by .CY
                    and .CS so  that  it is less likely that outsiders will
                    be  able  to  unsramble  the  information.  The .KE  is
                    followed  by a number between 1 and  65535, which  must
                    match the /K number on the receivers MDIST command line
                    For example:

                    If the  receiver  told  you ahead of time that his code
                    number  was /k8123 on his  MDIST command line, then you
                    would code this in your message:

                    .KE 8123
                    .CY
                    .CY This is an encrypted message, that can be read by
                    .CY a system with /k8123 on the MDIST command line.
                    .CY

                    Then the receiving system should have:

                    MDIST  /r:routing.bbs  /k8123




                                    - 25 -



        DOT Commands Cont'd
        ~~~~~~~~~~~~~~~~~~~
        

          .GL ..... If this  command  is  placed  in a netmail message to a
                    system  which  is sending you a G bag, that system will
                    respond with a report  of  the  current  status  of the
                    conferences you are receiving  and,  if  authorized,  a
                    list of conferences available on that remote system.

                    Example:      .GL

                    Where  the "." is  located in the first position of the
                    line.

          .GM ..... If this  command  is placed  in  a netmail message to a
                    system which is sending you a G bag, it  will allow you
                    to add conferences or modify the  day  number  that you
                    are receiving in a currently received conference.

                    Example:      .GM e00/001,810

                    Again,  where  the "." would  be  located  in the first
                    position of the line.  The  GM  is followed by a single
                    space and the echo conference number  you  wish to add/
                    modify, followed by the new or starting day number.

          .GQ ..... If this command  is  placed  in a  netmail message to a
                    system which is sending you  a G bag, it will allow you
                    to drop a conference from the G bag you are receiving.

                    Example:      .GQ e00/001

                    As  above,  the  "."  should  be  located  in the first
                    position of the line.  The  GQ  is followed by a single
                    space and the echo conference number you wish to remove

          .MA ..... This command  is  much  like  the  .FA command. It will
                    also accept full pathname  specification  or default to
                    the \MAILOUT\FILEOUT directory,  when  no  pathname  is
                    given.  It  will  take  the  named  file  and  create a
                    message  to  be  sent  with  the  "cover message".  The
                    attached  message will be given the same security level
                    as the "cover message".  One caveat exists, that is the
                    attached message must be an ASCII text file, the  first
                    line of which has  the  following:  MSG ATTACH.  If the
                    message does not contain the  MSG ATTACH  header,  then
                    the file will not be attached.  This provision is made,
                    so  that  the sysop  will have control over which ASCII
                    files are attachable in this manner.  For example:

                           .MA c:\wp\text.dat




                                    - 26 -



        DOT Commands Cont'd
        ~~~~~~~~~~~~~~~~~~~


          .RA ..... This is a Remote File  Attach.  The command works  much
                    like a  FR (File Request) command, except that it works
                    through normal network  channels, causing the receiving
                    system to generate a FA for the  requested  file.  Only
                    files located in the \MAILOUT\FILEOUT  directory can be
                    obtained in this manner, as pathnames are not supported
                    with this command.  For example:

                           .RA foobar.dat

                    Would generate the following on the host system:

                           .FA foobar.dat

                    And automatically send the  message  and  attached file
                    back to the original requestor.

          .RR ..... This  is the  Return  Receipt  Request.  The  receiving
                    system will respond with a message  confirming  receipt
                    of the message containing the  .RR command.  The Return
                    Receipt should be in the following form:

                    ~CS

                    The following message was received at: 009/000
                    ==============================================
                        Msg No  :  2021
                        Date    :  3-13-89
                        Time    :  20:50
                        Sender  :  Paul Meiners
                        Topic   :  NOTHING IMPORTANT

                    Prepared By The MDIST Program:  3-13-89 22:10

                    ~CS

                    .ORIGIN: 009/000 - the Programmer's Workshop -West!

                    Note  the  usage  of .CS  encryption  to   help  insure
                    accuracy.  The  message  number  is  the  number of the
                    original  message  on  the sending system (the one with
                    the .RR command).

          .RV ..... An internal  system  command,  used  by  the  system to
                    provide  'return receipts '  associated  with  the  .RR
                    command.  Should not be directly used by individuals.






                                   - END -



                                    NOTES:
                                    ~~~~~~
                                    































                                    

























                                    NOTES:
                                    ~~~~~~