WILDNODE! v1.50

                   Nodelist Processor for WILDCAT! v3.+


           (c) Copyright 1991, 1992 by Online Computer Resources


                  4330-J Clayton Road, Concord, CA 94521
                Voice: (510) 687-1122  BBS: (510) 687-0236

                            All Rights Reserved
                             Revised: 09/03/92








                                 WILDNODE!

                             TABLE OF CONTENTS



          INTRODUCTION  . . . . . . . . . . . . . . . . . . . . . . . .   1

          ABOUT THIS DOCUMENTATION  . . . . . . . . . . . . . . . . . .   1

          PROGRAM AUTHORS . . . . . . . . . . . . . . . . . . . . . . .   1

          FILES INCLUDED  . . . . . . . . . . . . . . . . . . . . . . .   1

          INSTALLATION  . . . . . . . . . . . . . . . . . . . . . . . .   2

          EMS MEMORY  . . . . . . . . . . . . . . . . . . . . . . . . .   3

          COMMAND LINE OPTIONS  . . . . . . . . . . . . . . . . . . . .   4
               -Q . . . . . . . . . . . . . . . . . . . . . . . . . . .   4

          WILDNODE.CFG FILE . . . . . . . . . . . . . . . . . . . . . .   4
               NODE . . . . . . . . . . . . . . . . . . . . . . . . . .   5
               ZONES  . . . . . . . . . . . . . . . . . . . . . . . . .   5
               PVTLIST  . . . . . . . . . . . . . . . . . . . . . . . .   5
               COUNTRY  . . . . . . . . . . . . . . . . . . . . . . . .   7
               COST . . . . . . . . . . . . . . . . . . . . . . . . . .   7

          DISPLAY SCREEN  . . . . . . . . . . . . . . . . . . . . . . .   9
               CURRENTLY PROCESSING ZONE  . . . . . . . . . . . . . . .   9
               NET  . . . . . . . . . . . . . . . . . . . . . . . . . .  10
               TOTAL NODES COMPILED . . . . . . . . . . . . . . . . . .  10
               DBNET  . . . . . . . . . . . . . . . . . . . . . . . . .  10
               OVERALL TIME . . . . . . . . . . . . . . . . . . . . . .  10
               USING ZONES  . . . . . . . . . . . . . . . . . . . . . .  10
               TYPE . . . . . . . . . . . . . . . . . . . . . . . . . .  10
               NODELIST NAME  . . . . . . . . . . . . . . . . . . . . .  11
               START  . . . . . . . . . . . . . . . . . . . . . . . . .  11
               FINISH . . . . . . . . . . . . . . . . . . . . . . . . .  11
               ELAPSED  . . . . . . . . . . . . . . . . . . . . . . . .  11
               ZONES  . . . . . . . . . . . . . . . . . . . . . . . . .  11
               NETS . . . . . . . . . . . . . . . . . . . . . . . . . .  11
               NODES  . . . . . . . . . . . . . . . . . . . . . . . . .  11

          KEYSTROKE OPTIONS . . . . . . . . . . . . . . . . . . . . . .  11

          ADDITIONAL DISPLAY PROMPTS. . . . . . . . . . . . . . . . . .  12

          COMMON QUESTIONS/PROBLEMS . . . . . . . . . . . . . . . . . .  12






                                     i




                                 WILDNODE!

                             TABLE OF CONTENTS



          TECHNICAL SUPPORT . . . . . . . . . . . . . . . . . . . . . .  13

          PRODUCT REGISTRATION  . . . . . . . . . . . . . . . . . . . .  13

          LICENSING AND DISTRIBUTION AGREEMENT  . . . . . . . . . . . .  14

          NO WARRANTY . . . . . . . . . . . . . . . . . . . . . . . . .  14










































                                    ii



          WILDNODE! v1.50                                        Page  1
          INTRODUCTION



          INTRODUCTION
         
          WILDNODE! is used to process a Fidonet compatible St. Louis style
          raw nodelist and create the necessary database files so WILDCAT!
          v3+ can properly make use of the Netmail features.  WILDNODE! does
          this by making use of a special control file to define pricing,
          nodelist(s) to process and zone usage information. 



          ABOUT THIS DOCUMENTATION

          This document is a reference manual on installing, configuring and
          using WILDNODE!.  Since WILDNODE! requires the use of a raw
          nodelist, it is beyond the scope of this documentation to explain
          how to create and/or maintain these nodelists.  

          This manual assumes a fundamental working knowledge of operating
          in Fidonet compatible network(s) and thus is not a tutorial on
          using Netmail in a Fidonet compatible environment. 



          PROGRAM AUTHORS

          WILDNODE! v1.00 was originally written by Derek Koopowitz of Online
          Computer Resources.  Due to work constraints on the WILDMAIL!
          project, the release of v1.10 has been updated by Dave Cody.  This
          most current release was revised by Eric Cozzi of OCR fame.



          FILES INCLUDED

          Your WILDNODE! installation kit is distributed in a file called
          WNODE150.ZIP and contains these files:

          README.1ST          Introductory comments and any last minute
                              changes.

          WILDNODE.EXE        The executable.

          WILDNODE.DOC        This documentation file.

          WILDNODE.CFG        Sample configuration file used to control how
                              WILDNODE! processes the nodelist.





          WILDNODE! v1.50                                        Page  2
          INSTALLATION



          INSTALLATION

          Setup and configuration of WILDNODE! is relatively simple and
          straight forward.  Outlined below is the recommended procedure when
          initially installing WILDNODE!.

          1)   Using PKUNZIP, uncompress the WNODE150.ZIP into a temporary
               directory.

          2)   Copy WILDNODE.EXE into one of your DOS "pathed" directories. 
               This can be your \WC30 directory if so desired.  Consult your
               DOS manual on setting up a DOS PATH.

          3)   Depending on which version of WILDCAT! you're running, there
               are two possible location methods used where your WILDNODE.CFG
               file should be placed.

               When using WILDCAT! v3.00-3.02, the WILDNODE.CFG must be
               placed in the same location where your NODEINFO.DAT file
               resides.  Normally this in your C:\WC30\DATA directory. 
               Please refer to General Definition, Part 1 in MAKEWILD, option
               #12 for the exact path to place the WILDNODE.CFG file in.

               If you're running WILDCAT! v3.5+, a new DOS environment
               variable called WCNODELIST which (if used) contains the path
               to where WILDNODE.CFG and your NODELIST file(s) should be
               located and is used to override the default MAKEWILD settings
               (see above).  Making use of the path via the SET WCNODELIST=
               command is the preferred method because it prevents having to
               maintain multiple sets of the NODELIST file saving on your
               valuable disk space requirements.

               If you don't use the SET WCNODELIST= command, the WILDNODE.CFG
               file must be placed in the same location as if you're running
               WILDCAT! v3.00-3.02 (see above).

               Shown below is an example command in the batch file you use
               to execute your mailer and/or WILDCAT!. 

                    Example Usage:   SET WCNODELIST=C:\FD\NODELIST\

               Please note the inclusion of the trailing backslash on the DOS
               path.  THIS MUST BE THERE!  You are allowed to use the same
               "original" nodelist file as your mailer uses as long as it's
               in untouched form and conforms to the St. Louis style format. 
               In other words, if you're using FrontDoor or D'Bridge, you can
               set this path to the same subdirectory as previously defined
               for your mailers nodelist.





          WILDNODE! v1.50                                        Page  3
          INSTALLATION



          INSTALLATION - continued

          4)   Using the DOS cd\ command, change directories to the location
               of your WILDNODE.CFG file.

          5)   Edit the WILDNODE.CFG file according to the specific
               requirements for your system referencing the section on the
               setup/configuration for this file.

          6)   From the DOS prompt, execute WILDNODE.  No command line
               parameters are needed, just the simple execution of the
               program.  From here, WILDNODE! will use the parameters defined
               in WILDNODE.CFG to dictate message costing, zone usage and any
               additional nodelists to process.  

               WILDNODE! must be executed from the same directory where
               WILDNODE.CFG exists!  VERY IMPORTANT!

          Something worth mentioning here, your WILDNODE.CFG, NODELIST.nnn
          and any private nodelists should ALL be in the SAME directory!  The
          SET WCNODELIST= command is used to simply tell WILDCAT! where to
          look for the WILDNODE.nnn, WILDNODE.DAT, WILDNODE.IX and
          WILDNODE.DIA files.  Other than WILDNODE.CFG, these files are all
          created when WILDNODE! is executed from the command line. 

          Reference is being made to the path in the SET WCNODELIST= because
          this is where WILDNODE! MUST BE EXECUTED FROM and where the
          WILDNODE.CFG file must exist in order to execute properly and
          create the above files.


          EMS MEMORY

          WILDNODE! automatically detects the presence of EMS memory and if
          it's available, makes use of it.  Presently, it will grab all that
          it can in order to speed up the compilation process.

          Care must be taken when operating under DESQview in that if you
          don't limit the maximum amount of EMS memory that can be used by
          the window that WILDNODE! executes in, there may not be sufficient
          EMS memory available for other programs to use while WILDNODE! is
          running.  Of course when WILDNODE! exits, all memory used is freed
          up again.





          WILDNODE! v1.50                                        Page  4
          COMMAND LINE OPTIONS



          COMMAND LINE OPTIONS

          At present, only one command line parameter can be used when
          executing WILDNODE!.

               -Q
                    This parameter is used to invoke the "quiet mode".  This
                    means the fancy screen with the bar graphs are turned
                    off and only a simple screen is displayed indicating
                    that WILDNODE! is busy compiling the nodelist(s).  This
                    could be useful in saving some processing time when
                    compiling the nodelist(s).

                              Example Usage:  WILDNODE -Q


          WILDNODE.CFG FILE
         
          In this section, we'll describe the configuration file options and
          their usage in the WILDNODE.CFG file.  Please note that the names
          of the various parameters are shown for visual clarity.  In normal
          usage, options in the configuration file are NOT case sensitive. 
          In other words, upper and lowercase characters are treated the
          same.

          Shown below are the contents of a sample WILDNODE.CFG file.

                    NODE 1:161/123
                    ZONES 1 8 86 100
                    PVTLIST FDNET.PVT
                    COUNTRY 1
                    COST  20  125
                        1-415-   4
                        1-510-   4
                        1-916-  15
                    END

          The contents of the WILDNODE.CFG file can be edited with just about
          any true ASCII text file editor.  The usage of editors like
          WordPerfect and WordStar if not used in the ASCII (non-document)
          format can produce unpredictable results.  Shown below is a
          breakdown of all the individual keywords available.





          WILDNODE! v1.50                                        Page  5
          WILDNODE.CFG FILE



          NODE <zone:net/node> 
          [REQUIRED]

               This informs WILDNODE! what your primary address is.  This
               must be a complete <zone:net/node> network address.  

                    Example Usage:   Node 1:161/123 

               In the above example, "1" is the Zone, "161" is the Net, and
               "123" is the Node. 

        
          ZONES <number> <number> ...
          [OPTIONAL]

               The numbers (separated by spaces) here indicate the zones you
               wish to include when compiling the nodelist.  You can use this
               option to reduce the database size by specifying only those
               zones that are necessary.  Up to 255 separate zones can be
               defined and if you wish to include all the zones from the
               defined nodelists, simply leave this keyword out.  If you
               specify the zones to include, make sure to include the zone
               number(s) in all the PVTLIST defined nodelists as well,
               otherwise they won't be included in the compilation process.

                    Example Usage:   ZONES 1 7

               In the above example, this tells WILDNODE! that you wish to
               include only zones 1 and 7 in the resulting database file used
               by WILDCAT!.  

         
          PVTLIST <filename>
          [OPTIONAL]

               By default, WILDNODE! will use a file called NODELIST.nnn as
               the primary nodelist to compile (where <nnn> equals day of the
               year).  The use of this keyword allows additional nodelists
               to be included in the compilation process.

                    Example Usage:   PVTLIST MAGNET
                                           or
                                     PVTLIST FDNET.PVT

               In the first example, WILDNODE! will include the most recent
               nodelist "MAGNET.nnn" file found based on the extension number
               (where nnn equals the numbered day of the year).  By leaving
               off the actual file extension, you may have multiple
               MAGNET.nnn files in the directory, but WILDNODE! will only use
               the most recent file based upon the highest number found in
               its extension.





          WILDNODE! v1.50                                        Page  6
          WILDNODE.CFG FILE



          PVTLIST <filename> - continued

               The second example instructs WILDNODE! to use a specific file
               name when compiling nodelists.  This is commonly used by those
               systems that are running FrontDoor as their mailer.  

               FrontDoor's FDNC nodelist compiler also allows multiple
               nodelists and produces a output file called FDNET.PVT.  This
               file contains the contents of all the additional nodelists in
               raw form (they're simply appended together).  WILDNODE! can
               easily take advantage of this "all private nodelists in one"
               file instead of defining each individual nodelist via the
               PVTLIST command.  Using either method (individual PVTLIST's
               or FDNET.PVT) produces the same satisfactory results.

               Remember if you use the FDNET.PVT file, you MUST execute FDNC
               prior to executing WILDNODE! to ensure the compilation process
               uses the most current nodelists!  Up to 10 PVTLIST definitions
               can be used by simply defining multiple PVTLIST entries on
               separate lines.  The actual nodelists must all reside in the
               SAME directory as the primary NODELIST.nnn file.  THIS IS VERY
               IMPORTANT!

               WILDNODE! will create a output file called WILDNODE.nnn where
               the extension number matches your current NODELIST.nnn
               extension.  There will also be a WILDNODE.IX (index file)
               created as well.  These nodelist database files are what's
               required by WILDCAT! for proper operation will contain the
               zones (and node's) specified via the ZONE keyword.

               It should be mentioned that the file, WILDNODE.nnn will only
               be created when PVTLIST nodelists are defined.
  




          WILDNODE! v1.50                                        Page  7
          WILDNODE.CFG FILE



          COUNTRY <number> 
          [REQUIRED]

               This is used to define the COUNTRY CODE prefix of what country
               you're located in.  In other words, a 1 would indicate United
               States because to dial long distance within the US requires
               a 1 before the area code.  

                    Example Usage:   COUNTRY 1 

               In the cost tables, this entry defines what would qualify as
               an international call verses an in-country or domestic call. 
               Examples of other COUNTRY CODES are as follows. 

                    Chile     56        Egypt     20        Japan     81
                    Mexico    52        Norway    47        Peru      51
                    Spain     34        Sweden    46        Taiwan    886

               Please refer to your local phone book for specifics on
               additional COUNTRY CODE numbers.


          COST [<domestic>][<international>]
          [REQUIRED]

               The cost table is used to set both a default per-message cost
               value and a specific per-message cost.  

               A specific cost value would be one in which a match was found
               in the "cost table" (located between the COST and END
               keywords) with it's associated ACTUAL COST value defined to
               the right of the DIALING PREFIX number.  

               A default value cost would be one where no match was found in
               the "cost table" but was defined on the same line as the COST
               keyword (either domestic or international). 

                    Example Usage:   COST 11 125
                                          1-510-687    4  
                                          1-707-       6  
                                          1-805-334    10 
                                          61-          79  
                                     END

               The COST statement begins the actual per-message "cost table"
               and normally contains two arguments on the same line.  These
               two arguments define the DEFAULT costing if no matches are
               found within the body of the cost table.  The first number
               being a domestic cost, and the second number being an
               international cost.  These two numbers MUST be separated by
               a space.  





          WILDNODE! v1.50                                        Page  8
          WILDNODE.CFG FILE



          COST - continued

               In the above example, the number 11 indicates a per-message
               cost of .11 cents within the COUNTRY CODE prefix of 1 (United
               States).  The number 125 indicates a per-message cost of $1.25
               for messages destined for OUTSIDE of the U.S. (International
               calls).  

               These values are used when checking the user record of the
               person entering the Netmail message to ensure they have
               sufficient Netmail "credits" to send the message.  

               For example, if a caller is replying to a Netmail message
               originating from Japan and their user record only has 75
               Netmail credits, they will not be allowed to reply because the
               default cost of an international message is 125 credits (or
               $1.25).  Now if they had more than 125 credits, WILDCAT! would
               allow them to continue with the reply.

               The first line BELOW the COST keyword begins the actual lookup
               table for phone numbers to match for specific costing.  These
               entries are broken up into two categories or columns, the
               DIALING PREFIX and the ACTUAL COST.  These two columns MUST
               be separated by at least one space.  A COST value of 0
               indicates there are no Netmail "credits" required to send mail
               within the defined DIALING PREFIX.  Shown below are some
               sample entries.

                                1-510-687    4
                                1-415-       0  
                                1-707-       6  
                                1-805-334    10 
                                61-          79  

               As previously stated, the first column is the DIALING PREFIX. 
               The dialing prefix can contain something simple such as 1-707-
               which would mean a match would be found for any phone number
               of systems with that area code.  Or something as detailed as
               a complete phone number.  The shorter the string of numbers
               defined, the greater the possibility of a match.  

               In the above example, a first column entry of 61- indicates
               that any messages addressed to ANY phone numbers of systems
               in Australia (61 is its COUNTRY CODE) would have an associated
               cost of 79 Netmail credits (79 cents).  

               Likewise, the 1-510-687 entry is used to define a per-message
               cost of 4 Netmail credits (cents) to phone numbers of systems
               that begin with that number sequence.




          WILDNODE! v1.50                                        Page  9
          WILDNODE.CFG FILE



          COST - continued

               A maximum number of dialing prefix entries is 200.  Typically,
               the cost table lists domestic prefixes first, including a
               section devoted to your local calling area.  The latter
               portion is devoted to international prefixes, if applicable.

               It should be noted that the end of the "costing table" is
               defined appropriately enough, by placing the END keyword after
               the last dialing prefix/cost.  VERY IMPORTANT!


          DISPLAY SCREEN

          With the release of v1.50 of WILDNODE!, a new display screen has
          been added to enhance the quality of the program.  This screen
          displays a visual indication of the compilation progress thru the
          use of "gas gauge" bar graphs and a table of the nodelist(s) to
          process.  Shown below is a sample screen.


     ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
     ³ WILDNODE! v1.50     Nodelist Compiler for WILDCAT! v3.+     (09/01/92) ³
     ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
     ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
     ³ Currently Processing Zone: 100  Net: 102  Total Nodes Compiled: 14305  ³
     ³                                                                        ³
     ³        DBNET.234 : ÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛ°°°°  92%    ³
     ³     Overall Time : ÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛ°  99%    ³
     ³     Using Zones  : 1 8 86 100                                          ³
     ³                                                                        ³
     ³ Type   Nodelist Name   Start     Finish   Elapsed   Zones  Nets  Nodes ³
     ³ ÄÄÄÄÄ  ÄÄÄÄÄÄÄÄÄÄÄÄÄ  ÄÄÄÄÄÄÄÄ  ÄÄÄÄÄÄÄÄ  ÄÄÄÄÄÄÄÄ  ÄÄÄÄÄ  ÄÄÄÄ  ÄÄÄÄÄ ³
     ³ (Pri)  NODELIST.234   16:12:09  16:14:11  00:02:02    6     586  18814 ³
     ³ (Pvt)  MAGNET.234     16:14:11  16:14:19  00:00:08    1     21   187   ³
     ³ (Pvt)  FMLYLIST.234   16:14:19  16:14:35  00:00:16    1     112  957   ³
     ³ (Pvt)  POWERNET.234   16:14:35  16:14:36  00:00:01    1     2    13    ³
     ³ (Pvt)  DBNET.234      16:14:36                                         ³
     ³                                                                        ³
     ³                                                                        ³
     ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾
      ESC-Abort        (c) Online Computer Resources 1991, 1992 (510) 687-1122


          When executing WILDNODE!, the following three display items are
          referencing the nodelist that is currently being compiled (in this
          case, DBNET.234).  These items are:

          CURRENTLY PROCESSING ZONE: 100 -
               The number indicated here shows the zone that is currently
               being processed.  This number increments as each zone is being
               processed. 




          WILDNODE! v1.50                                        Page 10
          DISPLAY SCREEN



          DISPLAY SCREEN - continued

          NET: 102 -
               This number is similar to the zone, except this is the network
               address that is being processed for the current zone number.

          TOTAL NODES COMPILED: 14305 -
               The number here indicates the number of nodes that WILDNODE!
               has added to its database.  This is not to be confused with
               the total number of nodes in the various nodelists.


          As a visual representation of the status of WILDNODE! as it
          progresses, bar graphs are used to show percentage of completion. 
          In addition to the graphs, a numeric percentage is also displayed
          to the right of the bar graph.  These items are:


          DBNET.234 : -
               The filename indicated here is the nodelist that is currently
               being processed.  To the right of this name is the bar graph
               that indicates the percentage of completion for this nodelist
               only.

          OVERALL TIME : -
               This graph indicates the overall estimated time required to
               process all of the defined (as indicated) nodelist(s).

          USING ZONES  : 1 8 86 100 -
               The numbers indicated here represent the zones to include as
               configured via the ZONES keyword in the WILDNODE.CFG file. 
               Since there can be up to 255 zones defined, if the total
               number of selected zones can not be placed on the screen,
               those that will fit will be followed by "..." to indicate more
               zones are to be processed.


          The above information is followed by a table that is dynamically
          built according to the number of PVTLIST keywords that have been
          previously defined in the WILDNODE.CFG file.  In other words, if
          you've defined 2 PVTLIST nodelists to be processed, they will be
          displayed after the primary NODELIST for a total of three nodelists
          to be processed.  Below is a breakdown of the various fields in
          this table.


          TYPE -
               At present, there are only two types of nodelists that can be
               compiled, primary and private.  The primary nodelist is one
               which is called NODELIST.nnn and is indicated by the (Pri)
               flag.  All other nodelists defined via the PVTLIST keyword
               will display the (Pvt) or private flag in this column.




          WILDNODE! v1.50                                        Page 11
          DISPLAY SCREEN



          DISPLAY SCREEN - continued

          NODELIST NAME -
               This field is self-explanatory in that this is the DOS file
               name of the nodelist(s) to be processed.

          START -
               The number indicated here represents the start time in
               [hh:mm:ss] when processing began on this nodelist.

          FINISH -
               The number indicated here represents the time in [hh:mm:ss]
               when processing completed on this nodelist.

          ELAPSED -
               This field indicates the total time required to process this
               nodelist in [hh:mm:ss] format.

          ZONES -
               This number is used to represent the total number of zones
               that have been FOUND within this nodelist.  This should not
               be confused with the actual number of zones to include when
               compiling.

          NETS -
               As with the Zones field, this number represents the total
               number of networks FOUND within this nodelist.

          NODES -
               This number is similar to both Zones and Nets in that it
               indicates the total number of node addresses that are in the
               CURRENT nodelist.


          KEYSTROKE OPTIONS

          When WILDNODE! has been executed, it could take several minutes to
          complete.  If you've spotted something that possibly wasn't
          configured properly, you can simply press [ESCAPE] at anytime to
          abort the process.  Pressing this key brings up a friendly prompt
          asking if you really want to abort the compilation process or not. 
          If you wish to carry on, answering NO will continue the process,
          otherwise you will be returned to the DOS prompt.






          WILDNODE! v1.50                                        Page 12
          ADDITIONAL DISPLAY PROMPTS

     

          ADDITIONAL DISPLAY PROMPTS

          Once WILDNODE! has finished compiling the nodelists and if EMS
          memory was present, a prompt at the bottom of the screen indicates
          it's busy writing the files out to disk.  WILDNODE! at this point
          is merely flushing the information stored in EMS to the database
          files.

          Once the file has been successfully written to disk, WILDNODE! will
          pause a few seconds giving you time to read the screen before
          returning to DOS.  Prior to actually displaying the DOS prompt,
          WILDNODE! will indicate the total time it took to process all the
          nodelists.


          COMMON QUESTIONS/PROBLEMS

          Question: When I attempt to enter a Netmail message, the following
                    prompt is displayed.  Why?

                    "Netmail services are currently unavailable"

          Answer:   This prompt is generated by WILDCAT! when it can't find
                    the necessary database files to look up the destination
                    address.  Generally this indicates one of the following:
                    1) WILDNODE.DAT/IX files are not in the same path as
                    NODEINFO.DAT, 2) the SET WCNODELIST command hasn't been
                    defined, 3) it's incorrectly set or 4) WILDNODE! hasn't
                    been successfully installed.  Please review the
                    installation procedures outlined in the beginning of
                    this DOC file for additional details.


          Question: Upon entering in the destination address for the Netmail
                    message, WILDCAT! displays the following prompt.  Why?

                    "Sorry, you don't have sufficient netmail credit to send
                    this message"

          Answer:   Actually, the message is self-explanatory.  It's
                    WILDCAT!'s way of stating that the user record of the
                    person in question simply doesn't have the necessary
                    Netmail "credits" to send the message.  From the SysOp's
                    Menu, [U]ser Database, Option #30  displays the current
                    Netmail Balance.  Simply establish a balance higher than
                    the minimum "per message" cost (defined in WILDNODE.CFG)
                    and you'll be able to send the message.






          WILDNODE! v1.50                                        Page 13
          TECHNICAL SUPPORT



          TECHNICAL SUPPORT

          You may contact Online Computer Resources at 1:161/503 or 1:161/504
          via netmail or by logging on to the BBS for technical support.  We
          can also be reached in the WILDCAT! conference on Fidonet.  Our
          regular business hours are 9am-6pm M-F and 10am-5pm Saturdays PST
          and our VOICE number is (510) 687-1122.

          For even faster support, zip up your WILDNODE.CFG and any nodelist
          file(s) in question into a unique file name and send it to our
          support board at:

                    (510) 687-0236 (1:161/503) USR Dual Standard
                    (510) 687-2134 (1:161/504) V.32bis PPI

          If your configuration file is already on our system before you
          call, we will be able to immediately look at your present
          configuration and offer any assistance needed much faster and
          ultimately more effectively.


          PRODUCT REGISTRATION

          WILDNODE! is released free of charge to the general public and no
          registration fees are required for its usage.  A simple thank you
          is sufficient payment.




          WILDNODE! v1.50                                        Page 14
          LICENSING AND DISTRIBUTION AGREEMENT



          Copyright (C) 1991, 1992 by Online Computer Resources.  ALL RIGHTS
          RESERVED.  COMMERCIAL DISTRIBUTION AND/OR USE PROHIBITED WITHOUT
          WRITTEN PERMISSION FROM Online Computer Resources.

          Non-Commercial distribution and/or use is permitted under the
          following terms:

          1)   You may copy and distribute copies of WILDNODE! executable
               code as you receive it, in any medium, provided that you do
               so in a lawful, friendly manner and that you conspicuously and
               appropriately publish on each copy of each file that is a part
               of the distribution package a valid copyright notice:

               "Copyright (C) 1991, 1992 by Online Computer Resources.  Any
               copies that you distribute must be distributed free of charge
               to the recipient of the copy.  WILDNODE! may not be sold and
               you may not rent or lease it to any other person."

          2)   You must keep this License Agreement intact and give any other
               recipients of the WILDNODE! program a copy of this License
               Agreement along with the program.

          3)   You must distribute WILDNODE! in unmodified form.  You may not
               add an advertisement for your Bulletin Board System, User
               Group, or anything else either as a file in the distribution
               packet or as a header in any archive.  You may not add, modify
               or delete any of the files in the WILDNODE! distribution
               archive.

          4)   WILDNODE! must be distributed for free. You may not charge a
               distribution fee for the physical act of transferring a copy
               of this program.  You may not place this program in any file
               area of a Bulletin Board System where a fee is required for
               download.

          5)   You may not modify your copy or copies of WILDNODE! or any
               portion of it and you can not copy and distribute any
               modifications.  WILDNODE! is distributed in ZIP format and you
               may not distribute it in any other form.

          6)   You may not copy, sublicense, distribute or transfer WILDNODE!
               except as expressly provided under this License Agreement. 
               Any attempt otherwise to copy, sublicense, distribute or
               transfer WILDNODE! is void and your rights to use the program
               under this License agreement shall be automatically
               terminated.




          WILDNODE! v1.50                                        Page 15
          LICENSING AND DISTRIBUTION AGREEMENT



          7)   You may not incorporate parts of WILDNODE! into other programs
               without the written permission of Online Computer Resources.
               Permission may or may not be granted based upon a
               determination of what your intended use is.

          8)   For the purposes of this document, "COMMERCIAL USE" is defined
               as concurrent operation of the software on one or more
               computers or data lines owned by the same for-profit
               organization.  Any organization may operate this software
               under the terms of this Non-Commercial Agreement if operation
               is limited to two or less computers or data lines.

          9)   You may use the software only after understanding and agreeing
               upon the above terms.



          NO WARRANTY
          ===========

          THIS PROGRAM IS GUARANTEED TO DO ABSOLUTELY NOTHING EXCEPT TAKE UP
          DISK SPACE.  USE IT AT YOUR OWN RISK.  NEITHER ONLINE COMPUTER
          RESOURCES NOR ANY OTHER PERSON INVOLVED IN IT'S DISTRIBUTION IS
          RESPONSIBLE IN ANY WAY, FOR ANY DAMAGES RESULTING FROM ITS USE OR
          MISUSE, DIRECTLY OR INDIRECTLY.

          THE ENTIRE RISK AS TO THE QUALITY AND PERFORMANCE OF WILDNODE! IS
          ENTIRELY WITH YOU.  SHOULD WILDNODE! PROVE DEFECTIVE, YOU ASSUME
          THE COST OF ALL NECESSARY SERVICING, REPAIR OR OTHER DAMAGES TO
          YOUR EQUIPMENT, SOFTWARE, OR OTHER PROPERTY.

          ONLINE COMPUTER RESOURCES IS NOT RESPONSIBLE TO YOU FOR DAMAGES,
          INCLUDING BUT NOT LIMITED TO, ANY LOST PROFITS, LOST MONIES, OR
          OTHER SPECIAL, GENERAL, INCIDENTAL OR CONSEQUENTIAL DAMAGES ARISING
          OUT OF THE USE OR INABILITY TO USE (INCLUDING BUT NOT LIMITED TO
          LOSS OF DATA OR DATA BEING RENDERED INACCURATE OR LOSSES SUSTAINED
          BY THIRD PARTIES OR A FAILURE OF THE PROGRAM TO OPERATE WITH ANY
          OTHER PROGRAMS) OR ANY OTHER LOSS EVEN IF YOU HAVE BEEN ADVISED OF
          THE POSSIBILITY OF SUCH DAMAGES, OR FOR ANY CLAIM BY ANY OTHER
          PARTY.