FILE: AC.DOC
                                                      
                                                        JAMES GRIGGS
                                                        10/29/86


                ANALOG CIRCUIT ANALYSIS PROGRAM





THIS PROGRAM ENABLES ANALOG AC CIRCUIT ANALYSIS TO BE PERFORMED
ON A ATARI ST COMPUTER. THE CIRCUIT MAY BE OF A  PASSIVE  OR
ACTIVE TYPE.



TO RUN THE PROGRAM:
   Open file "AC.PRG"


THERE ARE SEVERAL RULES TO FOLLOW IN USING THIS ROUTINE.

1) WHEN ASKED FOR THE NUMBER OF NODES, THE ANSWER SHOULD NOT 
   INCLUDE GROUND WHICH IS ALWAYS NODE "0".
2) ALL UNUSED PINS OF ACTIVE DEVICES MUST BE TIED TO GROUND
   (NODE "0").
3) ALL COMPONENTS THAT ARE TIED TO DC SUPPLIES MUST BE 
   ENTERED AS TIED TO NODE "0".
4) THE LIWER LIMIT OF THE ENTERED FREQUENCY RANGE CANNOT
   BE 0 HZ.
5) WHEN USING THE LOG FREQUENCY INCREMENT (ENTER A NEGATIVE
   NUMBER), THE NUMBER ENTERED MUST BE THE NUMBER OF LOG-SPACED
   FREQUENCIES DESIRED BETWEEN THE FREQUENCY LIMITS SPECIFIED.
6) FOR TRANSISTORS, Rbe CAN BE CALCULATED IF THE QUIESCENT
   EMITTER CURRENT IS KNOWN BY:

                             -3
                Rbe = 26 X 10
                      ---------------
                      EMITTER CURRENT

    FOR EXAMPLE: IF THE EMITTER CURRENT = 2ma, THEN 
                     -3          -3
        Rbe = (26 X10  ) / (2 X10  ) = 13 OHMS.

     FOR MOST CIRCUITS, A VALUE OF "1" MAY BE USED AND GET VERY
CLOSE RESULTS.








THE FOLLOWING ARE EXAMPLES OF CIRCUITS ANALYZED BY
THIS PROGRAM.

FIRST, LETS ANALYZE THE FOLLOWING CIRCUIT...

NODE:1           NODE:2           NODE:3        NODE:4
O--------- R1 -----X------ L1 ------X---- L2 -----X------
INPUT              |                |             |     |
O--                |                |             |     |
  |            C1 ---           C2 ---        C3 ---    R2
  |               ---              ---           ---    (LOAD)
  |                |                |             |     |
  |                |                |             |     |
 GND              GND              GND           GND   GND

R1= 50 OHMS
R2= 50 OHMS(LOAD)
L1= 330UH
L2= 330UH
C1= 0.053UF
C2=0.177UF
C3=0.053UF

THE DATA MUST BE ENTERED IN THE FOLLOWING FORMAT:

R (RESISTOR)            FROM NODE#, TO NODE#, VALUE IN OHMS
C (CAPACITOR)           FROM NODE#, TO NODE#, VALUE IN UFD
L (INDUCTOR)            FROM NODE#, TO NODE #, HENRIES
F (FET)                 GATE, SOURCE, DRAIN, GAIN(A/V)
N (NPN)                 JBASE, EMIT, COLL, BETA, B-E OHMS
A (OP AMP)              +IN, -IN, +OUT, -OUT, GAIN, OHMS OUT
E (END OF DATA MARKER)  INPUT NODE #, OUTPUT NODE #



THE FOLLOWING IS HOW TO ENTER THE ABOVE PROGRAM...
NUMBER OF NODES: 4

R 
1,2,50

C 
2,0,0.053    (NODE 0 IS GROUND, DC VOLTAGE SOURCE, OR UNUSED OP AMP PINS)

L
2,3,3.3E-04

C
3,0,0.177









L
3,4,3.3E-04

C
4,0,0.053

R
4,0,50

E 
1,4

START FREQ,END FREQ,FREQ INCREMENT
100,60000,10000


PROGRAM RESULTS:

FREQ            DB              PHASE
100             -6.02           -.5
10100           -6.02           -50.2
20100           -6.05           -103.2
30100           -6.55           -166.4
40100           -10.57          118.7
50100           -18.47          64.9

HERE, WE SEE THE FREQUENCY RESPONSE FROM 100HZ TO 60KHZ AND THE
PHASE RELATIONSHIP.























NEXT, LETS ANALYZE THE FOLLOWING OP AMP CIRCUIT...


NODE:1      +  U1
    O---------|\    NODE:3
              | >---X-------- OUTPUT
        ------|/    |
        |    -      |
        X-------R1--|
NODE:2  |
        |
        R2
        |
        |
       GND

U1= TYPICAL OP AMP
R1= 9 K OHMS
R2= 1 K OHM


THE FOLLOWING IS HOW TO ENTER THE ABOVE PROGRAM...
NUMBER OF NODES: 3

R 
2,3,9000

R
2,0,1000

A
1,2,3,0,20000,1         (FORMAT: +IN, -IN, +OUT, -OUT, GAIN, OHMS OUT)

E
1,3

START FREQ,END FREQ,FREQ INCREMENT
1,11,5

PROGRAM RESULTS:

FREQ            DB              PHASE
1               20              0
6               20              0
11              20              0










NEXT, LETS ANALYZE THE FOLLOWING FET CIRCUIT...

                                 NODE:0
         ------------X-----R1----VCC
         |           |
         C1          |
  NODE:0 |           |
        GND          |NODE:3
            |--------X------------- OUTPUT  
NODE:1      |
----------->| Q1
            |
            |---
               | NODE:2
               |
               R2
               |
       NODE:0 GND


Q1= FET
R1= 10 K OHMS
R2= 1 K OHM
C1= 0.01 UF

THE FOLLOWING IS HOW TO ENTER THE ABOVE PROGRAM...
NUMBER OF NODES: 3

R 
3,0,10000

R
2,0,1000

F
1,2,3,200               GATE, SOURCE, DRAIN, GAIN(A/V)

C
0,3,.01

E
1,3

START FREQ,END FREQ,FREQ INCREMENT
1,2000,100









PROGRAM RESULTS:

FREQ            DB              PHASE
1               20.06           180
101             20.04           176.4
201             19.99           172.8
301             19.91           169.3
401             19.79           165.9
501             19.65           162.5
601             19.48           159.3
701             19.29           156.2
801             19.08           153.3
901             18.85           150.5
1001            18.61           147.8
1101            18.36           145.3
1201            18.1            143
1301            17.84           140.7
1401            17.57           138.6
1501            17.3            136.7
1601            17.03           134.8
1701            16.75           133.1
1801            16.48           131.5
1901            16.21           129.9


NOTE:
     This program is interactive with the user and requires
the circuit net work to be reentered each time the program 
is run. Two other versions are available from me. The first
is like this one except with  Gem and mouse features, and a 
second that lets the user enter the circuit data in a sequential
file from a word processor such as 1st word. When run, the program
gets all the circuit netword data from the file and displays
analysis of the node selected. This has an advantage of only having
to enter the data once and then running the program as often
as you like. Also, when designing a circuit, one value can
be changed in the file and the program rerun without having 
to retype any of the other values. If interested my address is

James Griggs
5213 35th Ave W.
Bradenton, Fl. 33529