YAESU 757 GX MK II CAT PROGRAM
                             By Dick Roux N1AED



                   Please support the SHAREWARE concept !!
              If this Program is usefull to you please send a
                             donation of $15 to:
  
                               Dick Roux N1AED
                              25 Greenfield Dr.
                             Merrimack N.H. 03054

               You will then be notified of any updates to the
                              program which may
                         be obtained for a small fee





           CAT757.EXE is a Computer Aided Tuning program written for
        IBM & MSDOS computers utilizing the YAESU FT-757 GX Mark II
        Tranceiver and the YAESU FIF-232C Computer Interface. It was
        written in BASIC and compiled with Microsoft's Quickbasic
        3.0.
           The program exploits the full capability of the FT-757 GX
        MK II's capability of sending status back to the computer
        (which the older FT-757 GX does not) and displaying it on
        the computers screen. Also nearly every front panel function
        can be controlled via the computer.
           Also,  the program has a Stations Directory display where
        up to 120 stations can be programmed for instant call-up with
        just 1 keystroke.
  
        CONFIGURATION
        -------------
           The program can be run from either a floppy drive or a
        hard disk, just make sure that the two files CAT757.EXE &
        STATIONS.DIR reside on the floppy or in the same subdirec-
        tory on you hard drive.
        Cable the Tranceiver and FIF-232C to the computer via COM
        PORT 1

        OPERATION
        ---------
           To run the program just type CAT757 at the DOS prompt. You
        will then get the Shareware banner followed by a prompt
        asking you if you want Color or not. You will then get the
        Main Menu with which you can select the different displays.
        Hitting [1] will send out a polling instruction to the
        tranceiver and give a detailed status display of the
        condition of the VFO's, MEMORIES, SPLIT, DIAL LOCKING,
        CLARIFIER and what the present OPERATING FREQUENCY is. Any
        manual changes made to the tranceiver on its front panel will
        not show up on the status display untill another poll is made
        of the tranceiver's condition by exiting and re-entering the
        STATUS display.
       
        PLEASE NOTE:
       
        The STATUS function only works on the FT-757 GX Mark II. the
        older FT-757 GX does not provide status to the tranceiver and
        program lock-up will occur.
          If program lock-up occurs on the FT-757 GX Mark II when
        trying to poll the tranceiver's status, check your
        tranceiver, interface and cables as this indicates that no
        response is being supplied from the tranceiver and the
        program will literally wait forever for the tranceiver to
        respond.  Resetting the computer is the best way of exiting
        this condition.


           Hitting a [2] at the Main Menu brings you to the
        CONFIGURATION Display where you can make changes to the
        operating parameters of the tranceiver. It's use is pretty
        self-explanatory and should be easy to use with some
        experimentation.  Hitting a [3] will bring you to the
        STATIONS DIRECTORY display where you can insert up to 120
        pre-programmed frequencies. A few have been already entered
        for you. The prompt at the bottom of the display allows you
        to EDIT (or add) any entries, QUIT to the Main Menu or LOAD
        pre-programmed entries into the Tranceiver's Memories.
           To EDIT a frequency just hit <E> and you will be prompted
        for the entry to edit followed by a prompt:
 
        NAME,FREQ,MODE
 
        enter name followed by a comma ,the frequency (in KHZ)
        followed by a comma, and the mode (USB,AM etc). Here is a
        sample entry:

        WWV,10000,AM

          Up to 120 entries can be programmed and are automatically
        saved to disk when exiting the STATIONS DIRECTORY.
          To load frequencies from the Directory into the
        tranceiver's memories just type <L>. you will then be
        prompted for memory # and display selection, like this:

        INPUT MEMORY #, SELECTION TO LOAD?

        Typing 0,10 will load memory # 0 on the radio with Directory
          10's contents.
          And of course hitting [4] will let you exit to DOS.

           The program is very functional and could have had alot of
        "bells and whistles" added which may be included in future
        releases if acceptance to the Program is widespread.
           Please feel free to contact me if you have any comments
        and/or suggestions on the Program.