CAT757

                                  Version 3.0

                             Yaesu FT-757GX Mark II

                         Copyright (c) 1989, 1990, 1991

                                   Written by

                             Richard M. Roux N1AED
                               25 Greenfield Dr.
                              Merrimack, NH 03054
                                 (603)429-0945








                              PROGRAM DESCRIPTION


            CAT757 is a control program designed to provide control of
         the Yaesu FT-757 GX Mark II with an IBM compatible PC.  The
         program provides programming of all front panel functions
         from the keyboard. The program allows you to store a maximum
         of 480 frequencies in the Station Directory, which may be
         scanned in numerous ways. Alternate files may be loaded
         providing database functions limited only by disk storage
         available.  The program has a built-in Terminal Program for
         PACKET/RTTY or AMTOR that allows simultaneous transceiver
         control. A second COM port is required for a simultaneos
         Terminal function.

            Minimum requirements for hardware are 512K of memory,
         Mono/CGA/EGA/VGA display and one COM port (2 Desirable).


                                    Disclaimer

           This Demonstration Disk is being distributed via the
         Shareware concept. You are encouraged to try the program out
         and make unmodified copies for others who may be able to make
         use of the program, but no fees may be charged other than a
         nominal copying fee.

           If you would like to order the program, Please send $39.95
         plus $3.00 Shipping & Handling to the author at the above
         address. Specify 5.25" or 3.5" disk.




                                    -- 1 --









                              PROGRAM INSTALLATION


         FLOPPY SYSTEM

            No special installation is required. Make a working copy
         of the distribution diskette, log on to the drive where the
         working disk is located and run the setup program to
         configure colors, COM port setup and baud rate for the
         Terminal program. DO NOT write protect the disk, this will
         allow updated Station Directory entries to be saved to the
         working disk.

         HARD DRIVE SYSTEM

            Create a sub-directory to hold the files, such as C:\CAT.
         Copy all the files to it and run the setup program to
         configure colors, COM port setup and baud rate for the
         Terminal program.


                               THE SETUP PROGRAM
         NOTE: The SETUP program only exists in the Registered Version

            After you have either created a working disk or copied the
         files to your hard drive, log onto the floppy where the
         program files are located or into the subdirectory on your
         hard drive where the files are located. At the DOS prompt
         type SETUP. The setup program will check to see if a color
         card is present and if a COM 2 port exists.

            If a COM 1 and COM 2 port are detected, you will be
         prompted for port assignments for the Transceiver controller
         and for the Terminal program. If only one COM port is
         detected, the Transceiver controller is automatically
         assigned to COM 1 and assignment of COM 2 is bypassed. You
         will be prompted for the desired SCANDELAY and STEPRATE
         values when the program boots. These may be changed within
         the program, but this prompt allows setup of the initial
         values.

            You will then be prompted if all settings are correct.
         Next, you will be prompted for color assignments.  If a
         monochrome card was detected in the previous step, then color
         assignments are bypassed, settings are saved, and you will
         exit the SETUP program. With a color graphics card detected,
         you will be shown a screen where you can select foreground ,
         background, status line, highlight, and window colors. The
         color number is shown near each selection to aid you in
         selecting the color. If you have a color graphics card and a
         monochrome monitor then you are limited in your selections.





                                    -- 2 --









         The available colors are:

          0  Black       8  Gray
          1  Blue        9  Light Blue
          2  Green       10 Light Green
          3  Cyan        11 Light Cyan
          4  Red         12 Light Red
          5  Magenta     13 Light Magenta
          6  Brown       14 Yellow
          7  White       15 High-Intensity White

            After desired colors are selected, selecting '8' will save
         the settings and allows you to exit the program.


                               PROGRAM OPERATION


            Log on to the drive where the program is on a floppy
         system or on a hard drive system CD to the sub-directory
         where the program resides. Run the setup program by typing
         SETUP at the DOS prompt. The SETUP program examines the
         computer for the presence of a Color Graphics Card and a
         second COM port. Answer all the prompts and exit the program
         to store all your selections.
            Start the program by typing in CAT757.  Additionally,
         alternate files for the station directory may be loaded on
         the DOS command line at this time.  Just type CAT757
         filename. A couple of sample Directory files are supplied on
         the distribution disk.

         EXAMPLE:

         CAT757 TOP100.DIR or CAT757 TOP100

            This loads the program and the alternate Directory
         TOP100.DIR. The default directory CAT757.DIR will be loaded
         if no alternate directory is specified on the DOS command
         line.

            After the initial Welcome and Copyright screen the Main
         Status Display will appear. At the graphic presentation of
         the FT-757, the program sends the radio an initialization
         command putting the transceiver in somewhat of a "known"
         condition.  Then a STATUS REQUEST is sent to the Transceiver.
         The GX Mark II responds with 75 bytes of status and, at this
         point, the correct VFO and Mode should appear on the Main
         Status Display. If "0.00" for a VFO frequency appears, then
         there is an interface problem between the Computer and the
         Transceiver. Check all cables, the interface and make sure
         everything is powered up. Also make sure you have selected
         the correct COM port in the SETUP program.




                                    -- 3 --









                            THE MAIN STATUS DISPLAY


         The commands available on the Main Display:

         Alt-Q

            Hitting Alt-Q will allow you to exit to DOS.

         F1

            Brings up the Help Window.  Hitting any of the command
         keys activates that function and any other key closes the
         window.

         F10

            Pressing F10 will bring up the Memory Contents Window
         allowing you to view the contents of the transceiver's 10
         memories. Hitting any key closes the window.

         ( < Left Arrow ) Load VFO W/ Memory

            This allows you to load the contents of any of the
         memories into the active VFO. The Memory Contents Window will
         appear allowing you to view what's in the transceiver's 10
         memories.

         ( > Right Arrow ) Load Memory W/VFO

            This allows you to program any of the 10 memories with the
         contents of the current active VFO. The Memory Contents
         Window will appear allowing you to view what's in the
         transceiver's 10 memories.

         (S)plit

           Hitting "S" toggles the transceiver in/out of the split
         mode.

         (D)ial Lock

            This toggles the Dial Lock on/off.


         (V)FO A/B

            This toggles between A and B VFO.

         (C)larifier

            Toggles the clarifier on/off.




                                    -- 4 --










         (F)requency Change

            Allows you to type in a new VFO frequency between the
         limits of 150 - 29999.99 Khz. All frequencies in this program
         are displayed and typed in Khz only. Mhz input is rejected.

         EXAMPLE: Enter 21.230.10 Mhz as 21230.10

         Status Re(Q)uest

            This allows you to request a fresh set of parameters from
         the transceiver to update the display if you have made any
         manual changes to the transceiver.

         S(W)ap VFO/MEMORY

            This swap the contents of the VFO with the contents of the
         currently selected memory.

         (M)ode Change

            This step the current VFO through the six available modes.

         (H)am/General

            Toggles between HAM and General receive.

         Change Step (R)ate

            This allows change of the step rate, minimum of which is
         .01 Khz. This is the change in VFO frequency when the "+" and
         "-" keys are hit. Great for fine tuning SSB and Packet
         signals. .01 Khz.= 10 Hertz/Cycles

         Station Director(Y)

            This bring you to the 480 entry Station Directory display.

         (L)og VFO Freq/Mode to Station Directory

            This allows logging of the current VFO Freq. & Mode to the
         first empty entry in the Station Directory. You will be
         prompted for a Name/Description (IE:"Radio Moscow") for the
         entry.  Only the first 21 characters of the description are
         retained.

         (T)erminal Program

            This selects the built-in terminal program which is
         suitable for controlling a TNC for PACKET/RTTY/AMTOR. If no
         second COM port is detected you will be given an error
         informing you of that fact. All baud rates 300 - 9600 are
         available in the Setup Program.  You can change VFO


                                    -- 5 --









         frequencies, change modes, and make small (down to .01 khz.)
         step changes in VFO frequency while using the Terminal
         Program.  The controller for the transceiver is connected to
         one COM port while the TNC is connected to the other.  If you
         don't have a second COM port, consider installing one, as
         this program makes operating a TU a real pleasure.  Most
         serial I/O cards have provision for a second COM port and all
         that is usually required is installing some extra chips. See
         the section on the Terminal Program for detailed instructions
         on how to use the Terminal function.

         (E)dit Memory Contents

            This allows you to edit/update any of the 10 transceiver's
         memories. The Transceiver's memory is updated as well as the
         Memory Contents Display.

         (Up-Arrow)

            Step the active VFO Frequency up 500 Khz.

         (Down-Arrow)

            Step the active VFO Frequency down 500 Khz.

         (+) (-) Fine Tune

            This allows incrementing of VFO frequency by an amount
         determined by the setting of the STEP RATE.

         ALSO NOTE: The "=" also functions as the "+" key for those of
         you who have keyboards that do not have the separate number
         keypad.

         (SPACE)

            Hitting the SPACE bar will update the Signal Strength
         meter which displays relative signal strength. If you AGC set
         on SLOW, this might need to be tapped a second or two after
         changing frequencies. Actually, hitting any other none-
         command key will update the signal-strength meter.


                             THE STATION DIRECTORY


            After selecting 'Y' form the Main Menu, the first page of
         the Station Directory will appear. The Station Directory
         provides up to 480 frequencies at your disposal for uploading
         to the VFO or for programming of any or all of the
         transceiver's 10 memories.  Any entry in the directory can be
         tagged for scanning or uploaded to memory or can be locked
         out for bypass the same way a police scanner operates. This
         way you can limit scanning to the particular frequencies of


                                    -- 6 --









         interest.

            Adding and editing entries is a breeze, as compared to
         older versions of CAT757. Scan delay and step rate are also
         fully adjustable from the Station Directory as well as the
         "+" and "-" fine tune keys being functional during this
         display making small adjustments of the VFO frequency a
         simple task.

            Printing of the Station Directory entries to a line
         printer is also supported, with printout of up to 120 entries
         per page.

         The commands available on the Station Directory in detail:

         F1 Help

           Displays the Help Window

         PageUp/PageDown/End/Home

            These keys allow you to move back and forth, to the
         beginning or to the last full page of the Station Directory.

         Selecting Entries

            To select an entry to be uploaded to the transceiver's VFO
         type in the entry number and hit <ENTER>. No other menu
         selection is required.

         Tagging Entries

            Entries are tagged for scanning/upload by selecting the
         entry number, followed by a "T" for tagging or a "L" for
         lockout and hitting <ENTER>. A check-mark will appear near
         the tagged entries or a small block near the locked out
         entries.

         EXAMPLE:

         22T <ENTER>

         Will tag entry # 22.

         22 <ENTER>

         Will load entry # 22 into the active VFO.

           To untag/unlock entries, type the entry followed by a "U"
         and <ENTER>. This will either untag or unlock any previously
         tagged or locked out entries. The check-mark and/or graphics
         block will then disappear.




                                    -- 7 --









         ESC

            Exit back to the Main Status Display.

         (A)dd

            Hitting ADD will advance you to the first empty Directory
         Entry and the cursor will be placed on the Name field.  Type
         the name of the entry followed by <ENTER>. The cursor will
         be advanced to the Frequency field. Type a valid frequency
         (in Khz) and hit <ENTER>. Invalid frequencies will be
         rejected. The cursor will advance to the Mode field.  Type a
         valid mode (USB, AM etc.) and hit <ENTER>. Invalid modes will
         be rejected.

            The cursor will advance to the next empty Directory
         listing. The ADD function has a DITTO mode in which hitting
         <ENTER> on any one of the three fields will bring up the
         entry of the field on the PREVIOUS directory entry. If you
         need to enter a group of entries with the same Name and Mode
         the DITTO will save you a bit of unnecessary typing.
         Continue until you've entered all the listings you desire.
         To terminate the ADD function type DONE in the name field on
         the last entry and the ADD mode will be terminated.

            All entries are now in memory and will be saved when you
         exit back to the Main Status Display. Matter of fact, any
         changes made to the Station Directory will ONLY be saved
         if you exit back to the Main Status Display or if you select
         another Directory file for loading. MAKE SURE that if you are
         running the program from a floppy, that disk IS NOT write
         protected. Powering down the computer WITHOUT exiting back to
         the Main Status Display will cause loss of all updates, so
         make sure to exit the Directory.

         (B)lock Load

            This allows upload of any 10 tagged or continuous
         Directory entries to the transceiver's memories. Make sure
         not to tag or select more than 10 entries or the input will
         be rejected. Locked-Out entries are ignored in TAGGED mode
         but are included when a continuous block is uploaded.

         (C)lear

            This selection allows you to globally clear all tags and
         lockouts.

         (D)elay

            This allows adjustment of the scan delay (entered in
         seconds) from a minimum of .5 seconds to HOURS (if you want
         to calculate the seconds).



                                    -- 8 --









         (E)dit

            This allows editing of the Directory entries. You will be
         prompted for the entry to edit and the cursor will be placed
         on that Directory entry Name field. If you don't want to
         change anything in a particular field, hit <ENTER> and the
         previous entry will be retained. Continue on for the
         Frequency and Mode fields and you will automatically exit the
         Edit mode. Typing ERASE in the name field will erase that
         complete entry and exit the edit mode.  Empty directory
         listings will be purged from the file when it is saved to
         disk.

         (L)oad Memory

            You will be prompted for the selection to upload and the
         transceiver's memory number to be loaded.

         Li(M)it Scan

            This will allow you to scan between two VFO frequencies.
         You will be prompted for the Beginning and Ending
         frequencies, again, invalid frequencies are rejected. Make
         sure to set the desired SCAN DELAY, STEP RATE and SINGLE STEP
         or CONT. scan before selecting LIMIT SCAN.

            The VFO will scan at the rate and delay you selected.  If
         in the CONT. scan mode, the SPACE bar pauses the scan.
         Hitting SPACE a second time resumes the scan. If in the
         SINGLE STEP mode, pressing the SPACE bar advances the VFO
         only. Hitting <ESC> exits the LIMIT SCAN mode.

         (N)ew Directory

            Clears out the present Station Directory, first saving any
         changes made to disk, then prompting you for a filename to
         create a new file. Type in a name up to 8 characters (NO
         EXTENSION). A filename extension of ".DIR" is automatically
         added.

         SteP (R)ate

            This allows you to specify a new step rate. A minimum of
         .01 Khz on up. Use something realistic. Setting a step rate
         of 100 Mhz probably will cause the program to crash. Common
         step rates are:

         1.0 initial setting for SSB, CW, Packet, RTTY etc.

         .01 for fine tuning SSB, CW, Packet RTTY etc.

         5.0 for AM broadcast (start with a frequency ending in 0;
             IE 9650.00)



                                    -- 9 --









         (S)can

            Starts the SCAN mode. As in the LIMIT SCAN. set the STEP
         RATE and SCAN DELAY and CONT/SINGLE STEP functions first.
         When entering the SCAN MODE you will be prompted if you want
         to scan just TAGGED selections. If you type "Y" the scan
         starts in the TAGGED mode. A minimum of two (2) Directory
         entries are required for TAGGED scan. If "N" is answered to
         the prompt then you will be prompted for the beginning and
         ending selections to scan. When the scan process begins the
         SPACE pauses the scan as explained in the LIMIT SCAN above.
         Any Locked Out entries will be skipped. ESC terminates the
         SCAN FUNCTION.

         Prin(T)

           Allows printing of the Station Directory to a line printer,
         120 entries per page. Make sure the printer is ON-LINE.

         (X)change Directory

           This allows you to load an alternate Station Directory.
         You will be shown a disk directory of all files with the
         extension of ".DIR". Type the filename (no extension needed)
         and the alternate file will be loaded. Any previous Directory
         updates will automatically be saved to disk.

         "/" Slash

            The slash key toggles the CONTINUOUS and SINGLE STEP modes
         of scanning.

         "+" "-" Fine Tune

            Allows adjustment of the VFO frequency by an amount
         determined by the setting of STEP RATE. The "=" also
         functions as the "+" key for those keyboards without a
         separate number keypad.


                           TERMINAL PROGRAM OPERATION


            If you have a second COM port selecting "T" from the Main
         Status Display, selects the TERMINAL PROGRAM.  A menu of
         options appears at the top of the screen and a STATUS BAR is
         at the bottom of the screen.

            You now have control over your transceiver and a TU or
         TNC.

         The Commands available are:




                                    -- 10 --









         ESC

           Exits the Terminal Mode and returns to the Main Status
         Display.

         F1 Clear Screen

           Clears the screen.

         F2 Disk Save

            Toggles the Save-To-Disk mode. The first press of F2
         prompts you for a file name. After that, all received text is
         saved to disk and the word "Saving.." appears on the Status
         Bar. The second press of F2 closes the disk file and
         terminates disk saving.

         F3 Change Frequency

           Allows you to change the VFO frequency. Operates the same
         as the CHANGE FREQUENCY on the Main Status Display.

         F4 Change Mode

           Toggles the transceiver though all six receive modes. Same
         operation as on Main Status Display.

         F5 Change Step Rate

           Changes the step rate. Same operation as on Main Status
         Display.

         F6 / F7 VFO Up/Down

           Works the same as the "+" & "-" keys on the Main Status
         Display and the Station Directory.


                                  Program Tips


            The Station Directory Files are in standard delimited
         ASCII format, as in the following example:

         "Radio Moscow","7115","AM"

            It is possible to edit or create them using an ASCII text
         editor. Being in the delimited format, they can be easily
         imported/exported to most popular filing programs. Keep each
         file you create down to 480 entries. Files containing more
         than 480 entries will only load to the 480th entry.

            Directory files can be sorted using the DOS SORT command.
         The following format should be used.


                                    -- 11 --










         SORT <source file >target file

         This will sort the file by Name/Description first, then by
         frequency and then by mode. The DOS file SORT.EXE will have
         to be in the path or reside on disk when using a floppy
         system.

            You might want to organize the Directory Files into
         similar type services. World Band stations in one, Ham Nets
         in another, Government Frequencies etc. Also, what is handy
         when storing AM shortwave stations is to store files by
         operating time. You could, lets say, create a file of all
         stations that are on the air from 2000 - 2100 UTC and give it
         a filename of T20-21Z.DIR. This way, you would know all the
         stations loaded into the program would be on the air during
         that time frame.

            In closing I would like to thank all the Hams who have
         used this program and have provided their support and
         suggestions on how to improve CAT757 in prior versions. I
         have implemented as many as practical and attempted to keep
         the program useful and easy to learn. As always all comments
         are welcome.

         NOW.. Explore the Airwaves and see what is being transmitted
         from 150 Khz to 30 Mhz ....

                                    ENJOY !!



























                                    -- 12 --