CATY 
		Control program for Yaesu CAT system transceivers.
	
				     Version 0.6
				    (PRERELEASE)

		Written in Turbo Pascal for PCDOS/MSDOS computers 
				by D. J. Wilke, N3HGQ.

		PRELIMINARY DOCUMENTATION - December 13, 1989.

OVERVIEW:

	CATY is a program designed to take command of your Yaesu radio 
        equipped with the CAT (Computer-Aided Tuning) system using your
	personal computer.  The software exploits the full implementation
	of the CAT system, allowing control of VFO/memory data entry,
	mode selection and tuning.  Complete status reporting from the 
	radio is displayed on screens showing all parameters grouped in 
	a logical, straightforward manner.  

	In addition to the memory channels designed into the radio, CATY 
	provides "Expanded Memory" for your Yaesu.  100 additional memory 
	channels per datafile can be copied to the internal VFO from disk, 
	allowing unlimited libraries of frequencies, modes, offsets and 
	identifying data to be archived.  These additional channels reside
	in RAM array once loaded from disk, and can be scrolled and selected 
	instantaneously.  Repeater offsets can be set automatically from
	the stored data, eliminating the tedious procedure at the radio's
	front panel.  An initial library of datafiles is provided for both 
	VFO operation and memories, containing known active services such as
	International shortwave stations, amateur repeaters, AMTOR, standard
	time signals, Radioteletype, CW, FAX, packet and standard broadcast.  

	All controllable parameters are entered from full-screen menus and 
	function keys, with the most often used functions occupying prominent 
	positions.  Between commands to the radio, the software returns 
	control to the operator, allowing manual operation to resume.  An on-
	screen real-time clock displays time in both local and UTC formats.

HARDWARE REQUIREMENTS:

	IBMPC/XT/AT or compatible with at least 256k memory.
	MDA/CGA/EGA/VGA display adapter and monitor.
	RS-232 serial communications adapter configured as COM1: or COM2:.
	Yaesu FT-747, FT-757 or FT-767 transceiver with CAT system.
	TTL to RS-232 interface for Yaesu radio.
	
THE FILES:

The distribution disk contains the following files:

	PROGRAMS:
	CATY767.EXE - The main executable program.
	LOADY.EXE   - Command line-driven memory channel loader.

        ASCII FILES:
	CATY.DOC    - What you're reading now.
	CATY1.CFG   - Config file for COM1:, rename to CATY.BAT.
	CATY2.CFG   - Config file for COM2:, rename to CATY.BAT.
	CATY.BAT    - Batch file to load CATY767.EXE with command line options.
	LOADY1.BAT  - Batch file to load memories through COM1:.
	LOADY2.BAT  - Batch file to load memories through COM2:.

	ASCII DATABASE FILES (capacity 100 entries per file):
	Y767AMB.DAT - Standard AM broadcast VFO database.
	Y767PAK.DAT - Packet radio HF/VHF VFO database.
	Y7672MR.DAT - 2 meter voice repeater VFO database.
	Y767SWA.DAT - International shortwave 2-11.5 mHz. VFO database.
	Y767SWB.DAT - International shortwave 11.5-28 mHz. VFO database.
	Y767TTA.DAT - Commercial radio teletype 2-14.5 mHz. VFO database.
	Y767TTB.DAT - Commercial radio teletype 14.5-19.3 mHz. VFO database.
	Y767TTC.DAT - Commercial radio teletype 19.3-25.5 mHz. VFO database.
	Y76725M.DAT - 25 meter shortwave band VFO database.
	Y76731M.DAT - 31 meter shortwave band VFO database.

	ASCII DATAFILES FOR MEMORIES (capacity 10 entries per file):
	Y767DEF.MEM - Default (demo) FT-767GX memory datafile.    
	Y767AMT.MEM - AMTOR/SITOR channels memory datafile.    
	Y767CWB.MEM - Amateur CW band edge memory datafile.
	Y767PHB.MEM - Amateur Phone band edge memory datafile.
	Y767PAK.MEM - HF/VHF packet radio memory datafile.
	Y7672MR.MEM - 2 meter voice repeater memory datafile.
	Y767FAX.MEM - Commercial Facsimile memory datafile.
	Y767RTY.MEM - Commercial radioteletype memory datafile.

INSTALLATION:

	Configure your computer so that the serial RS-232 port(s) are 
	available as COM1: or COM2:.  The Yaesu radio MUST have an external 
	RS-232 interface to connect to your computer OR you must provide 
	a way to communicate to/from the radio using its provided TTL 
	interface connector.  Only three communications lines are used: 
	TX (Transmit Data), RX (Receive Data) and Signal Ground.  There 
	is no hardware handshaking in the Yaesu CAT implementation, 
	so the interconnections are minimal.

	If COM1: is chosen, invoke the batch file CATY1.BAT; likewise
	CATY2.BAT for COM2:.  These files can be edited to inform the 
	local/UTC clock routines in CATY which timezone to use, the 
	default is EST.  To change to EDT, edit the second command 
	line option within the corresponding batch file, for example: 
	<CATY767 /comport /timezone> where /comport = [/1] or [/2] and
	/timezone = [/S] (Eastern Standard) or [/D] (Eastern Daylight.)

	If your system does not have a real-time clock/calendar card, 
	edit CATY1.BAT or CATY2.BAT, adding DOS DATE and TIME commands
	to set the correct local time for CATY's RTC as in the following 
	CATY2.BAT example:

		echo off
		CATY767 /2 /S
		date
		time

	If running from floppy disk, be certain all supporting files are
	present.  On hard disk systems, copy entire set of files into a
	separate directory named \CATY.  

USING THE OPTIONS:

	The program is entirely menu and function key driven.  Upon startup,
	you are presented with a full screen Main Menu and the Function 
	Keys on line 25.  The available options are:

        KEY                       WHAT IT DOES
	===  =============================================================
	1    Displays radio's status as a full screen display
	2    Queries operator and sets operating frequency
	3    Queries operator and sets programmed frequency step DOWN
	4    Queries operator and sets programmed frequency step UP
	5    Selects between VFO A, VFO B or memory
	6    Selects active memory channel, 0 through 9
	7    Sets operating mode to LSB, USB, CW, AM, FM OR FSK
	8    Selects between Ham bands and general coverage receiver
	9    Sets CTCSS tone frequencies (NOT IMPLEMENTED IN THIS RELEASE)
	0    Turns off Split, Clarifier, Offset functions
	+    Steps UP 10 Hertz in frequency, displays result
	-    Steps DN 10 Hertz in frequency, displays result

        F1   Loads memories from disk datafile
        F2   Queries operator and loads VFO A from disk datafile
        F3   Moves down to next lower band (depends on Ham/General setting)
        F4   Moves up to next higher band (depends on Ham/General setting)
        F5   Toggles SPLIT on or off
        F6   Toggles CLARIFIER on or off
        F7   Moves selection from selected memory to VFO A
	F8   Moves selection from VFO A to selected memory
        F9   Swaps contents of VFO A and selected memory
        F10  Quits the program and returns to DOS

QUICK MEMORY LOAD:

	There is a convenient way to quickly load or change all memory
	frequencies from the command line.  The datafiles ending with .MEM 
	can be loaded into the Yaesu's memories using a separate file named
	LOADY.EXE.  Two batch files are included which allow the use of
	your choice of COM port.  It is only necessary to indicate the 
	category of the desired service on the command line to LOADYx.BAT,
	as in:

		LOADY1(or 2) PAK<CR> - Loads frequencies in Y767PAK.MEM
		LOADY1(or 2) FAX<CR> - Loads frequencies in Y767FAX.MEM

					or

	You can invoke LOADY.EXE directly, providing your own command line 
	option such as:

		LOADY PAK /1<CR> - Loads Y767PAK.MEM through COM1:
		LOADY PAK /2<CR> - Loads Y767PAK.MEM through COM2:

	The default COM port is COM1: if no command line argument is 
	supplied.

        For simplicity, the command to LOADY is shortened to the three
	characters preceding the .MEM in the memory datafiles:

		Y767DEF.MEM = LOADY DEF<CR> or LOADY DEF [/1] [/2]
		Y767AMT.MEM = LOADY AMT<CR> or LOADY AMT [/1] [/2]
		Y767CWB.MEM = LOADY CWB<CR> or LOADY CWB [/1] [/2]
		Y767PHB.MEM = LOADY PHB<CR> or LOADY PHB [/1] [/2]
		Y7672MR.MEM = LOADY 2MR<CR> or LOADY 2MR [/1] [/2]
		Y767RTY.MEM = LOADY RTY<CR> or LOADY RTY [/1] [/2]

	New datafiles can be created using your favorite ASCII editor,
	just be sure to follow the structure of the included files and
	don't exceed 10 entries.  The file naming convention must be
	followed for LOADY.EXE to work.

RELEASE NOTES:

	This is a preliminary release of CATY.  This .DOC file requires 
	a great deal of work, and the code is still evolving.  The 
	program was developed entirely in Turbo Pascal Version 5.5 
	utilizing Unit files.  Future planned enhancements include:
	
		An automatic logging module
		A frequency scan function
		Integrated TNC control
		Integrated datafile creation
		Lookup tables for packet commands
		Linkage to existing BBS programs
		A DOS shell function
		And ideas from contributors

	Inputs, recommendations, critiques, wish lists and bug reports
	are requested.  I have purposely not released the source code, 
	as it is still in development.  If there is enough interest, 
	I will consider releasing the source in the public domain so 
	that the program may benefit from programmers more proficient 
	and clever than the writer.

			Don Wilke, N3HGQ
			4228 Mount Carmel Road
			Upperco, MD 21155
			(301) 374-2735
			or @KA3QAC packet BBS (145.03)