Controller Program for the

                                 Icom IC-735

                               Copyright 1988
                                     by
                               Dick Roux N1AED



            IC735.EXE is a program for the IBM & compatibles that will
         allow you to control an Icom IC-735 that is equipped with the
         CT-17 Communications Interface.

            It allows you to program most front panel functions and
         gives you the ability to store up to 480 frequencies that can
         be called up with one keystroke.  Also, the program has a
         built-in dumb terminal for controlling a phone modem or a
         Terminal Node Controller (TNC).

            Start out by making a copy of the master disk and use this
         as your working disk. Do NOT use the master disk as your
         working disk. After a good copy is made, store it away in the
         event that you damage your working copy.

            Once your working copy is made, just log onto the drive where
         the programs are stored and type IC735. You will then get the
         welcome prompt. If you have a fixed disk just copy all the files
         from the master disk to the desired subdirectory on your hard
         drive.

            After hitting the enter key from the welcome you will get the
         main menu. If your transceiver is connected and properly inter-
         faced to the computer, you will get a status bar on the bottom
         of the screen as to what frequency and mode the selected VFO is
         in.

         FREQUENCY SELECTION:
            Selecting "F" from the main menu will prompt you as to what
         frequency you want. Valid frequency is from 100 Khz - 29999.99
         Khz.

         MODE:
            Selecting "M" will prompt you with a menu of selectable modes,
         USB, LSB, AM, CW, RTTY, & FM.

         VFO STATUS REQUEST:
            Hitting "R" will initiate a status request to the transceiver.
         This is useful if you make any manual changes to the IC-735 and
         you wish to update the computer display.

         STATION DIRECTORY:
            Selecting "T" will bring you to the Station Directory where you
         are able to store and call up to 480 frequencies. (E)dit allows you
         to add or change directory entries, (L)oad allows you to load
         any memory in the transceiver with data contained in any of the dir-
         ectory listings. (B)lock load allows you to load all 12 memories of
         the transceiver with any continuous 12 directory listings. (S)can
         allows you to sequentially scan all the active listings in the dir-
         ectory.

         VFO SELECT:
            Selecting a "V" will prompt you to VFO "A" or "B".

         SELECT MEMORY:
            Selecting "S" will prompt you as to what memory you want to
         select, 1 - 12.

         WRITE VFO >MEMORY:
            Selecting a "W" will write the VFO's frequency and mode into
         the selected memory.

         LOAD MEMORY:
            Selecting "L" will allow you to directly load any of the 12 mem-
         mories with the desired frequency and mode.

         MEMORY UP - DOWN:
            When in memory mode, selecting "U" or "D" will step upwards or
         downwards in the transceiver's memories.

         WRITE MEMORY >VFO:
            Selecting "I" will write the currently selected memory into the
         currently selected VFO.

                                   STATUS

            When the program is started, status checking is ON, meaning that
         whenever any commands are sent to the transceiver, a STATUS REQUEST
         is sent to the radio to register the updated status. While this is a
         nice touch, at 1200 BAUD this noticeably slows down program
         operation.  Therefore, the means for disabling status checking has
         been implemented. Selecting a "#" disables status checking and a "&"
         enables it. With status disabled, your able to more rapidly make a
         large number of changes without having to constantly wait for updated
         status.

                                 DUMB TERMINAL

            Also, there is a Dumb Terminal function that can be utilized to
         control a Terminal Node Controller (TNC) or a telephone modem at
         1200 Baud. The Dumb Terminal portion of the program can be assigned
         the same or a different COM PORT than the controller portion of the
         program (via the CONFIGURE PROGRAM function from the main menu).

         EXAMPLE:
            You can set up the controller portion of the program to COM 1 and
         connect the CT-17 to COM 1 and control the IC735 then connect a TNC
         to COM 2 for packet communications.

         EXAMPLE:
            Both the Dumb Terminal and the controller can be set to the same
         COM port (1 or 2) and the IC735 could be remotely controlled via a
         1200 baud telephone modem at the computer end and the IC735, null
         modem adapter, and another 1200 baud telephone modem at the remote
         end. The Dumb Terminal could then facilitate the dialing and hangup
         commands needed to control the telephone modem to establish contact.

                               CONFIGURE PROGRAM

            Selecting "O" from the main menu will allow you to configure the
         program to your needs. You will be prompted as to your choice of
         monitor, COM PORT assignment, if you want to disable the keyboard
         sounds and what SCAN DELAY you would like. The SCAN DELAY is the
         time that the transceiver will stay on a scanned frequency while
         in the SCAN mode (STATION DIRECTORY menu). Valid time is from .5
         to 10 seconds.
 

            The program is very functional and could have had alot of
         "bells and whistles" added which may be included in future
         releases if acceptance to the Program is widespread.
            Please feel free to contact me if you have any comments
         and/or suggestions on the Program.