SB-820

TR-7625 Final Module Relpacement                        3-20-80


When replacing the output hybrid with a "Red" Mitsubishi logo, and
additional 47pF cap must be installed between teh M57712H output terminal
and the RFO wrap post.

Install the M57712H with white silicone heatsink compound.  Install a 47pF
as shown between the hybird output and the RFO terminal.  Spread L21 as
necessary for at least 30W output at approximately 5.5 A total current
consumption.

Note:  Hybirds not having a red mitsubishi logo do not require the
additional cap or adjustment.


JEB/yn
(c) 32080TKC