ÜÜÜÜÜÜÜÜ                ÜÜ
                       ÛÛÛÛÛÛÛÛ              ÜÛß
                       ÛÛÛÛÛÛÛÛ            ÜÛß
                       ÛÛÛÛÛÛÛÛ          ÜÛß
                       ÛÛÛÛÛÛÛÛ        ÜÛß
                       ÛÛÛÛÛÛÛÛ      ÜÛß
                       ÛÛÛÛÛÛÛÛ    ÜÛß
                       ÛÛÛÛÛÛÛÛ  ÜÛß
                       ÛÛÛÛÛÛÛÛÛÛÛß     ÜÜÜÜÜÜÜÜÜ
                       ÛÛÛÛÛÛÛÛÛÛÛ       4  4  0
                       ÛÛÛÛÛÛÛÛ ÛÛÜ     ßßßßßßßßß
                       ÛÛÛÛÛÛÛÛ  ÛÛÜ
                       ÛÛÛÛÛÛÛÛ   ÛÛÛ
                       ÛÛÛÛÛÛÛÛ    ÛÛÛÜ
                       ÛÛÛÛÛÛÛÛ     ÛÛÛÛÜ
                       ÛÛÛÛÛÛÛÛ      ÛÛÛÛÛÜ
                       ÛÛÛÛÛÛÛÛ       ÛÛÛÛÛÛÜ
                       ÛÛÛÛÛÛÛÛ        ÛÛÛÛÛÛÛÜ
                       ÛÛÛÛÛÛÛÛ  ÜÜÜÜÜÜÜÛÛÛÛÛÛÛÛÜÜÜÜÜÜ
                       ÛÛÛÛÛÛÛÛ   S  p  o  i  l  e  r
                       ßßßßßßßß  ßßßßßßßßßßßßßßßßßßßßß

                        THE 440 SPOILER: VERSION 1.01
                    PRELIMINARY TECHNICAL-REFERENCE MANUAL


     The 440  Spoiler lets  you use  and enjoy the full operating power of the
Kenwood TS-440S  amateur radio  transceiver.   The Spoiler is fully functional
software that  makes your transceiver superior to any other transceiver on the
market in speed, convenience, and versatility of operating.

     The 440  Spoiler software is provided to you through shareware marketing,
a method  which gives  you the  finest software  available at a minimum price.
You are  invited to  use the  440 Spoiler for a period of up to one month.  If
you decide  to use  the 440  Spoiler thereafter, you must obtain a license for
the software  by registering  it with  the QSO2000  Project, 5518 12th Street,
Lubbock, TX,  79416 for  a nominal fee of $39.  A convenient registration form
is included at on the last page of this manual.

     Your registering  your software  provides you  with significant benefits.
You receive  a diskette copy of the most-recent revision of the Spoiler.  This
version of  the software  will contain latest enhancements, latest maintenance
revisions,  and   no  shareware   notices.     In  addition,   you  receive  a
professionally written,  printed, and  bound copy of the 440 Spoiler Technical
Reference Manual.   You  also receive  technical support and assistance as you
require it in your use of the 440 Spoiler.

     Your registration  is also  your way  of ensuring  continued improvement,
development, and  maintenance of  the 440  Spoiler throughout  the long useful
lifetime of you Kenwood TS-440S transceiver.

     The last section of this documentation file provides detailed information
about registration  of the  440 Spoiler  as well  as  form  for  your  use  in
registering your copy.

                                 INTRODUCTION

     The Kenwood  TS-440S is  one of  the  most  sophisticated  high-frequency
transceivers available  for amateur-radio  use.  It contains 100 memories (110
counting the  separate transmit  and receive  memories for the upper 10 memory
channels). It  contains a  general-coverage receiver  and  transmitter  and  a
unique receive  and transmit increment-tuning system.  The operating potential
of the transceiver is astounding.

     Because of  the operating  power of  the transceiver,  however, operation
from the  front panel  is of necessity, complex.  Storing, altering, and using
all of  the information  into TS-440S  memories is  time-consuming  and  often
confusing.

     The TS-440S keypads present operating problems.  It is easy to forget the
sequence of keystrokes required by the keypads on the front panel if you don't
use them very often.  Also, infrequent use of the keypads leads to key bounce;
you can  press them  many times  before you condition them to switch only once
for each  time you press them.  Additionally, all storage and control from the
front panel  is performed  on the  current memory  or VFO: you can't prepare a
memory or  a vfo for switching to it while you are operating on another memory
or VFO.

     The TS-440S  display also presents operating problems.  You can't see the
frequency and mode of a memory or VFO unless you select it and therefore cease
to receive  or transmit  on your  current frequency  and mode.   Moreover, you
can't see  your transmit frequency at the same time your receiving, no can you
see your  receive frequency  while you  are transmitting.   If  you are  using
increment tuning  on either  transmit or  receive, the  display shows  you the
result of  your using  it but  it doesn't show you the actual frequency of the
vfo or memory that is currently selected.

     The 440  Spoiler overcomes  the problems  presented by  the  front  panel
switches and  the display.  Your MSDOS computer keyboard provides considerably
more convenient and legible control of the transceiver.  With a minimal number
of keystrokes,  you can  select any  of the  operating parameters  (frequency,
mode, etc.)  stored in  the  TS-440S,  and  you  can  conveniently  alter  the
operating parameters stored in the transceiver.

     Additionally, the  Spoiler displays  all  operating  frequencies,  modes,
frequency splits,  tuning increments,  and other  operating information on the
screen of your computer.  Half of the parameter memories stored in the TS-440S
are displayed  on the  screen at  all times;  you can toggle between the lower
half and  the upper  half at  any time  with a  single keystroke.  The Spoiler
makes information  entry and display extremely simple, convenient, and fast as
prompts on the screen direct you through a minimum of key strokes.

     The display always shows the current operating conditions of the TS-440S,
regardless of  whether you  have used the front panel or the computer keyboard
to change  the conditions.   If  you change  frequency, mode, split, increment
tuning, or  memories from  the front panel, the Spoiler updates its display to
show the remotely entered data.

     The 440 Spoiler contains a complete memory-management system that enables
you to  store up  to tens  of thousands  of frequency  and  mode  memories  on
computer disk.   Stored  in banks  of 100 memories, the memories may be loaded
into your TS-440S with a few key strokes.  You may customize individual memory
banks for  different modes  of operation,  for  different  bands,  for  DX  or
traffic-net operation, for monitoring broadcasts, citizens band transmissions,
or whatever your specialized interests include.  Moreover, the Spoiler manages
VFOs and  memories in a way that does not disturb your current operation.  You
can enter  new frequencies  and modes into unselected memories or VFOs without
missing a word on a net or a calling frequency you are currently monitoring.

     Simplicity of  operation is  the most important design feature of the 440
spoiler.   From your screen, you see prompts to lead you through any operation
you care  to perform.   If you want to change the operating mode of a vfo or a
memory, you  press  the  MODE  function  key;  you  press  SOURCE,  FREQUENCY,
INCREMENT  TUNING,   and  MEMORY   MANAGEMENT  keys   with  similar   ease  to
instantaneously control every feature of your transceiver.

     The 440  Spoiler also contains provisions for accessing a log-maintenance
program and  a digital-controller  program while  you maintain the 440 Spoiler
resident in memory for quick recall.

                            HARDWARE REQUIREMENTS

     The 440 Spoiler requires an MSDOS or PCDOS computer with at least 256K of
memory, one  diskette drive,  and one  serial (COM)  port.  Performance of the
program is  improved, of  course, with  your running  it from hard disk rather
than floppy.  The faster your CPU speed the more responsive the program.

     Your TS-440S  must be  equipped for serial (RS-232C) communications.  You
must have  the two  interface chips  such as  the ones  Kenwood sells as a kit
designated as  the IC-10  as well  as a  TTL/RS-232C level  converter such  as
Kenwood sells  as the IF-232C adapter.  It is not necessary for you to use the
parts that  Kenwood markets.   The  necessary interface chips are common ones,
and if  you are experienced in digital-circuit design you might build your own
level converter.   Kenwood prices are high, but Kenwood is a convenient source
for ready-made components that are guaranteed to work with your transceiver.

                                  OPERATION

     The opening  screen of  unregistered copies  of the  Spoiler  contains  a
reminder that  the software  is a  shareware  package  that  depends  on  user
registration to provide for its initial and continued development.  The screen
is displayed  for 5  seconds: after  the initial  period, you can bring up the
operating screen  by pressing  any key.  Registered copies, of course, contain
no waiting period.

     Registered copies  of the  Spoiler display an opening screen for only the
length of  time it takes you to press a key.  The opening screen also contains
no shareware notice.

     The operating  screen shows  every parameter that enters into transceiver
operation, regardless  of whether  changes in  operation occur  from the front
panel or  from the  computer keyboard.   It  also shows  commands  which  make
computer-keyboard control of the TS-440S incredibly easy and fast.

                             THE OPERATING SCREEN

     The operating  screen consists  of four  display areas  for each  of  the
following:  (1)  current  operating  sources,  (2)  command  options,  (3)  55
memories, and  (4) commands.  Figure 1 shows a typical operating screen (which
has  been   shortened  horizontally   to  fit   within  the  margins  of  this
documentation file.   Current  operating sources  are shown  in the box in the
upper left.   Command  options are shown in the box which contains the program
logo when  no command  has been issued.  Transceiver memory contents are shown
in the  large, J-shaped  box to  the right and bottom of the screen.  Commands
are shown on the bottom line.



ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍËÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ» ÉÍÍÍÍÍÍÍÍÍ¸ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
º      RECEIVE       ºTR 21.005.00 CW  61º º11f  7.00³³ CW ³33f  2.500.00 AM º
º   21.005.00 CW     ºÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄº º12f  7.01³³ CW ³34f  5.000.00 AM º
º         61         ºTR 27.285.00 AM  VAº º13f  7.01³³ CW ³35f 10.000.00 AM º
ÌÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¹TR  3.921.44 LSB VBº º14f  7.02³³ CW ³36f 15.000.00 AM º
º      TRANSMIT      ºÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄº º15f  7.02³³ CW ³37f 20.000.00 AM º
º   21.005.00 CW     ºNo Increment..-0.05º º16f  7.03³³ CW ³38f 14.005.00 CW º
º         61         º                   º º17f  7.04³³ CW ³39f 14.010.00 CW º
ÌÍÍÍÍÍÍÍÍÍÍÍÍÍËÍÍÍÍÍÍÊÍÍÍÍÍËÍÍÍÍÍÍÍÍÍÍÍÍÍ¹ º18f  7.06³³ CW ³40f 14.015.00 CW º
ºTime:14:30:11ºZEROS1.MRY  ºDate:01-01-90º º19f  7.07³³ CW ³41f 14.020.00 CW º
ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÊÍÍÍÍÍÍÍÍÍÍÍÍÊÍÍÍÍÍÍÍÍÍÍÍÍÍ¼ º20f  7.15Z³ LSB³42f 14.030.00 CW º
ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼21f  7.16³³ LSB³43f 14.050.00 CW º
º     ÜÜÜÜ       Ü      ºº00f  3.505.00 CW ³22f  7.18³Z LSB³44f 14.070.00 CW º
º     ÛÛÛÛ     Üß       ºº01f  3.515.00 CW ³23f  7.19³³ LSB³45f 14.151.00 USBº
º     ÛÛÛÛ   Üß         ºº02f  3.525.00 CW ³24f  7.20³³ LSB³46f 14.155.00 USBº
º     ÛÛÛÛ Üß ÜÜÜÜÜ     ºº03f  3.780.00 LSB³25f  7.21³³ LSB³47f 14.160.00 USBº
º     ÛÛÛÛÛÛ  TS440     ºº04f  3.790.00 LSB³26f  7.22³³ LSB³48f 14.175.00 USBº
º     ÛÛÛÛ ÛÜ ßßßßß     ºº05f  3.905.00 LSB³27f  7.23³³ LSB³49f 14.190.00 USBº
º     ÛÛÛÛ  ÛÜ          ºº06f  3.910.00 LSB³28f  7.23³³ LSB³50f 14.205.00 USBº
º     ÛÛÛÛ   ÛÛÜ        ºº07f  3.928.00 LSB³29f  7.24³³ LSB³51f 14.220.00 USBº
º     ÛÛÛÛ ÜÜÜÛÛÛÜÜÜ    ºº08f  3.933.00 LSB³30f  7.24³³ LSB³52f 14.240.00 USBº
º     ÛÛÛÛ  Spoiler     ºº09f  3.935.00 LSB³31f  7.24³³ LSB³53f 14.250.00 USBº
º     ßßßß ßßßßßßßßß    ºº10f  3.940.00 LSB³32f  7.29³³ LSB³54f 14.270.00 USBº
ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
1SLCT S 2FREQ S 3MODE S 4INCR T 5MOVE S 6FILE M 7EDIT M 8CTRL P 9LOG   10QUIT

                           Figure 1.- Operating screen

CURRENT-SOURCES DISPLAY BOX

     The display  box in  the upper  left of  the  operating  screen  displays
current sources:  the two  VFOs, the  memory selected  by the TS-440S, and the
increment tuning.   This box shows every detail about the current operation of
the transceiver.  An example of the current-sources box is shown in figure 2.

                  ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍËÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
                  º      RECEIVE       ºTR 21.005.00 CW  61º
                  º   21.005.00 CW     ºÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄº
                  º         61         ºTR 27.285.00 AM  VAº
                  ÌÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¹TR  3.921.44 LSB VBº
                  º      TRANSMIT      ºÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄº
                  º   21.005.00 CW     ºNo Increment..-0.05º
                  º         61         º                   º
                  ÌÍÍÍÍÍÍÍÍÍÍÍÍÍËÍÍÍÍÍÍÊÍÍÍÍÍËÍÍÍÍÍÍÍÍÍÍÍÍÍ¹
                  ºTime:14:30:11ºZEROS1.MRY  ºDate:01-01-90º
                  ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÊÍÍÍÍÍÍÍÍÍÍÍÍÊÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

                      Figure 2.- Current-sources display

     The box  contains areas  for receiving  and transmitting  frequency,  for
detailed source information, and for current Spoiler operation.

Receive and Transmit Areas

     Overall transceiver  operation is  summarized in the Receive and Transmit
areas to  the left  of the  box.   These areas show, irrespective of operating
components that  go into  transceiver operation,  the  current  receiving  and
transmitting frequencies,  and modes.   The  frequency and  mode that  you are
hearing on  the transceiver,  as well  as  the  frequency  and  mode  you  are
transmitting on when your press your microphone button, tap a key, or activate

your digital  controller, are  displayed to an accuracy of 10 KHz in these two
areas.

      Receive  and Transmit  areas show  the combined effects of VFO or memory
frequency selection,  split-frequency sources,  and currently active increment
tuning.   The displayed frequencies are the actual frequencies of transmission
and reception.   The  receiving frequency  accounts for  any receive increment
tuning (RIT),  and the  transmit frequency accounts for any transmit increment
tuning (XIT).

Source-Detail Area

     To the  right of  the Receive  and Transmit  areas is  an area containing
detailed information  about the components of the current sources: frequencies
and modes  of the  two VFOs  and  the  selected  memory,  the  split-frequency
operating status, and the status of increment tuning.

     In the source-detail box to the right, the upper partition identifies the
currently active source(s) and shows frequency and mode.  The middle partition
shows the  sources "on reserve" for your use at the press of the TS-440S VFO/M
and  A/B  switches.    The  lower  partition  shows  current  increment-tuning
frequency and status

     Unlike the receive and transmit areas to the left or the TS-440S display,
the detail-area  source display  does not  reflect increment  turning.  If you
turn on increment tuning for transmit or receive, for example, the area to the
left will  show the  result of  the increment tuning, but the detail area will
continue to  show the  exact frequency  of the  source without  the effect  by
increment tuning.   The  last two  characters of  the line identify the source
with VA  for VFO  A, VB  for VFO  B, and  a number  between 00  and 99 for the
selected memory.   The  first two  characters of  the line identifies the role
that the source contributes to split-frequency operation.

     The upper  partition of the detail-source display may contain one line to
indicate a  non-split source operating on both transmit and receive (therefore
prefaced by  TR), as  it does  in figure 2, or it may contain two lines, as in
the display of split-VFO operation shown in figure 3.

                  ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍËÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
                  º      RECEIVE       ºRX  7.209.04 CW  VAº
                  º    7.209.04 CW     ºTX  3.959.23 LSB VBº
                  º         VA         ºÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄº
                  ÌÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¹TR  3.525.00 CW  02º
                  º      TRANSMIT      ºÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄº
                  º    3.959.23 LSB    ºNo Increment..-0.03º
                  º         VB         º                   º
                  ÌÍÍÍÍÍÍÍÍÍÍÍÍÍËÍÍÍÍÍÍÊÍÍÍÍÍËÍÍÍÍÍÍÍÍÍÍÍÍÍ¹
                  ºTime:14:43:54ºGENPUR1.MRY ºDate:01-07-90º
                  ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÊÍÍÍÍÍÍÍÍÍÍÍÍÊÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

                         Figure 3.- Split VFO display

     During split-frequency operation, there are always two lines in the upper
partition.   The receiving-frequency  source is  always identified  in the top
line with  the designation RX, and the transmitting-frequency source is always
identified in the second line with the designation TX.  Split-frequency memory
operation is displayed , as shown in figure 4

                  ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍËÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
                  º      RECEIVE       ºRX  7.154.00 LSB 99º
                  º    7.154.00 LSB    ºTX  7.131.02 LSB 99º
                  º         99         ºÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄº
                  ÌÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¹RX  7.209.04 CW  VAº
                  º      TRANSMIT      ºTX  3.959.23 LSB VBº
                  º    7.131.02 LSB    ºÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄº
                  º         99         ºNo Increment..-0.03º
                  ÌÍÍÍÍÍÍÍÍÍÍÍÍÍËÍÍÍÍÍÍÊÍÍÍÍÍËÍÍÍÍÍÍÍÍÍÍÍÍÍ¹
                  ºTime:14:47:11ºDEFAULT.MRY ºDate:01-07-90º
                  ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÊÍÍÍÍÍÍÍÍÍÍÍÍÊÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

                       Figure 4.- Split memory display

     When the  upper area  contains two lines, the source is split so that the
top line  shows the  receiving-source frequency  and mode  and the bottom line
shows the transmitting frequency and mode.  With a VFO selected, the frequency
and mode  of either  VFO A  or VFO B appears in the top line prefaced by an RX
designation indicating  a receiving  source.   The frequency  and mode  of the
transmitting VFO appears in the lower line prefaced by TX.

     The middle partition of the detailed display area shows alternate sources
that are  currently selected:  these are  the sources  that  you  can  use  by
toggling between VFO A and VFO B or between VFO and memory.

     The lower  partition shows  the frequency and status of increment tuning.
The frequency  is shown  to the  right of the line, and the status is shown to
the left.   Status  may be  No Increment,  RX  Increment  (receive  only),  TX
Increment (transmit only), or TR Increment (both transmit and receive).

     You should notice very carefully that if you toggle between VFO A and VFO
B any  increment tuning that is in effect remains in effect, but if you toggle
between either  VFO and  memory any  increment turning loses its effect.  This
peculiarity is simply a design feature of the Kenwood TS-440S.

Current Spoiler Operation

     The current  time, the  active file  of memories stored in your computer,
and the  current date  are displayed  in the  area across  the bottom  of  the
current-sources box.

MEMORY DISPLAY

     The contents  of TS-440S  memory sources are displayed in the largest box
on the screen.  Figure 5 shows a full-width memory-display box.

                             ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
                             º11f  7.006.12  CW³33f  7.000.00 LSBº
                             º12f  2.500.00  AM³34f  7.154.00 LSBº
                             º13f  0.000.00    ³35f  7.131.02 LSBº
                             º14f  0.000.00    ³36f  0.000.00    º
                             º15f  0.000.00    ³37f  0.000.00    º
                             º16f  0.000.00    ³38f  0.000.00    º
                             º17f  7.220.00 LSB³39f  0.000.00    º
                             º18f  7.213.00 LSB³40f  1.590.00 LSBº
                             º19f  7.249.00 USB³41f  1.320.00 LSBº
                             º20f  3.933.00 USB³42f  0.000.00    º
           ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼21f  0.000.00    ³43f 28.000.00 LSBº
           º00f  3.933.00 LSB³22f  7.290.00 LSB³44f  3.395.00 LSBº
           º01f  3.935.00 LSB³23f  1.590.50 AM ³45f  0.000.00    º
           º02f  7.290.00 USB³24f 14.305.00 USB³46f  0.000.00    º
           º03f 14.334.00 USB³25f  1.590.50 AM ³47f  0.000.00    º
           º04f 28.454.00 USB³26f  1.590.50 AM ³48f  0.000.00    º
           º05f  7.100.00  CW³27f  1.590.50 AM ³49f  0.000.00    º
           º06f 28.000.00 USB³28f  0.000.00    ³50f 28.000.00 LSBº
           º07f  7.250.00 LSB³29f  0.000.00    ³51f  0.000.00    º
           º08f 21.000.00 LSB³30f  3.900.00 LSB³52f  0.000.00    º
           º09f 28.454.00 USB³31f  0.000.00    ³53f  0.000.00    º
           º10f  7.100.00  AM³32f  0.000.00    ³54f  0.000.00    º
           ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

                        Figure 5.- Memory display box

     The box,  at any  particular time, shows the frequencies and modes stored
in half  of the  transceiver's 100  memories.   When the  Spoiler is initially
loaded, the  box shows  the contents of memories 0 through 54.  When you press
F9 (function key F9), the upper 55 memories are displayed.

     Within the  memory box,  memories 0  through 89  are  identified  by  the
designations 00f through 89f.  The lower 90 memory channels of the TS-440S are
capable of  operating on  only a  single, non-split  frequency and  mode.  The
upper 10  memory channels  consist of  two memories  apiece:  one  memory  for
receive and  one memory  for transmit.    Beginning  with  memory  90,  memory
channels are,  therefore, identified  by a  channel number  with either an "r"
(receive) or  a "t" (transmit) suffix.  Channel 97 is therefore represented in
the memory display box by both 97r and 97t.

SPOILER COMMAND LINE

     The bottom  line of  the Spoiler  display is  a prompt for command entry.
Figure 6 shows this line.

------------------------------------------------------------------------------
1SELECT 2FREQ   3MODE   4INCR   5COPY   6FILES  7LOG    8CNTL   9M TOG  10QUIT
------------------------------------------------------------------------------

                       Figure 6.- Spoiler command line

                               SPOILER COMMANDS

     The Kenwood  TS-440S is  a completely self-contained transceiver, and the
front panel,  although sometimes  cumbersomely, provides  ways to  control its
operation.   Your MSDOS computer provides you with an alternative to the front
panel.   The Spoiler  display provides  current information  about transceiver
operating parameters,  regardless of  whether you change the parameters at the
front panel or at the keyboard.

     Spoiler commands  are represented  by numbers  from 1  through 10.    The
numbers correspond  to function  keys on  MSDOS computers.  Command number 10,
labeled QUIT  on the  command line,  causes the Spoiler to cease operation and
control of the computer to return to the disk operating system (DOS).

     The commands  are listed  on the  command  line  by  abbreviation.    The
abbreviations correspond to the brief descriptions shown in table 1.

 Source selection.........................Select a VFO, VFO split, or a memory
 Frequency selection.................Change the frequency of a VFO or a memory
 Mode selection...........................Change the mode of a VFO or a memory
 Increment Tuning........Add frequency increment to transmit of receive source
 Copy sources.......................Copy or exchange between VFOs and memories
 Memory management.......................Use computer files for memory storage
 Logging program..........Run a logging program while the Spoiler is in memory
 Controller program....Run a controller program while the Spoiler is in memory
 Memory display toggle.........Toggle display between memories 0-54 and 55-99t
 Quit................................Quite Spoiler operation and return to DOS

               TABLE 1.- Brief descriptions of Spoiler commands

     When you  press a  function key  to invoke  a spoiler command, you open a
window behind  the Spoiler  logo in the box at the lower left of the operating
screen.   The window  prompts you  for information that you need to provide to
complete any control operation for the transceiver.

     The following  sections of  this documentation  file describe each of the
Spoiler commands in detail.  Each command option is also described.

SOURCE SELECTION

     The source-select  command invoked by F1 determines the primary frequency
and mode  source for  TS-440S reception  and transmission.   The frequency and
mode of  your reception and transmission are always from a certain source, the
VFOs or  the memories,  as you  determine by  issuing a source-select command.
Figure 7  shows the  options you are presented with in the command-options box
for the source-select command.

                          ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
                          º   Source Selection    º
                          º VFO A...............A º
                          º VFO B...............B º
                          º Memory..............M º
                          º Split...............S º
                          º Mem Num............## º
                          º Quit................Q º
                          º                       º
                          º                       º
                          º                       º
                          º                       º
                          ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

                   Figure 7.- Source-select command options

     As figure  7 shows, you may choose VFO A, VFO B, or the current memory to
be  your   current  reception   and  transmission  source.    You  may  choose
transmission and reception to be split, with one VFO being used on receive and
the other being used on transmit.  Additionally, you may also choose any other
memory channel  in the  transceiver to  be  your  reception  and  transmission
source, with  channels 0 through 89 providing for only non-split operation and
channels 90 through 99 providing for split transmit/receive operation.

     The option  box is a simple reflection of this powerful command.  You may
press A, B, or M to select the VFO A, VFO B, or current memory.  You may enter
the number  of any  other memory to cause it to become both the current memory
and the  selected source.   And you may toggle the VFOs between split and non-
split operation.

     Your pressing  a single  key (A,  B, or  M) causes  VFO A,  VFO B, or the
current memory  to become  the current source.  If the source is a VFO and the
VFOs were  last used  in split-source  operation, your  reselecting them  will
bring them  up for split operation (regardless of which of them you select for
your primary  (receive) VFO.  If the source is a memory, memories 0 through 89
always provide  you with  a non-split source, while memories 90 through 99 can

provide you  with either  split frequencies and modes or non-split frequencies
and modes, depending on what you have placed in them before.

     Your pressing  the S  key while  either VFO  is selected  toggles between
split and  non-split operation.  Pressing the S key while a memory is selected
has no effect.

     For the  VFOs, the  status of  split-frequency operation remains constant
until your  change it.  If you switch from a VFO to a memory source, while the
VFOs are  linked for  split-frequency operation,  you'll find  the VFOs  still
linked when you switch back from memory to VFO operation.

     You do  have an  alternative to  pressing alphabetic  keys to  change the
current sources  for your  transceiver.   While the  source-selection  box  is
displayed, the  command letters  are displayed  across the  last line  of  the
screen.   Pressing a  function key accomplishes the same result as pressing an
alphabetic key.   Pressing  F2, for  example, selects  VFO B  as your  current
source.

     Figure 8 shows the last-line display of source-selection command options.

------------------------------------------------------------------------------
 1 A     2 B     3 M     4 S     5       6       7       8       9       10 Q
------------------------------------------------------------------------------

                 Figure 8.- Source-selection command options

     Response to  your pressing the A, B, M, Q, or function keys is immediate.
The Spoiler  does not wait for you to press enter.  If you mistakenly enter an
unrecognized command  character, the  Spoiler will prompt you again for a good
command option.   If  you want to abort the source-selection operation, simply
press either Q or the enter key at the prompt.

FREQUENCY SELECTION

     You have  two methods  of frequency  selection available  to you.    Your
primary method  is using a frequency-selection command to change the frequency
of any  source.  An alternate method permits you to tune your primary VFO from
the keyboard.

Frequency-Selection Command

     The frequency-selection  command invoked by F2 provides you with the same
basic options  that you have with current-source selection.  You can choose to
enter a  frequency for  VFO A, VFO B, the current memory, or any memory stored
in the transceiver.

     Figure 9  shows the options you are presented with in the command-options
box for the frequency-selection command.

                          ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
                          º  Frequency Selection  º
                          º VFO A...............A º
                          º VFO B...............B º
                          º Memory..............M º
                          º Mem Num............## º
                          º Quit................Q º
                          º           _           º
                          º                       º
                          º                       º
                          º                       º
                          º                       º
                          ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

                Figure 9.- Frequency-selection source options

     A powerful  feature of the Spoiler is that your entry of information into
an unselected  source does  not require  you to  select the  source before you
enter it.   If  you choose  to enter a new frequency into an unselected VFO or
memory, you do so without interrupting your listening to and transmitting from
your currently selected source.  If you are operating with VFO A or VFO B, for
example, you  can change  the contents  of all  memories and the alternate VFO
without missing  a single  word of  a net  or a  single baud  of  your  CW  DX
monitoring.

     You may  select the source sources with the function keys as well as with
the alphabetic  keys.   Pressing F3,  as figure  9 shows,  selects the current
memory for frequency entry, just as pressing M does.

     After you  have selected the source that you want to change the frequency
of, the  command-option box  prompts you  for the  new frequency,  as shown in
figure 10.   The  prompt verifies  the source  you have  selected (VFO  A, for
example, in  figure 10).   For  frequencies below  10 MHz,  you may  enter the
frequency in  either KiloHertz  or MegaHertz.   If you want to enter 7,001,010
Hz, you may enter either 700101 or 7.00101.  In addition, numeric precision is
assumed, so that your entering ????????

                          ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
                          º  Frequency Selection  º
                          º VFO A...............A º
                          º VFO B...............B º
                          º Memory..............M º
                          º Mem Num............## º
                          º Quit................Q º
                          º           A           º
                          º  TR A: _              º
                          º                       º
                          º                       º
                          º                       º
                          ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

                    Figure 10.- Frequency-selection prompt

     If you  want to  abort the  frequency-selection command  at  the  prompt,
simply press enter.

     If you  select a  memory channel  capable of split-source operation (from
channels 90  through 99),  you will  be prompted to enter frequencies for both
sources, as shown in figure 11.

                          ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
                          º  Frequency Selection  º
                          º VFO A...............A º
                          º VFO B...............B º
                          º Memory..............M º
                          º Mem Num............## º
                          º Quit................Q º
                          º           A           º
                          º  RX 93: _             º
                          º  TX 93: _             º
                          º                       º
                          º                       º
                          ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

           Figure 11.- Frequency-selection prompt for split source

     The prompt  for frequency of the receive memory appears first.  If you do
not want  to change the receive memory, simply press the enter key to bring up
the prompt  for frequency  of the  transmit memory.   Similarly,  if you  have
entered a frequency in receive memory and do not wish to enter a new frequency
in transmit memory, simply press the enter key at the TX prompt.  Pressing the
enter key at both prompts aborts the frequency-selection command.

     A special  circumstance occurs  when a TS-440S memory is completely empty
(with no previous frequency or mode stored in it).

     One of  the characteristic   of  the TS-440S  memory is that it can store
into an  empty memory  neither frequency  nor mode  without storing  the other
parameter.   Because  the  Spoiler  stores  frequency  and  mode  in  separate
operations, the program must store a "boilerplate" mode into a memory whenever
you store  a frequency.   This  mode is LSB.  If you enter a frequency into an
empty memory,  the LSB mode stored simultaneously in memory.  If you want some
other mode  for the  memory, you  can change  it quite  conveniently from  the
keyboard with the mode-selection command invoked by F3.

Tuning from the Keyboard

     You may  tune the  frequency of  your currently  selected VFO by pressing
your UP  and DOWN  arrow keys.   Tuning  is inhibited  while you  are entering
command options

     When you  use the  arrow keys  to tune  your currently  selected VFO, the
resulting change  in frequency  is always  applied  to  your  current  receive
frequency.   If you  have not selected split-frequency operation, it will also
alter your  transmit frequency.  If split-frequency operation is selected, the
transmit frequency remains unchanged.

     If you  want to use keyboard tuning as extended receive increment tuning,
you should  enter the  same frequency  into both  VFOs and select split-source
operation.   Your transmit frequency will remain unchanged while you vary your
receive frequency.

MODE SELECTION

     The mode-selection command invoked by F3 provides convenient selection of
one of  the six  operating modes  for either  VFO, the  current memory, or any
unselected memory.   All  of these  sources can  receive and  transmit in  the
following modes.

                         Lower sideband (LSB)
                         Upper sideband (USB)
                         Continuous wave (CW)
                         Frequency modulation (FM)
                         Amplitude modulation (AM)
                         Frequency-shift keying (for RTTY)

     To select  a mode  for a  source, you  first select the source within the
command options box, as shown in figure 12.

                          ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
                          º      Select Mode      º
                          º VFO A...............A º
                          º VFO B...............B º
                          º Memory..............M º
                          º Mem Num............## º
                          º Quit................Q º
                          º                       º
                          º                       º
                          º                       º
                          º                       º
                          º                       º
                          ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

                  Figure 12.- Mode-selection source options

     Your selection  is verified  in the mode-selection prompt that appears in
the box, as shown in figure 13.

                          ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
                          º      Select Mode      º
                          º VFO A...............A º
                          º VFO B...............B º
                          º Memory..............M º
                          º Mem Num............## º
                          º Quit................Q º
                          º           86          º
                          º  TR 86 (LUCFAR): _    º
                          º                       º
                          º                       º
                          º                       º
                          ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

                  Figure 13.- Mode-selection source options

     The prompt  for mode  selection shown in figure 12 indicates that you are
selecting the mode for memory channel 86.  If you want to abort the selection,
simply press enter at the prompt.

     If you select from memory channels 90 through 99 as your source, you will
be prompted  for the  mode of  both channels, as shown in figure 14.  Pressing
enter at  the receive-source  prompt leaves  the mode  for the  receive memory
unchanged, and  pressing  enter  at  the  transmit-source  prompt  leaves  the
transmit memory unchanged.  Pressing enter at both prompts aborts the command.

                          ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
                          º      Select Mode      º
                          º VFO A...............A º
                          º VFO B...............B º
                          º Memory..............M º
                          º Mem Num............## º
                          º Quit................Q º
                          º           86          º
                          º  RX 91 (LUCFAR): _    º
                          º  TX 91 (LUCFAR): _    º
                          º                       º
                          º                       º
                          ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

          Figure 14.- Mode-selection source options for split source

     A special  circumstance occurs  when a TS-440S memory is completely empty
(with no previous mode or frequency stored in it).

     Because the Spoiler stores mode and frequency in separate operations, the
program must store a "boilerplate" frequency into an empty memory whenever you
store a  frequency.   This frequency 3.9956 MHz.  You may change the frequency
conveniently with the Frequency Selection command invoked by the F2 key.

INCREMENT TUNING

     You may  use TS-440S  increment tuning  to alter  the receive or transmit
frequency of  your selected  VFOs or  memories.   Increment tuning, because it
affects frequencies  with memories  as a primary source, is more powerful than
keyboard tuning, but it has a more limited range.  You may tune above or below
your primary source frequency by only 1270 Hz (1.27 KHz).

     You may  invoke increment  tuning with  the F4  key, or you may alter the
increment tuning frequency from the keyboard.

The Increment-Tuning Command

     The increment-tuning command, invoked by F4, provides you with options to
apply  a   tuning  increment  to  your  current  receive  frequency,  transmit
frequency, or  both frequencies.   You  may set the increment frequency to any
value between  -1.27 KHz  and 1.27 KHz, or you may clear the increment (set it
to 0).  Figure 15 shows the options box for the increment-tuning command.

                          ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
                          º    Increment Tuning   º
                          º RX Toggle...........R º
                          º TX.Toggle...........T º
                          º Clear...............C º
                          º Freq............ñN.NN º
                          º Quit................Q º
                          º                       º
                          º                       º
                          º                       º
                          º                       º
                          º                       º
                          ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

                 Figure 15.- Increment-tuning command options

     The  results  of  toggling  receive  and  transmit  increment  tuning  is
displayed in  the lowest  partition of  the source-detail  area of the screen.
The possibilities  are No  Increment,  RX  increment,  TX  increment,  and  TR
Increment.

     The source-detail  area of  the screen  shows the  frequency of increment
tuning even  when it  is not applied to receive and transmit frequencies.  You
may alter  this frequency  from the  keyboard or  the front panel at any time,
regardless of  whether it  is being  applied to a current frequency.  You will
notice that when you alter increment frequency from the keyboard, the position
of the  RIT control  on the  TS-440S no  longer corresponds  to the  increment
frequency; when  you next  alter increment  tuning from  the front  panel, the
position of the control will once more correspond to the increment frequency.

     Whenever you  enter an increment frequency at the command-options prompt,
you will notice that the response to your entry is not immediate.  The Spoiler
must, in  fact, send  discrete commands  to the  TS-440S for each 10 Hz of the
increment, so full-range excursions may take up to 5 seconds (depending on the
speed of  your computer).   Clearing  the increment  (setting it to 0) occurs,
however, instantaneously.

Keyboard Increment Tuning

     You may  use the RIGHT and LEFT arrow keys to alter the frequency of your
increment tuning.   Pressing  the keys, however, while a command option box is
displayed, has no effect

COPYING SOURCES

     You may,  by using  the source-copy  command, copy  the contents  of  any
source into  any other  source.  You may also exchange the contents of any two
sources.   This command,  invoked by F5, provides you with a convenient way to
reorganize the frequencies and modes stored in your VFOs and memories.

     The option box for the source-copy command is shown in figure 16.

                          ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
                          º     Copy Sources      º
                          º Copy................C º
                          º Exchange............E º
                          º Quit................Q º
                          º           _           º
                          º                       º
                          º                       º
                          º                       º
                          º                       º
                          º                       º
                          º                       º
                          ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

                   Figure 16.- Source-copy command options

     If  you  select  the  copy  option,  you  are  prompted  for  origin  and
destination sources, as shown in figure 17.

                          ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
                          º     Copy Sources      º
                          º Copy................C º
                          º Exchange............E º
                          º Quit................Q º
                          º           C           º
                          º From (A,B,M,##): A    º
                          º   To (A,B,M,##): _    º
                          º                       º
                          º                       º
                          º                       º
                          º                       º
                          ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

                           Figure 17.- Copy option

     You abort the copy operation if you press enter at either prompt.  If you
select the  Exchange option,  you are  provide similar  prompts, as  shown  in
figure 18.

                          ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
                          º     Copy Sources      º
                          º Copy................C º
                          º Exchange............E º
                          º Quit................Q º
                          º           E           º
                          º Src 1 (A,B,M,##): 32  º
                          º Src 2 (A,B,M,##): _   º
                          º                       º
                          º                       º
                          º                       º
                          º                       º
                          ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

                         Figure 18.- Exchange option

     Both the  copy and  exchange options  handle the contents of single (non-
split) sources.   Your  entering memory number 99 as an origin or destination,
therefore, indicates  the receive  memory of  channel 99.    If  you  want  to
indicate the  transmit memory  of channel 99 you must append a T to the memory
number, as in figure 19.

                          ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
                          º     Copy Sources      º
                          º Copy................C º
                          º Exchange............E º
                          º Quit................Q º
                          º           C           º
                          º From (A,B,M,##): 99T  º
                          º   To (A,B,M,##): _    º
                          º                       º
                          º                       º
                          º                       º
                          º                       º
                          ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

                      Figure 19.- Transmit memory entry

MEMORY FILE MANAGEMENT

     The 100  memory channels  in the  TS-440S provide  for a  great  deal  of
flexibility for most applications, but they may be insufficient for the varied
uses that  a single  transceiver may  be put to.  They are probably sufficient
for  most  people's  use  in  traffic-net  participation,  DX  monitoring,  SW
broadcast monitoring,  CB monitoring,  and  the  like,  but  they  are  likely
insufficient for  combinations of these activities.  Reorganizing and altering
100 memory channels is a tedious task that no one wants to do unnecessarily.

     To help  you with  memory management,  the Spoiler lets you store TS-440S
memories in  computer disk  files.   With the file-management command, invoked
with the  F6 key,  you can  store all 100 memory channels to disk, restore all
100 channels from disk, and clear all 100 channels (setting them off).

     Figure 20 shows the memory-management command option box.

                          ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
                          º   Memory Management   º
                          º List................L º
                          º Open................O º
                          º New.................A º
                          º Clear XCVR..........C º
                          º Quit................Q º
                          º                       º
                          º                       º
                          º                       º
                          º                       º
                          º                       º
                          ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

                    Figure 20.- Memory management options

     The LIST  option displays the names of all TS-440S memory files stored on
disk (in  the current  drive and directory).  On disk, these files always have
an MRY  extension;  the  list,  however  shows  the  file  names  without  the
extension.   The list is displayed in the command-option box.  When the number
of files on disk exceeds the number of lines in the box, the display is paused
for your  reading a partial list until you press any key.  Figure 21 shows the
beginning and end of a list that is too long to fit into the option box.

             ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»  ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
             º     List of Files     º  º     List of Files     º
             º        CBRADIO        º  º        DEFAULT        º
             º        TRAFFIC        º  º        SKEDS          º
             º        CWNETS         º  º End of MRY file list  º
             º        DXFONE         º  º Press a key . . .     º
             º        SWL            º  º                       º
             º        JACKS          º  º                       º
             º        40CONTIN       º  º                       º
             º        75CONTIN       º  º                       º
             º        10SCAN         º  º                       º
             º Press a key . . .     º  º                       º
             ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼  ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

           Figure 21.- Initial and terminal displays of a file list

     The OPEN  option reads  a file from disk into both Spoiler memory and the
memories of  the TS-440S.   The  option box  prompts you  for the name of your
file.  Note that when you initialize the spoiler for your TS-440S it reads the
contents of  the transceiver  memories into  a file called DEFAULT in order to
preserve the  memories for  you.   This prevents you from losing the data that
you already  have stored in the transceiver when you download other files into
the transceiver.

     The file  that is  open is  continuously updated  by the  Spoiler as  you
change the memories of your transceiver.  New memory sources are automatically
saved as  you enter  them.   Also, when you leave the Spoiler to run any other
program, you  will find  when you  again run the spoiler that it automatically
opens the file you last opened before quitting.

     The NEW  option writes  the currently opened file to disk, closes it, and
initializes a  new file with the same contents.  This option provides you with
a convenient  way to  edit the  contents of  an old file without automatically
storing the changes in the file.  The changes are stored only in the new file.

     The CLEAR XCVR option lets you erase all of the memories in your TS-440S.
You may  want to  use this option whenever you wish to begin a new memory file
from scratch or you wish to maintain security about your operating frequencies
while other  operators are using your transceiver.  The option requires you to
enter a new file name; after the transceiver is cleared, new file by that name
containing zeroed  sources is  opened and  maintained on  disk.    Of  course,
thereafter you  may by  using the  OPEN command  load  your  transceiver  with
sources from any other file you have saved.
RUNNING A LOGGING PROGRAM

     The F7  key provides you with a convenient way to run a program that logs
your QSOs  or SWL  observations.   The Spoiler  remains resident in memory, so
that returning to it takes a minimum of time.

     Before you use F7, you should alter the batch file LOG.BAT to include the
name of your logging program.

     When your  logging program  returns you to DOS, enter the EXIT command to
return to the Spoiler.

RUNNING A DIGITAL CONTROLLER PROGRAM

     The F8 key provides you with a convenient way to run a program to control
RTTY, CW,  Packet, and  other such transmission.  The Spoiler remains resident
in memory, so that returning to it takes a minimum of time.

     Before you  use F8,  you should  alter the batch file CLTR.BAT to include
the name of your logging program.

     When your  controller program  returns you to DOS, enter the EXIT command
to return to the Spoiler.

TOGGLING THE MEMORY DISPLAY

     The memories  currently displayed  by the  spoiler  are  toggled  between
numbers 0  through 54  and 55  through 99t  by your  pressing F9.    When  you
initially run  the spoiler,  the lower  numbered memories appear in the memory
display box.  Your pressing F9 displays the higher numbered memories, and your
pressing F9 again displays the lower numbers once more, and so on.

QUITTING THE SPOILER

     Pressing F10  causes you  to exit  the spoiler  program, unload  it  from
memory, and return to DOS control of your computer.

                            USING THE 440 SPOILER

     There is  only one task that you have to undertake to get the 440 Spoiler
working for  your radio-operating  pleasure.   You  must  connect  your  MSDOS
computer to  your TS-440S.  After your transceiver and computer are connected,
you are at your leisure to learn how to use the Spoiler by trial and error, by
reading, or by a most-efficient combination of both activities.

COMPUTER/TRANSCEIVER CONNECTION

     Your simplest  way  to  physically  connect  your  transceiver  and  your
computer is  for you  to obtain an RS-232 interface box and integrated-circuit
chip set marketed by Kenwood.  You will also need a serial cable to connect an
RS-232 output  of your computer to the interface box.  The interface box, chip
set, and cabling will cost you approximately $100 retail.

     Optionally, you  might want  to obtain  a switch so that your RS-232 port
for devices  other than  control of  your TS-440S  at the  flip of  a  switch.
Connectors and  people can  stand only  so much plugging and unplugging, but a
simple switch solves both problems.

     A more-complex,  but much  cheaper, way  is for you to make up the cables
and build  an interface  box.  It is beyond the scope of this manual to detail
how the  equipment should  be constructed, but construction is a simple matter
if you  are familiar with digital technology.  In the do-it-yourself approach,
you can  expect to  save approximately $65 frugal dollars, but you'll probably
spend about 10 hours on construction and testing.

     When you have the box and the cables in hand, plug them up.  Turn on your
transceiver, and run the Spoiler.

     If something  is amiss in the hardware (the transceiver, the cabling, the
interface box, or the computer), the spoiler will tell you upon installation.

INSTALLING THE SPOILER

     The Spoiler performs its installation procedure whenever it does not find
the file SPOILER.DEF in the current directory.

     During installation,  the Spoiler  asks you  for the number of the serial
port that  you have connected your TS-440S interface box to.  The Spoiler then
proceeds  to   run  by  checking  your  communications  between  computer  and
transceiver and  reading all  of the  information stored  in your  transceiver
memories.   The Spoiler  stores the  information in a file called DEFAULT.MRY,
and it opens the file.

     You will  quite likely  alter the  contents of  your  TS-440S  memory  by
exploring the  operation of  the Spoiler.  If you want to save the contents of
your transceiver  memories so  that you can restore them to be exactly as they
were before  you used  the Spoiler,  you'll want  to go  through the following
procedure that follows.

     Issue a  Memory Management command by pressing F6.  At the command-option
prompt, enter  the NEW option by pressing the N key or pressing F3.  You'll be
asked to  enter a  file name  (2 through  8 alphanumeric  charcters  with  the
extension ".MRY"  assumed by  the program) for a new disk file for you to work
with.   The new file that the Spoiler produces will initially have exactly the
same contents  as DEFAULT.MRY,  and your can proceed with your installation in
the security  of knowing  that all  changes you  make to  TS-440S  memory  are
affecting only the transceiver and your new file.

     If you  want to  restore the memories in the TS-440S to exactly what they
were before your exploration, you should perform the following procedure.

     Open the  DEFAULT file  by pressing F6 and choosing the O (or F1) option.
Enter the file name DEFAULT at the prompt.  The Spoiler will load the original
memory values  into your  TS-440.   If you  don't want  to alter  the original
memory contents, you should then immediately quit the Spoiler by pressing F10.
Your transceiver  memories will  be restored to the same as they were when you
first ran the 440 Spoiler.

     You'll want  to follow this procedure each time you work with the Spoiler
therefore if  you want  to save  your  original  memory  information  in  your
transceiver.   When you  feel comfortable  with your operation of the Spoiler,
you will  want to  alter the  memories extremely often, as the Spoiler permits
you to do at will.

COURSING THROUGH THE SPOILER

     You should  initially consider  the Spoiler  a display  window  into  the
operation of  your TS-440S.  All operating parameters are displayed in the box
to the  upper-left of  your screen, and all memory information is presented in
the J-shaped  (largest) box  to the right and bottom of your screen.  When you
change any  operating parameter  (frequency, mode, split, RIT, XIT, source, or
memory) from  the TS-440S  front panel,  the Spoiler  updates its  display  to
reflect the change.

     Later, you  should work  with the  Spoiler commands that are initiated by
your pressing  the function keys listed at the bottom of the Spoiler operating
screen.  Using the Spoiler, you'll find that you have little use for the front
panel of  your TS-440S  except for such "analog" functions as your controlling
volume, passband  tuning, antenna  tuning (if  your transceiver has an antenna
tuner installed, and the like.

     The 440  Spoiler, combined  with the  operating  power  of  the  TS-440S,
provides you  with a  quantum leap in radio communications ability.  You'll be
able to operate many traffic nets simultaneously, and you'll quickly find your
DX tallies  among only  those possessed  by other  operators who are using the
Spoiler.   If you  are looking  for world  news from  international  shortwave
broadcasts during whatever international crisis the future brings, you'll find
it much  faster with  the Spoiler.   If  you're looking  for  music  broadcast
throughout the  world, you'll  find your  selection to be both wide and quick.
If you  want to  know what the CB citizenry has evolved into, the Spoiler will
help you find out with convenience that rewards your curiosity.

                         REGISTERING THE 440 SPOILER

     As with all shareware, the 440 Spoiler is supported largely for those who
obtain registered  copies of  the software  and documentation.    The  QSO2000
project is  not Microsoft  Corporation, and  nobody in the project wants it to
become more than a cooperative endeavor among the avant garde communicators of
the world  so that  the world of amateur-radio communications can more rapidly
become better.

     Several hundreds  of hours  of research,  trial-and-error,  and  software
development have  gone into  development of  the 440  Spoiler, and  before the
useful life  of the program is over several hundreds of hours will go into its
maintenance and  enhancement.   We urge you to consider the value that the 440
Spoiler represents  to you and to therefore register your copy of the software
by your  printing the  form provided below and mailing it with your remittance
to The QSO2000 Project.

     Your registration of the 440 Spoiler brings you by return mail the latest
version of  the 440  Spoiler on  diskette and  a copy  of  the  professionally
written,  printed,  and  bound  440  Spoiler  Technical  Reference  Manual  (a
significant enhancement  and update  of the  material  in  this  documentation
file).   It also entitles you to free upgrades of the 440 Spoiler software and
updated documentation on disk for a year after your registration.  You will be
notified  of  the  upgrades  by  mail  for  the  entire  year  following  your
registration.

     Shareware versions  of the  440 Spoiler  will be  maintained and enhanced
throughout the  useful like  of the package to a lesser extent than registered
versions are.   Rewards  for sharing  in the  resources  expended  by  further
development of the package will be significant.

     Please distribute  copies of  the latest  shareware version  of  the  440
Spoiler to  other operators  as widely  as you care to distribute them so that
they are invited to share in our progress.  Please include all of the files in
the 440  Spoiler package.   You  may not, of course, distribute copies of your
registered version  of the  440  Spoiler  in  accordance  with  the  licensing
agreement on the form printed below.

     Licensees for  a registered  version of  the Spoiler are welcome to write
the QSO2000  Project with  comments and questions.  Licensees are also welcome
to communicate  directly with  the authors  of the 440 Spoiler on the bulletin
board listed below,

                        Bulletin Board ECHO (Education)
                        806-741-1570
                        1200-2400 baud, 19200 baud USR-HST

     Licensees are  automatically registered  on the  board, and  upon calling
they will be routed into the Wireless Conference, the home of the 440 Spoiler.

------------------------------------------------------------------------------

                        440 SPOILER REGISTRATION FORM
                        -----------------------------





Bill Brewer. K5KNC, Coordinator
The QSO2000 Project
5518 12th Street
Lubbock, Texas 79416

     I hereby  apply for  licensed use of the 440 Spoiler software package and
enclose a  payment of  $39.00 for each licensed copy of the 440 Spoiler that I
am ordering.

     I understand  that I  will receive  by return mail a diskette copy of the
most current  registered version  of  the  440  Spoiler  and  a  copy  of  the
professionally written,  printed, and  bound 440  Spoiler Technical  Reference
Manual.   I also  understand that I will receive software support by both mail
and through Bulletin Board ECHO (Education) for a period of one year following
registration and  that I may obtain free upgrades of the registered version of
the 440 Spoiler within a year of the date printed below.

     I further  understand that  I will  be notified  of upgrades  as they are
available and  that I  may obtain  them by submitting the cost of shipping and
diskette to the QSO2000 project.

     I will  not distribute any copy of my licensed, registered version of the
440 Spoiler  that I  receive to  persons who  do not  reside in  my  immediate
household.




                                       ---------------------------------------
                                       Signature


                                       ---------------------------------------
                                       Name (please print)



                                       ---------------------------------------
                                       Street, P.O Box



                                       ---------------------------------------
                                       City, State  ZIP




      REMITTANCE: For _____ copies of registered versions at $39.00 each



                             A total of ________





      Please make checks and money orders payable to BILL BREWER, K5KNC

------------------------------------------------------------------------------

                         JOINING THE QSO2000 PROJECT

     You are  welcome to  join The  QSO2000 Project  in more  ways  than  your
registering for  your copy  of the  440 Spoiler.   We  will be happy to review
software that  you have  written that  is related to Amateur Radio and to work
with you in assessing it its role in the project.