LOOP ANTENNA CALCULATOR

                        by GEORGE CSAHANIN JR.
                                WB2DYB
                              7 JULY 1986


   THIS PROGRAM WILL CALCULATE THE VARIOUS PARAMETERS OF THE W5QJR SMALL LOOP
AS DESCRIBED IN JUNE 1986 QST.  THE FORMULAS ARE FROM TED HART'S BOOK ON SMALL 
LOOPS. THIS VERSION WILL CALCULATE THE CAPACITY, VOLTAGE, Q, BANDWIDTH. ETC. 
FOR THIS FINE ANTENNA. TED HAS NOTED THAT THE ACTUAL BANDWIDTHS ARE GREATER 
THAN THE FORMULAS CALCULATE, AND IN FACT I HAVE FOUND THIS TO BE TRUE WITH MY 
LOOP. MY BANDWIDTH IS ABOUT 2.2 TIMES WHAT THE FORMULA SHOWS IT TO BE. AT ANY 
RATE THIS IS A FINE ANTENNA, AND WORTH A SHOT IF YOU HAVE A SPACE PROBLEM. MY 
INSTALLATION IS IN MY ATTIC, WHERE IT ACTUALLY PERFORMS NECK& NECK WITH MT 
DIPOLE, OR VERTICAL. IN FACT MY FIRST QSO ON IT WAS ON 40 METERS FROM MY QTH 
IN TEXAS TO JAPAN! THE THING DIDN'T EVEN HAVE IT'S MOTOR DRIVE YET, IT WAS 
JUST SITTING ON THE BOOKSHELF NEXT TO ME IN THE SHACK, BAREFOOT, 100 WATTS, 
AND THIS JA7 CAME BACK TO ME. NOISE IMMUNITY ISN'T WHAT IT IS CRACKED UP TO 
BE. IT ISN'T WORSE, JUST NOT BETTER. 

  TED HART SELLS A CAPACITOR, WHICH I RECOMMEND. I GOT A STEPPING MOTOR FROM 
HERBACH & RADEMAN FOR $3.50. IT HAS LARGER STEPS, BUT I HAVE NOT HAD ANY 
PROBLEM WITH IT YET. WITH THE CAPACITOR THAT I GOT FROM TED, MY 3 FOOT 
DIAMETER LOOP (WHICH I DID HAVE TO PRUNE A BIT) TUNES FROM 6.950 MHZ TO 14.250 
MHZ. I GAVE UP PRUNING FURTHER, AS THIS DID ALL I NEEDED. IF YOU DO ANY 
SNOOPING AROUND THE INTERNATIONAL BROADCAST BANDS WITHIN THIS IS A GREAT FIND. 
AS FOR MOUNTING, I HAVE IT HUNG FROM THE 2X4'S IN THE ATTIC WITH NYLON ROPE. 

  IF YOU ARE AN ANTENNA EXPERIMENTER, OR IF YOU JUST HAVE A PLAIN OLD SPACE 
PROBLEM, TRY THIS ONE. FOR THE COST OF THE CAPACITOR, SOME SOLDER, AND SOME 
COPPER TUBING IT WILL PROVE ITSELF TO YOU. AS FOR THE FORMULAS, AND THIS 
PROGRAM WHICH IS WRITTEN FIRST IN BELIEVE IT OR NOT, COMMODORE BASIC, 
TRANSLATED TO MBASIC, AND FORTHER REFINED UNDER BASICA, THEN COMPILED WITH 
TURBOBASIC, TRY THEM. IF YOU NEED THE BASIC FILE DROP ME A NOTE THRU THIS 
AMATEUR RADIO BBS, OR THRU COMPUSERVE, OR DEEP THOUGHT IN AUSTIN, I'LL GET IT 
FOR YOU. THIS PROGRAM IS NOT FOR SALE, AND IS FREE FOR THE USE OF ALL ENGAGED 
IN NOT FOR PROFIT ACTIVITIES, RELATIVE TO NEWLOOP.EXE, OR NEWLOOP.BAS

GEORGE
512-331-9568 HOME
512-476-3636 WORK

PS- ALSO I HAVE INCLUDED NULOOP FROM ANOTHER SOURCE. IT DOES THE SAME, BUT DO 
NOT BE CONFUSED BY THE DIFFERENCE IN TUNING CAP RESULT. MINE IS SHOWING TUNING 
CAP MINUS THE DISTRIBUTED CAPACITANCE. NULOOP ALSO WANTS DIMENSION IN LENGTH 
OF A SIDE FOR AN OCTAGON, NEWLOOP(MINE) WANTS LOOP DIAMETER.

GEORGE 72060,3640/75706,577