AA4RE BBS and the G8BPQ Switch.


The AA4RE BBS can now be used via the DEDHOST Driver. See file DEDHOST.DOC
for full details of DEDHOST. The BBS must be configured as if you are using
a DRSI card, but you shouldnt load TNCTSR. You must run BBSETTNC before BB.
My testing was with AA4RE version 2.10, using parameters given below.


In PARAM.BB:

port
  port_type       = PC*PA-0
  com             = 255
  max_pac         = 128
  speed           = 4800
  max_connect     = 8
  max_channel     = 9
  max_pending     = 3
  monitor         = YES
  time_out        = 180
  fwd_min         = 15
  bbs_only        = N
  remote_sysop    = Y
  upload_download = Y
  broadcast       = y			; sends mail beacon on all radio ports
  port_name       = 144.650/432.675 NODE
  broadcast_path  = MAIL		; is ignored - set in config.txt file
  monitor_color   = 121
  no_out_fwd      = N
endport


In ROUTE.BB

G8BPQ  LEAVE
@BLANK LEAVE
*      GB7BAD


In PATH.BB

PATH GB7BAD A GB7BAD FORCE
T 0000 2300
C SWITCH				; note initial C SWITCH
SC GB7BAD
R* to *


Startup File.

BPQCODE
DEDHOST 9 1 1 8 255
BBSETTNC
BB

If you are using DesqView, BPQCODE should be loaded before DV, and DEDHOST
should be loaded in the AA4RE window.




John Wiseman, G8BPQ.
16/3/91