MAPPER .. A DX MAP DRAWING and Propagation Program
             for IBM PC Compatibles with graphics capability.


                              by

                         Dennis P. Murray
                         11165 McDonald Street
                         Culver City, Ca. 90230
                         CompuServ 72770,2765


     This program, written for BASIC compilers such as MICROSOFT QUICK
BASIC or BORLAND TURBO BASIC, displays a map of the world centered on
a user-selectable QTH, and does propagation predictions based upon a
modified MINIMUF method. It shows the regions of sunlight and darkness
around the world, and updates these regions automatically at user-
specified time intervals. It can also accept arbitrary times and dates
at the user option. The program accepts DXCC prefixes or
latitude/longitude values for the DX location, draws the path from the
home QTH to that location, and displays the range and azimuth from the
home QTH. The user can select either short or long paths. The sunspot
number used for propagation prediction can be changed either
temporarily, or be set as the new default value. The propagation
prediction gives the MUF (maximum usable frequency), LUF (lowest
usable frequency) based upon E-layer screening, and the minimum number
of F-layer hops for a 5 degree minimum launch angle.

     This program is  written for IBM PC compatible computers with an
EGA Graphics capability and color display. The source code provided
could be modified by the user to use other graphics displays supported
by your BASIC compiler. The program runs quite quickly on an AT clone
with a hard disk and 640k of RAM, but it might be a 'dog' on a floppy-
only machine because it must read some long files for the map data.

     The author does not intend to support this software, but is
simply releasing it into the public domain for non-commercial use by
HAMS who know what they are doing with their computer. The BASIC
source code is included for that reason.


     The author encourages the distribution of this program to anyone
who might find it useful, or onto bulletin boards which deal with HAM
radio or shortwave listening. Please make sure to include ALL the
required files in any uploading however. These files are:


          1- MAPPER.BAS       The Program Source Code

          2- MAPPER.EXE       the Q-BASIC v3.0 executable code

          3- MAPPER.ATL       An Atlas of DXCC countries and their
                              latitudes, longitudes, and DX prefix.
                              This is an ASCII file ,sorted by prefix,
                              which can be added onto by the user with
                              a word processor or text editor.

          4- MAPPER.DEF       A short file used to store some default
                              values used by the program.

          5- MAPPER.SCR       A large file which is used to store and
                              retrieve the screen data for a world map
                              centered on the user's location. This
                              file is rewritten whenever the user
                              changes the 'Home' location. ( It is
                              interesting to view the world as seen
                              from DX locations.) This data is read
                              into a large array in memory to permit
                              rapid redrawing of the map as the sun
                              moves. The file is written into the
                              integer array NSTORE by BLOAD and BSAVE
                              commands. Because the program uses a lot
                              of memory to speed things up, this array
                              is DYNAMIC and does not generally reside
                              in the normal BASIC data segment. The
                              version of the program supplied for
                              Q-BASIC uses the CALL PTR86 subroutine
                              supplied by MICROSOFT, and this module
                              must be specified during the linking
                              process. In TURBO-BASIC the VARSEG
                              command can be used to find the array
                              segment used in lines 3220 and 12140.

          6- MAPPER.DOC       This instruction file.

          7- WORLDMAP.DAT     A large ASCII file containing the
                              lat/lon of the world's borders. This is
                              used to recompute the map whenever the
                              map center point is redefined.






INSTRUCTIONS:


     To run this program simply enter 'MAPPER'. After an initial
message explaining the program is displayed, and you press any key to
proceed, you will be presented with a 3-choice initial menu which
allows you to change the default values of sunspot number, Home QTH
latitude and longitude, or the time interval at which the
daylight/darkness areas are redrawn. Pressing the appropriate number
key will put up prompts to allow changes to these variables, and will
return you to this menu after a change is entered. Pressing <ENTER> at
the menu prompt will store these new values in the MAPPER.DEF file and
proceed on to the map drawing.

     The map drawing will first put up a blank box, then calculate the
position of the sun at the time and date currently held by the DOS,
draw the solar terminator ( it looks like a satellite ground trace ),
and color the sun-lit portions of the world in red. It will then go on
to draw the country boundaries, color the oceans blue, and color the
USA green. The land areas which are in darkness will show up in black.
The program may miss coloring part of the oceans blue because of the
position of the solar terminator blocking the PAINT commands used in
the subroutine at line 8000 ... . I got tired of adding ocean points
to this routine to cover all the contingencies.

     After the map is drawn the Main Menu will appear on the left of
the screen, with 9 choices:

           1-   Select DX Prefix.
                    This is the default choice ( <enter> will select
                it. ). You will be prompted to enter a DX prefix ( eg.
                ZS for S. Africa ). The program will then search the
                DX atlas for an occurrence of this prefix. It will
                display all of the entries ( ie ZS1,ZS2,... ) that
                contain this string and ask you to select one. If the
                number of candidate entries is large you can simply
                <ENTER> to continue the search.

                    When a selection is made the program will fetch
                the location of the prefix, make a propagation
                prediction for the currently selected date and time,
                draw the path from your QTH to that location, and
                display sundry useful information at the top of the
                screen.

           2-Specify Country Name.
                Same as option 1 except that you are prompted for the 
                name of a country ( or a subset of that name such as 
                'AUS', which will find both Austria and Australia ). 
                The search process is insensitive to the case of your 
                entry.

  
           3-Specify Lat/Lon.
                    Same as the above option except you will be
                prompted to enter the latitude and longitude of the
                desired DX location.

           4-Change Sunspot Number.
                    Prompts for a new value of sunspot number. The
                program will use this new value until it is changed
                again during this session, but it will not change the
                value in the default file that is read when the
                program starts.

           5-Select Date/Time.
                    Prompts for a new date and time to be used to
                calculate solar terminator and make propagation
                predictions. <ENTER> responses to either of these
                prompts will fetch the current DOS value of date or
                time. This option will also turn off the automatic
                updating of the terminator and map redraw.

           6-Use Real Time.
                    This option will reset the above option to the
                real ( DOS ) date and time and enable the auto update
                feature.

           7-Select Short Path.
                    This toggles the path from the long path option
                back to short path.

           8-Select Long Path.
                    This option toggles long path calculations.

           9-Quit.
                    Exits the program and returns you to DOS.


     The program is entirely menu-driven so you don't have to remember
any special commands to use it.

     Good luck!!




Some Technical Information:

     The propagation is based upon the MINIMUF method, but with some
modifications of the author.

    1-I limit the ground range per F-layer hop to 3500km. This keeps
      the minimum elevation angle to about 5 deg. for F-layer heights
      of 300km. It is a rare HAM who has a high enough antenna or good
      enough ground screen to get much energy below 5 degrees. For
      those souls who want to be optimistic you can change line 40030
      to some longer range per hop.

    2-Rather than use the standard MINIMUF method of only looking at
      the first and last ionospheric bounce points ( the two control
      point method ), I calculate the propagation at every hop and
      select the worst-case condition out of all of them. This results
      in generally much more pessimistic MUF and LUF estimates than
      MINIMUF.

   3- I have included the E-layer screening frequency and lowest-
      usable frequency ( LUF ) estimation technique given in chapter 4
      of 'Amateur Radio Software ', by John Morris GM4ANB , RSGB
      Books, Lambda House, Cranborne Road, Potters Bar, Hertfordshire
      EN6 3JW. The subroutine starting at line 45000 contains this
      calculation.

    4-I have used what apparently is the HAM convention for longitudes
      being positive-West for the input and output in this program, in
      the MIMIMUF subroutine, and in the DX Atlas file MAPPER.ATL.
      However, in the internals of the program I immediately reverse
      the sign of the longitude. Being an engineer by training I think
      in terms of right-handed coordinate systems! Therefore those who
      want to modify the program should be wary of the sign of the
      longitude being used.

    5-Note that I have changed the names of the variables in the
      MINIMUF subroutine from the standard values to names which are
      descriptive of what the variable actually is.