MINIPROP (TM)

                     Ionospheric Propagation Predictions
                                 Version 2.0

                           A User-Supported Program

               Copyright 1985, 1987 by Sheldon C. Shallon, W6EL
                     Protected by Federal Copyright Law.
         Permission granted for non-commercial use and distribution.
        Not to be used for commercial advantage.  All rights reserved.





























                       This document contains 34 pages.









                              TABLE OF CONTENTS


      1. Introduction                                                   4
           Background                                                   4
           Fundamentals of Ionospheric Propagation                      5
           Disclaimer                                                   7
           Distribution and Use of MINIPROP                             8

      2. Starting MINIPROP                                              9

      3. The Master Menu                                               10

      4. Running a MINIPROP Prediction (Master Menu Choice 1)          11
           Latitudes and Longitudes                                    11
           Entering Terminal A Data                                    12
           Entering Terminal B Data                                    13
           Entering the Date                                           13
           Entering the Sunspot Number or Solar Flux                   13
           An Example                                                  14
           The Command Line                                            19

      5. DX Compass (Master Menu Choice 2)                             21
           Entering Data                                               21
           An Example                                                  21

      6. Changing Prediction Parameters (Master Menu Choice 3)         23
           Change Frequencies Used in Signal Level Predictions         23
           Change Antenna Minimum Radiation Angle Used in Predictions  24
           Suppress Output of Low Signal Levels                        25
           Suppress Output of Signal Levels at Frequencies
              Higher than Predicted FMUF                               25
           Change Path (Short or Long) to be Computed First            26
           Restore Original Set of MINIPROP Defaults                   26

      7. MINIPROP Utilities (Master Menu Choice 4)                     28

      8. Create or Modify Terminal A Default
         (MINIPROP Utilities Choice 2)                                 28

      9. Display Entries in MINIPROP Atlas
         (MINIPROP Utilities Choice 3)                                 29

     10. Add, Modify or Delete Entry in MINIPROP Atlas
         (MINIPROP Utilities Choice 4)                                 29
           Adding an Atlas Entry                                       29
           Modifying an Atlas Entry                                    30
           Deleting an Atlas Entry                                     30

     11. Display MINIPROP Documentation on Screen
         (MINIPROP Utilities Choice 5)                                 30

     12. Send MINIPROP Documentation to Printer
         (MINIPROP Utilities Choice 6)                                 31


                                      -2-









                               Table of Contents


     13. Print Table of Great-Circle Bearings
         (MINIPROP Utilities Choice 7)                                 31

     14. Convert Version 1 MINIPROP.ATL to Version 2 MP.ATL
         (MINIPROP Utilities Choice 8)                                 32

     15. References                                                    33














































                                      -3-









1. Introduction
---------------

     MINIPROP is a program for predicting ionospheric (skywave) propagation on
frequencies between 3 and 30 MHz.

     Background
     ----------

     I wrote my first propagation prediction program in 1966 to help me work
DX.  That first program, a computerized version of the cook-book procedure in
NBS Circular 462 (1), was written in BASIC on a GE time-sharing computer.
During the next several years the program was revised several times to take
advantage of improved prediction algorithms contained in several government
publications, primarily NBS Monograph 80 (2), ESSA Technical Report ITSA-1 (3),
and ESSA Technical Report ERL 110-ITS 78 (4).  Additional information was
obtained through personal correspondence with one of the authors of ERL 110-
ITS-78.  Additional program versions were written in BASIC for several
computers, and versions were written in FORTRAN and RPN.

     All of these programs predicted only signal strength.  MUF was predicted
manually, using the two-control-point method with a control point near each end
of the path, from world maps with superimposed predicted iso-MUF(ZERO)F2 and
iso-MUF(4000)F2 curves (5)(6).

     In December, 1982, MINIMUF-3.5 (7)(8), developed by the U.S. Naval Ocean
Systems Center, appeared in QST (9).  Although it used an incorrect algorithm
for control points that are in midnight sun conditions (10)(11) and for some
control points that are in polar night conditions, MINIMUF made practical the
prediction of F-layer MUF on microcomputers.

     MINIPROP version 1, released August 19, 1985, for CP/M computers, combined
the prediction of signal levels, F-layer MUF (using an improvement on the
MINIMUF-3.5 model with corrections for the midnight sun and polar night
conditions), and E-layer cutoff frequency.  The MS-DOS version was released the
following October.  MINIPROP was a compiled program written in the Pascal
programming language.

     MINIPROP was the most comprehensive propagation prediction program for
microcomputers that was available to the radio amateur, and copies of version 1
spread quickly worldwide.  As usage expanded, an increasing number of requests
were made for additional features.  At the same time, improved ionospheric
propagation models were acquired from several sources.  In particular, a
superior F-layer model (12) and other prediction techniques (13) used by the
BBC were made available through published literature and personal
correspondence, and an improved method for predicting E-layer cutoff frequency
was obtained from a report of the ITU International Radio Consultative
Committee (CCIR) (14).  The additional features and improved propagation models
have been combined in version 2 of MINIPROP.  The improved models are more
complex than those in the original MINIPROP and so have a longer running time,
but the additional time is well worth the improved prediction accuracy.





                                      -4-









     Fundamentals of Ionospheric Propagation
     ---------------------------------------

     The ionosphere is that region of the earth's atmosphere in which free ions
and electrons exist in sufficient abundance to affect the properties of
electromagnetic waves that are propagated within and through it.  Ions are
produced in the atmosphere partly by cosmic rays but mostly by solar radiation.
The latter include ultraviolet light, x rays, and particle radiation (during
storm periods).  These radiations are selectively absorbed by the several
gaseous constituents of the atmosphere, ion-electron pairs being produced in
the process.  For practical purposes, the ionosphere can usually be assumed to
extend from about 50 to roughly 2000 km above the earth's surface.  The
structure of the ionosphere is highly variable, and this variability is
imparted onto signals propagated via the ionosphere.  The ionosphere is divided
into three vertical regions -- D, E, and F -- which increase in altitude and in
electron density.

     The D region has an altitude range from 50 to 90 km.  The electron density
in the region has large diurnal variations highly dependent upon solar zenith
angle.  The electron density is maximum near local noon, is higher in summer
than in winter, and is lowest at night.

     The E region spans the altitude range from about 90 to 130 km.  The
maximum density occurs near 100 km, although this height varies with local
time.  The diurnal and seasonal variations of electron density are similar to
those of the D region.  Collisions between electrons and neutral particles,
while important in the E region, are not as numerous as in the D region.  The E
region acts principally as a reflector of hf waves, particularly during
daylight hours.

     Embedded within the E region is the so-called sporadic-E layer.  This
layer is an anomalous ionization layer that assumes different forms --
irregular and patchy, smooth and disklike -- and has little direct bearing to
solar radiation.  The causes of sporadic-E ionization are not fully known.  The
properties of the sporadic-E layer vary substantially with location and are
markedly different at equatorial, temperate, and high latitudes.  "Short-skip"
openings, sometimes on an otherwise dead band, are often a result of one-hop
sporadic-E ionization.  When sporadic-E ionization is sufficiently widespread,
multi-hop propagation is possible.  MINIPROP predictions do not include the
effects of sporadic-E ionization.

     The highest ionospheric region is termed the F region.  The lower part of
the F region, from 130 to 200 km, is termed the F1 region, and the part above
200 km is termed the F2 region.

     The F2 region is the highest ionospheric region, usually has the highest
electron density, and is the region of greatest value in long-distance hf
ionospheric propagation.  The region exhibits large variability in both time
and space in response to neutral winds and electrodynamic drifts in the
presence of the earth's magnetic field.  The maximum electron density generally
occurs well after noon, sometimes in the evening hours.  The height of the
maximum ranges from 250 to 350 km at midlatitudes to 350 to 500 km at
equatorial latitudes.  At midlatitudes, the height of the maximum electron
density is higher at night than in the daytime.  At equatorial latitudes, the
opposite behavior occurs.

                                      -5-









     The F1 region, like the E region, is under strong solar control.  It
reaches a maximum ionization level about one hour after local noon.  At night
and during the winter the F1 and F2 regions merge and are termed simply "F
region".

     Electromagnetic waves are refracted when passing through an ionized
medium, the refraction increasing with increased electron density and
decreasing with increase of frequency.  If the refraction is large enough, a
wave reaching the ionosphere is bent back toward earth as though it had been
reflected, thereby permitting reception of the wave at a large distance from
the transmitter.  The F2 layer is the most important in this regard because of
its height and its high electron density.  The maximum earth distance traversed
in one F2-layer "hop" is about 4000 km.  Round-the-world communication can
occur via multiple hops.

     If the frequency is too high, the wave is not refracted sufficiently to
return to earth.  The maximum frequency for which a wave will propagate between
two points is called the maximum usable frequency (MUF).  Frequencies higher
than the existing MUF at any given time are not supported, no matter how much
power is used.  However, because of the large variability that exists in the
electron density of the F2 region, predicted MUFs are not absolute limits, but
are statistical in nature.  The actual MUF at any given time may be higher or
lower than the predicted MUF.  Predicted MUFs are intended to be median values;
i.e., the actual MUF will exceed the predicted MUF 50 percent of the time, and
will be less than the predicted FMUF 50 percent of the time.  The predicted
frequency that will be supported only 10 percent of the time is a frequency
higher than the predicted MUF called the highest probable frequency (HPF), but
even higher frequencies are possible 10 percent of the time.  The predicted
frequency that will be supported 90 percent of the time is a frequency lower
than the predicted MUF called the optimum traffic frequency (FOT).  Curves of
predicted HPF, MUF, and FOT for several paths appear each month in QST.  In
MINIPROP, the predicted F2-layer maximum usable frequency is referred to as
FMUF.

     Signals on their way to or from the F2 layer must pass through the E
region of the ionosphere.  The E layer is also capable of "reflecting" hf
signals, and if the E-layer MUF is too high, the signals to or from the F2
layer are blocked -- or cut off -- by the E layer.  In MINIPROP, the E-layer
cutoff frequency is referred to as ECOF.  Signals at frequencies below the ECOF
will not pass through the E layer.  Signals can propagate between two points on
earth via the E layer in the same manner as they do via the F2 layer, but the
maximum earth distance traversed in one E-layer hop is only about 2000 km, so a
significantly greater number of hops is usually required on DX paths.  E-layer
propagation modes are not predicted by MINIPROP.

     The D region of the ionosphere must be traversed by signals on their way
to and from the F2 or E layers.  Electron densities in the D region are not
large enough to cause hf signals to be returned to earth, but the high
collision frequency between the electrons and neutral particles in the D region
gives rise to absorption of signals passing through it.  The reduction of
signal strength can be substantial, particularly in daytime on the lower hf
frequencies.  Antenna installations that provide low radiation (take-off)
angles can minimize the number of hops required between two stations, thereby
reducing the number of passes through the D region and the amount of signal
absorption.

                                      -6-









     Electron density in the ionosphere increases with increased solar
activity.  Therefore, MUFs and signal absorption both increase as solar
activity increases.  The Zurich smoothed mean sunspot number has been used
extensively as an index of solar activity and the one with which propagation
data has been correlated over the years.  Therefore, most propagation
prediction models require that the user specify the sunspot number to be used
in making a prediction.  The 2800-MHz (10.7-cm) solar noise flux is generally
considered a more accurate measure of solar activity, but with a smaller base
of propagation observations.  Since the two indices are highly correlated,
either index may be used.  MINIPROP allows you to specify either sunspot number
or solar flux as a measure of solar activity.

     Ionospheric propagation is susceptible to several kinds of short-term
disturbance that are usually associated with solar flares.  Depending upon the
nature of the disturbance, they are called sudden ionospheric disturbances,
polar cap absorption events, or ionospheric storms.  These disturbances upset
the electron configuration in the ionosphere, and consequently affect
propagation.  Propagation is also affected by changes in the earth's magnetic
field.  The magnetic field is constantly fluctuating, but the fluctuation
occurs over much wider limits during magnetic storms that accompany ionospheric
storms.  Ionospheric and magnetic storms are also often accompanied by visible
aurora.

     Except for the tendency of these disturbances to recur in synchronism with
the 27-day rotation period of the sun, they are difficult for the amateur (as
well as the professional) to predict and to quantify.  The severity of magnetic
disturbances is indicated by A and K indices that are broadcast by WWV at 18
minutes past each hour.  The A index is a daily measure of geomagnetic field
activity on a scale of 0 to 400.  The K index is a measure, for a 3-hour
period, of variation or disturbance in the geomagnetic field on a scale of 0 to
9.  In general, MUFs decrease and signal absorption increases as geomagnetic
field activity increases, although MUFs sometimes increase in equatorial
regions.

     Propagation only along great-circle paths is considered in MINIPROP.
Backscatter modes and bent-path modes are not considered.

     More information about ionospheric propagation can be found in "The
Shortwave Propagation Handbook" by W3ASK and N4XX (15), and in Chapter 22 of
the "The 1987 ARRL Handbook" (16).

     Disclaimer
     ----------

     Sheldon C. Shallon shall have no liability or responsibility to user or
any other person or entity with respect to any loss or damage caused or alleged
to be caused directly or indirectly through the use of this documentation or
the MINIPROP program.








                                      -7-









     Distribution and Use of MINIPROP
     --------------------------------

     MINIPROP is a copyrighted program.  All rights are retained by the author.
MINIPROP is not to be sold; nor is it to be used for commercial purposes.  You
may freely distribute MINIPROP, and you are encouraged to do so, but you may
not charge for doing so.  The following files should be included in any
distribution:
                                 MP.COM
                                 MP1.000
                                 MP1.CHN
                                 MP2.CHN
                                 MP3.CHN
                                 MP4.CHN
                                 MP.DOC
                                 MP.ATL
                                 READ.ME

     MINIPROP is a user-supported program.  This means that if you find
MINIPROP useful you should consider sending a contribution in the suggested
amount of $25.00 to the author:

                           Sheldon C. Shallon
                           11058 Queensland St.
                           Los Angeles, CA  90034-3029

     Your comments and suggestions regarding MINIPROP will be welcome.  Please
enclose a self-addressed stamped envelope if you wish a reply.

                                          Good DXing,
                                          Shel, W6EL
                                          2-24-87
























                                      -8-









2. Starting MINIPROP
--------------------

     If you have not already done so, please make a working copy of MINIPROP.
The disk on which you received MINIPROP should be put away for safekeeping, and
the working copy used when you want to run MINIPROP.  Do not write protect the
working copy because MINIPROP has to able to write to the disk.

     Your working disk should contain the following files:

          MP.COM   (Required to start MINIPROP.)
          MP1.000  (You cannot run a MINIPROP prediction without this file.)
          MP1.CHN  (Required to start MINIPROP.)
          MP2.CHN  (Necessary for the DX Compass feature only.)
          MP3.CHN  (You will not be able to change several of the
                    built-in prediction parameters without this file.)
          MP4.CHN  (You will not be able to use the MINIPROP utilities
                    without this file.)
          MP.DOC   (This MINIPROP documentation.)
          MP.ATL   (Atlas of latitudes and longitudes.  Not essential,
                    but very helpful.)
          READ.ME  (Help in starting MINIPROP.)

     In addition, a MP.DEF file will be created automatically the first time
you run MINIPROP.  This file will hold any changes you make to several of the
values and settings used in the MINIPROP predictions, as well as the latitude
and longitude of your location.  Be sure there is room on the disk and in the
disk directory for this short file.

     All of the MINIPROP files should be on the logged disk drive and in the
current directory.

     To run MINIPROP, type "MP" following the > prompt from your computer's
operating system.  (In this documentation, everything you are to enter on your
computer keyboard appears in quotes.  You should type everything between the
quotes exactly as shown, but do not type the quotes.  You may always use either
upper or lower case letters.)  Then press the ENTER or RETURN key, depending on
the keyboard of your computer.  When running MINIPROP, you will see this key
referred to on the screen as <ENTER>, <RETURN>, or <RTN>.

     After MINIPROP has been loaded from disk into RAM, an opening message and
the MINIPROP master menu will appear on the screen.














                                      -9-









3. The Master Menu
------------------

     The MINIPROP master menu will appear on your screen as follows:

                                  MASTER MENU

           0. Exit from MINIPROP (Quit)
           1. Run a MINIPROP prediction (you may also press <ENTER>)
           2. DX Compass (directions of band openings)
           3. Change prediction parameter defaults
           4. MINIPROP utilities

                    Your choice :

     If you do not wish to continue, enter "0" to terminate MINIPROP and return
to the operating system.  You may also enter "Q" or "X".

     Use choice 1 to predict propagation between two locations (terminals).
This is the choice you will probably use most often.  You may also press just
<ENTER> or <RETURN> to invoke this choice.  See Section 4 below.

     Choice 2 will give you a picture of the highest frequencies that are most
likely to be open to DX in several directions from a specified location
(terminal) at a given time of day.  See Section 5 below.

     Choice 3 gives you the option to change certain prediction parameters from
their default values.  These options are:

     Change frequencies used in signal level predictions
     Change antenna minimum radiation angle used in predictions
     Suppress output of low signal levels
     Suppress output of signal levels at frequencies higher than predicted FMUF
     Change path (short or long) to be computed first
     Restore original set of MINIPROP defaults

More information on these options can be found in Section 6 of this
documentation.

     Choice 4 gives you access to the MINIPROP utilities.  With these utilities
you can:

     Create or modify Terminal A default
     Display entries in MINIPROP atlas
     Add, modify, or delete entry in MINIPROP atlas
     Display MINIPROP documentation on screen
     Send MINIPROP documentation to printer
     Print table of great-circle bearings
     Convert version 1 MINIPROP.ATL to version 2 MP.ATL

See Sections 7 through 14 of this documentation for more information about the
MINIPROP utilities.




                                     -10-









4. Running a MINIPROP Prediction (Master Menu Choice 1)
-------------------------------------------------------

     Latitudes and Longitudes
     ------------------------

     To compute a propagation prediction between two terminals, MINIPROP needs
to know the locations of those two terminals.  A location is defined in terms
of its latitude and longitude.  You will be asked for the latitude and
longitude of the terminals at the two ends of the propagation path.  One of the
terminals is called Terminal A; the other is Terminal B.  It makes no
difference which terminal is A and which is B.

     Latitude is a measure of angular distance north or south of the earth's
equator.  It is measured in degrees.  The latitude of the equator is 0 degrees.
The north pole is at 90 degrees north latitude, and the south pole is at 90
degrees south latitude.  Latitudes can never exceed 90 degrees in magnitude.
To distinguish between north and south latitudes, the latter must be preceded
by a minus (-) sign.  For example, 40 degrees north latitude would be entered
as 40; 40 degrees south latitude would be entered as -40.  Do not place a plus
(+) sign in front of north latitudes.

     Longitude is a measure of angular distance east or west of the prime
(Greenwich) meridian.  It is measured in degrees.  The longitude of the prime
meridian is 0 degrees.  Longitudes to the west of the prime meridian (e.g., in
the western hemisphere) are west longitudes.  Longitudes to the east of the
prime meridian (e.g., in the eastern hemisphere) are east longitudes.  The
meridian half way around the world from the prime meridian is at longitude 180
degrees; its longitude can be given as either 180 degrees east or 180 degrees
west (180 or -180).  Longitudes usually have magnitudes between 0 and 180
degrees.  However, any particular meridian of longitude can be reached by
travelling either east or west from the prime meridian.  Therefore, a longitude
of 90 degrees west is equivalent to a longitude of 270 degrees east, for
example.  MINIPROP will accept longitudes with magnitudes between 0 and 360
degrees.  To distinguish between west and east longitudes, the latter must be
preceded by a minus (-) sign.  For example, 100 degrees west longitude would be
entered as 100; 100 degrees east longitude would be entered as -100.  Do not
place a plus (+) sign in front of west longitudes.

     An atlas containing latitudes and longitudes of more than 350 locations is
supplied with MINIPROP, but you will probably have need for your own latitude
and longitude and for latitudes and longitudes of other locations that are not
in the MINIPROP atlas.  You can generally find these in atlases that are
available in bookstores and libraries, or you may scale them from maps or
charts.  A note of caution is in order with respect to latitudes and longitudes
that are tabulated in atlases.  They are usually shown as decimal numbers, but
are often in a degree.minute format.  Thus, 40.54 might mean 40.54 degrees, but
it usually means 40 degrees, 54 minutes.  If the latter is meant, the
equivalent decimal value is 40.9 degrees.

     MINIPROP will accept latitudes and longitudes as decimals or in a degree
minute second format.  If you wish to enter a latitude or longitude in the
latter format, leave one blank space between the degrees and minutes, and
another between the minutes and seconds, if any.  Leading and trailing blank
spaces are invalid.  Here are some examples.  All of the values in each column

                                     -11-









are equivalent.

     "40.9"         "0.5"         "-28 10 30"    "-135" (east longitude)
     "40 54"        "00 30"       "-28 10.5"     "225"  (west longitude)
     "40 54 0"      "00 30 0"     "-28.175"
     "40 54 00"     "00 30 00"

The following entries are invalid.

          "33 60"      (Minutes and seconds must be less than 60.)
          "118  25"    (Too many blank spaces.)
          "-34 -25"    (Put minus sign in front only.)
          " 42"        (Leading blanks not allowed.)
          "42 "        (Trailing blanks not allowed.
          "85.5 25"    (Decimal allowed only in last part of entry.)
          "91"         (If a latitude, may not exceed 90.)
          "361"        (Longitudes may not exceed 360.)
          "+34"        (Leading + sign not needed or allowed.)

     Entering Terminal A Data
     ------------------------

     When you run a MINIPROP prediction you will see the following prompt on
the screen.

      Enter Terminal A latitude (or <RTN> for default), or prefix, or <?> :

     You have four choices:  (1) You may enter the latitude of Terminal A.
(2) you may press <RTN> to use the Terminal A default location.  (Remember,
<RTN> means you should press the RETURN or ENTER key.)  (3) you may enter the
country prefix (or other unique identifier) if you want to use a MINIPROP atlas
entry.  (4) you may press <?> followed by <RTN> if you want to be reminded of
the prefixes that are available in the atlas.

     If you enter a latitude in response to the latitude prompt, you will next
be prompted for the longitude of Terminal A.  Enter the longitude.  Then you
will be asked for the name of Terminal A.  You may want to enter a call sign,
city name, or other identifier.  The name you enter will appear in the
prediction heading as an identifier for your use.  MINIPROP makes no other use
of the name.  The name may contain up to 17 characters and blanks.  You may
press only <RTN> if you do not want to enter a name.

     If you press only <RTN>, MINIPROP will look in the MP.DEF disk file for
the default latitude, longitude, and name of Terminal A.  This saves you the
trouble of entering your own latitude, longitude, and terminal name each time
you want a prediction on a path from your own station.  If you have not already
created a Terminal A default for your own location, one of the MINIPROP
utilities (Master Menu choice 4) will help you do so.

     If you enter a prefix in response to the latitude prompt, MINIPROP will
search the MP.ATL atlas file to find the entry with that prefix.  The contents
of the atlas entry will appear on the screen and the displayed values will be
used in the prediction.

       If you need to be reminded of the prefixes in the MINIPROP atlas, press

                                     -12-









<?>.  All of the prefixes in the atlas will appear on the screen, followed
again by the above prompt.

     Entering Terminal B Data
     ------------------------

     The following prompt will appear next.

          Enter Terminal B latitude, or prefix, or <?> :

     Except for the Terminal A default, your choices are the same as for
Terminal A.  Proceed as for Terminal A.  You may not use the Terminal A default
location for Terminal B.

     Entering the Date
     -----------------

     Next you will be asked for the date to be used in the prediction.
MINIPROP needs the date to compute the position of the sun, the times of
sunrise and sunset, and the directions of the gray lines at the path terminii.
Enter the date as a six-digit number with no leading, trailing, or embedded
spaces and no punctuation.  Examples:

     122585 is December 25, 1985
     010187 is January 1, 1987
     070410 is July 4, 2010

     MINIPROP will convert the last two digits to a year between 1945 and 2044,
inclusive.  This 100-year span allows you to obtain current predictions, to
compare MINIPROP predictions with actual propagation records back to the
beginning of the post-WW II DXCC, and to predict propagation well into the
future.  Invalid dates (e.g., 022987) will not be accepted.

     Entering the Sunspot Number or Solar Flux
     -----------------------------------------

     You have to enter one more item of information.  You will see the
following prompt on the screen.

          Sunspot number (or solar flux, e.g., F70) for above date?

     If you want to enter a sunspot number, just enter the number and press
<RTN>.  If you want to enter a solar flux value, first enter "F" or "f",
immediately followed (no blanks) by the value and press <RTN>.  For example, a
sunspot number of 45 would be entered as "45"; a solar flux of 70 would be
entered as "F70" or "f70".  MINIPROP will do the conversion for you.

     The sunspot number and solar flux are both measures of solar activity.
They are highly, but not 100-percent, correlated with each other.  Therefore, a
range of sunspot numbers can correspond to a particular value of solar flux,
and vice versa.  For example, the sunspot number was 0 on eight days in
November, 1986; on those days, the solar flux value ranged from 71 to 80.  On
six days when the value of the solar flux was 76, the sunspot number ranged
from 0 to 23.  Various formulas to approximate the relationship between sunspot
number and solar flux have appeared in the literature.  MINIPROP uses the

                                     -13-









following formula published by the Institute for Telecommunication Sciences
(6):

          solar flux = 63.75 + 0.728 ssn + 0.00089 ssn^2

In this formula, ssn is the 12-month moving average Zurich sunspot number, and
ssn^2 is the square of that number.  The solar flux is in units of 10^-22 watts
per square meter per Hz.

     MINIPROP will accept sunspot numbers between 0 and 390, and solar flux
values between 60 and 483.  However, if you input a solar flux value between 60
and 63.75, MINIPROP will substitute a solar flux value of 63.75 corresponding
to a sunspot number of 0.  Solar flux values less than 60 will not be accepted.

     Predicted sunspot numbers are published monthly in conjunction with the
propagation charts in QST, and in George Jacobs' propagation column in CQ.  QST
also predicts the solar flux value, but the formula relating QST's predicted
sunspot number and solar flux value differs somewhat from the above formula
used in MINIPROP.  Daily values of solar flux are broadcast by WWV at 18
minutes past each hour.  In addition, the weekly KH6BZF Reports contains up-to-
date sunspot numbers, solar flux values, A and K indices, propagation
conditions, and other useful information.

     MUFs do not seem to follow day-to-day variations in solar activity, so I
prefer to use monthly predicted sunspot numbers.  However, a change in solar
activity, when sustained for a period of time (several days, say), does
influence MUFs.  Therefore, you may want to use solar flux values representing
the average of the values broadcast by WWV for the past several days.
Absorption in the D region reacts more quickly to solar activity, but
significant changes in predicted signal strengths would not be expected except
for very large changes in solar activity, and then only on daytime paths at the
lower frequencies.

     MINIPROP will start computing the propagation prediction as soon as you
have entered a sunspot number or solar flux value.

     An Example
     ----------

     As an example, let's predict what propagation will be like on the path
from Omaha, Nebraska, to Agalega (3B6) on January 25, 1990, if the predicted
smoothed sunspot number is 114.  I have chosen this example because it
demonstrates the several elements of a MINIPROP prediction and illustrates how
band openings are predicted on the 10- through 80-meter bands.

     Start MINIPROP by entering "MP" following the > prompt from your
computer's operating system.  When the MINIPROP master menu appears on the
screen, enter the number "1" or press the ENTER or RETURN key.

     We will assume that the latitude and longitude of Omaha have not been
entered as the Terminal A default and are not in the MINIPROP atlas, so we have
to look them up and enter them manually.  My Rand McNally atlas lists the
coordinates as 41 deg 15 min N, 95 deg 56 min W.  In response to the prompt for
the latitude of Terminal A, enter "41 15".  In response to the longitude
prompt, enter "95 56".  In response to the name prompt, we can enter any string

                                     -14-









of up to 17 characters.  Let's use only the city name; enter "Omaha".

     Let's use the MINIPROP atlas entry for Agalega.  In response to the prompt
for the latitude of Terminal B, enter "3B6".

     For the date enter "012590".  For the sunspot number enter "114".

     After a brief delay, the following display will appear on the screen while
MINIPROP continues to compute the prediction.


                                  MINIPROP
                                 01-25-1990
   Sunspot Number : 114.0   Flux : 158.3   Min. Radiation Angle :  1.5 deg

        TERMINAL A : Omaha              TERMINAL B : Agalega
          Latitude :  41.25 N             Latitude :  10.42 S
         Longitude :  95.93 W            Longitude :  56.65 E

           Sunrise : 1346 UTC              Sunrise : 0211 UTC
         Gray line : 26/206 deg          Gray line : 19/199 deg

            Sunset : 2326 UTC               Sunset : 1440 UTC
         Gray line : 334/154 deg         Gray line : 341/161 deg

           SHORT-PATH  Bearing from A to B :  45.8 deg
                       Bearing from B to A : 326.7 deg
                       Path Length : 15651 km    9726 mi (U.S.)

           LONG-PATH   Bearing from A to B : 225.8 deg
                       Bearing from B to A : 146.7 deg
                       Path Length : 24349 km   15131 mi (U.S.)


     The second line shows the date you specified in expanded form showing the
four-digit year.  On the next line are the sunspot number you entered and the
equivalent solar flux value.  If you had entered the solar flux value, MINIPROP
would have computed and displayed the equivalent sunspot number.  The third
line also shows the antenna minimum radiation (take-off) angle that is being
used in computing the prediction.  The default (initial setting) for this
parameter is 1.5 degrees.  If your antenna installation or horizon obstructions
preclude achievement of this low an angle, Master Menu choice 3 allows you to
increase the value.  (See Section 6 below.)  The value may also be decreased if
appropriate to your installation.  For this example, we will use the default
1.5 degrees.

     The next seven lines contain two columns of information, one for each of
the terminals.  For each terminal, the name, latitude, and longitude are
displayed.  In this example the latitudes and longitudes were specified in
degree-minute format, but MINIPROP has converted them to decimals.  Although
shown to two decimal places, latitudes and longitudes are carried to greater
accuracy within MINIPROP.  Instead of a plus (implied) or minus sign, a letter
(N, S, E, or W) indicating the direction from the equator or the prime meridian
is shown.


                                     -15-









     Sunrise and sunset times and directions of the gray lines are also shown
for each terminal.  There are several definitions of sunrise and sunset (e.g.,
civil, nautical, astronomical), and times can differ by several minutes between
the different definitions.  MINIPROP defines sunrise and sunset as the times
when the center of the sun is on the celestial horizon.  The gray line is the
fuzzy band around the earth separating daylight and darkness.  Many DXers point
their antennas along the gray line at sunrise and sunset to look for DX.  For
each sunrise and sunset, the first gray line direction shown is the most
northerly direction and the second direction is the most southerly;  the two
directions are 180 degrees apart.  In this example, sunrise at Omaha is at 1346
UTC.  Around that time you would point your antenna at 26 or 206 degrees east
of north to point along the gray line.

     Next, the bearings and path lengths are shown for both the short great-
circle path and the long great-circle path between the two terminii.  You will
note that on neither path do the bearings from one terminal to the other differ
by 180 degrees (e.g., 45.8 and 326.7 degrees on the short path).  This point is
mentioned because some people are surprised that this is true.  Except for some
unique geometries, the bearings will not be 180 degrees apart.  Of course, the
short-path and long-path bearings from any one terminal are 180 degrees apart
(e.g., 45.8 and 225.8 degrees).

     By the time you have read this far, MINIPROP will probably have finished
computing the propagation prediction for the short path.  MINIPROP displays its
progress at the bottom of the screen while it is computing the prediction.  It
displays a period (.) periodically while it is computing absorption along the
path, a lower case f while computing F-layer MUF, and a lower case e while
computing the E-layer cutoff frequency.  When MINIPROP has finished computing
the prediction, "Press any key when ready for predictions." appears at the
bottom of the screen.  Press any key when you are ready.

     The table of predictions on the next page will appear on your screen.

     The information displayed at the top of the screen is similar to the
information in the previous display, but somewhat abbreviated.  Bearings and
path length are shown only for one path, in this case the short path.  MINIPROP
has computed and displayed the minimum number of F hops corresponding to the
minimum radiation angle (1.5 degrees) that appeared on the previous display.
In this example, 5 F hops are required.  The resulting predicted radiation
angle is shown to be 5 degrees.

     The predicted F-layer MUF (FMUF), E-layer cutoff frequency (ECOF), and
received signal levels are shown for every two hours UTC.

     The predicted signal levels are shown for frequencies in the five primary
hf bands.  You may change these built-in frequencies to any five frequencies of
your choice between 3 and 30 MHz.  (See Section 6 below.)  The signal levels
are in dB with respect to 0.5 microvolt "behind" 50 ohms, and assume a matched
antenna load.  On my receiver 0.5 microvolt produces an S3 signal.  So 0 dB
would be S3.  At 5 dB per S unit, 10 dB would be S5, 30 dB would be S9, etc.
The signal levels assume 100 watts radiated power with half-wave dipole
antennas in free space at both ends of the path, and with the antennas oriented
for maximum gain along the path.  Add or subtract whatever number of dB you
think appropriate for the antennas and power levels in use.


                                     -16-









     Predicted signal levels are computed independently of the FMUF and ECOF
under the assumption that the number of F hops (in this case 5) shown in the
header are present at all times and for all frequencies, and that there is no
E-layer cutoff.  (To take E-layer reflections into account in computing signal
levels would be time prohibitive.)  This is important to remember: SIGNAL LEVEL
PREDICTIONS ASSUME THAT A REFLECTING F LAYER IS ALWAYS PRESENT AND THAT THERE
IS NO REFLECTING E LAYER.


MINIPROP (TM) SHORT-PATH PREDICTIONS     01-25-1990     Path Length : 15651 km
Sunspot Number : 114.0   Flux : 158.3   F Hops :  5   Radiation Angle :  5 deg
TERMINAL A : 41.25 N    95.93 W   Omaha               Bearing to B :  45.8 deg
TERMINAL B : 10.42 S    56.65 E   Agalega             Bearing to A : 326.7 deg
Terminal A Sunrise/Set : 1346/2326 UTC  Terminal B Sunrise/Set : 0211/1440 UTC

                           ----------- SIGNAL LEVELS ABOVE 0.5 uV ------------
UTC      FMUF     ECOF     3.6 MHZ    7.1 MHZ   14.1 MHZ   21.2 MHZ   28.3 MHZ

0000     15.9      5.8      40.5 a     35.5 A     29.2 A     24.9
0200     12.5      4.6      39.3 a     35.1 A     29.1 B
0400     14.0     13.8       8.4 a     22.4 a     25.1 B
0600     14.8     17.8                 -0.9 a     17.7 a     19.5
0800     14.2     19.3                            10.7 a     16.2
1000     11.3     19.1                             6.6
1200     11.5     16.9                             6.9
1400     17.3     11.6                            10.8 A     16.3
1600     26.1     14.1                  2.7 a     18.9 A     20.1 A     18.9 B
1800     30.8     15.3     -12.8 a     13.7 a     22.3 a     21.7 A     19.9 A
2000     29.5     14.4       6.9 a     21.8 a     24.9 a     22.9 A     20.6 A
2200     23.3     10.8      28.0 a     30.4 a     27.6 A     24.2 A     21.3

<G>raph, <T>able, <P>rint table, <Q>uit, <M>enu, or <L>ong path ?


     The "A", "a", "B", and "b" flags are included in the predictions to flag
predicted band openings and to aid in interpreting the predicted signal levels.
The table on the next page shows how the flags indicate the relationship that
exists between the frequency at the top of a  column and the FMUF and ECOF, and
also shows the probability that propagation on the path can be supported by the
F layer.

     "A"s or "a"s in a particular frequency column flag the times that openings
are most probable on that frequency.  At these times, the frequency at the top
of the column is less than the predicted FMUF.  Therefore, it is expected that
the probability of F-layer propagation is greater than 50 percent.  The
difference between "A" and "a" is that the frequency is above the ECOF in the
first case, but below the ECOF in the second.  (The "A" flag has the same
meaning as the "+" flag in MINIPROP version 1.0.)  When the "A" flag is
present, the predicted signal levels apply.  When the "a" flag is present,
usually when one or both of the two terminii is in daylight, E hops are added
to, or substituted for, F hops.  This causes additional absorption loss, and
possibly additional ground reflection loss, that results in weaker signals than
the predicted values.  The reduction of received signal level can be very
large, particularly at the lower frequencies.  Transmitter power and high
antenna gains may sometimes be used to overcome the increased signal loss.

                                     -17-









This allows you to hear foreign broadcast stations in the middle of the day on
the 41 meter band, but this approach usually is not practical for radio
amateurs.

             Frequency at Top     !   Flag   !   Probability of
                of Column         !          !   F-Layer Support
           ========================================================
             Below FMUF           !          !
             ---------------------!----------!
                and above ECOF    !    A     !    More than 50%
             ---------------------!----------!
                and below ECOF    !    a     !
           ========================================================
             Between FMUF and HPF !          !
             ---------------------!----------!
                and above ECOF    !    B     !       10 - 50%
             ---------------------!----------!
                and below ECOF    !    b     !
           ========================================================
             Above HPF            !   None   !    Less than 10%
           ========================================================

     "B"s or "b"s in a particular frequency column flag the times that the
frequency at the head of the column is greater than the predicted FMUF, but is
predicted to be less than the F-layer HPF.  Therefore, the probability of F-
layer propagation is expected to be less than 50 percent, but greater than 10
percent.  When this possible opening actually occurs, and if the flag is "b",
signal levels are expected to be weaker than shown because E-layer cutoff is to
be expected; the predicted signal levels apply when the opening occurs and the
flag is "B".

     Propagation may occur, with low probability, on frequencies even higher
than the HPF, so predicted signal levels are shown for frequencies up to 150
percent of the predicted FMUF.  The display of signal levels is normally
suppressed for frequencies greater than 150 percent of the FMUF, but this
suppression can be cancelled if you wish; see Section 6 below.  Of course, the
signal levels that are shown at the higher frequencies are only applicable when
the actual MUF is high enough to permit propagation at these frequencies.

     The display of signal levels below -20 dB is normally suppressed because
weaker signals are generally unusable by radio amateurs, even after allowance
is made for transmitter power and antenna gains.  The blanks in the 3.6- and
7.1-MHz columns are a result of this suppression.  The suppression threshold
can be changed; see Section 6 below.

     In this example, 10 meters will most probably be open with good signals
from 1800 to 2000 UTC, as indicated by the "A" flag in the 28.3-MHz column.
The "B" flag in this column indicates that there is a probability between 10
and 50 percent that the band will open as early as 1600.  If the band does not
open early, the signal level shown at 1600 has no meaning.

     15 meters will be open from 1600 to 2200 with a probability in excess of
50 percent.



                                     -18-









     20 meters will probably open around 1400 UTC with only fair signals.
Signals will build until 1600, drop some around 1800 to 2000 as a result of E-
layer cutoff, and then build to strong signals around 0000 UTC.  The band will
probably go out on this path from 0200 to 0400; predicted signal levels
opposite the "B" flags apply only if the band stays open, and should be
disregarded otherwise.  20 meters will be open again from 0600 to 0800, but
signals will be weaker than shown because of E-layer cutoff.

     On 40 meters, signals will be good from 0000 to 0200.  E-layer cutoff will
reduce signal levels, probably below usable levels because of the low
frequency, during most of the remainder of the day.

     E-layer cutoff will reduce all signal levels shown for 80 meters, but
signals will be best around 0000 to 0200 UTC.

     The Command Line
     ----------------

     At the bottom of the screen is a line containing several command choices.
Make your choice by pressing the initial letter of the command; either upper or
lower case may be used.

     <G>raph.  This choice causes the following screen display to appear.


SHORT-PATH PREDICTIONS               01-25-1990               Omaha TO Agalega
Sunspot Number : 114.0   Flux : 158.3   F Hops :  5   Radiation Angle :  5 deg
           MHZ            X = FMUF         O = ECOF            MHZ
           30 -----------------------------------XX+XXX-------- 30
           28                                  XX      X        28
           26                                 X         XX      26
           24                                X            X     24
           22                               X              X    22
           20 ---------------OOOOOO--------X----------------X-- 20
           18            OOOO      OOO    X                  X  18
           16 X        OO             OO X       OOOO         X 16
           14  X    XXXXXXXXXXXX        OO   OOOO    OOOO       14
           12   XXXX O          XXXXXXXX  OOO            O      12
           10 ------O-------------------------------------OO--- 10
            8      O                                        O    8
            6 O                                              OO  6
            4  OOOO                                              4
            2                                                    2
            0 -------------------------------------------------  0
              0   0   0   0   0   1   1   1   1   1   2   2   0 U
              0   2   4   6   8   0   2   4   6   8   0   2   0 T

<G>raph, <T>able, <P>rint table, <Q>uit, <M>enu, or <L>ong path ?


The graph uses the letters X and O to plot FMUF and ECOF versus time.  The time
resolution is 30 minutes instead of the 2-hour resolution in the previous
prediction table.  However, the limited screen height limits the frequency
resolution to 2 MHz.  When both an X and an O should appear in the same
location on the graph, the one that is predicted to be at the highest frequency

                                     -19-









appears.  At 0400 UTC in this example, FMUF and ECOF are both 14 MHz to the
nearest 2 MHz; an X appears because the FMUF of 14.0 MHz exceeds the ECOF of
13.8 MHz.  At 1300, only an O appears at 14 MHz because the ECOF is higher than
the FMUF, with both rounding to 14 MHz.  (The predicted ECOF of 14.9 MHz
exceeds the predicted FMUF of 13.5 MHz.)  The plus (+) sign at 1830 indicates
that the predicted FMUF exceeds 31 MHz.  The command line is repeated below the
graph.

     <T>able.  This choice causes the prediction table to reappear.

     <P>rint table.  This choice sends the prediction table to your printer.
The longer page length as compared to the screen height allows predictions to
be printed for every 30 minutes instead of every 2 hours.  Otherwise, the table
is the same as seen on the screen.  57 lines will be printed, so make sure the
paper is adjusted in your printer so that printing can start within 10 lines
from the top of the page.  It is assumed that your page length is 66 lines.

     <Q>uit.  This choice terminates MINIPROP.

     <M>enu.  This choice causes the MINIPROP master menu to reappear on the
screen.  From the master menu you can choose to run another prediction, or you
can select one of the other master menu choices.

     <L>ong path.  This choice is available only after the short-path
prediction has been displayed first, and causes MINIPROP to compute a
propagation prediction for the long great-circle path between terminals A and
B.  Both table and graph displays are available as in the above example.  Long-
path propagation is difficult to predict reliably; predicted openings often do
not occur, particularly on the higher frequencies.

     <S>hort path.  This choice is available only after the long-path
prediction has been displayed first, and causes MINIPROP to compute a
propagation prediction for the short great-circle path between terminals A and
B.






















                                     -20-









5. DX Compass (Master Menu Choice 2)
------------------------------------

     The DX Compass is a screen display showing the highest FMUF you can expect
on twelve bearings separated at intervals of 30 degrees from a specified
location for Terminal A and at any specified time of day.  This feature is
especially useful for planning your operations during DX contests.

     Entering Data
     -------------

     Data entry is similar to the data entry described above in Section 4 for
MINIPROP predictions.  Only one terminal is used in the DX Compass, so you will
not be asked for Terminal B data.  Entry of Terminal A data, the date, and the
sunspot number or solar flux are the same as in Section 4.

     One new piece of data must be entered.  The following prompt will appear
on the screen after the sunspot number or solar flux is entered.

          DX Compass for what UTC (e.g., 0215) (or <RTN> to quit)?

As indicated in the prompt, a four-digit UTC in 24-hour format should be
entered.  Valid times are from 0000 to 2400.  Press <RTN> if you want to quit
the DX Compass and return to the MINIPROP master menu.

     An Example
     ----------

     As an example, let's use the same data we used in the prediction example
in Section 4, except that there is no Terminal B.  Terminal A is Omaha,
Nebraska.  The date is January 25, 1990.  We assume a predicted smoothed
sunspot number of 114.

     Start MINIPROP by entering "MP" following the > prompt from your
computer's operating system.  When the MINIPROP master menu appears on the
screen, enter the number "2".

     In response to the prompt for the latitude of Terminal A, enter "41 15".
In response to the longitude prompt, enter "95 56".  For the name of Terminal
A, enter "Omaha".

     For the date enter "012590".  For the sunspot number enter "114".

     For UTC, let's use the time of sunrise.  From the example in Section 4,
we know this to be 1346; so enter "1346".

     When MINIPROP has finished computing the DX Compass, the display at the
top of the next page will appear on the screen.

     The time you specified is shown in the center of the display together with
the specified latitude, longitude, and date.  The FMUF values are arranged in a
"circle" around the center of the display.  Immediately below "FMUF" in the top
line is the FMUF that applies on a bearing of 0 degrees (due north) from
Dallas.  The other FMUFs around the DX Compass are for bearings in steps of 30
degrees.

                                     -21-









Sunrise: 1346 UTC                     FMUF           Radiation Angle:  1.5 deg
Sunset:  2326 UTC                                        Sunspot Number: 114.0
Omaha                                 13.2                   Solar Flux: 158.3

                          12.1                    15.9


                     11.9                              19.8


                                    1346 UTC
                  13.3         41.25 N   95.93 W         25.3
                                   01-25-1990


                     15.6                              26.9


                          18.6                    24.9

                                      22.2

DX Compass for what UTC (e.g., 0215) (or <RTN> to quit)?


     The displayed values of FMUF are an indication of the highest-frequency
bands that can be expected to be open to DX on either a short or long great-
circle path in the different directions around the compass from Terminal A.  In
this example, 10 meters is not yet open in any direction at the time of
sunrise.  15 meters would be expected to be open, with a probability exceeding
50 percent, to DX on bearings between 90 and 180 degrees from Omaha.  20 meters
would be expected to be open on bearings of 30 degrees, through south, to 240
degrees.  20 meters would not yet be open from 300 through 360 degrees, but 40
meters (and 30 meters) would be expected to be open in these directions.  Keep
in mind that the predicted values of only the FMUF are shown, so you cannot
tell, from the DX Compass alone, how strong the received signals might be.
However, the first band lower in frequency than the indicated FMUF will
probably be usable for working DX.

     A different interpretation of the compass display applies when Terminal A
is at either the north or south pole.  Instead of compass bearings, the twelve
positions around the "circle" represent meridian longitudes measured west from
the prime meridian.  For example, the FMUF shown in the 30-degrees position
would be the maximum FMUF to be expected on a path from the pole along the 30-
degree west meridian.

     The time prompt appears again at the bottom of the screen.  You can enter
additional times to see how the expected band openings shift during the day.
Press only <ENTER> or <RETURN> when you want to quit and return to the MINIPROP
master menu.






                                     -22-









6. Changing Prediction Parameters (Master Menu Choice 3)
--------------------------------------------------------

     There are several default (preset) values and settings (e.g., frequencies)
used in the MINIPROP predictions.  Five of these can be changed by the user.
In addition, you can restore the original set of MINIPROP default values and
settings.  If you make any changes, you will be given the chance to save them
in the MP.DEF file of default settings upon returning to the master menu.  Your
settings will then be in effect each time you use MINIPROP.  If you do not save
your changes, they will remain in effect only during the current MINIPROP
session.
     To change any of the defaults, first start MINIPROP by entering "MP"
following the > prompt from your computer's operating system.  When the
MINIPROP master menu appears on the screen, enter the number "3".  The
following Defaults Change Menu will appear on the screen.


                             DEFAULTS CHANGE MENU

           0. Return to MASTER MENU
           1. Change frequencies used in signal level predictions
           2. Change antenna minimum radiation angle used in predictions
           3. Suppress output of low signal levels
           4. Suppress output of signal levels at frequencies
              higher than predicted FMUF
           5. Change path (short or long) to be computed first
           6. Restore original set of MINIPROP defaults

                    Your choice :

To make your choice, enter a number, 0 to 6.  Choice 0 will return you to the
MINIPROP Master Menu.  Choices 1 through 6 are explained in the following
sections.

     Change Frequencies Used in Signal Level Predictions
     ---------------------------------------------------

     In the MINIPROP propagation predictions described above in Section 4,
signal levels are predicted for frequencies of 3.6, 7.1, 14.1, 21.2, and 28.3
MHz.  You may change these frequencies to any combination of five frequencies
between 3 and 30 MHz.  This will allow you to obtain signal level predictions
for frequencies in the 12-, 17-, or 30-meter bands or in the shortwave
broadcast bands, for example.

     The frequencies currently in effect will be displayed.  You will then be
asked if you want to change the frequencies.  If you answer "N" (without the
quotes), the Defaults Change Menu will reappear.  If you enter "Y", the
following (top of next page) will appear.








                                     -23-









         You may enter 0 to 5 frequencies between 3 and 30 MHz.
         If you do not enter at least one frequency, signal levels
         will not be included in the predictions.

         Enter your frequencies, if any, one at a time.
         Press only <ENTER> or <RETURN> when finished.

         Frequency 1 :

     Press only <ENTER> or <RETURN> if you do not want signal levels to appear
in the predictions; this will save time when running predictions if you are
only interested in the FMUF and ECOF predictions.  If you do want signal levels
to appear, enter one to five frequencies, one at a time.  You may enter them in
any order; MINIPROP will place them in numerical order and will round them to
the nearest 0.1 MHz.  Duplicate frequencies will be rejected.  If you want to
enter less than five frequencies, press only <ENTER> or <RETURN> when asked for
the next frequency.

     MINIPROP will display the new frequencies that are now in effect and will
ask you if you want to change them.  If you are not satisfied with the
frequencies, enter "Y" and you will again be asked to enter your frequencies.
When you are satisfied with the displayed frequencies, enter "N" and the
Defaults Change Menu will reappear.  You may select other default parameters
that you want to change, or you may choose to return to the MINIPROP Master
Menu.  If you make the latter choice, and you have changed any of the defaults,
you will be given the opportunity to save your changes in the MP.DEF defaults
file before the MINIPROP Master Menu is reloaded.

     Change Antenna Minimum Radiation Angle Used in Predictions
     ----------------------------------------------------------

     The minimum usable antenna radiation (take-off) angle depends primarily
upon antenna heights and horizon obstructions.  In both the propagation
predictions and the DX Compass, MINIPROP assumes this minimum angle to be 1.5
degrees unless you change it.  You may change the antenna minimum radiation
angle to any value between 0 and 45 degrees.  MINIPROP uses this value to
determine the minimum number of F hops required on a given path, and then
computes the actual antenna radiation angle from the resulting path geometry.
If you specify too great a radiation angle, the number of hops on a given path
may be excessive.  In this case, a screen message will advise you that the
prediction computation has been aborted.

     The antenna minimum radiation angle currently in effect will be displayed.
You will then be asked if you want to change the angle.  If you answer "N", the
Defaults Change Menu will reappear.  If you enter "Y", you will be asked to
enter an angle between 0 and 45 degrees.

     MINIPROP will display the new antenna minimum radiation angle that is now
in effect and will ask you if you want to change it.  If you are not satisfied
with the value, enter "Y" and you will again be asked to enter an angle.  When
you are satisfied with the displayed angle, enter "N" and the Defaults Change
Menu will reappear.  You may select other default parameters that you want to
change, or you may choose to return to the MINIPROP Master Menu.  If you make
the latter choice, and you have changed any of the defaults, you will be given
the opportunity to save your changes in the MP.DEF defaults file before the

                                     -24-









MINIPROP Master Menu is reloaded.

     Suppress Output of Low Signal Levels
     ------------------------------------

     In the discussion of the prediction example in Section 4, it was stated
that signal levels below -20 dB with respect to 0.5 microvolt are normally not
displayed or sent to the printer because weaker signals are generally unusable
by radio amateurs.  However, listeners to shortwave broadcasting stations that
use high power and high-gain antennas might find it desirable to use a lower
threshold which, after correction for the power and antenna gain, might result
in a usable received signal strength.  You may set the suppression threshold to
0, -20, -40, or -60 dB according to your needs, or you may completely eliminate
suppression of the output of low signal levels.

     The suppression level currently in effect will be displayed.  You will
then be asked if you want to change the suppression threshold.  If you answer
"N", the Defaults Change Menu will reappear.  If you enter "Y", the following
will appear.

         A  Do not show signal levels that are below 0 dB
            with respect to 0.5 microvolt.

         B  Do not show signal levels that are below -20 dB
            with respect to 0.5 microvolt. (Default)

         C  Do not show signal levels that are below -40 dB
            with respect to 0.5 microvolt.

         D  Do not show signal levels that are below -60 dB
            with respect to 0.5 microvolt.

         E  Do not suppress output of low signal levels.

            Your choice :

To make your choice, enter a letter, A through E.

     MINIPROP will display the new suppression threshold that is now in effect
and will ask you if you want to change it.  If you are not satisfied with the
threshold, enter "Y" and you will again be asked to enter your choice of A
through E.  When you are satisfied with the new threshold, enter "N" and the
Defaults Change Menu will reappear.  You may select other default parameters
that you want to change, or you may choose to return to the MINIPROP Master
Menu.  If you make the latter choice, and you have changed any of the defaults,
you will be given the opportunity to save your changes in the MP.DEF defaults
file before the MINIPROP Master Menu is reloaded.


     Suppress Output of Signal Levels at Frequencies Higher than Predicted FMUF
     --------------------------------------------------------------------------

     Signal level predictions are normally suppressed for frequencies greater
than 150 percent of the predicted FMUF, but you may cancel this suppression.
This is a toggle; the suppression is either on or off.

                                     -25-









     The  current setting of the toggle will be displayed.  You will then be
asked if you want to change the setting to the other state.  If you answer "N",
the Defaults Change Menu will reappear.  If you enter "Y", the setting will be
reversed.

     MINIPROP will display the new toggle setting that is now in effect and
will ask you if you want to change it.  If you are not satisfied with the
setting, enter "Y" and the setting will again be reversed.  When you are
satisfied with the toggle setting, enter "N" and the Defaults Change Menu will
reappear.  You may select other default parameters that you want to change, or
you may choose to return to the MINIPROP Master Menu.  If you make the latter
choice, and you have changed any of the defaults, you will be given the
opportunity to save your changes in the MP.DEF defaults file before the
MINIPROP Master Menu is reloaded.

     Change Path (Short or Long) to be Computed First
     ------------------------------------------------

     Short-path predictions are normally computed first, long-path second.  You
may reverse this order.  This is a time saver if you need only the long-path
prediction.  This a toggle.

     The  current setting of the toggle will be displayed.  You will then be
asked if you want to reverse the setting.  If you answer "N", the Defaults
Change Menu will reappear.  If you enter "Y", the setting will be reversed.

     MINIPROP will display the new toggle setting that is now in effect and
will ask you if you want to change it.  If you are not satisfied with the
setting, enter "Y" and the setting will again be reversed.  When you are
satisfied with the toggle setting, enter "N" and the Defaults Change Menu will
reappear.  You may select other default parameters that you want to change, or
you may choose to return to the MINIPROP Master Menu.  If you make the latter
choice, and you have changed any of the defaults, you will be given the
opportunity to save your changes in the MP.DEF defaults file before the
MINIPROP Master Menu is reloaded.

     Restore Original Set of MINIPROP Defaults
     -----------------------------------------

     The original set of defaults built into MINIPROP are:

          Prediction frequencies of 3.6, 7.1, 14.1, 21.2, and 28.3 MHz

          Antenna minimum elevation angle of 1.5 degrees

          Suppression threshold for low signal levels at -20 dB

          Output of signal levels suppressed for frequencies higher
          than 150% of FMUF

          Short-path predictions computed before long-path predictions

     You will be asked if you want to restore this set of defaults.  If you
answer "N", the Defaults Change Menu will reappear.  You may select other
default parameters that you want to change, or you may choose to return to the

                                     -26-









MINIPROP Master Menu.  If you enter "Y", the original settings will be restored
for the current MINIPROP session, and you will be asked to press any key before
returning to the Defaults Change Menu.  You may then select other default
parameters that you want to change, or you may choose to return to the MINIPROP
Master Menu at which time you will be given the opportunity to save your
changes in the MP.DEF defaults file before the MINIPROP Master Menu is
reloaded.

















































                                     -27-









7. MINIPROP Utilities (Master Menu Choice 4)
--------------------------------------------

     When you select Master Menu choice 4, the following MINIPROP Utilities
menu will appear.

                           MINIPROP (TM) UTILITIES

             0.  Exit from MINIPROP (Quit)
             1.  Return to MASTER MENU
             2.  Create or modify Terminal A default
             3.  Display entries in MINIPROP atlas
             4.  Add, modify, or delete entry in MINIPROP atlas
             5.  Display MINIPROP documentation on screen
             6.  Send MINIPROP documentation to printer
             7.  Print table of great-circle bearings
             8.  Convert version 1 MINIPROP.ATL to version 2 MP.ATL

                      Your choice :

     Use choice 0 to quit MINIPROP without first returning to the Master Menu.
To return to the MINIPROP Master Menu, use choice 1.  Choices 2 through 8 are
discussed in the following sections.

8. Create or Modify Terminal A Default (MINIPROP Utilities Choice 2)
--------------------------------------------------------------------

     There is probably a location you will use most often as one of the
terminals when running a MINIPROP prediction.  This utility allows you to save
the latitude, longitude, and name of this location as the Terminal A default.
Then when you want to use this location in a MINIPROP prediction or in the DX
Compass, it will only be necessary to press <ENTER> or <RETURN> when you are
prompted for the latitude of Terminal A; you will not have to enter the
latitude, longitude, and name  each time.  The Terminal A Default is saved on
your disk in the MP.DEF file (the same file that holds the default values of
several of the prediction parameters).

     When you select choice 2 on the MINIPROP Utilities menu, the latitude,
longitude, and name of any existing Terminal A default location will be
displayed.  Then you will be directed to enter your desired Terminal A default.
Enter the latitude, longitude and name the same as you would enter them
manually when running a MINIPROP prediction (Section 4 above).  When you have
finished making these entries, they will be repeated back on the screen, and
you will be asked if they are correct.  If you want to make any corrections,
answer "N".  In this case, you will again be asked to enter the latitude,
longitude, and name.  When the displayed entries are correct, answer "Y".  You
will then be asked to confirm that you want the entries saved in the MP.DEF
defaults file.  If you do want them saved, answer "Y"; but if you want to abort
the creation or change of the Terminal A default location, answer "N".

     You will be directed to press any key to continue, and the MINIPROP
Utilities menu will reappear.




                                     -28-









9. Display Entries in MINIPROP Atlas (MINIPROP Utilities Choice 3)
------------------------------------------------------------------

     This choice allows you to view all of the entries in the MINIPROP atlas.
The entries will appear in alphabetical order of the prefix.  (ASCII
alphabetization is used.  Numerals precede letters.  The numeral 0 precedes the
numeral 1.)  The prefix, latitude, longitude, and name will be displayed for
each entry.  The scrolling of the display will stop after every 20 entries; to
continue, press any key.  The total number of atlas entries will be displayed
after the last atlas entry.  If you want to terminate the atlas display before
the last entry is reached, press Control-X (Hold down the CONTROL key; then
type "X".).

10. Add, Modify or Delete Entry in MINIPROP Atlas (MINIPROP Utilities Choice 4)
-------------------------------------------------------------------------------

     You may add, modify, or delete entries in the MINIPROP atlas.  The only
limit on the number of atlas entries is the capacity of your disk.  When you
select this utility from the MINIPROP Utilities menu, the following message and
list of edit choices will appear on your screen.

         You will be given a chance to abort before any change is made
         in the atlas.

                          <A>dd an entry
                          <M>odify an entry
                          <D>elete an entry
                          <R>eturn to utilities menu

                           Your choice :

     Enter "A", "M", or "D" to add, modify, or delete an atlas entry.  The list
of available edit choices will reappear after each addition, modification, or
deletion.  Enter "R" to return to the MINIPROP Utilities menu.

     Adding an Atlas Entry
     ---------------------

     You will first be asked for the prefix to be added to the atlas.  Prefixes
may contain from one to six characters.  Leading, trailing, and embedded spaces
are not allowed, and you will not be allowed to enter an all-numeric prefix.
Country prefixes, call area prefixes, station call signs, or any other unique
identifier may be used.  Letters may be entered in either upper or lower case;
MINIPROP will convert all letters of a prefix to upper case before the entry is
made in the atlas.

     MINIPROP will check to make sure the new prefix is not already in the
atlas; if it is not, you will be asked to enter the latitude, longitude, and
name for the new entry.  Enter these in the same manner as they are manually
entered when you run a MINIPROP prediction (Section 4 above).  The latitude and
longitude may be entered as a decimal or in deg min sec format.  North
latitudes and west longitudes are positive (with no plus sign); south and east
are negative (with a minus sign).  Latitudes greater than 90 degrees in
magnitude, and longitudes greater than 360 degrees in magnitude, will not be
accepted.  Names may not exceed 17 characters in length, and may contain any

                                     -29-









combination of characters.  You might want to look at some examples in the
atlas; use choice 4 in the MINIPROP Utilities menu.

     After you have entered the name, your new atlas entry will be repeated
back on the screen, and you will be asked if it is correct.  If you want to
make any corrections, answer "N".  In this case, you will again be asked to
enter the prefix, latitude, longitude, and name.  When the displayed entry is
correct, answer "Y".  You will then be asked to confirm that you want the entry
put in the MINIPROP atlas file.  If you do want the entry put in the atlas
file, answer "Y"; but if you want to abort the addition to the atlas, answer
"N".  You will then be given the choice of adding, modifying, or deleting
another atlas entry or returning to the MINIPROP Utilities menu.

     Modifying an Atlas Entry
     ------------------------

     You will be asked for the prefix of the atlas entry that you want to
modify.  MINIPROP will then display the current contents of that entry, and you
will be asked to enter your changes.  If you do not want to change an item
(prefix, latitude, longitude, or name) within an entry, just press <ENTER> or
<RETURN> and the current contents for that item will appear on the screen.
When you do want to change an item, enter your desired contents for that item.
After the name is entered, the modified atlas entry will be repeated back on
the screen, and you will be asked if it is correct.  If you answer "N", the
modification will be aborted.  If the displayed entry is correct, answer "Y".
You will then be asked to confirm that you want the modified entry put in the
MINIPROP atlas file.  If you do want the modified entry put in the atlas file,
answer "Y"; but if you want to abort the modification, answer "N".  You will
then be given the choice of adding, modifying, or deleting another atlas entry
or returning to the MINIPROP Utilities menu.

     Deleting an Atlas Entry
     -----------------------

     You will be asked for the prefix of the atlas entry that you want to
delete.  MINIPROP will then display the contents of that entry, and you will be
asked to confirm that you want the entry deleted.  If you do want the entry
deleted from the atlas file, answer "Y"; but if you want to abort the deletion,
answer "N".  You will then be given the choice of adding, modifying, or
deleting another atlas entry or returning to the MINIPROP Utilities menu.

11. Display MINIPROP Documentation on Screen (MINIPROP Utilities Choice 5)
--------------------------------------------------------------------------

     Use this choice in the MINIPROP Utilities menu if you want to read this
documentation on the screen.  The page number at the bottom of each page will
not appear on the screen, and where the documentation contains multiple
adjacent blank lines, only one blank line will appear on the screen.  The last
line of documentation on each screen will be repeated at the top of the next
screen.  The scrolling of the display will stop after every 22 lines; to
continue, press any key.  This documentation is lengthy, so it will take a
while to read it all.  If you want to terminate before the end of the
documentation is reached, press Control-X (Hold down the CONTROL key; then type
"X".).


                                     -30-









12. Send MINIPROP Documentation to Printer (MINIPROP Utilities Choice 6)
------------------------------------------------------------------------

     When you make this choice in the MINIPROP Utilities menu, the following
instructions will appear on the screen.

         Please turn on your printer and set it for 80 characters per
         line and 66 lines per page.  Adjust the paper so printing
         can start within 10 lines from the top of the page.  There
         will be as many as 57 printed lines on each page.

         Press any key when printer is ready.

     Just follow these instructions.  The documentation is lengthy, so be sure
there is plenty of paper in your printer.  (The total number of pages will
appear at the bottom of the first page.)  Printing will begin when you press
any key.  You may interrupt printing (and return to the MINIPROP Utilities
menu) by pressing Control-X.

13. Print Table of Great-Circle Bearings (MINIPROP Utilities Choice 7)
----------------------------------------------------------------------

     This choice in the MINIPROP Utilities menu allows you to print a
customized table of great-circle bearings (beam headings) from any location
(Terminal A) to all of the locations in the MINIPROP atlas.

     If you have saved a Terminal A default location in the MP.DEF defaults
file, you will be asked if you want the bearings to be from the default
location.  If you answer "N", or if their is no default location in the
defaults file, you will be asked to enter the latitude, longitude, and name of
Terminal A.  Enter these as described in Section 4.

     You will now be asked for information needed by MINIPROP to optimize the
printing of the table by your printer.  You will be asked first for the number
of lines per page (form length) for your printer with the paper you will be
using.  (66 lines per page is standard in the U.S.)  You will be asked next for
the maximum number of characters that your printer will print on one line.
Then you will be given the opportunity to send any control codes that may be
required to configure your printer.  But first turn on your printer and adjust
the paper so printing can start 4 to 6 lines from the top of the page.  Press
any key when ready.

     Now enter the number of lines per page (form length) for your printer with
the paper you will be using.  This value must be an integer between 48 and 126.
The U.S. standard of 66 lines per page will allow 52 bearings to be printed in
each column.

     The heading and first few entries of a column in the printed table might
look like this:

                         PREFIX LOCATION          DEG
                         1A0    S.M.O. of Malta    34
                         1S     Spratly Is.       302
                         3A     Monaco             36


                                     -31-









The number of pages required to hold the table of great-circle bearings depends
upon the number of characters that your printer can print on one line.  A
larger number of characters per line will allow a larger number of columns on a
page, and fewer pages will be needed to hold the complete table.  A table will
appear on the screen showing how the maximum number of characters per line
affects the number of columns of great-circle bearings that will be printed on
each page and the number of pages that will be required.  If your printer
prints 80 characters on a line, only two columns will fit on a page.  If your
printer has more than one character width, you will probably want to specify
the number of characters corresponding to the narrowest character width.  For
example, an OKIDATA ML92 printer can print 80 characters per line at 10
characters per inch (cpi), 96 at 12 cpi, and 136 at 17.1 cpi.  The best choice
is 136; this allows four columns to be printed on each page.  Be sure to
specify an exact, instead of approximate, number of characters per line so
MINIPROP can center the columns correctly on the page.

     You will next be asked if you want to send control codes to your printer.
Control codes are special non-printable codes -- usually numbered 1 through 31
(decimal) -- that tell your printer to change the way it prints.  For example,
control code 29 must be sent to the ML92 printer in the above example to cause
it to switch to 136 characters per line. Control code 27 is often combined with
other codes into what are called "escape sequences".  Your printer user's
manual will tell you what control codes or escape sequences, if any, are needed
to set up your printer for the number of characters per line you have
specified, to choose a type style, or for another purpose.  If you answer "N"
(you do not want to send control codes), printing will begin.  If you answer
"Y" (you want to send control codes), you will be directed to enter the first
control code followed by <ENTER> or <RETURN>.  Enter the integer decimal value
of the first code you want sent.  MINIPROP will send the code to your printer
and will ask you for another control code.  Enter as many codes as are required
by your printer.  Press only <ENTER> or <RETURN> to tell MINIPROP you are
finished.  Printing will begin.  You may interrupt printing (and return to the
MINIPROP Utilities menu) by pressing Control-X.

     The entries in the printed table will appear in alphabetical order of the
prefix.  (ASCII alphabetization is used.  Numerals precede letters.  The
numeral 0 precedes the numeral 1.)  The bearings are measured in degrees east
of north, and are in the range 0 through 359 degrees.  However, if Terminal A
is at either the north or south pole, the west longitudes (0 through 359
degrees) of  the atlas entries are printed in the DEG column.  Three asterisks
(***) are printed in the DEG column when Terminal A and an atlas entry are co-
located or when Terminal A and the atlas entry are antipodes.

14. Convert Version 1 MINIPROP.ATL to Version 2 MP.ATL
------------------------------------------------------
    (MINIPROP Utilities Choice 8)
    -----------------------------

     An atlas file containing latitudes and longitudes for all DXCC countries
and several additional geographic locations is supplied with this version of
MINIPROP.  If you already have such an atlas, named MINIPROP.ATL, that you used
with MINIPROP version 1, you can use it with version 2 but its internal format
must be changed before it can be read by the new version of MINIPROP.  This
utility will do the conversion for you.


                                     -32-









       MINIPROP will look for your MINIPROP.ATL file on the logged disk drive
and in the current directory that should also contain the MINIPROP version 2
files. The new atlas file will be created in the same directory and will be
named MP.ATL.  The new MP.ATL will occupy somewhat more disk space than does
your MINIPROP.ATL file; be sure there is enough space for it on your disk.  Any
existing file named MP.ATL will be renamed to MPBACKUP.ATL, and any existing
file named MPBACKUP.ATL will be erased. Your MINIPROP.ATL file will remain
intact.  The conversion will abort if your atlas contains more than 800 entries
or an invalid latitude or longitude, or if a prefix contains leading, trailing,
or embedded spaces, is longer than six characters, or is all-numeric.

     When you select this utility, you will be asked if you want to proceed
with the conversion.  Answer "N" if you want to abort the conversion.  The
atlas will be converted if you answer "Y".  The conversion may take a while if
you have a large atlas or a slow disk drive.

15. References
--------------

1. National Bureau of Standards, "Ionospheric Radio Propagation", Circular 462,
1948.

2. Davies, K., "Ionospheric Radio Propagation", National Bureau of Standards
Monograph 80, 1965.

3. Lucas, D.L., and Haydon, G.W., "Predicting Statistical Performance Indexes
for High Frequency Ionospheric Telecommunication Systems", Technical Report
ITSA-1, Institute for Telecommunication Sciences and Aeronomy, Environmental
Science Services Administration, 1966.

4. Barghausen, A.F., Finney, J.W., Proctor, L.L., and Schultz, L.D.,
"Predicting Long-Term Operational Parameters of High-Frequency Sky-Wave
Telecommunication Systems", Technical Report ERL 110-ITS 78, Institute for
Telecommunication Sciences, Environmental Science Services Administration,
1969.

5. National Bureau of Standards, "Handbook for CRPL Ionospheric Predictions
Based on Numerical Methods of Mapping", Handbook 90, 1962.

6. Leftin, M., "The Estimation of Maximum Usable Frequencies from World Maps of
MUF(ZERO)F2, MUF(4000)F2 and MUF(2000)E", Telecommunications Research and
Engineering Report 13, Institute for Telecommunication Sciences, Office of
Telecommunications, 1971.

7. Rose, R.B., Martin, J.N., and Levine, P.H., "MINIMUF-3: A Simplified HF MUF
Prediction Algorithm", Technical Report 186, Naval Ocean Systems Center, 1978.

8. Rose, R.B., and Martin, J.N., "MINIMUF-3.5: Improved Version of MINIMUF-3, A
Simplified HF MUF Prediction Algorithm", Technical Document 201, Naval Ocean
Systems Center, 1978.

9. Rose, R.B., "MINIMUF: A Simplified MUF-Predicting Program for
Microcomputers", pp. 36-38, QST, December, 1982.



                                     -33-









10. Shallon, S.C., "MINIMUF for Polar Paths", p. 48 (Technical Correspondence),
QST, October, 1983.

11. Rose, R.B., "MINIMUF Revisited", p. 46 (Technical Correspondence), QST,
March, 1984.

12. Fricker, R., "A Microcomputer Program for the Critical Frequency and Height
of the F Layer of the Ionosphere", pp. 546-550, Fourth International Conference
on Antennas and Propagation, Institution of Electrical Engineers (UK), 1985.

13. Fricker, R., "A Microcomputer Method for Predicting the Field Strengths of
HF Broadcast Transmissions", to be published.

14. International Radio Consultative Committee, "CCIR Atlas of ionospheric
characteristics", Report 340, International Telecommunication Union, Geneva,
1983.

15. Jacobs, G. and Cohen, T.J., "The Shortwave Propagation Handbook", 2nd ed.,
CQ Publishing Inc., 1982.

16. "The 1987 ARRL Handbook for the Radio Amateur",  64th ed., American Radio
Relay League, 1986.


































                                     -34-









r, 1983.

11. Rose, R.B., "MINIMUF Revisited", p. 46 (Technical Correspondence), QST,
March, 1984.

12. Fricker, R., "A Microcomputer Program for the Critical Frequency and Height
of the F Layer of the Ionosphere", pp. 546-550, Fourth International Conference
on Antennas and Propagation, Institution of Electrical Engineers (UK), 1985.

13. Fricker, R., "A Microcomputer Method for Predicting the Field Strengths of
HF Broadcast Transmissions", to be published.

14. International Radio Consultative Committee, "CCIR Atlas of ionospheric
characteristics", Report 340, International Telecommunication Union, Geneva,
1983.

15. Jacobs, G. and Cohen, T.J., "The Shortwave Propagation Handbook", 2nd ed.,
CQ Publishing Inc., 1982.

16. "The 1987 ARRL Handbook for the Radio Amateur",  64th ed., American Radio
Relay League, 1986.


































                                     -34-









r, 1983.

11. Rose, R.B., "MINIMUF Revisited", p. 46 (Technical Correspondence), QST,
March, 1984.

12. Fricker, R., "A Microcomputer Program for the Critical Frequency and Height
of the F Layer of the Ionosphere", pp. 546-550, Fourth International Conference
on Antennas and Propagation, Institution of Electrical Engineers (UK), 1985.

13. Fricker, R., "A Microcomputer Method for Predicting the Field Strengths of
HF Broadcast Transmissions", to be published.

14. International Radio Consultative Committee, "CCIR Atlas of ionospheric
characteristics", Report 340, International Telecommunication Union, Geneva,
1983.

1