PACK-PRO
 
                   Multimode Communications Program
 
                                  for
 
 
                 PC Compatibles and the Kantronics KAM
 
                              Version 1.1
 
 
 
                (c)Copyright 1991, Andrew C. Manti Jr.
 
 
 
 
         This program and documentation are protected under United
         States Copyright Laws and as such cannot be sold or in any
         way distributed for profit without the prior written consent
         of the author.  While you may distribute this program through
         bulletin board systems, it must be distributed unmodified and
         without charge of any kind.  As every possible use of this
         program cannot be forseen, PACK-PRO is provided as-is, and
         without warrantee of any kind.
 
 


 
                        SHAREWARE REGISTRATION
 
 
         PACK-PRO is distributed as a Shareware product, meaning that
         you have the opportunity to try the program before buying it.
         You are free to copy and redistribute the entire file to
         friends or other bulletin board systems as long as the files
         are not modified in any way and no fee is charged. If, after
         trying this program you feel it is of value to you, then you
         are asked to pay the registration fee of $20 (US) plus
         applicable sales tax if you are a Massachusetts resident.
 
         Your registration fee will guarantee you telephone support as
         well as a copy of the next release of PACK-PRO.  Releases
         beyond the next will be made available to you at special
         upgrade rates.
 
         As you can imagine, your registration fee does NOT make me a
         rich man, but rather helps defray the costs of further
         program development and distribution. (Disks, Paper, Postage,
         etc).  If for any reason you can not afford the $20, send
         what you can afford.  You will still be registered, receive
         phone support, and be able to obtain updates to the program
         at much reduced rates. If nothing else, send me your comments
         so that I can use them to make PACK-PRO an even better
         program.
 
         Please use the registration form at the end of this document
         or in the file REGFORM.DOC to register you copy.
 
         Thank you for your support!
 
                       Andrew C. Manti Jr.   W1VL
                              2 Deana Road
                            Methuen MA 01844
 
 

 PACK-PRO         Pg 1.
 
                             INTRODUCTION
 
 
         PACK-PRO is a multimode communications program designed for
         use with IBM PCs and compatibles and the Kantronics KAM, all
         mode TNC.  The program is designed to take the work out of
         using the KAM by providing a user friendly interface for all
         modes except WEFAX.  The program will run on floppy or a hard
         disk and requires a minimum of 384K of memory.  An Epson or
         IBM compatible printer is required if you intend to use the copy
         to print option.  Both color and monochrome monitors are
         supported.  The main features of this program are as
         follows:
 
              - Operates on COM1 or COM2 of your PC
              - Modes: VHF/HF Packet, RTTY, AMTOR, CW, NAVTEX, ASCII
              - Split screen display
              - Brag file for RTTY/AMTOR
              - Unlimited nine (80 characters each) message files
              - Text Editor for files up to 300 lines in length
              - Screen review (last 6 screens)
              - ASCII Text file transmission
              - Automatic CQ generator with auto answer detection
              - Automatic SELCAL generation from inputed call
              - Capture to Disk capability
              - Automatic unattended mail capture for packet
              - Routing file capability
              - Multiple Monitor modes for packet
              - Hot key selectable baud rates and shifts
              - ASCII file upload/download capability for packet
              - Script capability for packet multiple node connects
              - Contest capability with serial number generator
              - Toggles for :
                         - RTTY/ASCII/AMTOR tone selection
                         - DX CQ's
                         - Time Stamp for Packet
                         - Packet Beacons
                         - Mail Capture
                         - Auto capture to disk of all packet connects
                         - Local Echo
                         - Capture to printer
 
  

PACK-PRO         Pg 2.
 
                                SET-UP
 
 
         Initial set up of PACK-PRO is very straightforward. The
         program can be run from either floppy or a hard disk. Just
         copy the files on the distribution disk to your working
         floppy or a hard disk directory. The only other action
         required is the set up of the PPACK.SYS file.  This file is
         used to initialize both the KAM and the program to your
         requirements.  A sample PPACK.SYS file is included to aid in
         setting up your own.  You may generate this file using any
         word processor which is capable of generating true ASCII
         files or by using the built in text editor feature of PACK-
         PRO. You invoke PACK-PRO with the dos command:
 
                            PACK_PRO <ENTER>
 
         NOTE: THIS WILL BRING THE PROGRAM UP IN COLOR, IF YOU ARE
                USING A MONOCHROME OR B/W MONITOR, TYPE:
 
                          PACK_PRO M <ENTER>.
 
 
         The inital shareware screen will appear. Entering the letter
         <E> at this point will take you immediately to the PACK-PRO
         editor.  Any other key will load and execute PACK_PRO.  To
         edit or create the PPACK.SYS file enter 'E' and then enter
         the filename PPACK.SYS at the prompt.  You will then be in
         editor mode.  Pressing <F1> while in the editor will give you
         a help file showing the various editing keys you may use.


PACK-PRO         Pg 3.
 
         The PPACK.SYS file MUST be set up in a specific format for
         the program to function properly. This format is as follows:
 
         Line #1      Your Call
         Line #2      Your AMTOR SELCAL
         Line #3      Drive Identifier for all Msg files (Drive Letter
                      Only  i.e  A B C D etc)
         Line #4      CQ_Delay in Seconds (Time to wait before
                      repeating auto CQ's).
         Line #5      Your QTH
         Line #6      Text for Beacons (up to 80 characters)
         Line #7      Communications port number (1,2,etc)
         Line #8      Terminal to TNC baud rate code as follows:
 
                              0  -  110 baud
                              1  -  150 baud
                              2  -  300 baud
                              3  -  600 baud
                              4  -  1200 baud
                              5  -  2400 baud
                              6  -  4800 baud
                              7  -  9600 baud
                          (Note that most TNC's may not run reliably
                           at over 1200 baud)
         Line #9      Number of stop bits (1,2)
         Line #10     Number of Data Bits (7,8)
         Line #11     Parity code as follows:
 
                              0  -  None
                              1  -  Odd
                              2  -  None
                              3  -  Even
 
         Line #12     Number of times to repeat CQ text in auto mode
         Line #13     BBS Read Message Command (usually RM)
         Line #14     Default start up CW speed (default is 13 WPM)
         Line #15     Next Sequential Serial Number (Prog will update
                      this number automatically each time you exit.
         Line #16    Additional TNC Start up commands go on this line
                      and any following. (Line #16 must be present)
 
         NOTE: All lines must be included and must end with a carriage
               return (<ENTER>).  If you do not wish to use a specific
               line just leave a blank line in its place.
 
               It is assumed that your TNC has already been set up for
               the proper baud rate etc and that these values have
               been PERMed.  (See your TNC manual for more
               information).
 
         Review the included PPACK.SYS file as an example. Be sure to
         change the calls and QTH information before running the
         program.
 

PACK-PRO         Pg 4.
 
                      OTHER PROGRAM RELATED FILES
 
 
         The PPACK.SYS file as mentioned above is the only file
         required to run PACK-PRO.  However, additional files will be
         needed if you wish to fully utilize all the features of the
         program.  These files can be created with an ASCII editor
         before you begin running PACK-PRO or by using the built in
         editor.  These additional files are:
 
            BRAG.MSG  - Brag file (usually contains information on
                                   your station and equipment. Used
                                   extensively on RTTY and AMTOR.)
 
            *.MSG     - Message files used with the auto message send
                        option.  These files can each contain up to
                        nine (9) message lines of up to 78 characters
                        each.  Each line must end with a carriage
                        return.  These are very easily constructed
                        using the built in Create Message Option.
                        These messages are great for CW or for
                        contesting.  They may contain special
                        characters as outlined in the MAKE MESSAGE
                        option description later in this document.
 
            CALL_LST.SYS - This is a PATH file for packet use. This
                        file, again generated by an ASCII editor or
                        the built in editor, includes preset paths to
                        specific stations.  The format of this file is
                        as follows:
 
                           Station Path <CR>
 
                        Be sure to leave ONE (1) space between the
                        station name and the path.  DO NOT put any
                        spaces in the station name. For example, if
                        the path to W1AW is W1AW V EMAS1,WRI,CCONN
                        then the associated line in the CALL_LST.SYS
                        file would be:
 
                         W1AW W1AW V EMAS1,WRI,CCONN <CR>
 
                        With this file you only need enter the station
                        name and the program will automatically look
                        up and connect via the path you have
                        established.  Note the use of commas to
                        separate the digipeaters in the path. Keep in
                        mind that the station name need not be call
                        letters. You may use any name you feel like.
                        If it is easier to remember JOHN rather than
                        John's call, use JOHN for the station name.
                        Then every time you wish to connect to John,
                        just enter his name as the call.


PACK-PRO         Pg 5.
 
                        This file may be as long as desired, but each
                        line must be less than 80 characters in
                        length.  The call of the station you wish to
                        work must be entered using the <F5> Enter Call
                        option and called using the <Alt><F4> Make
                        First Call option, both of which are described
                        later in this document.
 
              CAPTURE.TXT - This is the capture to disk file. If
                        Capture to Disk is enabled, it will contain a
                        copy of all information which is displayed on
                        the screen.  The program will create this file
                        automatically.  Keep in mind that you may want
                        to edit or delete this file on occasion as it
                        can become very big, very fast.
 
              MESSAGE.00x - These files, also created by the program
                        as needed, is where all <Ctrl><F4> option,
                        automatically captured packet mail will be
                        put.  All messages obtained with the Auto Mail
                        Capture option will be copied to this file,
                        one after the other.  Again you may want to
                        review these files on occasion and delete or
                        edit them.  Each time new mail is received the
                        .00x is incremented.
 
              *.SCR  -  These are script files for use in packet
                        modes. These script files are for use when
                        connecting to another station through a series
                        of nodes.  This differs from digipeaters and
                        the CALL_LST.SYS file in that nodes commonly
                        require you to connect to each individually.
                        The script file which can have any name
                        (extension must be .SCR) is merely an ASCII
                        file of exactly what you would type to perform
                        the connect.  For example, to connect to W1VL
                        through the nodes SNH, EMASS, and port 4 of
                        METK the script file would look like this:
 
                             C SNH
                             C EMASS
                             C 4 W1VL V METK
 
                        Note that each line ends with a carriage
                        return and only one connect command per line.
                        These files also can be generated with any
                        ASCII text editor or the PACK-PRO editor.
 
    

PACK-PRO         Pg 6.
 
                             SPLIT SCREEN DISPLAY
 
 
         PACK-PRO operates with a "split-screen" display.  This means
         that information coming from the TNC to the computer is
         displayed in the top or receive section of the screen, while
         data which you type or is sent from the computer to the TNC,
         will appear in the lower or transmit portion of the screen.
         In the case of non-packet modes of operation, everything you
         type in the transmit area, will also appear in the receive
         area as the information is actually transmitted.  In TNC
         lingo, this is the XMITECHO ON.  In packet modes, this will
         not occur  so that incoming and outgoing data are not
         intermixed on the screen.
 
         At the bottom of the screen is a summary list of the most
         common hot keys.  Pressing <F1> will give you a complete
         listing of these keys.
 
         The top line of the display will display the <F1>Help prompt,
         followed by the time in 24 hour format. Note that this is the
         time in your computer clock!  When in packet modes, the
         existing Receive Mode will be displayed next.  In other modes this
         will be replaced by the next serial number to be sent in Message
         mode, if the serial number is greater than 1.  The end of
         this line will show the name of the message file presently
         loaded into memory, or if packet mail "auto capture" is on,
         MAIL CAPTURE ON will appear.  If mail has been received, the
         word MAIL will be flashing.
 
         The box at the bottom of the screen is the operating status
         line.  This contains the present mode of operation, baud rate
         (or CW speed), shift and transmit/receive status.  The call
         of the station you are working will also appear on this line
         between the shift and transmit/receive areas.
 
         This line also shows the status of various toggles just after
         the mode of operation.  These indicators are as follows:
 
                Toggle                On        Off
                ------                ---       ---
 
           Capture to Disk            [CTD]      -
 
           Invert (RTTY,AMTOR)        [INV]     [NOR]
 
           DX Flag                    [DX]       -
 
           Copy to Printer            [PRT]      -
 
           LO Tones Toggle            [L]        -
 
     

PACK-PRO         Pg 7.
 
                       COMMAND KEYS AND PROGRAM OPTIONS
 
 
         COMMAND KEY (Hot Key) Summary:
 
           Function Keys:
 
              <F1> - Help                  <F2> - Select Mode
              <F3> - Send Brag Msg         <F4> - Send Calls
              <F5> - Enter Call            <F6> - Call CQ
              <F7> - Invert (Mark/Space)   <F8> - Receive Mode
              <F9> - Delay Receive         <F10> - Transmit Mode
 
          Control Keys:
 
           <Ctl><F1> Make Txt File       <Ctl><F2> Edit Txt File
           <Ctl><F3> Send Text File      <Ctl><F4> Mail Capture toggle
           <Ctl><F5> D/L ASCII File      <Ctl><F6> U/L ASCII File
           <Ctl><F7> Send Script         <Ctl><F8> Clr Rcv Screen
           <Ctl><F10> Drop to DOS
 
           Alt Keys:
 
             <Alt><A> Auto Capture          <Alt><B> Beacon toggle
             <Alt><C> COM Port Select       <Alt><D> DX Flag toggle
             <Alt><E> Local Echo toggle     <Alt><F> Force Command
             <Alt><G> Load Msg File         <Alt><H> Heard List
             <Alt><I> Initialize KAM        <Alt><J> Low Tones
             <Alt><K> Edit Msg File         <Alt><L> Lock on CW
             <Alt><M> Make Msg File         <Alt><N> Reset S/N
             <Alt><O> RTTY USOS toggle      <Alt><P> Printer toggle
             <Alt><R> Packet Receive Mode   <Alt><S> Port Parameters
             <Alt><T> Time Stamp toggle     <Alt><U> Unlock CW Speed
             <Alt><F1> Disk Capture toggle  <Alt><F4> Make First Call
             <Alt><n> Send Message n        <Alt><X> Exit Program
 
           Other keys:
 
             <PgUp> Screen Review          <->> Increment Baud/Speed
             <<-> Decrement Baud/Speed     <Up Arrow> Change Shift
             <END> End of transmission
 
            NOTE: TNC commands may be issued manually at any time. If in
                  a Packet mode, simply type the command and press <ENTER>.
                  If in any mode other than Packet, press the <Alt><F>
                  Force Command hot key and then enter the command and
                  <ENTER>.
 
                  If you use the <Alt><F> combination, you must then press
                  <F2> and reselect your previous operating mode.


PACK-PRO        Pg 8.
 
         The following details the options and funtions within the
         program.  The functions are listed based on the operating mode
         in use.
 
 
                *****  ALL MODES (COMMON KEYS & FUNCTIONS) *****
 
 
         END TRANSMISSION  <END>  - All Modes
 
              The <END> key can be used to end transmissions in all
              modes.  In the Packet modes, this key will send ' DE
              your call >>' to signify to the other station that you
              are done transmitting.
 
              In AMTOR mode this key will send the '+?' code to
              indicate you are waiting for the other station to now
              transmit.
 
              In these two modes, a switch to receive after pressing
              <END> is automatic.
 
              In all other modes, this key will send the call of the
              station you are working (if entered with the <F5> option
              described later) followed by 'DE', your call and  'K'.
              In these modes, the program will return to receive mode
              as soon as all information in the transmit buffer has
              been sent.
 
 
         SCREEN REVIEW  <PGUP> - All Modes
 
              This option allows you to review the six previous
              screens of information which have already scrolled by in
              the receive text area.  Once this option is selected,
              all further monitoring of the data from the TNC is
              halted.
 
              The use of the following keys allows you to scroll
              through the previous screens:
 
                        B  - Back one page
                        F  - Forward one page
                        Q  - Quit and return to previous mode
 
 
         CHANGE SHIFT  <UP ARROW> - All Modes
 
              This key will cycle through the shifts available for
              each respective mode.  Generally, you will shift through
              the 170, 425, 850, and Modem shifts.  The shift in use
              will appear in the appropriate place on the status line.
 

PACK-PRO         Pg 9.
 
         INCREASE/DECREASE SPEED & BAUD - <LEFT & RIGHT ARROWS> - All
 
              The left and right arrow keys are used to increase and
              decrease baud rate or cw send speed.  The speed or baud
              being used will appear in the status line.  The baud
              rates will increase/decrease based on the rates
              available for the particular mode you are in.  In CW,
              the speed will increment or decrement in one (1) WPM
              steps.  The default at startup is 13 WPM.
 
              Should you change modes and later return, the program
              will reenter the previous mode with the baud and shift
              parameters set as when you left.  Once you exit the
              program, the initial values will be the program
              defaults.
 
 
         HELP SCREEN  <F1> - All Modes
 
              The Help Screen gives a listing of all hot keys used by
              the program and a brief description of their function.
 
 
         SELECT MODES  <F2> - All Modes
 
              This option is used to select the operating mode you
              wish to use.  Selecting by number will place the program
              and TNC in the proper condition for the selected mode.
              If you are returning to a previously used (during the
              same session) mode, the program will return you with the
              parameters (shift, baud,etc) that you were in when you
              left it.
 
 
         SEND CALLS <F4> - All Modes
 
              This key will send the call of the station your are in
              QSO with (if entered with <F5>) followed by ' DE ' and
              your call. This will only be transmitted if in the
              TRANSMIT mode or after you enter TRANSMIT mode. once
              sent you will remain in this mode and may carry on your
              contact.
 
 
         ENTER CALL <F5> - All Modes
 
              The enter call option is used to enter the call of the
              station you are about to call or that has called you.
 
              In packet mode enter the call of the station you wish to
              connect to and use the FIRST CALL key <Alt><F4> to
              perform the connect.  In this mode, the program will
              check for any CALL_LST.SYS file and any paths that may
              exist before accepting the call as entered.
 

PACK-PRO         Pg 10.
 
              In CW, RTTY, and ASCII modes, enter the call of the
              station are calling or is calling you.  This entry of
              the call will insure that other options such as SEND
              CALLS will have the correct call to use.  You should
              enter this call before making contact.
 
              In the AMTOR mode, after you have entered the call of
              the station, the program will automatically determine
              the stations SELCAL using accepted techniques. You will
              see the SELCAL and be asked if it is correct (in case
              the other station is not complying with accepted
              practices). If it is simply enter 'Y'. If not enter 'N'
              and then you will be able to enter the SELCAL manually.
              Once entered you will be able to use the SEND FIRST CALL
              <Alt><F4> option to actually make the link.
 
 
         RECEIVE MODE  <F8> - All Modes
 
              The Receive mode option allows you to return IMMEDIATELY
              to the receive mode.  Any information in the type ahead
              buffer or the TNC which has not yet been sent will be
              cleared.  This allows you to clear the buffer, or to
              stop an unintentional transmission.
 
              In the packet modes, this option will issue a DISCONNECT
              command to the TNC, disconnecting you from the station
              you are talking to.
 
 
         TRANSMIT  <F10> - All Modes
 
              The F10 key will place you in transmit mode.  When in
              one of the packet modes, you will be placed in CONVERSE
              mode. Thus everything you type will be sent to the TNC
              for transmission.  If operating Packet, the FIRST
              Call <Alt><F4> option should be used when making a
              connect.  This is really the Transmit switch when
              operating in CW or RTTY modes. In the AMTOR mode this
              key can be used to seize the link.
 
              In CW, RTTY, and ASCII modes, this key will activate the
              transmitter and all text already in the type ahead
              buffer or typed real time at the keyboard will be
              transmitted.  This allows you to prepare a transmission
              while the other station is transmitting.  When ready to
              send your text, just press <F10>. After the text already
              in the buffer is sent, you will remain in a transmit
              mode.
 

PACK-PRO         Pg 11.
 
         MAKE TXT FILE  <Ctrl><F1> - All Modes
 
              The Make Text File option allows you to create a pure
              ASCII file of up to 300 lines in length.  These files
              may be message files you wish to upload to a Packet BBS
              or files you want to use to send information during a
              QSO (Station equipment, etc).  The BRAG.MSG file
              mentioned earlier is a good example of this type of
              file.  When this option is selected, you will be
              prompted for the filename to create. If a file by that
              name already exists, you will not be able to create a
              new one.  You may however use the EDIT TXT FILE
              <Ctrl><F2> option to be described next to edit the
              existing version.
 
              This is a very simplistic text editor and does not have
              a great deal of features. It is intended for creation
              and editing of small files for use by the program.
              Larger files should be created and edited using your
              standard ASCII word processor or editor.  The following
              editing keys can be used with this editor:
 
                   < -> >     - Move cursor Right
                   < <- >     - Move cursor Left
                   <Up Ar>    - Move up one line
                   <Dn Ar>    - Move down one line
                   <PG DN>    - Move down one page (15 lines)
                   <PG UP>    - Move up one page (15 lines)
                   <DEL>      - Delete character under the cursor
                   <INS>      - Toggle from Insert to Overwrite Mode
                   <HOME>     - Move to Start of line
                   <END>      - Move to End of line
                   <Ctl><HOME>- Move to Top of File
                   <Ctl><END> - Move to End of FIle
                   <Alt><I>   - Insert Line Above Cursor
                   <Alt><D>   - Erase entire line
                   <ESC>      - Exit Editor WITHOUT Saving file
                   <Ctl><S>   - Save File and Exit Editor
 
              At this time (Version 1.1) word wrap does not exist so
              files must be created in "typewriter mode", or in other
              words, press <ENTER> at the end of each line as if you
              were using a standard typewriter.
 
 
         EDIT TXT FILE   <Ctrl><F2> - All Modes
 
              This option allows you to edit previously created text
              files in the same manner as above. When you have entered
              the filename at the prompt, the program will check to be
              sure the file exists. If no such file exists you must
              use the MAKE TXT FILE <Ctrl><F1> option to create it.
              The same editing keys mentioned above apply when
              editing.
  

PACK-PRO         Pg 12.
 
         SEND TEXT FILE  <Ctrl><F3>  - All modes
 
              This option allows you to send any existing ASCII text
              file.  When selected, you will be asked for the
              filename. If the file exists it will be sent
              immediately.  If the file does not exist, the request
              will be ignored and you will be returned to the program.
 
 
 
         CLEAR RECEIVE SCREEN   <Ctrl><F8> - All Modes
 
              This option clears the receive portion of the screen
              display.
 
 
         DROP TO DOS   <Ctrl><F10>  - All Modes
 
              This option allows you to drop to dos and execute other
              dos commands without leaving the program.  This command
              may not operate if you have less than 512K of RAM in
              your system, since the program and COMMAND.COM must be
              able to coexist.  If the program clears the screen and
              then immediately returns to the program, you have
              insufficient memory for this funtion to work.
 
              Once you have dropped to DOS, you may execute other DOS
              commands, (DIR, FORMAT, ERASE, etc).  Note that
              COMMAND.COM must be in your root directory in order for
              this option to work.
 
 
         TOGGLE COM PORT - <Alt><C>  - All Modes
 
              This option will toggle between COM1 and COM2 ports.
              The program defaults to COM1.
 
 
         LOCAL ECHO TOGGLE   <Alt><E>  - All Modes
 
              This will toggle the program local echo on and off.  If
              ON then everything you type in the Transmit area of the
              screen will be displayed.  If OFF, nothing will be
              displayed.  This defaults to ON.  Note that this is NOT
              the local echo (or ECHO) command for your TNC.
 
 
         FORCE COMMAND   <Alt><F>  - All Modes
 
              This combination will force the TNC back into Command
              (cmd:) mode.  Keep in mind that if you are in a mode
              other than packet, you must reselect the <F2> select
              mode command to return to the previous mode.
   

PACK-PRO         Pg 13.
 
         LOAD MESSAGE FILE   <Alt><G>  - All Modes
 
              This will load a message file prepared previously with
              the <ALT><M> Make Message File Command.  Once loaded,
              this group of up to nine message lines (see MAKE MESSAGE
              FILE) will remain in memory until a new message file is
              selected, or you exit the program.
 
         HEARD LIST   <Alt><H>  - All Modes
 
              This option will display a listing of the last 18
              packet stations heard.  This is essentially the MH
              command for the TNC.  Keep in mind that while this list
              is displayed, the TNC will not be in Monitor mode, so no
              additional information will be received until you return
              to the program.
 
         INITIALIZE  KAM  <Alt><I> - All Modes
 
              This command will reinitialize the KAM with the same
              parameters as when the program was started.  This is
              handy if you have issued additional manual commands from
              the keyboard and now wish to return to the original
              setup.
 
         EDIT MESSAGE FILE  <Alt><K> - All Modes
 
              This is used to edit any of the Message files created
              with the MAKE MESSAGE FILE  <Alt><M> command.
 
         MAKE MESSAGE FILE  <Alt><M>  - All Modes
 
              This option is used to generate the nine (9) part
              message files for use by the program.  When selected, a
              screen will appear where you can enter each of the nine
              80 character messages.  As you enter each message, you
              will be prompted for the next in that file.  Entering
              just a carraige return <ENTER> instead of a message will
              save the file.  The following special characters made be
              used in these message files:
 
                       &&  - insert call of station in QSO with
                       #   - insert a sequential serial number
                       !   - repeat last serial number
 
                   For example a Sweepstake QSO file for W1VL in
                   his 235th QSO with W9ZZZ might take the form:
 
                         && DE W1VL  NR # A W1VL 60 EMA =
 
             This would transmit as: W9ZZZ DE W1VL NR 235 A W1VL 60 EMA (BK)
 
                   The next serial number to be sent can be
                   changed with the RESET SERIAL NUMBER option.


PACK-PRO         Pg 14.
 
         RESET SERIAL NUMBER COUNTER  <Alt><N> - All Modes
 
              This option will prompt you to change the next
              sequential serial number to be sent with message files.
              NOTE that each time you exit PACK-PRO, the Serial Number
              counter will be saved in PPACK.SYS. Be sure not to remove
              your program disk before this is saved.
 
         PRINTER TOGGLE  <Alt><P> - All Modes
 
              This option will toggle capture to printer on and off.
              When on, all text displayed on the receive screen will
              be copied to the printer.  If you are using an extremely
              slow printer, the use of a print spooler is recommended
              so as not to cause a slow down in program operation.
 
 
         PORT PARAMETERS  <Alt><S>  - All Modes
 
              This option allows you to change the computer to TNC
              port parameters.  Note that this only changes the
              settings in the computer.  If you wish to change TNC
              parameters, you must issue the appropriate TNC commands.
 
 
         DISK CAPTURE TOGGLE  <Alt><F1> - All Modes
 
              This option allows you to capture all of the received
              text to a disk file named CAPTURE.TXT.  This file is
              created by the program if it does not exist.  When
              toggled on, all received text will be copied to this
              file.  When toggled again (OFF), no further text is
              added to the file.  Be cautious since this file can
              become very large very quickly.
 
 
         MAKE FIRST CALL  <Alt><F4> - All Modes
 
              In the Packet communications modes, this command will
              use the call entered with the <F5> Enter Call option and
              will issue the 'Connect' command to the TNC.  If Auto
              Capture <Alt><A> is enabled, all incoming text will be
              captured to the Capture.TXT file once the connect has
              been made.
 
              In all other modes, this option, when used after the
              <F5>, Enter Call, routine will make the first call to a
              station.  The difference between this and the <F4> Send
              Calls option is that this option will send the calls
              more than once.  Rather than W1ZZZ DE W1VL, this option
              will send W1ZZZ W1ZZZ W1ZZZ DE W1VL W1VL W1VL K K.   In
              the AMTOR mode, this option will issue a call to the
              other stations SELCAL.


PACK-PRO         Pg 15.
 
         SEND MESSAGE n  <Alt><n> (n = 1 to 9)  - All Modes
 
              This option will send the message number 1 to 9 from the
              message file loaded using the <Alt><G> Load Message File
              option.  The message will be sent and you will remain in
              the transmit mode.
 
 
         EXIT PROGRAM  <Alt><X> - All Modes
 
              This will load a shut down sequence into the KAM and
              then will exit the PACK-PRO program.  All open files
              will be closed as you exit the program. NOTE that all open
              files will be closed and the contents of the program's
              serial number counter for contesting etc. will be saved
              in the PPACK.SYS file.  Be sure to allow time for this to
              occur before removing your program disk.  When the program
              returns you to the DOS prompt after exiting, all of these
              clean up chores have been completed.
 

PACK-PRO         Pg 16.
 
                *****   ALL MODES   E X C E P T   PACKET  *****
 
         SEND BRAG <F3> - All Modes  EXCEPT Packet -
 
              This key will automatically send the contents of the
              BRAG.MSG file if it exists.  If you should press <F3>
              while in the receive mode, the file will be opened but
              will not be sent until you go to the TRANSMIT <F10>
              mode.  As soon as you go into transmit, the file will be
              sent.  If you are in transmit mode and press <F3> the
              file will not begin sending until all text in the type
              ahead buffer has been transmitted.
 
 
         CALL CQ  <F6> - All Modes EXCEPT Packet -
 
              The <F6> key invokes the Auto CQ function.  In this mode
              a CQ will be generated with the number of lines entered
              as the CQ number in your PPACK.SYS file.  The format of
              the CQ will be different but appropriate for each mode.
              If the DX toggle has been selected (as shown by [DX] on
              the status line), a CQ DX will be called.
 
              Once the CQ has been transmitted, the program will go
              into LISTENING mode.  In this mode it will listen for a
              preset time (set in PPACK.SYS) for a response to your
              call.  If no response is detected after the preset time,
              the CQ will be repeated.  This will continue until a
              response is heard or you press the <F8> RECEIVE mode
              key.
 
              When listening for a response, the program looks for
              your call followed by 'DE ' in an incoming text. It then
              takes the incoming information after this text and
              assumes it is the call of the station calling you.  If
              this call is interpreted wrong or is missed, and you are
              receiving a call, press <F8>, then enter the call using
              the <F5> Enter Call functions.
 
 
         DELAY RECEIVE  <F9> - All Modes except PACKET
 
              The delay receive option is the normal method of
              returning to the receive or listening mode.  When this
              key is pressed, the TNC will return to Receive mode
              AFTER all text in the type ahead buffer or messages in
              process are sent.
 
 
         DX FLAG TOGGLE - <Alt><D>  - All EXCEPT Packet
 
              This key combination will toggle the DX flag on and off.
              This flag when on will add 'DX' to all your CQ calls.
              If off, a normal CQ will be sent.  The state of this
              flag is displayed on the left of the status line as [DX]
              if ON and nothing '   ' if OFF.
  

PACK-PRO          Pg 17.
 
                        *****   PACKET  ONLY  *****
 
         MAIL CAPTURE TOGGLE <Ctrl><F4> - Packet ONLY -
 
              MAIL CAPTURE allows you to receive mail from your local
              BBS while the rig is unattended.  The <Ctrl><F4> key
              combination will toggle mail capture on and off. This
              function will only work in the 'CQ/BEACON' receive mode
              for packet.  Once toggled on, the program waits for
              beacons from the local BBS's.  As each beacon is
              received, the program will first note the call of the
              station, displaying it on the right side of the status
              line.  It then watches for the word 'Mail'. Once this
              has been found, the program will wait to see if your
              call appears in the mail list.  If it does, the program
              will automatically issue a connect request to the BBS,
              and then issue a Read Mail (Mine) request.  The message
              that it receives will be put in a file called
              MESSAGE.00x on your default drive.  The file will be
              created if it does not exist.  As additional messages
              are retrieved, they will be added with extensions .002,
              .003 etc.   These files can be erased at any time as
              they will be recreated as needed.  Since this option
              does not at present erase or kill the message after it
              has been downloaded, please be sure to log back into the
              BBS and kill all messages which have already been read.
 
         DOWNLOAD ASCII FILE   <Ctrl><F5> -  Packet ONLY
 
              This option allows you to download an ASCII text file
              from your local BBS or another packet station.  When
              selected, you will be prompted for a download command.
              At this prompt, enter the entire download command as you
              would normally do for the BBS involved. For example, to
              download the file 'TEST.TXT' from your local BBS
              you would enter  'D Files Test.Txt' then that is what
              you would enter at the prompt.  The program will
              transmit the command to the BBS and at the same time
              will break the command down, based on the location of
              the '.' and open a file of the same name.  Be sure to
              include the '.' and extension when using this command.
              Pressing any key while the file is being transferred
              will abort the save to disk on your end and return you
              to command mode.
 
         UPLOAD ASCII FILE   <Ctrl><F6> - Packet ONLY
 
              This option allows you to upload files from you to your
              local BBS or another packet station.  When prompted,
              enter the normal upload command as required by the
              local BBS.  The program will then issue that command and
              begin sending the file. Naturally, the file must exist
              in order to be sent.  The file will be transmitted, one
              line at a time with a 3-4 second delay between lines to
              allow for acknowledgements to occcur.
 

PACK-PRO         Pg 18.
 
         SEND SCRIPT FILE  <Ctrl><F7> - Packet ONLY
 
              The script file option allows you to use a pre-defined
              file when connecting to other stations which may require
              the use of network nodes.  Many times you cannot simply
              connect using vias in the path.  In these cases, the
              script file can be used.  This is a standard ASCII file
              with each line being one step in the connect process and
              ending with a carriage return.  An example of this is:
                              C W1VL
                              C 3 EMASS
                              C W1XYZ V NETH
 
              A file such as this would issue each of the individual
              commands to the TNC, wait for a connect response and
              then issue the next command.  If at any time a 'FAILURE
              with' or 'BUSY from' response is received, the program
              will abort the rest of the script and return you to
              normal operating mode.
 
         AUTO CAPTURE TO DISK   <Alt><A>  - Packet ONLY
 
              When toggled on (see Help window), all connects made
              using the ENTER CALL <F5> and SEND FIRST CALL <Alt><F4>
              modes will automatically be captured to disk.  All text
              being received and displayed on the screen will also
              appear in the file CAPTURE.TXT.  This file will be
              created if it does not exist.   Pressing the <Alt><A>
              combination again will disable this funtion.  The
              program defaults to Auto Capture ON.
 
         BEACON TOGGLE   <Alt><B>  - Packet ONLY
 
              This key combination will alternately enable and disable
              the transmission of beacon signals.  Be sure your BTEXT
              has the information you wish to include with your beacon
              if you use this option.
 
         RECEIVE MODE SELECT <Alt><R>  - Packet ONLY
 
              This option will give you a choice of receive modes for
              packet operation.  These are:
 
                    - Everything - all packet information heard
                    - CQ/Beacon  - CQ's and Beacons Only
                    - Traffic    - all connected packet information
                    - Myself     - only packets addressed to you.
 
         TIME STAMP TOGGLE  <Alt><T>  - Packet ONLY
 
              This option will toggle the time stamping of incoming
              packets on and off.  When on, all received packet
              headers will be followed by the date and time as
              recorded by the TNC clock.
    

PACK-PRO          Pg 19.
 
                        *****   CW  ONLY  *****
 
 
         LOCK ON CW  <Alt><L>   - CW Mode ONLY
 
              This key combination will lock the KAM at the speed of
              the CW signal presently being received.  Also see UNLOCK
              CW SPEED <Alt><U>
 
 
         UNLOCK CW SPEED  <Alt><U> - CW ONLY
 
              This option will unlock the TNC CW tracking of speed and
              allow you to start tracking another signal.
 
 
 
 
 
 
                        *****   RTTY  ONLY  *****
 
 
         RTTY USOS TOGGLE  <Alt><O> - RTTY ONLY
 
              This option will toggle RTTY unshift on space on and
              off.
 
 
 
 
 
 
 
                    *****   RTTY/ASCII/AMTOR  ONLY  *****
 
 
         INVERT <F7> - RTTY/ASCII/AMTOR Modes -
 
              The <F7> key will toggle the mark and space tone
              polarities for these modes.  The status of the tones
              will be indicated on the left portion of the status line
              as either [NOR]mal or [INV]verted.
 
 
         LO TONES Toggle - <Alt><J> - RTTY/ASCII/AMTOR Modes -
 
              The lo tone toggle will toggle between US and European
              tone sets for these modes.
 
 
 
     

 
 
 
 
 
                          PACK-PRO Registration Form
                                Version 1.1
 
 
              YES, please register me as a user of PACK-PRO.
 
              I understand that payment of the requested $20
              registration fee will entitle me to a copy of the next
              release of PACK-PRO as well as unlimited telephone
              support and reduced registration fees on future products
              as they become available.
 
              If the $20 registration fee is a problem, as it may be
              in this day and age, a voluntary registration fee which
              you feel is appropriate will still entitle you to full
              registration and telephone support.  The next and later
              PACK-PRO releases will be available at reduced registration
              fees.
 
 
              NAME: _________________________  Call:____________
 
              STREET: __________________________________________
 
              CITY: ____________________________________________
 
              STATE: ____________  ZIP: __________________
 
              PHONE: (optional) ________________________________
 
 
              TNC: __________  COMPUTER: _________________ DISK SIZE: _____
 
 
              REGISTRATION FEE ENCLOSED: $__________
                   (PLEASE - MA residents add 5% sales tax)
 
              Please forward this application with the appropriate
              registration fee to:
 
                                Andrew C. Manti Jr.
                                   2 Deana Road
                                 Methuen MA 01844
 
              I thank you for supporting the shareware system!
 
              NOTE: PLEASE USE THE BACK OF THIS FORM TO REPORT PROGRAM
                    BUGS OR SUGGESTIONS.
 
                    PLEASE NOTE MODE OF OPERATION ALONG WITH AS MUCH
                    DETAIL AS POSSIBLE ON WHAT WAS BEING DONE WHEN THE
                    PROBLEM OCCURRED.