PACKWIN.EXE v1.2, 03/25/86
                         Packet Radio TNC Control Software
                         Copyright (c) Charles Stampf, 1986

            PACKWIN evolved as a result of a need for a simple yet functional
       program to interface between my computer, and my TNC (Terminal Node
       Controller).  As I surveyed the situation, I began to realize that
       there was no single software product that was fun, fast and
       uncomplicated to use.

            I plan to add several other more powerful functions to this
       package as time goes by and hope to receive your input and
       suggestions.  It seems that, at present, there is no standard or
       agreed upon protocol for binary file transfer.  However the next level
       of this program will contain some type of simple yet effective binary
       file transfer routine.

            PACKWIN was written to operate on an IBM PC or a close compatible
       with at least 128k available RAM.  It has been tested using the TAPR
       1, TAPR 2 and GLB PK-1 TNC's.  Hardware handshaking between the
       terminal and TNC has been implemented, as a result it is expected that
       more than the  "3 wire hook-up" be used at the Async port.  A short
       discussion of this requirement follows later on in this documentation.

            PACKWIN is a compiled BASIC program making extensive use of
       ASSEMBLER calls.  Windows are used to provide an uncluttered area to
       enter data and select program functions.  The screen is usually
       restored to the state prior to activating a window so that continuity
       and data flow is not lost.
       
       
       HARDWARE REQUIREMENTS:

            An IBM PC or close compatible, 128k RAM, ASYNC port, graphics
       display (preferred) and, a TNC compatible to those mentioned above is
       all that is required.

            TAPR and GLB PK-1 are capable of hardware handshaking to prevent
       buffer overflow during data transfer.  Both TNC's use the CTS signal
       to indicate when they are ready to receive data.  PACKWIN uses this
       signal to avoid sending data to an unwilling TNC.  This signal is
       located at pin number 5 on your RS-232 connector and must be
       functional for the proper operation of PACKWIN.
       
       TAPR 1, PK-1 and TAPR 2 use different signals to determine the status
       of the terminal (whether or not the computer is ready for data).  TAPR
       2 uses the signal DTR (pin 20, RS-232) whereas TAPR 1 and PK-1 use RTS
       (pin 4, RS-232).  You should be sure that your configuration conforms
       to these parameters.  PACKWIN will handle either of these conventions.
       
       
       OPERATION:

            Turn on your TNC and invoke PACKWIN from the DOS prompt by typing
       'PACKWIN'.  You will shortly see the sign-on message followed by the
       HELP menu.  The HELP menu lists the available function keys and their






PACKWIN - TNC Control Software

       operation.  In addition, the communication port data and the states of
       three toggles are presented.  You are shown which port you are using,
       the present baud rate and word length.  The ECHO, PRINTER and ASCII
       SAVE status are also displayed.  These features are toggles, that is,
       they can be turned on and off using the same function key.  The
       default communications parameters are set to COMM2, 9600 baud, 8 bit
       word NO parity.  They can be changed as described below.
       
       
       FUNCTION KEYS:
       
       F1   Displays the HELP menu.
       
       F2   LOG drive.  Allows changing the currently logged drive.  Enter
            your new drive letter (A - F).  The program responds with the new
            logged drive and gives available free space.
       
       F3   Change SUBDIR.  Allows you to change the currently logged sub-
            directory.  Enter the name of the new sub-directory preceded by
            '\'; ie.'\newdir'(without the quotes).  Press ENTER without an
            argument to exit without any changes.
       
       F4   Change COMM parameters.  Enter the desired parameters as they are
            presented.  The present and new configuration are given.  Press
            ENTER at the COMM port menu without an argument to exit without
            any changes.
       
       F5   Immediately CLEARS the screen.
       
       F6   ECHO toggle.  Allows local echo to the screen.  Pressing F6
            alternately turns echo on/off.  If you are getting double
            characters on the screen when you type, either turn echo off at
            your TNC or press F6.
       
       F7   File VIEW.  Allows you to view an ASCII file stored on disk.
            Enter a valid filespec and press enter.  PACKWIN responds with
            the file length and creation date and displays several lines of
            the file.  To continue viewing simply press 'C' until the file is
            complete.  To discontinue viewing just press ENTER.
       
       F8   Gives directory of currently logged disk and sub-directory.
       
       F9   ASCII Receive.  To store received data to disk press F9 and
            supply PACKWIN with a valid file name.  PACKWIN will store all
            subsequent data received to the file.  To stop saving data just
            press F9 again.  A message will be printed to the screen
            indicating that the function has completed.  In addition, the
            status of this function is displayed on the HELP menu.
       
       F10  Xmit ASCII.  To transmit an ASCII file, you should first place
            your TNC in the TRANSPARENT mode (MX/E on the PK-1, or TRANS on
            TAPR).  Then press F10.  Supply a valid file name to transmit.
            PACKWIN will open the file and get ready to transmit.  When the
            other station is ready to receive your file press 'T' to begin
            transmission.  PACKWIN will begin sending the file, stopping if
            required, to honor a handshaking request (BUFFER FULL).  You will
            see the file displayed on the screen as it is being loaded to the
            TNC's buffer.  When the entire file is sent to the TNC you will






PACKWIN - TNC Control Software

            be returned to the receive mode.  It may take a while for your
            TNC to 'catch up' as the buffer is emptied.  You may then return
            to conversational mode or continue in transparent.  Pressing
            ENTER without an argument at the file name prompt will exit this
            routine.
       
       Alt F1    EXIT the program.  Answering 'Y' to the prompt will exit
            PACKWIN.  All files and devices are closed and a graceful exit to
            DOS is performed.
       
       Alt F2    PRINTER toggle.  Pressing Alt-F2 will toggle printer echo.
            Useful for capturing received data without saving it to a file.

            Most functions can be terminated at their first menu prompt by
       simply pressing ENTER.
       

            A primitive error reporting method will display any errors that
       PACKWIN cannot handle.  The line and error number will be shown before
       exiting to DOS.  Please include this info when writing to me.
       

            I am distributing PACKWIN via the "FREEWARE" concept.  to prove
       that the AMATEUR Radio community will support this method of program
       development.  If you feel that PACKWIN is of use to you and if you
       would like to receive the latest version, one that allows BINARY file
       transfer and  customized COMM port parameters please consider the
       donation of $15.00 to my efforts.  Send me your COMM port requirements
       and a blank diskette and when it is completed I will return the latest
       version of PACKWIN.

            Thanks to Thomas Hanlin III for his ADVBAS.LIB collection of
       BASIC compiler subroutines and to Dave Evers for his ideas on pop-up
       windows.

            Send any error indications and or suggestions.  I will attempt to
       correct all errors an promise to review any and all suggestions.
       73, Gud Luck
       
                                Charlie Stampf, N2CJ
                                Bloomer Rd.
                                LaGrangeville NY 12540
       
       
       
       DISCLAIMER OF LIABILITY:
       
       I, Charles Stampf, as author of the PACKWIN.EXE software contained in
       this package, hereby disclaim all responsibility for any consequence
       arising out of the use, misuse, or non-use of any of the material
       included herein.