CONSORCE CODE AND LOGGING PROGRAM                   
             

GETTING STARTED
1. Turn on your printer if you are going to print out the log.

2.  Insert   the  program disk  in drive  A.  It is   recommended 
that the   program disk  contain the  autoexec.bat file  to  cause   
the proper prompts to appear for date and time

If  you   wish  to  have the  logs  and  messages  on   a  second 
diskette then insert that diskette in drive B.

3.  If  the  system power is off turn  it on and if not hit  CTRL 
ALT DEL keys to reboot the system

4.  When   the prompts appear answer  the date and time   prompts 
asin  normal DOS  load.  Be sure to  enter these if you  wish  to 
havethe log correct.  The next prompt is for the  filename of the 
logfile.


Following  that   is the filename for  the print file  and   then 
the filename for the message file. The  logfile must exist or must 
be created  after   the  program starts   and  before  any   other 
function that would use it.

5.  At   this  time  a   screen will come  up  and  display   the 
program name  and version.  Hit the enter key and you are ready to 
go.


FORMAT OF THE SCREEN
The screen is divided as follows:

Lines    1   through  10   are   the    transmit   buffer.    All  
characters entered   in  this area are  transmitted out using  the 
current code type. At this time only morse is implemented.

Lines   11  through   20   are   for  the   receive   buffer.  No  
receive functions are implemented at this time.

Lines  21  through 23 show function  keys and current  status  of 
the program.

Line  24 is used for entering  certain data to the  program  such 
asthe speed,   received log data  , etc.  This will be  explained 
inthe section on operating the program.






PROGRAM OPERATION


FUNCTION KEYS

Lines  20   and  21  are used  to display   the  function   keys. 
These keys   change  the  values  of status  indicators   or  call  
certain functions as described below

SF--------SHIFT  AND  A FUNCTION KEY.  The following are pf  keys           
but with the shift key also pressed.

1/CK------DUP CHECK.  This key  causes the  binary tree  of calls          
to be tested for the existance of the present ID. 

2/ID------ENTER NEW  ID. You will  be prompted  on line 24  for a          
new    id  to  be  entered.   This   id  will  automatically   be          
checked for duplication.

3/RXD-----ENTER  NEW  RECEIVED DATA  FOR  THE  LOG. You  will  be          
prompted   on  line  24  for   new  received  data.   This   data          
will be put in the log and printed.

4/SN------ENTER NEW SERIAL NUMBER.  You will be prompted on  line            
24  for  a  new  serial  number.  This  number  is  automatically             
updated  each time a log entry is made with S/F10.

5/RPT-----REPEAT THE  TRAMSMIT BUFFER SCREEN. The  cursor returns          
to line 1 column 1 and transmit takes place if active.

10/LOG----ENTER DATA TO THE LOG. This  key enters new data to the          
log   and   to   the  dup  checking  tree.    It  will   not   be           
entered if it is a duplicate call.

A:--------ALT KEY. The  following are alpha keys  on the keyboard          
pressed at the sime time as the ALT key.

A/AC------ASCII CODEB/IF------INITIALIZE FILE.  This key is  used 
to  initialize a log file.

C/BC------TOGGLES USE BAND  AS PART  OF  CALL  FOR  DUP CHECK.

E/GM------RETRIEVE  MESSAGE  FROM MESSAGE FILE

G/GT------STORE MESSAGES TO BUFFER. This key changes the value of          
msg.   When   msg   is  TRUE  KEYS  F1-F10  STORE  the   transmit          
buffer   first   256  characters  to  the  message   buffer   and          
when  FALSE the partition of F retrieves the message and puts  it 
in  the  transmit  buffer.

K/LG------TOGGLES WRITING DATA  TO  LOG 

FILE. Changes logd.

M/MC------MORSE CODE MODE.

O/ON------TRANSMIT   MODE ON/OFF  TOGGLE.  If TRUE  the  transmit          
screen buffer is transmitted else no transmit occurs. 

P/PT------PRINT LOG ENTRIES.

R/RS------RESET. The  screen is cleared and  certain defaults are          
reset.

S/SP------TRANSMISSION SPEED RESET. You  will be prompted for the          
speed on line 24.

T/TY------BAUDOT RADIOTELEPRINTER CODE MODE.

W/BND-----ENTER THE BAND IN USE FOR THE LOG.

X/XD------ENTER THE TRANSMIT DATA FOR THE LOG.



STATUS INDICATORS

The  rest  of  line  21 and Lines 22 and 23  show  the  following 
status indicators:

SP--------TRANSMISSION SPEED

SN--------PRESENT  VALUE  OF  THE  SERIAL  NUMBER.  This  can  be          
manually   set.   It  is  incremented   each  time  a  new   call                
is successfully entered in the log

ON--------THE  PRESENT   STATE  OF  TRANSMISSION.  TRUE indicates          
that data in the transmit screen will be sent.

MG--------IF TRUE  KEYS  1-10 ARE USED TO STORE  A MESSAGE. FALSE          
AND KEYS F1-F10 ARE USED TO RETRIEVE A MESSAGE.

CB--------TRUE AND THE  BAND IS INCLUDED AS PART OF  THE CALL DUP          
CHECKING. FALSE AND THE BAND IS NOT INCLUDED.

RD--------TRUE AND RECEIVE  DATA HAS BEEN ENTERED  SINCE THE LAST          
LOG  ENTRY.  This  must be  TRUE before  log entry SF10) is allowed.

PT--------PRINT LOG ENTRIES IF TRUE.

ID--------LATEST CALL ENTERED.

LD--------TRUE  AND  LOG  functions  active.  FALSE  and  no  log 
functions are active including  DUPCHECK.


LOG DATA STATUS LINE

The  line 23 is  used to display important log data  to  keep  it 
in view  even if you wish to  make changes.  For example  RECEIVED 
DATA may  change  because of a  receive error or  a change by the 
other station.


SN--------PRESENT VALUE OF THE SERIAL NUMBER WHICH  IS 
UPDATED WHENEVER   A  SUCCESSFUL  LOG  ENTRY   IS MADE.

RDATA-----LATEST READ DATA ENTERED


BND-------BAND IN USE FOR LOG ENTRY


                   Schematic (Print 132 wide)
 


                       7805C                                  RS232/20--1 |-----|14                          |-----|             |     | |             +8-18V--|    |     |        X--3 |     | |                     |    ||-|-||        |    |     | | MC148
9                                                             |     | | |         |    |     | | #276-2521                     |-----| | |+5       | |7 |-----| | Radio                             |----------------|-X---------|-|----------| Shack          
  |                X-----------|-X            |              -----         | |--RS232/7                         |               ---          |                                    |                -           |  ANY GENERAL PURPOSE               |          
                  |  NPN TRANSISTORS                   |--\/\/\/\--X-----\          |                                       1k      |       \ |     /                                                 |         |---/        -------------XMTR                 
         |         |           /             KEYING                        |       / |         |/                                            |     /             |  THIS ONE MUST TAKE                        |----/------------- |  KEY CURRENT AND           
                      |-------|      |\     VOLTAGE                                   -----     |      |  \                                              ---      |          |                                              -       |----------|