The first stage of the Remote Sysop facility is now available. The system
also provides the same facilities locally. The program may be run as a
normal DOS program, either in a Desqview window or standalone, or in may
run as a TSR. The TSR mode would normally be used if you were running a
standalone node, or a BBS system that doesnt need DesqView (eg AA4RE).
In TSR mode, commands cannot be entered locally, and the SAVENODES command
is disabled.


Installation.

1. Add an extra port to TNCPORTLIST (unless you have a spare)

2. Add a suitible application name as the third APPLICATIONS Param, ie

     APPLICATIONS=BBS,,*SYSOP

   I suggest you use a name starting with a '*', as this will 'hide' the
   command from the Valid Commands display.

3® Creatå á file¬ PASSWORD.BPQ, containing a string of up to 80 characters.

4. Run program SYSOP, with a single parameter of the TNCPORT specified above,
   either on its own, or in a DesqView window. If a second parameter of
   'RESIDENT' is specified, the program will become a TSR routine.




Commands may mow be entered directly on the PC, (unless in TSR mode) or
remotely by connecting to the Node, and entering the APPL name (eg *SYSOP).
When accessed remotely, a password prompt is sent, containing 5 random numbers
in the range 1 to the length of the PASSWORD.BPQ string. The first command
entered must be the corresponding five letters from the password string, 
or the user will be disconnected.

Available Commands.

The following commands are supported:

BYE - Disconnect remote user (even if entered from console)

TXDELAY
MAXFRAME
FRACK
RESPTIME
PACLEN
RETRIES
QUALITY
PERSIST
TXTAIL
XMITOFF
DIGIFLAG
DIGIPORT
USERS
VALIDCALL
L3ONLY
BBSALIAS

Setting XMITOFF will supress all TX activity on a port (including CWID,
beacons, etc). I put it in so I could monitor the satellites without
causing QRM

Setting BBSALIAS will cause connects to the port call or port alias to go to
the BBS rather than the node.

The above display or update the corresponding parameter for a specified port,

eg   PACLEN 1 100
     PERSIST 2 50

If the third parameter is omitted, the current value is displayed.

It is not currently possible to update VALIDCALLS, but you can display
the current setting.


*** Warning ***  

At the moment the FRACK value is in 1/3sec units, and the TXDELAY is in
50ms units for HDLC cards, and 10ms units for KISS TNCs. I'll be sorting
this out when I get the time to rationalize the timer code, but in the 
meantime, I suggest you make a note of the current values before you
start fiddling. 

Also KISS users should note that the params are only sent to the TNC every
5 mins or so, so the updated values may not take effect for a while.


ROUTES

To display ROUTES table, enter ROUTES

To display entry for a particular neighbour, enter ROUTES Call Port,

eg   ROUTES G8BPQ-2 2

To update an entry, enter ROUTES Call Port Params

eg   ROUTES G8BPQ-2 2 100	- Set quality to 100
     ROUTES G8BPQ-2 2 !         - Toggle 'Locked Route' flag
     ROUTES G8BPQ-2 2 100 !     - Set quality and toggle 'locked' flag

SAVENODES

Not available in TSR mode.

Writes the ROUTES and NODES tables to the BPQNODES file.


The SAVENODES function may also be invoked directly from the DOS command
line - this function replaces BPQNODES.COM

     ie.  SYSOP SAVENODES


Please let me know what other parameters you would like to be able to 
update.



John Wiseman, G8BPQ
29.5.90

A version has now been produced to use with BPQ Host Mode - SYSOPH. It is
functionally equivalent to SYSOP, but the port number can be in the range
1 to 64.

20.2.91