LAB.BAS  is  a  basic  program written for the  IBM  or  IBM 
compatible with 128k of RAM,  two disk drives and a printer.   It 
may  be  run  on a one drive system by  removing  the  "B:"  from 
several lines in the program files LAB.BAS, LAC.BAS AND SEM.BAS.
     The  program  is  written  in  using  double  precision  for 
accuracy.   If  accurate  station locations and  current  orbital 
elements  are used angle accuracy is within .05 degrees and range 
to about 50 meters.
     This  is  a menu driven program using overlays  to  minimize 
core requirements.  The following files are required:
                    LAB.BAS   (saved in ASCII)
                    LAC.BAS   (saved in ASCII)
                    SEM.BAS   (saved in ASCII)
                    ELSET.FIL
                    STATION.FIL
     The  basic files must be stored on disk using the /A  switch 
in  order  for  the  overlay technique  to  be  used.   The  disk 
containing  the  above  files must be placed in drive  B  with  a 
SYSTEM  disk  containing  BASIC,BASICA or  GWBASIC  in  drive  A.  
Output is to the printer therefore the printer must be on line.
     The  file "STATION.FIL" is the file containing the  location 
of the station for which data are to be computed.  The parameters 
are  latitude,  longitude,  height above the  spheroid,  meridian 
deflection and prime deflection.  Height, meridian deflection and 
prime  deflection  may  be  entered as zero  if  unknown  without 
serious degradation of output.   Longitude is positive east.  The 
following is an example of a location near the Tech Lab at PAFB:
               28 13 34.8742 LAT
              279 24  2.0120 LONG
              -14.94 METERS above spheroid
                 .84 meridian deflection  (seconds of arc)
                1.17 prime deflection  (seconds of arc)
     ELSET.FIL  contains  the orbital elements of the  object  of 
interest. Samples are included in the file.
     With the default drive A, type BASIC B:LAB, BASICA B:LAB or 
GWBASICA B:LAB.  Make menu selections and away you go.
     When computing angles you will be prompted for the station 
name, object number and object name.  Give names stored in 
STATION.FIL and ELSET.FIL.  You will then be prompted for the 
date of the desired look angles. The form is Julian (yydoy) or 
year and day of year.  Example 86001 is the first of Jan. 1986.  
The stop date is in the same format. The next prompt is for the 
interval between points.  Enter the number of seconds (1 to 
86400).  The computation begins.
     The display will show U(3), (the number of kilometers above 
or below the tangent plane), WD (the vertical velocity in 
kilometers/sec, the current revolution the target is in and the 
elevation angle in degrees.  These are displayed to show you the 
computer is working and the printer will receive only those 
points with a positive elevation.
     Happy computing.