Note: Print using WS 3.3

Multiple-tuned Amplifier Program

Jack Porter
Cubic Corporation
P. O. Box 85587
San Diego, CA 92138
(619) 277-6780

Permission to publish the above information is granted.


The program was developed using a TRS-80 Model 4 computer with the DOSPLUS
IV operating system and Model 4 Basic, a version of Microsoft Basic which
is very similar to the one used on the IBM PC.  The program should run
with very minor changes using any version of Microsoft Basic.  The effects
of any statements which are peculiar to Model 4 Basic, DOSPLUS, or the
Gemini 10 printer are explained by remarks in the program at those lines.

The program requires 16K of memory and a monochrome display. The display
formats in the program use 80 columns and 24 lines.






Abstract:
This program is used to design tuned amplifier coupling networks which
consist of one to eight tuned circuits each.  These filter networks may
be of any conventional filter type, such as Butterworth, Chebyshev or
Bessel.  The program calculates capacitor, inductor and resistor values,
and transformer turns ratios required to form a filter network with a 
specified shape, center frequency, and bandwidth which will provide the
desired mismatch ratios for the transistors which are coupled by it. 
The program also calculates low-pass prototype element values for
Butterworth and Chebyshev filters. For other types of filters these
must be entered from the keyboard.



Variable Descriptions:
Am: Chebyshev filter passband ripple in dB.  Am=0 for Butterworth filters.
Ap: Power gain in dB.
BS, BL: Imaginary parts of source and load admittances.
BW: Bandwidth in MHz.
Ck: Tuning capacitance of k'th tuned circuit in pF.
Ck,k+1: Coupling capacitance between tuned circuits k and k+1.
Ct: Total capacitance at each node in pF.
F0: Design center frequency in MHz.
Fc: Corrected center frequency used in calculations.
GS, GL: Real parts of source and load admittances.
K: Stern stability factor.
L: Tuned circuit inductance in nH.
Mia, Moa: Input and output mismatch ratios for transistor a.
Mib, Mob: Mismatch ratios for transistor b.
MS, ML: Source and load mismatch ratios.
N: Number of tuned circuits.
N1, N2: Turns ratios at filter input and output.
Q0: Reciprocal of filter fractional bandwidth.  Q0=Fc/BW.
Q1, Q2: Q's of the first and last tuned circuits in the filter.
QL: Loaded Q of a single-tuned circuit.
Qu: Unloaded circuit Q; approximately equal to inductor Q.
r: Low-pass prototype filter termination resistance for N odd,
   or conductance for N even.
R1, R2: Loading resistance values at filter input and output.
S: Alignment sensitivity.
Y11, Y21, Y12, Y22: Transistor short circuit admittance parameters.
     Enter these values in data statements in that order,
     real part of each Y parameter first.
Yi, Yo: Transistor input and output admittances.







Sample program run showing text which is displayed on the screen:

RUN "TUNEDAMP/BAS"
TUNED AMPLIFIERS                                           05/12/86
N, Am(dB)? 3, -1
Prototype element values
 1 ? 2.2034
 2 ? .97051
 3 ? .33742
Prototype element values:
 1  2.2034       2  .97051       3  .33742      
 r= 1 

Print element values? Y
TUNED AMPLIFIERS   N= 3    Am=-1                           05/12/86
Transistors:
 1. MRF904 10V 2.5mA  180 MHz            2. 2N4957 10V 2.0mA  180 MHz
Coupling network types:
1. Interstage  2. Input  3. Output? 1
Transistors? 1, 2
Mia, Moa, Mib, Mob? 10, 20, 8, 12
Ka= 2.833   Sa= .64357                   Kb= 5.0985   Sb= .454846 
Are K and S OK? N
Mia, Moa, Mib, Mob? 10, 50, 10, 20
Ka= 6.88015   Sa= .378057                Kb= 10.0663   Sb= .270341 
Are K and S OK? Y
TUNED AMPLIFIERS   N= 3    Am=-1                           05/12/86
Transistors:
 1. MRF904 10V 2.5mA  180 MHz            2. 2N4957 10V 2.0mA  180 MHz
Mia= 10            Moa= 50             Mib= 10             Mob= 20 
 Ka= 6.88015        Sa= .378057         Kb= 10.0663         Sb= .270341 

F0(MHz), BW(MHz), Qu? 180, 15, 120
Options:  1. Select C12  2. Select Ct  3. N1=1  4. N2=1? 1
C12(pF)? .5
Fc= 179.844 MHz                 Ap= 16.5514 dB
Q1= 26.4178     Q2= 4.04552     Qu= 120 
R1= 6207.32     R2= 679.082     N1= 2.53424     N2= 2.54096 
 L= 89.3367 nH  Ct= 8.76639 pF
C 1 = 7.80128   C 2 = 6.98868   C 3 = 5.48921   
C 12 = .5       C 23 = 1.27771 

 




Print results? Y
New C? N
New M's? N
TUNED AMPLIFIERS   N= 3    Am=-1                           05/12/86
Transistors:
 1. MRF904 10V 2.5mA  180 MHz            2. 2N4957 10V 2.0mA  180 MHz
Coupling network types:
1. Interstage  2. Input  3. Output? 0
TUNED AMPLIFIERS                                           05/12/86
N, Am(dB)? 2, .1
Specify:  1. Ripple BW   2. 3 dB BW? 2
Prototype element values:
 1  1.6545       2  1.22071     
 r= .737811 
Print element values? N
TUNED AMPLIFIERS   N= 2    Am= .1                          05/12/86
Transistors:
 1. MRF904 10V 2.5mA  180 MHz            2. 2N4957 10V 2.0mA  180 MHz
Coupling network types:
1. Interstage  2. Input  3. Output? 2
Transistor? 1
GS, BS, MS, Mib, Mob? .02, 0, 2, 10, 50
K= 6.88015      S= .378057 
Are K and S OK? Y
TUNED AMPLIFIERS   N= 2    Am= .1                          05/12/86
Transistor:
 1. MRF904 10V 2.5mA  180 MHz
 MS= 2                                 Mib= 10             Mob= 50 
                                         K= 6.88015          S= .378057 

F0(MHz), BW(MHz), Qu? 180, 15, 120
Options:  1. Select C12  2. Select Ct  3. N1=1  4. N2=1? 1
C12(pF)? .5
Fc= 179.844 MHz                 Ap(Transducer)=-5.13807 dB
Q1= 19.8367     Q2= 19.8368     Qu= 120 
R1= 12263.2     R2= 5653.23     N1= 7.86234     N2= 4.82723 
 L= 91.9257 nH  Ct= 8.51949 pF
C 1 = 8.01949   C 2 = 7.50881   
C 12 = .5       






Print results? Y
New C? N
New M's? N
TUNED AMPLIFIERS   N= 2    Am= .1                          05/12/86
Transistors:
 1. MRF904 10V 2.5mA  180 MHz            2. 2N4957 10V 2.0mA  180 MHz
Coupling network types:
1. Interstage  2. Input  3. Output? 0
TUNED AMPLIFIERS                                           05/12/86
N, Am(dB)? 1, 0
Prototype element values:
 1  2           
 r= 1 

Print element values? N
TUNED AMPLIFIERS   N= 1    Am= 0                           05/12/86
Transistors:
 1. MRF904 10V 2.5mA  180 MHz            2. 2N4957 10V 2.0mA  180 MHz
Coupling network types:
1. Interstage  2. Input  3. Output? 3
Transistor? 2
Mia, Moa, ML, GL, BL? 10, 20, 1, .02, 0
K= 10.0663      S= .270341 
Are K and S OK? Y
TUNED AMPLIFIERS   N= 1    Am= 0                           05/12/86
Transistor:
 2. 2N4957 10V 2.0mA  180 MHz
Mia= 10            Moa= 20               ML= 1 
  K= 10.0663         S= .270341 

F0(MHz), BW(MHz), Qu? 180, 25, 120
Options:  1. Select C12  2. Select Ct  3. N1=1  4. N2=1? 3
Fc= 179.565 MHz                 Ap= 20.4109 dB
QL= 7.18262     Qu= 120 
R1= 1033.43                     N1= 1           N2= 3.50168 
 L= 37.8275 nH  Ct= 20.7677 pF
C 1 = 18.8655   


Print results? N
New C? Y
Options:  1. Select C12  2. Select Ct  3. N1=1  4. N2=1? 2
Ct(pF)? 8
Fc= 179.565 MHz                 Ap= 20.4109 dB
QL= 7.18262     Qu= 120 
R1= 2682.74                     N1= 1.6112      N2= 5.6419 
 L= 98.1986 nH  Ct= 8 pF
C 1 = 7.26726   






Print results? Y
New C? N
New M's? N
TUNED AMPLIFIERS   N= 1    Am= 0                           05/12/86
Transistors:
 1. MRF904 10V 2.5mA  180 MHz            2. 2N4957 10V 2.0mA  180 MHz
Coupling network types:
1. Interstage  2. Input  3. Output? -1

Ready



Printer output from sample program run:

TUNED AMPLIFIERS         05/23/86

  N= 3 
Prototype element values:
 1  2.2034          2  .97051           3  .33742 
 r= 1 

Transistors:
MRF904 10V 2.5mA  180 MHz              2N4957 10V 2.0mA  180 MHz
Y11= +1.730E-03 +5.063E-03j            Y11= +2.585E-03 +6.348E-03j
Y21= +6.583E-02 -2.481E-02j            Y21= +5.396E-02 -2.084E-02j
Y12= -2.305E-05 -5.248E-04j            Y12= -7.264E-08 -4.480E-04j
Y22= +7.946E-05 +1.590E-03j            Y22= +1.397E-04 +1.296E-03j

Mia= 10            Moa= 50             Mib= 10             Mob= 20 
 Ka= 6.88015        Sa= .378057         Kb= 10.0663         Sb= .270341 
Yia= +5.317E-03 +1.345E-02j            Yib= +5.769E-03 +1.459E-02j
Yoa= +8.434E-04 +3.375E-03j            Yob= +4.682E-04 +2.146E-03j

  N= 3 
 F0= 180 MHz        BW= 15 MHz          Fc= 179.844 MHz
 Ap= 16.5514 dB
 Q1= 26.4178        Q2= 4.04552         Qu= 120 
 R1= 6207.32 6      R2= 679.082 6
 N1= 2.53424        N2= 2.54096 

  L= 89.3367 nH     Ct= 8.76639 pF
 C1= 7.80128 pF
                   C12= .5 pF
 C2= 6.98868 pF
                   C23= 1.27771 pF
 C3= 5.48921 pF







TUNED AMPLIFIERS         05/23/86

Transistor:
                                       MRF904 10V 2.5mA  180 MHz
                                       Y11= +1.730E-03 +5.063E-03j
                                       Y21= +6.583E-02 -2.481E-02j
                                       Y12= -2.305E-05 -5.248E-04j
                                       Y22= +7.946E-05 +1.590E-03j

 MS= 2                                 Mib= 10             Mob= 50 
                                         K= 6.88015          S= .378057 
 GS= .02            BS= 0              Yib= +5.317E-03 +1.345E-02j
                                       Yob= +8.434E-04 +3.375E-03j

  N= 2              Am= .1 dB          3 dB BW
 F0= 180 MHz        BW= 15 MHz          Fc= 179.844 MHz
 Ap(Transducer)=-5.13807 dB
 Q1= 19.8367        Q2= 19.8368         Qu= 120 
 R1= 12263.2 6      R2= 5653.23 6
 N1= 7.86234        N2= 4.82723 

  L= 91.9257 nH     Ct= 8.51949 pF
 C1= 8.01949 pF
                   C12= .5 pF
 C2= 7.50881 pF








TUNED AMPLIFIERS         05/23/86

Transistor:
2N4957 10V 2.0mA  180 MHz
Y11= +2.585E-03 +6.348E-03j
Y21= +5.396E-02 -2.084E-02j
Y12= -7.264E-08 -4.480E-04j
Y22= +1.397E-04 +1.296E-03j

Mia= 10            Moa= 20               ML= 1 
  K= 10.0663         S= .270341 
Yia= +5.769E-03 +1.459E-02j
Yoa= +4.682E-04 +2.146E-03j             GL= .02             BL= 0 

  N= 1              Am= 0 dB
 F0= 180 MHz        BW= 25 MHz          Fc= 179.565 MHz
 Ap= 20.4109 dB
 QL= 7.18262                            Qu= 120 
 R1= 2682.74 6
 N1= 1.6112         N2= 5.6419 

  L= 98.1986 nH     Ct= 8 pF
 C1= 7.26726 pF