.N:1
.H:...Page F-$$$...


FIRST.DOC

Copyright 1986, by Thomas F. Droege, All Rights Reserved.


                               DROEGE

      Design Robot for Origination of Exacting Graphic Engineering

        DROEGE is a general purpose program for the design of printed circuit 
photomasters.  Is was created as a demonstration program for our low cost 
precision photoplotter.  As it was developed it became more and more useful as 
a design tool, so eventually the circuit boards and the mechanical drawings for 
our photoplotter were done using this program.  

        This is a manual CAD system.  That is, it does nothing automatically 
like schematic capture, wire listing, routing, parts lists, etc..  It does 
provide a computer aided equivalent of a taped master or drawing board with the 
advantage that things are always in perfect registration and one can work on 
selected layers.  

        General features are a 65 x 65 inch working area 12 layers deep.  
Resolution over this area is 0.001 inch.  At least this is the way it is 
labeled - the output can be scaled to anything so what is really provided is a 
65000 X 65000 point working space.  The layers can be turned on and off and 
assigned to any available color.  Lines, Pads (something a photoplotter can do 
- a small object drawn all at once), Symbols (a named collection of other 
objects), Arcs, and Labels can be entered.  The Symbol feature is particularly 
powerful since Symbols can be nested within Symbols to many levels (20) 
allowing construction of very complex objects with a few keystrokes.  

        The program being distributed through free channels is a limited 
version.  It has most programming features, however storage space is 
restricted.  Depending on how clever one is in conserving space, circuits can 
be designed with ten to twenty chips or about 100 components.  As can be seen 
from the demonstration files,  fairly elaborate designs can be created with the 
"free" version.  The program with full storage allocation will accommodate 
designs of about 300 chip equivalents.  

        You will find no appeal to guilt to get you to buy the registered 
version.  If you really use it, it will be in your interest to buy a license.  
If you try this demonstration version  on something small to test its features 
you are earning what you get by your work,  and helping us sell the product - a 
fair exchange we think.  Print FEATURES.DOC to learn the advantages of buying a 
licensed copy and to print an order form.  Print PLOTTER.DOC to learn about our 
low cost photoplotter.  

        Print DEMO.DOC for instructions for a quick tour around the facilities.  
TUTOR.DOC directs you through a few simple tasks.  Do not underestimate the 
effort required to learn to use this or any other CAD system.  As a member of a 
CAD selection committee for a large laboratory the author has reviewed many 
systems, it is an awful job.  My current view is that one just begins to know 
the features needed after six months use.  

                       ***** SPECIAL OFFER ***** 

        For a limited time, if you follow the procedure in PHOTOOL.DOC we will 
produce a phototooling set for your job.  We will plot anything you can get on 
8" x 10" film, for $25.00 per layer (Since we don't know when you will read 
this, this offer is subject to confirmation, see PHOTOOL.DOC for the 
procedure).  

        The following lists the documentation on this disk with a brief 
description of what each file contains.  We suggest you do DEMO.DOC and 
TUTOR.DOC and don't bother to look at much else until you have tried to do a 
few things.  KEYTREE.DOC will help show you where you are going in the program: 

FIRST.DOC 

        This document.  

MANUAL.BAT - PRINTS A MANUAL CONSISTING OF THE FOLLOWING SECTIONS: 
             (You may print individual sections if you wish)

        INTRO.DOC 

        Introduction and design philosophy.

        DEMO.DOC

        This leads you through a demonstration of what the system will do.  You 
        do not get to do anything, just look.  This is our "gee whiz" demo.  

        TUTOR.DOC

        This leads you step by step through a few simple tasks.  We have tried 
        to start with excruciating detail and gradually tell you less and less 
        as you become familiar with our general approach.  

        QUICK.DOC

        Quick summaries of how to perform the most common tasks.

        HOWTO.DOC

        How to do some more complex operations.

APPENDIX.BAT - PRINTS AN APPENDIX TO THE MANUAL CONSISTING OF THE FOLLOWING 
               SECTIONS (Or you can print them separately): 

        COMMANDS.DOC

        An alphabetical listing of the command keys.  This is the primary 
        reference document for all the operations that are available.

        KEYTREE.DOC

        Operation of this program is by use of the function keys.  Each key 
        press typically reassigns the keys to a new set of values.  KEYTREE.DOC 
        is a "map of the cave" showing the route through the menu keys with 
        very brief summaries of key operation.  The key menu is presently 
        fourteen layers deep and has hundreds of entries, many of them 
        repeated.  A number of the key operations are reentrant so that much 
        deeper entry is possible.  The design allows quick movement to a menu 
        that will do what you want.  It may be useful to print this out and 
        hang it on the wall when you first start using this program to remind 
        you of what is available and as an index for COMMANDS.DOC.  We thought 
        this would be very useful.  We find it almost impossible to read, but 
        we include it because we went to the work to prepare it and it might 
        fit someone's taste.  

        ERRORS.DOC

        Error messages and their meaning.

        STANDARD.DOC

        This document suggests a set of standards to get you started.  It pays 
        to approach a job in a consistent manner.  This file gives a set of 
        standard procedures for producing a design for a two sided plated 
        through hole board.  If you follow this standard we will be able to 
        plot your job for you with minimal hassle.  

        PLOTOUT.DOC

        How to generate a plot output file with sample file output.

THE FOLLOWING MISCELLANEOUS DOCUMENTS CAN ALL BE PRINTED WITH MISC.BAT 
OR THEY MAY BE PRINTED SEPARATELY:

        PHOTOOL.DOC

        How to get a set of phototooling prepared from your design.  Read this 
        before you prepare a job for us to plot.  

        UPGRADE.DOC

        A list of the planned upgrades.

        WISH.DOC

        A form to submit requests for improvements and upgrades.

        USERS.DOC

        We will collect and distribute useful libraries.  This is a form to 
        make a submission.

        BUG.DOC

        The bug reporting form and procedure.  Serious bug finders may write 
        for a version containing bug identification tools.  

        FEATURES.DOC

        Features of the full version of this program, and an order form.

        PLOTTER.DOC

        Features of our Photoplotter.

        UPDATE.DOC

        Changes and bug fixes by date.

        NEWBUG.DOC

        Known Unfixed Bugs