(comments in brackets are by G.HARRISON) 

                     Comments on BASIC Engineering Programs

                              Richard B. Kolbly, PE
                               Golden Rule Systems
                              5782 Turquoise Avenue
                          Alta Loma, California  91701


        FILTER.ASC  was originally written to run on a CP/M system  under 
        Microsoft MBASIC version 5.2.  The formulas were derived from the 
        Burr-Brown "Handbook of Operational Amplifier Active RC Networks" 
        (1966).  This program is confined to the multiple-feedback active 
        filter.   The  performance  of  the  filter is based  on  the  s-
        parameter response from standard servo theory.
        (Program does lp, hp and bp. Enter gain as positive)
    
        MFILTER.ASC  is  an  extension  of  FILTER.ASC.   it  allows  for 
        cascading of multiple-feedback filters and 'tuning' of the element 
        values.   In addition,  a routine has been incorporated to  allow 
        selection   of   standard  RETMA  values  for  circuit   elements 
        automatically.   The analysis portion allows multiple 'looks'  at 
        filter response and component changes.
        (Enter the gain, cutoff, and damping for each section & the program
        calculates the resistor and capacitor values for each section and
        the cascaded response)
 
        This  program  has  been used to design many active  filters  and 
        measured  results have agreed with performance predicted  by  the 
        program.  Note  that this program assumes an "ideal"  operational 
        amplifier. More precise results could be used by using NET85.ASC.  
        The  program  NET85.ASC  is an analysis  program,  not  a  design 
        program,  so  should  be  used after component values  have  been 
        determined.

        NET85.ASC is an adaptation of a network analysis program  written 
        up  in a trade magazine (EDN,  February 4,  1981 pp 126-133)  and 
        published  in  a BASIC-like Hewlett-Packard language for  one  of 
        their  early desktop computers.  The program has been  translated 
        into  BASIC  and many "bells and whistles" added for storing  and 
        loading circuits and results in files for use by other  programs.  
        The fundemental program has not been changed.
        (Hints to use:Number nodes starting from 1. Make the higest number
        node be ground. Components can be changed by first removing the
        component by putting a negative component across it.)
 
        RFDESIGN.ASC  is an adaptation of a Smith Chart program published 
        in  RF Design magazine for June of 1985 and has been  adapted  to 
        run  on the IBM-PC or compatable.   This program does not use any 
        of the advanced BASIC features,  and is currently being run on  a 
        Zenith Z-150 with GWBASIC with excellent results.
        (Runs ok on pc using basica)

        SABIN.ASC  is an adaptation of a signal analysis program by  W.E. 
        Sabin  published  in EDN for June,1983 (page 243).  It  has  been 
        adapted  to  run  under Microsoft GWBASIC.   SABINFIX.ASC  is  an 
        extension of SABIN.ASC to allow more direct user controls,  and a 
        list  of  the things done,  as well as allowing  dual  arrays  to 
        transform  and  manipulate.   Also,  file  operations  have  been 
        extended. 
        (Removed direct statements in file. Seems to run. I do not have
        Sabins original article so am unable to check further.)  

        (Disk.asc designs a parabolic dish and the sub-reflector for a
         Cassegrain feed. Looks ok)

        (Satellit.asc runs)




                                        1