Active Filter Design V1.5
                          (c) 1988 L.P. Kahhan

     This program is being placed on the market as SHAREWARE. It is not
     free software. The user is granted a limited license to use this
     product for a period of 30 days, at which time they are expected to
     either register the software for continued use, or to stop using the
     software and destroy all copies. This software may be freely
     distributed, either via disk, or bulletin board systems, provided that
     the program and documentation files are left intact and not modified
     in any way. Registering this software will not only enable you to
     obtain support and bug fixes, but will encourage the development of
     new and more diverse engineering software packages. To register, send
     a check or money in the amount of $15.00 order to:

                           Larry P. Kahhan
                           519 Fairman Lane
                           Langhorne, PA 19047

     Quantity discounts and site licensing info. available on request.




                                WARRANTY

     This software is provided without warranty, express or implied, of any
     kind. Although reasonable care has been exercised in the preparation
     and testing of this package, I can in no way be held responsible for
     any damages arising out of any use or mis-use of this package. It is
     up to the user to verify any designs produced by this package prior to
     implementation.





                            PROGRAM FEATURES


     In using this program, all entries must be entered as real numbers,
     not in engineering units, e.g., if entering a filter's cutoff
     frequency or center frequency, enter 2000, not 2K or 2 kHz. When asked
     to select a capacitor value, the value is to be entered in micro-
     farads, e.g. .01, not .01 uf.

     This package allows the user to quickly determine values for a variety
     of filter types as follows:

                    1. Low-pass
                       a. 2nd order Butterworth
                       b. 2nd order Chebychev
                       c. 4th order Butterworth
                       d. 4th order Chebychev

                    2. High-pass
                       a. 2nd order Butterworth
                       b. 2nd order Chebychev
                       c. 4th order Butterworth
                       d. 4th order Chebychev

                    3. Band-pass
                       a. For Q <= 10
                       b. For Q <= 40

                    4. Band-reject


     For each filter type, select the desired implementation from the menu
     and follow the on-screen instructions. As you work your way through
     the menus, you'll see that only specific values of filter order, gain,
     and Q are permitted. The program output is shown in schematic form on
     the CRT, and may be printed on any dot matrix printer supporting IBM's
     Pro-printer line graphics. Resistor values should be converted by the
     user to the nearest standard 5%, 2%, or 1% value, as the values
     calculated are pretty close to exact for the specified filter
     parameters, and may not be commercially available values. Future
     versions of this package may allow greater variety of selection of
     filter parameters, as well as the ability to generate a netlist for
     analysis by such commercially available packages such as ECA by TATUM
     LABS.



                          PROGRAM SOURCE CODE

     This is my first attempt at writing a shareware package, and was
     quickly put together using QuickBasic 4.0, the new MicroSoft Basic
     compiler. The source code will not be made publicly available, but
     I'll consider making custom modifications to this package on a
     consulting basis.




                      CHANGES FROM ORIGINAL RELEASE

      The bugs found and corrected in the original release are as
      follows:

             1. Bandpass filters with a Q>= 40 will now work. The
                original problem was due to a typographical error.

             2. Resistor values were rounded up to the nearest integer
                such that values of less than 1K were displayed as 0k.
                This has been corrected, and an attempt has been made
                to display at least 2 or 3 significant digits. Values
                of less than 1K will be displayed as, e.g., .5K for
                the value of 500 ohms. All values are still displayed
                in K-ohms.

             3. In checking through every path for one final test
                before releasing V1.5, bugs were found in 3 filter
                types affecting numerical accuracy. These filters were
                the 2nd order high-pass Chebychev, 4th order
                high-pass Chebychev, and multiple feedback bandpass
                filter. These bugs have been corrected.



      User feedback is welcome. If additional bugs are uncovered, please
      bring them to my attention. They will be corrected in the next
      release.