ADDRESS DECODING PROGRAM
                         by Bryon Moyer
 
This  program  generates Boolean Equations for  address  decoding
applications.   All  you have to provide is the number of address
pins (up to 16), and the bottom and top addresses of the range to
be decoded, and the program will crank out the Boolean Equations.
 
The procedure is really quite simple and painless.  The following
are  just some helpful hints in case something just doesn't  make
sense.
 
To invoke the program, merely type
 
                         DECODE

You  can  either generate equations on the screen,  or have  them 
sent to a file.   If you choose to have them sent to a file, they 
will be sent to a file named "decode.out".  Note that if you have 
run this program previously,  you will already have a file  named 
"decode.out"  if you did not rename it afterwards.   The  program 
will  let  you quit and rename the old file so that you will  not 
lose it.   If you continue the program instead, the old file will 
be lost.
 
The  prompts should lead you through the  procedure.   Note  that
when the addresses are requested,
 
     -- enter them in HEX (upper or lower case).
 
     -- use  as  many  digits as appropriate for  the  number  of
        address  bits  you are using,  including all leading  0s.
 
        For instance,  if the bottom address is 0, then you would
        enter 0 for 1 - 4 address bits,  but enter 000 for 9 - 12
        bits.   If you don't do this, the program will keep after
        you until you appease it.
 
     -- don't  enter an address that's out of range;  you'll  get
        caught.
 
     -- don't enter a bottom address that's greater than the  top
        address.   First,  this  makes  no  sense.   Second,  the
        program won't let you.
 
When  you enter an appropriate address,  the program will echo it
in BINARY.
 
After the top and bottom addresses have been entered, the program
will calculate the equations and print them out.  The output name
will  be Xi,  where i just keeps track of the number of equations
you have generated.  ALL input pins are specified as Aj,  where j
is  the  appropriate  bit.     Thus,   if  8  address  lines  are
specified,   then the  input  pins  will  be  A7...A0,   with  A7
being  the  most significant bit.
 
After  the equation has been displayed,  the program will  report
the number of product terms and inputs used.  This may be trivial
for some equations,  but, for instance, if you specify 16 address
lines,  and  have bottom address 0001 and  top address FFFE,  240
product terms  result;  I  challenge you to count them  as   they 
scroll merrily by.
 
At  this  point,  you will be offered the opportunity  to  decode
another address range.  When asked, if you enter anything but "Y"
(or "y"), it will assume "no", and terminate the program.
  
If  you have generated a file containing the   equations,  rename 
the  file after you are done if you wish to keep it.   Otherwise, 
the  next time you run this program,  you will have to rename  it 
then.  You will   also need   to use an editor to perform  global 
replacements   of  default   pin  names  with the ones you  want.     
Note  that  the equations are generated as active HI signals;  if 
you want active LO signals,  be sure to add a slash ('/') to  the 
left-hand  side of the equations.    You can then merge this file  
in with  your  PDS file.
 
Happy decoding...