SECTION                    PAGE #

INTRODUCTION
  Purpose of this software ..................  1
    Current Capability ......................  1
    Future Enhancements .....................  2
      Support for Abel ......................  2
      Support for Cupl ......................  2
      Reduction of Boolean Equations ........  2

GETTING STARTED
  Hardware Requirement ......................  3
    Minimum Required System .................  3
    Recomended Hardware .....................  3
  Main Menu Commands ........................  4
    Naming the pins .........................  4
    Entering the signal list order ..........  4
    Drawing the signals on the screen .......  4
    Creating the PALasm 2 formated file .....  5
    How to exit and save your work ..........  6
    How to exit without saving your work ....  6

SAMPLE DESIGNS
  4 bit counter .............................
    with reset ..............................
    with set, reset, and load ...............
  8 bit ring counter ........................
    with reset ..............................
    with reset and hold .....................

ADVANCED FEATURES
  More than one state machine in a PAL ......
  Extended simulation capability ............
  Designing a continuous counter ............

LIMITATIONS
  *** CAUTION *** ...........................

WHO TO CONTACT WITH PROBLEMS ................

 A. INTRODUCTION

    1. Purpose of this software

       a) Current Capability

               The TiDE program is very nearly a finished product.  In
          the near future there will be a few minor additions to the
          software which will be discussed in the next paragraph.
          Aside from these additions I will take sugestions from users
          of the software on what they would like to see added or
          changed.  In the present revision [ver 2.16] only registered
          outputs are supported.  This will be changed in ver 2.17 and
          latter versions.
               The TiDE software will allow a design engineer to enter
          a minimal amount of information about the actual device to
          be used and then enter a description of what the state
          machine should do by drawing the timing diagram on the
          screen of the PC or PC clone.

       b) Future Additions

          1) Support for Abel

                  In the near future TiDE will ask you if you will be
             using MMI's PALasm 2 or Data I/O's ABLE software.  It will
             then generate the proper file for use with your software.

          2) Support for Cupl

                  Due to the fact that I have not seen as many customers
             using the Assisted Technology CUPL software I will be
             waiting to see the number of requests that I get for this
             feature.  If enough people want it I will do it.

          3) Reduction of Boolean Equations

                  I had intended to include a boolean reduction program
             for use with PALasm 2 but I now feel that it would be better
             to release a working version of the program and then add the
             reduction routine in a future release.



 B. GETTING STARTED

    1. Hardware Requirement

       a) Minimum Required System

               The minimum system that this software has been tested
          on was a DATA GENERAL ONE laptop computer with 256 K of
          memory.  This system is an MS Dos machine with a few
          exceptions.  I feel that if it runs on this machine it
          should run on any MS Dos computer.  If you find an MS Dos
          machine that this will not run on please contact me with the
          details.
               Due to the method used for drawing the wave forms you
          do not need to have any graphics capability at all.  The
          program is small enough to only require a single floppy disk
          to hold both the program and the files created by the
          program.  With these limited requirements it should be
          possible to run TiDE on allmost any MS Dos computer.

       b) Recomended Hardware

               There is only one piece of hardware that would make a
          nice addition and that is an IBM graphics printer.  The
          Epson printers and their clones will not work for screen
          dumps of the timing diagram without the use of special
          software such as Print Works by SoftStyle.  The reason for
          this is that the graphics on the screen are only the
          extended character set of the IBM PC and are not really
          graphics at all.  On an Epson or equivalent the graphics
          characters are not there and instead you will get italics
          characters.  This is only a limitation if you wish to get a
          hardcopy of the screen while in the drawing mode.


    2. Main Menu Commands

       a) Naming the pins - F1

               This is the first option on the main menu and it is
          used to enter the mneumonics that you wish to assign to the
          inputs and outputs of the device to be designed.  To invoke
          this Press the F1 key while the main menu is desplayed. This
          is the first thing that must be done on any new design.

       b) Entering the signal list order - F2

               This option does not need to be used unless you wish to
          have the signals shown in an order other than the pin number
          order.  When you use this option you have the ability to
          have the same signal displayed as many times as you wish.
          The only warning is that a signal that is showing in two or
          more places on the screen should not be edited.  You will
          get very strange results if you try to do this.  Even with
          this precaution you may wish to display the same signal more
          than once to allow you to compare the timing of this signal
          to another.

       c) Drawing the signals on the screen - F3

               This is the fun part.  Once you have entered the pin
          names you may begin to draw the signals by using this
          option.  A menu of the available commands is located at the
          bottom of the screen.  This menu lists all of the keys that
          may be used to enter data, edit signals, or control the
          screen.
               The first part that we will discuss is the method for
          entering the data.  The valid input keys for this are the
          "X", "H", and the "L" keys.  Upper or lower case will work.
          The meaning of the keys are:
            X : don't care - the signal is undefined at this point.
            H : high -
                on input signal - pin will be high during the next
                                  rising edge of the clock.
               on output signal - this signal is to go high after the
                                  next rising edge of the clock if the
                                  previous columns conditions are met.
            L : low - same as for H except defines the low condition.

               The character entered will be displayed directly above
          the cursor after which the cursor will advance one position.
          The four arrow keys will all move the cursor in the
          indicated direction.  The cursor may not be moved off of the
          screen nor will it scroll the screen when it hits the top or
          bottom.  If you wish to view the next five signals press the
          pgdn key on the cursor control keypad.  To view the previous
          five signals use the pgup key.  Due to the fact that there
          are seven signals displayed on the screen there will always
          be a two signal overlap for continuity.
               The last of the control keys are the ins and del keys
          again located on the cursor control keypad.  These keys will
          allow you to insert a spot into a signal which can then be
          changed to the proper value.  The cursor should be placed
          under the first location that is to be moved to the right to
          make room for the new value.  The del key will delete the
          value directly above the cursor and move everything to the
          right of the cursor left to fill the hole.  The use of these
          two keys will help when you wish to make a small change
          after entering a long signal so as not to have to enter the
          entire signal again.

       d) Creating the PALasm 2 formated file - F4

               After you have entered the timing diagram you are ready
          to produce the text file which will contain the heading,
          equations and the simulation in a PALasm 2 format.  If you
          follow all the steps carefully in your design you should not
          have to use an editor on the file at all.  It is usually
          possible to generate a file which is complete and ready to
          be assembled into the fuse pattern for your part.
               When this section starts it will ask you for a file
          name.  At this point you should enter the name for the
          PALasm 2 file.  Standard convention dictates that the
          extension to the file name should be ".PDS", this stands for
          Pal Design Specification.  Care should be taken here not to
          enter a filename that is already being used,  at present no
          checking is done to insure that a file is not overwritten
          when the new file is created.  This is a feature that will
          be added to a future version.
               After you have entered the filename you will be asked
          several questions.  If you are familiar with PALasm 2 you
          will recognize that each of these questions is for the
          heading of the file.  If you are just testing a portion of
          your design and this will not be the final version of your
          design you may just press the ENTER key and leave the
          heading blank.  The exception to this is the part type,  if
          you do not enter a part type the software will declare the
          part as a PALXXXX in the text file.  At this point the file
          will not work with palasm and you will have to use an editor
          to change the part type to a valid one.  This can be used to
          your advantage if you wish to get the equations and then go
          back to decide which Pal you wish to use.
               The last question will ask you if you are using a part
          which has the capability of programmable output polarity.
          If you answer this question yes the software will determine
          if an output should be written active low or active high
          based on which will require the least number of product
          terms.  If you are not using a part with programmable
          polarity all equations will be written active low.  An
          example of a part with programmable output polarity is the
          PAL16P8 vs. the PAL16L8.  The P in the part number
          designates that the part has programmable polarity.  Many of
          the new parts being done by MMI have the added feature of
          programmable polarity.

       e) How to exit to Dos and save your work - F5

               When you have finished entering information or if you
          are interrupted you may save your work and continue it at a
          latter time.  This will save all pin names and signal values
          that have been entered up to this point.  This will also
          allow you to come back into the screen editor and change the
          timing diagram if you find a problem in the PAL at a latter
          date.

       f) How to exit to Dos without saving your work -F6

               I hope that you will not need this option but if you do
          here it is.  If you make a major mistake while editing your
          design file and you decide that you would like to lose the
          changes that have been made since the last save you may do
          so by using this key.  A check is made to insure that you
          really want to do this as there is no turning back once it
          is done.


 C. SAMPLE DESIGNS

    1. 4 bit counter

       a) with reset



       b) with set, reset, and load




    2. 8 bit ring counter

       a) with reset



       b) with reset and hold




 D. ADVANCED FEATURES

    1. More than one state machine in a PAL

            Due to the way that this software generates the
       equations to implement your design it is possible to define
       multiple independent state machines in the same device.  In
       order to do this all you will have to do is insure that the
       seperate sections are not drawn under each other.  This
       means that at least one column of nothing but don't cares
       must seperate the sections.  You can use this method to
       implement several different sections in the same device.

    2. Extended simulation capability

            When the simulation section of the output file is being
       generated it works from the timing diagram.  The only signal
       lines that it looks at are the input signals and the control
       signals such as output enable.  By extending one of the
       input signals such as a output enable type simulation will
       continue.

    3. Designing a continuous counter

            In order to make a state machine that will loop back on
       itself you will need to show the starting point for the loop
       as the last column of the design.  For examples of this and
       other special features look at the sample files on this
       disk.  Files with an extension of ".SIG" are design examples
       that you can use to experiment with.


 E. LIMITATIONS

    1. *** CAUTION ***

            This section will be used to list bugs that have been
       found and reported.  I will try to keep this section of the
       manual current.  Since this is the first official release of
       the program I do not have any reported bugs as yet.



 F. Who to contact with problems

         If you have a problem with the operation of this
    software or if you decide that a feature needs to be added I
    have a computer bulletin board which you may use to leave me
    a comment.  The phone # for the board is (513) 866-5157.
    This board will also contain the latest version of this
    software along with the manual, as well as having other
    utility programs to help you in designing with MMI Pal
    devices.


 G. Credits

    Author :            Bill Hollon
                        Field Applications Engineer
                        Monolithic Memories Inc.
                        261 Trumpet Drive
                        Dayton, Ohio      45449


    Concept and Ideas : Mike Wier
                        Regional Sales Manager
                        Monolithic Memories Inc.


    Anyone who makes a contribution of a signifigant idea will
    be added to this list.  So send in any and all ideas for
    improvement.

                                 Thanks;

                                       William R. Hollon