In radio and television broadcasting (as well as in amateur 
radio) the measure of signal transmission quality from the 
transmitter through the transmission line to the antenna is the 
ratio of the forward voltage (or current) to the reflected voltage 
(or current). This ratio is called SWR, or Standing Wave Ratio. It 
is a simple ratio and can be mathematically represented as: 

              SWR = Reverse Voltage / Forward Voltage 

   In commercial broadcasting VSWR or Voltage Standing Wave Ratio 
is the most commonly used parameter. It reflects the quality of 
the impedance match of the transmission line to the antenna system 
or the combination of transmitter, transmission line, and antenna 
system. It is the ratio of the square root of the Reflected Power 
to the square root of the Forward Power. This ratio is called 
GAMMA in several texts and can be mathematically represented as: 

         GAMMA = sqrt( (Reflected Power / Forward Power) ) 

   Thus, to find the VSWR of an antenna system, one needs to know 
the forward and reflected powers (assuming matched impedances). 

               VSWR = ( (1 + GAMMA) / (1 - GAMMA) ) 

   However, if the Forward Power and VSWR are known, the reflected 
power can be computed: 

 Reflected Power = sqr( (VSWR - 1) / (VSWR + 1) ) * Forward Power 

   Because many VSWR meters are accurrate to only two decimal 
places, there can be a large area of reflected power values given 
for a given VSWR. For example, assuming a forward visual power of 
18.6 KW at 100% power and a VSWR of 1.06, a reflected power 
anywhere from 13.3 Watts to 18.4 Watts could be expected to be 
measured. Therefore, this program displays VSWR to the nearest 
hundredth and the reflected power to the nearest tenth of a watt. 

   This program will compute the VSWR and/or Reflected Power of 
any television aural and visual transmitter. Under the current FCC 
ruling concerning measurement of aural power (73.1560c(2)), 100% 
is the maximum allowable aural power any TV station can radiate 
and represents 22% of the station's peak visual power. When 
calibrating the visual reflectometer (73.663b(1)(2)(3)), the peak 
video power of the transmitter should be measured with a wattmeter 
of known calibration, with carrier modulated with black picture at 
75% set-up and 25% sync at 4.8 usec horizontal sync pulse duration 
into a dummy load of substantially zero reactance and resistance 
equal to the transmission line characteristic impedance, visual 
carrier only. The wattmeter reading then should be multiplied by 
the FCC correction factor of 1.68 to obtain the peak visual power 
of license. 

   This program was written to satisfy a need to correlate remote 
monitor data against the calibrated local transmitter forward 
power and VSWR reflectometers.