ID:QM Quarterdeck Memory Driver Interface
Quarterdeck Developers Note



The Quarterdeck Memory Driver interface is available in version 4.2x and above of
QEMM.  It allows the developer(s) of third party applications to determine if a
Quarterdeck Memory Driver (QDMEM) is present, which driver (QEMM, VIDRAM etc.) is
present, and it will enable the third party developer to determine where the high
memory chain begins. 

QEMM permits this through the INT 2F Resident Program Communication Interface
(RPCI).  For the rest of this documentation, the term 'driver' will normally refer
to a program that uses RPCI irrespective of its method of implementation (device
driver or TSR).  If you are unfamiliar with RPCI or INT 2FH please refer to
Appendix B for information on using this specification to communicate with a QDMEM
driver.

In order to communicate with a QDMEM driver such as QEMM you will need to
determine the RPCI identification number.  Trying different values for the RPCI
identification number and calling the 2FH vector using the QDMEM_CHECK_PRESENCE
subfunction your program can determine the identification code a QDMEM driver is
using.  If the call returns with a special response signature, then the
identification number being tested is the correct number for that system.

It is necessary that your program follow the convention of trying identification
numbers starting at D2H to FFH, then C0H to D1H.  Following this convention
exactly as specified is very important.

In order to determine whether an identification number is free (in addition to the
QDMEM_CHECK_PRESENCE call), the driver can utilize the following two facts:

If the segment of the previous INT 2FH vector is 0 (zero) then the vector has not
been initialized yet and hence nothing has hooked 2f.

If the AL register returns with a non-zero value (usually FFH) when it has
originally been set to 00H and the previous INT 2FH called, then the
identification number in AH is probably in use by a driver - this is a generalized
convention in use by many software manufacturers.  If however, the call returns
with AL equal to 00H, then that identification number is considered free.

The QDMEM_CHECK_PRESENCE call uses this convention, but also sets a response
signature in BX,CX and DX if a special calling signature resides in those
registers when the call was made.  This was done so that an RPCI driver can check
if another RPCI specific driver is loaded.

QDMEM_PREFERRED_ID  EQU  0D2H ;First function number (AH) to try to use


This is the first RPCI ID number to use when determining the QDMEM driver RPCI ID. 
Once this ID number is determined, it should be passed in AH with each consecutive
call to INT 2f.


QDMEM_CHECK_PRESENCE          Check for Quarterdeck Memory Driver Presence

     AL   =    00H  
     BX   =    'QD' ;(5144h)  QDMEM_BX_SIG
     CX        'ME' ;(4D45h)  QDMEM_CX_SIG
     DX   =    'M0' ;(4D30H)  QDMEM_DX_SIG

This subfunction should be called by your program to determine the QDMEM
identification number (RPCI identification).  If a QDMEM driver is installed using
this ID number, it will return the following:

     AL   =    FFH  ;(-1)
     BX   =    'ME' ;(4D45H)  QDMEM_BX_RESPONSE
     CX   =    'MD' ;(4D44H)  QDMEM_CX_RESPONSE
     DX   =    'VR' ;(5652H)  QDMEM_DX_RESPONSE


QDMEM_DVR_ID                  ;Determine Quarterdeck Memory Driver Type

     AL   =    01H            ;Subfunction 1

This subfunction should be called with the following signatures to determine if
the QDMEM driver installed is QEMM, if there is High RAM present, and to determine
if VIDRAM and HIMEM are present:


     Signature to check for QEMM (subfunc 1)

     BX   =    'QE' ;(5145H)  QDMEM_QEMM_BX_SIG
     CX   =    'MM' ;(4D4DH)  QDMEM_QEMM_CX_SIG
     DX   =    '42' ;(3432H)  QDMEM_QEMM_DX_SIG

     Response from QEMM (subfunc 1)

     BX   =    'OK' ;(4F4B)   QDMEM_QEMM_BX_RESPONSE

     Returns in ES:DI the function entry point.  The following calls can then be 
     made to that entry point:

     NOTE: All routines return CY if not supported or if failed.

          QEMM_GET_STATUS         EQU     0 ;AH
               ; Returns AL = 0 if on
               ;         AL = 1 if auto/on
               ;         AL = 2 if off
               ;         AL = 3 if auto/off
     
          QEMM_SET_STATUS         EQU     1 ;AH
               ; Takes   AL as above

          QEMM_GET_VERSION        EQU     3 ;AH
               ; Returns 
                         BX = version number

     Signature to check for high RAM driver (subfunc 1)

     BX   =    'HI' ;(4849H)  QDMEM_HIGHRAM_BX_SIG
     CX   =    'RA' ;(5241H)  QDMEM_HIGHRAM_CX_SIG
     DX   =    'M0' ;(4D30H)  QDMEM_HIGHRAM_DX_SIG

     Response from high RAM driver (subfunc 1)

     BX   =    'OK' ;(4F4BH)  QDMEM_HIGHRAM_BX_RESPONSE

Returns in CX the first high segment, in DX the reserved owner.  QEMM uses     
the same structure for the high memory chain as DOS does for its memory     
chain.  You should follow the same procedures you would normally to traverse    
the memory chain using the segment returned in CX as the start of the chain.  If
you are unfamiliar with the DOS memory chain, please see APPENDIX A for references
that will provide information on it. 



     Signature to check for HIMEM (subfunc 1)

     BX   =    'HI' ;(4849H)  QDMEM_HIMEM_BX_SIG
     CX   =    'ME' ;(4D45H)  QDMEM_HIMEM_CX_SIG
     DX   =    'MQ' ;(4D51H)  QDMEM_HIMEM_DX_SIG

     Response from QD HIMEM driver (subfunc 1)

     BX   =    'OK' ;(4F4BH)  QDMEM_HIMEM_BX_RESPONSE
     
     Returns in ES:DI the function entry point



     Signature to check for VIDRAM (subfunc 1)

     BX   =    'VI' ;(5649H)  QDMEM_VIDRAM_BX_SIG
     CX   =    'DR' ;(4452H)  QDMEM_VIDRAM_CX_SIG
     CX   =    'AM' ;(414DH)  QDMEM_VIDRAM_DX_SIG

     Response from QD VIDRAM driver (subfunc 1)

     BX   =    'OK' ;(4F4BH)  QDMEM_VIDRAM_BX_RESPONSE

     Returns in ES:DI the function entry point










Following is an example procedure to check for the presence of a QDMEM driver and
determine the RPCI ID number that it is using:

include     qdmem.equ ; equates are described above

;ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
;³ QDMEM_Presence (Checks for presence of QDMEM driver)      ³
;ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
;³ QDMEM_Presence bombs AX                                   ³
;ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
;³ Success:                                                  ³
;³  ah=QDMEM QDI ID#                                         ³
;³ Failure:                                                  ³
;³  ah=0                                                     ³
;ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

QDMEM_Presence   PROC
        push    bx
        push    cx
        push    dx
        mov     ax,352fh                ; DOS Get Vector returns es:bx 
        int     21h
        mov     cx,es
        test    cx,cx                   ; segment of 2F handler is 0? 
        jz      qdmem_noqdmem           ; no 2f handler found
        mov     ah,QDMEM_PREFERRED_ID   ; RPCI ident. number
        mov     al,QDMEM_CHECK_PRESENCE

qdmem_try_next:
        mov     bx,QDMEM_BX_SIG
        mov     cx,QDMEM_CX_SIG
        mov     dx,QDMEM_DX_SIG
        push    ax
        push    ds
        int     2fh
        mov     di,ax
        and     di,0ffh                 ;And off high byte
        pop     ds
        pop     ax
        jz      qdmem_noqdmem           ;If no response, this func is free
        cmp     di,0ffh                 ;Someone responded incorrectly?  
        jne     qdmem_bump_func         ;If so, cannot use this func
        cmp     bx,QDMEM_BX_RESPONSE    ;Signature matches?
        jne     qdmem_bump_func
        cmp     cx,QDMEM_CX_RESPONSE
        jne     qdmem_bump_func
        cmp     dx,QDMEM_DX_RESPONSE
        je      qdmem_done              ;AH = xdi id

qdmem_bump_func:
        inc     ah                      ;Bump func byte
        jnz     qdmem_check_done        ;Jump if not yet wrapped
        mov     ah,0c0h                 ;Wrap down to 0C0h

qdmem_check_done:
        cmp     ah,QDMEM_PREFERRED_ID   ;Wrapped back to start?
        jne     qdmem_try_next          ;If not, try this func

qdmem_noqdmem:
        xor     ah,ah                   ;no response so zero out ah for return

qdmem_done:
        pop     dx
        pop     cx
        pop     bx
        ret
QDMEM_Presence    ENDP



                                  APPENDIX - A

References:


The Waite Group's MS-DOS Papers for MS-DOS Developers and Power Users.
Howard W. Sams & Company - ISBN# 0-672-22594-8
Chapter 6, Page 160.

The Waite Group's MS-DOS Bible - Second Edition by Steven Simrin
Howard W. Sams & Company - ISBN# 0-672-22617-0
Chapter 12, page 220.

                                  APPENDIX - B




             INT 2F Resident Program Communication Interface (RPCI)


Resident Program Communication Interface

Quarterdeck's specification for communicating with external drivers.  These
drivers may be implemented either as a DOS device driver (loaded by CONFIG.SYS),
or a Terminate and Stay Resident program (TSR).

For the rest of this documentation, the term 'driver' will normally refer to a
program that uses the RPCI irrespective of its method of implementation (device
driver or TSR).


Interrupt 2FH
 
All communication with the external driver occurs through interrupt 2FH. As this
interrupt vector is often multiplexed for several different functions, RPCI uses
an identification number (passed in the AH register) to identify the call as an
RPCI message.
 
For maximum flexibility, this identification number may vary from
configuration to configuration.  A later section describes the convention a driver
should use to determine the RPCI identification number.



Cascading Interrupt 2FH
 
"Hooking up" to INT 2FH is performed by pointing the INT 2FH vector to a program's
own INT 2FH handler code using the DOS Set Vector call.  It is this piece of code
which monitors the AH register whenever it is called to determine if the call is
in fact an RPCI call.
 
Note, however, that an RPCI driver must log the previous interrupt 2FH vector when
it is initializing since it is necessary for the RPCI subfunction routines to
"cascade" to any other driver that was loaded before itself. This requirement is
necessary for multiple RPCI drivers to coexist in the system.
 
"Cascading" is the process of calling the code that was being pointed to by an
interrupt vector before it was redirected to a program's new interrupt handling
code.
 

This is the basic principle behind the operation of the Resident Program
Communication Interface.



Driver Implementation Techniques
 
An RPCI driver can be implemented in one of two ways - as a device driver, or as
a Terminate and Stay Resident program (TSR).
 

RPCI Device Driver
 
If implementing an RPCI device driver (loaded by CONFIG.SYS), hooking up to the
RPCI will be performed in the driver's initialization procedure (driver command
code 0).  The 2FH interrupt and RPCI subfunction routines may be located anywhere
within the device driver.
 

RPCI TSR
 
A TSR program normally consists of two parts - a resident portion and a transient
portion.  The transient portion (which often performs initialization and installs
the resident portion) will usually contain the routines to hook up to the RPCI. 
The resident portion will contain the 2FH interrupt and RPCI subfunction routines.

Hooking up to the RPCI
 
In order to hook up to the RPCI, a driver must perform several tasks.  It must
determine the RPCI identification number that it will use.  In addition, it must
both save the previous INT 2FH vector as well as setting the vector to point to
the driver's 2FH interrupt handler.
 
Note that it is the first RPCI driver loaded that will choose the RPCI
identification number (it does this by determining that it is the only RPCI driver
in the system) and all subsequent RPCI drivers inquire the RPCI driver loaded
previous to it what the identification number is. Because of this "chaining
effect", all RPCI drivers must implement an RPCI call (the RPCI_CHECK_PRESENCE
call, described later) correctly. 

RPCI ID Number

Determining the RPCI number
 
One RPCI call that should be made is the RPCI_CHECK_PRESENCE call.  Trying
different values for the RPCI identification number and calling the previous 2FH
vector using the RPCI_CHECK_PRESENCE subfunction a driver can determine the
identification code when loaded after another RPCI driver.  If the call returns
with a special response signature, then the identification number previously used
is the correct number for that system.
 
If the RPCI driver is the first one loaded into the system, then this technique
used as is would fail and needs to be extended (since no driver would already
exist to respond to the RPCI_CHECK_PRESENCE call).  Consequently, in addition to
the above, if the RPCI driver finds a free identification number that is not being
used by any other driver (whether RPCI or otherwise) then it should assume that
it should mark it the RPCI identification number.
 
In order for this extended technique to perform correctly, it is necessary that
the driver follows the convention of trying identification numbers starting at DEH
up to FFH, then C0H to DDH.  Following this convention exactly as specified is
very important.
 
In order to determine whether an identification number is free (in addition to the
RPCI_CHECK_PRESENCE call), the driver can utilize the following two facts:
 
If the segment of the previous INT 2FH vector is 0 (zero) then the vector has not
been initialized yet and hence any identification number could (theoretically) be
chosen.
 
If the AL register returns with a non-zero value (usually FFH) when it has
originally been set to 00H and the previous INT 2FH called, then the
identification number in AH is probably already in use by some other driver - this
is a generalized convention in use by many software manufacturers. If however, the
call returns with AL equal to 00H, then that identification number is considered
free.
 
The RPCI_CHECK_PRESENCE call uses this convention, but also sets a response
signature in BX,CX and DX if a special calling signature resides in those
registers when the call was made.  This was done so that an RPCI driver can check
if another RPCI specific driver is loaded.
 
Setting the 2FH Vector
 
Once the identification number is found, the driver can point the INT 2FH vector
to its own 2FH interrupt handling routine.  This should be done by using the DOS
Set Vector call.


RPCI Installation                

Pseudo Code example
 
The complete installation procedure for hooking up to the RPCI can be summed up
in the following Pseudo Code:
 
   preferred_id = DEH
   save INT 2FH vector as previous INT 2FH vector
 
   IF segment of previous INT 2FH vector = 0 THEN
 
      RPCI_id = preferred_id
 
   ELSE
 
     FOR id = preferred_id to FFH and then C0H to preferred_id - 1
 
        CALL previous INT2FH vector with AH = id, AL = 0
                             and BX,CX,DX = RPCI signature
 
        IF AL = 0 THEN
           RPCI_id = id              /* This value is not in use */
           JMP hook_vector:
 
        ELSEIF AL = FFH and BX,CX,DX = RPCI response signature THEN
           RPCI_id = id    /* Another RPCI driver uses this value */
           JMP hook_vector:
        ENDIF
 
       /*Value returned is non-zero - this value must be in use    */
        NEXT id
 
       OUTPUT "No id numbers available"
       END driver installation with error
 
    ENDIF
 
LABEL hook_vector:
   hook int 2FH to 2FH interrupt handler
 
END successful driver installation
 
Note that the RPCI calling and response signatures are defined in the
RPCI_CHECK_PRESENCE call - see that subfunction for details
 

2FH Interrupt Handler
 
The 2FH interrupt handler code is fairly simple.  It should check to see if AH
equals the RPCI identification number.  If it does not, then it should immediately
cascade to the previous 2FH vector.
 
If the identification numbers match, then the handler can dispatch the call to the
appropriate RPCI subfunction routine.
 
Here is the Pseudo Code for the 2FH interrupt handler:
 
 
IF AH = RPCI_id THEN
  STI
  JMP RPCI subfunction routine based on AL
ELSE
  JMP previous 2FH handler
ENDIF


RPCI Subfunctions
 
The type of RPCI subfunction is determined by the value in the AL register when
an INT 2FH is made.
 
All calls must be passed on from one RPCI driver to the next.  For some calls, an
RPCI driver should do its work before passing the call along.  For others, it
should pass the call along first and then do its work.
 
The driver should not perform any DOS or BIOS calls during any work
performed in an RPCI subfunction.  




  ************************************************************************
  *This technical note may be copied and distributed freely as long as it*
  *is distributed in its entirety and it is not distributed for profit.  *
  *         Copyright (C) 1990-2 by Quarterdeck Office Systems           *
  ************************ E N D   O F   F I L E *************************