Tips and Tricks for Using the SupraFAXModem with PCB/FaxMail

                            by Rod L. Renner, SysOp
                               The Lightning Rod BBS
                               Silver Spring MD 20904
                               BBS: 301-622-0708 (v.32bis)

Introduction

     I run a PCBoard system using a SupraFAXmodem v.32bis modem.  The modem 
     has worked well with this system, but I have been interested in using its 
     FAX capability as well.  Mark Herring's PCB/FaxMail gateway provided an 
     excellent means to implement this feature, but his program was written 
     primarily for use with Bit Corporation's BitFax software, which does not 
     currently support the Supra modem.  The only DOS based facsimile software 
     program that currently supports the Supra modem is FaxTalk Plus by 
     Thought Communications, Inc.  Fortunately, it has enough of the critical 
     features needed to implement a working FaxMail gateway on the PCBoard 
     system.  

     Since BitFax and FaxTalk Plus operate differently, setting up a FaxTalk 
     Plus based system requires several changes in procedure, some of which 
     were determined by trial and error, or by calling Thought Communications' 
     Tech Support line.  It was also necessary to write a customized program, 
     called FPCHECK, to read the FaxTalk Plus log file and report to FaxMail 
     the success or failure of the fax transfer.  A copy of FPCHECK is 
     included in this package.  

     In order to use FaxTalk Plus with FaxMail, the user should have read or 
     reviewed the documentation that accompanies both products.  These notes 
     are intended to point out key settings or techniques which can be used to 
     make the FaxMail/FaxTalk combination work.  

FaxTalk Plus Installation and Configuration

     Install the FaxTalk Plus programs following directions in the FaxTalk 
     documentation and FaxMail instructions.  These examples assume that the 
     FaxTalk Plus software is installed in C:\PCB\FAX and that the location of 
     the WORK directory for outgoing messages, including those converted to a 
     FaxTalk format, is C:\FAXOUT.  If you use a different directory, please 
     adjust these instructions accordingly.  There are several important 
     settings that must be used if it to be successful.  

     CONFIGURE option in the FINSTALL program.

          o   NOTE that FaxTalk Plus requires that the modem return numeric 
              result codes ('V0' setting in the 'Modem Init String') rather 
              than word result codes which are required by PCBoard.  Before 
              returning to PCBoard, the modem must be reset to its original 
              settings for PCBoard by sending an ATZ command; otherwise, 
              PCBoard will not be able to communicate with the modem.  This 
              can be done with a simple ECHO command or by running a shareware 
              program such as ATSEND.  
              
     CONFIG options in the FAXPLUS program.
     
          o   Under the 'SYSTEM' menu, be sure to set the following critical 
              options: 

              Background Operation [Y/N]                         - N
              Automatic Answering [Y/N]                          - N
              Number of Time(s) to Try Dialing [1-8]             - 1
              Error Correction Mode Enabled [Y/N]                - N
              Send File Directory                - C:\FAXOUT

              Background Operation must be set to [N]o in order to insure that 
              the program waits while the fax is sent and control is not 
              allowed to proceed until completion or failure.  Since this is a 
              send-only system, Automatic Answering should be set to [N]o.  
              The Number of Time(s) to Try Dialing MUST be set to [1] time!!  
              If this number is set higher than 1 and the transmission fails, 
              FaxTalk would automatically schedule it for retransmission, but 
              allow control to continue resulting in unpredictable, but 
              undesirable consequences!  Due to a firmware error with the 
              Supra modem (according to Thought Communications) and by 
              frustrating trial-and-error on my part, Error Correction Mode 
              must be Disabled ([N]o).  Enabling ECM causes the fax program to 
              hang up unexpectedly after transmitting one page or less and to 
              report a transfer failure.  Finally, the Send File Directory may 
              be set to point to the location of the WORK directory for FaxMail.
 
          o   Under the 'CONVERT' menu, set the following option:

              Delete Converted Images After Sending [Y/N]          - Y

              This setting will cause the FaxTalk converted images to be
              deleted after they are sent, as there is no need to keep them
              around.  FaxMail will take care of deleting the original ASCII
              test file.

     Other settings are at the users discretion or at the suggestion of the 
     FaxTalk software.

FaxMail Main Menu Selections

     Paths & Filenames

          Name/Loc of the WORK file................. C:\FAXOUT\WORK

               The path chosen should match the Send File Directory setting as 
               used when configuring FaxTalk Plus SYSTEM menu.  I recommend 
               that the filename (WORK) NOT contain a file extension.  This 
               allows FaxTalk to create the pages of converted images with 
               filenames WORK.001, WORK.002, etc.  This will also be the 
               directory in which FaxTalk writes its log file (SEND.LOG).  

          Fax Software DOS command.................. RUNFAX %FILE %PHONE

               In the C:\PCB\FAX directory, create a BATch file called 
               RUNFAX.BAT which contains the following commands: 

                    CONVERT %1 /e /f
                    SENDAFAX %1 %2

               These two FaxTalk programs convert the %FILE file passed by 
               FaxMail (C:\FAXOUT\WORK) into faxable images (WORK.001 etc.), 
               then sends the converted image to the recipient fax at the 
               phone number.  '/e' tells CONVERT that WORK file is ASCII text 
               while '/f' selects fine resolution.  
          
          Fax Software VERIFY command........  FPCHECK C:\FAXOUT\SEND.LOG

               FPCHECK.EXE is a customized program that will read the last
               entry in the log file created by SENDAFAX, then create the
               file named "OK" in the current directory to report the status
               (SUCCESS, BUSY, or NOGOOD) back to the FaxMail gateway.  Be
               sure to copy FPCHECK.EXE included in this package into the
               C:\PCB\FAX directory.

          Cycle count for temporary work files................. 0

               Set this value to 0 as each fax will be processed before the
               next one is sent.

          Use other values as suggested in the FaxMail documentation for
          Paths & Filenames.

     Fax Type Definitions

          The *TYPE: and *INCLUDE: commands are probably not available with
          the FaxTalk program unless the user can think of a clever way to
          convert an uploaded file into a FaxTalk file and imbed into the
          message the appropriate '&&filename' statement as outlined in the
          FaxTalk manual.

FAX.BAT or $$LOGOFF.BAT files

     The sequence of commands for running the FaxMail gateway using a sample
     FAX.BAT file would look something like this:

          CD \PCB\FAX          <- Make this the default directory
          FAXTSR /l            <- Loads FAXTSR into memory
          FAXMAIL /SCAN        <- Run FaxMail gateway
          FAXTSR /u            <- Unload (remove) FAXTSR from memory
          ECHO ATZ >COM1       <- Reset the modem!! (Use the right COM port)
          CD \PCB              <- Change back to \PCB directory
          BOARD                <- Rerun PCBoard

     NOTE the 'ECHO ATZ >COMx' command.  It is VERY IMPORTANT to include a
     command to reset the modem on its COM port back to its PCBoard settings,
     particularly the use of word result codes, otherwise PCBoard will be
     unable to communicate with the modem and will fail to recycle properly.
     It is also OK to use a shareware program such as ATSEND to accomplish
     this.

Tricks on Rescheduling a Failed Fax Connection

     Occasionally, the SupraFAX fails to make a connection with a remote fax 
     machine on the first try.  Because FaxTalk must be told not to redial the 
     number, the reported NOGOOD prevents it from being retried.  However, 
     there is a way to have the attempt tried several times through clever use 
     of options.  FPCHECK has the '/B' option which will report a 'Failed' 
     attempt as a BUSY rather than a NOGOOD.  FaxMail will mark these messages 
     as BUSY, which can then be retried, rather than as Failed which stops 
     further attempts.  By setting up two configuration files for FaxMail 
     using the /CFG= option (one calling FPCHECK with the /B option and the 
     second without the /B), FaxMail can be called several times in a row to 
     retry Failed connections.  Here is a sample EVENT.SYS file that 
     illustrates the technique: 

          CD \PCB\FAX                    <- Make this the default directory
          FAXTSR /l                      <- Loads FAXTSR into memory
          FAXMAIL /SCAN /CFG=WITHB       <- Run FaxMail marking Failed as Busy
          FAXMAIL /BUSY /CFG=WITHB       <- Rerun FaxMail for Busy or Failed
          FAXMAIL /BUSY /CFG=WITHOUTB    <- Try a third time but allow Failures
          FAXTSR /u                      <- Unload (remove) FAXTSR from memory
          ECHO ATZ >COM1                 <- Reset the modem!!
          CD \PCB                        <- Change back to \PCB directory
          BOARD                          <- Rerun PCBoard

     Note that the last call to FaxMail makes certain that messages which fail 
     3 times (or were BUSY then fail twice) do not continue to be marked BUSY.

Final Notes

     This information and the FPCHECK program were tested with FaxMail 1.01
     and FaxTalk Plus v1.65C using a SupraFAXmodem V.32bis modem with the
     "J" (Caller ID) chip.  

     Good luck and success in using the FaxMail door with FaxTalk Plus and
     the SupraFAXmodem!  I imagine there may be better ways to implement
     this combination, but I find this does work quite adequately.  Feel free
     to experiment.

     I offer this information and programs for free and on an AS IS basis!
     There is ABSOLUTELY NO WARRANTIES OR GUARANTEES OF ANY KIND associated
     with the use of this information or programs.  USE ENTIRELY AT YOUR OWN
     RISK AND EXPENSE.

     FaxMail 1.01 is Copyright 1993 by Mark Herring.
     SupraFAXmodem is a tradeMark of the Supra Corporation.
     FaxTalk is a registered trademark of Thought Communications, Inc.